MINIMUM QUALITY CONTROL STANDARDS

MQCS - III (Version 3, May 2000)

NOTE		See specification for quality control Indicators Q1 to Q20 at the end of this appendix

( = space (ASCII 32)

Element	Error				Action

1	iT ( 3-5	Correct manually, otherwise (

2	AAAA ( valid year	Correct manually otherwise reject

3	MM ( 01 - 12	Correct manually otherwise reject

4	YY ( valid day of month	Correct manually otherwise reject

5	G ( 00 - 23	Correct manually otherwise reject

6	Q ( 1, 3, 5, 7	Correct manually and Q20 = 5, otherwise Q20 = 4

Q = (	Q20 = 2

7	LaLaLa ( 000-900	Correct manually and Q20 = 5, otherwise Q20 = 4

LaLaLa = (((	Q20 = 2

8	LoLoLoLo ( 0000-1800	Correct manually and Q20 = 5, otherwise Q20 = 4

LoLoLoLo = ((((	Q20 = 2

But		LaLaLa = LoLoLoLo = ((((()		Correct manually otherwise reject

Time sequence checks

Change in latitude > 0.7o /hr	Correct manually otherwise Q20 = 3

Change in longitude > 0.7o /hr	Correct manually otherwise Q20 = 3

when lat. 00-39.9

Change in longitude > 1.0o /hr	Correct manually otherwise Q20 = 3

when lat. 40-49.9

Change in longitude > 1.4o /hr	Correct manually otherwise Q20 = 3

when lat. 50-59.9

Change in longitude > 2.0o /hr	Correct manually otherwise Q20 = 3

when lat. 60-69.9

Change in longitude > 2.7o /hr	Correct manually otherwise Q20 = 3

when lat. 70-79.9

9		No checking

10	h ( 0-9, (	Correct manually and Q1 = 5, otherwise Q1 = 4

h = (	Q1 = 9

11	VV ( 90-99, ((	Correct manually and Q2 = 5, otherwise Q2 = 4

VV = ((	Q2 = 9

12	N ( 0-9, (, /	Correct manually and Q3 = 5, otherwise Q3 = 4

N < Nh	Correct manually and Q3 = 5, otherwise Q3 = 2

13	dd ( 00-36, 99, ((	Correct manually and Q4 = 5, otherwise Q4 =4

dd = ((, //	Q4 = 9

dd versus ff

dd = 00, ff  00	Correct manually and Q4 or Q5 = 5 otherwise

Q4 = Q5 = 2

dd ( 00, ff = 00	Correct manually and Q4 or Q5 = 5 otherwise

Q4 = Q5 = 2

14	iw ( 0, 1, 3, 4	Correct manually, otherwise Q5 = 4

15	ff > 80 knots	Correct manually and Q5 = 5, otherwise Q5 = 3

ff = ((, //	Q5 = 9

16	sn ( 0, 1	Correct manually, otherwise Q6 = 4

17	TTT = (((, ///	Q6 = 9

If -25 > TTT >40 then

when Lat. < 45.0

TTT < -25	Q6 = 4

TTT > 40	Q6 = 3

when Lat. >= 45.0

TTT < -25	Q6 = 3

TTT > 40	Q6 = 4

Element	Error	Action

TTT versus humidity parameters

TTT < WB (wet bulb) 		Correct manually and Q6 = 5, otherwise Q6 = Q19 = 2

TTT < DP (dew point)		Correct manually and Q6 = Q7 = 5, otherwise Q6 = Q7 = 2

18	 st( 0, 1, 2, 5, 6, 7	Correct manually, otherwise Q7 =4

19	DP > WB	Correct manually and Q7 = 5, otherwise Q7 = Q19 = 2

DP > TTT	Correct manually and Q7 = 5, otherwise Q7 = Q6 = 2

WB = DP = (((	Q7 = 9

20	930 > PPPP > 1050 hPa	Correct manually and Q8 = 5, otherwise Q8 = 3

870 > PPPP > 1070 hPa	Correct manually and Q8 = 5, otherwise Q8 = 4

PPPP = ((((	Q8 = 9

21	ww = 22-24, 26, 36-39, 48,	Correct manually and Q9 = 5, otherwise Q9 = 4

49, 56, 57, 66-79, 83-88, 93,

94 and latitude <20o

ww = ((, //			Q9 = 9

22, 23	W1 = W2 = 7 and latitude <20o 	Correct manually and Q9 = 5, otherwise Q9 = 4

W1 < W2				Correct manually and Q9 = 5, otherwise Q9 = 4

W1 = W2 = (, /			Q9 = 9

24,25,

26,27	N = 0, (, 9 and NhCLCMCH ( (	Correct manually and Q3 = 5, otherwise Q3 = 4

28	 ss ( 0, 1	Correct manually otherwise Q10 = 4

29	TwTwTw = (((, ///	Q10 = 9

if -2.0 > TwTwTw > 37.0 then

when Lat. < 45.0

TwTwTw < -2.0			Control manually and Q10 = 5, otherwise Q10 = 4

TwTwTw > 37.0			Control manually and Q10 = 5, otherwise Q10 = 3

when Lat. >= 45.0

TwTwTw < -2.0			Control manually and Q10 = 5, otherwise Q10 = 3

TwTwTw > 37.0			Control manually and Q10 = 5, otherwise Q10 = 4

30	Indicator ( 0-7, (	Correct manually, make it ( if not correctable

31	Indicator ( 0-9, (	Correct manually, make it ( if not correctable

32	20 < PwPw < 30	Q11 = 3

PwPw ( 30 and ( 99	Q11 = 4

PwPw = ((, //	Q11 = 9

33	35< HwHw < 50	Q12 = 3

HwHw  > = 50	Q12 = 4

HwHw = ((, //	Q12 = 9

34	dw1 dw1 ( 00-36, 99, ((	Correct manually and Q13 = 5, otherwise Q13 = 4

swell1 = swell2 = (	Q13 = 9

35	25 < P w1P w1 < 30	Q13 = 3

P w1P w1 ( 30 and ( 99	Q13 = 4

36	35 < H w1H w1 < 50	Q13 = 3

H w1H w1->= 50	Q13 = 4

37	Is ( 1-5, (	Correct manually, otherwise (

38	EsEs ( 00-99, ((	Correct manually, otherwise ((

39	Rs ( 0-4, (	Correct manually, otherwise (

40	Source ( 0-6	Correct manually, otherwise (

41	Platform ( 0-9	Correct manually, otherwise (

42	No call sign	Insert manually, otherwise reject

43	No country code	Insert manually

44		No Quality Control

45	Q ( 0-6, 9	Correct manually, otherwise (

46	ix ( 1-7	Correct manually, otherwise (

47	iR = 0-2 and RRR = 000, ///, (((	Correct manually, otherwise Q14 = 4

iR = 3 and RRR ( 000, ///, (((	Correct manually, otherwise Q14 = 2

iR  =4 and RRR ( ///, (((	Correct manually, otherwise Q14 = 2

iR ( 0 - 4 	Correct manually, ortherwise Q14 = 4

Element	Error				Action

48	RRR ( 001 - 999 and iR = 1, 2	Correct manually and Q14 = 5, otherwise Q14 = 2

49	tR  0-9	Correct manually and Q14 = 5, otherwise Q14 = 4

50	sw ( 0, 1, 2, 5, 6, 7, 9	Correct manually, otherwise Q19 = 4

51	WB < DP	Correct manually and Q19 = 5, otherwise Q19 = Q7 = 2

WB = ///, (((	Q19 = 9

WB > TTT	Correct manually and Q19 = 5, otherwise Q19 = Q6 = 2

52	a ( 0-8, (	Correct manually and Q15 = 5, otherwise Q15 = 4

a = 4 and ppp ( 000	Correct manually and Q15 = 5, otherwise Q15 = Q16 = 2

a = (	Q15 = 9

53	150 < ppp ( 250	Correct manually and Q16 = 5 otherwise Q16 =  3

ppp > 250	Correct manually and Q16 = 5 otherwise Q16 = 4

ppp = (((	Q16 = 9

54	Ds ( 0-9, (	Correct manually and Q17 = 5, otherwise Q17 = 4

Ds = (, /				Q17 = 9

55	Vs ( 0-9, (	Correct manually and Q18 = 5, otherwise Q18 = 4

Vs = (, /	Q18 = 9

56	dw2dw2 ( 00-36, 99	Correct manually and Q13 = 5, otherwise Q13 = 4

57	25 < Pw2Pw2 < 30	Q13 = 3

Pw2Pw2 ( 30 and ( 99	Q13 = 4

58	35 < Hw2Hw2 < 50	Q13 = 3

Hw2Hw2 >= 50	Q13 = 4

59	ci ( 0-9, (	Correct manually, otherwise (

60	si ( 0-9, (	Correct manually, otherwise (

61	bi ( 0-9, (	Correct manually, otherwise (

62	Di ( 0-9, (	Correct manually, otherwise (

63	zi ( 0-9, (	Correct manually, otherwise (

Specifications for quality control Indicators Q1  to Q20

0	No quality control (QC) has been performed on this element

1	QC has been performed; element appears to be correct

2	QC has been performed; element appears to be inconsistent with other elements

3	QC has been performed; element appears to be doubtful

4	QC has been performed; element appears to be erroneous

5	The value has been changed as a result of QC

6, 7	Reserved for GCCs

8	Reserve

9	The value of the element is missing

Use of flag 6:

The GCCs wil set the flag to 6 if the flag has been set to 1 by the Contributing member and the GCCs find it not in accordance with the MQCS

Use of flag 7:

The GCCs wil set the flag to 7 if the flag had been set to 5 by the Contributing member andnthe GCCs find it no in accordance with the MQCS

---oooOooo---