Proposed Ingest Format

The two basic metadata record types (header and data) are listed.  Within the data record type, there are different subsidiary record types defined for the different sensor types that are presently defined (the data record list could be expanded in the future).  The descriptions of the fields that make up each record type are listed in Table 1.

1.  Header Record (HR is the identifier for the metadata header record)

HR; ts; WMOn; stn; Ain; ind; oed; cnty; ragy; Idum; DA; Lat; Lon; WC; lngth; brth; diam; hult; huln; mtyp; cmsy; Stt; foo; dfmt; wdpth; plt; DI; WebA; footnote # 1; footnote # 2; footnote # 3; footnote # 4; footnote # 5

2.  Data Records (DR is the identifier for the sensor information record, thus designated data record) the first six elements will link the data record to the header record.  A data records will only exist when there is an actual sensor on the platform and it can be repeated for every sensor of a given type.

"Sno" in the eighth element represents the sequence number of sensors located on the platform e.g. if two anemometer sensors were on the platform there would be two data records for anemometers indicated in elements 7 and 8 as AN;1 and AN;2".

The "ind" field is a critical part in linking records in the case where a platform was moved or totally re-equipped or redesigned, this will allow the correct data records to be linked to the proper header record especially in cases where the same identifier was reissued at a later date.

AN metadata record: Anemometer sensor (AN in  7th element)

DR; ts; WMOn; stn; AIn; ind; AN; Sno; anmI; aMS; anmL; anDB; anDC; hwl; ouAN; sfWD; sfWS; apWD; apWS; amWS; cmpT; apWG; amWG; amScd; amID; amSD; footnote # 1

AT metadata record: Air temperature sensor (AT in 7th element)..

DR; ts; WMOn; stn; AIn; ind; AT; Sno; ats; atsMS; atsL; atsDB; atsC; atswl; ouAT; sfAT; apAT; atScd; atID; atSD; footnote # 1; footnote # 2

WT metadata record: Water temperature sensor (WT in 7th element).

DR; ts; WMOn; stn; AIn; ind; WT; Sno; wts; wtsMS; wtsL; wtsDB; wtsC; dws; ouWT; sfWT; apWT; wtScd; wtID; wtSD; footnote # 1

SA metadata record: Salinity sensor (SA in 7th element).

DR; ts; WMOn; stn; AIn; ind; SA; Sno; Sstp, Ssm; SsL; SsDB; SsC; dss; ouSs; sfSs; apSs; mSs; SsScd; SsID; SsSD; footnote # 1

BP metadata record: Barometric Pressure (BP in 7th element).

DR; ts; WMOn; stn; AIn; ind; BP; Sno; bps; bpsMS; bpsL; bpsDB; bpsC; bpswl; ouBP; sfBP; apBP;  bpScd; bpsID; bpsSD

RH metadata record:  Relative Humidity (wet bulb/dew point) sensor (RH in 7th element)

DR; ts; WMOn; stn; AIn; ind; RH; Sno; hs; hsMS; hsL; hsDB; hsC; hswl; ouHS; sfHS; apHS; hsScd; hsID; hsSD

PG metadata record:  Precipitation gauge (PG in 7th element).

DR; ts; WMOn; stn; AIn; ind; PG; Sno; pg; pgMS; pgL; pgDB; pgC; pgwl; pupg; sfPG; apPG; pgScd; pgID; pgSD

RD metadata record:  Radiation sensor (RD in 7th element).

DR; ts; WMOn; stn; AIn; ind; RD; Sno; srs; rMS; rsL; rsDB; rsC; srwl; ours; sfSR; apSR; srScd; rsID; rsSD

CR metadata record:  Ocean Current sensor (CR in 7th element).

DR; ts; WMOn; stn; AIn; ind; CR; Sno; OC; Tsmoc; dmOC; ouOC; sfOC; apOC; ocScd; ocID; ocSD

WS metadata record:  Wave Spectra (WS in 7th element).

DR; ts; WMOn; stn; AIn; ind; WS; Sno; wasp; Digf; Nblks; Npts; spAT; sfWAS, apWAS

HV metadata record:  Horizontal Visibility (HV in 7th element).

DR; ts; WMOn; stn; AIn; ind; HV; Sno; hvm; hvit; hvl; hvDB; hvC; hvwl; hvou; hvsf; hvap; hvScd; hvID; hvSD

Table 1

ODAS  Metadata-base Contents

| Record type and sequence # | Field Abbre-viation | Input codes | Description of fields |
| --- | --- | --- | --- |
| Header Record (HR) |
| HR | 1 | ts | MB DB ID FP IS AL CM PF OT | Type of station - Moored Buoy Drifting buoy Ice Drifter Fixed Platform (oil Rig, etc.) Island Station Automatic Light Station Coastal Marine Automated Station Profiling floats (e.g. ARGO - a global array of profiling floats) Other (specify in footnote # 1 Header Record) |
|  | 2 | WMOn |  | WMO Number - 5 digit identifier |
|  | 3 | stn |  | Unique call sign if available; otherwise, station name (C-MAN, Platforms, etc.) |
|  | 4 | AIn |  | Additional Identifier Number ; define in footnote # 2 (e.g. ARGOS = up to 7 digits, GOES No., others) |
|  | 5 | ind |  | Period of validity / beginning of historical record (initiation date - year, month, day e.g. 19950321) date of mooring, launching, or platform instrumentation (date the platform began collecting weather observations under its current ID and location). If the platform is moved or assigned a new ID then a new period of validity should be initiated. |
|  | 6 | oed |  | Operational end date of platform operations (year, month, day e.g. 20000127). This item is associated with the entry above which shows the beginning date and this item the ending date when a platform closed operations. If for example a moored buoy was placed in the Great Lakes each Spring and withdrawn each Winter the beginning date would not change unless the identifier, ownership, or location changed at some point. When one of these change a new beginning date should be entered ind above and a operational end date entered in this field. |
|  | 7 | cnty | see list | Country of ownership - International Organization for Standardization (ISO) country code (Alpha-2; two character alpha code) |
|  | 8 | ragy |  | Responsible agency/organization within a country responsible for the platforms operations, launch, and metadata [e.g. in the USA it could be National Ocean Service (NOS) NOAA , National Data Buoy Center (NDBC) NOAA, Woods Hole Institute, etc.] List the full name of the organization or agency responsible. There should be a link between the responsible agency/organization and web address listed in item 114. |
|  | 9 | ldmu |  | Last date metadata updated (year, month, day e.g. 20000527 representing 27 May 2000) |
|  | 10 | DA | 1 2 3 4 5 | Degree of Automation Fully automated Always supplemented with manual input Occasionally supplemented with manual input Fully manual (no automation) Unknown |
|  | 11 | Lat |  | latitude - degrees, up to three decimal places if available (e.g. 50. 985 N/S) |
|  | 12 | Lon |  | Longitude - degrees, up to three decimal places if available (e.g. 124.976 E/W) |
|  | 13 | WC |  | Watch Circle - nearest whole meter (e.g. 346.5 = 347 meters) . The maximum distance a moored buoy can be located from its central position related to the length and type of mooring. Outside the watch circle and the moored buoy is likely adrift. |
|  | 14 | lngth |  | Length - the length of the platform (if rectangular or boat shape hull). See code diam below if the platform is a discus. Meters to tenths (e.g. 26. 9 meters) |
|  | 15 | brth |  | Breath - the breath (width) of the platform (if rectangular or boat shaped hull). Meters to tenths ( e.g. 12.6 m) |
|  | 16 | diam |  | Diameter - platform dimension for discus type hulls. Diameter in meters to tenths (e.g. 6.0 m) |
|  | 17 | hult | DS BS RS SP OD NM TR CN OR DR OT | Hull type Discus (Cylinders) Boat shaped hull Rectangular shape Spars ODAS 30 series NOMAD Torus Conic Omnidirectional wave-rider Directional wave-rider Other (specify in footnote # 3 Header Record) |
|  | 18 | huln |  | Hull or platform number - enter as assigned (a combination of numeric and alpha characters if required) |
|  | 19 | mtyp | AC ST FC PC HS TS WS PA NL OT | Mooring type - Mooring type if a moored buoy or drouge type if drifting buoy. All Chain (shallow depths generally up to 90 meters) Semitaut (intermediated depths generally 60 to 600 meters-generally nylon cable) Float Inverse Catenary (deep ocean generally 600 to 6000 m-generally nylon with glass floats) Poly-nylon Inverse Catenary (deep ocean generally 1200 to 6000 m) Drouge Type Holey sock drogue Tristar Window shade Parachute Non-Lagrangian sea anchor Use for either mooring or drouge as needed Other (specify in footnote # 4 Header Record) |
|  | 20 | cmsy | GO AR GA RF OT | Satellite Data Collection System - system used to transmit the observations GOES DCP ARGOS PTT GOES primary ARGOS backup RF Other (specify in footnote # 5 Header Record) |
|  | 21 | Stt |  | Satellite transmission time - time slot assigned for observation transmission. Hours and minutes UTC (e.g. 1230 ) or for example, on the hour, on the half hour, two orbits per day, etc. |
|  | 22 | foo |  | Frequency of observations - hours and minutes (e.g. every hour = 1.0, every 6 hours = 6.0, or every half hour 0.5, etc., I = irregular) |
|  | 23 | dfmt |  | Data format - data format (WMO codes; Pub 306) the observations was transmitted or digitized (i.e. observational form). Buoy code -FM 18-X Ship code - FM 13-X TESAC - FM 64-IX WAVEOB - FM 65-IX BUFR - FM 94-XI Other WMO codes added as needed Note: use actual WMO Code designator as the abbreviation ( e.g. FM 18-X) |
|  | 24 | wdpth |  | Water Depth (nearest whole meter) |
|  | 25 | plt |  | Payload Type (e.g. DACT, VEEP, GSBP, ZENO, ODAS33, etc.) Details should be provided regarding each type of payload (payload description) |
|  | 26 | DI | AV NA | Digital image - a phtograph or schematic of the platform and equipment Available in digital file Not available |
|  | 27 | WebA |  | Web Address (URL) where additional information can be obtained |
| ANEMOMETER (AN) |  |  |  |  |
| DR | 1 | anmI | P TC FC S WT OT | Anemometer instrument type propeller/vane three cup four cup sonic WOTAN (wind observation through ambient noise) other (define in footnote) |
|  | 2 | aMS |  | Anemometer - model (manufacturer/series no.) |
|  | 3 | anmL | FM AM CM RY LY OT | Anemometer - location foremast aftmast centermast (mainmast) right yardarm left yardarm other (define in footnote) |
|  | 4 | anDB |  | Anemometer - distance from the bow or front of platform (meters to tenths) |
|  | 5 | anDC |  | Anemometer - distance from center line or from center of discus (meters to tenths) |
|  | 6 | hwl |  | Anemometer- height above water line (meters to tenths). Value can be negative for WOTAN |
|  | 7 | ouAN |  | Anemometer - operational range and units of measurement (e.g. 0 to 60 m/s ; 000 to 360 degrees) |
|  | 8 | sfWD |  | Sampling frequency (Hz) - wind direction (e.g. 1.28 Hz) |
|  | 9 | sfWS |  | Sampling frequency (Hz) - wind speed (e.g. 1.28 Hz) |
|  | 10 | apWD |  | Averaging period (minutes to tenths) - wind direction (e.g. 8.0 minutes) |
|  | 11 | apWS |  | Averaging period (minutes to tenths) - wind speed (e.g. 8.0 minutes) |
|  | 12 | amWS | S V | Averaging method - wind speed Scalar Vector |
|  | 13 | cmpT |  | Compass type/model No. - anemometer |
|  | 14 | apWG |  | Averaging period (seconds) - wind gust (e.g. 5 seconds) |
|  | 15 | amWG | S V | Averaging method - wind gust Scalar Vector |
|  | 16 | amScd |  | Calibration date- Anemometer sensor No. Date sensor was last calibrated ( year, month, day e.g. 20000723) |
|  | 17 | amID |  | Anemometer sensor installation date (year, month, day e.g. 19950228). If the direction sensor and speed sensor are separate instruments then use footnote # 1 in the Anemometer data record to enter the dates for speed sensor and this position for direction sensor. |
|  | 18 | amSD |  | Anemometer out of service dates (beginning and ending dates; year, month, day e.g. 19960123-19960212). If known these dates should be entered anytime either the direction , speed, or both is unavailable due to equipment outage (non-reporting or invalid reports) |
| AIR TEMPERATURE (AT) |  |  |  |  |
| DR | 1 | ats | ER M MS A AS OT | Air temperature sensor- instrument type electrical resistance thermometer mercury-in-glass thermometer screen shelter - mercury thermometer alcohol-in-glass thermometer screen shelter - alcohol thermometer other (specify in footnote # 1 in the air temperature data record) |
|  | 2 | atsMS |  | Air temperature sensor - model (manufacturer/series no.) |
|  | 3 | atsL | FM AM CM RY LY OT | Air temperature sensor - location foremast aftmast centermast (mainmast) right yardarm left yardarm other (specify in footnote # 2 in the air temperature data record) |
|  | 4 | atsDB |  | Air temperature sensor - distance (meters to tenths) from bow or front of platform note: leave this field blank if platform is a discus |
|  | 5 | atsC |  | Air temperature sensor - distance (meters to tenths) from center line or center of discus |
|  | 6 | atswl |  | Air temperature sensor - height (meters to tenths) above water line |
|  | 7 | ouAT |  | Air temperature sensor - Operational range and units of measurement (e.g. - 40C to + 50C) |
|  | 8 | sfAT |  | Sampling frequency (Hz) - air temperature sensor (e.g. 1.28 Hz) |
|  | 9 | apAT |  | Averaging period (minutes to tenths) - air temperature sensor (e.g. 8.0 minutes) |
|  | 10 | atScd |  | Calibration date- Air temperature sensor No. Date sensor was last calibrated ( year, month, day e.g. 20000723) |
|  | 11 | atID |  | Air temperature sensor installation date (year, month, day e.g. 19950228). |
|  | 12 | atSD |  | Air temperature sensor out of service dates (beginning and ending dates; year, month, day e.g. 19960123-19960212). If known these dates should be entered anytime the air temperature is unavailable due to equipment outage (non-reporting or invalid reports) |
| WATER TEMPERATURE (WT) |  |  |  |  |
| DR | 1 | wts | HC HT RT ER TT BU CTD STD RM XC NS AL XBT OT | Water temperature sensor - instrument type Hull contact sensor "Through hull" sensor Radiation thermometer Electrical resistance thermometer Trailing thermistor Bucket thermometer CTD ( conductivity-temperature-depth) STD (salinity-temperature-depth) refractometer XCTD (expendable CTD probe) Nansen cast ALACE (autonomus Lagrangian Circulation Explorer) Expendable Bathythermograph Other (specify in footnote # 1 in the water temperature data record) |
|  | 2 | wtsMS |  | Water (sea) temperature sensor - model (manufacturer/series no.) |
|  | 3 | wtsL |  | Water temperature sensor - location (e.g. port bow, bottom of discus, etc.) |
|  | 4 | wtsDB |  | Water temperature sensor - distance (meters to tenths) from the bow or front of platform Note: left blank for discus hulls and subsurface temperatures |
|  | 5 | wtsC |  | Water temperature sensor- distance (meters to tenths) from center line or center of discus |
|  | 6 | dws |  | Depth of water temperature sensor; tenths of meters (e.g. 10.3 meters) below the water line. |
|  | 7 | ouWT |  | Operational range and units of measurement-water temperature sensor (e.g. range - 4 C to + 40 C) |
|  | 8 | sfWT |  | Sample frequency (Hz) - Water temperature sensor (e.g. 1.28 Hz) |
|  | 9 | apWT |  | Averaging period (minutes to tenths) - Water temperature sensor (e.g. 8.0 minutes) |
|  | 10 | wtScd |  | Calibration date- Water temperature sensor No. Date sensor was last calibrated ( year, month, day e.g. 20000723) |
|  | 11 | wtID |  | Water temperature sensor installation date (year, month, day e.g. 19950228). |
|  | 12 | wtSD |  | Water temperature sensor out of service dates (beginning and ending dates; year, month, day e.g. 19960123-19960212). If known these dates should be entered anytime the water temperature is unavailable due to equipment outage (non-reporting or invalid reports) |
| SALINITY (SA) |  |  |  |  |
| DR | 1 | Sstp | CTD STD RM XC NS AL OT | Salinity - sensor type CTD ( conductivity-temperature-depth) STD (salinity-temperature-depth) refractometer XCTD (expendable CTD probe) Nansen cast ALACE (autonomus Lagrangian Circulation Explorer) Other (specify in footnote # 1 in the salinity data record) |
|  | 2 | Ssm |  | Salinity sensor (model/manufacturer/series no.) |
|  | 3 | SsL |  | Salinity sensor No. - Location (note: to be used only for those sensors attached to a platform) |
|  | 4 | SsDB |  | Salinity sensor No. - distance from bow or front of platform Note: to be used only when sensor is attached to a platform (same as location above) |
|  | 5 | SsC |  | Salinity sensor No. - distance from center line or center of discus |
|  | 6 | dss |  | Depth of salinity sensor No. - meters to tenths (e.g. 10.7 m) of salinity sensor below the water line (surface of the water) |
|  | 7 | ouSs |  | Salinity sensor - operational range and units of measurement (e.g. 25 to 45 parts per thousand. Salinity is calculated based on the measurement of chlorinity) |
|  | 8 | sfSs |  | Sample frequency - available only for automated digital sensors |
|  | 9 | apSs |  | Averaging period - available only for automated digital sensors |
|  | 10 | mSs |  | Method used to compute the salinity (e.g. chlorinity, electrical conductivity, refractive index, etc. ) |
|  | 11 | SsScd |  | Calibration date - salinity sensor No. Date the sensor was last calibrated (year, month, day e.g. 20000207) |
|  | 12 | SsID |  | salinity sensor installation date (year, month, day e.g. 19950228). |
|  | 13 | SsSD |  | Salinity sensor out of service dates (beginning and ending dates; year, month, day e.g. 19960123-19960212). If known these dates should be entered anytime the salinity is unavailable due to equipment outage (non-reporting or invalid reports) |
| BAROMETRIC PRESSURE (BP) |  |  |  |  |
| DR | 1 | bps |  | Barometric pressure sensor - instrument type |
|  | 2 | bpsMS |  | Barometric pressure sensor - model (manufacturer/series no.) |
|  | 3 | bpsL |  | Barometric pressure sensor - location (e.g. centermast) |
|  | 4 | bpsDB |  | Barometric pressure sensor - distance (meters to tenths) from the bow or front of platform Note: leave this field blank if platform is a discus |
|  | 5 | bpsC |  | Barometric pressure sensor - distance (meters to tenths) from center line or center of discus |
|  | 6 | bpswl |  | Barometric pressure sensor - height (meters to tenths) above water line |
|  | 7 | ouBP |  | Barometric pressure sensor - Operational range and units of measurement (e.g. 900-1100 hPa) |
|  | 8 | sfBP |  | Sampling frequency (Hz) - Barometric pressure sensor (e.g. 1.28 Hz) |
|  | 9 | apBP |  | Averaging period (minutes to tenths) - Barometric pressure sensor (e.g. 8.0 minutes) |
|  | 10 | bpScd |  | calibration date - barometric pressure sensor No. Latest date of calibration (year, month, day e.g. 20000207) |
|  | 11 | bpsID |  | Barometric pressure sensor installation date (year, month, day e.g. 19950228). |
|  | 12 | bpsSD |  | Barometric pressure sensor out of service dates (beginning and ending dates; year, month, day e.g. 19960123-19960212). If known these dates should be entered anytime the barometric pressure is unavailable due to equipment outage (non-reporting or invalid reports) |
| RELATIVE HUMIDITY (RH) |  |  |  |  |
| DR | 1 | hs |  | Relative Humidity (wet bulb/dew point) sensor -instrument type |
|  | 2 | hsMS |  | Relative Humidity (wet bulb/dew point) sensor -model (manufacturer/series no.) |
|  | 3 | hsL |  | Relative Humidity (wet bulb/dew point) sensor -location (left yardarm mast) |
|  | 4 | hsDB |  | Relative Humidity sensor - distance (meters to tenths) from the bow or front of platform Note: leave this field blank if platform is a discus |
|  | 5 | hsC |  | Relative Humidity sensor - distance (meters to tenths) from center line or center of discus |
|  | 6 | hswl |  | Relative Humidity sensor - height (meters to tenths) above water line |
|  | 7 | ouhs |  | Relative Humidity (wet bulb/dew point) sensor - Operational range and units of measurement (e.g. range 0-100 %) |
|  | 8 | sfhs |  | Sampling frequency (Hz)-Relative Humidity (wet bulb/dew point) sensor (e.g. 1 Hz) |
|  | 9 | aphs |  | Averaging period (minutes)-Relative Humidity (wet bulb/dew point) sensor (e.g.1 min.) |
|  | 10 | hsScd |  | Calibration date - Relative Humidity (wet bulb/dew point) sensor No. Latest date the sensor was calibrated (year, month, day e.g. 20000207) |
|  | 11 | hsID |  | Relative Humidity (wet bulb/dew point) sensor installation date (year, month, day e.g. 19950228). |
|  | 12 | hsSD |  | Relative Humidity (wet bulb/dew point) sensor out of service dates (beginning and ending dates; year, month, day e.g. 19960123-19960212). If known, these dates should be entered anytime the Relative Humidity (wet bulb/dew point) is unavailable due to equipment outage (non-reporting or invalid reports) |
| PRECIPITATION (PG) |  |  |  |  |
| DR | 1 | pg |  | Precipitation gauge -instrument type (e. g. weighing bucket, tipping bucket, etc.) |
|  | 2 | pgMS |  | Precipitation gauge - model (manufacturer/series no.) |
|  | 3 | pgL |  | Precipitation gauge -location |
|  | 4 | pgDB |  | Precipitation gauge - distance (meters to tenths) from the bow or front of platform |
|  | 5 | pgC |  | Precipitation gauge - distance (meters to tenths) from center line or off center of a discus |
|  | 6 | pgwl |  | Precipitation gauge- height (meters to tenths) above water line |
|  | 7 | oupg |  | Precipitation gauge - Operational range and units of measurement (e.g. 0 to 25 cm per hour) |
|  | 8 | sfPG |  | Sampling frequency - Precipitation gauge (e.g. continuous) |
|  | 9 | apPG |  | Averaging period-Precipitation gauge (e.g. 6 hours; then reset) |
|  | 10 | pgScd |  | Calibration date -Precipitation gauge No. Latest date sensor/gauge was calibrated (year, month, day e.g. 20000207) |
|  | 11 | pgID |  | Precipitation gauge installation date (year, month, day e.g. 19950228). |
|  | 12 | pgSD |  | Precipitation gauge out of service dates (beginning and ending dates; year, month, day e.g. 19960123-19960212). If known, these dates should be entered anytime the precipitation measurement is unavailable due to equipment outage (non-reporting or invalid reports) |
| RADIATION (RD) |  |  |  |  |
| DR | 1 | srs |  | Solar radiation sensor -instrument type |
|  | 2 | rMS |  | Radiation sensor - model (manufacturer/series no.) |
|  | 3 | rsL |  | Radiation sensor -location (e.g. foremast) |
|  | 4 | rsDB |  | Radiation sensor - distance (meters to tenths) from the bow or front of platform Note: leave this field blank if platform is a discus |
|  | 5 | rsC |  | Radiation sensor - distance (meters to tenths) from center line or center of discus |
|  | 6 | srwl |  | Solar radiation sensor- height (meters to tenths) above water line |
|  | 7 | ours |  | Radiation sensor - Operational range and units of measurement (e.g. 0.07-1.65 cal. cm-2 min-1) |
|  | 8 | sfSR |  | Sampling frequency (Hz)-Solar radiation sensor (e.g. 1 Hz) |
|  | 9 | apSR |  | Averaging period (minutes to tenths) - Solar radiation sensor (e.g. 8.0 minutes) |
|  | 10 | srScd |  | Calibration date - Solar radiation sensor No. Latest date the sensor was calibrated (year, month, day e.g. 20000207) |
|  | 11 | rsID |  | Radiation sensor installation date (year, month, day e.g. 19950228). |
|  | 12 | rsSD |  | Radiation sensor out of service dates (beginning and ending dates; year, month, day e.g. 19960123-19960212). If known, these dates should be entered anytime the radiation measurement is unavailable due to equipment outage (non-reporting or invalid reports) |
| OCEAN CURRENTS (CR) |  |  |  |  |
| DR | 1 | OC | C M E | Ocean current speed reported calculated measured estimated |
|  | 2 | TSmoc |  | Type sensor measuring ocean currents (type/model/manufacturer) |
|  | 3 | dmOC |  | Depth of measurement (in meters, e.g. 10 m) of the ocean current |
|  | 4 | ouOC |  | Ocean currents - Operational range and units of measurement (range e.g.-10 m/s to +10m/s) |
|  | 5 | sfOC |  | Sampling frequency (Hz) -Ocean currents (e.g.0.667 Hz) |
|  | 6 | apOC |  | Averaging period (minutes to tenths) - Ocean currents (e.g. 20.0 minutes) |
|  | 7 | ocScd |  | Calibration date - Ocean current sensor (year, month, day e.g. 20000208) |
|  | 8 | ocID |  | Ocean current sensor installation date (year, month, day e.g. 19950228). |
|  | 9 | ocSD |  | Ocean current sensor out of service dates (beginning and ending dates; year, month, day e.g. 19960123-19960212). If known, these dates should be entered anytime the ocean current measurement is unavailable due to equipment outage (non-reporting or invalid reports) |
| WAVE SPECTRA (WS) |  |  |  |  |
| DR | 1 | wasp |  | Wave spectra - type of surface elevation sensor (From which wave spectra is derived) |
|  | 2 | Digf |  | Digital filter used - wave spectra |
|  | 3 | Nblks |  | Number of blocks used for averaging - wave spectra |
|  | 4 | Npts |  | Number of points in each block - wave spectra |
|  | 5 | spAT |  | Spectral analysis technique (e.g. FFT, MEM, etc.) |
|  | 6 | sfWAS |  | Sampling frequency -Wave spectra (e.g. 2.56 Hz) |
|  | 7 | apWAS |  | Averaging period- length of record for averaging period -Wave spectra (e.g. 20 minutes) |
| HORIZONTAL VISIBILITY (HV) |  |  |  |  |
| DR | 1 | hvm | MAN ATM | Horizontal visibility manual automated |
|  | 2 | hvit |  | Instrument type (automated sensor) - model/manufacturer/series no. |
|  | 3 | hvl |  | Location - Horizontal visibility sensor No. |
|  | 4 | hvDB |  | Horizontal visibility sensor - distance (meters to tenths) from the bow or front of platform Note: leave this field blank if platform is a discus |
|  | 5 | hvC |  | Horizontal visibility sensor - distance (meters to tenths) from center line or center of discus |
|  | 6 | hvwl |  | Horizontal visibility sensor- height (meters to tenths) above water line |
|  | 7 | hvou |  | Horizontal visibility sensor - Operational range and units of measurement (e.g. 0000 to 9999 meters or < 0.1km -10km) |
|  | 8 | hvsf |  | Sampling frequency - Horizontal visibility sensor No. |
|  | 9 | hvap |  | Averaging period - Horizontal visibility sensor No. |
|  | 10 | hvScd |  | Calibration date- Horizontal visibility sensor No. Latest date sensor was calibrated (year, month, day e.g. 20000208) |
|  | 11 | hvID |  | Horizontal visibility sensor installation date (year, month, day e.g. 19950228). |
|  | 12 | hvSD |  | Horizontal visibility sensor out of service dates (beginning and ending dates; year, month, day e.g. 19960123-19960212). If known, these dates should be entered anytime the visibility measurement is unavailable due to equipment outage (non-reporting or invalid reports) |

_____________