|  | VOS and VOSClim Report for 2006 | Canada |
| --- | --- | --- |
|  | a. | Programme description: |
|  | Category | No. of ships at 31 Dec 2006 | Comments |
|  | Selected | 50 |  |
|  | Supplementary | 7 |  |
|  | Auxiliary | 25 |  |
|  | Other (specify) | 14 |  |
|  | Total National VOS Fleet | 96 |  |
|  | b. | VOS: |
|  | Number of VOS vessels recruited in 2006 | 0 |
|  | Number of VOS vessels de-recruited in 2006 | Approximately 20. Canada is actively de-recruiting VOS vessels through the winter 2006/2007 in response to its VOS optimization program. |
|  | Target number of ships in the national VOS Fleet | 75 Automatic VOS ships |
|  | c. | VOSClim: |
|  | Number of VOSClim vessels at 31 December 2006 | 14 |
|  | Number of VOSClim vessels recruited in 2006 | 0 |
|  | Number of VOSClim de-recruitments in 2006 | 0 |
|  | Number of VOSClim recruitments planned for 2007 | 26 |
|  | Target number of ships to participate in VOSClim | 75 (The complete AVOS network) |
|  | d. | Automated observing systems: |
|  | Type | No. of ships at 31 Dec 2006 | Manual Input Yes / No | Method of Comms | 2007 Planned installations |
|  | AVOS manufactures by Axys Technologies | 39 | Both | INMARSAT | 12 |
|  | e. | Data management: |
|  | Total number of ship observations (BBXX) distributed on the GTS in 2006 | 103,419 (of which 55,575 generated with Generic SHIP ident) |
|  | Frequency of VOS data submitted for the GCC in 2006 |  |
|  | f. | Electronic logbooks: |
|  | Software & version | No. of ships at 31 Dec 2006 | Implementation plans |
|  | 1.23.14 Bridge PC 1.15 AVOS | 39 |  |
|  | g. | Major challenges and difficulties: |
|  | There is a need for a deeper understanding of the stealth mode function and its proper usage on AVOS. Some ships are choosing to place the AVOS in stealth mode permanently, making the AVOS nothing more than a data collector for climate data after the fact. Data is available in real time when the AVOS Stealth mode is activated. |
|  | h. | Research / development / testing: |
|  | A software upgrade incorporating IMMT3 and MQCS 5 is to be implemented in all operational AVOS vessels spring 2007 A canned message using Iridium communications was sent out from an AVOS ship travelling the Mackenzie river the summer of 2006, with good results. An AVOS, completely retrofitted with an Iridium transmission package will be installed on a ship travelling through the St. Lawrence river continuing on to the Canadian Arctic summer 2007. |
|  | i. | Other comments: |