|  | ASAP Report for 2006 | EUMETNET |
| --- | --- | --- |
|  | a. | Catalogue of ASAP vessels in 2006 (see Appendix 3): |
|  | b. | Major challenges and difficulties: |
|  | Major technical problems are damages on the electronic equipment due to permanent vibrations of the ship. Further difficulties are delayed or unstable satellite transmissions. The average terminal sounding height also includes flights with sounding heights of only 100 hPa. In most cases the actual burst heights of these flights were higher. But due to late transmission of TEMP C and D the data were received later than HH+120 on the GTS. Three in nine vessels under E-ASAP management sail between North America and Western Mediterranean. Because there is no PMO in the Mediterranean there is also no routine technical maintenance of these ASAP systems. In November/December 2006 many transmissions failed due to the unexpected closing of the LES Goonhilly. |
|  | b. | Other comments: |
|  | The station PCs on the E-ASAP vessels were replaced by semi-rugged notebooks to allow easy exchange of equipment in ‘remote’ ports (i. e. away from E-ASAP base ports). On some ships the Inmarsat transceiver is routinely changed from starboard (on eastbound crossings) to portside (on westbound crossings) to ensure proper connection to the satellite. Security concerns were raised regarding the availability of the true position of the ships on some web sites. Therefore all ship callsigns in the data messages were replaced by a generic station name. The generic station name is composed of 6-7 characters: Char 1,2: ‘AS’, fixed (i. e. ‘Aerology’ and ‘Ship’) Char 3,4: ISO 3166-1-alpha-2 country code (‘EU’ for EUMETNET) Char 5,6: sequential number Char 7: free |

| d. | ASAP Performance |
| --- | --- |
| Ship Callsign | Station name | Total number of sondes launched | Number of succesful soundings(1) | Average terminal sounding height (km) (2) | Balloon size (gm) | Percentage on GTS (3) |
| KRPD | ASEU01 | 430 | 352 | 21.8 | 350 | 73 |
| WPKD | ASEU02 | 422 | 364 | 22.1 | 350 | 82 |
| ZCBE7 | ASEU03 | 266 | 253 | 20.5 | 350 | 90 |
| ZCBF3 | ASEU04 | 235 | 223 | 21.8 | 350 | 92 |
| V2BD9 | ASEU05 | 418 | 382 | 22.1 | 350 | 94 |
| SKUN | ASDE01 | 325 | 307 | 20.6 | 200 | 91 |
| DBBH | ASDE02 | 286 | 277 | 20.1 | 200 | 86 |
| WAAH | ASDE03 | 440 | 380 | 20.7 | 200 | 79 |
| ELML7 | ASDE04 | 385 | 374 | 20.4 | 200 | 84 |
| ZCBP6 | ASGB01 | 378 | 325 | 22.4 | 350 | 75 |
| (1) Due to transmission errors the number of successful soundings is higher than the number of transmissions. (2) The average terminal sounding height is taken from part D (or C, if D is missing) of the TEMP. All balloons are designed to achieve at least 100 hPa. Balloons which do not reach 100 hPa are not representative (low battery, poor telemetry, failing transmission of parts C and D, rough handling, adverse weather conditions, etc.). Therefore, these launches are not taken into account to be compared with the balloon size. (3) Percentage on the GTS is the ratio of reports received against reports transmitted, and is based upon reports received at a data centre or GTS insertion point (name) . |

Appendix 3. Catalogue of ships participating in ASAP in 2006.						EUMETNET

10 ASAP units operated during the year on 10 ships

| Type of ship (1) | Ship name | Callsign | Comms method (2) | Windfind method / sonde type (3) | Launch method (4) | Launch height (5) | Area of operation (6) | ASAP unit ID No. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Merchant | Sealand Performance | KRPD | Inmarsat C | GPS/Vaisala RS92-SGP | container (semi automatic) | ca. 22 m | North Atlantic | E-ASAP1 |
| Merchant | Sealand Achiever | WPKD | Inmarsat C | GPS/Vaisala RS92-SGP | container (semi automatic) | ca. 22 m | North Atlantic | E-ASAP2 |
| Merchant | Endurance | ZCBE7 | Inmarsat C | GPS/Vaisala RS92-SGP | container (semi automatic) | ca. 22 m | North Atlantic/ Western Med. | E-ASAP3 |
| Merchant | Power | ZCBF3 | Inmarsat C | GPS/Vaisala RS92-SGP | container (semi automatic) | ca. 22 m | North Atlantic/ Western Med. | E-ASAP4 |
| Merchant | Melfi Italia II | V2BD9 | Inmarsat C | GPS/Vaisala RS92-SGP | container (semi automatic) | ca. 15 m | North Atlantic/ Western Med. | E-ASAP5 |
| Merchant | Atlantic Compass | SKUN | Inmarsat C | GPS/Vaisala RS92-SGP | container (semi automatic) | ca. 22 m | North Atlantic | D-ASAP1 |
| Research | FS Meteor | DBBH | Inmarsat C | GPS/Vaisala RS92-SGP | container (semi automatic) | 6 m | Worldwide | D-ASAP2 |
| Merchant | Sealand Motivator | WAAH | Inmarsat C | GPS/Vaisala RS92-SGP | container (semi automatic) | ca. 22 m | North Atlantic | D-ASAP3 |
| Merchant | Hornbay | ELML7 | Inmarsat C | GPS/Vaisala RS92-SGP | container (semi automatic) | ca. 15 m | North Atlantic | D-ASAP4 |
| Merchant | Mississauga Express | ZCBP6 | Inmarsat C | GPS/Vaisala RS92-SGP | Container (semi-automatic) or deck launcher (portable) | 22 m | North Atlantic | GB/ASAP1 |
| (1) Type of ship: Merchant, research, supply (2) Comms method: Inmarsat C or others (3) Windfind method / sonde type: eg. GPS/Vaisala RS80-G, Loran/Vaisala RS80-L, VIZ GPS Mark II Microsonde, etc (4) Launch method: deck launcher (portable), deck launcher (fixed), container (manual), container (semi automatic), other (5) Launch height: height above sea level from where the sonde is released (6) Ocean area: North Pacific, North Atlantic, Indian Ocean, variable |