| WORLD METEOROLOGICAL ORGANIZATION ________________________ | INTERGOVERNMENTAL OCEANOGRAPHIC COMMISSION (OF UNESCO) ________________________ |
| --- | --- |
| JOINT WMO/IOC TECHNICAL COMMISSION FOR OCEANOGRAPHY AND MARINE METEOROLOGY (JCOMM) SHIP OBSERVATIONS TEAM FOURTH SESSION GENEVA, SWITZERLAND, 16 TO 21 APRIL 2007 |  |  | SOT-IV/Doc. I-6.2.2 (15.II.2007) __________ ITEM I-6.2.2 Original: ENGLISH |

Programme Operations and Development

Coding issues: BUFR Templates for VOS/VOSClim, XBT/XCTD, META-T

(Submitted by the Secretariats)

Summary and purpose of document This document summarizes the issues regarding GTS table driven coding requirements for ship-based observations.

ACTION PROPOSED

The Ship Observations Team is invited to:

- integrate the different coding activities under the SOT and update the Terms of References and membership for its Task Team accordingly;

- discuss whether there is a need to revise, supersede, and/or integrate existing VOS templates;

- make specific recommendations regarding GTS distribution of high resolution ASAP data in BUFR;

- make specific recommendations regarding GTS distribution of XBT/XCTD data in BUFR;

- make specific recommendations regarding GTS distribution of ADCP data in BUFR;

- make specific recommendations regarding GTS distribution of TRACKOB data in BUFR;

- discuss requirements for other ship-based observations templates;

- make specific recommendation regarding transition to table driven codes for VOS data;

______________________

Appendices:	A.	Terms of References of the SOT Task Team on Coding

- Terms of References of the JCOMM DMPA Task Team on Table Driven Codes

- PMO-III RECOMMENDATIONS ON MIGRATION FROM SHIP TO BUFR

- Code Migration Schedule

- List of proposed fields for inclusion in a new BUFR template for VOS data

- BUFR template for synoptic reports from sea stations suitable for VOS observation data (B/C10 –Reporting SHIP data in TDCF)

- BUFR Template for VOS data

- BUFR Template for ASAP data (B/C25 – Reporting TEMP, TEMP SHIP and TEMP MOBIL data in TDCF)

- BUFR template for XBT/XCTD report (sequence 3 15 004)

- BUFR Template for TRACKOB data (Approved by CBS Ext. 6)

- B/C32 –Reporting CLIMAT SHIP data in TDCF

- B/C35 – Reporting CLIMAT TEMP and CLIMAT TEMP SHIP and data in TDCF

DISCUSSION

1	Ship Observations Team (SOT) requirements

1.1	VOS

1.1.1	The third SOT meeting (SOT-III), Brest, 7-12 March 2005 discussed GODAE High Resolution SST Pilot Project (GHRSST) requirements for GTS distribution of SST data and decided to establish a Task Team on Coding chaired by Dr Craig Donlon to address this issue.  The members and TOR of the Task Team are in Appendix A.

1.1.2	The task team has then been working via email and submitted a proposal to the CBS Expert Team on Data Representation and Codes (ET/DRC) for its meeting in Montreal, Canada, 8-12 May 2006. The Task Team proposed additions for SST temperature type/method of measurement as well as the depth of measurement below the sea surface.  As the VOS SHIP template was still being considered for other requirements (PMO-III recommendations, META-T), it was not proposed to substantially change it at the time of the ET/DRC meeting.  Only the following modifications related to (i) B/C10 – Regulations for reporting SHIP data in TDCF – and (ii) to the BUFR template for synoptic reports from sea stations suitable for VOS observation data have been proposed as pre-operational (Appendix F):

- New entries in code table 0 02 038 “Method of water temperature and/or salinity measurement” to deal with additional methods such as infrared radiometer, in line thermosalinograph, and towed body;

- New descriptor 0 07 063 Depth below sea water surface (High resolution) to provide for higher resolution of depth (scale=2, i.e. 1cm);

- Change sequence 3 02 056 for adding descriptor 0 07 063 for indicating water temperature depth.  So the sequence 3 02 056 (comprised of 0 02 038 “Method of sea surface temperature measurement” and 0 22 043 “Sea/water temperature”) in the templates was replaced by the new one.

1.1.3	It must be noted that there are now three different templates (existing or proposals) for VOS data:

- B/C10, Regulations for reporting SHIP data in TDCF (Appendix F). This is basically a translation of FM-13 SHIP data into BUFR.

- BUFR Template for VOS data (Appendix G). This is the result of past discussions between the ET/DRC, the SOT, and various experts regarding the requirement for GTS distribution of VOS data. Specific requirements such as the need to report sensor height have been added.

- PMO-III list of required fields for the VOS and VOSClim (Appendix C). See below for details.

1.1.4	The SOT might consider how many templates will eventually be needed bearing in mind that this number should be kept to a minimum. One or two templates/list might be merged or integrated in a new template that would supersede them.

1.2	SOOPIP

1.2.1	The existing BUFR template for XBT and XCTD data is listed in Appendix I. SOT-III agreed that this template met most of the current requirements for GTS distribution of such data. SEAS, USA is now evaluating development costs for starting GTS distribution of XBT data in BUFR using the existing template. The SOT Technical Coordinator and SEAS will report on progress at SOT-IV. The SOT will be invited to make further recommendations in that regard.

1.2.2	Regarding ADCP data, SOT-III invited Member States presently making ADCP measurements and having the capability and willingness of transmitting the data in real time on the GTS to work with the SOT in order to study feasibility of using BUFR. The meeting therefore asked such Members States to designate appropriate contact points to work with the SOOP Coordinator in order to work on potential impact of developing BUFR encoding/distribution capability and to work out a proposed BUFR template for ADCP data. Once a template is agreed upon, the meeting invited the SOOP Coordinator to submit proposed template to the ET/DRC. This will have to be coordinated with the META-T Pilot Project in liaison with the newly established JCOMM/DMCG Table Driven Codes group.

1.3	ASAP

1.3.1	SOT-III noted that high-resolution ASAP sounding data were required for new modeling. The meeting also noted that such high resolution data could be collected using BUFR codes, be archived in relevant national archives and be made available on their web sites after each cruise. The meeting suggested that the E-ASAP store high-resolution data, if appropriate and possible.

1.3.2	E-ASAP explained recently that BUFR capability still needed to be developed. Data telecommunication costs associated with the distribution of higher resolution data remains an issue.

1.3.3	The SOT will be invited to discuss whether there will be a need to revise existing ASAP template (Appendix H).

1.4	GOSUD

1.4.1	SOT-III noted that GOSUD was developing a BUFR template to move beyond limitations imposed by the present character code form TRACKOB in order to consider new requirements such as for pCO2 and those expressed by SAMOS. GOSUD will be invited to report on progress.

1.4.2	At its meeting in Muscat, Oman, from 5 to 8 December 2005, the ET/DRC approved for validation the TRACKOB template and sequence that had been proposed by the Japan Meteorological Agency (JMA). The descriptors are listed in the Appendix J. After the meeting, a validation test for these table D descriptors has been carried out by the European Centre for Medium-range Weather Forecast (ECMWF) and JMA with sample BUFR data produced by JMA.  Result of the test shows no problem was found in those descriptors.

1.5	GTSPP

1.5.1	SOT-III agreed that the addition of the GTSPP unique tag in BUFR tables and templates will be required and asked the SOT Technical Coordinator to pursue this issue. This has not been done so far. It is proposed that the SOT Task Team on Codes and the META-T addressed the issue in liaison with the newly established JCOMM/DMPA Table Driven Codes group.

1.6	SeaKeepers

It has been proposed to use the BUFR Master Table 10 (MT10) as a Pilot Project for the real-time distribution of ship data produced by SeaKeepers while taking GHRSST-PP requirements into account. The DMCG-II suggested that the new DMCG Table Driven Codes group be responsible for regularly reviewing and updating BUFR Master Table 10 for oceanographic data.

2	Third International PMO workshop recommendations

2.1	The third International Workshop of Port Meteorological Officers (PMO-III), Hamburg, 23-24 March 2006, discussed migration to table driven code forms for VOS and VOSClim observations. It made recommendations and established a small group to review the data and metadata elements that would be required in a VOS (including VOSClim) BUFR template and to develop a draft template to be submitted for endorsement by SOT-IV (Appendix C).

2.2	The group eventually agreed on a draft “template” (i.e. list of required field) which is provided in Appendix E.

3	Expert Team on Marine Climatology

3.1	For reference, ETMC-I (Gdynia, Poland, 7-10 July 2004) made a limited review of marine BUFR data (http://icoads.noaa.gov/etmc/etmc1/doc3.2.pdf) based on comparisons of BUFR data from NOAA’s National Centers for Environmental Prediction (NCEP) with originally reported ship (FM-13) and buoy (FM-18) data.  Following are selected general findings from that review:

- Among the (limited) set of elements compared, data problems or omissions still existed in NCEP’s version of BUFR. Generally, however, the problems appeared to be confined to secondary elements such as clouds and waves, or special codes mixed with data that otherwise were translated properly to BUFR (e.g., the code 99 for variable wind direction in FM 13, which at least at that time was not represented in the BUFR ship template).

- In addition to data improperly or incompletely converted, fields could be completely absent in BUFR that were present in the original GTS data. The comparisons were limited in scope, concentrating on the most widely used and often reported elements. Not all FM-13 and FM-18 elements were checked for their presence and accuracy as represented in BUFR.

- Retention by NCEP of the original GTS message strings was felt to be critically, and was recommended for consideration for inclusion in the BUFR template, because it permits effective, automated verifications of the translations made into BUFR by NMCs from the original data.

- For example, differences were known to exist between the BUFR data produced by NCEP, the UK Met Office, and the US Navy (FNMOC). Among these NMCs it appeared that only NCEP attached (or otherwise archived) the original message strings.

- Even if the BUFR template was able to prescribe a complete set of field-by-field mappings of FM 13 and FM 18 into BUFR (which it does not appear to have achieved yet), differences likely would arise between versions of BUFR produced at different NMCs due to differences (or inadvertent errors), in the event that the handling of a given field is not 100% specified (as for instance in the case of variable wind direction).

3.2	In addition to a possible participation of the ETMC in the development and continuing review of the VOS and possibly other marine and oceanographic template(s), the ETMC might be willing to investigate further development of the following templates:

- B/C35 – Reporting CLIMAT TEMP and CLIMAT TEMP SHIP and data in TDCF (Appendix L)

- B/C32 –Reporting CLIMAT SHIP data in TDCF (Appendix K)

4	Water Temperature Metadata Pilot Project (META-T)

4.1	The META-T Pilot Project is currently defining the instrumental metadata required for GTS distribution in real time as far as water temperature and SST measurements are concerned. The exercise is considering a number of requirements, including  (i) SST analysis and GODAE High Resolution SST Pilot Project (GHRSST), (ii) data assimilation and ocean field analysis; (iii) ocean modeling; (iv) ocean modeling validation; (v) climate forecasting; (vi) seasonal to decadal climate variability; (vii) numerical weather prediction; (viii) satellite calibration; (ix) satellite validation; (x) operational activities (e.g. weather forecasters, disaster response) (xi) quality assurance activities serving above applications, and (xii) diagnostics for platform operators.

4.2	Metadata from ship-based observing systems (among other marine and oceanographic data) falls within the remit of this project, including those under the VOS, the VOSClim, and the SOOP.

4.3	Progress will be reported at SOT-IV by the META-T Pilot Project. META-T requirements will have to be considered and merged into existing ship-based observations BUFR templates or into the new ones being defined.

5	Recommendations from the Data Management Coordination Group (DMCG)

5.1	At its second Session, Geneva, 10-12 October 2006, the DMCG noted that Groups and Panels under the JCOMM are increasingly requiring additions or changes to the WMO Code Tables, and, in particular, to the BUFR and CREX Tables, and to the BUFR templates.  Some of the requirements relate to more than one Panel (e.g., META-T, Tsunami monitoring, GHRSST and ADCP).  Additionally, the provision of the same variable or metadata from different types of platforms or instruments requires introducing some level of consistency between the different BUFR templates proposed (e.g., Consistency between templates Expendable Bathythermograph (XBT) / Expandable Conductivity, Temperature and Depth profiling system (XCTD) and Argo templates, consistency between the VOS and TRACKOB (Report of marine surface observation along a ship's track, FM 62–VIII Ext. TRACKOB), consistency between all ship templates with regards to metadata and consistency between all templates providing SST and/or Temperature profile data as far as metadata are concerned (META-T).  In other cases, one Panel might have to deal with different coding requirements.  For example, the JCOMM Ship Observations Team (SOT) was considering a large number of coding requirements, and has established a Task Team on coding to deal with GHRSST-PP requirements, as well as an ad-hoc SOT Task Team on BUFR for the VOS and the VOSClim, which was established by PMO-III.  The SOT is currently interacting with the META-T Pilot Project considering metadata encoding requirements.  The DMCG noted that the SOT intended to further review all these requirements and proposals at its next meeting in April 2007.

5.2	A summary of JCOMM table driven coding requirements are listed in the table below:

| Requirement | Panels | Code | Status |
| --- | --- | --- | --- |
| Real time distribution of Tsunami monitoring stations and buoys | GLOSS, DBCP | CREX | Considered by ET/DRC, May 2006 Requirements still unclear |
| GODAE High Resolution SST Pilot Project and requirements for SST type/method of measurement and depth | GHRSST-PP, SOT | BUFR | Considered by ET/DRC, May 2006 |
| VOSClim requirements (quality information flags as well as metadata) | SOT | BUFR | Under study by SOT |
| VOS data | SOT | BUFR | Considered at PMO-3-INT, list has been proposed |
| ASAP data | SOT | BUFR | Existing template |
| XBT and XCTD data | SOT | BUFR | To be defined |
| ADCP data | SOT, DBCP | BUFR | To be defined |
| GOSUD (TSG data distributed in TRACKOB) | GOSUD SOT | BUFR | To be defined |
| Seakeepers ship data | SOT | BUFR, MT10 | To be defined |
| META-T requirements for real time distribution of metadata along with the observation (i.e. category 1 metadata) | META-T, DBCP, SOT, etc. | BUFR | To be defined |
| Buoy directional and non directional wave data | DBCP | BUFR | Considered by ET/DRC, Dec 2005, needs validation |
| GTSPP and water temperature profile data, including Argo profiling float data | GTSPP Argo DMT | BUFR | Considered by ET/DRC, Dec 2005, validated |
| NWP and requirements for upper air profiles | SOT (ASAPP) | BUFR | To be clarified |
| Marine Climatology | ETMC | BUFR | To be considered by ETMC-II |

5.3	All the above-mentioned requirements need to be relayed to the Commission for Basic Systems (CBS) Expert Team on Data Representation and Codes (ET-DRC) for adoption (see the Codes migration schedule as adopted at CBS Ext. 06 in Appendix D).  Each Panel is presently submitting its requirements separately.  Considering the diversity of the requirements, the number of groups involved, and cross-cutting issues, DMCG-II agreed that it would be more efficient if there was a group within the JCOMM DMPA responsible for collecting all JCOMM-related coding requirements, for compiling them in a consolidated JCOMM proposal and for submitting them to the CBS Expert Team.  A representative from the group could also attend the CBS ET-DRC Meeting on behalf of the JCOMM. The DMCG-II therefore established a Table Driven Codes Group. Its Terms of References and Membership is given in Appendix B.

5.4	A strategic plan for JCOMM Data Management is nearing completion. Draft recommendations related to the migration to table driven codes include the following:

Recommendation 4.2a: DMPA lead the development of the detailed plan to change GTS data reporting from TACs to TDCs.

Recommendation 4.2b: The DMPA in association with the appropriate WMO committee should evaluate MT10 for its relevance to present needs.

Recommendation 4.2c: Enhanced interaction between JCOMM and CBS or other appropriate WMO committees is needed to expand the scope of TDCs to more fully incorporate JCOMM considerations, including software reliability, human readability, and the archival and exchange of historical and delayed-mode data in its originally reported form.

Recommendation 4.3.3b: JCOMM work with partners to encourage the continuing evolution of exchange formats to more robust forms, while at the same time assuring that sufficient flexibility and agility can be preserved for the archival of JCOMM’s delayed mode data and metadata.

6	The way forward for ship-based observations

6.1	The JCOMM Ship Observations Team (SOT) is working on this issue and is presently considering a large number of requirements. It is not yet in a position to make a comprehensive proposal at this meeting because:

- working groups such as the SOT Task Team on Coding (of SST), the ad-hoc SOT Task Team on BUFR for VOS/VOSClim established at the Third International Port Meteorological Officers Conference  (Hamburg, 23-24 March 2006), and the recently established water temperature metadata (META-T) Pilot Project, need to provide the SOT with their conclusions or recommendations before the SOT-IV, and

- approval from the 4th SOT meeting in early 2007 will be required before any proposal can be made to the ET/DRC, Darmstadt, Germany, 23-27 April 2007.

6.2	Proposals for new SHIP (VOS and VOSClim), XBT/XCTD, and TRACKOB templates are being defined and will eventually be proposed. The SOT is invited to consider how the ASAP and ADCP templates need to be addressed. The SOT will be invited to review the requirements expressed by ETMC-II. The following requirements are being considered:

- Requirements for the GODAE High Resolution SST Pilot Project (GHRSST).

- VOSClim requirements (metadata and quality information flags)

- META-T Pilot Project (metadata of category 1 required for real-time exchange)

- XBT/XCTD requirements

- GTSPP, SOOPIP, TIP, and Argo requirements: Consistency between templates XBT/XCTD and Argo templates (both providing sub-surface temperature profiles)

- GOSUD requirements: Consistency between VOS and TRACKOB

- Consistency between all ship templates as far as metadata

- Requirements for high resolution upper air soundings (ASAP)

- Requirements for ocean current profiles (ADCP)

- Requirements for marine climatology (ETMC-II recommendations)

- Requirements for Seakeepers

_____________

Appendices:  12

Appendix A

Terms of References of the SOT Task Team on Coding

Tasks:

1.	Develop a draft new code table for BUFR, which accommodates new types of SST measurements.

2.	Submit the draft proposal to a relevant body of the CBS.

3.	Investigate possible future inclusion of bio-chemical data in BUFR through various interactions with other ship-based observation communities.

4.	Report to SOT-IV.

Members:

Craig Donlon (TT chairperson, United Kingdom)

Graeme Ball (Australia)

Etienne Charpentier (JCOMMOPS)

Bob Keeley (Canada)

Loïc Petit de la Villéon (France)

_____________

Appendix B

TERMS OF REFERENCE (TOR) OF THE

JCOMM DMPA TASK TEAM ON TABLE DRIVEN CODE FORMS

Objectives:

- collect and compile requirements from the JCOMM Panels and Expert Teams and submit them to the CBS Expert Team on Data Representation and Codes (ET-DRC) (one Member of the Group to attend the ET-DRC Meetings);

- to make BUFR Master Table 10 (MT10) compliant with the WMO Rules;

- defining a mechanism for updating and maintaining the MT10 on behalf of the JCOMM in compliance with rules defined by the CBS ET-DRC.  Coastal variables and bio-chemical data will have to be included;

- look at templates and suggest how to standardize content.

Current Membership:

Bob Keeley (TT Chairperson), (a metadata expert designated by the NMDIS), Mr Etienne Charpentier (WMO Secretariat), Ms Hester Viola (Technical Coordinator of the SOT), an expert designated by David Thomas, an IODE expert designated by Leslie Rickards, Scott Woodruff (Chairperson, ET-MC), and an E2EDM expert designated by Nick Mikhailov.

_____________

Appendix C

PMO-III RECOMMENDATIONS ON MIGRATION FROM SHIP TO BUFR

- Frits Koek and Sarah North undertook to review the required data and metadata elements that would be required in a VOS (including VOSClim) BUFR template. The resultant list would then be submitted to a new informal ad hoc SOT task team on VOS migration to BUFR (Frits Koek, Sarah North, Pierre Blouch, Graeme Ball, Julie Fletcher, Etienne Charpentier) by 1 June 2006. Comments submitted by the team by 1 July 2006.

- WMO will liaise with CBS ET/DRC and ET/MTDCF and advise that the SOT is working on revisiting the list of elements for inclusion in the VOS BUFR template for ship data and is seeking ET/DRC help.

- The SOT and ET/DRC will liaise to develop a draft BUFR template suitable for VOS and VOSClim, which will be submitted for endorsement by SOT-IV.

The meeting considered possible implementation scenarios as follows:

  - Phase 1, target 2007: Member countries to work on software that converts SHIP to BUFR (1 to 1 conversion) and implement it on a case-by-case basis.

  - Phase 2, target 2006 to SOT-IV: analyze requirements and consider possible solutions (e.g. (proprietary format + metadata) to BUFR, or (“SOT” format + metadata) to BUFR. “SOT” format is a format inspired on FM-13 SHIP format and should be regarded as proprietary; it is not intended for direct GTS distribution but as a practical way of using existing software slightly modified to achieve BUFR distribution of the data on the GTS.

  - Phase 3, target 2008: Implementation of proposed recommendations.

  - Phase 4, target 2012: Operational system in place.

_____________

Appendix D

##### Code Migration Schedule

| Category ( | Cat.1: common | Cat.2: satellite observations | Cat.3: aviation(1) | Cat. 4: maritime | Cat. 5(2): miscellaneous | Cat. 6(2): almost obsolete |
| --- | --- | --- | --- | --- | --- | --- |
| Lists of ( Traditional code forms Schedule ( | SYNOP SYNOP MOBIL PILOT PILOT MOBIL TEMP TEMP MOBIL TEMP DROP CLIMAT CLIMAT TEMP | SAREP SATEM SARAD SATOB | METAR SPECI TAF AMDAR ROFOR | BUOY TRACKOB BATHY TESAC WAVEOB SHIP CLIMAT SHIP PILOT SHIP TEMP SHIP CLIMAT TEMP SHIP | RADOB IAC IAC FLEET GRID(to GRIB) RADOF | CODAR ICEAN GRAF NACLI etc. SFAZI SFLOC SFAZU RADREP ROCOB ROCOB SHIP ARFOR WINTEM MAFOR HYDRA HYFOR |
| Start experimental Exchange (3) | Nov. 2002 for some data (AWS SYNOP, TEMP USA) | Current at some Centres | 2006 2002 at some Centres for AMDAR | 2005 2003 for Argos data (BUOY, sub-surface floats, XBT/XCTD) | 2004 | Not applicable |
| Start operational exchange (3) | Nov. 2005 | Current at some Centres | 2008 2003 for AMDAR | 2007 2003 for Argos data (BUOY, sub-surface floats, XBT/XCTD) | 2006 | Not applicable |
| Migration complete | Nov. 2010 | Nov. 2006 | 2016 2005 for AMDAR | 2012 2008 for Argos data (BUOY, sub-surface floats, XBT/XCTD) | 2008 | Not applicable |

Notes:

- Aviation Codes require ICAO coordination and approval, except for AMDAR

- For category 5 consider that codes need to be reviewed in order to decide whether or not they should be migrated to BUFR/CREX.  Codes in category 6 are not to be migrated.

- All dates above are meant as "not later than".  However, Members and Organizations are encouraged to start experimental exchange, and, if all relevant conditions (see below) are satisfied, to start operational exchange as soon as possible.

- Start of experimental exchange: data will be made available in BUFR (CREX) but not operationally, i.e. in addition to the current alphanumeric codes, which are still operational.

- Start of operational exchange: data will be made available in BUFR (CREX) whereby some (but not all) Members rely on them operationally.  Still the current alphanumeric codes will be distributed (parallel distribution).

- Migration complete: at this date the BUFR (CREX) exchange becomes the standard WMO practice.  Parallel distribution is terminated.  For archiving purposes and at places where BUFR (CREX) exchange still causes problems the alphanumeric codes may be used on a local basis only.

Relevant conditions to be satisfied before experimental exchange may start:

- Corresponding BUFR/CREX-tables and templates are available;

- Training of concerned testing parties has been completed;

- Required software of testing parties (encoding, decoding, viewing) is implemented;

Relevant conditions to be satisfied before operational exchange may start:

- Corresponding BUFR/CREX-tables and templates are fully validated;

- Training of all concerned parties has been completed;

- All required software (encoding, decoding, viewing) is operational.

_____________

Appendix E

List of proposed fields for inclusion in a new BUFR template for VOS data

|  | Element | Code | WMO code table | Units | Scale | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Identifier for a ship report (BBXX) | MiMiMjMj | 2582 |  |  |  |
| 2 | Ships call sign | D....D |  |  |  |  |
| 3 | WMO Regional Association | A1 | 0161 |  |  |  |
| 4 | Subdivision of the WMO Regional Association | bw | 0161 |  |  |  |
| 5 | Type and Serial number of bouy or platform | nbnbnb |  |  | 0 |  |
| 6 | Day of the month | YY |  | Day | 0 |  |
| 7 | Time of observation to the nearest hour UTC | GG |  | Hour | 0 |  |
| 8 | Time of observation to the nearest minutes UTC | gg |  | Minute | 0 |  |
| 9 | Wind speed indicator | iw | 1855 |  |  |  |
| 10 | Latitude in degrees and tenths | LaLaLa |  | Degree | 1 |  |
| 11 | Longitude in degrees and tenths, hundreds included | LoLoLoLo |  | Degree | 1 |  |
| 12 | Precipitation data indicator | iR | 1819 |  |  |  |
| 13 | Type of station and present and past weather indicator | ix | 1860 |  |  |  |
| 14 | Height above sea of the base of the lowest cloud seen | h | 1600 |  |  |  |
| 15 | Horizontal visibility at surface | VV | 4377 |  |  |  |
| 16 | Total amount of cloud | N | 2700 |  |  |  |
| 17 | True direction from which the surface wind is blowing | dd | 0877 | Degrees true | -1 |  |
| 18 | Surface Wind speed | ff |  | from iw | 0 |  |
| 19 | Wind speed, when speed >= 99 | 00fff |  | from iw | 0 |  |
| 20 | Sign of air temperature | Sn | 3845 |  |  |  |
| 21 | Air temperature | TTT |  | C | 1 |  |
| 22 | Sign of dew point temperature | Sn | 3845 |  |  |  |
| 23 | Dew point temperature | TdTdTd |  | C | 1 |  |
| 24 | Relative humidity of the air, in per cent, the first figure being zero except for UUU = 100 per cent | UUU |  | % | 0 |  |
| 25 | Sea level pressure | PPPP |  | Pa | 1 |  |
| 26 | Characteristic of the pressure tendency during the three hours preceding the time of the observation | a | 0200 |  |  |  |
| 27 | Amount of pressure tendency at station level during the three hours preceding the time of observation | ppp |  | Pa | 1 |  |
| 28 | Amount of precipitation which has fallen during the period preceding the time of observation, as indicated by tR | RRR | 3590 |  |  |  |
| 29 | Duration of period of reference for amount of precipitation, ending at the time of the report | tR | 4019 |  |  |  |
| 30 | Present weather | ww | 4677 |  |  |  |
| 31 | Past weather (primary type) | W1 | 4561 |  |  |  |
| 32 | Past weather (secondary type) | W2 | 4561 |  |  |  |
| 33 | Present weather reported from an automatic weather station | wawa | 4680 |  |  |  |
| 34 | Past weather reported from an automatic weather station (primary type) | Wa1 | 4531 |  |  |  |
| 35 | Past weather reported from an automatic weather station (secondary type) | Wa2 | 4531 |  |  |  |
| 36 | Amount of all the CL cloud present or, if no CL cloud is present, the amount of all the CM cloud present | Nh | 2700 |  |  |  |
| 37 | Clouds of types Stratocumulus, Stratus, Cumulus and Cumulonimbus | CL | 0513 |  |  |  |
| 38 | Clouds of types Altocumulus, Altostratus, and Nimbostratus | CM | 0515 |  |  |  |
| 39 | Clouds of types Cirrus, Cirrocumulus, and Cirrostratus | CH | 0509 |  |  |  |
| 40 | Ships course (true) made good during the three hours preceding the time of the observation | Ds | 0700 |  |  |  |
| 41 | Ships average speed made good during the three hours preceding the time of the observation | Vs | 4451 |  |  |  |
| 42 | Sign and type of sea temperature | Ss | 3850 |  |  |  |
| 43 | Sea surface temperature | TwTwTw |  | C | 1 |  |
| 44 | Period of waves, obtained by instrumental methods | PwaPwa |  | s | 0 |  |
| 45 | Height of waves, obtained by instrumental methods | HwaHwa |  | m | log(2) |  |
| 46 | Period of the wind waves | PwPw |  | s | 0 |  |
| 47 | Height of the wind waves | HwHw |  | m | log(2) |  |
| 48 | Direction (true) from which the predominant/first swell waves are coming | dw1dw1 | 0877 | degrees true | -1 |  |
| 49 | Direction (true) from which the secondary swell waves are coming | dw2dw2 | 0877 | degrees true | -1 |  |
| 50 | Period of predominant swell waves | Pw1Pw1 |  | s | 0 |  |
| 51 | Height of predominant swell waves | Hw1Hw1 |  | m | log(2) |  |
| 52 | Period of the secondary swell waves | Pw2Pw2 |  | s | 0 |  |
| 53 | Height of secondary swell waves | Hw2Hw2 |  | m | log(2) |  |
| 54 | Ice accretion on ships | Is | 1751 |  |  |  |
| 55 | Thickness of ice accretion on ships in centimeters | EsEs |  | m | 2 |  |
| 56 | Rate of ice accretion on ships | Rs | 3551 |  |  |  |
| 57 | Icing plain language |  |  |  |  |  |
| 58 | Height of waves, obtained by instrumental methods | HwaHwaHwa |  | m | 1 |  |
| 59 | Indicator for the sign and type of measurement of sea surface temperature | Sw | 3855 |  |  |  |
| 60 | Wet-bulb temperature | TbTbTb |  | C | 1 |  |
| 61 | Concentration or arrangement of sea ice | ci | 0639 |  |  |  |
| 62 | Stage of development | Si | 3739 |  |  |  |
| 63 | Ice of land origin | bi | 0439 |  |  |  |
| 64 | Bearing of principal ice edge | Di | 0739 |  |  |  |
| 65 | Present ice situation and trend of conditions over preceding three hours | zi | 5239 |  |  |  |
| 66 | Sea ice plain language |  |  |  |  |  |
| 67 | Sign of maximum air temperature | sn | 3845 |  |  |  |
| 68 | Maximum air temperature | TxTxTx |  | C | 1 |  |
| 69 | Sign of minimum air temperature | sn | 3845 |  |  |  |
| 70 | Minimum air temperature | TnTnTn |  | C | 1 |  |
| 71 | Amount of individual cloud layer or mass whose genus is indicated by C | Ns | 2700 |  |  |  |
| 72 | Genus of cloud | C | 0500 |  |  |  |
| 73 | Height of base of cloud layer or mass whose genus is indicated by C | hshs | 1677 |  |  |  |
| 74 | Supplementary information | SpSpspsp | 3778 |  |  |  |
| 75 | Total amount of precipitation during the 24-hour period ending at the time of observation, in tenths of a millimetre | R24R24R24R24 |  | m | 4 |  |
| 76 | Highest gust during the 10-minute period immediately preceding the observation | FmFm |  | m/s | 0 | This may be reported under the 9 group -SpSpspsp (see table 3778 910ff ) |
| 77 | Highest gust during the period covered by W1W2 | FxFx |  | m/s | 0 | This may be reported under the 9 group -SpSpspsp (see table 3778 911ff ) |
|  | Additional elements for VOSClim |  |  |  |  |  |
| 78 | Ship's heading; the direction to which the bow of the ship is pointing referenced to True North | HDG |  | degrees true | 0 |  |
| 79 | Ship's ground course; the direction that the vessel actually moves over the fixed globe referenced to True North | COG |  | degrees true | 0 |  |
| 80 | Ship's ground speed; the speed of the vessel over the fixed earth | SOG |  | knots | 0 |  |
| 81 | Maximum height of the deck cargo above the Summer load line | SLL |  | m | 0 |  |
| 82 | Sign of hh | sL |  |  |  |  |
| 83 | Departure of reference level (Summer load line) from actual sea level. Positive when Summer load line is above sea level and negative if below the water line | hh |  |  |  |  |
| 84 | Relative wind direction in degrees off the bow | RWD |  | degrees | 0 |  |
| 85 | Relative wind speed reported in units indicated by iw | RWS |  | from iw | 0 |  |
|  | Additional requirements for the VOS |  |  |  |  |  |
| 86 | Height of the barometer above the Summer load line (fixed) |  |  | m |  |  |
| 87 | Height of the anemometer (if fitted) above the Summer load line (fixed) |  |  | m |  |  |
| 88 | Height of the temperature sensor/screen above the Summer load line (fixed) |  |  | m |  |  |
| 89 | Depth of the sea temperature sensor below the Summer load line (fixed) |  |  | m |  |  |
| 90 | Depth of the the keel below the Summer load line (fixed) |  |  | m |  |  |
| 91 | Average draught at the time of the observation (variable) |  |  | m |  |  |
| Note | use 90 + 91 (all known values) instead of 82 + 83 to derive heights and depths |  |  |  |  |  |

_____________

Appendix F

BUFR template for synoptic reports from sea stations

suitable for VOS observation data

B/C10 –Reporting SHIP data in TDCF

(details at http://www.wmo.int/web/www/WMOCodes/MigrationTDCF/MANUALTEMPLATES.html)

TM 308009 - BUFR template for synoptic reports from sea stations suitable for SHIP data

| 3 08 009 |  | Sequence for representation of synoptic reports from a sea station suitable for SHIP data |
| --- | --- | --- |
|  | 3 01 093 | Ship identification, movement, date/time, horizontal and vertical coordinates |
|  | 3 02 001 | Pressure data |
|  | 3 02 054 | SHIP “instantaneous” data |
|  | 0 08 002 | Vertical significance |
|  | 3 02 055 | Icing and ice |
|  | 3 02 057 | SHIP marine data |
|  | 3 02 060 | SHIP “period” data |

This BUFR template for synoptic reports from sea stations further expands as follows:

| 3 01 093 |  |  | Ship identification, movement, date/time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 036 | 0 01 011 | Ship or mobile land station identifier D….D | CCITT IA5, 0 |
|  |  | 0 01 012 | Direction of motion of moving observing platform(3) Ds | Degree true, 0 |
|  |  | 0 01 013 | Speed of motion of moving observing platform(4) vs | m s-1, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  |  | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  |  | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  |  | 0 05 002 | Latitude (coarse accuracy) LaLaLa | Degree, 2 |
|  |  | 0 06 002 | Longitude (coarse accuracy) LoLoLoLo | Degree, 2 |
|  | 0 07 030 |  | Height of station platform above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  |  |  | Pressure data |  |
| 3 02 001 | 0 10 004 |  | Pressure P0P0P0P0 | Pa, –1 |
|  | 0 10 051 |  | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  | 0 10 061 |  | 3-hour pressure change ppp | Pa, –1 |
|  | 0 10 063 |  | Characteristic of pressure tendency a | Code table, 0 |
| 3 02 054 |  |  | SHIP “instantaneous” data |  |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 052 | 0 07 032 | Height of sensor above marine deck platform (for temperature and humidity measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature and humidity measurement) | m, 1 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature (sc.2) snTTT | K, 2 |
|  |  | 0 02 039 | Method of wet-bulb temperature measurement | Code table, 0 |
|  |  | 0 12 102 | Wet-bulb temperature (scale 2) swTbTbTb | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |

|  |  |  | Visibility data |  |
| --- | --- | --- | --- | --- |
|  | 3 02 053 | 0 07 032 | Height of sensor above marine deck platform (for visibility measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for visibility measurement) | m, 1 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  | 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 3 02 034 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud hshs | m, -1 |
| 0 08 002 |  |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Icing and ice |  |
| 3 02 055 | 0 20 031 |  | Ice deposit (thickness) EsEs | m, 2 |
|  | 0 20 032 |  | Rate of ice accretion Rs | Code table, 0 |
|  | 0 20 033 |  | Cause of ice accretion Is | Flag table, 0 |
|  | 0 20 034 |  | Sea ice concentration ci | Code table, 0 |
|  | 0 20 035 |  | Amount and type of ice bi | Code table, 0 |
|  | 0 20 036 |  | Ice situation zi | Code table, 0 |
|  | 0 20 037 |  | Ice development Si | Code table, 0 |
|  | 0 20 038 |  | Bearing of ice edge Di | Degree true, 0 |
| 3 02 057 |  |  | SHIP marine data |  |
|  | 3 02 056 |  | Sea surface temperature, method of measurement, and depth below sea surface |  |
|  |  | 0 02 038 | Method of sea/water temperature measurement | Code table, 0 |
|  |  | 0 07 063 | Depth below sea/water surface (for sea surface temperature measurement) | m, 2 |
|  |  | 0 22 043 | Sea/water temperature ssTwTwTw | K, 2 |
|  |  | 0 07 063 | Depth below sea/water surface (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Waves |  |
|  | 3 02 021 | 0 22 001 | Direction of waves | Degree true |
|  |  | 0 22 011 | Period of waves PwaPwa | s, 0 |
|  |  | 0 22 021 | Height of waves HwaHwa | m, 1 |
|  | 3 02 024 | 0 22 002 | Direction of wind waves | Degree true, 0 |
|  |  | 0 22 012 | Period of wind waves PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves HwHw | m, 1 |
|  |  | 1 01 002 | Replicate 1 descriptor 2 times |  |
|  |  | 3 02 023 | Swell waves (2 systems of swell) dw1dw1, Pw1Pw1, Hw1Hw1 dw2dw2, Pw2Pw2, Hw2Hw2 |  |
| 3 02 060 |  |  | SHIP“period” data |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Precipitation measurement |  |
|  | 3 02 040 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 3 02 058 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 059 | 0 07 032 | Height of sensor above marine deck platform (for wind measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for wind measurement) | m, 1 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)	Within RA-III, the maximum daytime temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)	0 01 012: Means course made good (average course over the ground) during the three hours preceding the time of observation.

4)	0 01 013: Means speed made good (average speed over the ground) during the three hours preceding the time of observation.

5)	If “plain language” text is reported within Section 2, this information can be conveyed in BUFR via the use of an appropriate 205YYY field as an extra descriptor following the above basic template.

_____________

Appendix G

BUFR Template for VOS data

This template is a modified version of the SHIP observation template. Delayed replications have been used extensively to reduce the volume of an individual message, which is a crucial aspect for transmission from VOS stations. It is proposed to represent this template by a single descriptor 3 08 008 from Category 8 – Surface report sequences (sea).

Sequence descriptor numbers written in blue in this template, have not yet been included in BUFR table D (release November 2005).

3 08 008  =  3 01 093  +  3 02 062   +  3 02 063

| 3 01 093 |  |  | Ship identification, movement, type, date/time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 036 | 0 01 011 | Ship or mobile land station identifier D….D | CCITT IA5, 0 |
|  |  | 0 01 012 | Direction of motion of moving observing platform(3) Ds | Degree true, 0 |
|  |  | 0 01 013 | Speed of motion of moving observing platform(4) vs | m s-1, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  |  | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  |  | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  |  | 0 05 002 | Latitude (coarse accuracy) LaLaLa | Degree, 2 |
|  |  | 0 06 002 | Longitude (coarse accuracy) LoLoLoLo | Degree, 2 |
|  | 0 07 030 |  | Height of station platform above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
| 3 02 062 |  |  | SHIP “instantaneous” data from VOS |  |
|  |  |  | Pressure data |  |
|  | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 052 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 02 039 | Method of wet-bulb temperature measurement | Code table, 0 |
|  |  | 0 12 102 | Wet-bulb temperature (scale 2) swTbTbTb | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 053 | 0 07 032 | Height of sensor above marine deck platform (for visibility measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for visibility measurement) | m, 1 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  | 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 034 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
|  | 0 08 002 |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Icing and ice |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 055 | 0 20 031 | Ice deposit (thickness) EsEs | m, 2 |
|  |  | 0 20 032 | Rate of ice accretion Rs | Code table, 0 |
|  |  | 0 20 033 | Cause of ice accretion Is | Flag table, 0 |
|  |  | 0 20 034 | Sea ice concentration ci | Code table, 0 |
|  |  | 0 20 035 | Amount and type of ice bi | Code table, 0 |
|  |  | 0 20 036 | Ice situation zi | Code table, 0 |
|  |  | 0 20 037 | Ice development Si | Code table, 0 |
|  |  | 0 20 038 | Bearing of ice edge Di | Degree true, 0 |
|  |  |  | Sea/water temperature |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 056 | 0 02 038 | Method of sea surface temperature measurement | Code table, 0 |
|  |  | 0 22 043 | Sea/water temperature ssTwTwTw | K, 2 |
|  |  |  | Waves |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 021 | 0 22 001 | Direction of waves | Degree true, 0 |
|  |  | 0 22 011 | Period of waves PwaPwa | s, 0 |
|  |  | 0 22 021 | Height of waves HwaHwa | m, 1 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 024 | 0 22 002 | Direction of wind waves | Degree true, 0 |
|  |  | 0 22 012 | Period of wind waves PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves HwHw | m, 1 |
|  |  | 1 01 002 | Replicate 1 descriptor 2 times |  |
|  |  | 3 02 023 | Swell waves (2 systems of swell) dw1dw1, Pw1Pw1, Hw1Hw1 dw2dw2, Pw2Pw2, Hw2Hw2 |  |
| 3 02 063 |  |  | SHIP“period” data from VOS |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Precipitation measurement |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 040 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 058 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  |  | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 064 | 0 07 032 | Height of sensor above marine deck platform (for wind measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for wind measurement) | m, 1 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 1 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  |  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 1 |

Notes:

1) Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2) Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3) 0 01 012: Means course made good (average course over the ground) during the three hours preceding the time of observation.

4) 0 01 013: Means speed made good (average speed over the ground) during the three hours preceding the time of observation.

5) If “plain language” text is reported within Section 2, this information can be conveyed in BUFR via the use of an appropriate 205YYY field as an extra descriptor following the above basic template.

_____________

Appendix H

BUFR Template for ASAP data

B/C25 – Reporting TEMP, TEMP SHIP and TEMP MOBIL data in TDCF

(details at http://www.wmo.int/web/www/WMOCodes/MigrationTDCF/MANUALTEMPLATES.html)

A BUFR (or CREX) message should be sent when level the 100 hPa is reached.  In any case, a BUFR (or CREX) message shall be produced when the sounding is completed containing data from the entire sounding.

TM 309052 - BUFR template for P, T, U and wind vertical profiles suitable for TEMP, TEMP SHIP and TEMP MOBIL observation data

| 3 09 052 |  | Sequence for representation TEMP, TEMP SHIP and TEMP MOBIL observation type data |
| --- | --- | --- |
|  | 3 01 111 | Identification of launch site and instrumentation |
|  | 3 01 113 | Date/time of launch |
|  | 3 01 114 | Horizontal and vertical coordinates of launch site |
|  | 3 02 049 | Cloud information reported with vertical soundings |
|  | 0 22 043 | Sea/water temperature (for ship stations) |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 002 | Extended delayed descriptor replication factor |
|  | 3 03 054 | Temperature, dew-point and wind data at a pressure level |
|  | 1 01 000 | Delayed replication of 1 descriptor |
|  | 0 31 001 | Delayed descriptor replication factor |
|  | 3 03 051 | Wind shear data at a pressure level |

This BUFR template for P, T, U and wind profiles further expands as follows:

| 3 01 111 |  | Identification of launch site and instrumentation |  |
| --- | --- | --- | --- |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 013 | Solar and infrared radiation correction | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark (for mobile stations) | Code table |

| 3 02 049 |  | Cloud information reported with vertical soundings |  |
| --- | --- | --- | --- |
|  | 0 08 002 | Vertical significance | Code table |
|  | 0 20 011 | Cloud amount (of low or middle clouds Nh) | Code table |
|  | 0 20 013 | Height of base of cloud (h) | m, scale –1 |
|  | 0 20 012 | Cloud type (low clouds CL) | Code table |
|  | 0 20 012 | Cloud type (middle clouds CM) | Code table |
|  | 0 20 012 | Cloud type (high clouds CH) | Code table |
|  | 0 08 002 | Vertical significance ( = missing value) | Code table |
| 0 22 043 |  | Sea/water temperature (for ship stations) | K, scale 2 |
|  |  | Temperature, dew-point and wind data at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 054 |  | Temperature, dew-point and wind data at a pressure level with radiosonde position |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 10 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, scale 2 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 3 03 051 |  | Wind shear data at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 061 | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
|  | 0 11 062 | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

Notes:

- Time of launch 3 01 013 shall be reported with the highest possible accuracy available.  If the launch time is not available with second accuracy, the entry for seconds shall be put to zero.

- Long time displacement 0 04 086 represents the time offset from the launch time 3 01 013 (in seconds)

- Latitude displacement 0 05 015 represents the latitude offset from the latitude of the launch site.  Longitude displacement 0 06 015 represents the longitude offset from the longitude of the launch site.

- If additional information on sounding instrumentation is required, the sequence <3 09 052> may be supplemented by one or more additional parameters to allow data representation of this information, e.g. Radiosonde serial number (0 01 081).

_____________

Appendix I

# BUFR template for XBT/XCTD report (sequence 3 15 004)

| Name | Descriptor | Order | Forced value | Forced missing | Name | Comment |
| --- | --- | --- | --- | --- | --- | --- |
| XBT/XCTD | 001003 | 1 |  |  | WMO region |  |
| XBT/XCTD | 001020 | 2 |  |  | WMO region sub-area |  |
| XBT/XCTD | 001005 | 3 |  |  | Buoy/platform identifier |  |
| XBT/XCTD | 001011 | 4 |  |  | Ship call sign |  |
| XBT/XCTD | 001019 | 5 |  |  | Ship name |  |
| XBT/XCTD | 001080 | 6 |  |  | Ship line number according to SOOP |  |
| XBT/XCTD | 005036 | 7 |  |  | Ship transect number according to SOOP |  |
| XBT/XCTD | 001036 | 8 |  |  | Agency in charge of operating the observing platform |  |
| XBT/XCTD | 301011 | 9 |  |  | Date |  |
| XBT/XCTD | 301012 | 10 |  |  | Time |  |
| XBT/XCTD | 301021 | 11 |  |  | Latitude and longitude (high accuracy) |  |
| XBT/XCTD | 007030 | 12 |  |  | Height of station above MSL |  |
| XBT/XCTD | 002040 | 13 |  |  | Method of removing platform direction and speed from current |  |
| XBT/XCTD | 022067 | 14 |  |  | Instrument type for water temperature profile measurement |  |
| XBT/XCTD | 022068 | 15 |  |  | Water temperature profile recorder type |  |
| XBT/XCTD | 008080 | 16 | 0 |  | Qualifier for quality class | Value: 0=global water pressure profile |
| XBT/XCTD | 033050 | 17 |  |  | Global GTSPP quality class | For global water pressure profile as qualified above |
| XBT/XCTD | 008080 | 18 | 1 |  | Qualifier for quality class | Value: 1=global water temperature profile |
| XBT/XCTD | 033050 | 19 |  |  | Global GTSPP quality class | For global water temperature profile as qualified above |
| XBT/XCTD | 008080 | 20 | 2 |  | Qualifier for quality class | Value: 2=global water salinity profile |
| XBT/XCTD | 033050 | 21 |  |  | Global GTSPP quality class | For global water salinity profile as qualified above |
| XBT/XCTD | 008080 | 22 | 3 |  | Qualifier for quality class | Value: 3=global water conductivity profile |
| XBT/XCTD | 033050 | 23 |  |  | Global GTSPP quality class | For global water conductivity profile as qualified above |
| XBT/XCTD | 025100 | 24 |  |  | XBT/XCTD fall rate equation coefficient a |  |
| XBT/XCTD | 025101 | 25 |  |  | XBT/XCTD fall rate equation coefficient b |  |
| XBT/XCTD | 022063 | 26 |  |  | Total depth of water |  |
| XBT/XCTD | 302021 | 27 |  |  | Waves |  |
| XBT/XCTD | 306004 | 28 |  |  | Sea temperature and salinity profile | Sequence containing the profile itself |
| XBT/XCTD | 002030 | 29 |  |  | Method of current measurement |  |
| XBT/XCTD | 306005 | 30 |  |  | Time/duration of current measurement, depths/directions/speeds |  |
| XBT/XCTD | 007032 | 31 |  |  | Height of thermometer above station platform | Here height of thermometer |
| XBT/XCTD | 012101 | 32 |  |  | Dry-bulb temperature (scale 2) |  |
| XBT/XCTD | 012103 | 33 |  |  | Dew-point temperature (scale 2) |  |
| XBT/XCTD | 007032 | 34 |  |  | Height of anemometer above station platform | Here height of anemometer |
| XBT/XCTD | 011001 | 35 |  |  | Wind direction |  |
| XBT/XCTD | 011002 | 36 |  |  | Wind speed |  |

_____________

Appendix J

BUFR Template for TRACKOB data

(Approved by CBS Ext. 6)

BUFR template

3 08 010	0 01 011	Ship or mobile land station identifier

1 13 000	Delayed replication of 13 descriptors

0 31 001	Delayed descriptor replication factor

3 01 011	Date

3 01 012	Time

3 01 021	Latitude/Longitude (high accuracy)

0 04 080	Averaging period for following value

0 22 049	Sea surface temperature

0 04 080	Averaging period for following value

0 22 059	Sea surface salinity

0 04 080	Averaging period for following value

0 22 005	Direction of sea surface current

0 02 042	Indicator for sea surface current speed

0 22 032	Speed of sea surface current

0 02 042	Indicator for sea surface current speed (cancel)

0 04 080	Averaging period for following value (cancel)

CREX template

D 08 010	B 01 011	Ship or mobile land station identifier

R 13 000	Delayed replication of 13 descriptors

D 01 011	Date

D 01 012	Time

D 01 021	Latitude/Longitude (high accuracy)

B 04 080	Averaging period for following value

B 22 049	Sea surface temperature

B 04 080	Averaging period for following value

B 22 059	Sea surface salinity

B 04 080	Averaging period for following value

B 22 005	Direction of sea surface current

B 02 042	Indicator for sea surface current speed

B 22 032	Speed of sea surface current

B 02 042	Indicator for sea surface current speed (cancel)

B 04 080	Averaging period for following value (cancel)

_____________

Appendix K

B/C32 –Reporting CLIMAT SHIP data in TDCF

(details at http://www.wmo.int/web/www/WMOCodes/MigrationTDCF/MANUALTEMPLATES.html)

TM 308013 - BUFR template for reports of monthly values from an ocean weather station suitable for CLIMAT SHIP data

| 3 08 013 |  | Sequence for representation of monthly values suitable for CLIMAT SHIP data |
| --- | --- | --- |
|  | 3 08 011 | Monthly values from an ocean weather station |
|  | 3 08 012 | Monthly normals for an ocean weather station |

| Monthly values from an ocean weather station (data of CLIMAT SHIP Section 1) Sequence BUFR descriptor <3 08 011> expands as shown in the leftmost column below. |
| --- |
|  |  | Station identification, date/time, horizontal and vertical coordinates | Unit, scale |
| 0 01 011 |  | Ship's call sign | CCITT IA5, 0 |
| 0 02 001 |  | Type of station | Code table, 0 |
| 3 01 011 | 0 04 001 | Year(1) | Year, 0 |
|  | 0 04 002 | Month(1) | Month, 0 |
|  | 0 04 003 | Day (= 1) (1) | Day, 0 |
| 3 01 012 | 0 04 004 | Hour (= 0) (1) | Hour, 0 |
|  | 0 04 005 | Minute (= 0) (1) | Minute, 0 |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) LaLaLa | Degree, 2 |
|  | 0 06 002 | Longitude (coarse accuracy) LoLoLoLo | Degree, 2 |
| 0 07 030 |  | Height of station platform above mean sea level | m, 1 |
| 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  |  | Monthly mean values of pressure, temperature, vapour pressure and sea/water temperature |  |
| 0 04 074 |  | Short time displacement (= UTC - LST) (1) | Hour, 0 |
| 0 04 023 |  | Time period (= number of days in the month) | Day, 0 |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table, 0 |
| 0 10 051 |  | ______ Pressure reduced to msl PPPP | Pa, –1 |
| 0 07 032 |  | Height of sensor above marine deck platform (for temperature measurement) (3) | m, 2 |
| 0 07 033 |  | Height of sensor above water surface (for temperature measurement) (3) | m, 1 |
| 0 12 101 |  | _____ Temperature/dry-bulb temperature snTTT | K, 2 |
| 0 13 004 |  | ____ Vapour pressure eee | Pa, -1 |
| 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 3 02 056 |  | Sea surface temperature, method of measurement, and depth below sea surface |  |
|  | 0 02 038 | Method of sea/water temperature measurement(3) | Code table, 0 |
|  | 0 07 063 | Depth below sea/water surface (for sea surface temperature measurement) (3) | m, 2 |
|  | 0 22 043 | ________ Sea/water temperature snTwTwTw | K, 2 |
|  | 0 07 063 | Depth below sea/water surface (set to missing to cancel the previous value) | m, 2 |
| 0 08 023 |  | First order statistics (set to missing to cancel the previous value) | Code table, 0 |
|  |  | Monthly precipitation data |  |
| 0 04 003 |  | Day (= 1) (2) | Day, 0 |
| 0 04 004 |  | Hour (= 6) (2) | Hour, 0 |
| 0 04 023 |  | Time period (= number of days in the month) (2) | Day, 0 |
| 0 07 032 |  | Height of sensor above marine deck platform(3) | m, 2 |
| 0 13 060 |  | Total accumulated precipitation R1R1R1R1 | kg m-2, 1 |
| 0 13 051 |  | Frequency group; precipitation Rd | Code table, 0 |
| 0 04 053 |  | Number of days with precipitation equal to or more than 1 mm nrnr | Numeric, 0 |
| 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
| Monthly normals for an ocean weather station (data of CLIMAT SHIP Section 2) Sequence BUFR descriptor <3 08 012> expands as shown in the leftmost column below. |
|  |  | Normals of pressure, temperature, vapour pressure and sea/water temperature | Unit, scale |
| 0 04 001 |  | Year (of beginning of the reference period) | Year, 0 |
| 0 04 001 |  | Year (of ending of the reference period) | Year, 0 |
| 0 04 002 |  | Month | Month, 0 |
| 0 04 003 |  | Day (= 1) (1) | Day, 0 |
| 0 04 004 |  | Hour (= 0) (1) | Hour, 0 |
| 0 04 074 |  | Short time displacement (= UTC - LST) (1) | Hour, 0 |
| 0 04 022 |  | Time period (= 1) | Month, 0 |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table, 0 |
| 0 10 051 |  | ______ Pressure reduced to msl PPPP | Pa, –1 |
| 0 07 032 |  | Height of sensor above marine deck platform (for temperature measurement) (3) | m, 2 |
| 0 07 033 |  | Height of sensor above water surface (for temperature measurement) (3) | m, 1 |
| 0 12 101 |  | _____ Temperature/dry-bulb temperature snTTT | K, 2 |
| 0 13 004 |  | ____ Vapour pressure eee | Pa, -1 |
| 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value | m, 2 |
| 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
| 3 02 056 |  | Sea surface temperature, method of measurement, and depth below sea surface |  |
|  | 0 02 038 | Method of sea/water temperature measurement(3) | Code table, 0 |
|  | 0 07 063 | Depth below sea/water surface (for sea surface temperature measurement) (3) | m, 2 |
|  | 0 22 043 | ________ Sea/water temperature snTwTwTw | K, 2 |
|  | 0 07 063 | Depth below sea/water surface (set to missing to cancel the previous value) | m, 2 |
| 0 08 023 |  | First order statistics (set to missing to cancel the previous value) | Code table, 0 |
|  |  | Normals of precipitation |  |
| 0 04 001 |  | Year (of beginning of the reference period) | Year, 0 |
| 0 04 001 |  | Year (of ending of the reference period) | Year, 0 |
| 0 04 002 |  | Month | Month, 0 |
| 0 04 003 |  | Day (= 1) (2) | Day, 0 |
| 0 04 004 |  | Hour (= 6) (2) | Hour, 0 |
| 0 04 022 |  | Time period (= 1) | Month, 0 |
| 0 07 032 |  | Height of sensor above marine deck platform (for precipitation measurement) (3) | m, 2 |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table, 0 |
| 0 13 060 |  | Total accumulated precipitation R1R1R1R1 | kg m-2, 1 |
| 0 04 053 |  | Number of days with precipitation equal to or more than 1 mm nrnr | Numeric, 0 |
| 0 08 023 |  | First order statistics (set to missing to cancel the previous value) | Code table, 0 |

Notes:

- The time identification refers to the beginning of the one-month period. Except for precipitation measurements, the one-month period is recommended to correspond to the local standard time (LST) month [7].

- In case of precipitation measurements, the one-month period begins at 06 UTC on the first day of the month and ends at 06 UTC on the first day of the following month [5].

- If the heights/depth of sensors or method of sea/water temperature measurement were changed during the period specified, the value shall be that which existed for the greater part of the period.

_____________

Appendix L

B/C35 – Reporting CLIMAT TEMP and CLIMAT TEMP SHIP and data in TDCF

(details at http://www.wmo.int/web/www/WMOCodes/MigrationTDCF/MANUALTEMPLATES.html)

A BUFR (or CREX) message shall contain reports for one specific month only.

TM 309054 - BUFR template for reports of monthly aerological means suitable for CLIMAT TEMP and CLIMAT TEMP SHIP data

| 3 09 054 |  | Sequence for representation CLIMAT TEMP and CLIMAT TEMP SHIP data |
| --- | --- | --- |

Sequence BUFR descriptor <3 09 054> expands as it is shown in the leftmost column below:

|  |  | Identification of launch site | Unit, scale |
| --- | --- | --- | --- |
| 3 01 001 | 0 01 001 | WMO block number | Numeric, 0 |
|  | 0 01 002 | WMO station number | Numeric, 0 |
| 0 01 011 |  | Ship's call sign | CCITT IA5, 0 |
|  |  | Date/time(1) |  |
| 3 01 011 | 0 04 001 | Year(1) | Year, 0 |
|  | 0 04 002 | Month(1) | Month, 0 |
|  | 0 04 003 | Day (= 1) (1) | Day, 0 |
| 3 01 012 | 0 04 004 | Hour (= 0) (1) | Hour, 0 |
|  | 0 04 005 | Minute (= 0) (1) | Minute, 0 |
|  |  | Horizontal and vertical coordinates |  |
| 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, 5 |
|  | 0 06 001 | Longitude (high accuracy) | Degree, 5 |
| 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
| 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
| 0 07 007 |  | Height release of sonde above mean sea level | m, 0 |
|  |  | Monthly mean data |  |
| 0 04 023 |  | Time period (= number of days in the month) | Day, 0 |
| 0 04 059 |  | Times of observations used to compute the reported mean values | Flag table, 0 |
| 1 15 000 |  | Delayed replication of 15 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
| 0 08 001 |  | Vertical sounding significance | Flag table, 0 |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table, 0 |
| 0 07 004 |  | Pressure | Pa, –1 |
| 0 10 009 |  | Geopotential height | gpm, 0 |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, 2 |
| 0 12 103 |  | Dew-point temperature | K, 2 |
| 0 08 023 |  | First order statistics (= 32; vector mean) | Code table, 0 |
| 0 11 001 |  | Wind direction | Degree true, 0 |
| 0 11 002 |  | Wind speed | m s-1, 1 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table, 0 |
| 0 11 019 |  | Steadiness of wind | %, 0 |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 2; temperature) | Code table, 0 |
| 0 08 020 |  | Total number of missing entities (days) | Numeric, 0 |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 9; wind) | Code table, 0 |
| 0 08 020 |  | Total number of missing entities (days) | Numeric, 0 |

Note:

(1)  The time identification refers to the beginning of the one-month period.

_____________

# Footnotes

MT10 is a distinct set of BUFR tables for oceanographic data (MT0 contains the usual meteorological tables) that had been defined a few years ago and is now being reviewed to comply with the rules proposed by the CBS ET/DRC for establishing and maintaining separate Master Tables.