### GPS-BASED RADIOSONDE SYSTEM

|  | GPSonde GL98 (WMO code 77) SR2K Ground station |
| --- | --- |
| Main Features |
| GPSonde GL98 | SR2K Ground station |
| FULLY-CODED GPS RADIOSONDE PRESSURE DERIVED FROM GPS ALTITUDE SENSORS CALIBRATION STORED ON EEPROM GROUND CHECK FACILITY 400 TO 406 MHz DIGITAL SYNTHESISER 200 KHz STEP FREQUENCY SETTING DIGITAL TRANSMISSION IN 1 SEC CYCLES NARROW BANDWIDTH POWER SUPPLY WITH DRY CELL BATTERIES BATTERIES LIFE > 3HOURS NO SUSPENSION LENGTH LIMITATION | 19 Inch RACK FITTED 12-CHANNEL GPS RECEIVER REAL TIME DIFFERENTIAL GPS (DGPS) BOTH RAW AND PROCESSED DATA AVAILABLE EDITION OF WMO CODE MSG STANDARD COMPUTER ABILITIES FRIENDLY USE SOFTWARE WORKING ON NT4 & NT5 OPERATING SYSTEM REAL TIME GRAPHICAL VISUALIZATION BUILT-IN FREQUENCY SCANNER OMNIDIRECTIONAL AERIALS EASY TO INSTALL SONDE PROGRAMMING INTERFACE |

# SUMMARY OF TECHNICAL SPECIFICATIONS

GPSonde GL98 RADIOSONDE:

| GENERAL |  |  | BATTERIES |  |
| --- | --- | --- | --- | --- |
| Dimensions | : 113 x 155 x 146 mm |  | Technology | : 1.5V Alkaline |
| Weight | 405 g (including batteries) |  | Autonomy | : >3 h |
|  |  |  | Package | : 8-battery pack |

| TEMPERATURE |  |  | HUMIDITY |  |
| --- | --- | --- | --- | --- |
| Sensor type | : Thermistor |  | Sensor type | : Capacitor |
| Measurement range | : +50° to –90° |  | Measurement range | : 0% to 100% |
| Resolution | : 0.1°C |  | Resolution | : 0.1% |
| Absolute accuracy | : +/- 0.5°C |  | Absolute accuracy | : +/-5% |
| Response time | : <2s |  | Response time | : <2s |
| Measurement rate | : 1 Hz |  | Measurement rate | : 1 Hz |
| Calibration adjustment | : Calibration prior launch |  | Calibration adjustment | : Calibration prior launch |
| Factory calibration | : Stored in EPROM |  | Factory calibration | : Stored in EPROM |

| WIND MEASUREMENT |  | TRANSMITTER |  |
| --- | --- | --- | --- |
| General | : DGPS with C/A code altitude |  | Frequency range | : 400 to 406 MHz |
| Altitude Range | : Unlimited with authorisation |  | Frequency step | : 200 KHz |
| Position accuracy | : 10 m |  | Frequency setting | : Programming interface |
| Horizontal Wind accuracy | : 0.15 m/s |  | Maximum drift | : +/- 1 KHz |
| Wind direction accuracy | : 2 ° |  | Output Power | : 300 mW |
| Position resolution | : 0.01 m |  | Modulation type | : Digital PSK 4800 bauds |
| Horizontal wind resolution | : 0.01 m/s |  |  |  |
| Wind direction resolution | : 0.1 ° |  | CALIBRATION |  |
| Measurement rate | : 1 Hz |  | Factory calibration | : Stored on EPROM |
|  |  |  | Ground Check | : Prior launch |

###### SR2K GROUND STATION

| GENERAL |  |
| --- | --- |
| Dimensions | : 19’’ rack - Width: 450 mm – Depth: 320 mm – Height: 135 mm |
| Weight | : 12 kg |
| Consumption | : 150 W |
| Output | : Real time data, COM1, COM2, LP1, VGA, USB, PS2, Ethernet |
| Programming interface | : Front panel connector with cable |
| GPS | : 12-channel receiver |
| Computer functions | : Non dedicated PC allowing work on others Windows applications |
| Accessories | : All standard computer accessories can be connected: Printer, modem, … |
| TELEMETRY Built-in receiver Tracking range Modulation | : 400 – 406 MHz digital Synthesiser : 250 Km : PSK |  |