Publication No. 47

Layout and Abbreviations Used

Table 1.  Layout of Columns

| Column No. | Column/Field code name | Description of field |
| --- | --- | --- |
| 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38 39 40 41 42 | name call IMOn rcnty vssl vsslP vsslD brdg vsslM Atm blc rte barm bMS brmH brmL brmU brmC thrm thMS thmE thmL thmH tscale hygr hgrE sstM sstD barg anHL anHD anmL anDB anDC anmI anmU anmC wwH othI phGr prSt chgd | Ships name Ships call sign IMO number Recruiting Country Vessel type Vessel digital image (profile) Vessel Dimensions (in m)-length, breadth, average freeboard, average draft (max. summer loadline), average cargo height Position of bridge - distance from the bow Type of meteorological reporting ship Automation Baseline check Route(s) Type of barometer Model (brand) of barometer (manufacturer/series no.) Height of barometer (tenths of meters) Barometer location Pressure units Barometer calibration date Type of thermometer - dry bulb Model (brand) of thermometer (manufacturer/series no.) Conditions of exposure of thermometer Location of instruments used to measure dry bulb/hygrometer Height of thermometers Temperature scale; original units Type of hygrometer Conditions of exposure of hygrometer Method of obtaining sea surface temperature Depth of sea temperature measurement Type of barograph Height of anemometer (above the maximum load line) Height of anemometer (above the deck) Anemometer location Anemometer distance (from the bow) Anemometer distance (from the center) Anemometer Instrument type (manufacturer/series no.) General anemometer usage Anemometer calibration date Visual wind/wave observational height Other meteorological instruments Telephoney & telegraphy Teleprinter & satellite Change date |

Table 2. Explanation of abbreviations used in fields

| Column: No. Name | Abbre- viation | Description of abbreviation |
| --- | --- | --- |
| 1 | name |  | Ship name - full name of the ship |
| 2 | call |  | Call sign - 3 to 7 alphanumeric characters |
| 3 | IMOn |  | IMO number – this number is allocated by IMO and remains valid for the lifetime of the ship (Solas, Chapter 11). |
| 4 | rcnty | see list | Recruiting Country - International Organization for Standardization (ISO) country code (Alpha-2; two character alpha code) |
| 5 | vssl | BC CC F FV GC GT LT CS PV PL RR RF RV SV T Y BS OW CG MS DR TU IF B LV OT | Vessel type Bulk Carrier Closed container Ferry Other fishing vessel General Cargo Gas tanker Liquid tanker Container Ship Passenger vessel Passenger liner Ro/Ro container Ro/Ro ferry Research vessel Support vessel Trawler Yacht/pleasure craft Banana ship Ocean weather ship Coast guard ship Military ship Dredger Tug Inshore fishing vessel Barge Light vessel Other (specify in a footnote) |
| 6 | vsslP | AV NA PA | Vessel Digital Image - a photograph, schematic, diagram, or plan of the ships profile providing the ships shape. A publicity photo from the shipping Co. would be an ideal input source for this digital image to illustrate the ships shape. Otherwise, a photo taken by the PMO would suffice. Available in separate digital file Not available Photograph available, but not yet scanned and placed in separate digital file |
| 7 | vsslD |  | Vessel Dimension (in metres) -- length, breadth, average freeboard, average draft (max summer loadline), average cargo height above the deck |
| 8 | brdg |  | Bridge location on the ship - distance of the bridge from the bow in tenths of meters (e.g. 23.7 m) |
| 9 | vsslM | 10 20 21 22 40 60 61 70 80 81 88 89 90 99 | Type of Meteorological reporting ship (VOS category/observing programme) SELECTED SHIPS Selected Ships (special) Selected Ships (merchant) Selected Ships (trawlers) SUPPLEMENTARY SHIPS Supplementary Ships (merchant) Supplementary Ships (trawlers) AUXILIARY SHIPS Auxiliary Ships (occasional) Auxiliary Ships (trawlers) (88-90) Additional codes for ships recruited by the USA, but not registered in the USA Selected Ships (not USA registry) Supplementary Ships (not USA registry) Auxiliary Ships (not USA registry) Unknown |
| 10 | Atm | 1 2 3 4 5 | Automation of observation Fully automated Always supplemented by manual input Occasionally supplemented by manual input Unknown Fully manual (no automation) |
| 11 | blc | 1 2 3 | Baseline check – does the automatic observing equipment run or allow a periodic baseline check to ensure the equipment is operating satisfactorily? Yes No No automation |
| 12 | rte |  | Routes (s) The areas or routes on which the ship is normally plying. Each recruiting country has defined its own set of routes - see separate data file Ships Routes for specific set of route codes. |
| 13 | barm | AN DA MER SAN | Type of barometer Aneroid barometer (issued by Port Meteorological Officer or Meteorological Agency)) Digital aneroid barometer Mercury barometer Ships aneroid barometer |
| 14 | bMS |  | Model (brand) of barometer - manufacturer/series no. |
| 15 | brmH |  | Height of barometer - height above the maximum load line in tenths of meters (e.g. 25.7 m) |
| 16 | brmL | WH CR OT | Barometer location (e.g. wheelhouse, chart room, etc.) Wheelhouse Chart room Other (specify in footnote) |
| 17 | brmU |  | Pressure units - as observed (e.g. millibars, hectapascals, inches Hg, millimeters Hg, etc.) |
| 18 | brmC |  | Barometer Calibration Date - date of latest calibration on the barometer (e.g. 01121998) - Day (01-31); Month (01-12); Year (e.g. 1998, 2005, etc.)- |
| 19 | thrm | ALC ELE MER | Type of thermometer - dry bulb Alcohol thermometer Electric (resistance) thermometer Dry Bulb mercury thermometer |
| 20 | thMS |  | Model (brand) of thermometer - dry bulb (manufacturer/series no.) |
| 21 | thmE | A S SG SL SN US VS W | Conditions of exposure of thermometer Aspirated (Assmann type) Screen (not ventilated) Ships sling Sling Ships screen Unscreened Screen (ventilated) Whirling |
| 22 | thmL | 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 OT | Location of instruments (dry bulb & wet bulb) Bridge wing port Bridge wing starboard Bridge wing both sides Bridge wing windward side Wheelhouse top port Wheelhouse top starboard Wheelhouse top both Wheelhouse top center Wheelhouse top windward side Mainmast Foremast Mast on Wheelhouse top Main deck port side Main deck starboard side Main deck both sides Other (specify in footnote) |
| 23 | thmH |  | Height of thermometers - dry bulb/wet bulb above the maximum load line (in tenths of meters; e.g. 12.1 m) |
| 24 | tscale | 1 2 3 4 5 6 7 8 | Temperature scale; original units (general reporting practice) Centigrade to tenths* half degrees Centigrade* whole degree Centigrade* whole degree Fahrenheit* Fahrenheit to tenths* dry bulb in Centigrade, wet bulb in Fahrenheit dry bulb in Fahrenheit, wet bulb in Centigrade other combinations or scale (specify in footnote) * all reported temperatures (dry bulb & wet bulb/dew point) |
| 25 | hygr | E H P Hg C T Cm OT | Type of hygrometer Electric Hair hygrometer Psychrometer Hygristor Capacitance Torsion Chilled mirror Other (specify in footnote) |
| 26 | HgrE | A S SG SL SN US VS W | Conditions of exposure of hygrometer Aspirated (Assmann type) Screen (not ventilated) Ships sling Sling Ships screen Unscreened Screen (ventilated) Whirling |
| 27 | SstM | BTT BU C HC HT RAD TT OT | Method of Obtaining sea surface temperature Bait tanks thermometer Bucket thermometer Thermometer in condenser intake on steam ships, or inlet engine cooling system on motor ships Hull contact sensor Through hull sensor Radiation thermometer Trailing thermistor Other (specify in footnote) |
| 28 | SstD |  | Depth of sea temperature measurement (tenths of meters below maximum load line; e.g. 5.7 m) |
| 29 | Barg | OS OS1 OS2 OS3 OS4 OS5 OS6 OS7 OS8 OS9 SS OT | Type of barograph Open scale barograph Open scale barograph with 1-day clock Open scale barograph with 2-day clock Open scale barograph with 3 day clock Open scale barograph with 4-day clock Open scale barograph with 5-day clock Open scale barograph with 6-day clock Open scale barograph with 7-day clock Open scale barograph with 8-day clock Open scale barograph with 9-day clock Small scale barograph Other (specify in footnote) |
| 30 | AnHL |  | Height of anemometer - height above the maximum load line, in tenths of meters ( e.g. 30.4 m) |
| 31 | AnHD |  | Height of anemometer - height above the deck on which it is installed, in tenths of meters (e.g. 10.6 m) |
| 32 | AnmL | 1 2 3 4 5 6 7 8 9 10 11 12 13 OT | Anemometer location - description of location Not fitted Mainmast Mainmast port yardarm Mainmast starboard yardarm Aft mast Foremast Foremast port yardarm Foremast Starboard yardarm Meteorological mast Mast on wheelhouse top Mast on wheelhouse top port yardarm Mast on Wheelhouse top starboard yardarm Handheld Other (specify in footnote) |
| 33 | anDB |  | Anemometer distance- distance from the bow in tenths of meters ( e.g. 24.2 m) |
| 34 | anDC |  | Anemometer distance - distance of anemometer from center line in tenths of meters ( plus port/starboard indicator; e.g. 3.6 m starboard) |
| 35 | anmI |  | Anemometer instrument type (manufacturer/series no.) ; Provide best available description e.g. propeller vane-Seiki Japan, Thomas Walker, Seiki F235, Jules Richard No. 64, anemograph, etc. |
| 36 | anmU | 1 2 3 4 | Anemometer usage (general observing practice) Anemometer measurement generally used, true wind computed Anemometer measurement generally used, true wind manually determined visual estimates (sea state) generally used visual estimate generally used for the open sea, anemometer used near port |
| 37 | anmC |  | Anemometer Calibration Date (primary) - date of latest anemometer calibration - Day (01-31); Month (01-12); Year (e.g. 1998, 2005, etc.)- |
| 38 | wwH |  | Visual wind/wave observational height - height above the maximum load line that the visual wind and wave observations are taken. Height in tenths of meters (e.g. 18.7 m). |
| 39 | othI | BAT BT MAX MIN P R RG RSD RT ST TSD W XBT LWR SWR OT | Other meteorological instruments Bathythermometer Bathythermograph (towed) Maximum thermometer Minimum thermometer Pilot balloon sounding apparatus Radiosounding apparatus Rain-gauge Radar storm and meteorological phenomena detection Reversing thermometer Sea thermograph Temperature/salinity/depth probe Radio or radarwind apparatus Expendable bathythermograph Long wave radiometer Short wave radiometer Other - any instrument aboard a ship that does not appear on this list should be reported so it can be added to the list and entered into Pub. 47 (specify in a footnote) |
| 40 | phGr | R T | Telephony & telegraphy Radiotelegraphy Radio telephone |
| 41 | prSt | A C E I Y G | Teleprinter & satellite Argos communication facility INMARSAT-C communication facility Environmental satellites communication facility INMARSAT-A communication facility Direct printing radiotelegraphy Global positioning system (GPS) |
| 42 | Chgd |  | Change Date - the date the PMO last updated this table (information) on the ship (e.g. 26021998) - Day (01-31); Month (01-12); Year (e.g. 1998, 2005, etc.)- |

Publication No. 47 database

Fields

| Order | Code name | Explanation |
| --- | --- | --- |
| 1 | name; | Ship name |
| 2 | call; | Ship call sign |
| 3 | IMOn; | IMO number assigned to the hull |
| 4 | rcnty; | Recruiting country (two letter abbreviation) |
| 5 | vssl; | Vessel type (general cargo = GC, liquid tanker = LT, etc.) |
| 6 | vsslP; | Vessel digital image (profile) |
| 7 8 9 10 11 | lenvsslD; brdvsslD; frbvsslD; drfvsslD; chtvsslD; | Vessel dimension - length (in meters) - breadth - freeboard - draft (maximum summer loadline) - cargo height |
| 12 | brdg; | Distance of the bridge from the bow (to tenths of meters) |
| 13 | vsslM; | Type of VOS ship (Selected Ships = 01, Supplementary Ships = 40, etc.) |
| 14 | Atm; | Automation of observation |
| 15 | blc; | Baseline check |
| 16 17 18 19 20 21 22 23 24 25 | rte; rte; rte; rte; rte; rte; rte; rte; rte; rte; | Ships route No. 1 Ships route No. 2 Ships route No. 3 Ships route No. 4 Ships route No. 5 Ships route No. 6 Ships route No. 7 Ships route No. 8 Ships route No. 9 Ships route No. 10 |
| 26 27 | barm; barm; | Barometer No. 1 - type Barometer No. 2 - type |
| 28 29 | bMS; bMS; | Model (manufacturer/series no.) No. 1 Model (manufacturer/series no.) No. 2 |
| 30 31 | brmH; brmH; | Barometer No. 1 - height in meters to tenths from max load line Barometer No. 2 - height in meters to tenths from max load line |
| 32 33 | brmL; brmL; | Barometer No. 1 - location (e.g. wheelhouse, chart room, etc.) Barometer No. 2 - location |
| 34 35 | brmU; brmU; | Pressure Units No. 1 Pressure Units No. 2 |
| 36 37 | brmC; brmC; | Barometer calibration date No. 1 Barometer calibration date No. 2 |
| 38 39 | thrm; thrm; | Thermometer No. 1 - type Thermometer No. 2 - type |
| 40 41 | thMS; thMS; | Thermometer model (manufacturer/series no.) No. 1 Thermometer model (manufacturer/series no.) No. 2 |
| 42 43 | thmE; thmE; | Thermometer No. 1 - conditions of exposure Thermometer No. 2 - conditions of exposure |
| 44 45 | thmL; thmL; | Thermometer No. 1 - location Thermometer No. 2 - location |
| 46 47 | thmH; thmH; | Thermometer No. 1 - height Thermometer No. 2 - height |
| 48 49 | tscale; tscale; | Thermometer No. 1 - scale Thermometer No. 2 - scale |
| 50 51 | hygr; hygr; | Hygrometer No. 1 - type Hygrometer No. 2 - type |
| 52 53 | hgrE; hgrE; | Hygrometer No. 1 - conditions of exposure Hygrometer No. 2 - conditions of exposure |
| 54 55 | sstM; sstM; | Sea surface temperature measurement - Method No. 1 Sea surface temperature measurement - Method No. 2 |
| 56 57 | sstD; sstD; | SST - depth of method No. 1 (tenths of meters below max load line) SST - depth of method No. 2 (tenths of meters below max load line) |
| 58 59 | barg; barg: | Barograph No. 1 - type Barograph No. 2 - type |
| 60 61 | anHL; anHL; | Anemometer No. 1 - height (meters to tenths), measured from max load line Anemometer No. 2 - height (meters to tenths), measured from max load line |
| 62 63 | anHD; anHD; | Anemometer No. 1 - height (meters to tenths), height above deck on which it is installed Anemometer No. 2 - height (meters to tenths), height above deck on which it is installed |
| 64 65 | anmL; anmL; | Anemometer No. 1 - description of location Anemometer No. 2 - description of location |
| 66 67 | anDB; anDB; | Anemometer No. 1- distance from the bow Anemometer No. 2- distance from the bow |
| 68 69 | anDC; anDC; | Anemometer No. 1 - distance from center line (port/ starboard indicator) Anemometer No. 2 - distance from center line (port/ starboard indicator) |
| 70 71 | anmI; anmI; | Anemometer No. 1- Instrument type (manufacturer/ series no./ etc.) Anemometer No. 1- Instrument type (manufacturer/ series no./ etc.) |
| 72 | anmU; | Anemometer - general observing practice |
| 73 74 | anmC; anmC; | Anemometer No. 1 - calibration date Anemometer No. 2 - calibration date |
| 75 | wwH; | Visual wind/wave observational height |
| 76 77 78 79 80 81 | othI; othI; othI; othI; othI; othI; | Other meteorological instrument aboard - No. 1 - type Other meteorological instrument aboard - No. 2 - type Other meteorological instrument aboard - No. 3 - type Other meteorological instrument aboard - No. 4 - type Other meteorological instrument aboard - No. 5 - type Other meteorological instrument aboard - No. 6 - type |
| 82 83 | phGr; phGr; | Radio-telephony and telegraphy - No. 1 - type Radio-telephony and telegraphy - No. 2 - type |
| 84 85 86 87 88 | prSt; prSt; prSt; prSt; prSt; | Radio-telephony and satellite - No. 1 - type Radio-telephony and satellite - No. 2 - type Radio-telephony and satellite - No. 3 - type Radio-telephony and satellite - No. 4 - type Radio-telephony and satellite - No. 5 - type |
| 89 | chgd; | Change date (date information was updated on the ship by the PMO) |
| 90 91 92 93 94 95 96 97 98 99 | fieldAbrev; fieldAbrev; fieldAbrev; fieldAbrev; fieldAbrev; fieldAbrev; fieldAbrev; fieldAbrev; fieldAbrev; fieldAbrev; | Code name of field to which footnote No. 1 applies Code name of field to which footnote No. 2 applies Code name of field to which footnote No. 3 applies Code name of field to which footnote No. 4 applies Code name of field to which footnote No. 5 applies Code name of field to which footnote No. 6 applies Code name of field to which footnote No. 7 applies Code name of field to which footnote No. 8 applies Code name of field to which footnote No. 9 applies Code name of field to which footnote No. 10 applies |
| 100 101 102 103 104 105 106 107 108 109 | footID; footID; footID; footID; footID; footID; footID; footID; footID; footID; | Footnote No. 1 - code number of text required Footnote No. 2 - code number of text required Footnote No. 3 - code number of text required Footnote No. 4 - code number of text required Footnote No. 5 - code number of text required Footnote No. 6 - code number of text required Footnote No. 7 - code number of text required Footnote No. 8 - code number of text required Footnote No. 9 - code number of text required Footnote No. 10 - code number of text required |