# IRD NOUMEA REPORT ACTIVITIES

July 199 – December 1999

# NATIONAL  IRD (Noumea) XBT PROGRAMME ACTIVITIES

## National and International Objectives

The objectives of the ECOP program (Etudes Climatiques de l’Ocean Pacifique tropical) at I.R.D Noumea are to observe and understand the climate variability associated with the El Niño Southern Oscillation (ENSO) phenomenon. There are two different research activities within ECOP:

- The study of the ENSO mechanism.

- The study of the ENSO impact on the southwest Pacific regional environment.

ECOP operates different observations network for the tropical Pacific (X.B.T, T.S.G and coastal stations), that benefit to these research programs. These networks are the ECOP’s contribution to the international CLIVAR program (PMRC, 1995).

## Collaborating Agencies

National:

- C.N.E.S, Toulouse

(Centre National d’Etudes Spatiales)

- IFREMER, Brest

(Institut Français de Recherche pour l’Exploitation de la mer)

- Meteo France, Paris & Noumea

International:

- N.O.A.A, Seattle

(National Oceanic and Atmospheric Administration)

- S.I.O, San Diego

(SCRIPPS Institution of Oceanography)

- CSIRO, Hobart

(Commonwealth Scientific Industrial Research Organization)

- JAMSTEC, Tokyo

(Japan Marine Science & Technology Center)

- JIMAR, Honolulu

## Funding Support and Status

The present X.B.T and T.S.G networks are funding mainly by I.R.D (most of the equipment as well as 3.5 man years in salary), with contributions from the N.O.A.A (3000 XBT probes in 1999; GOES / TSG transmitters), from the South Pacific Regional Environment Program (SPREP; one TSG line equipped in 1999) and from the local ZoNeCo program (300 XBT probes in 1999). The IRD contribution is sponsored by the “Programme National d'Etudes de la Dynamique du Climat”.

The IRD funding is likely to continue in 2000, and the XBT probes obtained from N.O.A.A will be reduced by about 50%.

# DATA COLLECTION

## XBT Lines operated

I.R.D Nouméa operates 7 commercial ships within S.O.P, which run in the west Pacific (4 ships) and on a round the world line (3 ships), and the I.R.D research vessel “ALIS”.

Sampling is every 6 hours (00h00, 06h00, 12h00, 18h00 Gmt), with an extra sampling at the equator. For the period July 1998 – December 1999, a total of 4162 probes have been launched.

See Annex A for details.

AX03		Europe - New York

IX01		Fremantle - Sunda Straits

IX10		Read Sea - Malacca Strait/Singapore

PX04		Japan - Kiribati - Fiji/Samoa

PX05		Japan - New Zealand

PX06		Suva, Fiji - Auckland, New Zealand

PX09		Hawaii - Noumea/Auckland

PX12		Tahiti - Coral Sea

PX17		Tahiti/Maruroa - Panama

PX28		Tahiti - Sydney/Auckland

PX30		Brisbane - Noumea

PX51		Taiwan/Mindanao - Coral Sea/New Caledonia

PX53		Taiwan/Mindanao – Fiji

Due to the decrease of probes to be provided by N.O.A.A to I.R.D Nouméa in 2000 (1300 probes instead of 2600), two XBT sampling systems will be removed from the M/v Crusader and the M/v Challenger. These ships run in the west Pacific between New Caledonia, Fiji, New Zealand and Australia (January – February 2000). These ships will continue to take water samples every six hours.

The ships which run on the round the world line (M/V Washington, M/v Rome & M/v London) will stop launching probes in the Atlantic ocean on the AX03 line (Europe - New York) and in the Indian ocean on the IX01 & IX10 lines. Launching will continue in the Pacific Ocean on the PX17, PX28 & PX09 lines.

There’s no change for the M/V Coral Islander & Pacific Islander sampling strategy, which have priority for the ECOP research program.

See Annex A for route details.

## Other Sources of National Data

## Instrumentation

# Laptop computers, PROTECNO interfaces, ARGOS transmitters, SIPPICAN Deep Blue probes.

## Instrument Evaluations

## Other Shipboard Instrumentation and Data Collection Activities

### Shipboard ThermoSalinoGraphs:

I.R.D Nouméa also operates a Thermosalinographs network. Some of the ships that run within the SOOP plus two other ships are equipped with a T.S.G system.

The M/v Coral Islander, Pacific Islander, Kyowa Hibiscus & Kyowa Cattleya in the west Pacific, The M/v Washington, Rome & London on the round a world line, The M/v Lady Geraldine around New Caledonia and the I.R.D research vessel ALIS in the Pacific. In March 1999, in cooperation with N.O.A.A, the M/v Argentina Star has been equipped with the same system. This ship runs in the central Pacific between California and New Zealand – Australia. The system on that ship has been removed in February 2000 due to a ship rerouting (probably to South America).

The T.S.G system uses a Thermosalinograph SeaBird SBE 21, generally installed in the engine room. A Gps provides the ship’s position, and the data are recorded on a computer. The system samples every 15 seconds, and a median is recorded every 5 minutes. Since the beginning of 1999, all the ships equipped with a T.S.G are transmitting data in real time via satellite using a GOES transmitter (3 hourly median transmitting every 3 hours).

See Annex B for route details.

### Moored Thermograph and Thermosalinograph (Coastal stations).

I.R.D Nouméa has developed an observing network of coastal stations around New Caledonia and in the Pacific as well. There’s 11 stations equipped with a thermograph and 3 stations with a thermosalinograph which record the near sea surface temperature and salinity (Two are equipped with both thermograph and thermosalinograph).

The systems used are based on ONSET sensors for the thermographs and on SBE 16 for the thermosalinographs. The system installed at Sabine Bank in 1999 (Vanuatu) is a Wave & Tide recorder SeaBird SBE 26 that is connected to a conductivity sensor SeaBird SBE 4 for salinity. For all the system, sampling interval is every 30 minutes, and data are collected twice a year.

# See Annex C for details.

### Oceanographic cruise

The Wespalis1 cruise onboard the R/V l'Alis was carried out during October November 1999 in the southwestern tropical Pacific (see the map for the Wespalis2 cruise below). An RDI 150kHz ADCP was installed on the R/V and 70 CTD and L-ADCP casts were made during the cruise, together with continuous TSG and meteorological measurements.

# DATA MANAGEMENT

## Data Flow Monitoring Activities

## Quality Control Procedures

### Delayed mode:

#### X.B.T

- Potential date and position errors are corrected in displaying data on a map, using the XBT logbook filled up by the officers.

- Spurious values are then deleted through a qualitative procedure based on climatic limits as well as on a visual comparison of each drop with nearby drops.

- Spurious values are further deleted through a quantitative procedure based on a comparison of each drop with a local 1979-1985 mean +/- the standard deviation (Picaut and Tounier, JGR, 1991).

- Dare are inserted into the data bank with the following quality flags :

1: 	No correction except data below a given level truncated

2.	Some data have been corrected using an interpolation

4. 	Bad launch

#### T.S.G

- Potential date and position errors are corrected in plotting SST and SSS as a function of longitude, latitude and time.

- Data gathered when the vessels call in ports are deleted.

- Spurious values are then deleted through a qualitative procedure based on climatic limits as well as on a visual comparison of each value with nearby values.

- Data are de-spiked to remove spurious values.

- Spurious values are further deleted through a quantitative procedure based on a comparison of each value with a local 1979-1992 mean +/- the standard deviation (Delcroix, JGR, 1998).

- Pre/post calibration coefficients obtained from the manufacturer (SeaBird, Seattle) are used to correct the data, if necessary.

- Data are inserted into the data bank with the following quality flags :

1: 	de-spike & qualitative correction (comparison of each value with nearby values)

2.	idem 1 + comparison with local 1979-1992 mean +/- the standard deviation. (Delcroix, 1998).

3. 	idem 2 + comparison with simultaneous CTD and/or water samples.

4. 	idem 1 + pre/post calibration of sensors.

5. 	idem 2 + pre/post calibration of sensors.

6. 	idem 1 + comparison with simultaneous CTD and/or water samples + pre/post calibration of sensors.

7. 	idem 2 + comparison with simultaneous CTD and/or water samples + pre/post calibration of sensors.

### Real time:

#### X.B.T

There’s no quality control at I.R.D Noumea on the real time XBT data.

#### T.S.G

There’s no quality control at I.R.D Noumea on the real time TSG data. The real time data are downloaded daily to check the systems and contact the ship is there’s any problem.

## Delayed Mode Data Submission status

Every three months, the delayed mode data are extracted from the data bank and then transmitted to IFREMER – Brest in a special format (ftp://public.ifremer.fr/).

Contact: 	Yvette RAGUENES, IFREMER Brest, France

mailto:raguenes@ifremer.fr

# FUTURE PLANS

The future IRD-Noumea plans within SOOPIP include the continuation of the XBT and TSG lines, the realisation of an oceanographic cruise in the southwestern tropical Pacific, and activities linked to TSG data collection and distribution.

## X.B.T activities

The IRD-Noumea involvement regarding XBT will be maintained in the tropical Pacific in the coming year. The number of drops will be revised depending on available XBT probes obtained from N.O.A.A and on the presently discussed implementation of France within ARGO.

## T.S.G activities

The TSG activities will be maintained in the coming year. A proposal for adding a new line in the western tropical Pacific has been accepted recently; this new line should be operational in mid-2000.

## Oceanographic cruise

The Wespalis 2 cruise will be carried out onboard the Research Vessel l’ALIS from IRD-Noumea from mid April to mid May 2000. The aim of this cruise, which follows the Wespalis 1 cruise undertaken about 6 month ago, is to observe and understand the hydrological structure changes (temperature, salinity and currents) of the south western tropical Pacific, with a special emphasis on the South Pacific Convergence Zone as well as on the impact of the on-going La Nina event. Measurements of temperature, salinity, zonal and meridional currents, as well as classical meteorological measurements will be performed in station (black dots) and en route. Intervention on TAO moorings (red dots) will be made if necessary.

## Other activities.

The validated sea surface salinity data collected since 1969 (bucket measurements) and since 1989 (TSG) will be released this year to the CLIVAR community, in line with the data sharing era discussed at the Oceanobs99 conference. This will be made either via ftp and/or via a dedicated CD-Rom.

# FURTHER INFORMATION

# RELATED NATIONAL WEB SITE LINKS

- I.R.D Noumea ECOP Program

http://noumea.ird.nc/ECOP/

- I.R.D Brest XBT Program

http://www.ifremer.fr/ird/xbt/xbt_orst.html

- I.R.D Brest SOOP

http://www.brest.ird.fr/soopip/

- Z.O.N.E.C.O

http://www.gouv.nc/zoneco/

# RELEVANT REFERENCES AND PUBLICATIONS

- Gourdeau L., J. Verron, T. Delcroix, A. Busalacchi et R. Murtugudde, 2000. Assimilation of Topex/poseidon altimetric data in a primitive equation model of the tropical Pacific Ocean, 1992-96. J. Geophys. Res., in press.

- Alory G. and T. Delcroix. Climatic variability in the vicinity of Wallis, Futuna and Samoa islands (13S-15S; 80-170W). Ocean. Acta, 22, 249-263, 1999.

- Delcroix T. and J. Picaut. Zonal displacement of western equatorial Pacific fresh pool. J. Geophys. Res., 103, 1087-1098, 1998.

- Delcroix T. Observed surface oceanic and atmospheric variability in the Tropical Pacific at seasonal and ENSO time scales: a tentative overview. J. Geophys. Res, 103, 18611-18633, 1998.

- Delcroix T., L. Gourdeau and C. Hénin. Sea surface salinity changes along the Fiji-Japan shipping track during the 1996 La Niña and 1997 El Niño period. Geophys. Res. Letter, 25, 3169-3172, 1998.

- Gourdeau L. Internal tides observed at 2°S-156°E by in situ and TOPEX/Poseidon data during COARE. J. Geophys. Res., 103, 12629-12638, 1998.

- Hénin C., Y. du Penhoat and M. Ioualalen. Observations of sea surface salinity in the western Pacific fresh pool: large scale changes in 1992-1995. J. Geophys. Res., 103, 7523-7536, 1998.

- Inall, M. E., K. J. Richards and G. Eldin, The changing structure of the upper ocean in the western equatorial Pacific during Tropical Ocean Global Atmosphere Coupled Ocean Atmosphere Response Experiment. J. Geophys. Res., 103, 21385-21400, 1998.

- McPhaden, M J., A. J. Busalacchi, R. Cheney, J-R. Donguy, K. S. Gage, D. Halpern, M. Ji, P. Julian, G. Meyers, G. Mitchum, P. P. Niiler, J. Picaut, R. W. Reynolds, N. Smith, et K. Takeuchi. The Tropical Ocean Global Atmosphere (TOGA) observing system: A decade of progress. J. Geophys. Res., 103, 14169-14240, 1998.

- Quinn T.M., T.J. Crowley, F.W. Taylor, C. Hénin, P. Joannot, and Y. Join. A multicentury stable isotope record from a New Caledonia coral : Interannual and decadal SST variability in the southwest Pacific since 1657. Paleoceanography, 13, 412-426, 1998

ANNEX A : X.B.T information.

### List of Ship equipped with X.B.T system.

| Ship | Call Sign | Gts | Line | Drops |
| --- | --- | --- | --- | --- |
| R/v ALIS | FHQB | Yes | West Pacific | 200 |
| M/v Challenger | ELXD7 | Yes | Coral Sea | 410 |
| M/v Crusader | ELXD8 | Yes | Coral Sea | 431 |
| M/v Pacific Islander | HPEW | Yes | West Pacific | 976 |
| M/v Coral Islander | 3EVS | Yes | West Pacific | 500 |
| M/v CS London | ELVX4 | Yes | Round World | 576 |
| M/V CS Rome | ELVZ6 | Yes | Round World | 526 |
| M/v CS Washington | ELVZ5 | Yes | Round World | 521 |

### Number of drops & measure per month.

|  | 07/98 | 08/98 | 09/98 | 10/98 | 11/98 | 12/98 | 01/99 | 02/99 | 03/99 | 04/99 | 05/99 | 06/99 | 07/99 | 08/99 | 09/99 | 10/99 | 11/99 | 12/99 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Drop | 162 | 199 | 158 | 287 | 263 | 290 | 218 | 260 | 237 | 198 | 277 | 194 | 233 | 257 | 171 | 195 | 245 | 131 |
| T | 109157 | 131542 | 87495 | 175817 | 136663 | 173110 | 120137 | 154844 | 153864 | 114039 | 172897 | 126394 | 159217 | 172469 | 119558 | 135429 | 159780 | 82621 |

ANNEX B : Shipboard ThermoSalinoGraphs information.

### List of Ship equipped with T.S.G

| Ship | Call Sign | Line |
| --- | --- | --- |
| R/v ALIS | FHQB | West Pacific |
| M/v Lady Geraldine | FKKT | New Caledonia |
| M/v Coral Islander | 3EVS | West Pacific |
| M/v Pacific Islander | HPEW | West Pacific |
| M/v Kyowa Cattleya | 3FEW5 | West Pacific |
| M/v Kyowa Hibiscus | 3FMF4 | West Pacific |
| M/v CS London | ELVX4 | Round World |
| M/V CS Rome | ELVZ6 | Round World |
| M/v CS Washington | ELVZ5 | Round World |
| M/v Argentina Star | C6MD8 | Central Pacific |

### Number of measure per month.

|  | 07/98 | 08/98 | 09/98 | 10/98 | 11/98 | 12/98 | 01/99 | 02/99 | 03/99 | 04/99 | 05/99 | 06/99 | 07/99 | 08/99 | 09/99 | 10/99 | 11/99 | 12/99 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SST | 25384 | 20930 | 20037 | 21086 | 23028 | 20536 | 21283 | 20404 | 30229 | 26465 | 36794 | 32632 | 40207 | 35718 | 35466 | 43707 | 39945 | 22481 |
| SSS | 25834 | 20930 | 30031 | 21073 | 22877 | 18075 | 22700 | 20237 | 30246 | 22580 | 36671 | 28140 | 25388 | 30965 | 21280 | 32408 | 31007 | 21543 |

The following maps are only for information on the ship’s routes. There’s only one sample every four hours plotted on the map (The tsg system samples stores a median values every 5 minutes).

ANNEX C : Coastal stations information.

| Station | Code | Type | Lat | Lon | Depth | Start | End | Record | Active |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 303-british-nouville | brit | onset | -21,71 | 166,42 | 12 | 01-déc-96 | 20-sep-99 | 74633 | No |
| Anse Vata | vato | onset | -21,68 | 166,45 | 2 | 16-avr-97 | 21/09/1999 | 50926 | Yes |
| Boulari-nord | boun | onset | -21,5 | 166,44 | 14 | 01-nov-96 | 20-sep-99 | 95605 | No |
| Chaleix | chal | sbe16 | -21,72 | 166,42 | 2 | 01-aoû-91 | 17-fév-92 | 49585 | No |
| Chesterfield | ches | onset | -19,86 | 158,3 | 10 | 25-sep-97 | # | # | Yes |
| Dumbea-sud | dums | onset | -21,89 | 166,27 | 14 | 01-oct-96 | 19-sep-99 | 74507 | No |
| Goro | goro | onset | -22,16 | 167,06 | 10 | 04-mar-97 | 15-sep-99 | 42990 | Yes |
| Le Cap | goul | onset | -21,33 | 165,14 | 10 | 03-oct-97 | 28-mai-99 | 28657 | No |
| Marquises | marq | onset | -8,56 | -140,03 | 10 | 19-sep-97 | 12-mar-99 | 21686 | Yes |
| Phare Amedee | ameo | onset | -22,28 | 166,28 | 4 | 18-jun-97 | 20-sep-99 | 45305 | Yes |
| Poe | poeb | onset | -21,60 | 165,33 | 10 | 13-aoû-99 | # | # | Yes |
| Poindimie | poin | onset | -20,53 | 165,29 | 10 | 12-sep-96 | 11-sep-99 | 46870 | Yes |
| Recif-prony | rpro | onset | -21,7 | 166,19 | 11 | 01-déc-96 | 11-fév-99 | 97477 | Yes |
| Sabine Bank | sabi | sbe16 | -15,93 | 166,13 | 12 | 18-nov-99 | # | # | Yes |
| Sabine Bank | sabi | onset | -15,93 | 166,13 | 12 | 18-nov-99 | # | # | Yes |
| Sea-Horse Ponton | seah | onset | -21,7 | 166,19 | 9 | 01-oct-96 | 19-sep-99 | 90335 | No |
| Surprises | surp | onset | -18,29 | 163,04 | 10 | 28-sep-97 | 29-avr-99 | 27741 | Yes |
| Uitoe | uito | onset | -21,82 | 166,11 | 10 | 22-mai-92 | 19-sep-99 | 201966 | Yes |
| Uitoe | uito | sbe16 | -21,82 | 166,11 | 10 | 22-mai-92 | 19-sep-99 | 201966 | Yes |
| Wallis | wall | sbe16 | -13,21 | -176,25 | 10 | 25-aoû-98 | # | # | Yes |

ANNEX D : SOOP Lines description

### Atlantic ocean

| AX01 | Greenland - Iceland - Ireland/Scotland/Denmark |
| --- | --- |
| AX02 | Newfoundland - Iceland |
| AX03 | Europe - New York |
| AX04 | New York - Gibraltar/Lisbon |
| AX05 | Europe - Panama Canal |
| AX06 | New York - Dakar |
| AX07 | Gulf of Mexico - Gibraltar |
| AX08 | New York - Cape of Good Hope |
| AX09 | Trinidad - Gibraltar |
| AX10 | New York - Trinidad/Caracas |
| AX11 | Europe - Brazil |
| AX12 | Europe - Antarctica |
| AX13 | Rio de Janeiro - Monrovia (Liberia) |
| AX14 | Rio de Janeiro - Lagos (Nigeria) |
| AX15 | Europe - Cape of Good Hope |
| AX16 | Rio de Janeiro - Walvis Bay |
| AX17 | Rio de Janeiro - Cape of Good Hope |
| AX18 | Buenos Aires - Cape of Good Hope |
| AX19 | Cape Horn - Cape of Good Hope |
| AX20 | Europe - French Guyana |
| AX21 | Rio de Janeiro - Pointe Noire/Luan |
| AX22 | Argentina - Antarctica |
| AX23 | Gulf of Mexico |
| AX25 | Cape of Good Hope - Antarctica |
| AX26 | Cape of Good Hope - Lagos (Nigeria) |
| AX27 | Brazil - Cape Horn |
| AX29 | New York - Brazil |
| AX32 | New York - Bermuda |
| AX33 | Boston - Halifax/Nova Scotia |
| AX34 | Gulf of Guinea - Caribbean |
| AX35 | Cape of Good Hope - Recife |

### Indian Ocean

| IX01 | Fremantle - Sunda Straits |
| --- | --- |
| IX02 | Cape of Good Hope - Fremantle |
| IX03 | Red Sea - Mauritius/La Réunion |
| IX06 | Mauritius/La Reunion - Malacca Strait |
| IX07 | Cape of Good Hope - Persian Gulf |
| IX08 | Mauritius - Bombay |
| IX09 | Fremantle - Persian Gulf |
| IX10 | Read Sea - Malacca Strait/Singapore |
| IX11 | Calcuta - Java Sea |
| IX12 | Freemantle - Red Sea |
| IX14 | Bay of Bengal |
| IX15 | Mauritius - Freemantle |
| IX16 | Mombassa - Singapore |
| IX17 | Mombassa - Karachi |
| IX18 | Mombassa - Bombay |
| IX19 | La Réunion - Amsterdam/Kerguelen |
| IX20 | Mauritius - Rodriguez |
| IX21 | Cape of Good Hope - Mauritius |
| IX22 | Freemantle - Timor Strait/Banda Sea |
| IX23 | Hobart - Casey Station |
| IX25 | Mauritius - Karachi |
| IX26 | Red Sea - Karachi |
| IX27 | Mombassa - La Réunion |
| IX28 | Hobart, Tasmania - Dumont d'Urville |
| IX29 | Macquarie Island - Casey Station |
| IX30 | Hobart - Macquarie Island |
| IX31 | Melbourne - Freemantle |

### Pacific Ocean

| PX01 | California - Indonesia |
| --- | --- |
| PX02 | Flores Sea - Torres Strait |
| PX03 | Coral Sea |
| PX04 | Japan - Kiribati - Fiji/Samoa |
| PX05 | Japan - New Zealand |
| PX06 | Suva, Fiji - Auckland, New Zealand |
| PX08 | Auckland, New Zealand - Panama |
| PX09 | Hawaii - Noumea/Auckland |
| PX10 | Hawaii - Guam/Saipan |
| PX11 | Flores Sea - Japan |
| PX12 | Tahiti - Coral Sea |
| PX13 | New Zealand - California |
| PX14 | Alaska - Cape Horn |
| PX15 | Ecuador - Japan |
| PX16 | Peru - Hawaii |
| PX17 | Tahiti/Maruroa - Panama |
| PX18 | Tahiti - California |
| PX20 | California - Panama |
| PX21 | California - Peru |
| PX22 | Panama - Valpariso |
| PX23 | Mexico - 115W |
| PX24 | Panama - Indonesia |
| PX25 | Valparaiso - Japan/Korea |
| PX26 | TRANSPAC |
| PX27 | Guayaquil - Galapagos |
| PX28 | Tahiti - Sydney/Auckland |
| PX29 | Tahiti - Valparaiso |
| PX30 | Brisbane - Noumea |
| PX31 | Sydney/Noumea - California |
| PX32 | Sydney - Auckland |
| PX33 | Hobart - Macquarie Island |
| PX34 | Sydney - Wellington |
| PX35 | Melbourne - Dunedin |
| PX36 | Christchurch - McMurdo |
| PX37 | Hawaii - California |
| PX38 | Hawaii - Alaska |
| PX39 | Hawaii - Seattle/Vancouver |
| PX40 | Hawaii - Japan |
| PX41 | Hawaii - Taiwan/Hong Kong |
| PX42 | Hawaii - New Guinea/Solomon Islands |
| PX43 | Hawaii - Marshall Islands - Guam |
| PX44 | Taiwan - Guam |
| PX45 | Noumea - Marshall Islands |
| PX46 | 165 degrees East section |
| PX47 | Alaska - California |
| PX49 | Japan/Taiwan - Singapore |
| PX50 | Valparaiso - Auckland |
| PX51 | Taiwan/Mindanao - Coral Sea/New Caledonia |
| PX52 | Japan - Fiji |
| PX53 | Taiwan/Mindanao - Fiji |
| PX55 | Melbourne - Wellington |
| PX56 | Brisbane - Dunedin |
| PX57 | Brisbane - Wellington |
| PX76 | Costa Rica coast |
| PX77 | Peru coastal |
| PX78 | Peru coastal |
| PX79 | Valparaiso - 80 W |
| PX80 | Tahiti - Cape Horn |
| PX81 | Honolulu - Coronel (Chile) |