Ship Observations Team

EUMETNET Report for 2005

| 1. | Country | EUMETNET (20 European countries) |
| --- | --- | --- |
| 2. | Prepared by | Rudolf Krockauer, E-ASAP Programme Manager |
| 3. | Contributing national marine organizations: |
|  | # | Insert as applicable – VOS / VOSClim / SOOP / ASAP – Include additional detail where appropriate e.g (data management). |
|  | Organization | EUMETNET (Austria, Belgium, Cyprus, Denmark, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Luxembourg, Netherlands, Norway, Portugal, Spain, Sweden, Switzerland, United Kingdom) |
|  | Programmes # | ASAP |
|  | Website URL | www.eumetnet.eu.org |
| 4. | List of National Focal Points for SOT / VOS / VOSClim / SOOP / ASAP (see Appendix 1): |
| 5. | List of Port Meteorological Officers (see Appendix 2): |
| 6. | Programme Reports |

### Appendix 1: List of National Focal Points for SOT / VOS / VOSClim / SOOP / ASAP				(EUMETNET)

| Focal Point * | EUMETNET-ASAP | Integrated D-ASAP | Integrated UK-ASAP |
| --- | --- | --- | --- |
| Name | Rudolf Krockauer | Volker Weidner | Sarah North |
| Title | E-ASAP Programme Manager | Marine Networks Manager | Marine Networks Manager |
| Agency | c/o Deutscher Wetterdienst | Deutscher Wetterdienst | Met Office |
| Postal Address | Bernhard-Nocht-Strasse 76 D-20359 Hamburg, Germany | Bernhard-Nocht-Strasse 76 D-20359 Hamburg, Germany | A1 W04 FitzRoy Road Exeter EX1 3PB, United Kingdom |
| Email | Rudolf.Krockauer@dwd.de | Volker.Weidner@dwd.de | sarah.north@metoffice.gov.uk |
| Telephone | +49 40 6690 1580 | +49 40 6690 1410 | +44 1392 88 5617 |
| Facsimile | +49 40 6690 1496 | +49 40 6690 1496 | +44 870 900 5050 |

Appendix 2: List of Port Meteorological Officers								(EUMETNET)

| Port / Office | Hamburg |
| --- | --- |
| Name | Harald BUDWEG |
| Title | PMO |
| Postal Address | Deutscher Wetterdienst Bernhard-Nocht-Str. 76 D-20359 Hamburg, Germany |
| Email | Harald.Budweg@dwd.de |
| Telephone | +49 40 6690 1414 |
| Facsimile | +49 40 6690 1496 |
| Comment | Hamburg |

|  | ASAP Report for 2005 | (EUMETNET) |
| --- | --- | --- |
|  | a. | Catalogue of ASAP vessels in 2005 (see Appendix 3): |
|  | b. | Major challenges and difficulties: |
|  | Major difficulties are damages on electronic equipment due to permanent vibrations of the ship. Further difficulties are delayed or unstable satellite transmissions. Received messages later than HH+120 are worthless. Timeliness is not reflected in the column ‘Percentage on GTS’. Generally, the loss rate of launches (burst or crash at release etc.) is significantly higher than at land stations. Average ratio between flights on board and received messages on the GTS HH+120 is approx. 80%. The average terminal sounding height also includes flights with sounding heights of only 100 hPa. In most cases the actual burst heights of these flights were higher. But due to late transmission of TEMP C and D the data were received later than HH+120 on the GTS. |
|  | b. | Other comments: |
|  | Basic problem is the reduced network of PMOs. Three out of currently nine vessels under E-ASAP management sail between East coast US/Canada and Western Mediterranean. Because there is no PMO in the Mediterranean there is also no routine technical maintenance of these ASAP systems in Europe. Experiences show that routine maintenance is essential for the performance and efficiency of ASAP soundings. Three new E-ASAP systems were installed in Genoa (Italy) and commenced operation in 2005: The CP Endurance and the CP Power serve a route between Western Mediterranean and Montreal (Canada) on a four week rotation. Both ships were operating since January 2005. From the beginning there were serious problems due to technical and operating failures. Because there is no Port Meteorological Office in the Western Mediterranean these problems produced substantial outages of several months for both systems due to the lack of maintenance. The third system was installed on the Melfi Italia II which serves a route between Western Mediterranean, Halifax (Canada) and Havanna (Cuba) on a four week rotation. Although installed in February, first routine sounding data were received in May due to the lack of maintenance in the Med. After solving the initial problems the performance of the ship was good. Providing technical maintenance is considered to be essential for the future of these systems. All three ships call in Italian ports. One of the integrated German D-ASAP systems had to be removed from the ship SL Developer in January 2005 because the ship was de-commissioned to an East Asia service. E-ASAP succeeded to acquire another ship as replacement for the SL Developer. Thus, the D-ASAP system was installed on the Atlantic Compass in April and routine operations commenced in May. The ship serves a route between Gothenburg (Sweden) and North East coast US. |

| d. | ASAP Performance |
| --- | --- |
| Callsign | Total number of sondes launched | Number of TEMP SHIP transmitted | Number of relaunches | Average terminal sounding height (km) | Balloon size (gm) | Percentage on GTS (see note) |
| ZCBP6 | 495 | 349 |  | 18 | 350 | 99 |
| WAAH | 553 | 438 |  | 17 | 200 | 98 |
| SKUN | 229 | 188 |  | 20 | 200 | 98 |
| ELML7 | 569 | 480 |  | 17 | 200 | 97 |
| WPKD | 314 | 249 |  | 17 | 350 | 97 |
| KRPD | 326 | 240 |  | 19 | 350 | 85 |
| ZCBE7 | 129 | 87 |  | 17 | 350 | 89 |
| ZCBF3 | 177 | 140 |  | 16 | 350 | 97 |
| V2BD9 | 224 | 200 |  | 18 | 350 | 98 |
| Percentage on the GTS is the ratio of reports received against reports transmitted, and is based upon reports received at a data centre or GTS insertion point (name) |