|  | ASAP Report for 2005 | JAPAN |
| --- | --- | --- |
|  | a. | Catalogue of ASAP vessels in 2005 (see Appendix 3): |
|  | b. | Major challenges and difficulties: |
|  | b. | Other comments: |
|  | Japan Meteorological Agency will change sonde type from RS80-15G into RS92-SGP within 2006. |

| d. | ASAP Performance |
| --- | --- |
| Callsign | Total number of sondes launched | Number of TEMP SHIP transmitted | Number of relaunches | Average terminal sounding height (km) | Balloon size (gm) | Percentage on GTS (see note) |
| JGQH | 105 | 105 | 3 | 25.7 | 350 | 90.5 |
| JDWX | 84 | 84 | 12 | 25.1 | 350 | 98.8 |
| JIVB | 73 | 73 | 8 | 23.1 | 350 | 100 |
| JCCX | 120 | 120 | 0 | 23.5 | 350 | 99.2 |
| JNSR | 200 | 193 | 0 | 22.7 | 200 | 92.5 |
| Percentage on the GTS is the ratio of reports received against reports transmitted, and is based upon reports received at a data centre or GTS insertion point (name) |

Appendix 3. Catalogue of ships participating in ASAP in 2005.						JAPAN

5 ASAP units operated during the year on 5 ships

| Type of ship (1) | Ship name | Callsign | Comms method (2) | Windfind method / sonde type (3) | Launch method (4) | Launch height (5) | Area of operation (6) | ASAP unit ID No. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Research ship | Ryofu Maru | JGQH | Others (DCP via the GMS/MTSAT) | GPS/Vaisala RS80-15G | Container (Semi-automatic) | 8m | North Pacific | 708514 |
| Research ship | Kofu Maru | JDWX | Others (DCP via the GMS/MTSAT) | GPS/Vaisala RS80-15G | Container (Semi-automatic) | 6m | Seas adjacent to Japan | 191678 |
| Research ship | Seifu Maru | JIVB | Others (DCP via the GMS/MTSAT) | GPS/Vaisala RS80-15G | Container (Semi-automatic) | 6m | Seas adjacent to Japan | 458533 |
| Research ship | Chofu Maru | JCCX | Others (DCP via the GMS/MTSAT) | GPS/Vaisala RS80-15G | Container (Semi-automatic) | 6m | Seas adjacent to Japan | 126138 |
| Research ship | Mirai | JNSR | Inmarsat-C | GPS/Vaisala RS80-15G,RS80-15GH, RS92-SGP | Container (Semi-automatic) | 18m | Variable | - |
| (1) Type of ship: Merchant, research, supply (2) Comms method: Inmarsat C or others (3) Windfind method / sonde type: eg. GPS/Vaisala RS80-G, Loran/Vaisala RS80-L, VIZ GPS Mark II Microsonde, etc (4) Launch method: deck launcher (portable), deck launcher (fixed), container (manual), container (semi automatic), other (5) Launch height: height above sea level from where the sonde is released (6) Ocean area: North Pacific, North Atlantic, Indian Ocean, variable |