AUTOMATED SHIPBOARD

AEROLOGICAL PROGRAMME (ASAP)

# ANNUAL REPORT FOR 1999

WMO/TD-No. 1011

JCOMM Technical Report No. 6

| WORLD METEOROLOGICAL ORGANIZATION _____________ |  | INTERGOVERNMENTAL OCEANOGRAPHIC COMMISSION (OF UNESCO) ___________ |
| --- | --- | --- |

AUTOMATED SHIPBOARD AEROLOGICAL PROGRAMME (ASAP)

ANNUAL REPORT FOR 1999

WMO/TD-No. 1011

JCOMM Technical Report No. 6

N O T E

The designations employed and the presentation of material in this publication do not imply the expression of any opinion whatsoever on the part of the Secretariats of the Intergovernmental Oceanographic Commission (of UNESCO), and the World Meteorological Organization concerning the legal status of any country, territory, city or area, or of its authorities, or concerning the delimitation of its frontiers or boundaries.

Editorial note:  This publication is for the greater part an offset reproduction of typescripts submitted by the authors and has been produced without additional revision by the WMO Secretariat.

FOREWORD

I am pleased to introduce the Annual Report on ASAP operations for 1999.  It has been compiled by the ASAP Panel (ASAPP, formerly ASAP Co-ordinating Committee (ACC)) on the basis of national reports submitted by operators of ASAP and related ship-borne upper air sounding units.  A total of 21 such units were operated during last year.  Individual national reports are included in the annexes in a standard format agreed by ACC-IX, together with monitoring reports provided by ECMWF and EUMETSAT.

All operators have indicated that they plan to continue operations at the same level in the future years.  The ACC continues to work to encourage and assist the expansion of the ASAP, especially in ocean areas outside the North Atlantic. In particular, a new cooperative global ASAP project is under development, the Worldwide Recurring ASAP Project (WRAP).

Finally I have to thank all the ASAPP members for their contributions, as well as the Secretariat of WMO for its assistance.

Klaus Hedegaard

Chairman ASAPP

C O N T E N T S

page

FOREWORD	I

CONTENTS	iii

1.	Annual Report 1999	1

2.	Table 1	2

3.	Figure 1	3

4.	Figure 2	4

ANNEXES

I	National Reports 1999

Denmark	5

France	7

Germany	9

Iceland/Sweden	10

Japan	12

United Kingdom	16

United States of America	18

II	Monitoring Reports

Report of ECMWF	20

Report of EUMETSAT	39

ANNUAL REPORT 1999

The number of radiosoundings taken in the frame of the Automated Shipboard Aerological Programme (ASAP) has averaged around 5400 soundings annually over the last 5 to 10 years. There are fairly large fluctuations from year to year, mainly through the influence of enhanced activities in specific observational programmes such as FASTEX. This programme was carried out in 1997 and led to a decrease in soundings in the following year. This decrease was more than compensated for in 1999 with a nearly 20% increase in number of soundings compared to 1998. This increase could largely be ascribed to special programmes carried out by the United States and Japan. But also the fact that the United Kingdom started a new unit in mid 1999 led to the increase. The total number of ASAP or similar shipboard sounding units operated in 1999 was 21; the operators are: Denmark (2 units), France (4 units), Germany (3 units), Japan (7 units), Russia (1 unit), Sweden-Iceland (1 unit), United Kingdom (2 units) and the United States (1 unit).

The operational statistics provided by the operators for 1999 and the previous years are summarised in Table 1 and Figure 1. This report consists of the individual national reports and monitoring reports provided by ECMWF and EUMETSAT.

The ASAP Panel (ASAPP), which formerly was called the ASAP Co-ordinating Committee (ACC), consists of a group of national operators along with ECMWF and EUMETSAT. It held its annual meeting, ACC-XI, in Norrköping, Sweden, 29 September-1 October 1999. The operators from six countries were represented: Denmark, France, Iceland, Sweden, United Kingdom and the United States. Both ECMWF and EUMETSAT participated in the meeting.

The total number of ASAP soundings in 1999 corresponds approximately to the number of soundings which could be performed annually by a little less than 8 ocean weather ships. Their geographical distribution is presented in Figure 2. It displays the location of all the TEMP SHIP messages which were received in Toulouse, France, last year. Clearly, most of the soundings were taken in the northern Atlantic Ocean.

Under EUMETNET, which is a network grouping of 18 European national meteorological services, has been started a programme on ASAP, called E-ASAP. It will establish two ASAPs, one on a route within the Mediterranean, the other on a route between the English Channel and the Southeastern Seaboard of the United States. E-ASAP is jointly funded by the EUMETNET members, taking into account existing activities providing upper-air profile data from the oceans.

In order to expand the ASAP globally, the work programme of the ASAPP includes support and visits to selected countries in the Southern Hemisphere to encourage and assist implementation of ASAP in these data sparse ocean areas. Some progress in this area has been noted in 1999, in particular the identification of a suitable route passing both the Cape of Good Hope and Cape Horn, calling upon Australia, New Zealand, Brazil (May to December only) and ports in Western Europe. Such a project should be possible provided some sort of joint funding scheme can be established to cover running costs, and this should include both Southern Hemisphere and European countries (EUMETNET).

| Table 1. Statistics on ASAP units operated during 1999 |  |  |  |  |
| --- | --- | --- | --- | --- |
| Operator | ASAP units | Number of soundings | Average terminal sounding height (gpkm) | Percentage of data on the GTS |
| Denmark | 2 | 752 | 18.9 | 96% |
| France | 4 | 1421 | 22.5 | 100% |
| Germany | 3 | 1210 | 23.4 | 74%1) |
| Japan | 7 | 1098 | 22.5 | 100% |
| Russia | 1 | 1382) | 3) | 3) |
| Spain | 1 | 4) |  |  |
| Sweden-Iceland | 1 | 174 | 22.1 | 66% |
| United Kingdom | 2 | 151 | 25.2 | 100% |
| United States | 1 | 752 | 17 | 98% |
| Total or average | 22 | 5696 | 21.1 | 90% |
| Data only partially available Based upon reports received at ECMWF as published in the monthly ECMWF report (only those also reaching 100 hPa) Information not available as of April 2000 No activity reported |  |  |  |  |

(KH/DMI, 3 April 2000)

Annual National ASAP Report

COUNTRY: DENMARK		NAME OF AGENCY: DMI		YEAR: 1999

| 2 ASAP units operated during the year on 3 ships |
| --- |
| Type of ship1) | Name | Call sign | Comm. method2) | Windfind method3) | Launch height4) | Area of operations5) | ASAP Unit Serial No. |
| MS | Nuka Arctica | OXYH2 | Inmarsat-C | Loran-C/GPS | 18 m | North Atlantic | DK/ASAP1 |
| MS | Arina Arctica | OVYA2 | Inmarsat-C | Loran-C/GPS | 10 m | North Atlantic | DK/ASAP2 |
| MS | Irena Arctica | OXTS2 | Inmarsat-C | Loran-C/GPS | 10 m | North Atlantic | DK/ASAP1 |
| 1) Merchant ship, research ship, supply ship, etc. 2) Using IDCS, Inmarsat-C, or others 3) Loran-C, GPS, Loran/GPS, RTH 4) The height above sea level from where the sonde and balloon is released 5) Ocean area, e.g. North Pacific, North Atlantic, Indian Ocean, variable |

| Summary of performance of ASAP units during the year |
| --- |
| Call sign | Total No. of sondes launched | No. of messages transmitted | No. of relaunches | Average terminal sounding height (km) | Percentage on GTS1) |
| OXYH2 | 320 | 286 | 34 | 19.9 | 96.5% |
| OVYA2 | 327 | 314 | 13 | 19.2 | 95.5% |
| OXTS2 | 105 | 102 | 3 | 17.8 | 97.1% |
| Total or average | 752 | 702 | 50 | 18.9 | 96.2% |
| 1) Based upon reports received at a data centre or GTS insertion point, name: DMI. Ratio of reports received at ECMWF (500 hPa statistics) against reports transmitted, corrected for the switching error in Copenhagen for the UUAA part in parts of May and June 1999. |

Annual National ASAP Report (continued)

YEAR  1999

COMMENTS ON PERFORMANCE:

The systems have generally performed satisfactorily during the year. The transfer of launcher (10’ container based) and sounding equipment between the different ships continues, and is carried out without noticeable difficulties. The transfers are necessitated because of changes in sailing schedules for the ships. It concerned transfer from “Irena Arctica” (OXTS2) to “Nuka Arctica” (OXYH2) in late April and early May and vice versa in December. The data are transmitted through Inmarsat-C via telex to Copenhagen, where they are switched to Norrköping for insertion on the GTS. An error in the handling of the switching system caused that the Part A (the UUAA part) was not switched in the period 8 May until 14 June, with effect from 12 UTC. This meant that a total of 30 UUAAs from OVYA2 (9.6% of those transmitted) and 52 UUAAs from OXYH2 (18.2% of those transmitted) were not switched to the GTS. In the calculation of the transmission efficiencies this has been corrected for from the point of view that only parts of the data were lost, and use of Part B would fully compensate for the lack of Part A. A serious wind error has occurred on the OXYH2, with the effect that ECMWF blacklisted the wind from that unit for some time. The problem turned out to be linked with the mixed use of Loran-C and GPS causing an error in the set-up of the system giving erroneous Loran-C winds, and furthermore, an operator induced error also caused some wind errors.

ESTIMATES FOR FOLLOWING YEAR:

The programme is expected to continue more or less as in 1999.

oooOOOooo

Annual National ASAP Report

COUNTRY : FRANCE                NAME OF AGENCY: METEO-FRANCE         YEAR: 1999

| .....ASAP units operated during the year on 4 ships |
| --- |
| Type of ship1) | Name | Call sign | Comm method2) | Windfind Method3) | Lauch height | Area of operations5) | ASAP Unit Serial No |
| Merchant | Douce France | FNRS | IDCS | GPS | 27 | North Atlantic | FASAP 5 |
| Merchant | Fort Desaix | FNPH | IDCS | GPS | 27 | North Atlantic | FASAP 4 |
| Merchant | Fort Fleur d’Epée | FNOU | IDCS | GPS | 13 | North Atlantic | FASAP 2 |
| Merchant | Fort Royal | FNOR | IDCS | GPS | 13 | North Atlantic | FASAP 1 |
| 1) Merchant ship, research ship, supply ship, etc 2) Using IDCS, Inmarsat-C, or others 3) Loran-C, GPS, Loran/GPS, RTH 4) The height above sea level from where the sonde and balloon is released 5) Ocean area, e.g. North Pacific, North Atlantic, Indian Ocean, variable |

| Summary of performance of ASAP units during the year |
| --- |
| Call sign | Total No. of sondes launched | No. of messages transmitted | No. of relaunches | Average terminal sounding height (km) | Percentage on GTS1) |
| FNRS | 362 | 341 | 21 | 22.3 | 98.5 |
| FNPH | 348 | 326 | 22 | 22.5 | 100 |
| FNOU | 342 | 330 | 12 | 22.9 | 100 |
| FNOR | 369 | 351 | 18 | 22.2 | 99.7 |
| Total or average | 1421 | 1348 | 73 | 22.5 | 99.6 |
| 1) Based upon reports at a data center or GTS insertion point, name BDM Toulouse Ratio of reports received against reports transmitted |

Annual National ASAP Report (continued)

YEAR 1999

COMMENTS ON PERFORMANCE

In 1999, our principal problem has been the reliability of the Vaïsala GPS wind system. Globally, we have got a better availability of the wind data than in 1998, but the successful result of the sounding needs a bigger involvement of the F-ASAP operators in the test and the use of the radiosondes. We deplore a very high rate of rejection during the groundcheck (we have 22% of over consumption due to the rejection and the re-launch requisite after a failed attempt), and about 8% of soundings without wind data (we don’t try another launch if we miss some wind data).

99.6% of the TEMP-SHIP messages sent out during the last year have been accepted by the RTH of Toulouse. However, this good result is moderated by the fact that 10 to 15 % of these messages are corrupted. The data loss goes from the absence of a single data to the disappearing of almost the whole message (this case is very unusual).

ESTIMATES FOR FOLLOWING YEAR

The aim for next year is to improve the quality and the reliability of the wind data. This will not be possible without the will and the capacity of Vaisala to develop a radiosonde or a more efficient wind data processing system.

To reduce the transmission problems, we will develop a comprehensive maintenance process of our DCP systems. We hope the launch of MSG, with better DCS capabilities capacities than Meteosat will reduce some part of the data loss.

ooo000ooo

## Annual National ASAP Report

country:  GERMANY	NAME OF AGENCY:	DEUTSCHER WETTERDIENST	YEAR:  1999

| 2 ASAP units operated duringthe year on 2 ships |
| --- |
| Type of ship 1) | Name | Call sign | Comm. method 2) | Windfind method / Sonde type 3) | Launch height 4) | Area of operations 5) | ASAP Unit Serial No. |
| RESEARCH | METEOR | DBBH | DCP | GPS | 6 m | MEDITERANEAN SEA, RED SEA ATLANTIC | ASAP 1 |
| MERCHANT | HORNBAY | ELML7 | DCP | GPS | 10 m | HAMBURG CARIBBEAN SEA | ASAP 5 |
| research | polarstern | dblk | dcp | gps / vaisala | 10 m | north atlantic south atlantic | --- |
| Merchant ship, research ship, supply ship, etc. Using IDCS, Inmarsat-C, or others E.G. GPS/Vaisala RS80-G, Loran/Vaisala RS80-L, VIZ GPS Mark II Microsonde, etc. The height above sea level from where the sonde and balloon is released Ocean area, e.g. North Pacific, North Atlantic, Indian Ocean, variable |

| Summary of performance of ASAP units during the year |
| --- |
| Call sign | Total No. of sondes launched | No. of messages transmitted | No. of relaunches | Averrage terminal sounding height ( km ) | Percentage on GTS 1) |
| DBBH | 377 | 361 | --- | 19.808 | 96 % |
| ELML7 | 515 | 343 | --- | 18.439 | 67 % * |
| dblk | 318 | 188 | --- | 32.000 | 59 % * |
| Total or average | 1210 | 892 | --- | 23.416 |  |
| Based upon reports received at a data centre or GTS insertion point, name ................., Ratio of reports recelved against reports transmitted * data only partially available, because sometimes call sign mutilated |

Annual National ASAP Report

COUNTRY: Sweden-Iceland.     NAME OF AGENCY: SMHI  IMO   YEAR: 1999

| 1 ASAP units operated during the year on 2 ships |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of ship1) | Name | Call sign | Comm. method2) | Windfind method 3) | Launch height4) | Area of operations5) | ASAP Unit Serial No. |
| Mer-chant | Goda-foss | V2XM | Inmarsat- C | OMEGA/-LORAN-C | 13 m | N-Atlantic, (Iceland-USA) |  |
| Mer-chant | Selfoss | S6LA | Inmarsat- C | OMEGA/-LORAN-C | 13 m | N-Atlantic, (Iceland-USA) |  |
| 1) Merchant ship, research ship, supply ship, etc. 2) Using IDCS, Inmarsat-C, or others 3) Loran-C, GPS, Loran/GPS, RTH 4) The height above sea level from where the sonde and balloon is released 5) Ocean area, e.g. North Pacific, North Atlantic, Indian Ocean, variable |  |  |  |  |  |  |  |

| Summary of performance of ASAP units during the year |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Call sign | Total No. of sondes launched | No. of messages transmitted | No. of relaunches | Average terminal sounding height (km) | Percentage on GTS1) |
| V2XM | 69 | 54 | 0 | 21.2 | 78.3 |
| S6LA | 105 | 60 | 0 | 23.0 | 57.1 |
| Total or average | 174 | 114 | 0 | 22.1 |  |
| 1) Based upon reports received at a data centre or GTS insertion point, name: IMO Ratio of reports received against reports transmitted 100% |  |  |  |  |  |

Annual National ASAP Report (continued)

YEAR 1999.

COMMENTS ON PERFORMANCE: The ship operates between Reykjavik, Iceland and Norfolk, Virginia, USA, departing from Reykjavík every fourth Friday afternoon. During this year of operation there have been a series of problems.  Some of the problems were due to weather and mechanical reasons many were due to human factors.

In the beginning of May m/v Godafoss was replaced by m/v Selfoss.  We were able to transfer the instruments to Selfoss in the beginning of June.  It was a simple operation but expencive because of the short time we had.  On m/v Selfoss we had lot a series of problems because the crew was new and unexperienced and the shipping company put up new officers on every trip, so the problem was ongoing all year.  We also had serious problems with the transmission of messages with the old Inmarsat-C instrumentation onboard. One factor in diminishing the efficiency of the route is that the new ship goes faster than the older one, using less time at sea  [about 2 days pr trip or 4 soundings]

ESTIMATES FOR FOLLOWING YEAR: The ASAP unit is planned to be operated on the same basis as in 1999, using LORAN-C for windfinding.  Recently the route was changed a little. The ship is now usually calling upon Thorshavn in Faeroe Islands when leaving Reykjavik and therefore using more time at sea. Therefore, we are hopeful that the ASAPwill be more effective in year 2000.

oooOOOooo

Annual National ASAP Report

COUNTRY: JAPAN     NAME OF AGENCY: Japan Meteorological Agency       YEAR: 1999

| 7 ASAP units operated during the year on 7 ships |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of ship1) | Name | Call sign | Comm. method2) | Windfind method/ Sonde type 3) | Launch height4) | Area of operations5) | ASAP Unit Serial No. |
| R.V. | Ryofu Maru | JGQH | others (DCP) | GPS/Vaisala RS80-G | 8m | North Pacific | 708514 |
| R.V. | Kofu Maru | JDWX | others (DCP) | GPS/Vaisala RS80-G | 6 m | Seas adjacent to Japan | 191678 |
| R.V. | Seifu Maru | JIVB | others (DCP) | GPS/Vaisala RS80-G | 6 m | Seas adjacent to Japan | 458533 |
| R.V. | Chofu Maru | JCCX | others (DCP) | GPS/Vaisala RS80-G | 6 m | Seas adjacent to Japan | 126138 |
| R.V. | Keifu Maru | JBOA | others (DCP) | RTH/Meisei RS91 | 8 m | North Pacific | 32889 |
| R.V. | Shumpu Maru | JFDG | Inmarsat-C | GPS/Vaisala RS80-G | 4 m | Seas adjacent to Japan | － |
| R.V. | Mirai | JNSR | Inmarsat-C | GPS/Vaisala RS80-G | 16 m | North Pacific | － |
| 1) Merchant ship, research ship, supply ship, etc. 2) Using IDCS, Inmarsat-C, or others 3) E.G. GPS/Vaisala RS80-G, Loran/Vaisala RS80-L, VIZ GPS Mark II Microsonde, etc. 4) The height above sea level from where the sonde and balloon is released 5) Ocean area, e.g. North Pacific, North Atlantic, Indian Ocean, variable |  |  |  |  |  |  |  |

| Summary of performance of ASAP units during the year |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Call sign | Total No. of sondes launched | No. of messages transmitted | No. of relaunches | Average terminal sounding height (km) | Percentage on GTS1) |
| JGQH | 140 | 260 | 5 | 24.5 | 100% |
| JDWX | 75 | 75 | 6 | 25.8 | 100% |
| JIVB | 113 | 222 | 4 | 22.3 | 100% |
| JCCX | 163 | 290 | 7 | 20.0 | 100% |
| JBOA | 261 | 548 | 12 | 23.5 | 100% |
| JFDG | 54 | 54 | 2 | 20.9 | 100% |
| JNSR | 292 | 274 | 26 | 21.6 | － |
| Total or average | 1098 | 1723 | 62 | 22.5 | － |
| 1) Based upon reports received at a data centre or GTS insertion point, name: JMA Ratio of reports received against reports transmitted |  |  |  |  |  |

Annual National ASAP Report (continued)

YEAR  1999

COMMENTS ON PERFORMANCE:

The Japan Meteorological Agency (JMA) makes upper-air observations in the western North Pacific and the waters adjacent to Japan on a semi-regular basis on five vessels among six oceanographic/meteorological observation vessels operated by JMA.

From June 27 to July 6, 1999, four research vessels (Keifu Maru, Chofu Maru, Seifu Maru and Shumpu Maru) of JMA performed enhanced upper-air observations (4 or 8 times per day) in order to monitor and investigate mesoscale covective systems during the Baiu period in the East China Sea and south of Japan.  R/V Shumpu Maru does not make upper-air observation on a regular basis, but joined the enhanced observations.

From June 17 to July 17, R/V Mirai of the Japan Marine Science Technology Center (JAMSTEC) performed enhanced upper-air observations in the vicinity of Nauru island concerning the international study of tropical climate named ‘Nauru99’.

ESTIMATES FOR FOLLOWING YEAR:

Number of soundings is expected to decrease, because R/V Keifu Maru will be decommissioned in June 2000.

oooOOOooo

Annual National ASAP Report

COUNTRY: .Great Britain. . . . . . . .    NAME OF AGENCY: .Met. Office./ BAS . . . . . . . .     YEAR: .1999 . .

| . . . .2 . . ASAP units operated during the year on . . .2 . . ships |
| --- |
| Type of ship1) | Name | Call sign | Comm. Method2) | Windfind method/ Sonde type3) | Launch height4) | Area of operations5) | ASAP Unit Serial No. |
| Merchant | CanMar Pride | ZCBP6 | Inmarsat -C | GPS RS80-15GH | 22 metres | North Atlantic | N/A |
| Research | James Clark Ross | ZDLP | Inmarsat –C | GPS RS80-15GH | 17 metres | Arctic | N/A |
| Merchant ship, research ship, supply ship, etc. Using IDCS, Inmarsat-C, or others E.G. GPS/Vaisala RS80-G, Loran/Vaisala RS80-L, VIZ GPS Mark II Microsonde, etc. The height above sea level from where the sonde and balloon is released Ocean area, e.g. North Pacific, North Atlantic, Indian Ocean, variable |

| Summary of performance of ASAP units during the year |
| --- |
| Call sign | Total No. of sondes launched | No. of messages transmitted | No. of relaunches | Average terminal sounding height (km) | Percentage on GTS1) |
| ZCBP6 | 57 | 37 | 6 | 25228 | 100 |
| ZDLP | 94 | 74 | - | - | 100 |
| Total or average | 151 | 111 | 6 | 25228 | 100 |
| Based upon reports received at a data centre or GTS insertion point, name: EGRR. Ratio of reports received against reports transmitted. |

Annual National ASAP Report (continued)

YEAR  .1999

COMMENTS ON PERFORMANCE:  Figures in preceding tables are based on the first 5 ASAP operational voyages of the containership CanMar Pride. The first voyage, which commenced 19 July 1999, was a training session to teach the Deck Officers how to use the equipment. Overall, this was operationally successful, all equipment operating satisfactorily and the Officers learning how to operate the system. There were some operational problems during the 3rd and 5th voyages, which have since been rectified. No further information available re the James Clark Ross Arctic scien

ESTIMATES FOR FOLLOWING YEAR: The UK Met. Office will continue to operate one ASAP unit on the CanMar Pride. The British Antarctic Survey are expected to operate one ASAP unit on the James Clark Ross on some voyages.

oooOOOooo

Annual National ASAP Report

COUNTRY: . . .USA . . .   NAME OF AGENCY: . . NOAA/OGP. . . . . .. . .  YEAR: 1999. . . .

| ...1... ASAP units operated during the year on ...1... ships |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of ship1) | Name | Call sign | Comm. method2) | Windfind method/ Sonde type 3) | Launch height4) | Area of operations5) | ASAP Unit Serial No. |
| 1 | Ronald H. Brown | WTEC | Inmarsat- C | Vaisala RS-80 G | 3.2 m | Worldwide | 290644 |
| 1) Merchant ship, research ship, supply ship, etc. 2) Using IDCS, Inmarsat-C, or others 3) E.G. GPS/Vaisala RS80-G, Loran/Vaisala RS80-L, VIZ GPS Mark II Microsonde, etc. 4) The height above sea level from where the sonde and balloon is released 5) Ocean area, e.g. North Pacific, North Atlantic, Indian Ocean, variable |  |  |  |  |  |  |  |

| Summary of performance of ASAP units during the year |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Call sign | Total No. of sondes launched | No. of messages transmitted | No. of relaunches | Average terminal sounding height (km) | Percentage on GTS1) |
| WTEC | 752 | 625 |  | 17 | 98 |
| Total or average | 752 | 625 |  | 17 | 98 |
| 1) Based upon reports received at a data centre or GTS insertion point, name: ____________ Ratio of reports received against reports transmitted |  |  |  |  |  |

Annual National ASAP Report (continued)

YEAR  1999

COMMENTS ON PERFORMANCE:

There was a loss of about 17 % of the radiosondes as they came out of the box. Vaisala are aware of the problem, as are others, and it is hoped that things are corrected.

ESTIMATES FOR FOLLOWING YEAR:

Next year will have a limited use of the upper-air sounding system aboard the Ronald H. Brown.  The estimate is about 30 % of the number of soundings taken this past year.

oooOOOooo

# Status Of The Meteosat System

## Meteosat Satellites Operations

Meteosat-7 is the current prime operational satellite.

Meteosat-6 is the in-orbit spare located at 9°W. During the Autumn period Meteosat-6 was used to perform rapid scanning in support of MAP, the Mesoscale Alpine Programme. The spacecraft scanned the Alpine region up to six times per half hour slot.

Meteosat-5 continues to operate at 65°E providing data covering the Indian Ocean.

## DCPs on the Internet

The EUMETSAT DCP on-line service continues for DCP operators. The web based system for co-ordinating the IDCS channels was introduced at the end of 1998 and was enhanced in 1999.

## ASAP DCP Transmissions

Table 1 shows the ASAP DCP transmissions through the Meteosat satellite from January to December 1999. Figures 3 to 7 show this graphically for the various countries.

Monthly transmission figures are sent via e-mail to the ASAP monitoring Centre in Toulouse.

| DCP Address | DCP Name | Jan | Feb | Mar | Apr | May | June | July | Aug | Sep | Oct | Nov | Dec |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 112007C8 | D/ASAP 1 | 272 | 173 | 314 | 329 | 339 | 313 | 294 | 288 | 330 | 296 | 265 | 223 |
| 112044C2 | D/ASAP 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 112057B4 | D/ASAP 3 | 315 | 255 | 275 | 331 | 331 | 321 | 347 | 279 | 119 | 917 | 817 | 674 |
| 160037D2 | D/ASAP 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 1180F11A | F/ASAP 1 | 184 | 191 | 206 | 206 | 228 | 178 | 165 | 177 | 191 | 199 | 199 | 192 |
| 11810364 | F/ASAP 2 | 159 | 217 | 165 | 0 | 173 | 177 | 184 | 189 | 180 | 191 | 194 | 223 |
| 11819606 | F/ASAP 3 | 96 | 38 | 0 | 34 | 3 | 132 | 17 | 36 | 54 | 94 | 52 | 98 |
| 1181A39C | F/ASAP 4 | 131 | 49 | 194 | 216 | 193 | 188 | 191 | 179 | 201 | 190 | 189 | 195 |
| 1183207C | F/ASAP 5 | 169 | 191 | 197 | 203 | 186 | 190 | 191 | 183 | 185 | 170 | 89 | 172 |
| 11836376 | SPAIN/ASAP 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

Table 1: ASAP DCP transmissions

Figure 1: D/ASAP transmissions

Figure 2: F/ASAP transmissions

## ASAP IDCS Allocations

The following tables give the present allocations for the ASAP DCPs on I12.

ASAP COMMUNICATIONS SCHEDULE  FOR OPERATION ON IDCS CHANNEL 12

Transmission timeslots on International Channel 12 for ASAP use 90 second timeslots composed of a 30 second guard band and 59 seconds of data.

The following are the allocations for the primary first transmission timeslot at 0000 and 1200UTC. The second transmission is 30 minutes later. The backup timeslot is 1 hour after the primary timeslot :

| Operator | DCP name | DCP address | Primary Transmission Time For 0000 UTC First Transmission Second Transmission 00.30.00 - 01.00 00 01.00.00 - 01.30.00 |
| --- | --- | --- | --- |
| Spain | SPAIN/ASAP 1 | 11501112 | 00.30.00 - 00.31.30 | 01.00.00 - 01.01.30 |
| NOAA | GOES/SEAS 59 | A040056E | 00.31.30 - 00.33.00 | 01.01.30 - 01.03.00 |
| Reserved for future ASAP use | N/A | N/A | 00.33.00 - 00.34.30 | 01.03.00 - 01.04.30 |
| NOAA | GOES/SEAS 60 | A0401618 | 00.34.30 - 00.36.00 | 01.04.30 - 01.06.00 |
| Germany | D/ASAP 1 | 112007C8 | 00.36.00 - 00.37.30 | 01.06.00 - 01.07.30 |
| Germany | D/ASAP 2 | 112044C2 | 00.37.30 - 00.39.00 | 01.07.30 - 01.09.00 |
| Germany | D/ASAP 3 | 112057B4 | 00.39.00 - 00.40.30 | 01.09.00 - 01.10.30 |
| Germany | D/ASAP 4 | 160037D2 | 00.40.30 - 00.42.00 | 01.10.30 - 01.12.00 |
| Reserved for future ASAP use | N/A | N/A | 00.42.00 - 00.43.30 | 01.12.00 - 01.13.30 |
| NOAA | GOES/SEAS 61 | A0402382 | 00.43.30 - 00.45.00 | 01.13.30 - 01.15.00 |
| Reserved for future ASAP use | N/A | N/A | 00.45.00 - 00.46.30 | 01.15.00 - 01.16.30 |
| NOAA | GOES/SEAS 62 | A04030F4 | 00.46.30 - 00.48.00 | 01.16.30 - 01.18.00 |
| France | F/ASAP 1 | 1180F11A | 00.48.00 - 00.49.30 | 01.18.00 - 01.19.30 |
| NOAA | GOES/SEAS 63 | A0404664 | 00.49.30 - 00.51.00 | 01.19.30 - 01.21.00 |
| France | F/ASAP 2 | 11810364 | 00.51.00 - 00.52.30 | 01.21.00 - 01.22.30 |
| France | F/ASAP 3 | 11819606 | 00.52.30 - 00.54.00 | 01.22.30 - 01.24.00 |
| France | F/ASAP 4 | 1181A39C | 00.54.00 - 00.55.30 | 01.24.00 - 01.25.30 |
| Reserved for future ASAP use | N/A | N/A | 00.55.30 - 00.57.00 | 01.25.30 - 01.27.00 |
| France | F/ASAP 5 | 1183207C | 00.57.00 - 00.58.30 | 01.27.00 - 01.28.30 |
| Reserved for future ASAP use | N/A | N/A | 00.58.30 - 01.00.00 | 01.28.30 - 01.30.00 |

| Operator | DCP name | DCP address | Backup Transmission Time For 0000 UTC First Transmission Second Transmission 01.30.00 - 01.30 00 02.00.00 - 02.30.00 |
| --- | --- | --- | --- |
| Spain | SPAIN/ASAP 1 | 11501112 | 01.30.00 - 01.31.30 | 02.00.00 - 02.01.30 |
| NOAA | GOES/SEAS 59 | A040056E | 01.31.30 - 01.33.00 | 02.01.30 - 02.03.00 |
| Reserved for future ASAP use | N/A | N/A | 01.33.00 - 01.34.30 | 02.03.00 - 02.04.30 |
| NOAA | GOES/SEAS 60 | A0401618 | 01.34.30 - 01.36.00 | 02.04.30 - 02.06.00 |
| Germany | D/ASAP 1 | 112007C8 | 01.36.00 - 01.37.30 | 02.06.00 - 02.07.30 |
| Germany | D/ASAP 2 | 112044C2 | 01.37.30 - 01.39.00 | 02.07.30 - 02.09.00 |
| Germany | D/ASAP 3 | 112057B4 | 01.39.00 - 01.40.30 | 02.09.00 - 02.10.30 |
| Germany | D/ASAP 4 | 160037D2 | 01.40.30 - 01.42.00 | 02.10.30 - 02.12.00 |
| Reserved for future ASAP use | N/A | N/A | 01.42.00 - 01.43.30 | 02.12.00 - 02.13.30 |
| NOAA | GOES/SEAS 61 | A0402382 | 01.43.30 - 01.45.00 | 02.13.30 - 02.15.00 |
| Reserved for future ASAP use | N/A | N/A | 01.45.00 - 01.46.30 | 02.15.00 - 02.16.30 |
| NOAA | GOES/SEAS 62 | A04030F4 | 01.46.30 - 01.48.00 | 02.16.30 - 02.18.00 |
| France | F/ASAP 1 | 1180F11A | 01.48.00 - 01.49.30 | 02.18.00 - 02.19.30 |
| NOAA | GOES/SEAS 63 | A0404664 | 01.49.30 - 01.51.00 | 02.19.30 - 02.21.00 |
| France | F/ASAP 2 | 11810364 | 01.51.00 - 01.52.30 | 02.21.00 - 02.22.30 |
| France | F/ASAP 3 | 11819606 | 01.52.30 - 01.54.00 | 02.22.30 - 02.24.00 |
| France | F/ASAP 4 | 1181A39C | 01.54.00 - 01.55.30 | 02.24.00 - 02.25.30 |
| Reserved for future ASAP use | N/A | N/A | 01.55.30 - 01.57.00 | 02.25.30 - 02.27.00 |
| France | F/ASAP 5 | 1183207C | 01.57.00 - 01.58.30 | 02.27.00 - 02.28.30 |
| Reserved for future ASAP use | N/A | N/A | 01.58.30 - 02.00.00 | 02.28.30 - 02.30.00 |