# CHAPTER 3

# Joint distribution of wave directions and heights

If a wave field is comprised of several wave patterns, then each of the patterns /wind sea or swell(s)/ can be described by a corresponding wave height h, period (, for example and direction of propagation (.

The joint distribution density f(h, () is used most frequently for the probabilistic description of the wave field. An example of corresponding recurrence f(h,()dhd( (%) for the Baltic Sea (autumn) is given in Table 3.1 and is shown in Fig. 3.1.

The analysis of such joint distributions is specific because (h,() represents a system of random values where h is a scalar value and ( is an  angular value. The coefficient of colligation Cf will be used to check the hypothesis that random values h and ( are independent, as follows:

Figure 3.1. Probability of wave heights by direction

The Baltic Sea

Table 3.1.

Joint  probability (%) of mean wave heights and directions.

The Baltic Sea. Autumn. Total number of observations N=12770.

| h, m | N | NE | E | SE | S | SW | W | NW | f(h) dh |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.0-0.5 | 1 | 1 | 2 | 3 | 4 | 4 | 3 | 1 | 19 |
| 0.5-1.0 | 4 | 3 | 3 | 5 | 7 | 10 | 11 | 6 | 49 |
| 1.0-1.5 | 1 | <1 | 1 | 1 | 1 | 4 | 6 | 3 | 18 |
| 1.5-2.0 | <1 | <1 | <1 | – | <1 | 1 | 5 | 2 | 9 |
| 2.0-2.5 | <1 | – | – | – | – | <1 | 2 | 1 | 3 |
| 2.5-3.0 | – | – | – | – | – | <1 | 1 | <1 | 1 |
| >3.0 | – | – | – | – | – | – | <1 | <1 | <1 |
| f()d | 6 | 4 | 6 | 9 | 12 | 20 | 29 | 14 | 100 |

(3.1)

Also we will use regression lines:

(3.2)

(3.3)

and scedastic (conditional variance) curves:

,            (3.4)

(3.5)

According to [Mardia, 1972] the regression is estimated as the mean direction

(3.6)

while expression

(3.7)

with

gives an estimate for conditional variance (3.5).

The value

(3.8)

that follows from an analogy with a wrapped normal distribution can be used as a measure of spreading of angular value (. It is similar to the r.m.s. deviation. Tables 3.2 and 3.3 are based on the data from Table 3.1, and present conditional means /see (3.2),(3.3)/ and variances /see (3.4),(3.5)/ for height of waves from different directions.

Table 3.2.

Conditional means (3.2), variance (3.4), and r.m.s. deviation of wave height h for given direction (

| β | N | NE | E | SE | S | SW | W | NW |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| mh¦(, m | 0.8 | 0.7 | 0.6 | 0.6 | 0.6 | 0.8 | 1.3 | 1.1 |
| Dh¦(, m2 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.2 | 0.5 | 0.4 |
| (h¦(, m | 0.4 | 0.3 | 0.3 | 0.3 | 0.3 | 0.5 | 0.7 | 0.6 |

Table 3.3.

Conditional means (3.3), variance (3.5), and r.m.s. deviation of wave direction β
for given wave height h

| h, m | 0.25 | 0.75 | 1.25 | 1.75 | 2.25 | 2.75 | 3.25 | 3.75 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| m(¦h,0 | 189 | 239 | 264 | 273 | 276 | 275 | 275 | 275 |
| D(¦h, rad2. | 0.60 | 0.68 | 0.38 | 0.13 | 0.09 | 0.05 | 0.03 | 0.03 |
| ((¦h,0 | 78 | 86 | 56 | 30 | 25 | 18 | 14 | 13 |

The computations show that values of cf differ from 1, lines of regression (3.2) and (3.3) are not parallel to co-ordinates, conditional variance  D(|h differs from the absolute variance D( = 0.59 rad2,.(( = 76(. This suggests that the two-dimensional distribution density f(h,() has to be approximated by expression

(3.9)

Among existing approximations of f(((h) the most useful is the Mises distribution. Its mean ( and scale k parameters depend on wave height h:

(3.10)

where

Here

(3.11)

is the modified first type zero-order cylindrical function. Variation of parameters ( and k makes it possible to reconstruct all angular distributions, from uniform to a narrow one.

Comparisons of f(h,() and approximation (3.10) for parameters ( and k taken from Table 3.4 showed satisfactory agreement.

We can use the distribution F(h|() for any given ( to estimate hmax with the help of both methods of initial distribution and the annual maximum series. The absolute wave height distribution is a mixed distribution of waves coming from different sectors of  wave directions (i:

.                (3.12)

Here (i are weight coefficients, which meet the compliance condition that. Computation of extreme values for individual directions is then made by simple adjustment of omni-directional wave height distribution f(h) with distribution of wave height for given directions f(h|(i). Wave height h(T), expected to occur once in T years for direction ( will be equal to a certain quantile of the omni-directional distribution f(h).

Table 3.5 provides estimates of a hundred year mean wave height, both directional and omni-directional, based on data from Table 3.1.

Table 3.4.

Parameters ( and k of conditional distribution of wave heights (3.10).

Data from Table 3.1

| h, m | 0–0.5 | 0.5–1.0 | 1.0–1.5 | 1.5–2.0 | 2.0–2.5 | 2.5–3.0 | 3.0–4.0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (, 0 | 189 | 239 | 264 | 273 | 276 | 275 | 275 |
| k | 0.8 | 0.7 | 1.8 | 4.2 | 6.5 | 7.2 | 7.8 |

## Table 3.5

Directional and omni-directional estimates of one hundred year wave height.

AMS method. The Baltic Sea

| ( | N | NE | E | SE | S | SW | W | NW | omni-directional |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| h(100), m | 2.7 | 2.4 | 2.3 | 2.4 | 2.7 | 4.0 | 5.1 | 4.4 | 5.1 |

It is seen that the highest waves in the Baltic Sea mostly propagate from the west. If traditional computations of absolute and conditional distributions are used, a discrepancy often occurs that the omni-directional wave height estimate exceeds the maximum (over all directions) estimate computed taking into account directional distribution [Proceedings, 1986]. Estimates of long return period wave heights, if they are based on relation (3.12), eliminate this typical discrepancy.

---oooOooo---