## Slide 1: Copernicus Marine Environment Monitoring Service MED-MFC and In situ Tac: the data infrastructures and the use of data in the Med forecasting system
Giovanni Coppini (CMEMS MED-MFC coordinator)
Centro Euro-Mediterraneo sui Cambiamenti Climatici (CMCC), Ocean Predictions and Applications, Lecce, Italy
With contributions of colleagues from:
Istituto Nazionale di Geofisica e Vulcanologia (INGV), Bologna, Italy,
Hellenic Center for Marine Research (HCMR), Greece,
Istituto Nazionale di Oceanografia e di Geofisica Sperimentale (OGS), Trieste, Italy,
University of Bologna, Bologna, Italy
CNR, Italy
Aeronautica Militare
MERCATOR OCEAN

## Slide 2: Outline
Copernicus Marine Monitoring and Environment Service
  In situ Thematic Assembling Centre
  Mediterranean Monitoring and Forecasting Centre
  Service components
  Data assimilation and QC of used data
  Products
  Products’ quality and Cal/Val
EMODNET Physics
Conclusions

## Slide 3: CMEMS technical « internal » Framework: building blocks
http://marine.copernicus.eu
CMEMS is
coordinated by Mercator Ocean

## Slide 4: CMEMS Service timing
The CMEMS operational service is continuously improved and a new upgraded release is delivered every year.
V2 Enter Into Service
April 2016
April 2017
April 2018
May 2015
V3 Enter Into Service
V4 Enter Into Service
V1 Enter Into Service:
Start Operational service

## Slide 5: In Situ Thematic Assembly Centre for Marine Service
The CMS in situ TAC (INSTAC) is a distributed service which aims to provide in situ (water column & sea surface) data to fulfil operational oceanography needs.
It is a distributed service integrating data from various existing sources and services
It is built in the continuity of the developments made in the MyOcean project series turning into an operational service
It’s integrated in the European landscape of in situ data management with EUROGOOS, EMODNet and SeaDataNet.

## Slide 6: In Situ TAC Operation activities
6 regional ROOSes coordinated by 6 research institutes
1 global Distribution Unit hosted by the Coriolis data centre
IN SITU TAC activity coordinated by IFREMER

## Slide 7
External interfaces
Baltic PU
NWS PU
Global PU
IBI PU
Med PU
BS PU
Arctic PU
Baltic DU
NWS DU
Global DU
IBI DU
Med DU
BS DU
Arctic DU
Baltic INSTAC
NWS INSTAC
GLOBAL INSTAC
IBI INSTAC
MED INSTAC
BS INSTAC
Arctic INSTAC
Local Service Desk
CMEMS Service Desk
Global DU
Backup
CMEMS USERS

## Slide 8: Internal Interfaces
INS TAC
Arctic INS TAC
Baltic INS TAC
NWS INS TAC
SWS INS TAC
Med Sea INS TAC
Black Sea INS TAC
Upstream Systems
INS TAC PRODUCTS
Global INS TAC
& Global Backup
Global data sources (GTS, Argo, Ocean Sites)

## Slide 9: How the global Distribtion Unit get data from the GTS ?
INS TAC
Global INS TAC
GTS
Meteo France
Tesac Bathy Trackob
Meds (Canada)
Tesac Bathy Trackob
Ship Buoy Bufr
IAA Meteo France

## Slide 10: INSTAC within International and European lanscape

## Slide 11: Copernicus Ocean Color TAC and SST Mongoos framework
CNR is coordinating the Ocean Color TAC, produce the Ocean color products for the Med and the SST products for the MED in the OSI TAC

## Slide 12: CMEMS - Forecasting and reanalysis
Eastern North Atlantic
Global
Ocean
North West Shelves
Arctic
Baltic
Black Sea
Mediterranean
A Pan-European network of existing infrastructures, value-added by the Copernicus initiative,
coordinated and with common quality standards

## Slide 13
CMEMS Med-MFC Sea products @ marine.copernicus.eu
PHY Reanalysis (1987-2014)
    2D Sea Surface Height
    3D Salinity
    3D Potential Temperature
    3D Zonal/Meridional currents
BIO Reanalysis (1999-2014):
3D Chlorophyll
    3D Nitrate
    3D Phosphate
    3D Primary Production
    3D Phytoplankton biomass
    3D Oxygen
    3D pCO2
    3D pH
Daily mean – Monthly mean
Daily mean – Monthly mean
Monthly mean
PHY Reanalysis (1955-2014)
    2D Sea Surface Height
    3D Salinity
    3D Potential Temperature
    3D Zonal/Meridional currents
Monthly mean
MEDITERRANEAN SEA PHYSICS REANALYSIS (1987- 2014)
MEDITERRANEAN SEA PHYSICS REANALYSIS (1955- 2014)
MEDITERRANEAN SEA BIOGEOCHEMISTRY REANALYSIS (1999- 2014)

## Slide 14: High-level architecture for Med-MFC PU, DU and Backup sub-systems: in 2018 (V4)

## Slide 15: Med-MFC Physical-Biogeochemical components
NEMO-WW3
2-way Circulation-Wave model
Data Assimilation: OceanVar
Med-Currents
OGSTM-BFM
Transport-biogeochem model
Data Assimilation: 3DVAR
Med-Biogeochemistry
1/16o (~6km) hor. res
72 vert. levels

## Slide 16: Med-Currents component @ V2
+ register data rejected
BU: HCMR CMCC
DU: INGV CMCC
OBSERVATIONS
Along track satellite SLA
from CMEMS SL-TAC, for all available satellites:
Jason 2, Cryosat2, Saral/AltiKa
Satellite SST (L4)
from CMEMS OSI TAC
Vertical profiles of T and S
from CMEMS InSitu TAC:
Argo, XBT, Gliders
ATMOSPHERIC FORCINGS
ECMWF 1/8o forecast/analysis fields time resolution: 3/6 hrs:
mean sea level pressure (MSLP)
cloud cover
2m relative humidity
2m air temperature
10m wind velocity
Precipitation
LAND RIVER RUNOFF: Ebro, Rhone, Po, Vjosë, Seman, Buna-Bojana, Nile (climatological data)
DARDANELLES inflow parameterized as a river
BOUNDARY CONDITIONS in the Atlantic: daily analyses/forecasts from Global Ocean MFC @ 1/12° hor. res., 50 vert. lev.
INITIAL CONDITIONS from op. restart
NEMO-WW3
Circulation-Wave
modeling system
2-way hourly coupling
1/16o hor. res
72 vert. levels
Data Assimilation: 3DVar
Satellite and InSitu observations are jointly assimilated using a 3D variational assimilation scheme with a daily assimilation cycle. Non-solar heat flux correction is achieved through satellite SST nudging.
PRODUCTS
3D daily/hourly fields of: T, S, UV; 2D daily/hourly fields of: SSH, Stokes Drift, MLD, Tb
The Operational Chain

## Slide 17
Every Day
T, S, SST, SSH, U, V (indep. data from moorings: calval.bo.ingv.it/)
Med-Currents: Product Quality @ V2

## Slide 18
T, S, SST, SSH, U, V (indep. data from moorings: calval.bo.ingv.it/)
Every Week
T, S, SLA (misfits of quasi-indep. data) medforecast.bo.ingv.it/mfs-copernicus-evaluation/
Med-Currents: Product Quality @ V2
Every Day

## Slide 19
One year (2014) of model integration using ECMWF 10m analyses 6-h winds at 1/8 hor. res
Density scatter plot of WAM hindcast SWH (2014) versus merged buoys' observations
Buoys locations
Med-MFC Waves: 1st validation results
Spatial distribution of the statistical parameters: Bias, RMSE, and r, of the comparison between WAM hindcast SWH for year 2014 and satellite observations.
Bias (m)
RMSE (m)
r
Corr
Coeff
r

## Slide 20: Input data for the Copernicus Marine Service TO THE MED-MFC

## Slide 21: Input and Observations
Available vertical temperature and salinity profiles from Argo, XBT (eXpandable BathyThermograph) and Gliders, delivered via Copernicus INS-TAC Mediterranean Portal (IN SITU-Thematic Assembly Centre),
Sea Level Anomaly from the altimeter missions Saral/AltiKa, Cryosat-2 and Jason-2, provided by CLS SL-TAC
SST nudging is performed using Objective Analyses-Sea Surface Temperature (OA-SST) fields from CNR-ISAC (OSI-TAC)
Water and heat fluxes are interactively computed by bulk formulae using the 6-hours operational analysis and forecast fields from the European Centre for Medium-Range Weather Forecasts (ECMWF). The atmospheric forcing (temperature at 2m, total cloud cover, mean sea level pressure, dew point at 2m, wind at 10m) are downloaded daily from the Centro Nazionale di Meteorologia e Climatologia Aeronautica (CNMCA)

## Slide 22: Data Assimilation Observations
On Tuesday, when the production of the analyses starts, an operational pre-processing procedure checks the quality of the vertical profiles and the Sea Level Altimetry data.
These data are used in the Copernicus Validation System (http://marine.copernicus.eu/web/103-validation-statistics.php).

## Slide 23: Quality Check for IN-SITU Observations
Check date and location flags: only profiles with both flags equal to 1 (corresponding to a correct value) are considered;
Check on observation quality: for each level of the profile, check each pressure, temperature and salinity flags, if one of these is not equal to 1, the level is rejected;
stability check: Negative Brunt-Vaisala frequency data are rejected
Distance check: if two subsequent measurements of T and S are more spaced than 40 meters in the first 150 meters, the profile is rejected;
Spikes check removal.

## Slide 24: Quality Check for SLA Observations
Check date, location and value SLA flags: only data with all the flags equal to 1 are considered.

## Slide 25: SLA Data assimilation checks
Coastal observations: observation with model depth shallower than 150m are rejected
Land-sea mask check: if one of the four model grid point nearest the observation position is land, the observation is rejected
bias observation check: after along track bias removal, misfits bigger than 30cm are rejected

## Slide 26: ARGO Data assimilation checks
Coastal observation: observation with model depth shallower than 150m are rejected
Land-sea mask check: if one of the four model grid point nearest the observation position is land, the observation is rejected
Large misfit check: if T misfit > 5°C of S misfit > 2 PSU is rejected

## Slide 27: XBT Data assimilation checks
Same check for ARGO observation

## Slide 28: GLIDER Data assimilation checks
Same checks for ARGO observation
Too large departure from background: if the mean bias between observation and background vertical profile is bigger than 0.5°C and/or 0.3PSU the full profile is rejected

## Slide 29: Input file Statistics ARGO example
From 2015 the number of ARGO increased due to the usage of deep profilers.
Pre-processing removes on average 30% of input observation
3DVAR removes the 10% on NET input observation

## Slide 30: Input file Statistics SLA example
Pre-processing doesn’t remove observation because we use L3 data
3DVAR removes the 15% on NET input observation

## Slide 31: Input file Statistics GLIDER example
In this case Pre-processing removes a lot of observation because GLIDER observations are raw data with coarse checks
3DVAR removes the 15% on NET input observation

## Slide 32: Input file Statistics XBT example
In this case Pre-processing doesn’t remove data (we use already quality checked files)
3DVAR removes the 1% on NET input observation

## Slide 33: CAL/VAL system Overview
The CalVal (http://calval.bo.ingv.it) is a web-based validation platform developed at INGV for the Near Real Time INDEPENDENT validation of the Med-MFC.
CalVal network purpose is the collection of all the available moored buoys in the Mediterranean Sea. The MonGOOS partners (www.mongoos.eu) are therefore connected to the INGV collection centre in order to provide in NRT all observations and MonGOOS nested sub-systems data extracted at the buoys location.
NRT access to the in-situ observations and sub-regional ocean forecasts is established by FTP protocols between INGV and the collaborating institutes or between INGV and INS-TAC.
After retrieval and quality control check, all data are imported in the MySQL database and relevant model and satellite estimates are calculated.

## Slide 34
ACTUAL INDEPENDENT Cal/Val @ INGV
description
In order to evaluate the quality of the Med-MFC product, a NRT validation system based on Class 4 diagnostics (model and observational data comparison) has been developed.
Independent in-situ observations from 14 centers are daily downloaded operationally at INGV. Observations and corresponding model values are stored in a MySQL DataBase (DB) The evaluated statistics are: RMS and BIAS for model analysis and 3rd day of forecast. The validated variables are:
  Temperature
  Salinity
  Sea Surface Height
  Current velocities
  Sea Surface Temperature
Sea surface temperature is also compared with satellite data. Comparison of observations and model value are made on-fly on a dedicated website communicating with the DB.

## Slide 35
ACTUAL INDEPENDENT Cal/Val @ INGV
http://calval.bo.ingv.it/

## Slide 36: EMODnet Physics: Objectives
Provide through a portal:
  free and open access to marine data from measurement stations and ferryboxes.
  metadata to these parameters using INSPIRE standards.
Monitoring and reporting on the effectiveness of the portal in meeting the needs of users in terms of ease of use, quality of information and fitness for purpose of the products delivered.

## Slide 37: EMODnet Physics: Portal
The portal is providing access to more than 12,000 platforms giving more than 30,000 time series
 | drifting buoy (DB) | Ferrybox and ship (FB) | glider (GL) | fixed platform and mooring time series (MO) | profiling float (PF) | Argo Float (AR) | Radar (RD) | Others | TOTAL
Number | 4159 | 196 | 23 | 3170 | 757 | 4751 | 26 | 174 | 13256

## Slide 38: EMODnet Physics: support
The data can support:
  Maritime economic activities
  Marine Strategy Framework Directive
  Water Framework Directive
  Blue Economy

## Slide 39: Conclusions
Copernicus In situ TAC, Ocean Color and OSI TAC provide operational access to in situ and remote sensing data
In situ TAC receives inputs from GTS
Copernicus Marine Service MED-MFC represents the state of the art of the operational forecasting system for the Mediterranean Sea
Med-MFC operationally produce freely available physical and biogeochemical variables
Every year an upgrdaed version of the CMEMS system is released
Med-MFC performs products quality assessment with independent and quasi-independent data and at different temporal scales and data are QC
EMODNET physics provide free access to data and metadata using INSPIRE standards

## Slide 40
Thanks for your attention
Q/A time
Follow us @ http://marine.copernicus.eu www.sea-conditions.com http://ocean-lab.cmcc.it
Facebook: CMCC Climate e Sea Conditions Twitter: @CmccClimate #chemarefara @giovannicoppini
Youtube: CMCCvideo Contact us @ Giovanni.coppini@cmcc.it Ocean-lab@cmcc.it
Torre dell’Orso Salento Lecce, Apulia