## Slide 1: Using the WMO Rolling Review of Requirements for observing network design: Application to E-SURFMAR
Pierre BLOUCH, Paul POLI
WIGOS Workshop RA-VI – Split, Croatia – 5-7 September 2016

## Slide 2
EuroGOOS
EUMETNET
Data Buoy Cooperation Panel (DBCP)
Surface P, SST, SSS Current Wind, waves
Voluntary Observing Ship (VOS) Surface P, Temp., Hum., Wind, Visual param.,
Sea-Surface T. (SST)
Automated Shipboard Aerological Programme (ASAP) P., Temp., Hum., Wind (z)
T, S (P)
Ship of Opportunity Programme (SOOP)
Argo float
T, S, current (P)
SST, SSS
Global Ocean Surface Underway Data (GOSUD)
Global Sea Level Observing System (GLOSS)
H
Dissolved C, pH, T, S (P) Global Ocean Ship-based Hydrographic Investigations Program (GO-SHIP)
EUMETSAT (+OSI-SAF…)
Icons not to scale
E-SURFMAR
SST, wind, currents, and waves observed by buoys are essential to use satellites. (calibration, validation, monitoring)
(air mass)
(heat)
(ocean-atmosphere exchange of momentum and heat)
ECMWF
E-SURFMAR in the greater context

## Slide 3: Obs. System Network Evolution
Plus…
6-hourly  hourly
Reception delays shortened
Quality improved thanks to service QC
Metadata traceability
2002
2015
December
December
Conventional VOS
AWS on VOS
Moored Buoy
Drifting Buoy
Legend

## Slide 4: Why redesign E-SURFMAR?
We need to ensure the core mission still meets stakeholders needs: weather forecasting (and climate monitoring)
  Review of capacity with respect to user requirements
The context has evolved:
  Emerging needs from new operational applications
    European Copernicus services: oceanography, climate monitoring, emergency
    National or regional needs: coastal prediction
   New opportunities
    Allowed by technological developments
   Network design has matured
    e.g., "Observing network design principles“, WMO Pub. 1160

## Slide 5: Observing system needs and evolutions
Requirements
Actual Capacity
Gaps, Impact, Feasibility
Statements of Guidance,
by application area
OSCAR Requirements
WIGOS Information Resource
JCOMMOPS database already includes KPIs, by network

## Slide 6: 1st method: use Statements of Guidance
Structured by application area,
  and then by variable
Considerations
  Weight the various applications by « importance » for the funding body
  Observations serve more (in the end) than the intended purpose of whoever funds the network
  Capacity of a network, unless global or unique, is not that described in the SoG
 Homework needed to re-do the gap analysis, for the particular observation network

## Slide 7: 2nd method: Gap analysis, based on OSCAR database and current network capacity
Database of requirements: essentially a list
Each entry contains
  Variable
  Application area
  Uncertainty*
  Horizontal resolution*
  Observing cycle*
  Timeliness*
  Plus some other metadata (date of requirement, comment…)
*There are 3 levels: threshold, breakthrough, and goal

## Slide 8: E-SURFMAR gap analysis w.r.t. OSCAR
Select variables relevant to the marine surface:
  40 eligible variables
  Then order the variables according to a relevance index: mix of
    Feasibility
    Impact
  Consider variables with highest feasibility & impact
Derive current capacity of the network, by variable, and compare with requirements for
  Quality
  Spatio-temporal sampling
  Timeliness
  The following slides show examples for each.

## Slide 9: Quality example 1: Surface pressure observations at sea
0.35 hPa for drifting buoys
0.41 hPa for moored buoys
0.50 hPa for automated VOS recruited by EUMETNET countries
0.50 hPa for automated VOS recruited by non-EUMETNET countries
0.81 hPa for conventional VOS recruited by EUMETNET countries
0.98 hPa for conventional VOS recruited by non-EUMETNET countries
P(z)
Observation error estimates from Desroziers diagnostics applied to ECMWF observation feedback for observations at the sea surface between July and September 2015, for observations assimilated in the EUMETNET area

## Slide 10: Data quality for MSLP, from automated VOS
Separating by ship size, for S-AWS:
  by ship length L:
    4 m≤L<100 m: 0.39 hPa
    100 m≤L<200 m: 0.58 hPa
    200 m≤L<400 m: 0.61 hPa
  by barometer height H:
    1 m≤H<10 m: 0.37 hPa
    10 m≤H<20 m: 0.44 hPa
    20 m≤H<40 m: 0.58 hPa
Chart: 
Observation error estimates from Desroziers diagnostics applied to ECMWF observation feedback for observations at the sea surface between July and September 2015, for observations assimilated in the EUMETNET area

## Slide 11: Quality example 2: Wind speed
1.8 m/s for VOS (regardless of country of recruitment)
  Separating by ship length L:
    4 m≤L<100 m: 1.4 or 1.7 m/s (auto or conventional, resp.)
    100 m≤L: 1.9 m/s
1.2 m/s for moored buoys
Observation error estimates from Desroziers diagnostics applied to ECMWF observation feedback for observations at the sea surface between July and September 2015, for observations assimilated in the EUMETNET area

## Slide 12: Spatio-temporal sampling example 1 Surface pressure observations at sea
Applica-tion area | Type of requirement | Equivalent Spatio-temporal density, per km2 per hour
Climate-AOPC | Goal | 8.3 x 10-6
 | Breakthrough | 1.9 x 10-6
 | Threshold | 1.7 x 10-7
Global NWP | Goal | 4.4 x 10-3
 | Breakthrough | 1.7 x 10-5
 | Threshold | 3.3 x 10-7
High Res NWP | Goal | 2.0
 | Breakthrough | 4.0 x 10-2
 | Threshold | 8.3 x 10-4
Maritime Safety | Goal | 2.0 x 10-2
 | Breakthrough | 8.0 x 10-4
 | Threshold | 8.3 x 10-6
Coastal ocean forecasting | Goal | 1.0
 | Breakthrough | 3.3 x 10-3
 | Threshold | 2.7 x 10-4

## Slide 13: Example evolution scenarios for meeting Global NWP Breakthrough target
Density mapped into equivalent number of hourly platforms
Upgrade all (107) NOAA SST drifting buoys with barometers
(13  23%)
Both
(13  27%)
Convert EU fleets CONV VOS into AWS (13  15%)
ABOVE target
BELOW target
WHAT IF …

## Slide 14: Spatio-temporal sampling example 2: in situ (buoy, VOS) coastal wind observations
Black indicates data within 25 km from shore. If you can see the coastline (red or blue) then it means there are no wind data there.

## Slide 15: Timeliness example Observations from drifting buoys
Global NWP goal, breakthrough
High-res NWP goal, breakthrough
Maritime safety goal, breakthrough
All other requirements >1h

## Slide 16: Other considerations: Relative impact of the network, for a given application
Observations made by buoys have the largest per-observation impact on the reduction of 24-hour forecast error (according to a global dry energy norm)
This benefit comes mostly from drifters measuring surface pressure
Other impact studies, other domains (LAM, N.Atl.), other metrics (DFS, OSE…) have shown similar results
ECWMF result: obs. impact on data assimilation
András Horányi and Carla Cardinali, December, 2014, “The impact of mean sea level pressure observations from drifting buoys”,
WMO-ECMWF study.
Nov-Dec 2010
Jul-Aug 2012
Similar result in ECMWF reanalyses (ERA-Interim)
In fact SST (+sea-ice) and surface pressure form the backbone of a climate reanalysis system (ERA-20C)

## Slide 17: Other considerations: Data of no immediate measurable impact on the mission at hand*, but still highly relevant through satellite calibration and data assimilation Example: Wave data from moored buoys
*in situ wave data are generally not assimilated by global NWP

## Slide 18: Other example: sea-level tide gauges
The European ocean community (EuroGOOS) concentrate the data into the EMODNET Physics portal
The link to the GTS is missing, so few get exchanged there
  Their absence from the GTS is pointed out by SoG
  Several NHMS have responsibility to predict surges
  Pushing these data to the GTS should be done
 MoU to be prepared between EUMETNET and EuroGOOS

## Slide 19: Conclusions
E-SURFMAR network redesign builds heavily on Statements of Guidance and OSCAR requirements
  Two key elements of RRR
However, for a non-global or non-unique network, it is still required to carry out a gap analysis
  e.g., the SoG generally comments on global capacity
In the future, one may expect
  Capacity estimates (quantified) across the networks
    To be enabled by WIGOS Information Resource
    Notable progress already made (recently) by JCOMMOPS, with KPIs by network and by area
  Gap analysis by network and by area

## Slide 20: Thank you!