|  | VOS Report for 2015 | Country = | EUMETNET |
| --- | --- | --- | --- |
|  | a. | Programme description: |
|  | Category | No. of ships at 31 Dec 2015 | Recruitments in 2015 | De-recruitments In 2015 | Comments |
|  | Selected |  |  |  |  |
|  | Selected AWS | 9 | 1 | 1 | Minerva Uno : recruited ; Urania : derecruited |
|  | VOSClim |  |  |  |  |
|  | VOSClim AWS | 2 |  |  |  |
|  | Supplementary |  |  |  |  |
|  | Supplementary AWS | 22 | 4 |  | 3 EUCAWS prototypes plus one deck drifter recruited |
|  | Auxiliary |  |  |  |  |
|  | Auxiliary AWS |  |  |  |  |
|  | Other |  |  |  |  |
|  | National VOS Total | 33 |  |  |  |
|  | National VOS Target |  |  |  |  |  |
|  | National VOSClim Target |  |  |  |  |  |
|  | b. | Data management: |
|  | Total number of ship observations (BBXX) distributed on the GTS in 2015 | 167768 |
|  | Dates when VOS data submitted to the GCCs in 2015 |  |

|  | c. | Shipboard Automatic Weather System |
| --- | --- | --- |
|  | Type | No. of ships at 31 Dec 2015 | Manual Input Yes / No | Method of Comms | Year1 Plans |
|  | BATOS | 11 | Yes | INMARSAT/IRIDIUM | 0 |
|  | BAROS | 18 | No | IRIDIUM | 0 |
|  | EUCAWS (prototypes) | 3 | Yes | IRIDIUM | 2 |
|  | Deck Drifters | 1 | No | IRIDIUM | 0 |
|  | d. | Electronic logbooks: (TurboWin, SEAS, OBSJMA) |
|  | Software & version | No. of ships at 31 Dec 2015 | Implementation plans |

| e. | Standard Meteorological Equipment: (Types and Settings) |
| --- | --- |
| Equipment Type / Element | Manual Instrumentation | AWS Instrumentation |
| Barometer |  | PTB220 |
|  |  | PTB210 |
| Default national setting | Station Level | Station Level |
| Barograph |  |  |
| Default national setting | Station Level or Mean Sea Level | Station Level or Mean Sea Level |
| Thermometers |  | PT100 from humidity sensor (HMP45D, HMP110) |
| Sea Surface Temperature |  | PT100 |
| Wind Speed |  | WINDSONIC GILL |
| Wind Direction |  | WINDSONIC GILL |

| f. | PMO ship visit activities: (if a visit is for dual purposes, include all purposes) |
| --- | --- |
| Activity | Manual Ship | AWS Ship | Comment |
| Routine VOS inspections |  | 17 | Batos and Baros |
| VOS recruitment visits |  | 5 | Minerva Uno (Batos), 3 EUCAWS prototypes and one deck drifter |
| VOS de-recruitment visits |  | 1 | Urania (Batos) |
| VOS courtesy or foreign visits |  |  |  |
| Total visits to VOS |  |  |
| Routine ASAP inspections |  |  |  |
| ASAP recruitment visits |  |  |  |
| ASAP de-recruitment visits |  |  |  |
| ASAP courtesy visits |  |  |  |
| Total visits to ASAP |  |  |  |
| Routine SOOP visits |  |  |  |
| SOOP recruitment visits |  |  |  |
| SOOP de-recruitment visits |  |  |  |
| SOOP courtesy visits |  |  |  |
| Total visits to SOOP |  |  |  |
| Visits in support of DBCP (drifting buoys) | 14 |  | (Number of ship voyages used from European harbours) |
| Visits in support of Argo (profiling floats) |  |  |  |
| Total visits to other programs |  |  |  |
| Total visits by national PMOs |  | Sum of all ship visits (VOS + ASAP + SOOP) + visits to other program (DBCP + Argo) |

| g. | Major challenges and difficulties: |
| --- | --- |
| h. | Research / development / testing: |
| E-Surfmar exhaustively tested the new common AWS (EUCAWS). Series will be purchased in 2016. |
| i. | Other comments |
| Activities described in section f. were carried out by European national PMOs and Technicians as support for E-Surfmar. EUMETNET has no PMO in staff. Drifting buoys involuntarily picked up at sea and continuing to correctly work, are converted into deck drifters before being recovered or re-deployed. |