S.V. Borsch, A.V. Khristoforov, E.A. Leonteva

Guidelines for verification of hydrological forecasts

S.V. Borsch, A.V. Khristoforov, E.A. Leonteva

Guidelines for verification of hydrological forecasts

Guidelines for verification of hydrologic deterministic and probabilistic

forecasts developed as an addition for MOFFS of WMO using latest advances in statistical analysis of hydrometeorological information. They allow evaluating the applicability of forecasting methods, choosing of optimal forecasting algorithms, and determination of the direction for their further improvement.

The objective is to improve effectiveness and quality of water management activities planning and operational decision making in water-related hazard management and water resources management.

For specialists in hydrology, hydrological and meteorological forecasting, water management, and environmental monitoring.

Contents

Introduction.....................................................................................................................................4

Chapter 1. Stating the problem of hydrologic forecast verification...............................................5

1.1  General considerations.............................................................................................................5

1.2 Determination of hydrologic forecast error.............................................................................8

1.3 Cost effectiveness of hydrologic forecast...............................................................................10

Chapter 2. Estimation of deterministic forecast error ..................................................................13

2.1 General principles of forecast error estimation........................................................................13

2.2 Forecast error estimation methods...........................................................................................16

2.3 Long-range hydrological forecast verification example..........................................................20

2.4 Short-range hydrological forecast verification example..........................................................23

Chapter 3. Comparison of forecasting methods and their

applicability assessment...…..………….......................................................................................26

3.1 Comparison of hydrologic forecasting methods.....................................................................26

3.2 Hydrologic forecasting methods comparison examples…….................................................31

3.3 Forecast applicability assessment...........................................................................................36

3.4 Forecast applicability assessment examples...........................................................................39

Chapter 4. Estimation of admissible forecast error probability....................................................43

4.1 Admissible forecast error probability estimation rules..........................................................43

4.2 Admissible forecast error probability estimation examples...................................................48

Chapter 5. Probabilistic hydrological forecast............................................................................51

5.1 Probabilistic forecasting methods..........................................................................................51

5.2 Probabilistic forecast verification...........................................................................................56

Chapter 6. Probabilistic forecast examples...................................................................................63

6.1 Long-range probabilistic forecast example.............................................................................63

6.2 Short-range probabilistic forecast example............................................................................66

References.....................................................................................................................................71

Introduction

Hydrologic forecasting service primary mission is to provide reliable and timely forecasts for economy and population to ensure environmental safety and effective and safe water management operations. Effectiveness of hydrologic forecasts based water management planning and that of operational decision making in water-related hazard management and water resources management depend largely on the quality of those forecasts. The quality of hydrologic forecasts is defined in turn by their accuracy and lead time. Therefore, the development of modern objective methods for evaluating the quality of operational river flow forecasting methods is of great scientific and practical importance.

The proposed Recommendations are in line with WMO Management overview of flood forecasting systems (MOFFS) [28, 32, 37]. They can be applied to other hydrologic forecasts. To estimate deterministic and probabilistic hydrologic forecast error and to assess the forecast applicability, the system of statistical methods is recommended. The use of those methods allows for obtaining objective quality assessment of hydrologic forecasting algorithms. Using these methods allows for selecting optimal algorithm and developing scheme enhancement strategies taking into account the specific features of forecasting algorithm, as well as the amount of hydrologic and meteorological data, their contents and quality investigated during forecasting method development, testing and operational use.

The analysis of general problems related to hydrologic forecasts quality assessment is presented in Chapter 1. Recommendations for deterministic forecasting methods verification are presented in chapters 2, 3, and 4. Recommendations for probabilistic forecasting methods development and verification are presented in chapters 5 and 6.

Chapter 1.  Stating the problem of hydrological forecast verification

1.1 General considerations

The purpose of hydrologic forecasting is to predict the expected future water regime characteristics for rivers, channels, lakes, reservoirs, and other water bodies. Hydrologic forecasts are used for water resources management and water-related hazard management planning and operational activities [17].

River flow, river stage, flow velocity, flow depth, and runoff volume are water regime characteristics of rivers and channels at given points, as well as of reservoir inflow. Water stage and volume are water regime characteristics of lakes and reservoirs.

Their means, maximums, and minimums, as well as their changes over time, are forecasted for one day, a ten-day period, a month, a quarter, a season, a separate flood, a flood wave, ice season, or navigation season.

Mean, maximal and minimal ice thickness, dates of ice phenomena beginning, freezing, opening and breakup dates, and autumn and spring ice run dates are predicted ice regime characteristics of rivers, channels, lakes, and reservoirs [12, 13, 14, 17].

Hydrologic forecasts are issued once a day, a ten-day period, a month, a quarter, a season, a year. Deterministic forecast provides a future value  of an element of regime of the water body expected on date . Probabilistic forecast provides different characteristics of conditional probability distribution of value  depending on hydrometeorological information available on the date of forecast issue. The forecast lead time is the difference   between the date   and the date of forecast issue . The required forecast lead time is defined by the time period necessary for taking action on water resources management and water-related hazard management. The lead time possible to achieve depends on the evolution rate of forecast processes for certain water body and its catchment, as well as on meteorological forecast quality and hydrologic forecast service technical resources.

According to WMO classification, short-range forecasts are those with lead time of up to 2-3 days; medium-range forecasts, with that of 3-4 to 9-10 days; long-range forecasts, with lead time over 9-10 days. In a number of countries, short-range hydrologic forecasts are those with lead time up to 5-6 days; medium-range, with that of 6-7 to 12-15 days; long-range forecasts, with lead time over 12-15 days [1, 17, 18, 27].

The definition of forecast lead time categories is rather subjective. For instance, the forecast of the same element of the water regime may be classified as short-range forecast for a minor mountain river and as medium- and even long-range forecast, for a major plain river. The lead time of forecast of characteristic dates of hydrologic regime is defined by the forecast [5].

Forecast development relies on the information about river, lake, reservoir, etc. and its catchment.

Antecedent changes in hydrologic and meteorological parameters, as well as predicted weather changes over the hydrological forecast lead time period, are taken into account when producing a hydrologic forecast.

The forecast is based on a general method, a general approach to solving a problem, based on physical essence of processes which determine a predicted event or a predicted element of hydrologic regime. Depending on the specific features of the forecast, those methods reflect the regularities of catchment flow formation, of water motion within the river network, of heat exchange of water mass and ice cover with atmosphere and river bed or reservoir bed [13, 14, 15, 17].

Various forecasting models are designed basing on those methods: physically based distributed models, conceptual lumped or semi-distributed models, statistical relationships between the predicted element and the known hydrometeorological parameters on the date of forecast issue [1, 10, 26, 28, 30].

Hydrologic element forecasting method (algorithm) is based on one of the above mentioned general methods listed above. It represents specific features of a water body and of its hydrologic regime, as well as the amount and quality of hydrometeorological information used for algorithm development and available when operating that algorithm, including weather changes over the hydrological forecast lead time period and their assimilation techniques [5, 18].

Forecast updating is possible for some long- or medium-term forecasts. For example, snowmelt flood forecast is updated after most seasonal snow cover has melted. Additional new data, not available by the moment of issuing the forecast, are used for forecast updating [1, 27, 41]. Thus, the scheme of forecast updating should be considered as a stand-alone forecast method [5].

For a given lead time and given catchment, the quality of stream flow characteristics forecasting method is defined by its error. According to the International Institute of Forecasters research results, forecast accuracy is a principal quality index for 90 % of forecast users [44].

The factors contributing to forecast error have been well studied by now. The forecast scheme error sources are defined by the following factors:

– forecast lead time;

-  specific features of event formation and its spatial and temporal variability;

– adequate and full description of predicted event;

– predictor representativeness and effect of factors not taken into account;

– initial data representativeness, amount and accuracy;

– parameter estimation accuracy;

– the role of meteorological elements and the accuracy of their forecasting [5, 7, 16, 32, 38].

In many cases, input weather forecasts are the primary source of errors of hydrological forecasts [16, 34]. To identify hydrological and weather forecast errors when evaluating river flow forecast errors, it is proposed in some cases to use observed meteorological data for the period of lead time of certain hydrological forecast [5, 18, 13, 14].

Hydrologic regime elements forecasting method are based on hydrometeorological information about variability factors of these elements available on the date of forecast issue. An alternative forecast is based on long-term data statistical analysis of predicted element only. Climatology forecasting method (“climatology”) using mean long-term value of predicted element could be considered such unconditional alternative for long-range hydrological forecasts as well as for some medium-range forecasts. Inertial, or persistence forecast (“persistence”) using the known value of forecast element for the date of forecast issue could be considered an unconditional alternative for short-range and some medium-range hydrological forecasts. The practical use of a hydrological forecast method is reasonable if its accuracy is higher than that of alternative forecast [5, 18].

Forecast verification implies statistical analysis of the relation between actual values of hydrologic regime elements and their forecast values using this scheme. Verification procedures are the final necessary step to complete the process of forecast scheme development and implementation. Hydrological forecast error determination and analysis are an essential step in the process of scheme development and operation. First of all, for a given forecast lead time, forecast error is the key index of practical value of that forecast. Moreover, forecast error analysis allows for determining scheme weaknesses and outlining strategies for scheme enhancement. Analysis results for a set of forecast of different elements of hydrologic regime within a whole region may determine and prove the strategies for improving the hydrometeorological observation network and hydrometeorological data acquisition and processing system [5, 16, 27, 28, 32, 37].

1.2 Determination of hydrologic forecast error

Determination of hydrological forecast error is based on the assumption that the relationship between an observed value of some hydrological variable and its predicted value  has not changed since scheme development to its operational implementation. Thus, deterministic forecast scheme error is determined as mathematical expectation of a particular forecast error measure, which is the probability-weighted average of all possible values of and . In case of issuing forecasts throughout the year, it is reasonable to determine the forecast methodology error for particular seasons or months.

Actual values of hydrological variables have measurement or computation errors. Their possible values of magnitude are presented in [16]. In case of measuring discharge in floodplain-vegetated wide rivers or in mountain rivers with actively changing channels and therefore changing rating curves, there might be considerable measurement (computation) errors. The error of determining the actual value of a predictand is the lower limit of possible forecast error value. If a forecasting scheme error is close to that determination error, further methodology improvement is unreasonable [5].

Considering the world hydrological forecasting practice, mean squared forecast error is the most popular forecasting scheme error index, which is natural and simple in terms of mathematical sense:

=.                                                                                                         (1.1)

If a power value greater than 2 is used, the only one large forecast error might determine the total forecast error.

Forecasting model parameters are estimated using the easiest and most widespread least squares method.

Using some other measure of forecasting scheme error appears to be very difficult in terms of mathematical computations.

Using mean absolute forecast error is considered in a number of papers. In this case, parameter estimation is largely hampered, though using modern computational resources might solve this problem [1, 26, 28, 32, 37, 40, 41].

In case of low values of a hydrological predictand, e.g., low flow forecasting, mean squared relative forecast error can be used as the measure of forecasting scheme error. However, it is important to recognize the possible large values of that measure in case of extremely low predictand values even using a good forecasting scheme.

In case of large values of a hydrological predictand, e.g. flood peak flow forecasting, the mathematical expectation of  can be used as the measure of forecasting scheme error. However, using such an approach, forecast errors are virtually not taken into account in case of low predictand values.

Using mean squared forecast error of logarithmized hydrological variable is recommended in a number of papers, providing more arguments for using normal probability distribution for describing forecast error variability [19, 26, 28, 32, 37, 40, 41]. However, the reasons for using logarithimizing or another normalizing transformation for model parameters estimation must be proved each time, as it does not ensure an optimal statistical solution for a hydrological predictand itself. Simplification of forecasters’ task should be in agreement with the needs of hydrological forecast users, who do not need forecasts of logarithmized hydrological characteristics [5].

When choosing the best index of some forecasting scheme error, the needs of forecast users must be taken into account as well. Depending on particular water-management conditions, there might be different measures of forecasting scheme error due to different end-users of the same hydrological forecast [3, 5, 27, 33]. In light of the above, consider two reservoir inflow forecasting examples.

Example 1.

In case of extreme flood peak warning, water release rate to tail water must be rapidly increased [3]. If the flood peak is overforecasted, such activities are unwarranted and may result in increasing water deficit risk in the following low-flow period. However, the effect of largely underforecasting the flood peak may be considerably more dramatic and even catastrophic. In both cases, the cost of inaccurate forecast also depends upon the reservoir state. At high storage level, the negative effects of underforecasting would be greater than those at low level [3, 5]. Therefore, forecast error index should be increasing with rising storage level; in case of underforecasting reservoir inflow, that error index value should be large.

Example 2.

In case of warning of stream flow dramatically dropping to low values during low-flow period, urgent reduction in water release rate to tailwater is needed [3]. In case of underforecasting, such activities result in unwarranted hydropower plant productivity reduction, as well as in reduced possibilities for water use in the tailwater.  However, overforecasting may lead to even more severe economical and environmental damage. In both cases, the cost of inaccurate forecast also depends upon the reservoir state. At high storage level, greater negative effects are related to overforecasting, whereas at low level, to underforecasting [3, 5]. Therefore, forecast error index should be increasing with falling storage level; in case of overforecasting reservoir inflow, that error index value should be large.

As there can be several users of the same hydrological forecast and therefore, several measures of forecast error, a weighted average of individual ‘user’ measures can be used when developing and operating that forecasting scheme. In this case, the weights are proportional either to the scale of those users’ water management activities, or to the fees charged for forecasts [5].

The measure of deterministic hydrological forecast error considered in these Recommendations (see equation (1.1)) is the most widely used, the easiest and the most versatile.

Usually, the units of measure of a hydrological predictand and forecast error measure are the same. Thus, the accuracy of forecasting scheme is characterized by square root  instead of .

Cost-effectiveness analysis of hydrologic forecasts provides additional argumentation in support of the forecast error measure under consideration.

1.3 Cost effectiveness of hydrologic forecast

Cost-benefit analysis of using hydrological forecasts in water management allows for determining affordable costs for development and implementation of different forecast schemes and development of hydrometeorological monitoring system. At the same time, concerning particular water management activities, taking into account specific features of a forecasting scheme becomes possible of methodology development and implementation, from parameter estimation, validation, verification and applicability assessment to choosing an optimal operational forecasting scheme [5, 17, 33].

In general, the task of cost-effective and environmentally-friendly use of water resources comes to the search of an optimal set of water management decision parameters  ensuring maximum possible mean (or guaranteed) economic effect of water management activities  over the design period under conditions of environmental safety. Water use fees, costs of water protection activities, and possible losses due to hydrological hazards are taken into account when defining that optimal parameter set.

Consider a situation when economic effect of using water resources of a river, reservoir, etc. depends upon a variable  characterizing its water regime and is therefore expressed as a function . If  were known when making a water management decision defined by vector , that function would be defined precisely. Within the frameworks of environmental safety requirements, precise optimal  would be found such that  reaches its maximum. Replacing actual value  with its forecast , an approximate optimal decision  such that  reaches its maximum can be found. Due to forecast errors, the functions  and  might not be the same for different values of . Therefore, approximate decision  may differ from true optimal . When making -based decision , the difference between possible maximum value of economic effect  and its actual value  is the lost profit :

= –.							(1.2)

When optimizing the costs of water protection activities or losses related to hydrological hazards, definition of optimal parameters comes to finding the maximum of inverse cost (or loss) function. In such case,  is the measure of additional expenses or additional losses due to forecast error.

This is demonstrated in Figure 1.1.

Figure 1.1. Definition of lost profit

In each individual case, lost profit  is defined by forecast error and contribution of hydrological variable  to function  [33]. In case of no systematic forecast error, the difference – might be considered a random value with zero mean and variance  defined by equation (1.1). Mathematical expectation of – for all possible  and  is the value of mean lost profit  approximately defined by the following equation:

= ,										(1.3)

where  is a measure of mean economical loss due to inaccurate hydrological forecasts, defined by second partial derivatives of function  of variable  and components of water management decision vector  [5].

Equation (1.3) shows that mean lost profit is proportional to  defined by equation (1.1) as mean squared forecast error, which is the most widely used measure when defining economical loss due to inaccurate hydrological forecasts as mean lost profit.

In case of a more accurate forecasting scheme (< ), reduction in lost profit, additional expenses or additional losses is defined by the value , which is the upper limit of cost-effective expenses for developing and operating a more accurate forecasting scheme.

In a number of cases, using a less accurate though less expensive forecasting method may appear cost - effective. Denote the error of a less accurate alternative forecast (“climatology” or persistence) by . Using less accurate alternative forecasts may result in increasing lost profit, additional expenses or additional losses. That increase is defined by the value , which needs to be compared with the cost of forecasting scheme development, informational support and operation. If that cost is greater than lost profit reduction, using that scheme is unreasonable in terms of cost effectiveness [5, 17, 33].

Chapter 2.  Estimation of deterministic forecast error

2.1 General principles of forecast error estimation

Hydrological forecast error  is defined by formula (1.1) as mean squared difference between its actual value  and value  predicted using considered scheme. Before presenting the measure  estimation methods, considering forecast error estimation using dependent sample would be useful.

Consider a hydrological forecasting method based on -year joint hydro- and meteorological observation data. If average number of annually issued forecasts is , the number  of hydrological observations of predicted value taken into account when developing that method is , as well as that of hydrometeorological observations of its predictors. Those observations are used for generating the series of  forecasts. As a result, a test forecast error series ,…, is generated. Forecasting method error is characterized by the following index:

= ,							        (2.1)

where  is the number of forecasting model or formula parameters estimated using the same data of  hydrometeorological observations. In case of using graphs representing the relationship between predictors and predictand,  is defined using the following rule: = 2 for a linear relationship between one predictor and predictand; = 3 for a parabolic, exponential or logarithmic relationship, etc. [1, 15, 18, 26, 32].

Very important aspect of considered problem is that the test forecast error series used for producing the estimate  was generated based on the data used for developing the evaluated forecasting method. Choosing predictors, developing the forecasting formula, estimating its parameters or plotting relationship graphs was performed in such a way that the discrepancy between observed and predicted values  and  of some river runoff characteristic for

= 1, ...,  was minimal.

Due to the fact that dependent sample–based estimate  is characteristic of only residual variance  of the relationship between predictors and predictand , the true value of forecast error is therefore considerably underestimated. There is a relationship between that residual variance  and the variance  of predicted hydrological variable:

=								(2.2)

where  is a correlation ratio characterizing the predictors–predictand relationship strength, the coefficient of correlation between observed and predicted values  and . In case of using a linear regression equation for forecasting,  is equal to multiple regression coefficient [5].

Forecast error is defined by forecasting method robustness against the used observation data as well. Ceteris paribus, the larger the number of predictors and parameters (or the more flexible the set of relationship graphs), the lower the robustness of that predictors–predictand relationship and the larger the difference between residual variance  and forecast error  [17, 19, 23, 31, 38].

To recognize the discrepancy between  and , consider a case when stochastic relationship between predictors (components of vector ) and predictand  is described by a linear regression model for each date of forecast issue over the observation period and over projected period of operational use:

= + … +  + ,                                                                            (2.3)

Where ,…,  are the given functions in the forecasting formula, defined by the used forecasting model [5, 23].

As a rule, predictors–predictand relationships have an absolute term ensuring the absence of systematic forecast errors. In such cases, one of the above functions, for instance,, is identically equal to 1. Increasing number of vector  components known on the date of forecast issue allows for more comprehensive and adequate description of predicted hydrological event. The number  of statistically estimated model parameters ,…,  is increasing as well. Ambiguity of – relationship is characterized by a random value . Suppose that  is independent of predictors  and has normal probability distribution with zero mean, the latter allowing for producing a forecast free of systematic error. The variance of  is equal to residual variance characterizing the ambiguity of – relationship. In this case, correlation ratio  (see formula (2.2)) is equal to the coefficient of multiple correlation between  and ,…, . Moreover, independence of  belonging to different dates of forecast issue is supposed.

Model parameters are estimated using the least squares method basing on  joint hydro- and meteorological observation series. For each date of forecast issue, parameter estimates ,…,  define the forecast  of a runoff characteristic as follows:

= + … + .				                                   (2.4)

where  is -date predictors vector.

The relationship between residual variance  and forecast error  is described by the following equation:

= .			                                 (2.5)

The formula (2.5) given in [23] shows that forecast error is rapidly increasing with increasing number  of parameters, as residual variance  is not that rapidly decreasing due to more comprehensive and adequate description of predicted event. The above results in a well-known fact, that in case of verification using independent sample, simple but robust forecasting methods quite often appear to be more accurate than those using comprehensive and adequate models with many parameters to be estimated [5, 17, 23, 28, 37, 41].

When searching for optimal forecasting method, using the estimate  may lead to drawing wrong conclusions. Increasing number  of parameters allows not only for more adequate representation of actual – relationship but also for taking more predictors into account. As a result, dependent sample–based standard forecast error estimate  is always smoothly decreasing with increasing , whereas forecast error  is increasing after reaching its minimum for an optimal value of  (see Figure 2.1) [5, 17].

Figure 2.1. Schematic relationship plots of dependent sample–based forecast error  and the number  of estimated parameters (lower curve) and of actual forecast error  and  (upper curve) [17]

When estimating the error of forecasting scheme, possible statistical relationship between forecast errors of different issue dates (first of all, of adjacent dates) must be taken into account. Such a relationship may occur due to autocorrelation between predictand and its predictors including those not taken into account by the forecasting model. In case of short-range flow forecasting of major rivers, especially over low-flow period, there may be especially strong 1-day lagged forecast error autocorrelation [5, 24].

In accordance with hydrological forecasting traditions, in order to avoid over-complication of further analysis, it is reasonable to suppose that test forecast error autocorrelation is described by simple first-order autoregression model with one parameter, 1-day lagged forecast error correlation coefficient  [22, 24, 35, 39].

For a linear regression model (2.3), the measure  is systematically underestimating residual variance; its average value is equal to:

= ..					(2.6)

Standard statistical estimate of coefficient  is defined by the formula:

= .							(2.7)

Anderson test is recommended for evaluating statistical significance of estimate  [22, 24]. According to that test, a hypothesis of no test forecast error correlation may be accepted, if the following inequality is true:

< ,						(2.8)

where  is the normal probability distribution quintile for significance level . In particular,  = 1.96 for =5%. If condition (2.8) is not satisfied, there is significant test forecast error autocorrelation. Otherwise,  = 0.

2.2 Forecast error estimation methods

Depending on the volume and composition of available observation data used for developing and testing a forecast, one of the following methods is recommended for estimating deterministic hydrological forecast error [5].

Method 1.

If  forecasts of a hydrological variable  were issued using developed and implemented hydrological forecasting scheme, a series of forecast errors ,...,  is generated, representing the results of testing using independent sample. Forecast error estimate computed from that series is defined by the formula:

= .								(2.9)

The estimate  is unbiased, i.e., is free of systematic error. For quite large number  of independent test forecasts,  is close to actual forecast error  [1, 15, 19, 26, 27, 32].

For proper use of estimates  or , their statistical error of determination must be computed. For  and , their root mean squared errors (square root of variance) are approximately calculated using the formulas:

= ,								(2.10)

= .							(2.11)

The formulas (2.10) and (2.11) are in accordance with the above-considered linear regression model (2.3) where daily random fluctuations of  are stationary first-order autoregressive Gaussian random process [5, 22, 24]. Forecast error autocorrelation coefficient estimate  is defined by formula (2.7), replacing  with  and summation index , with .

As more observation data is available, a hydrological forecast may be corrected (updated) by re-estimating model parameters or refining the relationship graphs, which results in changing that forecasting method, in fact, in developing a new one which has to be tested separately.

Method 2.

In case of quite long -year hydro- and meteorological observation data series, a “leave-p-out” cross-validation method can be used [5, 9, 19, 27, 29, 32, 38]: ‘truncated’ -year random sample of original -year data is used as training set for developing a forecasting method and the remaining  observations are used as an independent validation set. On average,  forecasts are issued during each of  years; forecast error series length  is therefore equal to . That test data subset should be used for estimating the forecast error using a formula similar to (2.9).

Test dataset–based forecasting scheme remains the same, though its parameters or graphs may change. Thus, it is reasonable to change the indications and to denote such forecast by  for = 1,...,.

Using less observation data leads to lower accuracy of model parameters estimation. As a result, ‘truncated’ forecast error is somewhat larger than actual forecast error  derived from full data set of  observations. A correction coefficient resulting from formula (2.5) may be used to eliminate that fault [5]. If  parameters of forecasting scheme are to be estimated, the forecast error estimate computed from all  observations should be defined by the following formula:

= .					(2.12)

Root mean squared errors of estimates  and  are approximately calculated using the formulas (2.10) and (2.11).

Accuracy of that method may be considerably improved using the following approach: the above procedure should be repeated  times in such a way that the resulting test set consists of non-duplicate data for each of all available  years. That number  of iterations should satisfy the condition that the sum of all test sample lengths  + …+  is equal to total number  of observations. To ensure satisfying that condition, the numbers ,...,  may differ at each iteration.

Resulting forecast error estimate is computed from the series of forecast error estimates , …,  for  iterations:

= .									(2.13)

Root mean squared errors of estimates  and  are approximately calculated using the formulas (2.15) and (2.16) given below.

Method 3.

Consider a less favorable situation when original hydro- and meteorological observation data sample is quite short, not allowing for obtaining a validation set long enough, whereas no operational verification has been performed yet or there is still not enough data available for error estimation using the above method 1. In this case, a “leave-one-out” method, based on J.W. Tukey’s “jack-knife” method, is optimal [5, 23]. In case of small , this is an optimal modification of method 2 [5, 11, 23, 29, 36, 37].

Leaving out the -th year from -year observation period, the remaining –1 observations are used for developing an -th variant of forecasting method modification with new relationship parameters or graphs. Denote the number of forecasts issued during the -th year by . The series of forecast errors –  for = 1,...,  can be used as independent validation sample, as the values , as well as their predictors, were not taken into account when developing the -th variant of method.

For  = 1, …, , the described procedure is repeated for each -th year, each time returning the year left out on previous step to the training sample. Thus, method 3 is a modification of the above cross-validation method 2 in case of  = –1,  = 1, and  = . As a result, for = 1,...,  and  = 1, …, , a series of test forecast errors –  is generated, characterizing the forecast error derived from (–1)-year observation data, whereas the verified scheme is based on -year observation data. However, this may be considered negligible, as the correction coefficient following from formula (2.5) is close to 1. The “leave-one-out”-estimated forecast error is defined by the formula:

= .								(2.14)

In respect of theoretical results presented in [23], approximate root mean squared errors of estimates  and  are defined by the following formulas:

= ,					(2.15)

= .				(2.16)

Method 4.

The presented verification method is the easiest, allowing for validating the forecast using a dependent sample (the same data used for scheme development). This method is based on a hypothesis that stochastic relationship between predictors and predictand is described by a linear regression model (2.3) and daily random fluctuations of  are stationary first-order autoregressive Gaussian random process [5]. However, it is possible to use this method under less strict conditions: there must be a relationship between predicted runoff characteristic and its predictors expressed as (2.4) and its  parameters are estimated using least squares method. Using the estimates  and  defined by formulas (2.1) and (2.7), respectively, forecast error can be estimated as follows:

= .						(2.17)

In respect of theoretical results presented in [5, 23], approximate root mean squared errors of estimates  and  are defined by the following formulas:

= ,							(2.18)

= .						(2.19)

The following guidelines are recommended for deterministic hydrological forecast verification:

1. If there are enough operational forecasts issued to form an independent validation data set, it is reasonable to use method 1. Otherwise, one of the remaining three methods should be used.

2. If there is enough joint hydro- and meteorological data available for developing and validating a forecasting scheme, it is reasonable to use method 2.

3. Otherwise, it is reasonable to use method 3.

4. For any data volume available, it is reasonable to use method 4, if the forecasting equation is linear in its parameters.

5. We recommend that several verification methods be used if possible and analysis of results be performed.

2.3 Long-range hydrological forecast verification example

Consider using the above methods for long-range spring reservoir inflow forecast verification (case study of Sayano–Shushenskoe reservoir) [5]. Forecasts of mean April reservoir inflow volume = are issued on 26th March every year. Forecast lead time is 35 days. The following predictors  are used: predicted value of mean reservoir inflow for the last 10-day period of March  = and April 1–10 mean air temperature forecast at Kyzyl weather station.

Long-term observation data over the period from 1979 to 2003 were used for that forecasting scheme development. Series length  is equal to 25. Predictors–predictand relationship is described by a linear regression model. Its three parameters, an absolute term and the two coefficients, were estimated using the least squares method. The strength of relationship is characterized by multiple correlation coefficient  = 0.76. Annual values of actual April reservoir inflow , predicted inflow  and forecast error  are given in table 2.1 [5].

Table 2.1

Initial data for long-range forecasting of mean April inflow volume into Sayano–Shushenskoe reservoir and for forecast verification

| Year | , | , | , |
| --- | --- | --- | --- |
| 1979 | 400 | 426 | -26 |
| 1980 | 410 | 306 | 104 |
| 1981 | 886 | 791 | 95 |
| 1982 | 1003 | 670 | 333 |
| 1983 | 394 | 502 | -108 |
| 1984 | 420 | 395 | 25 |
| 1985 | 561 | 565 | -4 |
| 1986 | 533 | 595 | -62 |
| 1987 | 610 | 649 | -39 |
| 1988 | 705 | 549 | 156 |
| 1989 | 660 | 776 | -116 |
| 1990 | 460 | 514 | -54 |
| 1991 | 520 | 594 | -74 |
| 1992 | 630 | 694 | -64 |
| 1993 | 800 | 898 | -98 |
| 1994 | 698 | 738 | -40 |
| 1995 | 835 | 894 | -59 |
| 1996 | 490 | 396 | 94 |
| 1997 | 1360 | 938 | 422 |
| 1998 | 583 | 723 | -140 |
| 1999 | 611 | 666 | -55 |
| 2000 | 740 | 773 | -33 |
| 2001 | 900 | 808 | 92 |
| 2002 | 587 | 817 | -230 |
| 2003 | 504 | 642 | -138 |

Methods presented in section 2.2 are used for verification of considered long-range hydrological forecast.

Example of using method 1.

Observation data over the following 2004-2009 years ( = 6 years) allow for estimating mean squared forecast error using formula (2.9):  = 19598 ()2. Root mean squared forecast error estimate is  = 140 .

Testing the validation forecast error series for autocorrelation showed the following. Defined by formula (2.7), autocorrelation coefficient estimate  is equal to -0.12; therefore, the inequality (2.8) is true and there is no significant autocorrelation forecast errors, according to Anderson test, assuming  = 0, which allows for using formulas (2.10) and (2.11).

According to those formulas, root mean squared errors  and  of estimates  and  are equal to 11308 ()2 and 140 . Thus, in case of only 6-year independent validation forecast set, relative errors of estimating  and  using method 1 are 58% and 29%, respectively.

Example of using method 2.

Observation data over  =  = 20 years were used for estimating forecasting formula parameters, whereas the remaining = = 5 year observations were used as independent test set for estimating forecast error () using formula (2.12) for  = 3. The number of routine iterations of consequently excluding every 5-year sample from original 25-year observation data was  = 5.

Final estimate of mean squared forecast error , defined by formula (2.13), is equal to 24124 (c)2. Root mean squared forecast error estimate is  = 155 .

According to formulas (2.15) and (2.16), assuming  = 0, root mean squared errors of those estimates are  = 6823 ()2 and  = 22 , respectively. Therefore, using method 2 allows for more accurate forecast error estimation: relative errors of estimating  and  are 28% and 14%, respectively.

Example of using method 3.

Leaving out every - th year of 25-year observation period and returning the year excluded on previous step to training sample, forecasting formula parameters were estimated from the remaining –1 = 24 years using least squares method and forecast error was computed as - , generating a forecast error series –, …, –.

A “leave-one-out” estimated mean squared forecast error , defined by formula (2.14), is equal to 26922 ()2; root mean squared forecast error estimate is  = 164 .

According to formulas (2.15) and (2.16), assuming  = 0, root mean squared errors of those estimates are  = 8458 ()2 and  = 26 , respectively. Therefore, relative errors of estimating  and  using method 3 are 34% and 16%, respectively.

Example of using method 4.

As the conditions for using method 4 are satisfied, the formulas (2.1) and (2.17), assuming  = 0, were used for estimating residual variance of predictors–predictand relationship  = 22960 (cubic meters per second)2 and mean squared forecast error  = 26240 ()2, respectively. Root mean squared forecast error estimate is  = 162 .

According to formulas (2.18) and (2.19), root mean squared errors of those estimates are  = 8098 ()2 and  = 25 . Thus, relative error of estimating  and  using method 4 is 31% and 15%, respectively.

According to the above, a conclusion can be drawn that in case of long-range forecasting of April inflow into Sayano–Shushenskoe reservoir, identical forecast error estimates are derived using different verification methods [5].

2.4 Short-range hydrological forecast verification example

Consider using the above methods for short-range daily hydrologic forecast verification (case study of the Sochi River at Sochi, forecast lead time is 1 day). Conceptual snowmelt- and rainfall–runoff model was developed for forecasting. To feed that model, daily hydrometric and weather data observed at Sochi stream gauge and Sochi weather station are used, as well as weighted mean temperature and precipitation 1-day ahead forecasts derived from four available operational meteorological model outputs (COSMO-Ru 7, NCEP, REGION, and UKMO). For each month, using least squares method, 13 parameters of hydrological forecasting model were estimated from 18-year hydrometeorological observation data series over the period from 1984 to 2005 (accounting for observation gaps). Forecasts are issued once a day on daily basis; annual number of issued forecasts is therefore equal to 365-366. In respect of the number of days in a month, total monthly number of daily observations varies from 508 to 558. Mean long-term total annual number of daily observations is 6506 [6].

As the above forecasting scheme has been operationally implemented fairly recently, there is still not enough data available for using verification method 1 (see section 2.2). Therefore, methods 2, 3 and 4 were used for estimating forecast error.

Example of using method 2.

Randomly choosing  = 5 years 1984, 1990, 1998, 2000, and 2004 as ‘independent data’, initial 18-year observation data were cut to a 5-year validation set and 13-year training set. For each month, model parameters were estimated using that training sample and 5-year forecast error series was derived from test sample.

Figure 2.2 shows daily actual vs. predicted flow (discharge) plots, which coincide fairly closely.

Figure 2.2. Daily discharge of the Sochi River at Sochi in the year 1984: actual (blue solid line) vs. forecast (red dashed line)

For each month, forecast error was estimated using equation (2.12), where  = 141 - 155. For each month and the whole year, the estimates  are given in table 2.2, as well as the estimates of forecast error autocorrelation coefficient  defined by equation (2.7) from all available observation data. For 5% significance level, those estimates are statistically significant, if  > 0.12, according to Anderson test.

In respect of the equation (2.11), relative root mean squared error of estimating  is approximately equal to 6.4% for each month.

Example of using method 3

For =1,…,  ( = 18), consequently leaving out every -th year, forecasting model parameters were estimated from remaining –1 = 17 years. The data of that -th year were used for generating an independent set of forecast errors. For each month and the whole year, forecast error was estimated using equation (2.14). Estimates  are presented in table 2.2. According to (2.16), relative root mean squared error of estimating  is approximately equal to 3.5% for each month.

Example of using method 4.

As the conditions for using method 4 are satisfied, equations (2.1) and (2.17) were used for estimating forecast error for each month and for the whole year (see table 2.2, ). According to (2.19), relative root mean squared error of estimating  is approximately equal to 3.2% for each month.

Table 2.2

Daily stream flow forecast error estimates, cubic meters per second (case study of the Sochi River at Sochi)

|  | I | II | III | IV | V | VI | VII | VIII | IX | X | XI | XII | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0.02 | -0.02 | -0.01 | 0.01 | 0.13 | 0.15 | 0.14 | 0.08 | 0.10 | 0.01 | 0.05 | 0.10 | 0.06 |
|  | 12.3 | 10.2 | 10.4 | 9.6 | 16.3 | 11.9 | 10.2 | 12.5 | 9.6 | 16.4 | 15.7 | 17.1 | 12.7 |
|  | 11.4 | 8.2 | 11.1 | 8.8 | 17.2 | 12.5 | 9.7 | 10.4 | 9.8 | 14.5 | 16.1 | 15.7 | 12.1 |
|  | 10.4 | 8.5 | 10.7 | 8.6 | 14.8 | 12.1 | 9.2 | 11.2 | 8.8 | 15.3 | 14.5 | 16.2 | 12.0 |

As table 2.2 shows, for each month, identical forecast error estimates are derived using different verification methods. The features of hydrological regime, in particular, intramonthly flow variability, are well represented by monthly error distribution [5, 6].

According to the above examples, identical quite accurate short-range hydrological forecast error estimates can be derived using presented verification methods. As expected, method 2 appeared to be less accurate than methods 3 and 4, as the procedure of generating the training and validation samples was performed only once.

Chapter 3.  Comparison of methods and their applicability assessment

3.1 Comparison of hydrologic forecasting methods

In case when different methods may be used for forecasting the same hydrologic characteristic with the same lead time, there is a need to choose the most accurate methods. If an advanced modification of some previously used method is presented, its advantage must be substantiated. In all such cases, statistically significant difference between the estimated errors of hydrologic forecast methods must be determined [15, 27, 29, 40, 41, 42].

Consider using two concurrent methods for forecasting the same characteristic  with the same lead time. The differences may be related with forecast models, meteorological data assimilation schemes, the set of predictors taken into account, the set of parameters, parameter estimation methods, or forecast relation graphs. Denote the forecasts of characteristic  constructed using schemes “1” and “2” by  and , respectively, and mean squared forecast errors defined by formula (1.1), i. e., true error values of compared methodologies, by  and , respectively. The methods presented in section 2.2 must be used for computing the estimates  and  based on test forecast series using dependent or independent samples , series lengths are  and , respectively. There may be some number  of test forecasts issued on the same time using compared schemes.

Considering  test forecast series common for both schemes “1” and “2”, denote the forecasts of value  for i -th forecast time by  and . There may be strong correlation between forecast errors – and – due to the common observed value  and to the same (or strongly correlated) predictors. The factors not taken into account, for instance, weather conditions over hydrological forecast lead time period [5], contribute considerably to forecast error correlation.

Standard estimate of forecast error – and – correlation coefficient for  = 1,…, is defined by formula:

=.						(3.1)

According to Pitman test, there is statistically significant difference between estimated correlation coefficient and zero, if the following inequality is satisfied:

,						(3.2)

where  is the quintile of Student’s probability distribution with  degrees of freedom corresponding to probability of exceedance . Significance level  defines the probability of admitting of nonzero correlation coefficient, which is actually equal to zero [21, 35, 39]. Critical values of quintile  for different  and  = 5 % [5] are presented in table 3.1.

Table 3.1 Critical quintiles  for Pitman test ( = 5 %)

|  | 10 | 15 | 20 | 30 | 40 | 60 | 100 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 2.23 | 2.13 | 2.09 | 2.04 | 2.02 | 2.00 | 1.98 |

If the inequality (3.2) is not satisfied, the difference between correlation coefficient estimate  and zero may be considered negligibly small and that estimate should be admitted zero for further calculations.

Forecasting experience demonstrates that positive correlation coefficient estimate  is virtually always statistically significant. Error correlation of forecasts using different schemes must be taken into account when comparing the estimates  and , as that correlation results in increase in probability of advantage of one of schemes, i.e., in power increase of statistical tests used for comparing those schemes [5, 23].

Suppose method “1” to be more accurate, i.e., < likely due to the fact that method “1” is actually more accurate than method “2”, i.e., <. However, method “1” may only seem to have an advantage due to statistical error of compared estimates. Submitting or rejecting the advantage of one method over another actually comes to testing a statistical hypothesis that  against .

Depending on the properties of each test forecast error series, we recommend three statistical tests be used for assessing statistical significance of method “1” advantage. When using these tests, the following fact must be taken account: if scheme errors were estimated using dependent sample, the number of estimated parameters ( and  for schemes “1” and “2”, respectively) must be taken into account. Otherwise, if forecasts errors were estimated using independent sample, the values  and  must be replaced with zero for further calculations.

Test 1.

This test (criterion) is most powerful, i.e., the possibility of rejecting a false hypothesis is maximum, if the following conditions are satisfied:

- The relationship between a forecasted characteristic and its predictors matches linear regression model considered in section 2.1 and forecasting methodology “1” is based on formula (2.4).

- Method “2” is a simplified modification of method “1” with less predictors, less summands in (2.4), or using some a priori parameters (for instance, their generalized values) instead of their estimates. Such simplification is equivalent to supposing that last  parameters are equal to zero:  = ... =  = 0.

- For both forecasting methods, parameters and forecast errors are estimated using the same long-term series of forecasted characteristic and its predictors, i.e.,  = = = .

- Forecasting methods errors  and  are estimated using formulas (2.1) and (2.17) of method 4, where the number  of parameters is  and  for scheme “1” and “2”, respectively.

Under such conditions, we recommend the most powerful analysis of variance F-test be used for comparing forecast error estimates  and , taking into account the forecast error autocorrelation [5]. For significance level , the inequality < should be considered statistically significant and scheme “1”, obviously more accurate, if the following condition is satisfied:

=  > ,	      (3.3)

where  is the quintile of F-distribution with  and  degrees of freedom corresponding to probability of exceedance . Significance level  defines the probability of admitting of more accurate scheme “1”, though actually the  hypothesis is true [5, 21, 24, 44]. Critical quintile values  are presented in table 3.2 for different  and  while  = 5 %. In case of large , the last column corresponding to its infinitely large value should be used [6].

Table 3.2

Critical quintiles  for  = 5 %

|  | 15 | 20 | 30 | 40 | 60 | 120 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| = 1 | 4.54 | 4.35 | 4.17 | 4.08 | 4.00 | 3.92 | 3.84 |
| = 2 | 3.68 | 3.49 | 3.31 | 3.23 | 3.15 | 3.07 | 3.00 |
| = 3 | 3.29 | 3.10 | 2.92 | 2.84 | 2.76 | 2.68 | 2.60 |
| = 4 | 3.06 | 2.87 | 2.69 | 2.61 | 2.53 | 2.45 | 2.37 |
| = 5 | 2.90 | 2.71 | 2.53 | 2.45 | 2.37 | 2.29 | 2.21 |
| = 6 | 2.80 | 2.60 | 2.42 | 2.33 | 2.25 | 2.17 | 2.10 |

Test 2.

This test, given in [23], is a modification of asymptotically most powerful Wald likelihood-ratio test [5, 20]. It can be used if the following conditions are satisfied:

1 Test forecasts of the same forecast time are used for testing both forecasting methods, i.e.,  = = = .

2 For each forecasting method, test forecast error series is a random sample of normal probability distribution.

3 Forecast error estimates  and  were computed using methods 1, 2, or 3 described in chapter 2.

For significance level , the inequality < should be considered statistically significant and scheme  “1”, obviously more accurate, if the following condition is satisfied:

=  > ,		                                                    (3.4)

where  is the quintile of central chi-squared distribution with one degree of freedom corresponding to probability of exceedance . For  = 5%,  = 3.84 [5, 23].

One should pay attention to the fact that the left part of inequality (3.4) increases with increasing value of coefficient . This is indicative of the fact that in case of strongly correlated forecast errors of compared methods, even a slight advantage of one of forecasting method over another becomes statistically significant.

Values  corresponding to admitting of statistically significant <   and more accurate scheme “1”, according to test 2, are presented in table 3.3 for different  and  while  = 5 %.

Table 3.3

Minimal sufficient values of ratio  for  = 5 %

|  | = 25 | = 50 | = 100 | = 250 | = 500 |
| --- | --- | --- | --- | --- | --- |
| 0 | 0.67 | 0.76 | 0.82 | 0.88 | 0.92 |
| 0.25 | 0.68 | 0.76 | 0.83 | 0.89 | 0.92 |
| 0.50 | 0.71 | 0.78 | 0.84 | 0.90 | 0.93 |
| 0.75 | 0.77 | 0.83 | 0.88 | 0.92 | 0.94 |
| 0.95 | 0.88 | 0.83 | 0.88 | 0.92 | 0.94 |

Data given in table 3.3 show that minimal sufficient values  increase with increasing  and approach unity as the number  of test forecasts  increases.

Test 3.

The presented statistical test is recommended for the use in the most general case of no limitations of test forecast error series properties. In this case, we recommend the multidimensional statistical analysis Mahalonobis distance based test ([22]) given in [5]. The errors  and  of estimates  and , defined by different formulas (see section 2.2) depending on estimation method, must be taken into account when using that test. The only condition of using that test is sufficiently large number of test forecasts,  and  for methods “1” and “2”, respectively.

For significance level , the inequality < should be considered statistically significant and method  “1”, obviously more accurate, if the following condition is satisfied:

=  > ,		                (3.5)

where  is the normal probability distribution quantile corresponding to probability of exceedance . In particular, for  = 5%,  = 1.64.

Values  corresponding to admitting of statistically significant <   and more accurate method “1” [5], according to test 3, are presented in table 3.4 for  = = = and  = 5 %.

Table 3.4

Minimal sufficient values of ratio  for  = 5 %

|  | = 25 | = 50 | = 100 | = 250 | = 500 |
| --- | --- | --- | --- | --- | --- |
| 0 | 0.63 | 0.74 | 0.82 | 0.88 | 0.91 |
| 0.25 | 0.64 | 0.75 | 0.82 | 0.89 | 0.92 |
| 0.50 | 0.67 | 0.78 | 0.84 | 0.90 | 0.93 |
| 0.75 | 0.74 | 0.82 | 0.88 | 0.92 | 0.94 |
| 0.95 | 0.86 | 0.91 | 0.93 | 0.96 | 0.97 |

The values of ratio  presented in table 3.4 are close to those given in table 3.3. They demonstrate that in case of virtually synchronous error fluctuations of compared forecasting schemes even a slight difference in their error estimates is indicative of statistically significant advantage of one of those methods.

3.2 Hydrologic forecasting methods comparison examples

1. Example of comparing long-term hydrological forecasting methods

Compare two methods (algorithms) of long-term forecasting of mean April inflow volume into Sayano–Shushenskoe reservoir (lead time is 35 days). Both are based on the same data for the period from 1979 to 2003.

Method 4 can be used for estimating the forecast errors of algorithm “1” with 2 predictors and 3 estimated parameters of linear forecasting formula (see section 2.3). Estimate of mean squared forecast error , defined by formulas (2.1) and (2.17), is equal to 26240 ()2. The measure of forecast error, the root mean squared error , is equal to 162 .

Algorithm “2” is a simplification of algorihm “1” rejecting the second predictor, mean 10-day air temperature forecast for 1-st 10-day period of April  = ºC for Kyzyl weather station. Thus, algorithm 2” has only one predictor and 2-parametric linear forecasting formula. As for algorithm “1”, method 4 can be used for forecast error estimating. Mean squared forecast error , estimated by formulas (2.1) and (2.17), is equal to 30945 ()2. Root mean squared error  is equal to 176 .

According to formulas (2.18) and (2.19), method 4 allows estimating the values  and  for both schemes; relative error is 31% and 15%, respectively.

Defined by formula (3.1), forecast errors correlation coefficient estimate  is equal to 0.86, whereas the inequality (3.2) is true for any feasible significance level . There is therefore statistically significant correlation between errors of forecasts “1” and “2” for the same years, according to Pitman test.

Concerning specific features of the forecasting algorithms, with ,  and  estimates taken into account, the above statistical tests are used for comparing both forecasting methods.

Using test 1.

The linear forecasting formula of algorithm “1” and rejecting of second predictor in algorithm “2” allow for using the most powerful test 1. The number of parameters for the first scheme is =3, for the second, = 2 for = 1. The same observation series of = = 25 years length was used for developing both forecasting schemes.

Defined by formula (3.3), test measure  is equal to 3.27. For standard significance level  = 5 %, its critical value  is equal to 4.35. For such significance level, the inequality (3.3) is not true and, according to test 1, there is no statistically significant advantage of algorithm “1” over algorithm “2”. For  = 10 %, critical value  is equal to 2.95, the inequality (3.3) is true and the advantage of forecasting algorithm “1” over algorithm “2” is considered statistically significant.

In this case, we cannot come to a straightforward conclusion that forecasting algorithm “1” is more accurate than algorithm “2” and that therefore rejecting the second predictor (above mentioned mean 10-day air temperature forecast) in order to develop a simplified algorithm “2” is unreasonable.

Using test 2.

In case of using a more generalized test 2, test measure  defined by formula (3.4) is equal to 0.66. Even for a high significance level =10 %, critical value of  is =2.71 and therefore the inequality (3.4) is not true. According to test 2, there is no statistically significant advantage of algorithm “1” over algorithm “2”.

Using test 3.

In case of using the most generalized test 3, test measure  defined by formula (3.5) is equal to 0.74. Even for a high significance level =10 %, critical value =1.645 and the inequality (3.5) is not true. According to test 3, there is no statistically significant advantage of algorithm y “1” over algorithm “2”.

Thus, in case of long-term forecasting of mean April inflow volume into Sayano–Shushenskoe reservoir, using mean 10-day air temperature forecast for the first 10-day period of April for Kyzyl weather station =  ºC as second predictor does not result in statistically significant forecast accuracy improvement [5].

2. Example of comparing short-range hydrological forecasting methods

Compare two methods (algorithms) of short-range stream flow forecasting for the Sochi River at Sochi (lead time is 1 day). Both were developed using the same hydrometeorological observation data for the period from 1984 to 2005 accounting for observation gaps (series length  = 18 years). Total monthly number of daily observations varies from 508 to 558. For the whole year, mean long-term total number of daily observations is equal to 6506.

As for forecasting algorithm “1” presented in section 2.4, its forecasting formula has 13 parameters estimated for each month using least squares method.

As for forecasting algorithm “2” based on the same conceptual snowmelt- and rainfall-runoff model and using the same hydrometeorological data, its forecasting formula is simplified and has only  = 7 parameters estimated for each month.

Concerning specific features of the forecasting algorithms, with ,  and  estimates taken into account, the above statistical tests are used for comparing both forecasting methods.

Using test 1.

The most powerful test 1 can be used for comparing the above algorithms. The formulas (2.1) and (2.17) of method 4 considered in section 2.2 were used for computing the error estimates  and  with the results of forecast testing using dependent sample taken into account, as well as the number of estimated parameters  = 13 and  = 7 and correlation coefficient estimates  and  of forecast error values with 1-day time lag for algorithms “1” and “2” respectively, defined by formula (2.7). The values of , , ,  and , as well as the values of test measure  defined by formula (3.3) for  = 13 и  = 6, are presented in table 3.5.

Table 3.5

Stream flow forecasting algorithms comparison results using test 1 (case study of Sochi River flow forecasting at Sochi)

|  | I | II | III | IV | V | VI | VII | VIII | IX | X | XI | XII | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 554 | 508 | 526 | 540 | 558 | 540 | 558 | 526 | 540 | 558 | 540 | 558 | 6506 |
|  | 108 | 72 | 114 | 74 | 219 | 146 | 85 | 125 | 77 | 234 | 210 | 262 | 144 |
|  | -0.03 | 0.01 | 0.02 | 0.02 | 0.21 | 0.23 | 0.11 | 0.12 | 0.12 | -0.03 | 0.00 | 0.08 | 0.07 |
|  | 161 | 88 | 164 | 83 | 279 | 149 | 86 | 135 | 81 | 266 | 253 | 331 | 172 |
|  | 0.03 | 0.00 | -0.02 | -0.03 | -0.01 | -0.05 | -0.02 | -0.01 | -0.02 | -0.05 | -0.03 | 0.00 | -0.02 |
|  | 47.2 | 18.2 | 36.8 | 10.8 | 24.7 | 1.88 | 1.04 | 6.12 | 4.67 | 11.8 | 17.9 | 23.6 | 212 |

For significance level  = 5 %, = 6 and large value of , critical value of test measure  is equal to 2.10. According to the data given in table 3.5, for the whole year and for all months except for June and July, the inequality (3.3) is true and there is statistically significant accuracy advantage of algorithm “1” over algorithm “2”.

Using test 2.

The same error estimates  and  were considered when using more generalized test 2.  Correlation coefficient  of forecast “1” and forecast “2” errors for the same days was estimated using formula (3.1) for each month and for the whole year (see table 3.6). The values of test measure  defined by formula (3.4) are also given in table 3.6.

Table 3.6

Stream flow forecasting algorithms comparison results using test 2 (case study of Sochi River flow forecasting at Sochi)

|  | I | II | III | IV | V | VI | VII | VIII | IX | X | XI | XII | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 554 | 508 | 526 | 540 | 558 | 540 | 558 | 526 | 540 | 558 | 540 | 558 | 6506 |
|  | 108 | 72 | 114 | 74 | 219 | 146 | 85 | 125 | 77 | 234 | 210 | 262 | 144 |
|  | 161 | 88 | 164 | 83 | 279 | 149 | 86 | 135 | 81 | 266 | 253 | 331 | 172 |
|  | 0.81 | 0.87 | 0.84 | 0.92 | 0.85 | 0.96 | 0.98 | 0.97 | 0.93 | 0.90 | 0.90 | 0.89 | 0.90 |
|  | 61.5 | 20.7 | 56.6 | 11.5 | 28.9 | 0.73 | 0.54 | 13.0 | 2.61 | 11.9 | 24.2 | 35.7 | 265 |

For significance level  = 5 %, critical value of is = 3.84. According to the data given in table 3.6, for the whole year and for all months except for June, July, and September, the inequality (3.4) is true and there is statistically significant accuracy advantage of algorithm “1” over algorithm “2”.

Using test 3.

The same error estimates  and , defined by formulas (2.1) and (2.17), were considered when using the most generalized test 3. Correlation coefficient estimates  and  of forecast error values with 1-day time lag for schemes “1” and “2” respectively, defined by formula (2.7), were taken into account as well. Root mean squared errors  and  of estimates  and  respectively, defined by formula (2.18), are presented in table 3.7. The values of test measure , defined by formula (3.5) for  = = =  and  defined by formula (3.1), are also given in table 3.7.

Table 3.7

Stream flow forecasting algorithms comparison results using test 3 (case study of Sochi River flow forecasting at Sochi)

|  | I | II | III | IV | V | VI | VII | VIII | IX | X | XI | XII | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 554 | 508 | 526 | 540 | 558 | 540 | 558 | 526 | 540 | 558 | 540 | 558 | 6506 |
|  | 108 | 72 | 114 | 74 | 219 | 146 | 85 | 125 | 77 | 234 | 210 | 262 | 144 |
|  | 6.6 | 4.6 | 6.2 | 5.1 | 18.9 | 17.3 | 11.1 | 16.7 | 6.5 | 17.2 | 14.1 | 19.1 | 3.8 |
|  | 161 | 88 | 164 | 83 | 279 | 149 | 86 | 135 | 81 | 266 | 253 | 331 | 172 |
|  | 15.6 | 6.7 | 10.6 | 6.4 | 30.6 | 18.0 | 11.7 | 16.8 | 7.3 | 20.1 | 18.6 | 24.9 | 5.0 |
|  | 0.81 | 0.87 | 0.84 | 0.92 | 0.85 | 0.96 | 0.98 | 0.97 | 0.93 | 0.90 | 0.90 | 0.89 | 0.90 |
|  | 4.9 | 5.1 | 7.9 | 3.3 | 3.9 | 0.8 | 0.4 | 2.1 | 1.4 | 5.9 | 4.6 | 5.7 | 12.7 |

For significance level  = 5 %, critical value of is  = 1.64. According to the data given in table 3.7, for the whole year and for all months except for June, July, and September, the inequality (3.5) is true and there is statistically significant accuracy advantage of algorithm “1” over algorithm “2”. For the Sochi River, flood frequency is quite low in the period from July to September following the period of relatively low spring flood. Therefore, the impact of using simplified forecasting algorithm  “2” is minimal [6].

Thus, the results of using the above three tests allow to make the same conclusion that for the whole year and for almost all months, there is statistically significant accuracy advantage of forecasting algorithm “1” over algorithm “2” [5, 6].

3.3 Forecast applicability assessment

As mentioned in chapter 1, climatology forecasting method (“climatology”), as well as inertial (persistence) forecast, may be used as unconditional alternative of some hydrological forecasting method. If the latter is obviously more accurate than unconditional alternative forecast, the studied method has proved to be used in hydrological forecasting practice [5].

Climatology method is used as unconditional alternative of long-range and some medium-range hydrological forecasting techniques, as well as of occurrence dates forecasting of events characterizing the hydrological regime of a water body.

The forecast of some hydrologic characteristic  produced using the climatology method is characterized by its long-term value  averaged over the -year period of observations (,…, ). Such forecast error is usually characterized by  variance estimate defined by the following formula:

= . 			                                                         	(3.6)

The “climatology” forecast error is compared to the error of forecast produced using the evaluated method. That error is usually characterized by an index  defined by formula (2.1). That measure is an approximate estimate of residual variance related to the variance of forecasted value and correlation ratio  (see formula (2.2)) [18]. Squared  estimate is defined by the following formula:

= 1 – ,				                                   (3.7)

where  is observed actual value of forecasted hydrologic characteristic and  is its -year forecast produced using the evaluated scheme. The number of forecasting formula parameters is denoted by .

The above index , defined by formula (3.7), is a correction of Nash-Sutcliffe efficiency index widely used in a number of countries for assessing the hydrological forecast efficiency [5, 30, 38].

In a number of countries, the ratio  is used for assessing the applicability of a hydrological forecasting method. Depending on the value of  and the number of test forecasts , the evaluated method belongs to one of three possible categories: good, satisfactory or unsatisfactory. In particular, for  25, hydrological forecasting method is considered good if 0.50; satisfactory, if 0.50 <0.80; and unsatisfactory, if  > 0.80 [5, 18].

The index , defined by formula (3.6), is underestimating the “climatology” error. Also, this estimate does not take into account the possible autocorrelation of ,…, , first of all, the correlation coefficient  of 1-year lagged actual  values. As for flood characteristics,  is close to zero and is therefore negligible. Otherwise, in case of low flow related to deep groundwater supplies having low interannual variability,  may be quite large [5]. The following formula is used for estimating that coefficient:

= .						                        (3.8)

Anderson test, described in section 2.1, is recommended for determining the statistical significance of estimate .

According to [5, 21, 24], approximate unbiased estimate of “climatology” error is defined by the following formula:

= .				                        (3.9)

Its root mean squared error is defined as follows:

= .					 	                        (3.10)

When comparing evaluated hydrological forecasting method (“M”) and “climatology” (“C”), the correlation coefficient between synchronous “M” and “C” forecast errors must be taken into account. It is estimated as follows:

= ,						                                               (3.11)

where  is the correlation ratio estimate defined by formula (3.7).

Inertial forecast is the unconditional alternative of short-range and some medium-range hydrological forecasting methods. For -day forecast lead time, inertial forecast  of some flow characteristic for day  is based on that characteristic’s value  known on the date of forecast issue and is defined by the formula:

= + ,					                                 (3.12)

where , providing the absence of systematic error, is mean variation of forecasted hydrologic characteristic over the lead time period. That value is the arithmetic mean of the series  for  = 1,..., , where  is the total number of forecasted hydrologic characteristic variation values observed over a hydrological forecast lead time period. Inertial forecast error estimate  is defined by the formula:

= .						                      (3.13)

In a number of countries, the ratio  is used for assessing the applicability of hydrological forecasting method (see the above described criteria for using ratio ) [18].

The index  is underestimating the error of inertial forecast. Even in case of no  autocorrelation of inertial forecast errors, its mean squared error  =  instead of  = . However, there may be considerable error autocorrelation, especially of 1-day lagged errors. That correlation coefficient estimate  may be defined using the formula (2.7) after replacing the 1-day lagged errors of evaluated hydrological forecasting method with analog  inertial forecast errors. Anderson test, considered in chapter 2, is recommended for determining the statistical significance of estimate . In case of no statistical significance of ,  = 0.

According to [5, 21, 24], approximate unbiased estimate  of inertial forecast error is defined by the formula:

= ∙.				                     (3.14)

Approximate value of its root mean squared error is defined as follows:

= .						                     (3.15)

In some cases of medium-range hydrological forecasting, a problem of choosing an unconditional forecasting alternative may arise. The choice of “climatology” or inertial forecast is driven by the  and  ratio. For -day forecast lead time, that ratio is determined by the angle of incline () of the line  = f(), where  is the forecasted hydrological variable and  is its actual value observed  days before day . The criterion of choice is as follows:

if  1/2, then  >  and inertial forecast is therefore recommended as unconditional alternative of evaluated forecasting scheme;

if  < 1/2,  <  and “climatology” is therefore recommended as unconditional alternative of evaluated forecasting scheme [5, 18].

Applicability assessment of a hydrological forecast is based on comparing its  error with that of unconditional alternative forecast. One of the methods described in section (2.2) should be used to get the error estimate  of forecast depending on the volume and quality of available data.

In case of choosing “climatology” as alternative, we need to compare  with  defined by formula (3.9). If < , we recommend the statistical tests presented in section 3.1 be used for testing the statistical significance of accuracy advantage of evaluated method over “climatology”.

In case of choosing inertial forecast as alternative, we need to compare  with  defined by formula (3.14). If < , we recommend the above mentioned tests be used for testing the statistical significance of accuracy advantage of evaluated method over inertial forecast.

3.4 Forecast applicability assessment examples

1. Example of evaluating the applicability of a long-range hydrological forecast

Applicability evaluation of 35-days lead time forecasting method of mean April inflow volume into the Sayano–Shushenskoe reservoir, presented in section 2.3, is considered as the first example of forecast applicability assessment. Hydrometeorological data over the period from 1979 to 2003 were used for developing that forecasting method. A 3-parametric linear  formula defines the relationship between the forecasted inflow and its two predictors. Defined by formulas (2.1) and (2.17), mean squared forecast error  is equal to 26240 ()2. According to formula (2.18), relative error of estimating  using method 4 is equal to 31%.

Climatology method, using mean long-term value of mean April reservoir inflow volume  = 652 , averaged over 25-year observation period, is used as unconditional forecast alternative. Standard “climatology” error  defined by formula (3.6) is equal to 223 . There is no autocorrelation between “climatology”-forecasted 1-year lagged inflow values, as that autocorrelation coefficient estimate  defined by formula (3.8) is equal to -0.04. Defined by formula (3.9), mean squared “climatology” error  is equal to 51528 ()2. According to formula (3.10), its relative estimation error is equal to 29%.

There is an unambiguous relationship between the correlation coefficient  of annual “method” and “climatology” forecast errors and multiple correlation coefficient  (see formula (3.7));  = 0.65.

Standard efficiency index of forecasting method is  = 0.68, as to which the studied long-term reservoir inflow forecasting method can be considered satisfactory.

Using test 1.

Due to linear forecasting formula, the first of the above statistical tests is the most effective for assessing the applicability of forecasting method. Defined by formula (3.3) for   = 2 and  = 22, the test 1 index  is equal to 14.9. For a standard significance level  = 5%, its critical value is  = 3.44; inequality (3.3) is true, is significantly less than  and thus the evaluated forecasting method should be used for long-term reservoir inflow forecasting instead of “climatology”.

Using test 2.

In case of using a more generalized and therefore less powerful statistical test 2, its index , defined by formula (3.4), is equal to 4.69. For a standard significance level  = 5%, its critical value is  = 3.84; inequality (3.3) is true and the evaluated forecasting method is therefore better than “climatology”.

Using test 3.

In case of using the most generalized and therefore the least powerful statistical test 3, its index , defined by formula (3.5), is equal to 2.26. For a standard significance level  = 5%, its critical value is  = 1.64; therefore, inequality (3.5) is true and the evaluated forecasting method should be considered efficient and significantly more accurate than “climatology”.

Thus, in accordance with all three statistical tests, applicability of considered long-term reservoir inflow forecasting method has proved, as it is significantly more accurate than   climatology method [5].

2. Example of evaluating the applicability of a short-range hydrological forecast

Applicability evaluation of one-day lead time stream flow forecasting method for the Sochi River at Sochi, presented in section 2.4, is considered as the second example of forecast applicability assessment. Conceptual snowmelt- and rainfall-runoff model is used for forecasting; the model parameters were estimated using hydrometeorological observation data over the period from 1984 to 2005. For each month and for the whole year, the errors of that forecast, produced using different methods, are presented in table 2.1. Error estimates defined by formulas (2.1) and (2.17) of method 4 are considered in this example.

One-day lead time inertial forecast defined by formula (3.12) for  = 1 is used as unconditional forecast alternative. For each month and for the whole year, the table 3.8 presents the values of , as well as of  defined by formula (3.13), 1-day lag autocorrelation coefficient estimates  of inertial forecast errors, and inertial forecast error estimates  defined by formula (3.14).

Table 3.8

Characteristics of daily stream flow forecast errors for the Sochi River at Sochi

|  | I | II | III | IV | V | VI | VII | VIII | IX | X | XI | XII | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0.0 | -0.2 | 0.0 | -0.1 | 0.1 | -0.4 | -0.3 | 0.1 | -0.1 | 0.6 | -0.3 | 0.3 | 0.00 |
|  | 15.1 | 12.7 | 16.5 | 12.0 | 19.6 | 12.2 | 10.0 | 11.8 | 10.8 | 21.0 | 21.4 | 22.6 | 15.5 |
|  | -0.12 | -0.14 | -0.08 | -0.02 | -0.08 | 0.06 | -0.13 | -0.15 | 0.01 | -0.10 | -0.14 | -0.16 | -0.09 |
|  | 17.9 | 13.7 | 19.5 | 13.7 | 26.4 | 16.1 | 12.8 | 15.1 | 13.8 | 23.9 | 25.4 | 25.3 | 18.6 |

For each month and for the whole year, table 3.9 presents the following data: traditionally used ratio of , the ratio of evaluated forecast errors to inertial forecast errors /, and the coefficient  of correlation between same-day evaluated forecast errors and inertial forecast errors.

There is considerable difference between the evaluated forecast error probability distribution and normal probability distribution, as well as between the inertial forecast probability distribution and normal probability distribution. In respect of the above, the most generalized test 3 was used for assessing the efficiency of considered forecasting scheme. The values of that test index , defined by formula (3.5), are presented in table 3.9. For each month and for the whole year, those values are large enough for the inequality (3.5) to be true for any feasible significance level .

Table 3.9

Applicability characteristics of short-range daily stream flow forecast for the Sochi River at Sochi

|  | I | II | III | IV | V | VI | VII | VIII | IX | X | XI | XII | year |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 0.62 | 0.60 | 0.58 | 0.61 | 0.65 | 0.72 | 0.63 | 0.66 | 0.64 | 0.58 | 0.57 | 0.63 | 0.62 |
|  | 0.58 | 0.62 | 0.55 | 0.63 | 0.56 | 0.75 | 0.72 | 0.74 | 0.64 | 0.64 | 0.57 | 0.64 | 0.65 |
|  | 0.36 | 0.50 | 0.33 | 0.44 | 0.29 | 0.49 | 0.40 | 0.45 | 0.30 | 0.41 | 0.41 | 0.50 | 0.41 |
|  | 10.9 | 10.0 | 11.2 | 9.9 | 11.2 | 7.0 | 7.7 | 7.0 | 9.3 | 9.7 | 11.1 | 10.0 | 32.7 |

Thus, the considered method of 1-day lead time daily stream flow forecasting for the Sochi River at Sochi may be considered efficient for each month and for the whole year [5, 6].

Chapter 4.  Estimation of admissible forecast error probability

4.1 Admissible forecast error probability estimation rules

The main measure of hydrological forecast error, considered in previous chapters, is the mean squared forecast error  defined by formula (1.1). The probability of admissible forecast errors is a useful complement to that quality measure [5, 18].

Denote studied hydrologic characteristic by , its forecast constructed using the studied method by , and admissible limiting error value by . Forecast error is considered admissible, if its absolute value is less than or equal to that admissible limit, so that inequality  is satisfied.

For any given admissible limit , the probability  of that inequality is defined by formula:

= = .                                                      (4.1)

Thus, the measures  and  define the confidence interval for an expected hydrologic characteristic value  depending on its forecast  constructed using the studied method.  Estimating probability  and constructing such interval might be considered as a kind of probabilistic hydrological forecast.

Taking section 1.2 into account, it is obvious that it would be the best to define the value  in coordination with forecast users. A formal approach to defining  is also possible. The following procedures are used in hydrological forecasting in a number of nations.

1. Climatic forecast is used as unconditional alternative for studied method. It is expressed as the norm  =  computed from long-term series of observed runoff characteristic values. The measure  defined by formula (3.6) is the characteristic of climatic forecast error. In this case, admissible limiting value of forecast error is defined as  = 0,674.

2. Inertial forecast  is used as unconditional alternative for studied method. It is defined by formula (3.12). The measure  defined by formula (3.13) is the characteristic of inertial forecast error. In this case, admissible limiting value of forecast error is defined as   = 0,674.

Such definition of admissible forecast error is due to the fact that, given normal probability distribution of alternative forecast error  - , the probability of inequality 0,674 approaches 50% with increasing length of the series used for computing  =  or  = .

If forecast errors obtained using the assessed method also have normal probability distribution, then, given  = 0,674, the probability  of admissible forecast error is defined by the ratio  between root mean square errors of the studied method and of alternative forecast. The relationship between presented measures is given in table 4.1 [5, 18].

Table 4.1

Probability  of admissible forecast errors for different values

|  | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| , % | 100 | 99.9 | 97.5 | 91 | 82.5 | 74 | 66.5 | 60 | 54.5 | 50 |

In case of quite long series of test forecast errors, the ratio  does not differ  considerably from the ratio  between the measure of algorithm error defined by formula (2.1) and the measure of alternative forecast error  defined as  or . According to table 4.1, considering the forecasting method good or satisfactory, when inequality 0.80 is satisfied, is equivalent to probability  of admissible forecast errors greater than or equal to 60% [5, 18]. In the above simple case of normal probability distribution, the probability of admissible forecast errors might be considered an additional applicability measure of studied scheme.

Actually, probability distribution of alternative (climatic and inertial) forecast might considerably differ from normal distribution (see next section). In this case, the probability  of admissible alternative forecast error, i.e., of inequality 0,674 for each forecast issue, may vary from 15 to 85 %. The probability  deviation from 50% depends on the coefficient of skewness and kurtosis  (the coefficient of excess). For normal probability distribution, both those values are equal to zero. The contribution of kurtosis to that probability deviation is especially large, as kurtosis is a characteristic of occurrence probability of extremely large absolute forecast errors, given the same variance of distribution. In case of large negative values of kurtosis , the probability of admissible forecast errors approaches zero. In case of large positive , that probability approaches unity.

For any probability distribution of both forecasts errors, the relationship between probability values  and  is related with forecast method applicability measure . However, if those distributions differ considerably from normal distribution, there may be more complicated relationship [5].

Actually, for any given admissible forecast error , statistical assessment of unknown probability values  and  based on test method and alternative forecast error series, respectively, is needed.

The series of  test forecast errors ,...,  might be used for assessing the probability  of admissible forecast errors. Relative frequency  of admissible forecasts, equal to the number of cases when the inequality   is satisfied normalized by , is recommended for the use as the admissible forecast probability estimate. That estimate is unbiased, i.e., its mean value is equal to desired probability . Possible correlation between errors of forecasts issued on adjacent dates must be taken into account when analyzing the error of that estimate . In case of long-term forecasts, the correlation may be considered negligible; though that correlation may be strong in case of short-term forecasts.

We recommend the measure  be used as characteristic of test forecast error series autocorrelation impact on statistical properties of frequency :  is the frequency of adjacent forecasts simultaneously lying within admissible limits, i.e., inequalities  and  are simultaneously satisfied.

When describing statistical properties of frequency , it is reasonable to introduce an admissible error index :  = 1 when inequality  is satisfied; otherwise,  = 0. The frequency  is the arithmetic mean of all  values of that index. The coefficient estimate of correlation between adjacent admissible error index series members is defined by formula:

= .                                                                                            (4.2)

In case of no correlation between test forecast error series members, there is also no correlation between admissible error index series members. The frequency  is close to squared frequency  of admissible forecast errors, whereas the coefficient  is close to zero.

In case of very strong correlation between test forecast error series members, the frequency  is close to admissible forecast error frequency , whereas the coefficient  is close to unity.

According to [5], root mean squared error of frequency  may be approximately estimated using formula:

= .                                                                         (4.3)

A similar formula is used for estimating the probability  of alternative (climatic or inertial) forecast. Denoting alternative forecast by  (= or = in case of climatic and inertial forecast, respectively), the  test forecast error series ,...,  may be used for estimating admissible alternative forest error probability . We recommend relative frequency  of admissible forecasts be used as estimate of :  is defined as the number of cases when inequality  is satisfied, normalized by .

We also recommend the measure  be used as characteristic of alternative forecast error series autocorrelation impact on statistical properties of frequency :  is the frequency of adjacent forecasts simultaneously lying within admissible intervals, i.e., inequalities  and  are simultaneously satisfied.

The coefficient estimate  of correlation between adjacent members of admissible inertial forecast error index series is defined by formula (4.2), where frequency values  and  must be replaced by values  and .

According to [5], root mean squared error  of frequency  may be approximately estimated using formula (4.3), where  and  must be replaced by  and  [5].

Statistical significance test of inequality <  is presented in section 3.3. Successful test means that examined forecasting method is definitely more accurate than alternative forecast. We recommend that test be completed with a statistical significance test of inequality  > . If that additional test is successful, examined forecasting method has definitely higher admissible error probability than that of alternative forecast.

The correlation between errors of examined and alternative forecast must be taken into account when comparing the frequency estimates  and , as that correlation results in statistical relationship between those estimates. Consider two possible situations.

1. The initial observation series has some extremely high or extremely low value with extremely large positive or negative forecast error, respectively. Alternative forecast error will be very likely the same. As a result, both forecast error values are beyond admissible limits  and both frequency values  and  are underestimated.

2. The initial observation series has too many values close to norm. Forecast errors are very likely to lie within admissible limits and both frequency values  and  are overestimated.

Statistical relationship between  and  is characterized by the frequency  of both forecast errors simultaneously lying within admissible limits, i.e., when the inequalities  and  are simultaneously satisfied. According to [5], the correlation coefficient between  and  is estimated using the following formula:

= .                                                                           (4.4)

In case of no correlation between scheme and alternative forecast errors, there is also no correlation between  and ; therefore,  is close to the composition of frequency estimates  and correlation coefficient  is close to zero.

Otherwise, in case of fully synchronous fluctuations of scheme and alternative forecast errors, == and  = 1.

We recommend the following criterion be used for comparing  and . According to that criterion, the inequality  >  and testing method applicability should be considered statistically significant, if the following inequality is satisfied:

=  > ,                                        (4.5)

where  is the normal probability distribution quintile corresponding to probability of exceedance  [5]. Significance level  defines the probability to admit statistical significance of inequality  >  , whereas actually  = . In particular,  = 1.64 while  = 5 %.

4.2 Admissible forecast error probability estimation examples

First of all, consider two theoretical examples of using that criterion in case of no autocorrelation of both forecast error series and admissible inertial forecast error frequency  equal to 50 %.

Example 1.

Suppose there is no correlation between forecasting method and alternative forecast errors when correlation coefficient  is equal to zero. For  = 5 % and different series length values , minimal sufficient admissible forecast error frequency values  for examined forecasting scheme such that inequality (4.5) is satisfied and that methodology applicability is significant are given in table 4.2.

Table 4.2

Minimal sufficient frequency values  in case of no correlation of frequency estimates  and

|  | 10 | 25 | 50 | 100 | 250 | 500 | 1000 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| % | 87.3 | 75.7 | 68.9 | 63.6 | 58.7 | 56.0 | 54.4 |

Example 2.

Suppose forecasting method and alternative forecast errors are fully correlated when =1. For  = 5 % and different series length values , minimal admissible forecast error frequency values  for examined forecasting method such that inequality (4.5) is satisfied and that methodology applicability is significant are given in table 4.3.

Table 4.3

Minimal sufficient frequency values  in case of fully correlated frequency estimates  and

|  | 10 | 25 | 50 | 100 | 250 | 500 | 1000 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| % | 77.8 | 63.3 | 57.1 | 53.7 | 51.5 | 50.8 | 50.4 |

Comparison of data given in tables 4.2 and 4.3 shows, that even slight benefit of one algorithm becomes statistically significant with increasing forecast error correlation.

Example 3.

Consider the admissible error probability assessment of long-term reservoir April inflow forecast for Sayano–Shushenskoe reservoir (lead time is 35 days); the forecasting method is presented in section 2.3. Climatic forecast with error measure  = 223 is used as alternative forecast. Admissible forecast error , defined as 0,674 , is equal to 150 .

Series of studied long-term forecasting method errors and of alternative forecast errors were used for estimating admissible forecast error probability (series length  = 25). For both series, there is no statistically significant autocorrelation. Admissible error frequency of long-term forecast  = 84%. Admissible climatic forecast error frequency  = 56%.

According to probability distribution analysis of forecasted value , it does not match normal distribution but virtually perfectly matches 3-parametric gamma distribution with = 652 cubic meters per second, = 0,35, and  = 3. According to statistical analysis results of long-term test forecast error series presented in section 6.1, , it also does not match normal distribution.

When testing the statistical significance of inequality > , the frequency of both forecast errors lying within admissible limits was taken into account,  = 48 %. In case of using above presented criterion, the measure  defined by formula (4.5) is equal to 2.33. For standard significance level  = 5 %, critical value  = 1.64. Therefore, the inequality (4.5) is satisfied. According to that criterion, the inequality  >  should be considered statistically significant as well as the applicability of that method.

Example 4.

Consider the admissible error probability assessment of 1-day lead time flow forecast for the Sochi River at Sochi (see section 2.3), compared to alternative inertial forecast; admissible forecast error  is defined as 0,674.

Series of test forecast errors (series length  = 508–558) and of analogous inertial forecast errors were used for estimating admissible forecast error probability. According to statistical analysis results of those series presented in section 6.2, empirical probability distribution does not match normal probability distribution. Main difference is distribution “tails” due to anomalous high frequency of extremely large positive and negative forecast errors, indicative of high kurtosis values.

For each month of the year, the number of test forecasts  and admissible forecast error values  are presented in table 4.4, as well as estimates of admissible forecast error frequencies  (scheme) and  (alternative inertial forecast), correlation coefficients  and , root mean squared errors  and , correlation coefficient  between  and , and values of measure  computed using formula (4.5).

Table 4.4

Applicability characteristics of flow forecasting methodology for the Sochi River at Sochi

|  | I | II | III | IV | V | VI | VII | VIII | IX | X | XI | XII | год |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 554 | 508 | 526 | 540 | 558 | 540 | 558 | 526 | 540 | 558 | 540 | 558 | 6506 |
|  | 10.2 | 8.6 | 11.1 | 8.1 | 13.2 | 8.2 | 6.7 | 8.0 | 7.3 | 14.2 | 14.4 | 15.2 | 10.4 |
| % | 79.1 | 81.3 | 78.6 | 84.2 | 75.8 | 78.9 | 84.7 | 76.4 | 74.5 | 73.3 | 76.4 | 73.5 | 78.2 |
|  | -0.01 | 0.01 | 0.01 | 0.01 | 0.21 | 0.16 | 0.09 | 0.10 | 0.10 | -0.01 | 0.00 | 0.06 | 0.05 |
| % | 1.7 | 1.7 | 1.8 | 1.6 | 1.9 | 1.8 | 1.5 | 1.9 | 1.9 | 1.9 | 1.8 | 1.9 | 0.5 |
| % | 61.5 | 63.0 | 59.6 | 66.4 | 60.3 | 69.2 | 68.9 | 62.5 | 60.7 | 54.8 | 55.4 | 53.5 | 57.4 |
|  | -0.08 | -0.10 | -0.06 | 0.00 | -0.03 | 0.05 | -0.10 | -0.11 | 0.02 | -0.06 | -0.11 | -0.13 | -0.06 |
| % | 2.1 | 2.2 | 2.1 | 2.0 | 2.1 | 2.0 | 2.0 | 2.1 | 2.1 | 2.1 | 2.2 | 2.1 | 0.6 |
|  | 0.47 | 0.63 | 0.45 | 0.55 | 0.38 | 0.61 | 0.52 | 0.57 | 0.40 | 0.52 | 0.52 | 0.63 | 0.53 |
|  | 8.9 | 10.5 | 9.2 | 10.2 | 6.9 | 5.7 | 8.9 | 7.5 | 6.3 | 9.4 | 10.6 | 11.6 | 38.5 |

The data presented in table 4.4 demonstrate that all values of measure  substantially exceed the critical value  for any feasible significance level . According to that criterion, the inequality  >  must be considered statistically significant and the presented method, quite applicable.

Chapter 5.  Probabilistic hydrological forecast

5.1 Probabilistic forecasting methods

The reasons defining the discrepancy between deterministic forecast  and its observed value  were considered in chapter 1. Hydrologic forecast users must consider probable discrepancies between expected hydrological characteristic and its forecast. Due to stochastic nature of hydrological processes and possibilities of their forecasting, the deterministic forecast of values of hydrologic characteristics must be completed by forecast of probability distribution of those expected values (probabilistic forecast) [5, 17, 28, 32, 37].

Probabilistic forecasting implies the estimation of conditional probability distribution  of some expected hydrological characteristic. For any argument value , the function  defines conditional probability of inequality <  depending on hydrometeorological information available on forecast issue date, including weather prediction over the hydrological forecast lead time period. That probability distribution can be also expressed as conditional frequency curve defining the value , where  is its probability of exceedance [5, 18]. For each forecast issue, the functions  and can be given as formulas, graphs, or tables. In some cases, additional probabilistic forecast forms are needed.

Additional probabilistic forecast form 1

With hydrometeorological data available on forecast issue date taken into account, conditional probability  that expected value  lies in the given interval  is defined as –.

In case of low values of a hydrologic characteristic , recognizing the probability that  is less than some given value  ( lies in the interval , where  =  and  = ) is important for the hydrological forecast user. The probability that <  is defined as  using conditional probability distribution function .

In case of high values of a hydrologic characteristic , recognizing the probability that  is greater than some given value  ( lies in the interval , where  =  and  = ) is important for the hydrological forecast user. The probability that >  is defined as  using conditional probability distribution function  [5, 18].

Additional probabilistic forecast form 2

With hydrometeorological data available on forecast issue date taken into account, conditional confidence interval  is defined, where  is the given probability that value  lies in that interval. Confidence limits are defined as  =  and  =  using conditional frequency curve  for given probability values  and , such that .

In case of low values of a hydrologic characteristic , recognizing the value , such that probability of inequality <  is equal to , is important for the hydrological forecast user. Defining the value  is equivalent to defining the confidence interval  with limits  =  and  = . Using conditional frequency curve , the value  is defined as .

In case of high values of a hydrologic characteristic , recognizing the value , such that probability of inequality >  is equal to , is important for the hydrological forecast user. Defining the value  is equivalent to defining the confidence interval  with limits  =  and  = . Using conditional frequency curve , the value  is defined as  [5, 18].

So, probabilistic hydrological forecast can be completed by estimation of admissible forecast error probability, as well as the probability that expected runoff characteristic lies in a corresponding interval. Such probability estimation is considered in chapter 4.

Desired functions  and  describe probable discrepancy between expected value  and its conditional mathematical expectation  which depends on hydrometeorological data available on hydrological forecast issue date. If some value  is defined using this data, then the mathematical expectation  is minimal for  =  [5, 15, 35]. Forecasting method is developed such that forecast error  =  is minimal, where  is forecast of value . Thus,  is the estimate of conditional mathematical expectation , whereas conditional probability distribution estimation of expected runoff characteristic  must be based on statistical analysis of forecast errors (regardless of the form of their presentation).

Traditional hydrological probabilistic forecasting approach is based on the above conclusion [5, 18].

In the recent years, another approach, based on different modifications of dynamic-stochastic hydrological modelling method, has been developed [8, 17, 25, 31].

Forecast factors can be divided in two categories. Hydrometeorological factors which characteristics are available on the forecast issue date belong to the first category. Those characteristics are components of vector . Weather elements changing over the hydrological forecast lead time period belong to the second category. Their characteristics are the components of vector . The hydrological model used for hydrologic characteristic  forecasting defines  as function .

If hydrological forecast lead time is short enough for satisfactory weather forecast  accuracy, then hydrological forecast  is defined as , given the vector  components.

Otherwise, scenario ensemble of weather element forecasts over the hydrological forecast lead time period is used. That ensemble is expressed as the series ,...,  of vector  values. Substituting those values into forecasting model, we generate a series ,…, allowing for statistical estimation of conditional probability distribution  or frequency curve , whereas the series mean determines the forecast  [2, 4, 7, 12, 25, 31, 43, 45].

That series may be generated using weather observation data either over the same long-term period () or over a longer one (). In case of , the results of described procedure are the same as those of statistical analysis of test forecast error series [5]. In case of using a longer observation period, a problem of climate change–driven perturbation of stationarity of the above series ,…, may arise.

A weather generator, based on a meteorological model taking into account observed and projected climate change, may be used for generating scenario ensemble of weather element forecasts over the hydrological forecast lead time period. In this case, it is important to remember that developing and running such a model may be substantially more difficult than considered task of hydrological forecasting.

Such use of dynamic-stochastic modelling method is proved only for the case when hydrological forecast error is fully determined by uncertainty of weather element forecasts over the hydrological forecast lead time period. The above is possible, if weather conditions are of great importance during the period of hydrological forecast lead time and weather forecast error is large and the model used for hydrological forecasting is fully taking into account all other predictors, so that the function  is determining the true value of forecasted hydrological variable.

As the above is a rare condition, probabilistic forecasting based on statistical analysis of test forecasts is considered below. Such an approach is equivalent to supposing that all hydrometeorological data used for producing a hydrological forecast is represented in its deterministic form.

Probabilistic forecasting implies the estimation of functions  or  which describe the probability distribution of some expected hydrologic characteristic value depending on hydrometeorological data available on the hydrological forecast issue date. The series ,…, , where ,…,  is observation series and ,…,  is test forecast series, is used as input data for  and  estimation.

As a rule, such hydrological forecasting method is developed that deterministic forecasts have no systematic errors. In some cases, forecast correction is used for this purpose [5]. Thus, the mathematical expectation of forecast error  can be considered zero. Unconditional mathematical expectation of squared forecast error is equal to error measure considered in detail in chapters 1 and 2. However, conditional mathematical expectation of squared random variable  might depend on a given forecast value . If occurrence frequency of large forecast errors increases with increasing forecast value, it means that conditional mathematical expectation of squared forecast error increases with increasing forecast value [5].

In such cases, probabilistic forecasting might be largely hindered by using forecast error . Thus, there is another measure  of discrepancy between observed and forecast values  and , recommended for using instead of that error . That recommended measure  should satisfy the following requirements:

1) random fluctuations of forecast error  are independent of forecast value  and always have zero mean and same variance ;

2) the measure  has normal probability distribution (or any other quite simple probability distribution) for any forecast value .

Suggested hydrologic probabilistic forecasting algorithm implies the following stages:

- Choosing forecast error measure  satisfying the above requirements.

- Testing whether those requirements are met using statistical criteria presented in next section.

3.	Statistical estimation of probability distribution of that measure based on the series ,…, .

4.	Defining desired function  or  by probability distribution of the measure .

Three easiest and the best operational hydrological forecasting methods are presented below [5, 18].

Method 1

Trivial forecast error  is used as measure .

Suppose that forecast error  has normal probability distribution with zero mean and variance =  for any forecast value .

Methods presented in section 2.2 are used to obtain the variance estimate .

For an expected value  of hydrologic characteristic, the estimates of conditional probability distribution function  and conditional frequency curve  are defined by the following formulas, depending on forecast value :

= ,                                                                                                 (5.1)

=   .                                                                                          (5.2)

Here,  is Laplace distribution function:

=                                                                                             (5.3)

and  is its frequency curve. Both functions are defined using available computer programmes or tables presented in numerous papers on probability theory [20, 21, 35, 39].

Method 2

Relative forecast error  is used as measure .

Suppose that relative forecast error  has normal probability distribution with zero mean and variance=   for any forecast value .

To use the methods presented in section 2.2 for computing the variance estimate , forecast error values  are replaced with their relative values , where  is forecast value.

For an expected hydrologic characteristic value , the estimates of conditional probability distribution function  and conditional frequency curve  are defined by the following formulas, depending on forecast value :

= ,                                                                                                (5.4)

=   .                                                                                       (5.5)

Method 3

Hydrologic characteristic logarithm forecast error  is used as measure .

Suppose that forecast error  has normal probability distribution with zero mean and variance=   for any forecast value .

To use the methods presented in section 2.2 for computing the variance estimate , forecast error values  are replaced with logarithm forecast errors .

For an expected runoff characteristic value , the estimates of conditional probability distribution function  and conditional frequency curve  are defined by the following formulas, depending on forecast value :

= ,                                                                                         (5.6)

=  .                                                                                      (5.7)

In some individual cases, some other forecast error measures  having probability distribution different from normal would be the best for probabilistic hydrological forecasting. However, we recommend the above described general procedure be used for obtaining the estimates of functions  и .

5.2 Probabilistic forecast verification

The same test forecast – based series ,…, , completed by forecast error  series ,…, , should be used for probabilistic forecast verification. The values  =  for  = 1,...,  are equal to , , and  for methods 1, 2, and 3, respectively.

1. First of all, significance test for autocorrelation of series ,…,  must be performed using recommended Anderson test (see section 2.1). In this case, standard correlation coefficient estimate should be computed for adjacent series members:

=  .                                                                   (5.8)

Correlation coefficient is statistically significant, if the following inequality is satisfied:

>,                                                                         (5.9)

where  is the quantile of normal probability distribution;  is equal to 1.96 while =5 %.

If the inequality (5.9) is satisfied, then preliminary exclusion of adjacent forecast values is recommended in order to eliminate the correlation between series ,…, , leaving either odd or even numbers. As a result, two truncated series are generated. Using Anderson test, statistical significance of correlation is tested. If there is no statistically significant correlation, both truncated series must be used for further verification. If the inequality (5.9) is satisfied for those series, further series truncation might be performed, leaving only 1st, 4th, 7th , … members or 2nd, 5th, 8th members, or 3rd, 6th,9th …members, etc. Then, a test for the requirements satisfaction (see precious section) for the used forecast error measure must be carried out.

2. If the variance of forecast error measure  is constant for any forecast value , it means that there is no statistically significant correlation between  and . Pitman test (see section 3.1) is recommended for testing that correlation significance. In this case, standard estimate of correlation coefficient between  and must be computed:

= ,                                                            (5.10)

Where  and   are mean values of  and  computed from initial series.

There is no statistically significant correlation of random values  and , if the following inequality is satisfied:

< ,                                                                        (5.11)

where  is the quantile of Student’s probability distribution with  degrees of freedom, corresponding to probability of exceedance ; while  = 5 %,  is approximately equal to 2.

3. Standard goodness-of-fit tests should be used for testing the supposed normal probability distribution of the series ,…,  (or any other quite simple probability distribution). Hypothetical probability distribution function  of measure  implies preliminary estimation of  parameters based on series ,…, . When using the above recommended methods, hypothetical probability distribution is normal probability distribution with zero mean and variance . The latter is the only parameter to be estimated (= 1). Variance  is equal to , , and  for methods 1, 2, and 3, respectively.

Pearson goodness-of-fit test is recommended for use [5]. The following preliminary procedures are needed:

1) numerical axis is divided into  intervals  for  and ;

2) the recommended number of intervals  should be greater than  and less than ;

3) recommended intervals should be such that all hypothetical probabilities =  of values lying within each interval be approximately equal to ;

4) relative frequencies  of values lying within each interval are computed based on the series ,…, .

While the significance level (the probability of rejecting a true hypothesis) is equal to , the hypothetical probability distribution test result of measure  should be considered successful, if the following inequality is satisfied:

= ,                                                                       (5.12)

where  is the quantile of central chi-squared distribution with  degrees of freedom,  is the probability of exceedance [21, 35, 39]. The values of  for  = 5 % are presented in table 5.1 [5].

Table 5.1

Critical quantiles  of chi-squared distribution ( = 5 %)

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.84 | 5.99 | 7.81 | 9.49 | 11.07 | 12.59 | 14.10 | 15.51 | 16.92 | 18.31 |

In case of quite long series (> 25), Cramér–von Mises–Smirnov criterion is recommended for use [5, 21, 35, 39]. The following preliminary procedures are needed:

1) computing the values ;

2) generating a ranked series .

For significance level equal to , the hypothetical probability distribution test result of measure  should be considered successful, if the following inequality is satisfied:

= ,                                                              (5.13)

where  is the distribution quantile given in table 5.2 [5].

Table 5.2

Critical values  for different significant level values

| , % | 1 | 2,5 | 5 | 10 |
| --- | --- | --- | --- | --- |
|  | 0.74 | 0.58 | 0.46 | 0.34 |

For each additional probabilistic forecast form, probability distribution must be tested with regard to specific features of that forecast form.

The additional form 1 implies the estimation of conditional probability  that expected runoff characteristic lies within some given interval  depending on its forecast  obtained using the studied methodology. Knowing the conditional probability distribution function estimate  of expected runoff characteristic, obtained using above described methods, probability estimate  is computed as –.

For each member of test forecast series , conditional probability distribution function estimate  depends on forecast value . It is therefore reasonable to denote probability estimate  as .

We recommend the test revising Brier score widely used in probabilistic weather forecasting and based on an asymptotically most powerful Wald likelihood-ratio test [5, 7, 8, 20] be used for testing the correspondence between probability values ,...,  and series ,…, . When using this test, an indicator  is defined for each test forecast series member:  = 1 if a value  lies within an interval , otherwise,  = 0. For significance level , the test of correspondence between probability values ,...,   and test forecast series ,…,  should be considered successful, if the following inequality is satisfied:

= ,                                                (5.14)

where  is the quantile of central chi-squared distribution with  degrees of freedom, corresponding to probability of exceedance . The values  for  = 5 %  are given in table 5.3 [5, 20].

Table 5.3

Critical quantiles  of chi-squared distribution ( = 5 %)

|  | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 18.31 | 31.41 | 43.77 | 55.76 | 67.50 | 79.08 | 90.53 | 101.88 | 113.14 | 124.34 |

The additional form 2 implies the estimation of an interval , such that an expected hydrologic characteristic  lies within that interval with a given probability , knowing the forecast  of that characteristic. Knowing the conditional frequency curve estimate obtained using above described methods, the estimates of that interval limits are defined as  and , where =.

For each member of test forecast series , conditional frequency curve estimate  depends on forecast value . It is therefore reasonable to denote interval limit estimates as  and . We recommend the following statistical test be used for testing probabilistic forecast form 2.

Relative frequency  of observed values  lying within an interval (,) should be defined based on test forecast series.

For frequency , a confidence interval with such limits  and  is constructed that the probability that  lies within that interval is equal to 1–. For any , , and , upper and lower confidence limits  and  are defined using available computer programmes or tables presented in [5, 20, 35,39]. The values of  and  for  = 5 % and different  and  are given in table 5.4.

Table 5.4

Confidence limits ( = 5 %) for frequency

|  | 0.05 | 0.10 | 0.25 | 0.50 | 0.75 | 0.90 | 0.95 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| = 20 |
|  | 0.003 | 0.018 | 0.071 | 0.302 | 0.599 | 0.717 | 0.784 |
|  | 0.216 | 0.283 | 0.401 | 0.698 | 0.929 | 0.982 | 0.997 |
| = 40 |
|  | 0.009 | 0.036 | 0.142 | 0.361 | 0.613 | 0.720 | 0.857 |
|  | 0.143 | 0.220 | 0.387 | 0.639 | 0.858 | 0.964 | 0.991 |
| = 60 |
|  | 0.013 | 0.044 | 0.161 | 0.387 | 0.642 | 0.813 | 0.882 |
|  | 0.118 | 0.187 | 0.358 | 0.613 | 0.839 | 0.956 | 0.987 |

For significance level equals to  , the probabilistic forecast form 2 test should be considered successful, if the following inequality is satisfied:

< <.                                                                                                (5.15)

As well as for deterministic forecasting method, probabilistic forecasting method applicability assessment is based on comparing such forecast results with alternative climatic or inertial forecasts. So, alternative probabilistic forecasts must be constructed using the methods described in the previous section.

If the relation between probabilistic and test forecast series is closer than that between alternative and test series, the examined forecast methodology should be considered applicable for probabilistic forecasting.

As demonstrated in [5], statistical procedures of such comparison are quite time-consuming. However, probabilistic forecast applicability assessment can be substantially simplified using deterministic forecast applicability criteria presented in section 3.3, with allowance for specific features of each method.

1. In case of using method 1, forecast error estimates  and  must be compared.

2. In case of using method 2, the estimate  must be compared with alternative forecast error estimate .

3. In case of using method 3, hydrologic parameter logarithm forecast error estimate  must be compared with alternative forecast error estimate .

If a forecasting method presented in previous section can be applied for deterministic forecasting, it is also applicable for probabilistic forecasting.

Chapter 6.  Probabilistic forecast examples

6.1 Long-range probabilistic forecast example

Forecast of mean April inflow volumes into Sayano–Shushenskoe reservoir (lead time is 35 days) is presented as the example of long-term probabilistic forecasting method (see sections 2.3, 3.2, 3.4, and 4.2). An empirical formula is used for reservoir inflow  forecasting; predictors are: inflow volume averaged over the last 10 days of March and forecast of mean air temperature over the first 10 days of April for Kyzyl weather station. The parameters of the formula were estimated using the least squares method; series length of forecast value and its predictors is = 25. Input data are given in table 2.1 (see section 2.3).

The series ,…,  of daily forecast error  was used for development and verification of long-range probabilistic forecast for April inflow volumes into Sayano–Shushenskoe reservoir. The values  were calculated as , ,   for methods 1, 2, and 3, respectively. Anderson test showed no statistically significant autocorrelation for series ,…,   for any method of calculating forecast errors. Method 1 applicability test showed the following.

1. Correlation coefficient estimate between squared forecast errors  and forecast

values calculated using formula (5.10) is 0,39. While  = 5 %, the inequality (5.11) is not satisfied for any month and the correlation is statistically significant according to Pitman criterion. Thus, conditional expected value of squared forecast error increases with increasing forecast value

2. With series length = 25 taken into account, Pearson goodness-of-fit test was used for testing the hypothesis that forecast errors are normally distributed, with zero mean and standard deviation estimate  = 162 . While = 1 and numeric axis is divided into  = 7 equiprobable intervals, the measure , defined by formula (5.12), is equal to 12.21. While significance level  = 5 %, critical quantile of chi-squared distribution  for =12.21 is equal to 11.07. Thus, the inequality (5.12) is not satisfied and method 1 normal probability distribution hypothesis must be rejected. Thus, method 1 is rejected due to the fact that its applicability conditions are not satisfied.

Method 2 applicability test showed the following.

1. Correlation coefficient estimate between squared relative forecast errors  and forecast values  calculated using formula (5.10) is -0,13. While significance level  = 5 % the inequality (5.11) is satisfied. Thus, according to Pitman criterion, this correlation is not statistically significant. Thus, relative forecast error variance is independent of forecast value.

2. Pearson goodness-of-fit test was used for testing the hypothesis that forecast errors are normally distributed, with zero mean and standard deviation estimate = 0.21. While = 1 and numeric axis is divided into  = 7 equiprobable intervals, the measure  , defined by formula (5.12), is equal to 6.44. While significance level  = 5 %, critical quantile of chi-squared distribution  for =12.21 is equal to 11.07. Thus, the inequality (5.12) is satisfied and  method 1 normal probability distribution hypothesis can be accepted.

Thus, the method 2 applicability conditions are satisfied and this method can be used for long-range probabilistic forecasting of April inflow volume into Sayano–Shushenskoe reservoir.

Conditional probability distribution function and conditional frequency curve of mean April inflow volume into Sayano–Shushenskoe reservoir,  =  , depending on forecast value  are defined by formulas (5.4) and (5.7) while = 0,21. Conditional frequency values  are presented in table 6.1 for low, mean and high forecast values (400, 650, and 900 ), respectively, and different frequency values  [5].

Table 6.1

Conditional frequency curve of mean April inflow volume into Sayano–Shushenskoe reservoir

| , % | 5 | 10 | 25 | 50 | 75 | 90 | 95 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ,= 400 | 288 | 310 | 350 | 400 | 458 | 517 | 556 |
| ,= 650 | 468 | 503 | 568 | 650 | 744 | 840 | 903 |
| ,= 900 | 648 | 697 | 786 | 900 | 1030 | 1163 | 1251 |

Conditional probability  that observed value  lies in the interval (492; 766), defined for each year depending on forecast value , is the example of additional probabilistic forecast form 1. The interval limits,  = 492 and  = 766 , correspond to 25% and 75% probability of exceedance of unconditional probability distribution of observed reservoir inflow values , respectively. Thus, the unconditional probability that the observed value  lies in the interval (492; 766) is equal to 50%. For each forecast value , conditional probability  was computed using conditional probability distribution function  defined by formula (5.4). The yearly values of probability  and index  are presented in table 6.2. If observed reservoir inflow value is within interval (492; 766), the index  is equal to 1; otherwise, it is equal to 0.

Table 6.2

Probabilistic reservoir inflow forecast characteristics (Sayano–Shushenskoe reservoir), additional forms 1 and 2

| Год |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1979 | 0,23 | 0 | 372 | 487 |
| 1980 | 0,01 | 0 | 267 | 350 |
| 1981 | 0,43 | 0 | 691 | 905 |
| 1982 | 0,69 | 0 | 586 | 767 |
| 1983 | 0,52 | 0 | 439 | 574 |
| 1984 | 0,14 | 0 | 345 | 452 |
| 1985 | 0,69 | 1 | 494 | 647 |
| 1986 | 0,73 | 1 | 520 | 681 |
| 1987 | 0,71 | 1 | 567 | 743 |
| 1988 | 0,66 | 1 | 480 | 628 |
| 1989 | 0,46 | 1 | 678 | 888 |
| 1990 | 0,56 | 0 | 449 | 588 |
| 1991 | 0,73 | 1 | 519 | 680 |
| 1992 | 0,65 | 1 | 606 | 794 |
| 1993 | 0,21 | 0 | 785 | 1028 |
| 1994 | 0,55 | 1 | 645 | 844 |
| 1995 | 0,22 | 0 | 781 | 1023 |
| 1996 | 0,14 | 0 | 346 | 453 |
| 1997 | 0,15 | 0 | 820 | 1073 |
| 1998 | 0,59 | 1 | 632 | 827 |
| 1999 | 0,69 | 1 | 582 | 762 |
| 2000 | 0,47 | 1 | 676 | 885 |
| 2001 | 0,39 | 0 | 706 | 925 |
| 2002 | 0,37 | 1 | 714 | 935 |
| 2003 | 0,72 | 1 | 561 | 735 |

A measure , defined by formula (5.14), was computed to test the additional probabilistic forecast form 1. While = 25, = 1, and significance level  = 5 %, critical quantile of chi-squared distribution  for =23.08 is equal to 36.41. Thus, the inequality (5.14) is satisfied and the test results should be considered successful.

A confidence interval , defined for each year depending on reservoir inflow forecast value , is an example of additional probabilistic forecast form 2. The probability that expected value  lies in that range , is equal to 50%. Yearly confidence limits were defined using conditional frequency curve  for  = 75 % and  = 25 % (table 6.2).

The relative frequency  that yearly forecast values lie in the range  is equal to 60%. While significance level  = 5 %, = 25, and  = 50 %, the confidence limits are  = 41,7 % and  = 76, 4 % Thus, the inequality (5.15) is satisfied and the test results of probabilistic forecast form 2 should be considered successful.

Alternative climatic forecast and unconditional probability distribution of observed reservoir inflow values were used to estimate the applicability of long-range probabilistic forecasting of April inflow volume into Sayano–Shushenskoe reservoir. As mentioned in section 4.2, that distribution can be considered as three-parameter gamma distribution, where = 652 cubic meters per second, = 0,35, and  = 3.

According to  recommendations in section 5.2, the applicability of proposed probabilistic forecasting method can be tested using the criteria presented in section 3.3. As method 2 was used for probabilistic forecasting of inflow volume into Sayano–Shushenskoe reservoir, the estimate  must be compared with a similar estimate  of climatic forecast error. Relative root mean square forecast errors are = 0.21 and = 0.34, respectively. The correlation coefficient r between relative forecast errors is 0.65. The measure B defined by (3.4) for criterion 2 is 9.01. While significance level  = 5 %, critical quantile of chi-squared distribution  for =9.01 is equal to 3.84. Thus, the inequality (3.4) is satisfied and the methodology should be considered quite good and applicable for long-range probabilistic forecasting of April inflow into Sayano–Shushenskoe reservoir [5].

6.2 Short-range probabilistic forecast example

One-day ahead forecasting of daily stream flow for the Sochi River at Sochi is presented as example of short-term probabilistic forecast method (see sections 2.4, 3.2, 3.4, and 4.2). Regional snowmelt and rainfall runoff model is used for daily streamflow forecasting. The model parameters were estimated for each month from daily hydrometeorological observation series and daily weather forecast series (series length = 508 - 558).

The series ,…,  of daily forecast error  was used for development and verification of short-range probabilistic daily stream flow forecast method for the Sochi River. The values  were calculated as , ,   for methods 1, 2, and 3, respectively.

Anderson test showed no statistically significant autocorrelation for series ,…,  for any method of calculating forecast errors for all months except May and June. To eliminate autocorrelation, the 2nd, 4th, 6th, etc. series members were removed from the series. Truncated series for May and June are long enough to carry out further analysis. Truncated series length  = 279 (May) и  = 270 (June) is quite satisfactory for further analysis.

The method 1 applicability test showed that coefficient estimates of correlation between squared forecast errors  and forecast values calculated using (5.10) vary from 0.29 to 0.52 for different months. While  = 5 %, the inequality (5.11) is not satisfied for any month and the correlation is statistically significant according to Pitman criterion. Thus, for every month, forecast error variance increases with increasing forecast value. Thus, the method 1 is rejected as the first condition of its applicability is not satisfied.

The method 2 applicability test showed that coefficient estimates of correlation between squared forecast errors   and forecast values calculated using (5.10) vary from 0.29 to 0.52 for different months. While  = 5 %, the inequality (5.11) is not satisfied for any month and the correlation is statistically significant according to Pitman criterion. Thus, for every month, forecast error variance increases with increasing forecast value. Thus, the method 2 is rejected as well as the first condition of its applicability is not satisfied.

The method 3 applicability showed the following.

1. Coefficient estimates of correlation between squared forecast errors   and forecast values calculated using (5.10) vary from -0.03 to 0.06 for different months. While  = 5 %, the inequality (5.11) is satisfied for every month. Thus, according to Pitman criterion, this correlation is not statistically significant. Thus, in this case, forecast error variance is independent of forecast value.

2. Forecast method 3 is based on the assumption that Sochi River streamflow logarithm forecast errors have normal probability distribution with zero mean and standard deviation estimates, , for each month. The estimates  are presented in table 6.3.

Table 6.3

Series length  and estimates  : streamflow logarithm forecast for the Sochi River at Sochi

|  | I | II | III | IV | V | VI | VII | VIII | IX | X | XI | XII |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 554 | 508 | 526 | 540 | 279 | 270 | 558 | 526 | 540 | 558 | 540 | 558 |
|  | 0,43 | 0,37 | 0,37 | 0,22 | 0,37 | 0,44 | 0,61 | 0,87 | 0,90 | 0,99 | 0,66 | 0,52 |

With monthly series length taken into account, the above assumption was tested using the Cramér–von Mises–Smirnov criterion. The values  calculated for each month using formula (5.13) vary from 0.11 to 0.26. For any feasible significance level , the values  do not exceed extreme values  presented in table 5.2. Thus, the hypothesis that the streamflow logarithm forecast errors are normally distributed can be accepted for all months. Figure 6.1 demonstrates that the graph of Laplace distribution function  (see formula (5.3)) coincides quite well with the graph of empirical distribution function with normalized arguments , = 1,...,    (for November) [6].

Figure 6.1. Empirical (red dots) and normal (blue solid line) probability distribution of streamflow logarithm forecast errors for the Sochi River at Sochi

Thus, as all applicability conditions are satisfied, method 3 can be used for probabilistic short-range streamflow forecasting for the Sochi River at Sochi. Conditional probability distribution function  and conditional frequency curve  are defined for each month by formulas (5.6) and (5.7), substituting the estimates  from table 6.3.

Due to flood hazard in Sochi region, probabilistic forecasting of stream flow (additional form 1) is of greatest practical interest. According to different categories of flood danger, municipal authorities established three critical (threshold) stream flow values  for the Sochi River at Sochi.

Table 6.4

Critical (threshold) stream flow values  for the Sochi River at Sochi

| Category of flood danger |  |
| --- | --- |
| Storm alert | 300 |
| Adverse event | 500 |
| Dangerous event | 640 |

Depending on stream flow forecast , conditional probability  of exceeding critical streamflow  during next 24 hours is defined by:

= 1 –.					                                       (6.1)

Figure 6.2 shows the function  for the Sochi River at Sochi for November, the most flood-hazardous period for this region [6].

Figure 6.2. Forecast probability function  for the Sochi River at Sochi (November)

References

- American Society of Civil Engineers,1996: Hydrology Handbook, Second Edition, ASCE Manual and Reports on Engineering Practice No. 28, New York, 784 pp.

- Anderson J.L. A method for producing and evaluating probabilistic forecasts from ensemble model integrations // Journal of Climate. – 1996. – № 9. – pp. 1518–1530.

- Asarin A.E., Khristoforov A.V. and others. Calculations in Water Resource Management. - Moscow State University, 2012. – 142 pp.

- Beven K., Freer J. Equifinality, data assimilation, and uncertainty estimation in mechanistic modelling of complex environmental systems using the GLUE methodology // Journal of Hydrology. – 2001. – Vol. 249. – pp. 11–29.

- Borsch S.V., Khristoforov A.V. Hydrologic flow forecast verification. Moscow, Proceedings of Hydrometcentre of Russia, Special Issue 355, 2015, 198 pp.

- Borsch S.V., Simonov Y.A., Khristoforov A.V. Flood forecasting and early warning system for rivers of the Black Sea shore of Caucasian region and the Kuban River basin. Moscow, Proceedings of Hydrometcentre of Russia, Special Issue 356, 2015, 247 pp.

- Brier G.W. Verification of forecasts expressed in terms of probability // Mon. Wea. Rev. – 1950. – Vol. 78. – p. 1–3.

- Buizza R., Hollingsworth A., Lalaurette F., Ghelli A. Probabilistic Predictions of Precipitation Using the ECMWF Ensemble Prediction System // Weather and Forecasting. – 1999. – Vol. 14. – p. 168–189.

- Burman P., Chow E., Nolan D. A cross-validatory method for dependent data. Biometrika, 1994, № 81. 351–358 pp.

- Carpenter T.M., Georgakakos K.P., Sperfslage J.A. Distributed Hydrologic Modeling for Operational Use. 1999, 224 pp.

- Efron B. The Jackknife, the Bootstrap and Other Resampling Plans. Society for Industrial and Applied Mathematics, 1982. – 92 pp.

- Georgakakos K.P., Seo D.J., Gupta, H., Schake J., Butts M.B. Characterizing Stream flow Simulation Uncertainty through Multimodel Ensembles // Journal of Hydrology. – 2004. – Vol. 298.– pp. 222-241.

- Guide to Hydrological Forecasting. Issue 1. Long-range forecasts of hydrological regime of rivers and reservoirs. Leningrad, Gidrometeoizdat, 1989, 356 pp.

- Guide to Hydrological Forecasting. . Issue 2. Short-range forecasts of river streamflow and water stage. Leningrad, Gidrometeoizdat, 1989, 245 pp.

- Guide to Hydrological Forecasting. Issue 3. River and reservoir ice forecasts. Leningrad, Gidrometeoizdat, 1989, 166 pp.

- Guide to Hydrological Practices. Volume I. Hydrology – From Measurement to Hydrological Information // World Meteorological Organization - No. 168, 2008. - 296 pp.

- Guide to Hydrological Practices. Volume II. Management of Water Resources and Application of Hydrological Practices // World Meteorological Organization - No. 168, 2009. – 302 pp.

- Instruction to forecasting service. Section 3. Part 1. Forecasting of land hydrological regime. Leningrad, Gidrometeoizdat, 1962, 193 pp.

- Jolliffe I.T., Stephenson, D.B. Forecast Verification. – Wiley, 2003. – 240 pp.

- Kendall M. G. The advanced theory of statistics. Vol. I. Distribution theory.  Charles Griffin & Company Limited, 1945. – 457 pp.

- Kendall M. G., Stuart A. The advanced theory of statistics. Vol. II. Inference and relationship.  Charles Griffin & Company Limited, 1967. – 684 pp.

- Kendall M. G., Stuart A., Ord J.K The advanced theory of statistics. Vol. III. Design and Analysis and Time- Series.  John Wiley and Sons, 1984. – 565 pp.

- Khristoforov A.V. Reliability of river flow calculations. Moscow, Izdatelstvo MGU (Moscow State University), 1993, 166 pp.

- Khristoforov A.V. Theory of random processes in hydrology. Moscow, Izdatelstvo MGU (Moscow State University), 1994, 139 pp.

- Krzysztofowicz R. The case for probabilistic forecasting in hydrology // Journal of Hydrology. –2001. - №249. pp. 2–9.

- Management Overview of Flood forecasting Systems (MOFFS): Version 3. Geneva: HWR, 1995. – 26 pp.

- Manual on Flood Forecasting and Warning. // World Meteorological Organization - No. 1072, 2011. –138 pp.

- Lambert A.O. Development and Use of the Management Overview of Flood Forecasting Systems (MOFFS) / Technical Reports in Hydrology and Water Resources No. 55. Geneva: HWR, 1994. – 23 pp.

- Langford J. Quantitatively Tight Sample Complexity Bounds. — Carnegie Mellon Thesis, 2002. - 124 pp.

- Nash J. E., Sutcliffe J. V. River flow forecasting through conceptual models. Part 1 – A discussion of principles // Journal of Hydrology. – 1970. – Vol. 10. – pp. 282–290.

- National Research Council, 1988: Estimating probabilities of extreme floods, National Academy Press, Washington, D.C., 141 pp.

- National Weather Service River Forecast Verification Plan. Report of the Hydrologic Verification System Requirements Team. U.S. Department of Commerce. National Oceanic and Atmospheric Administration. – 2006. – 44 pp.

- Nijkamp P. Cost – Benefit Analysis and Water resource Management. Amsterdam, 2005. - 312 pp.

- Predictability of Weather and Climate / Ed. By T. Palmer and R. Hagedorn. Cambridge University Press, 2006. – 635 pp.

- Statistical methods in the Atmospheric Sciences. Edited by R. Dmowska, D. Hartman, H.T. Rossby. INTERNATIONAL GEOPHYSICS SERIES, Volume 100, 2011. -  676 pp.

- Tukey J.W. Exploratory Data Analysis. Reading, Mass, Addison-Wesley, 1977. – 688 p.

- Wang Juemou. Methods of Verification of Hydrological Forecasts. / Technical Reports in Hydrology and Water Resources No. 44. Geneva: HWR, 1994. - 15 pp.

- Welles E. Verification of river stage forecasts: Dissertation. University of Arizona. – 2005. – 157 pp.

- Wilks D.S. Statistical methods in the atmospheric sciences. 3rd ed. – (International geophysics series, vol. 100). Academic Press, 2011. – 676 pp.

- World Meteorological Organization. Intercomparison of Conceptual Models Used in Operational Hydrological Forecasting // Operational Hydrology Report No. 7, WMO - No. 429, Geneva, 1987. – 172 pp.

- World Meteorological Organization. Manual on Flood Forecasting and Warning // WMO - No. 1072. Geneva, 2011. – 138 pp.

- World Meteorological Organization. Simulated Real-time Intercomparison of Hydrological Models // Operational Hydrology Report No. 38, WMO–No. 779. Geneva, 1991. – 241 pp.

- Yen B.C. Stochastic and Risk Analysis in Hydraulic Engineering. Water Resources Publications, Littleton, Col., 1986. - 278 pp.

- Yokum J.T., Armstrong J.S. Beyond Accuracy: Comparison of Criteria Used to Select Forecasting Methods. International Journal of Forecasting, 1995, № 11. 591-597 pp.

- Zhang Z., Smith M., Koren V., Reed S., Moreda F., Kuzmin V., Anderson R.

A study of the relationship between rainfall variability and the improvement of

using a distributed model // Eds. Y. Chen, K. Takara, I. D. Cluckie, H. F. de

Smedt, GIS and Remote Sensing in Hydrology, Water Resources and Environment,

IAHS Publ. No. 289, 2004.