Progress in implementation of new verification procedures at Russian Hydrometeorological Research Centre

# 1. What has been done

## In the end of 2011 and the beginning of 2012, the new procedure of verification against analyses has been implemented that follows Annex 2 to draft Recommendation 4.4/1. The forecasts of global SL-AV model are verified.  An area-weighting is used for interpolating both forecast fields (regular 0.9°x0.72° grid) and analysis fields (regular 1.25°x1.25° grid) on a regular 1.5°x1.5° grid. The new 1.5 degrees climatology from ERA-Interim is used in calculating anomalies correlation.

## Forecast lead times: currently

## -24h, 48h, 72h, 96h, 120h for forecasts initiated at 00 UTC

## - 24h, 48h, 72h, 96h, 120h, 144h, 168h, 192h, 216h , 240h for forecasts initiated at 12 UTC

## Areas for verification:

## - Northern hemisphere extra-tropics (20°N - 90°N, all longitudes)

## - Southern hemisphere extra-tropics (90°S - 20°S, all longitudes)

## - Tropics (20°N‒20°S, inclusive, all longitudes)

## - Some part of Europe/North Africa (25°N–70°N 10°W–28°E)

## - Asia (25°N–65°N 60°E–145°E)

## - Russia (40°N–65°N 20°E–170°E)

## - Northern polar area (60°N‒90°N, all longitudes)

## - Southern polar area (90°S‒60°S, all longitudes)

## Parameters for all areas:

## -Mean sea-level pressure

## -Geopotential height at 850, 500 and 250 hPa

## -Temperature at 850, 500 and 250 hPa

## -Wind at 850, 500 and 250 hPa

## Scores:

## -Mean error

## -Root mean square (rms) error

## -Mean absolute error

## -Correlation coefficient between forecast and analysis anomalies (not for wind)

## - Correlation coefficient between forecast and analysis tendencies (not for wind)

## - S1 score (not for wind)

So far, we are running both new and old verification systems, and send the scores in old format calculated using the old system.

# 2. Future work

## Implementation of a procedure which will form daily reports in a new format according to new standard.  Expected to be ready by July 01, 2012.

## More forecast lead times (12, 36 hours etc)

## Verification against radiosondes

## Verification of relative humidity against analyses – awaits operational implementation of 3D-Var (later this year).