| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS OPAG on DPFS MEETING THE CBS EXPERT TEAM ON ENSEMBLE PREDICTION SYSTEMS (ET-EPS) Geneva, Switzerland, 14-18 November 2011 |  | DPFS/CBS/ET-EPS/Doc. 4.2(4) (11.11.2011) _______ Agenda item : 4.2 ENGLISH ONLY |
| --- | --- | --- |

Regional EPS progress at CMA

(Submitted by Jing Chen)

##### Summary and purpose of document

This document provides an update on development of the CMA  global ensemble prediction system since the last meeting in 2009

##### Action Proposed

The meeting is invited to note the recent developments

Operational REPS

The development of the regional ensemble prediction system in CMA started in 2006, and it was initially aimed to participate the WMO B08RDP project. This system has been upgrading after 2008, and been operationally running since June 2011. The REPS was based on the WRF-ARW model with the horizontal resolution of 15km and 35 vertical levels, and its ensemble size was 15. The BGM was used to produce the initial perturbations, and the lateral boundary conditions were provided by the he BV-based GEPS in CMA. The multi-physics method was used to represent the model error, and specifically was focused on the combination of cumulus convective parameterizations, boundary layer schemes and land surface schemes.

The REPS has experienced the transition from the research tests to operation during 2008 to 2010, the major upgradations were the expansion of horizontal domain to cover the entire China, and the inclusion of surface parameter perturbations in the BGM cycles. Table 1 gives the technical progress of REPS. The upgraded REPS has been running in real-time mode twice daily since July 2010, and the system was stable enough and has been declared as re-operational status in November 2010.  The flow chart of REPS is shown in figure 1.

Table 1   Technical progress for NMC/CMA REPS

|  | 2006 | 2007 | 2008 | 2010 |
| --- | --- | --- | --- | --- |
| Model | WRF-ARW V2.1 15km ; 35 levels (B08RDP target domain ) | WRF-ARW V2.1 15km ; 35 levels (B08RDP target domain ) | WRF-ARW V2.2 15km ; 35 levels (B08RDP target domain ) | WRF-ARW V2.2 15km ; 35 levels (extending domain ) |
| Member size | 15 | 15 | 15 | 15 |
| IC | WRF-3DVAR | WRF-3DVAR | WRF-DVAR (with more observation assimilated) | WRF-DVAR (with more observation assimilated) |
| IC pertur. | BGM | BGM | BGM | BGM perturbed surface parameters |
| Model pertur. | Multi-physics | Multi-physics | Multi-physics (optimized) | Multi-physics (optimized) |
| LBCs | GEPS with OI system | GEPS with OI system | GEPS with SSI 3D-VAR system. | GEPS with SSI 3D-VAR system. |

  - Operational products

Since June 2011, the REPS ensemble products have been distributed to all provincial level meteorological services as guidance products, and these products include two types of parameters: (1) the ensemble mean/spread and probabilistic products for surface parameters (precipitation accumulated over 3h, 6h,12h and 24h, 2m-temperature, 10m-wind et al. ); (2) two convective risk probabilistic products. Table 2 gives the list of distributed products.  In addition, REPS at CMA is also a data provider to the TIGGE-LAM.

Figure 1 The flowchart of REPS at CMA .

Table 2  The lists of distributed REPS products

| Names | Variables | REPS products | Thresholds |
| --- | --- | --- | --- |
| RAIN_3HR | 3h accum. Precip | Ensemble mean; Probabilistic map. | >0.1,>3,>10,>20,>50(mm) |
| RAIN_6HR | 6h accum. Precip |  | >0.1,>4,>13,>25,>60(mm) |
| RAIN_12HR | 12h accum. Precip. |  | >0.1,>5,>15,>30,>70(mm) |
| RAIN_24HR | 24h accum. precip. |  | >0.1,>10,>25,>50,>100(mm) |
| CIN | Convective inhibition | Ensemble mean |  |
| T2M | 2m temp. | Ensemble mean Probabilistic map. | >35 ,>38 cesuls degree |
| CAPE | Convective available potential energy | Ensemble mean Probabilistic map. | >500、1000、1500、2000J/kg |
| UV10M | 10m wind speed | Ensemble mean Probabilistic map. | >8, 12,16m/s |
| RISK_PRB | Convective risk prob. | Prob. | Prob. |

  - The verification of REPS

Before the operational running, the general objective verification and case evaluation has been shown that added values of the REPS for the forecast of precipitation forecast and other severe weather in the short-range are considerable.  Figure 1 shows the probabilistic forecasts for heavy rainfall case on 4 Aug. 2011 in the Chongqing

Figure 1  The probabilistic forecast for precipitation greater than 25 mm/24  and 50mm/24h. Top panel is observation

The REPS research plan

The next generation of operational model GRAPES (The Global/Regional Assimilation and Prediction System) with 4D-VAR data assimilation system is developing in CMA, therefore the singular vector (SV) method is designed to be used as initial perturbations for GRAPES-based GEPS and REPS in the future. Currently, the research for the development of SV-based GEPS with GRAPES is undergoing