Annual WWW Technical Progress Report

on the Global Data Processing System 1999

Japan Meteorological Agency (JMA)

1.  Summary of highlights

- Experimental operations of medium-range ensemble prediction began on 16 March 1999. A nine-member ensemble of eight-day forecasts is produced every day with a T63L30 version of JMA's Global Spectral Model (GSM). Perturbations in the initial conditions are generated by a breeding method.

- The coverage area of the storm surge model was extended over Tohhoku and Hokuriku districts (northern parts of Japan) in July 1999 .

- In August 1999, JMA started to issue the monthly ENSO outlook based on the model results for end users.

- A non-local planetary boundary layer scheme was implemented in the Regional Spectral Model (RSM) and the Mesoscale Model (MSM) on 29 November 1999. The latter model is a 10 km resolution version of RSM and has been experimentally operated twice a day to produce 12-hour forecasts since 1 March 1998.

- The physics package of GSM was updated on 7 December 1999. The new package includes a prognostic cloud water scheme, effects of orographic updraft and turbulence in the planetary boundary layer on cumulus convection, and direct effects of aerosol on radiation.

- Production of one-month forecast GPV products in GRIB format started on 1 December 1999 based on the operational ensemble forecasting system.

2.  Equipment in use at the Global Data Processing System (GDPS) Center in JMA

The features of major components of the Numerical Analysis and Prediction System (NAPS) are listed in Table 1.

Table 1   Major features of NAPS computers

Supercomputer				HITAC S-3800/480

Number of vector processors		4

Number of scalar processors		4

Peak vector performance		32 Gflops

Memory capacity			2 GB

Extended memory capacity		12 GB

Data transfer rate			4 GB/s

Disk storage capacity		205 GB

Automated CMT library capacity	2.1 TB(400MB/volume)

Peripheral equipment 		CMT(12 drives), LBP

Operating system			VOS3/AS

Meteorological message handling server	Hitachi unix server 3500

CPU cycle time			10 ns

Memory capacity			256 MB

Data disk storage capacity		2 GB x 2

Peripheral equipment		DAT, FPD

Workstation for NWP

Very short-range forecast ws			Hitachi unix ws 3050RX

Memory capacity			112 MB

CPU cycle time			10 ns

Disk storage capacity		2 GB

Peripheral equipment		DAT, FPD, LBP

Graphic processing ws			Hitachi unix ws 3050RX

Memory capacity			96 MB

CPU cycle time			10 ns

Disk storage capacity		2 GB

Peripheral equipment		DAT, FPD, LBP

Backup & Maintenance ws 			Hitachi unix ws 3050RX

Memory capacity			128 MB

CPU cycle time			10 ns

Disk storage capacity		3 GB

Peripheral equipment		DAT, FPD, LBP, MO(128MB)

General purpose server			Hitachi total management server

Instruction rate			18 MIPS(estimated)

Memory capacity			64 MB

Disk storage capacity		27 GB

Peripheral equipment		CMT(8 drives), MT(2 drives), LBP(4), LP

Operating system			VOS3/AS

3.  Data and products in use from GTS

3.1 Observations

The following observation reports are used in the data assimilation:

Table 2   Number of used observation reports

SYNOP/SHIP	32500/day

TEMP-A/PILOT-A	1700/day

TEMP-B/PILOT-B	1700/day

TEMP-C/PILOT-C	1100/day

TEMP-D/PILOT-D	1000/day

AIREP/AMDAR	33600/day

BUOY		6600/day

SATOB (SST)	7900/day

SATEM-A	9500/day

SATEM-C	9200/day

SATOB (WIND)	53100/day

TOVS		12300/day

PROFILER	600/day

BATHY/TESAC	5500/month

ERS		200/day

3.2 GRIB products

Following model products are also used. GRIB KWBC is used for preparation of WAFS products and the other ones are for internal reference and monitoring.

GRIB KWBC

GRIB ECMF

GRIB AMMC (under test)

4.  Data input system

Data input is fully automated with the exception of the manual input of typhoon position, size and intensity data. They are used to generate typhoon bogus data for global, regional and typhoon analyses.

5.  Quality control system

Stage 1 Decoding

All the code forms of messages are checked against the WMO international code forms. When a form error is detected, some procedures are applied in order to extract as much information as possible.

Stage 2 Internal consistency check

Checks of climatological reasonability are performed for all types of data. The data enlisted as problematic data in the "black list" are rejected. Contents of the "black list" are occasionally revised based on results of non real-time quality control.

Consistency of consecutive positions is checked for reports from mobile stations such as ships, drifting buoys and aircraft.  Consistency of consecutive reports and that among elements within a report are also checked for every surface station.

The vertical consistency is examined for TEMP and PILOT data using all parts of reports. The check items are:

(1) Icing of instruments,

(2) Temperature lapse rate,

(3) Hydrostatic relationship,

(4) Consistency among data at mandatory levels and those at significant levels,

(5) Vertical wind shear.

Bias correction is applied to TEMP data which have large persistent biases from the first guess fields. Another bias correction scheme which checks consistency between the surface pressure observation and the sea surface pressure has been introduced since August 1998.

Checks of lapse rate for SATEM data are also performed using the mean virtual temperature estimated from the thickness.

Stage 3 Quality control with reference to the first guess

Gross error and spatial consistency are evaluated against the first guess in order to remove erroneous observations. The difference (D) of the observation value from the first guess value is compared with tolerance limits CP and CR. CP is an acceptable limit and CR is a rejection limit. When D is smaller than or equal to CP, the datum is accepted for use in the objective analysis. When D is greater than CR, it is rejected. When D is smaller than or equal to CR and greater than CP, the datum is further checked by interpolating the neighboring data to the location of the datum. If the difference between the datum and the interpolated value is not within a reasonable tolerance CS, the datum is rejected.

These three tolerance limits vary according to the local atmospheric conditions which can be estimated by the first guess field. They are small if time tendency and horizontal gradient are small in the first guess field. The scheme is called "Dynamic QC" and is based on the idea that forecast errors would be small if the area is meteorologically calm and large if it is stormy.

Duplicate observation reports are frequently received through different communication lines. The most appropriate single report is chosen from these duplicate reports considering results from quality control of these reports.

All information on the quality of observational data obtained during the quality control procedure is archived in the Comprehensive Database for Assimilation (CDA). The CDA is used for non real-time quality control and global data monitoring activities.

6.  Monitoring of the observing system

The non real-time quality monitoring of observations is carried out using observational data, real-time quality control information and the first guess archived in the CDA. The quality monitoring is made according to:

(1)	Compilation of observational data rejected in the real-time quality monitoring;

(2)	Calculation of statistics on the difference between observations and first-guess;

(3) 	Statistical comparison of satellite data with collocated radiosonde data.

The above statistical information is effective in estimating systematic errors of observational data and also helpful to identify stations reporting suspect observations. If a station continuously reports suspect data for a long time, the data from the station are not used in the analysis.

The quality and availability of observational data are regularly issued as a monthly report entitled "JMA/NPD Global Data Monitoring Report". The statistics presented in the report are made according to the recommended procedures for the exchange of monitoring results by the Commission for Basic Systems (CBS). The report is sent to major Global Data Processing System (GDPS) centers as well as to the WMO Secretariat.

The RSMC Tokyo has been acting as a lead centre for monitoring quality of land surface observations in Region II since March 1991. The statistical characteristics of availability and quality for sea level pressure observations of land surface stations in Region II are published in the semiannual report entitled "Report on the Quality of Surface Observations in Region II".

JMA also acts as a Principal Meteorological and Oceanographic Center (PMOC) of Data Buoy Cooperation Panel (DBCP). Quality of meteorological data reported from ocean data buoys is monitored by time sequence maps for every observation element and comparing them with the first guess field of the JMA Global Data Assimilation System. Sea surface and subsurface temperatures reported from buoys are also examined against climatic values and oceanographic analysis by JMA. Information on the buoys transmitting inferior quality data is sent to DBCP and other PMOCs over the Internet.

7.  Forecasting system

JMA operationally performs three kinds of objective atmospheric analyses for the global, regional and typhoon forecast models. All of them employ three-dimensional Optimal Interpolation (3D-OI) scheme on model coordinates for the analysis of surface pressure, geopotential height, vector winds, and relative humidity.

A two-dimensional function fitting method is used for temperature and height analyses above 10hPa level to prepare initial conditions for dynamical one-month forecasts.

Global analyses at 00UTC and 12UTC are performed twice. An early run analysis with a short cut-off time is to prepare initial conditions for operational forecast, and a cycle run analysis with a long cut-off time is to keep quality of global data assimilation system. The first analysis is not performed at 06 and 18UTC.

The specifications of the atmospheric analysis schemes are listed in Table 3.

Daily global SST analysis is described in Table 4.

Table 3   Specifications of operational objective analysis

Cut-off time

(global)			2.5 and 3 hours for early run analyses at 00 and 12UTC,

13, 7.5, 12, 6.5 hours for cycle run analyses at 00, 06, 12, 18 UTC.

(regional)		3 and 3.5 hours for analyses at 00 and 12UTC

(typhoon)		1.5 hours for analyses at 06 and 18UTC

(upper stratospheric)	same as the global analysis

Initial Guess

(global)			6-hour forecast by GSM

(regional)		12-hour forecast by RSM

(typhoon)		6-hour forecast by GSM

(upper stratospheric)	analysis 6 hours before

Grid form, resolution and number of grids

(global)			Gaussian grid, 0.5625 degree, 640x320

(regional)		Lambert projection, 20km at 60N and 30N, 257x217, grid point

(1,1) is at north-west corner and (165,155) is at (140E, 30N)

(typhoon)		same as global analysis

(upper stratospheric)	latitude-longitude, 2.5 degree, 144x73

Levels

(global)			30 forecast model levels up to 10 hPa + surface

(regional)		36 forecast model levels up to 10 hPa + surface

(typhoon)		same as global analysis

(upper stratospheric)	7, 5, 3, 2, 1, 0.4hPa

Analysis variables

Wind, geopotential height (surface pressure), relative humidity and temperature

(Temperature is analyzed but not used as the initial condition for the forecast.)

Methodology

Multivariate three-dimensional optimum interpolation (3D-OI) scheme on model levels is employed for the analysis of geopotential height and wind except for the tropical region (15N-15S), where univariate OI analysis is applied. Geostrophic relation between geopotential height and wind is relaxed between 15N(S)-25N(S). Univariate 3D-OI scheme is employed for the analysis of temperature and relative humidity.

A two-dimensional function fitting method is used for upper stratospheric analysis.

Data Used

SYNOP, SHIP, BUOY, TEMP, PILOT, Wind Profiler, AIREP, SATEM, TOVS, SATOB, Australian PAOB, VISSR digital cloud data from the Geostationary Meteorological Satellite (GMS) and surface wind data by Scatterometer on ERS2.

Typhoon Bogussing

For a typhoon over the western North Pacific, typhoon bogus data are generated to represent its accurate structure in the initial field of forecast models. They are made up of artificial geopotential height and wind data around a typhoon. The structure is asymmetric.  At first, symmetric bogus data are generated automatically from the central pressure and 30kt/s wind speed radius of the typhoon. The asymmetric bogus data are generated by retrieving asymmetric components from the first guess field. Those bogus profiles are implanted into the first guess fields.

Initialization

Non-linear normal mode initialization with full physical processes is applied to the first five vertical modes.

Table 4   Specifications of SST analysis

Methodology		two-dimensional Optimal Interpolation scheme

Domain and Grids		global, 1x1 degree equal latitude-longitude grids

First guess		mean NCEP OI SST (Reynolds and Smith, 1994)

Data used			SHIP, BUOY and NOAA AVHRR SST data

observed in past five days

Frequency			daily

JMA runs a Global Spectral Model (GSM) twice a day (84-hour forecasts from 00 UTC and 192-hour forecasts from 12 UTC), a Regional Spectral Model (RSM) also twice a day (51-hour forecasts from 00 and 12 UTC). A Typhoon Model (TYM) is run twice a day (78-hour forecasts from 06 and 18 UTC) when a typhoon exists or it is expected to be formed in the western North Pacific. JMA carries out experimental medium-range ensemble forecast and dynamical one-month forecasts using a version of GSM with reduced horizontal resolution (T63). The basic features of the operational forecast models of JMA are summarized in Tables 6, 9 and 13.

An operational tracer transport model is run on request of national Meteorological Services in RA II or the International Atomic Energy Agency (IAEA) for RSMC support for environmental emergency response.

Three ocean wave models, Global Wave Model, Japan-area Wave Model and Coastal Wave Model, are run operationally. The specifications of the models are described in Table 15.

The numerical storm surge model is run four times a day when a typhoon is approaching Japan. The specifications of the model are described in Table 16.

The Ocean Data Assimilation System (ODAS), whose specifications are described in Table 17, is operated.

A numerical sea ice model runs to predict sea ice distribution and thickness over the seas adjacent to Hokkaido twice a week in winter. The specifications of the model are given in Table 18.

The very short-range forecast of precipitation is operationally performed every hour.   Precipitation data measured with AMeDAS (Automated Meteorological Data Acquisition System, a high density automated observation network) and radar reflectivity data are composed to make hourly precipitation map with a resolution of 5 km. These data are extrapolated in time to produce prognostic charts of precipitation up to three hours. In addition to the kinematical methods, the growth and decay of precipitation due to orographically induced updraft and downdraft are taken into account. The specifications of the model are described in Table 12.

7.1 System run schedule and forecast ranges

The Table 5 summarizes the system job schedule of NAPS and forecast ranges. These jobs are executed in batch on the HITAC S-3800/480.

Table 5   The schedule of the NAPS operation

Time (UTC)		NAPS operation  (Model forecast range)

0000 - 0035		12UTC decode, global cycle analysis

0035 - 0110		18UTC decode, global cycle analysis

0110 - 0112		SST analysis

0110 - 0120		verification

0120 - 0130		00UTC storm surge forecast (00h - 24h)

0230 - 0250		00UTC decode, global early analysis

0250 - 0305		00UTC global forecast (00h - 24 h)

0305 - 0320		00UTC decode, regional analysis

0320 - 0340		00UTC regional forecast (00h - 24h)

0340 - 0400		00UTC global forecast (24h - 51h)

0400 - 0420		00UTC regional forecast (24h - 51h)

0425 - 0450		00UTC global forecast (51h - 84h)

0450 - 0500		00UTC wave forecast (00h - 72h)

0500 – 0550		Ocean data assimilation / El Niño prediction

0700 - 0730		06UTC meso-scale forecast (00h - 12h)

0720 - 0730		06UTC storm surge forecast (00h - 24h)

0730 - 0745		06UTC decode, typhoon analysis

0745 - 0800		06UTC typhoon forecast (00h - 78h)

1320 - 1330		12UTC storm surge forecast (00h - 24h)

1320 - 1355		00UTC decode, global cycle analysis

1355 - 1430		06UTC decode, global cycle analysis

1500 - 1520		12UTC decode, global early analysis

1520 - 1535		12UTC global forecast (00h - 24h)

1535 - 1550		12UTC decode, regional analysis

1550 - 1610		12UTC regional forecast (00h - 24h)

1610 - 1630		12UTC global forecast (24h - 51h)

1630 - 1650		12UTC regional forecast (24h - 51h)

1655 - 1720		12UTC global forecast (51h - 84h)

1720 - 1730		12UTC wave forecast (00h - 72h)

1730 - 1830		12UTC global forecast (84h - 192h)

1830 - 1835		12UTC wave forecast (72h - 192h)

1835 - 1950		12UTC one month forecast (5 runs, twice a week)

or medium-range ensemble forecast (0 – 192h)

1900 - 1930		18UTC meso-scale forecast (00h - 12h, 5 times a week)

1920 - 1930		18UTC storm surge forecast (00h - 24h)

1930 - 1945		18UTC decode, typhoon analysis

1945 - 2000		18UTC typhoon forecast (00h - 78h)

7.2 Medium-range forecasting system (3 - 8 days)

7.2.1 Data assimilation, objective analysis and initialization (Table 6)

A multivariate three-dimensional optimum interpolation (3D-OI) scheme on model levels is employed for the analyses of geopotential height and wind except for the tropical region (15N-15S), where univariate OI analysis is applied. Geostrophic relation between geopotential height and wind is relaxed between 15N(S)-25N(S). Univariate 3D-OI scheme is employed for the analyses of temperature and relative humidity.

VISSR digital cloud data from GMS are combined with ship or surface observations, and they are used as proxy data to generate vertical moisture profile in global analysis.

Non-linear normal mode initialization with full physical processes is applied to the first five vertical modes.

7.2.2 Medium-range forecasting model

Table 6   Specifications of Global Spectral Model (GSM9603) for 8-day forecasts

Basic equation		Primitive equations

Independent variables	Latitude, longitude, sigma-p hybrid coordinate and time

Dependent variables		Vorticity, divergence, temperature, surface pressure, specific humidity

Numerical technique		Euler semi-implicit time integration, spherical harmonics for

horizontal representation and finite difference in the vertical

Integration domain		Global, surface to 10hPa

Horizontal resolution	T213 (about 0.5625 deg Gaussian grid) 640x320

Vertical levels		30

Forecast time		84 hours from 00UTC and 192 hours from 12UTC

Forecast phenomena		Synoptic disturbances and tropical cyclones

Orography		Original resolution 10' x 10' data-set, spectrally truncated and smoothed.

Horizontal diffusion		Linear, second-order Laplacian

Moist processes		Prognostic Arakawa-Schubert cumulus parameterization +

large-scale condensation

Radiation			Shortwave radiation computed every hour

Longwave radiation computed every three hours

Cloud			Prognostic cloud water, cloud cover diagnosed from moisture and

cloud water

Gravity wave drag		Longwave scheme for troposphere and lower stratosphere,

shortwave scheme for lower troposphere

PBL			Mellor-Yamada level-2 closure scheme and similarity

theory for surface boundary layer

Land surface		Simple Biosphere Model (SiB)

Surface state		SST anomaly added to seasonally changing climatological SST. Initial soil

moisture, initial snow depth, roughness length and albedo are climatological

values.

7.2.3 Numerical weather prediction products for Medium-range forecast

The following model output products from GSM are disseminated through the JMA radio facsimile broadcast (JMH or JMJ), the GTS and the RSMC Tokyo Data Serving System.

Table 7   Facsimile products for medium-range forecast

| Content | Level (hPa) | Area (see Fig.1a*) | Forecast Hours | Initial Time | Transmission Method |
| --- | --- | --- | --- | --- | --- |
| geopotential height, relative vorticity | 500 | O | 96, 120, 144, 168, 192 | 12UTC | GTS |
| temperature | 850 |  |  |  |  |
| sea level pressure | - |  |  |  |  |
| sea level pressure | - | C | 96, 120 |  | radio facsimile |
| rainfall amount | - |  |  |  |  |

Table 8   Grid point value products (GRIB) for medium-range forecast

| Contents | Level (hPa) | Area | Forecast Hours | Initial Time | Transmission Method |
| --- | --- | --- | --- | --- | --- |
| sea level pressure, rainfall amount | - | Global 2.5x2.5 Degree | 96, 120 | 12UTC | GTS RSMC DSS |
| temperature, wind | surface |  |  |  |  |
| geopotential height, temperature,wind | 850, 700, 500, 300, 250, 200, 100 |  |  |  |  |
| T-TD | 850, 700 |  |  |  |  |
| sea level pressure, rainfall amount | - |  | 144, 168, 192 |  |  |
| temperature, wind | surface |  |  |  |  |
| geopotential height, temperature, wind | 850, 700, 500, 300 |  |  |  |  |
| T-Td | 850, 700 |  |  |  |  |
| wind | 200 |  |  |  |  |

7.2.4 Operational techniques for application of GSM products

Surface air temperature is derived by Kalman-filtering technique and cloud amount, precipitation by MOS technique. Significant weather and cross section charts for international air navigation are produced twice a day.

Atmospheric angular momentum (AAM) functions are computed from analyzed and forecasted global wind and surface pressure data and sent to NCEP/NOAA.

7.3 Short-range forecasting system

7.3.1 Short-range forecasting system (0-51 hours)

7.3.1.1 Data assimilation, objective analysis and initialization

A multivariate three-dimensional optimum interpolation (3D-OI) scheme on model levels is employed for the analysis of geopotential height and wind. Univariate 3D-OI scheme is employed for the analysis of temperature and relative humidity.

VISSR digital cloud data from GMS are combined with ship or surface observation and they are used as proxy data to generate vertical moisture profile in the analysis.

Non-linear normal mode initialization (NMI) with full physical processes is applied to the first five vertical modes.

Physical initialization with the use of analyzed precipitation data is executed before NMI.

7.3.1.2 Short-range forecasting model (0-51 hours)

Table 9   Specifications of Regional Spectral Model (RSM9603)

Basic equation		Primitive equations

Independent variables	x-y coordinate on a Lambert projection plane and sigma-p hybrid coordinate

Dependent variables		Wind components of x-y direction, virtual temperature,

natural log of surface pressure and specific humidity

Numerical technique		Euler semi-implicit time integration, double Fourier for

horizontal representation and finite difference in the vertical

Projection and grid size	Lambert projection, 20km at 60N and 30N

Integration domain		East Asia centering on Japan, 257 x 217 grids

Vertical levels		36

Forecast time		51 hours from 00, 12UTC

Forecast phenomena		Meso-beta scale disturbances

Initial			3 (3.5)-hour cutoff for 00 (12) UTC analysis with 12-hour

RSM forecast as a first guess

Lateral boundary		0-51 hour forecast by GSM runs

Orography		Envelope orography.  Orography is smoothed and spectrally truncated.

Horizontal diffusion		Linear, second-order Laplacian.

Moist processes		Large scale condensation + Prognostic Arakawa-Schubert

convection scheme + middle level convection + shallow convection

Radiation (shortwave)	Every hour

(longwave)	Every hour

Cloudiness		Diagnosed from relative humidity, maximum overlap

Gravity wave drag		Shortwave scheme for lower troposphere is included.

PBL			Mellor-Yamada level-2 closure scheme for stable PBL, non-local scheme

for unstable PBL, and similarity theory for surface boundary layer

Land surface		Ground temperature is predicted with the use of four levels in the ground.

Evaporability depends on location and season.

Surface state		Observed SST (fixed during time integration) and sea ice distribution.

Evaporability, roughness length, albedo are climatological values.

Snow cover over Japan is analyzed every day.

7.3.1.3 Numerical weather prediction products for short-range forecast

The following model output products from GSM are disseminated through the JMA radio facsimile broadcast (JMH or JMJ), the GTS and the RSMC Tokyo Data Serving System.

Table 10   Facsimile products for short-range forecast

| Contents | Level (hPa) | Area (see Fig.1) | Forecast Hours | Initial Time | Transmission Method |
| --- | --- | --- | --- | --- | --- |
| geopotential height, relative vorticity | 500 | A' | 0 | 00UTC 12UTC | radio facsimile GTS |
| vertical p-velocity | 700 |  |  |  |  |
| temperture, wind arrow | 850 |  |  |  |  |
| geopotential height, relative vorticity | 500 |  | 24, 36 |  |  |
| wind arrow | surface |  |  |  |  |
| sea level pressure | - |  |  |  |  |
| rainfall amount | - |  |  |  |  |
| temperature | 500 |  |  |  |  |
| dew point temperature, vertical p-velocity | 700 |  |  |  |  |
| temperature,wind arrow | 850 |  |  |  |  |
| geopotential height, temperature, isotach | 250 | Q | 24 |  |  |
| geopotential height, temperature, isotach | 500 |  |  |  |  |
| sea level pressure | - | C | 24, 48, 72 |  |  |
| rainfall amount | - |  |  |  |  |
| geopotential height, relative vorticity | 500 |  |  |  | radio facsimile GTS(48, 72) |
| temperature, wind arrow | 850 |  | 24, 48 (12UTC) 72 (12UTC) |  | radio facsimile GTS(48) |
| vertical p-velocity | 700 |  |  |  |  |
| stream line | 200 | H | 24, 48 |  | radio facsimile GTS |
| stream line | 850 |  |  |  |  |
| significant weather chart | - | M, N | 24 |  |  |

Table 11   Grid point value products (GRIB, GRID) for short-range forecast

| Contents | Level (hPa) | Area | Forecast Hour | Initial Time | Transmission Method |
| --- | --- | --- | --- | --- | --- |
| sea level pressure | - | Global 2.5x2.5 degree | 0 | 00UTC | GTS RSMC DSS (GRIB) |
| temperature, wind, T-TD | surface |  |  |  |  |
| geopotential height, temperature, wind, T-TD | 1000, 850, 700, 500, 400, 300 |  |  |  |  |
| geopotential height, temperature, wind | 250, 200, 150, 100, 70, 50, 30, 20, 10 |  |  |  |  |
| sea level pressure, rainfall amount | - |  | 0 (12UTC) 24, 48, 72 | 00UTC 12UTC |  |
| temperature, wind | surface |  |  |  |  |
| geopotential height, temperature, wind | 850, 700, 500, 300, 250, 200, 100 |  |  |  |  |
| T-TD | 850, 700 |  |  |  |  |
| sea level pressure | - | 20N-90N 0-360E 5.0x5.0 degree | 24, 48, 72 | 12UTC | GTS (GRID) |
| geopotential height | 500 |  |  |  |  |
| sea level pressure, rainfall amount | - | 20S-60N 80E-160W 2.5x2.5 degree | 0, 6, 12, 18, 24, 30, 36, 48, 60, 72 | 00UTC 12UTC | RSMC DSS (GRIB) |
| temperature, wind, T-TD | surface |  |  |  |  |
| geopotential height, temperature, wind, T-TD, vertical p-velocity | 850, 700 |  |  |  |  |
| geopotential height, temperature, wind, T-TD, relative vorticity | 500 |  |  |  |  |
| geopotential height, temperature, wind | 300, 250, 200, 150, 100 |  |  |  |  |
| sea level pressure, rainfall amount | - | 20S-60N 80E-160W 1.25x1.25 degree | 0, 6, 12, 18, 24, 30, 36, 42, 48, 54, 60, 72 |  |  |
| temperature, wind, T-TD | surface |  |  |  |  |
| geopotential height, temperature, wind, T-TD, vertical p-velocity | 925, 850, 700 |  |  |  |  |
| geopotential height, temperature, wind, T-TD | 500, 400, 300 |  |  |  |  |
| geopotential height, temperature, wind | 250, 200, 150, 100 |  |  |  |  |
| relative vorticity | 500 |  |  |  |  |
| vorticity potential, stream function | 850, 200 |  |  |  |  |

7.3.1.4 Operational techniques for application of short-range NWP products

The Kalman-filtering technique and the Neural-network technique are applied to grid point values predicted by RSM to derive forecast elements. The Kalman-filtering technique is used to derive probability of precipitation, three-hourly precipitation amount, surface air temperature and surface wind. The Neural-network technique is introduced to derive three-hourly weather, minimum humidity, probability of heavy precipitation and probability of thunderstorm.

Significant weather charts and prognostic cross section charts for domestic aviation forecast are produced twice a day (00, 12UTC).

7.3.2 Very short-range forecasting system (0 – 3 hours)

7.3.2.1 Data assimilation, objective analysis and initialization

Using digitalized radar echo intensities observed at 20 land radar sites and precipitation observations by AMeDAS (Automated Meteorological Data Acquisition System,  a network of more than 1300 raingauges over Japan), one-hour precipitation data over Japan are analyzed every hour with 5km resolution. The Z-R relationship is employed in conversion from radar echo intensity to precipitation rate. Calibrated radar echo intensities (precipitation) at the initial time of a very short-range forecast are used as a initial field for the forecast.

7.3.2.2 Model

Table 12   Specifications of very short-range forecasting model

Forecast process	Linear extrapolation

Physical process	Topographic enhancement and dissipation (by seeder-feeder model)

Motion vector	Motion of precipitation system is evaluated by the cross correlation method.

Time step		10 minutes

Grid form		Oblique conformal secant conical projection

Resolution	5km

Number of grids	250 x 660

Initial		One-hour precipitation by radar echo calibrated by precipitation observations

Forecast time	Up to three hours from each initial time (hourly = 24 times/day)

7.3.2.3 Numerical weather prediction products

The basic products of the very short-range forecasting system are: (a) composite radar echo (echo intensity and echo top height), (b) estimated one-hour precipitation distributions with 5 km resolution and (c) one-hour precipitation forecasts up to three hours. These products are utilized to issue warnings on heavy precipitation.

7.4 Specialized forecasts

7.4.1 Typhoon track forecasting system

7.4.1.1 Objective analysis and initialization

The analysis for numerical typhoon track prediction is made using the global analysis model with data cutoff time of 1.5 hours. After symmetric typhoon bogus data is implanted into the analysis field while asymmetric components are preserved, nonlinear normal mode initialization with full physics is applied to the first five vertical modes.

7.4.1.2 Typhoon track forecast model (TYM)

The model specifications are identical to those of RSM (Table 9) except for the followings:

Table 13   Specifications of Typhoon Track Forecast Model

Basic equation		Primitive equations

Independent variables	x-y coordinate on a Lambert (Mercator) projection plane

for target typhoon north (south) of 20N and sigma-p hybrid

coordinate

Dependent variables		Wind components of x-y direction, virtual temperature,

natural log of surface pressure and specific humidity

Numerical technique		Euler semi-implicit time integration, double Fourier for

horizontal representation and finite difference in the vertical

Projection and grid size	Lambert (Merctor) projection, 40km at typhoon center when

center of target typhoon is north (south) of 20N.

Integration domain		Center of domain is set at median of expected track of target typhoon

in the western North Pacific, 163x163 transform grid points

Vertical levels		15

Forecast time		78 hours from 06, 18UTC, maximum two runs for each initial time

Forecast phenomena		Typhoons

Initial			Global analysis using 6-hour forecast by GSM as a guess field with data

cut-off time of 1.5 hours.

Lateral boundary		6-84 hour forecast by GSM initialized 6 hours earlier

Surface state		Observed SST fixed during time integration

climatological evaporability, roughness length and albedo

Typhoon bogussing		Symmetric vortex generated using manually analyzed central pressure and

radius of 30kt winds with gradient-wind balance assumed in the free atmosphere,

Ekman-frictional inflow and compensating outflow added in PBL and in upper

levels, respectively. The vortex is blended with Global Analysis with its

asymmetric components preserved.

7.4.1.3 Numerical weather prediction products for typhoon forecast

The following products from the output of GSM and TYM are disseminated through GTS.

Table 14  Numerical weather prediction products for typhoon forecast

| Contents | Level (hPa) | Area | Forecast Hours | Initial Time | Transmission Method |
| --- | --- | --- | --- | --- | --- |
| Center position of tropical cyclones by GSM | - | Eq. - 60N 100E-180E | 06, 12, 18, 24, 30, 36, 42, 48, 54, 60, 66, 72, 78, 84 | 00UTC 12UTC | GTS |
| Center position of tropical cyclones by TYM | - | Eq. - 60N 100E-180E | 06, 12, 18, 24, 30, 36, 42, 48, 54, 60, 66, 72, 78 | 06UTC 18UTC | GTS |

7.4.2 Environmental Emergency Response System

JMA is a Regional Specialized Meteorological Center (RSMC) for Environmental Emergency Response in RA II for preparation and dissemination of transport model products on exposure and surface contamination of accidentally released radioactive materials.

The transport model takes a Lagrangian method, where many tracers are released in time and space according to information on pollutant emissions, displaced due to three-dimensional advection and horizontal and vertical diffusions, dropped due to dry and wet depositions and removed due to radioactive decay. Advection, diffusion and deposition are computed from 6-hourly model-level outputs of the high resolution global numerical weather prediction (NWP) model (GSM96/T213L30). Main products of the RSMC are trajectories, time integrated low-level concentrations and total deposition up to 72 hours.

7.4.3  Ocean wave forecasting system

JMA operates three numerical wave models: Global Wave Model (GWM), Japan area Wave Model (JWM) and Coastal Wave Model (CWM).   GWM and JWM are classified into the third generation model.   CWM is diagnostic model.

7.4.3.1   Numerical wave prediction models

Table 15    Specifications of ocean wave prediction models

| Model name | Global Wave Model | Japan-area Wave Model |
| --- | --- | --- |
| Model type | spectral model (third generation) |
| Spectral component | 400 components (25 frequencies from 0.0375 to 0.3Hz and 16 directions) |
| Grid form | equal latitude-longitude grid on spherical coordinate |
| Grid size | 2.5deg.×2.5deg. (144×57) | 0.5deg.×0.5deg. (81×81) |
| Integration domain | global 70N-70S, 0E-180E-2.5W | sea adjacent to Japan 55N-15N, 115E-155E |
| Time step | 1 hour | 30 minutes |
| Forecast time | 72 hours from 00UTC 192 hours from 12UTC | 72 hours from 00,12UTC |
| Boundary condition | - - - | Global Wave Model |
| Initial condition | hindcast |
| Wind field | Global Spectral Model (GSM) Bogus gradient winds (for typhoons in the western North Pacific) |
| Model name | Coastal Wave Model |
| Model type | hybrid model of significant wave and spectral model |
| Spectral component | 16 direction for swell |
| Grid form | equal latitude-longitude grid on plain |
| Grid size | 0.1deg.×0.1deg. (400×400) |
| Integration domain | coastal sea of Japan 55N-15N, 115E-155E |
| Time step | 3 hours (Time interval, diagnostic model) |
| Forecast time | 72 hours from 00,12UTC |
| Boundary condition | Japan-area Wave Model |
| Initial condition | (diagnostic model) |
| Wind field | Regional Spectral Model (RSM) with the supplement of GSM Bogus gradient winds (for typhoons in the western North Pacific) |

7.4.3.2  Numerical wave prediction products

The grid point values (GPVs) of wave models are disseminated to domestic users.  The GPVs of GWM have been available in the RSMC Tokyo Data Serving System of JMA since August 1998.

The model products will also be reported to the Marine Pollution Emergency Response Authority (MPEROA) within the Marine Pollution Emergency Response Support System (MPERSS).

7.4.4 Typhoon tide forecasting system

7.4.4.1 Model

JMA extended the coverage area of the storm surge model over Tohhoku and Hokuriku districts (northern parts of Japan) in July 1999 .  The specifications of the model are given in Table 16.

## Table 16  Specifications of Numerical Storm Surge Model

| Coverage area | coastal area around Japan (128.0°- 141.5°E, 30.0°- 36.5°N) (135.5°- 143.0°E, 36.0°- 42.0°N) |
| --- | --- |
| Grid (type and resolution) | latitudal and longitudal grid of one minute (1.9km x 1.5km) resolution |
| Model type | Numerical dynamical model |
| Boundary conditions (open and coastal boundaries) | (1)Modified radiation condition at open boundaries; and (2)Zero normal flows at coastal boundaries. |
| Numerical procedure, time stepping | (1)Time integration: leap frog method; (2)Space differential: central difference method; and (3)Time step: 8 seconds. |
| Wind input | Grid winds as a sum of the two components: (1) gradient winds calculated by the Fujita's pressure model; and (2) moving velocity of the typhoon that is estimated from movements of the typhoon center that the forecaster determines every six hours. |

7.4.4.2 Numerical typhoon tide prediction products

Time series of predicted storm surge and predicted tidal level, and predicted highest tide for 142 ports are disseminated to the meteorological offices responsible for issuing storm surge advisory and warning.

7.4.5 Ocean data assimilation system

The Ocean Data Assimilation System (ODAS) with the following specifications has continued being operated.

Table 17   Specifications of Ocean Data Assimilation System

| Basic equation | Primitive equations, rigid lid |
| --- | --- |
| Independent variables | Lat-lon coordinate and z vertical coordinate |
| Dependent variables | u, v, T, s (salinity, nudged to climatological value) |
| Numerical technique | Finite difference both in the horizontal and in the vertical |
| Grid size | 2.5 degree (longitude) x 2.0 degree (latitude, smoothly decreasing to 0.5 degree toward the equator) grids |
| Vertical levels | 20 levels |
| Integration domain | Global (from 66N to 80S, toward poles from 60N and 60S, prognostic fields are nudged to climatology) |
| Forcing data | Ocean currents are driven by the surface wind fields derived by operational global 4DDA, temperature in the mixed layer is nudged to the daily global SST analysis |
| Observational data | Sea surface and sub surface temperature |
| Operational runs | Two kinds of run, final run and early run, with cut-off time of 30 days and 5 days, respectively, for ocean observation data |

The output of ODAS is fed to an interactive graphic tool for the analysis of　tropical ocean status.  Some figures based on ODAS outputs are included in the Monthly Ocean Report and in the Monthly Report on Climate System of JMA, and provided through the DDB homepage of JMA.  The data are also used as the oceanic initial conditions for the JMA coupled ocean-atmosphere model.

7.4.6 Numerical sea ice forecasting system

JMA issues information on the state of sea ice in the seas adjacent to Japan. A numerical sea ice model has been run to predict sea ice distribution and thickness in the seas adjacent to Hokkaido (mainly the southern part of the Sea of Okhotsk), twice a week in winter from December 1990 (see Table 18).

7.4.6.1 Numerical sea ice prediction model

Table 18  Specification of Numerical sea ice prediction model

Dynamical processes 	Viscous-plastic model (MMD/JMA, 1993, wind and sea water stress to sea ice, Coriolis' force, force from gradient of sea surface and internal force are considered)

Physical processes		Heat exchange between sea ice, atmosphere and sea water

Dependent variables 		Concentration and thickness

Grid size and time step 	12.5km and 6 hours

Integration domain 		Seas around Hokkaido

Forecast time 		168 hours from 00UTC twice a week

Initial 			Concentration analysis derived from GMS and NOAA satellite imagery and thickness estimated by hindcast

7.4.6.2 Products on sea ice condition

Analysis of sea ice conditions in the Sea of Okhotsk, the northern Japan Sea, the western North Pacific, the western Bering Sea and the Bohai Sea are disseminated by the JMA radio facsimile broadcast (JMH) every Tuesday and Friday from December to May. The sea ice conditions for the coming seven days predicted by the numerical sea ice model are also broadcast by JMH every Wednesday and Saturday.

7.5 Extended-range forecasting system

7.5.1 Data assimilation, objective analysis and initialization

The system is the same as that of the medium-range forecasting except for the analysis of the upper stratosphere. A two dimensional function fitting method is introduced for temperature and height analyses above 10hPa.  The result of the previous analysis is used as pseudo observations over data-sparse areas in order to avoid computational instability. Wind data are used for extratropical height analysis by assuming the geostrophic relationship.

7.5.2 Model

The model specifications are the same as those of the high resolution GSM (Table 6) except for the following ones:

Table 19   Specifications of GSM for one-month forecast

Integration domain		Global, surface to 1hPa

Horizontal resolution	T63 (about 1.875 deg Gaussian grid) 192x96

Vertical levels		30 (surface to 1hPa)

Forecast time		Five 30-day runs from perturbed 12UTC initial conditions

are carried out twice per week.

7.5.3 Ensemble Forecasting Procedure

For the extended-range forecast, an ensemble forecast technique is employed. Perturbations to be added to the initial analysis are determined using the singular vectors of a hemispheric balance model whose resolution is T21, 2-levels. Initial perturbations are superpositions of the greatest 10 singular vectors. A set of forecasts which are an unperturbed forecast and four perturbed forecasts is made on two consecutive days. Therefore, 10 model runs are offered for an ensemble forecast.

7.5.4 Numerical weather prediction products

JMA started to produce grid point value products for one-month forecast in GRIB format in December 1999 based on the operational ensemble forecasting system.

Table 20  Grid point value products (GRIB) for extended –range forecast

| Contents | Level (hPa) | Area | Initial time & Forecast Time |
| --- | --- | --- | --- |
| Ensemble mean value of forecast members averaged for 7 days forecast time range | Sea level pressure, rainfall amount | - | Global 2.5x2.5 degree | Initial time : 12UTC on Wednesday and Thursday) Forecast time : 2-8, 9-15, 16-22, 23-29 days from the latter initial time |
|  | Temperature, T-Td, wind(u,v) | 850 |  |  |
|  | Geopotential height | 500,100 |  |  |
|  | Wind (u, v) | 200 |  |  |
|  | Sea level pressure anomaly | - | Northern Hemi-sphere 2.5x2.5 degree |  |
|  | Temperature anomaly | 850 |  |  |
|  | Geopotential height anomaly | 500,100 |  |  |
| Spread (Standard deviation) among time averaged ensemble member forecasts | Sea level pressure | - |  | Forecast time : 2-8, 9-15, 16-22, 23-29, 2-15, 16-29, 2-29 days from the latter initial time |
|  | Temperature | 850 |  |  |
|  | Geopotential height | 500 |  |  |
| Occurrence probability of above (or below) normal of geopotential height. (greater or less than +-0.5*sigma of natural variability) | 500 |  |  |

7.5.5 Operational technique for an application of extended-range forecast

Statistics of ensemble forecasts are applied.  For example, ensemble mean fields and spread (standard deviation) of individual forecasts are calculated.  The surface temperatures (monthly mean, weekly mean), precipitation amounts (monthly total), sunshine durations (monthly total), and snowfall amounts (monthly total) are derived by the Perfect Prognosis Method (PPM) technique.

7.6 Long-range forecasting system

JMA started the operation of a coupled ocean-atmospheric model in 1998 for the outlook of El Niño and La Niña.  The oceanic part of the coupled model is identical to the model for ODAS.  The atmospheric part of the model is a reduced resolution (T42) version of the previous operational global spectral model that was used until February 1996.  In August 1999, JMA started to issue the monthly ENSO outlook based on the model results for end users.  JMA also plans to make the model results available through the DDB of JMA in 2000.

Table 21  Specification of the JMA coupled model

| Oceanic component | Identical to the model for ODAS |
| --- | --- |
| Atmospheric component | Basic equation | Primitive equation |
|  | Domain | Global |
|  | Resolution | T42, 21 vertical levels |
|  | Convection scheme | Kuo type |
|  | Land surface processes | SiB of Sellers et al. (1986) |
| Coupling | Coupling interval | 24 hours |
|  | Flux adjustment | Monthly heat and momentum flux adjustment |
| Forecast period | 18 months |
| Model run interval | 15 days |

8.  Verification of prognostic products

Objective verification of prognostic products is operationally performed against analysis and radiosonde observations according to the WMO/CBS recommendations. Results of the monthly verification for the year of 1999 are presented in Tables 22.1 to 22.20. All the verification scores are only for the prediction from the 1200 UTC initials.

9. Plans for the future

(1) Assimilation of ATOVS/BUFR data in the global and regional analyses will begin in January 2000.

(2) A three-dimensional variational assimilation method will be introduced to the global analysis in March 2000

with introduction of direct assimilation of TOVS radiance data.

(3) GPS data from ground receivers in the Tokai area of Japan and high resolution TBB data from GMS-5 will be

assimilated for preparation of initial conditions of MSM from March 2000.

(4) The land surface scheme of GSM will be upgraded in March 2000. The new scheme will include a revised

snow scheme, a multi-level model for soil temperature prediction, and frozen soil.

(5) A prognostic cloud water scheme will be implemented in RSM, MSM and TYM early in 2000.

10.  References

Maritime Meteorological Division, JMA, 1993: A numerical sea ice prediction in the southern part of the Okhotsk, Geophysical Magazine, 44, 143-155.

Numerical Prediction Division, JMA, 1997: Outline of Operational Numerical Weather Prediction at Japan Meteorological Agency.

World Meteorological Organization: NWPP Report Series No. 24, Numerical Weather Prediction Progress Report for 1997.

Japan Meteorological Agency, 1998: Enhanced Accuracy of Typhoon Prediction of the Advanced Numerical Models at the Japan Meteorological Agency, RSMC Tokyo - Typhoon Center Technical Review, No.2.

T. Iwasaki, T. Maki, and K. Katayama, 1998: Tracer transport model at Japan Meteorological Agency and its application to the FTEX data,  Atmospheric Environment, 32, 4285-4296.

Table 22.1 Root mean square errors of geopotential height at 500 hPa against analysis (m)

Northern Hemisphere (20-90N)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 18.4 | 17.7 | 15.4 | 15.5 | 13.9 | 13.1 | 12.4 | 12.7 | 13.8 | 15.4 | 17.4 | 15.6 | 15.1 |
| 72 | 49.0 | 48.1 | 41.1 | 43.6 | 36.8 | 33.5 | 30.5 | 30.4 | 36.3 | 40.9 | 46.5 | 40.4 | 39.7 |
| 120 | 82.0 | 83.9 | 71.2 | 77.3 | 66.1 | 57.8 | 50.6 | 50.1 | 64.4 | 68.5 | 78.2 | 71.8 | 68.4 |

Table 22.2 Root mean square errors of geopotential height at 500 hPa against analysis (m)

Southern Hemisphere (20-90S)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 20.8 | 23.5 | 21.5 | 24.4 | 25.4 | 28.0 | 28.0 | 24.7 | 25.1 | 22.2 | 21.9 | 21.4 | 23.9 |
| 72 | 49.2 | 58.3 | 55.6 | 60.1 | 64.0 | 72.3 | 68.3 | 61.5 | 60.4 | 56.7 | 53.4 | 52.7 | 59.4 |
| 120 | 76.3 | 82.2 | 85.2 | 90.0 | 98.3 | 106.2 | 101.6 | 89.7 | 90.9 | 84.4 | 81.7 | 76.4 | 88.6 |

Table 22.3 Root mean square errors of geopotential height at 500 hPa against observations (m)

North America

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 22.7 | 20.9 | 18.8 | 17.7 | 15.4 | 14.2 | 13.9 | 14.4 | 14.9 | 16.8 | 17.6 | 18.8 | 17.2 |
| 72 | 54.2 | 55.2 | 48.3 | 48.8 | 35.9 | 29.7 | 27.1 | 27.8 | 33.7 | 39.2 | 46.0 | 51.6 | 41.4 |
| 120 | 87.6 | 77.8 | 83.2 | 93.7 | 65.1 | 52.1 | 42.9 | 50.1 | 60.4 | 74.6 | 72.6 | 83.7 | 70.3 |

Table 22.4 Root mean square errors of geopotential height at 500 hPa against observations (m)

Europe

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 27.2 | 22.7 | 20.3 | 19.2 | 19.4 | 19.2 | 16.4 | 18.0 | 19.3 | 20.8 | 23.7 | 25.6 | 21.0 |
| 72 | 58.8 | 51.4 | 43.8 | 40.4 | 48.6 | 37.0 | 29.9 | 29.8 | 36.2 | 41.4 | 56.2 | 46.1 | 43.2 |
| 120 | 101.9 | 115.4 | 71.8 | 79.3 | 79.0 | 68.4 | 53.0 | 47.4 | 65.3 | 67.5 | 94.8 | 88.7 | 77.4 |

Table 22.5 Root mean square errors of geopotential height at 500 hPa against observations (m)

Asia

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 19.0 | 17.8 | 18.8 | 17.2 | 18.1 | 17.9 | 16.1 | 15.1 | 16.2 | 17.5 | 19.9 | 15.8 | 17.4 |
| 72 | 36.8 | 38.4 | 34.2 | 35.1 | 35.7 | 30.0 | 26.0 | 23.2 | 28.6 | 39.3 | 39.3 | 31.4 | 33.1 |
| 120 | 55.6 | 57.9 | 50.1 | 57.7 | 62.6 | 43.3 | 35.5 | 32.8 | 40.9 | 55.7 | 56.6 | 50.4 | 49.9 |

Table 22.6 Root mean square errors of geopotential height at 500 hPa against observations (m)

Australia / New Zealand

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 15.3 | 20.8 | 18.6 | 21.5 | 21.6 | 29.0 | 23.6 | 19.1 | 20.9 | 20.5 | 17.6 | 15.5 | 20.3 |
| 72 | 33.9 | 41.2 | 38.4 | 41.5 | 42.4 | 53.6 | 41.0 | 33.5 | 41.1 | 41.1 | 37.7 | 30.0 | 39.6 |
| 120 | 56.8 | 54.7 | 50.8 | 52.1 | 60.9 | 65.4 | 65.0 | 57.9 | 60.1 | 57.4 | 49.3 | 44.1 | 56.2 |

Table 22.7 Root mean square of vector wind errors at 250 hPa against analysis (m/s)

Northern Hemisphere (20-90N)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 6.8 | 6.8 | 6.5 | 6.4 | 5.9 | 5.9 | 6.0 | 6.1 | 6.2 | 6.4 | 6.5 | 6.5 | 6.3 |
| 72 | 13.4 | 13.3 | 12.4 | 12.7 | 12.0 | 11.9 | 11.5 | 11.7 | 12.7 | 12.7 | 13.0 | 12.3 | 12.5 |
| 120 | 19.3 | 19.8 | 17.8 | 19.0 | 17.9 | 16.7 | 15.8 | 16.3 | 18.4 | 18.4 | 19.4 | 18.1 | 18.1 |

Table 22.8 Root mean square of vector wind errors at 250 hPa against analysis (m/s)

Southern Hemisphere (20-90S)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 6.6 | 7.1 | 6.8 | 7.0 | 7.5 | 7.7 | 8.1 | 7.5 | 7.6 | 7.2 | 6.8 | 6.9 | 7.2 |
| 72 | 13.7 | 15.3 | 14.8 | 15.4 | 16.7 | 17.2 | 16.9 | 15.5 | 15.7 | 15.1 | 14.4 | 14.7 | 15.4 |
| 120 | 18.6 | 19.8 | 20.5 | 21.0 | 23.0 | 23.5 | 22.9 | 20.8 | 21.6 | 20.5 | 19.6 | 19.3 | 20.9 |

Table 22.9 Root mean square of vector wind errors at 250 hPa against observations (m/s)

North America

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 9.1 | 8.8 | 7.9 | 8.0 | 7.8 | 7.9 | 7.0 | 7.3 | 7.5 | 7.4 | 7.4 | 8.1 | 7.8 |
| 72 | 17.8 | 17.6 | 14.8 | 15.7 | 13.6 | 13.2 | 11.3 | 12.4 | 14.4 | 14.3 | 15.0 | 15.9 | 14.6 |
| 120 | 23.9 | 24.0 | 20.6 | 25.0 | 20.3 | 18.4 | 15.5 | 17.3 | 21.0 | 21.7 | 20.4 | 23.4 | 20.9 |

Table 22.10 Root mean square of vector wind errors at 250 hPa against observations (m/s)

Europe

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 8.2 | 7.5 | 7.0 | 7.2 | 7.4 | 7.6 | 7.2 | 7.8 | 8.4 | 8.7 | 8.3 | 8.7 | 7.8 |
| 72 | 15.1 | 13.6 | 12.6 | 12.6 | 12.2 | 13.4 | 12.2 | 12.5 | 13.5 | 13.9 | 16.3 | 14.0 | 13.5 |
| 120 | 23.4 | 25.2 | 18.7 | 20.3 | 18.5 | 21.2 | 18.1 | 17.8 | 20.7 | 20.9 | 24.4 | 21.7 | 20.9 |

Table 22.11 Root mean square of vector wind errors at 250 hPa against observations (m/s)

Asia

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 8.0 | 8.3 | 9.3 | 9.0 | 8.2 | 8.4 | 8.3 | 7.2 | 7.4 | 7.9 | 7.7 | 7.0 | 8.1 |
| 72 | 11.8 | 12.0 | 13.0 | 13.3 | 14.0 | 12.9 | 12.4 | 10.2 | 11.8 | 12.3 | 12.2 | 10.2 | 12.2 |
| 120 | 15.5 | 15.8 | 15.7 | 18.0 | 19.9 | 16.5 | 15.6 | 14.0 | 14.3 | 16.2 | 15.7 | 13.1 | 15.9 |

Table 22.12 Root mean square of vector wind errors at 250 hPa against observations (m/s)

Australia / New Zealand

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 7.5 | 8.5 | 8.6 | 8.9 | 9.5 | 9.0 | 8.9 | 9.0 | 9.1 | 8.7 | 8.3 | 8.5 | 8.7 |
| 72 | 11.4 | 13.9 | 13.7 | 14.1 | 14.6 | 14.6 | 14.1 | 13.1 | 14.2 | 13.4 | 12.3 | 13.1 | 13.5 |
| 120 | 14.1 | 17.9 | 17.9 | 17.6 | 18.5 | 17.9 | 19.3 | 17.2 | 17.9 | 17.5 | 17.0 | 15.4 | 17.3 |

Table 22.13 Root mean square of vector wind errors at 250 hPa against analysis (m/s)

Tropic

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 7.2 | 7.8 | 7.1 | 6.9 | 6.7 | 6.8 | 7.1 | 7.1 | 6.7 | 6.8 | 6.4 | 5.9 | 6.9 |
| 72 | 10.1 | 10.9 | 9.8 | 10.0 | 9.6 | 9.7 | 10.0 | 9.6 | 9.1 | 9.4 | 9.3 | 9.3 | 9.7 |
| 120 | 11.2 | 12.2 | 10.8 | 11.3 | 10.8 | 11.0 | 11.0 | 10.5 | 10.2 | 10.5 | 10.5 | 11.2 | 10.9 |

Table 22.14 Root mean square of vector wind errors at 850 hPa against observations (m/s)

Tropic

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 4.7 | 5.1 | 4.5 | 4.6 | 4.2 | 4.3 | 4.8 | 4.6 | 4.2 | 4.1 | 4.4 | 4.3 | 4.5 |
| 72 | 5.6 | 6.0 | 4.8 | 5.2 | 4.6 | 4.9 | 5.2 | 5.1 | 4.7 | 4.6 | 5.1 | 5.0 | 5.1 |
| 120 | 6.0 | 6.5 | 5.6 | 5.8 | 4.8 | 5.3 | 5.5 | 5.4 | 5.2 | 5.1 | 5.7 | 5.5 | 5.5 |

# Footnotes

* Figure 1 available in hard copy only.