ANNUAL WWW TECHNICAL PROGRESS REPORT ON THE GDPS

COUNTRY: Australia      CENTRE: NMOC Melbourne                          January 2001

1.     SUMMMARY OF HIGHLIGHTS:

Meteorological, Oceanographic and Computer Systems:

| 1 January: | Y2000 system change-over. |
| --- | --- |
| 22 January: | Trajectory guidance for Trans-Tasman balloon flight. |
| 6 April: | Introduction of decision tree thunderstorm and cold season tornado guidance, based on MESO_LAPS. |
| 1 May: | New NEC SX-5 available for operational use. |
| 3 May: | WMO and CTBTO/IDC EER Test - use of Joint Web Page. |
| 27 June: | Global WMO/IAEA EER Test. |
| 1 August: | Operational implementation of 1DVAR in GASP. |
| 21 August: | Semi-operational implementation of Sydney and Melbourne MESO_LAPS_PT050 for the Sydney 2000 Olympics/Paralympics. |
| 25 August: | Upgrade to Operational Sea State Forecast System incorporating changes to the discretisaion of the wave spectrum and a high resolution bathymetry. |
| 1 September: | Operational preparation of significant weather prognoses using Horace system. |
| 4 September: | 06 and 18UTC PAOBs used in LAPS_PT375. |
| 9 November: | Cray J90 decommissioned (used in archive conversion project during 2000). |
| 15 November: | Additional locally derived cloud drift winds (viz., water vapor, hourly IR, VIS and HRVIS) operationally implemented in LAPS_PT375. |
| 17 November: | 17 November: NEC SX-4 decommissioned. |

2.     EQUIPMENT IN USE AT CENTRE:

The National Meteorological Operations Centre (NMOC) Melbourne's computing backbone is provided by 11 Hewlett-Packard 9000 series Unix servers,  a dual-node supercomputing configuration (shared equally with CSIRO) consisting of 2 NEC SX-5 supercomputers (the second node having just undergone acceptance testing in January 2001). Currently, 8 of the HP servers have 2 cpus and the remaining 3 have a single cpu. All run under HP-UX B.10.20 with clock speeds and RAM up to 240 Mhz and 1536MB, respectively. Disc storage of approximately 1 TB is associated with the  servers. The first node, of the NEC SX-5 dual-node machine, has a configuration of 16 processors, 128GB of Memory, and 2TB of hippi and 288GB of scsi disc, and runs under the SUPER-UX Unix 9.2 SX-5 Operating System. The second node, at this stage, has 8 processors and 64GB of Memory. Real time scheduling is currently carried out on one of the HP Unix servers. A FDDI link provides the operational connections between the Unix servers and the NECs. A magnetic cartridge archive system is provided by a StorageTek Mass Store 4400 ACS (Automatic Cartridge System) and 2 StorageTek 9710 Library Storage Modules (with a 34TB capacity) using 12 DLT, ie Digital Linear Tape, units. Peripheral equipment includes HP Design Jet 650C plotters, HP LaserJet 5 SiMX printers, a HP LaserJet 4500DN and a HP Deskjet 1600CM coloured printer. There are a number of LANs which provide access to internal users. A PC-based digital facsimile system (DIFACS) is used for product dissemination nationally.

Basically, the main numerically intensive analysis and forecast components of the NWP systems run on the NEC SX-5(s), while the less intensive tasks (for eg message recognition and decoding, data base ingestion and extraction, post-processing, display, etc.) tend to be carried out on the HP computers.

2.1  Software in use at Centre:

The overall computer environment in the NMOC is mainly Unix. A real-time data base, currently using ORACLE 7.3.3.4.0, is used for storage of observational data and grids from the various NWP systems. The U.S. Navy's Environmental Operational Nowcasting System (NEONS) software is commonly used for accessing the data base. The operational NWP models are written mainly in Fortran, with many of the associated files having the NetCDF structure. Most displays are produced using the NCAR graphics package and IDL. During the year, the UK Met. Office’s Horace system was introduced into operations and used to prepare significant weather prognoses, replacing the old CIM CAD package. Sam-fs is currently being used for magnetic cartridge archives in the NMOC.

2.1  Peripheral Systems in use at Centre:

The DIFACS system is used to to disseminate a selection of basic analysis and prognostic charts, and some satellite imagery, to the Bureau's regional offices and some outside users. MCIDAS is used for comprehensive interaction and display of satellite imagery and products, observational and gridded data and is also a major component of the Australian Integrated Forecast System (AIFS). Products from the NWP systems are written to internal and external (www.bom.gov.au) web servers. Magnetic cartridge archives are kept of various NWP products with Australian region analyses available back to 1970 and Southern Hemisphere analyses back to 1972. Hard copy and microfilm archives of charts also exist. An aviation system, which interacts with the WAFS data, is used to view and display the data and prepare the various flight and route forecasts. Regular statistics (including S1 skill scores, root mean square errors and anomaly correlations) monitoring and comparing the performance of the NMOC's NWP systems (and also some overseas NWP models) are also produced.

3.     DATA AND PRODUCTS FROM GTS IN USE:

The following table gives a list of the major report types used in the NMOC Melbourne:

| Report Type | Description |
| --- | --- |
| AAXX | SYNOP |
| BBXX | SHIP |
| PPAA,PPBB,PPCC,PPDD | PILOT |
| QQAA,QQBB,QQCC,QQDD | SHIP PILOT |
| EEAA,EEBB,EECC,EEDD | MOBILE PILOT |
| TTAA,TTBB,TTCC,TTDD | TEMP |
| UUAA,UUBB,UUCC,UUDD | SHIP TEMP |
| IIAA,IIBB,IICC,IIDD | MOBILE TEMP |
| JJVV | BATHY |
| ZZYY | BUOY |
| ARP,AIREP,AMDAR | AIREP,AMDAR |
| VVAA,VVCC | SATEM |
| YYXX | SATOB |
| GRIB | UK,US,JAPAN |
| BUFR | US |

The following table gives approximate numbers of reports being received for a 24 hour period:

| SYNOPS | 33000 |
| --- | --- |
| PILOTS | 800 |
| TEMPS | 1150 |
| SHIPS | 2500 |
| BUOYS | 8000 |
| AIREPS,AMDARS | 17000 |
| SAT.WINDS | 250000 |
| SATEMS | 28000 |
| BUFR ENCODED 120 KM TOVS | 55000 |
| QUIKSCAT WINDS | 1000000 |

4.     DATA INPUT STREAM:

Automated. (Some manual intervention is available for correction of reports.) The observational data, along with NWP gridded data, is stored in a real-time relational data base system (ORACLE/NEONS).

5.     QUALITY CONTROL SYSTEM:

Validity checks are currently confined to within the respective assimilation or analysis schemes. Some gross checking outside these schemes may eventually be installed.

6.     MONITORING OF THE OBSERVING SYSTEM:

Monitoring of the observing system is carried out. The quantity of data available is monitored in real-time to ensure that reports are being received reliably and are made available to the operational systems, both automatic and manual. For the global system, statistics on the difference between observations and the first guess and analysis fields are routinely prepared to identify any problems with either the analysis system or individual data types. Lists of rejected data are also used to identify unreliable reporting from particular observing platforms.

7.     FORECASTING SYSTEM:

There are three major operational analysis and forecast systems (viz. the global GASP, regional LAPS and the tropical TLAPS) in the NMOC Melbourne. A mesoscale version of LAPS, called MESO_LAPS, provides additional high resolution forecast products over 3 smaller domains (viz., Australia, Sydney and Melbourne). The domains for each of these systems are shown in the figure below. The regional and tropical systems are dependent on the global system for their lateral boundary conditions, whereas the 3 MESO_LAPS systems are all nested in LAPS. An additional system, called TC_LAPS, is run whenever a tropical cyclone is present in the region. Manual intervention is used for mean sea level pressure in both the global and regional systems. The resulting hemispheric "pseudo-observations" for mean sea level pressure are disseminated on the GTS.    The tropical and Australian region

Domains of the operational NWP systems in NMOC Melbourne.

limited area systems use bogus moisture data derived from GMS satellite imagery together with a tropical cyclone bogus scheme. An additional feature of the tropical system is its dynamical nudging. Output from the global system is also used in the cold start procedure for the Australian region and tropical systems. It is noted that the MESO_LAPS  systems do not have their own separate  analyses but currently use initial (and boundary) conditions derived directly from LAPS.

Schematic representation of the operational analysis and prediction system in NMOC.

The global, Australian region and mesoscale streams have associated sea-state systems. There are a large number of other parts to the basic scheme. These include systems for sea surface temperature analysis, environmental emergency response, generation of weather elements from model output (MOF), amendment and dissemination of aviation products, MCIDAS, archives, verification, display and dissemination of products. A schematic representation of the overall system is shown in the figure above.

7.1    System Run Schedule and Forecast Ranges:

At the present time, the centre produces major analyses at 00 and 12 UTC daily for the globe, Australian region and a tropical domain. Global forecasts out to 8 days, Australian region  and tropical forecasts out to 48 hours, and mesoscale forecasts out to 36 hours, are produced off these major analyses. The ECMWF's Supervisor Monitor Scheduler is used to initiate and monitor the various tasks in the operational NWP suite. An approximate daily schedule for the main NWP systems is shown in the table below (with the times during the daylight saving months, November to March, shown in brackets).

System Run Schedule and Forecast Ranges

| SYSTEM | BASE TIME (UTC) | APPROXIMATE START TIME (UTC) | FORECAST AVAILABILITY (UTC) | FORECAST RANGE FROM BASE DATE/TIME (HRS) |
| --- | --- | --- | --- | --- |
| SSTANAL (REGIONAL) | 1200 | 0115 | 0130 | 0 |
| LAPS_PT375 | 0000 | 0145 (0045) | 0215 (0115) | +48 |
| MESO_LAPS_PT125 | 0000 | 0215 (0115) | 0335 (0235) | +36 |
| MESO_LAPS_PT050(ME) | 0000 | 0215 (0115) | 0245 (0145) | +36 |
| MESO_LAPS_PT050(SY) | 0000 | 0245 (0145) | 0330 (0230) | +36 |
| EER PREP (MESO_LAPS_PT050 ME) | 0000 | 0245 (0145) | 0300 (0200) | +36 |
| EER PREP (LAPS) | 0000 | 0315 (0215) | 0330 (0230) | +48 |
| WAVES (REGIONAL) | 0000 | 0315 (0215) | 0325 (0225) | +36 |
| EER PREP (MESO_LAPS_PT050 SY) | 0000 | 0330 (0230) | 0345 (0245) | +36 |
| EER PREP (MESO_LAPS_PT125) | 0000 | 0335 (0235) | 0350 (0250) | +36 |
| TLAPS375 | 0000 | 0345 | 0420 | +48 |
| TC_LAPS | 0000 | 0400 | 0410 | +48 |
| EER PREP (TLAPS375) | 0000 | 0500 | 0520 | +48 |
| GASP | 0000 | 0630 (0530) | 0800 (0700) | +192 |
| EER PREP (GASP) | 0000 | 0730 (0630) | 0830 (0730) | +72 |
| WAVES (GLOBAL) | 0000 | 0730 (0630) | 0750 (0650) | +96 |
| TLAPS375 | 0600 | 1045 | 1130 | +6 |
| TC_LAPS | 0600 | 1100 | 1140 | +6 |
| LAPS_PT375 | 0600 | 1130 (1030) | 1230 (1130) | +6 |
| LAPS_PT375 | 1200 | 1345 (1245) | 1415 (1315) | +48 |
| MESO_LAPS_PT125 | 1200 | 1415 (1315) | 1535 (1435) | +36 |
| MESO_LAPS_PT050(ME) | 1200 | 1415 (1315) | 1445 (1345) | +36 |
| MESO_LAPS_PT050(SY) | 1200 | 1445 (1345) | 1530 (1430) | +36 |
| EER PREP (MESO_LAPS_PT050 ME) | 1200 | 1445 (1345) | 1500 (1400) | +36 |
| EER PREP (LAPS) | 1200 | 1445 (1345) | 1500 (1400) | +48 |
| WAVES (REGIONAL) | 1200 | 1515 (1415) | 1525 (1425) | +36 |
| EER PREP (MESO_LAPS_PT050 SY) | 1200 | 1530 (1430) | 1545 (1445) | +36 |
| EER PREP (MESO_LAPS_PT125) | 1200 | 1535 (1435) | 1550 (1450) | +36 |
| TLAPS375 | 1200 | 1545 | 1620 | +48 |
| TC_LAPS | 1200 | 1600 | 1610 | +48 |
| EER PREP (TLAPS375) | 1200 | 1700 | 1720 | +48 |
| GASP | 1200 | 1830 (1730) | 2000 (1900) | +192 |
| EER PREP (GASP) | 1200 | 1930 (1830) | 2030 (1930) | +72 |
| WAVES (GLOBAL) | 1200 | 1930 (1830) | 1950 (1850) | +96 |
| TLAPS375 | 1800 | 2245 | 2330 | +6 |
| TC_LAPS | 1800 | 2300 | 2340 | +6 |
| LAPS_PT375 | 1800 | 2330 (2230) | 0030 (2330) | +6 |
| SST (SUB-SURFACE) | (Monthly) | 2215 (Tuesdays only) | 2245 (Tuesdays only) | 0 |
| NINO3 | (Monthly) | 2300 (Day 12 or 13 of each month) | 2310 (Day 12 or 13 of each month) | +12 months |
| SSTANAL (GLOBAL) | (Mid-week) | 2315 (Mondays only) | 2345 (Mondays only) | 0 |
| AD HOC (TOP PRIORITY): EER | ANYTIME | ANYTIME | ANYTIME + 30 mins | +72 |
| TC_LAPS | 0000 or 1200 | ANYTIME | ANYTIME + 45 mins | +48 |

7.2    Medium-range Forecasting System (4-10 DAYS):

The acronym GASP is given to the Global ASimilation and Prognosis system, which produces medium-range forecast products out to 8 days. Post-processed products from this system are disseminated on the GTS in GRIB form, nationally through "DIFACS" and MCIDAS, and also via Radio-facsimile broadcasts (AXI and AXM).

7.2.1  Data Assimilation,Objective Analysis and Initialization:

Assimilated data: Mean sea level pressure (surface network, ships, drifting buoys),                   thickness (radiosondes, satellite retrievals), moisture (dew points, satellite precipitable         water), wind (rawinsonde, aircraft, geostationary satellites, constant level balloons),            cloud-      clear radiances (from NOAA orbiting satellites).

Assimilation cycle, including cut-off time: 6 hourly cycling. H+6 cut-off.

Method of analysis: Multivariate statistical interpolation + univariate O.I. for moisture, one-      dimensional variational retrievals (1DVAR).

Analysed variables: Geopotential, wind, moisture.

First guess: 6 hour forecast from previous cycle.

Coverage: Global.

Horizontal resolution: Triangular 239.

Vertical resolution: 29 sigma levels (0.991, 0.975, 0.950, 0.925, 0.900, 0.875, 0.850, 0.800,                       0.750, 0.700, 0.633, 0.566, 0.500, 0.433, 0.366, 0.320, 0.290, 0.260, 0.230,

0.200, 0.170, 0.140, 0.110, 0.090, 0.070, 0.050, 0.030, 0.020, 0.010)

Initialization: Incremental non-linear normal mode.

7.2.2  Model:

Basic equations: Spectral primitive equations.

Independent variables: latitude,longitude,σ,t

Dependent variables: log p*,T,q,vorticity,divergence.

Numerical technique:

horizontal: Spectral.

vertical: Finite difference.

time: Semi-implicit semi-Lagrangian.

Integration domain (in horizontal and vertical): Global, surface to 10 hPa (approx.).

Horizontal and vertical resolution, time step: Triangular 239, 29 sigma levels,

600 sec.(approx.).

Orography, gravity wave drag: Both included.

Horizontal diffusion: Included.

Vertical diffusion: Included.

Planetary boundary layer: Included.

Treatment of sea surface, earth surface and soil: Included.

Radiation: Diurnal cycle, diagnostic clouds, interactive optical properties.

Convection (deep and shallow): Included.

Atmospheric moisture: Included.

Boundaries: Stand alone.

7.2.3  Numerical Weather Prediction Products:

The following post-processed fields are available from GASP:

| Mean sea level pressure | Surface pressure | Evaporation (over ocean) |
| --- | --- | --- |
| Surface temperature | Geopotential height | Snow |
| Temperature | Mixing ratio | Sub-surface temperature |
| Topography | Zonal velocity | High level cloud |
| Meridional velocity | Vorticity | Middle level cloud |
| Divergence | Stream function | Low level cloud |
| Velocity potential | Vertical velocity | Outgoing longwave radiation |
| Radiative tendency | Temperature Tendency | Albedo |
| Mixing ratio tendency | Vorticity surface flux tendency | Net downward radiation at surface |
| Divergence surface flux tendency | Zonal stress | Roughness length at surface |
| Meridional stress | Sensible heat flux | Earth albedo |
| Latent heat flux | Solar heating tendency | Net solar radiation |
| Precipitation | Soil moisture (over land) |  |

7.2.4  Operational Techniques for Applications of NWP Products:

The 10 m wind field from GASP is used to drive a global sea-state model.

7.2.5 Ensemple Prediction System: Not applicable yet.

7.3    Short-range Forecasting System (0-72 HRS):

The Australian region Limited Area Prediction System (LAPS), the Tropical Limited Area Prediction System (TLAPS) and the Mesoscale Limited Area Prediction System (MESO_LAPS) provide short-range forecasting guidance and products that are disseminated nationally through "DIFACS" and MCIDAS and also via Radio-facsimile broadcasts (AXI and AXM). TLAPS and TC_LAPS, for specific tropical cyclone guidance, are run on behalf of RSMC Darwin. Again it is noted that, at present, the 3 MESO_LAPS systems do not have their own assimilation, or analysis, but use an initial starting condition derived directly from LAPS. It is also noted that TC_LAPS runs in 2 basic parts. The first preparatory part produces analyses and prognoses over a large domain, or what is called the Large Scale Environment (LSE), and the second part then generates analyses and forecasts at a higher resolution on a relocatable domain centred on the tropical cyclone (and nested within the LSE part).

7.3.1  Data Assimilation, Objective Analysis and Initialization:

Assimilated data: Surface synop, ship, drifting buoy, radiosonde, rawinsonde, GTS TOVS,          locally processed TOVS, GTS and locally derived GMS cloud drift winds, aircraft single         level winds, bogus MSLP ("pseudo-observations"), synthetic GMS moisture data, tropical        cyclone bogus data.

Assimilation cycle, including cut-off time: 6 hourly cycling; cut-off: LAPS: H+2 hr,

TLAPS: H+4 hr.

Method of analysis: Multivariate statistical interpolation + univariate statistical                                              interpolation for moisture.

Analysed variables: Geopotential, wind, moisture.

First guess: 6 hour forecast from previous cycle.

Coverage:   LAPS: 17.1250N-65.00S, 65.00E-184.6250E

TLAPS: 44.250N-45.00S, 70.00E-188.250E

TC_LAPS: 19.250S-55.00S, 75.00E-159.750E (LSE),  27.00x27.00 (Relocatable)

Horizontal resolution: LAPS and TLAPS: 0.3750

TC_LAPS: 0.750 (LSE) and 0.150 (Relocatable)

Vertical resolution: LAPS, TLAPS: 29 sigma levels (0.9988, 0.9974, 0.9943, 0.9875, 0.9750, 0.9625, 0.9500, 0.9250, 0.9000, 0.8750, 0.8500, 0.8000, 0.7500, 0.7000, 0.6000, 0.5000, 0.4500, 0.4000, 0.3500, 0.3000, 0.2750, 0.2500, 0.2250, 0.2000, 0.1750, 0.1500, 0.1000, 0.0700, 0.0500)

TC_LAPS: 19 sigma levels (0.9910, 0.9750, 0.9500, 0.9000, 0.8500, 0.8000, 0.7500, 0.7000, 0.6000, 0.5000, 0.4000, 0.3500, 0.3000, 0.2500, 0.2000, 0.1500, 0.1000, 0.0700, 0.0500)

Initialization: LAPS and MESO_LAPS: Digital filtering technique.

TLAPS and TC_LAPS: diabatic dynamical nudging scheme incorporating                          GMS IR imagery.

7.3.2  Model:

Basic equations: Grid primitive equations.

Independent variables: x,y,z,t

Dependent variables: P*,T,q,u,v.

Numerical technique:

horizontal: Finite difference.

vertical: Finite difference.

time: Semi-implicit.

Integration domain (in horizontal and vertical):

LAPS: 17.1250N-65.00S, 65.00E-184.6250E, surface to 50 hPa (approx.)

TLAPS: 44.250N-45.00S, 70.00E-188.250E, surface to 50 hPa (approx.)

MESO_LAPS:

Australian: 4.8750S-55.00S, 95.00E-169.8750E, surface to 50 hPa (approx.)

Sydney: 30.050S-38.000S, 147.000E-154.950E, surface to 50 hPa (approx.)

Melbourne: 34.050S-41.000S, 141.000E-150.450E, surface to 50 hPa (approx.)

TC_LAPS:

LSE: 19.250N-55.00S, 75.00E-159.750E, surface to 50 hPa (approx.)

Relocatable: 27.00x27.00 , surface to 50 hPa (approx.).

Horizontal and vertical resolution, time step:

LAPS: 0.3750  , 29 sigma levels, 40 sec

TLAPS: 0.3750  , 29 sigma levels, 40 sec

MESO_LAPS:

Australian: 0.1250, 29 sigma levels, 10 sec

Sydney: 0.050, 29 sigma levels, 5 sec

Melbourne: 0.050, 29 sigma levels, 5 sec

TC_LAPS:

LSE:  0.750 , 19 sigma levels, 40 sec

Relocatable: 0.150 , 19 sigma levels, 15 sec.

Orography, gravity wave drag: Included.

Horizontal diffusion: Included.

Vertical diffusion: Included.

Planetary boundary layer: Included.

Treatment of sea surface, earth surface and soil: Included.

Soil moisture analysis: Included in LAPS, TLAPS, TC_LAPS and MESO_LAPS.

Radiation: Diurnal cycle, diagnostic clouds, interactive optical properties.

Convection (deep and shallow): Included.

Atmospheric moisture: Included.

Boundaries:  LAPS, TLAPS and TC_LAPS (LSE): Lateral boundaries from GASP.

MESO_LAPS (3 domains): Lateral boundaries from LAPS.

TC_LAPS (Relocatable): Lateral boundaries from LSE TC_LAPS.

7.3.3  Numerical Weather Prediction Products:

The following post-processed fields are available from the Limited Area Prediction Systems:

| Mean sea level pressure | Dew point depression | V-component of wind |
| --- | --- | --- |
| Surface temperature | Equivalent potential temperature | Potential temperature |
| Convective precipitation | Ucomponent ageostrophic wind | Divergence |
| Thickness (1000-500 hPa) | Shearing deformation | Relative humidity |
| Temperature gradient at 950 hPa | Ucomponent of deformation | Temperature advection |
| Lifting condensation level | Q vector in x-direction | Stretching deformation |
| Grassland fire danger index | U-component stream function | Pressure of cloud top |
| Surface mixing ratio | Moisture advection | Vertical velocity |
| Boundary layer convective energy flux | Surface pressure | Wet bulb potential temperature |
| Sensible heat | Non-convective precipitation | Frontogenesis function |
| U-component of wind | Total precipitation | Vcomponent ageostrophic wind |
| Temperature | Total totals index | 1000-500 hPa shear |
| Geopotential height | Topography | Vcomponent of deformation |
| Dew point temperature | Lifting index | Q vector in y-direction |
| Wind speed | Forest fire danger index | V-component stream function |
| Vorticity | Mixing ratio | Moisture convergence |
| Cloud cover | Stream function |  |
| Vorticity advection | Latent heat |  |

7.3.4  Operational Techniques for Applications of NWP Products:

The 10 m wind field from LAPS and MESO_LAPS are used to drive sea-state models for the Australian region and smaller domains. The Model Output Forecast (MOF) system, which is driven by LAPS and GASP, is used to produce numerous weather elements including temperatures (minimum, maximum,dry bulb, dew point, wet bulb and ground minimum), wind (speed and direction), precipitation, cloud amount, evaporation, sunshine and visibility. Meteograms, giving time series of meteorological variables, are also available. In addition, there is available thunderstorm, based on a decision tree approach, and cold-season tornado (“COLDIES”) guidance, with input from (the Australian domain) MESO_LAPS.

7.4    Specialized Forecasts:

An analogue/regression tropical cyclone model ("TOPEND") is available for providing guidance to the Australian Tropical Cyclone Warning Centres. Specialized sea-state forecasts are provided for the North West Cape and Bass Strait gas and oil fields.

7.4.1  Sea Wave Models:

The following table summarises the characteristics of the seastate system in the NMOC:

| Domain | Global | Australian Region | South East Australian |
| --- | --- | --- | --- |
| Numerical Scheme | Deep water 3rd generation (WAM) | Deep water 3rd generation (WAM) | Shallow water 3rd generation (WAM) |
| Wind data source | GASP (10m) | LAPS_PT375 (10m) | MESO_LAPS_PT125 (10m) |
| Grid | Latitude/ longitude | Latitude/ longitude | Latitude/ longitude |
| Resolution | 30 | 10 | 0.250 |
| Nesting | Stand alone | Within Global | Within Regional |
| Start time of forecast | 00,12 UTC | 00, 12 UTC | 00, 12 UTC |
| Initial state | 12 hr hindcasting and assimilation of satellite (ERS) altimeter data |  | No assimilation |
| Model output | Wind and swell significant wave height, period and direction. Significant wave spectra and probabilities. |  |  |
| Verification | With respect to rigs, buoys and satellite (ERS) altimeter data |  |  |

7.4.2  Storm Surge System:

A system capable of forecasting storm surges caused by tropical cyclones is currently driven by wind and pressure field distributions defined according to the central pressure and maximum wind radius bogussed for tropical cyclones by Darwin RFC.

7.4.3  Air Dispersion Model:

An air dispersion, or transport, system is available for running on demand, in an ad-hoc mode, and can produce forecast trajectories, concentrations (or exposures) and depositions for nuclear accident, volcanic ash, smoke and other episodes. Currently, the operational Environmental Emergency Response system consists of the Hybrid Single_Particle Lagrangian Integrated Trajectories (HY-SPLIT Version 4.0) system, developed at the NOAA Air Resources Laboratory, with meteorological input from the operational NWP systems in NMOC (viz., GASP, LAPS, TLAPS, and MESO_LAPS). Analysed backward trajectories are also available from GASP, LAPS and TLAPS in operations.

7.4.4  Solar Ultraviolet (UV) Radiation Forecast System:

Forecasts out to 36 hour forecasts of a UV index (defined as the product of the UV irradiance and a human skin response function) are produced operationally. The system analyses ozone concentrations, available from the global 120 km GTS TOVS data, using 2-dimensional univariate statistical interpolation. Forecasts of the ozone distribution are then computed using isentropic fields derived from GASP output. From  vertical profiles of temperature and ozone, the UV index is calculated. Currently, forecasts of the UV index are produced, once per day, after completion of the 1200 UTC run of GASP.

7.5 Extended-range Forecasts (10 - 30 DAYS): Not applicable yet.

7.6 Long-range Forecasts (30 DAYS - 2 YEARS):

A three-month rainfall seasonal climate outlook is prepared. Each month, a risk-assessment for three-month total rainfall across Australia is issued mid-month for the three-month period starting the following month. Probabilities are calculated for the three-month total rainfall being in the lowest one-third of historical falls (tercile 1), the middle one-third (tercile 2), and the upper one-third (tercile 3). The technique used is discriminant analysis, with the inputs being derived from recent Sea Surface Temperature (SST) patterns. Subsidiary techniques involved in the forecast model include principal component analysis of SSTs for the Pacific Ocean, Indian Ocean and Southern Ocean, and principal component analysis of rainfall patterns across Australia. SST EOF (Empirical Orthogonal Function) loadings, at one and three months lag, for the Pacific Ocean ENSO pattern and the Indian Ocean pattern are the current predictor inputs. The tercile probabilities, computed across Australia on a 10x10 grid are published in the form of contoured maps, tabulated averages for the 107 Australian rainfall districts, and tabulated interpolations for cities and towns around Australia. Similar outlooks are now provided for above/below median and for both maximum and minimum temperatures.

Additional guidance at the rainfall district level is presented in the form of stratified rainfall climatologies based on recent values of the SOI (Southern Oscillation Index). Rainfall outcomes for eastern Australia, obtained from SOI analogues, are also described.

Additional forecasts for NINO3 are provided based on an intermediate coupled atmosphere-ocean with sub-surface ocean temperature assimilation. A coupled atmosphere-ocean GCM (General Circulation Model) combined with a sub-surface ocean temperature data assimilation system has been developed and is currently being used to routinely provide forecasts which are currently being assessed.

8.     VERIFICATIONS OF PROGNOSTIC PRODUCTS:

An annual summary of verification statistics for 2000, for the Australian regional and global schemes, is given in the following tables.

The following abbreviations have been used in the tables:

S1         - 30 day mean Teweles skill score over Australian verification area

r           - anomaly correlation coefficient between forecast heights and climatology over                   Australian verification area

PERSIS  - 24, 36 or 48 hour persistence prediction

REGN    - Australian Regional System

GASP     - Global Assimilation and Prognosis model

RMSE    - Root Mean Square Error

Note:

REGN refers to LAPS (Limited Area Prediction System).

The LAPS and GASP results are with respect to their own analyses.

8.1   Skill Scores and Anomaly Correlation Coefficients:

24 HR VERIFICATION STATISTICS - AUSTRALIAN REGION 2000

BASE TIME: 0000UTC - VALID TIME: 0000UTC

|  |  |  | JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M S L P | S1 S1 r | PERSIS REGN REGN | 54 25 .97 | 53 23 .95 | 56 24 .93 | 48 23 .94 | 46 21 .96 | 49 20 .97 | 55 22 .97 | 59 24 .96 | 57 23 .96 | 59 22 .96 | 53 24 .96 | 45 21 .96 |
| 5 h 0 e 0 i h g p h a t | S1 S1 r | PERSIS REGN REGN | 45 18 .97 | 49 18 .96 | 45 17 .96 | 43 16 .97 | 42 16 .97 | 47 16 .98 | 45 15 .97 | 47 16 .97 | 43 15 .97 | 45 15 .97 | 43 16 .98 | 39 14 .97 |
| 2 h 5 e 0 i h g p h a t | S1 S1 r | PERSIS REGN REGN | 41 15 .97 | 44 14 .96 | 40 14 .97 | 38 13 .97 | 35 13 .97 | 39 12 .97 | 36 12 .97 | 38 13 .97 | 39 12 .96 | 40 12 .97 | 39 14 .98 | 37 12 .97 |

36 HR VERIFICATION STATISTICS - AUSTRALIAN REGION 2000

BASE TIME: 1200UTC - VALID TIME: 0000UTC

|  |  |  | JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M S L P | S1 S1 r | PERSIS GASP GASP | 66 29 .95 | 63 28 .93 | 66 27 .92 | 57 25 .95 | 56 25 .95 | 61 24 .96 | 65 26 .95 | 73 28 .96 | 64 26 .95 | 70 26 .94 | 64 25 .95 | 55 24 .94 |
| 5 h 0 e 0 i h g p h a t | S1 S1 r | PERSIS GASP GASP | 55 22 .96 | 60 23 .94 | 54 21 .95 | 51 20 .96 | 50 20 .95 | 59 20 .96 | 53 19 .95 | 59 19 .95 | 50 17 .96 | 56 18 .96 | 52 19 .97 | 49 16 .96 |
| 2 h 5 e 0 i h g p h a t | S1 S1 r | PERSIS GASP GASP | 49 18 .96 | 54 18 .95 | 48 17 .96 | 46 16 .96 | 42 16 .96 | 48 15 .95 | 43 14 .95 | 47 14 .96 | 46 13 .95 | 50 14 .97 | 46 16 .97 | 46 14 .97 |

48 HR VERIFICATION STATISTICS - AUSTRALIAN REGION 2000

BASE TIME: 0000UTC - VALID TIME: 0000UTC

|  |  |  | JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M S L P | S1 S1 r | PERSIS GASP GASP | 75 35 .93 | 68 33 .90 | 69 33 .88 | 60 30 .91 | 60 30 .92 | 66 31 .92 | 69 31 .94 | 78 35 .93 | 69 30 .92 | 76 31 .91 | 69 30 .93 | 59 30 .90 |
| 5 h 0 e 0 i h g p h a t | S1 S1 r | PERSIS GASP GASP | 60 26 .95 | 63 26 .92 | 56 25 .91 | 55 23 .94 | 54 25 .93 | 64 25 .93 | 58 23 .93 | 64 24 .92 | 53 19 .94 | 60 21 .94 | 55 22 .95 | 52 20 .94 |
| 2 h 5 e 0 i h g p h a t | S1 S1 r | PERSIS GASP GASP | 52 21 .94 | 56 22 .92 | 50 20 .93 | 49 19 .94 | 46 19 .93 | 53 18 .93 | 47 17 .94 | 50 17 .93 | 46 15 .94 | 54 17 .95 | 49 19 .95 | 49 18 .94 |

8.2  Root Mean Square Errors (Annual 2000):

| AREA | FIELD | RMSE UNIT | VERSUS | +24HR |  | +72HR |  | +120HR |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | 00UTC | 12UTC | 00UTC | 12UTC | 00UTC | 12UTC |
| NH | Z500 | m | Analyses | 17.2 | 17.1 | 42.7 | 42.8 | 69.7 | 70.0 |
| SH | Z500 | m | Analyses | 22.0 | 21.7 | 53.6 | 53.0 | 82.3 | 81.2 |
| NH | W250 | m/s | Analyses | 5.9 | 6.0 | 11.6 | 11.6 | 16.6 | 16.7 |
| SH | W250 | m/s | Analyses | 6.5 | 6.5 | 13.2 | 13.1 | 18.5 | 18.4 |
| TROPICS | W250 | m/s | Analyses | 5.5 | 5.6 | 8.4 | 8.3 | 10.0 | 9.9 |
| TROPICS | W850 | m/s | Analyses | 3.1 | 3.3 | 4.3 | 4.5 | 4.9 | 5.1 |

9.  PLANS FOR THE FUTURE:

Plans for future operational systems in the NMOC Melbourne include:

. an ongoing improvement and generalization of data processing, graphical display and editing    systems;

. the incorporation of the second node NEC SX-5 into operations;

. the introduction of a number of changes into LAPS_PT375 including: a warm running        assimilation with soil moisture nudging, parameterisation improvements for cloud and        radiation, a semi-implicit semi-Lagrangian formulation, more vertical levels, a non-           hydrostatic formulation and ensemble prediction;

. the introduction of a mesoscale assimilation system;

. enhancements to GASP incorporating: locally derived cloud drift winds and ERS              scatterometer winds, increased vertical resolution (50 levels up to 0.1 hPa), a longer forecast    period (viz. 10 days), 3DVAR and an ensemble prediction system;

. the implementation of an urban air quality forecasting system;

. an upgrade to a statistical interpolation version of the rainfall analysis system and the         introduction of a rainfall verification scheme;

. a move to drive the storm surge model using meteorological input from TC_LAPS;

. a move to produce the 96-hour global seastate forecasts at an improved resolution of 1.00;

. an ongoing improvement to the operational Environmental Emergency Response System     including the use of a unified wind input system and an extension to include a number of    chemical transformations;

. the introduction of a fully coupled ocean-atmospheric model for seasonal analysis and        prediction.

10.    REFERENCES:

Bourke W., Hart T., Steinle P., Seaman R., Embery G., Naughton M. and Rikus L. : "Evolution of the Bureau of Meteorology's Global Data Assimilation and Prediction System. Part 2: Resolution Enhancements and Case Studies." Australian Meteorological Magazine, 44, 19-40, 1995.

Davidson N.E. and Puri K. : "Tropical prediction using dynamical nudging, satellite defined convective heat source and a cyclone bogus." Monthly Weather Review, 120, 2501-2522, 1992.

Davidson N.E. and Webber H.C.: "The BMRC high resolution tropical cyclone prediction system TC-LAPS.”  Monthly Weather Review, 128, 1245-1265, 2000.

Draxler R.R. and Hess G.D. : "An overview of the HYSPLIT_4 modelling system for trajectories, dispersion and deposition." Australian Meteorological Magazine, 47, 295-308,  1998.

Harris B. and Steinle P.: “Variational TOVS Radiance Assimilation in the GASP Model in BMRC.” Technical Proceedings of The Tenth International ATOVS Study Conference, 241-257. Boulder, Colerado, 27January - 2 February, 1999.

Le Marshall J., Pescod N., Seaman R., Mills G. and Stewart P. : "An Operational System for Generating Cloud Drift Winds in the Australian Region and Their Imapct on Numerical Weather Prediction."  Weather and Forecasting, 9, 361-370, 1994.

Le Marshall J.F., Riley P.A., Rouse B.J., Mills G.A., Wu Z.-J., Stewart P.K. and Smith W.L.: "Real-time assimilation and synoptic application of local TOVS raw radiance observations." Australian Meteorological Magazine, 43, 153-166, 1994.

Mills G.A. and Colquhoun J.R.:” Objective Prediction of Severe Thunderstorm Environments: Preliminary Results Linking a Decision Tree with an Operational Regional NWP Model.” Weather and Forecasting, 13, 1078-1092 1998.

Puri K., Dietachmayer G.S., Mills G.A., Davidson N.E., Bowen R.A. and Logan L.W. : "The new BMRC Limited Area Prediction System, LAPS." Australian Meteorological Magazine, 47, 203-223, 1998.

Seaman R., Bourke W., Steinle P., Hart T., Embery G., Naughton M. and Rikus L. : "Evolution of the Bureau of Meteorology's Global Data Assimilation and Prediction System. Part 1: Analysis and Initialisation." Australian Meteorological Magazine, 44, 1-18, 1995.

Stewart P.K. : "RSMC Melbourne - Procedures, Standards, Results of Exercices and Ongoing Products." WMO Expert Team on Environmental Emergency Response. Beijing, China, 20-24 September 1999.