ANNUAL WWW TECHNICAL PROGRESS REPORT ON THE GDPS

COUNTRY: Australia      CENTRE: NMOC Melbourne                          January 2002

1.     SUMMMARY OF HIGHLIGHTS (2001):

Meteorological, Oceanographic and Computer Systems:

| 2 April: | Replacement of operational manual Australian Region mean sea level pressure prognosis by Horace on-screen manual-computer version. |
| --- | --- |
| 9 April: | Horizontal resolution of Global Wave Model upgraded to 10 (latitude/longitude). |
| 9 May: | MESO_LAPS_PT050 (Melbourne and Sydney domains) running on second node of NEC SX-5. |
| 22 May: | Global EER Test. |
| 3 July: | Test GASP Ensemble Prediction System running in Real-Time. |
| 27 August: | Replacement of operational manual Australian Region mean sea level pressure analysis by Horace on-screen manual-computer version. |
| 1 October: | GASP forecast period extended from 8 days to 10 days. |
| 2 October: | Test version of Kriging rainfall analysis running in Real-Time. |
| 31 October: | Operational scheduling / data base computer replaced. |
| 1 November: | Replacement of operational manual Southern Hemisphere mean sea level pressure analysis by Horace on-screen manual-computer version. |
| 18 December: | Change to Charnock factor in all LAPS systems. |

2.     EQUIPMENT IN USE AT CENTRE:

The following table shows the main computer systems used in NMOC Melbourne, with their basic functions:

| FUNCTION | COMPUTER | NO. OF CPUS | MEMORY | OPERATING SYSTEM | DISK STORAGE |
| --- | --- | --- | --- | --- | --- |
| Supercomputing (Assimilation and Prediction) | Dual-Node NEC SX-5 | Node 1: 16 Node 2: 16 | Node 1: 128 GB Node 2: 96 GB | SUPER-UX 10.2 SX-5 | 2.3 TB |
| Communications / Message Switching | (i) HP D380/2 (ii) HP D380/2 | (i) 2 (ii) 2 | (i) 768 MB (ii) 768 MB | (i) HP-UX 10.20 (ii) HP-UX 10.20 | 89 GB |
| Scheduling / Data Base | (i) HP N4000-55 (ii) HP N4000-55 | (i) 4 (ii) 4 | (i) 4096 MB (ii)4096 MB | (i) HP-UX 11.00 (ii) HP-UX 11.00 | (i) 6 GB (ii) 6 GB |
| Post-Processing / Graphics Processing | (i) HP D390 (ii) HP D390 | (i) 2 (ii) 2 | (i) 1500 MB (ii)1500 MB | (i) HP-UX 10.20 (ii) HP-UX 10.20 | (i) 8 GB (ii) 8 GB |
| Satellite Post-Processing | (i) HP D350 (ii) HP D350 | (i) 1 (ii) 1 | (i) 256 MB (ii) 256 MB | (i) HP-UX 10.20 (ii) HP-UX 10.20 | (i) 10 GB (ii) 10 GB |
| Horace | (i) HP C3600 (ii) HP C3600 (iii)HP C3600 | (i) 1 (ii) 1 (iii) 1 | (i) 512 MB (ii) 512 MB (iii) 512 MB | (i) HP-UX 10.20 (ii) HP-UX 10.20 (iii)HP-UX 10.20 | (i) 27 GB (ii) 35 GB (iii)30 GB |
| RADAR and Visualisation | (i) SGI Octane (ii) SGI-O2 | (i) 1 (ii) 1 | (i) 512 MB (ii) 128 MB | (i) IRIX 6.5 (ii) IRIX 6.5 | (i) 17 GB (ii)8.5 GB |
| web / ftp | (i) HP D390 (ii) HP D310 | (i) 2 (ii) 1 | (i) 512 MB (ii) 512 MB | (i) HP-UX 10.20 (ii) HP-UX 10.20 | (i) 18 GB (ii) 35 GB |
| MARS | 4-Node IBM RS/6000 SP | High Node 1: 4 High Node 2: 4 Wide Node 1: 2 Wide Node 2: 2 | 1 GB / cpu | AIX 4.3 | 1.5 TB |
| Development | (i) HP D380 (ii) HP RP4000 | (i) 2 (ii) 4 | (i) 1 GB (ii) 6 GB | (i) HP-UX 10.20 (ii) HP-UX 11.11 | (i) 32 GB (ii) 1.8 TB |

Peripheral Equipment:

Magnetic Cartridge Archive System:

StorageTek Mass Store 4400 ACS (Automatic Cartridge System)

1 StorageTek 9710 Library Storage Module (with a 37 TB capacity)

6 DLT (Digital Linear Tape) Units

24 drives, for 9840 fibre channel tapes, in silo (10 for SAM-FS, 8 for MARS and 6                for backup)

Hardcopy Printers/Plotters:

HP DesignJet 1055cm plus and 650C plotters

HP LaserJet 5 SiMX printers

HP LaserJet 4500DN

HP DeskJet 1600CM

Software in use at Centre:

The overall computer environment in the NMOC is mainly Unix. A real-time data base, currently using ORACLE 8.1.7.0.0, is used for storage of observational data and grids from the various NWP systems. The U.S. Navy's Environmental Operational Nowcasting System (NEONS) software is commonly used for accessing the data base. The operational NWP models are written mainly in Fortran, with many of the associated files having the NetCDF structure. Most displays are produced using the NCAR graphics package and IDL. The UK Met. Office’s Horace (V3.71) system is used to prepare, in an on-screen mode, manual-computer products for: significant weather prognoses, Australian Region surface analyses and prognoses and Southern Hemisphere surface analyses. Sam-fs is currently being used for magnetic cartridge archives in the NMOC. The Meteorological Archive and Retrieval System (MARS from the ECMWF) is currently being developed for research and operational use.

Other Systems in use at Centre:

The DIFACS system is used to to disseminate a selection of basic analysis and prognostic charts, and some satellite imagery, to the Bureau's regional offices and some outside users. MCIDAS is used for comprehensive interaction and display of satellite imagery and products, observational and gridded data, and is also a major component of the Australian Integrated Forecast System (AIFS). Products from the NWP systems are written to internal and external (www.bom.gov.au) web servers. Magnetic cartridge archives are kept of various NWP products with Australian region analyses available back to 1970 and Southern Hemisphere analyses back to 1972. Hard copy and microfilm archives of charts also exist. An aviation system, which interacts with the WAFS data, is used to view and display the data and prepare the various flight and route forecasts. Regular statistics (including S1 skill scores, root mean square errors and anomaly correlations) monitoring and comparing the performance of the NMOC's NWP systems (and also some overseas NWP models) are also produced.

3.     DATA AND PRODUCTS FROM GTS IN USE:

The following table gives a list of the major observation report types used in the NMOC Melbourne and the approximate numbers received in a 24-hour period:

| Observational Data Type or Report Type | Approximate number received during 24 hour period (unless otherwise stated) |
| --- | --- |
| SYNOP | 41000 |
| SHIP | 5300 |
| TEMP | 1200 |
| PILOT | 850 |
| BUOY | 11000 |
| AIREP / AMDAR | 23000 |
| SATOB | 250000 |
| SATEM | 21000 |
| ATOVS (120KM) | 85000 |
| METAR | 15000 |
| CLIMAT | 1500 / month |
| SATOB_SST | 6000 |
| BATHY | 100 |
| WAVEOB | 900 |
| TRACKOB | 100 |
| ACAR | 80000 |
| AMV | 550000 |
| TOVS1C | 250000 |
| SAT_ALT | 60000 |
| QUIKSCAT | 1100000 |

The following Gridded Products are also received in NMOC Melbourne:

GRIB (ECMWF)

GRIB (EGRR)

GRIB (KWBC)

GRIB (JMA)

GRID (ECMWF)

4.     DATA INPUT STREAM:

Automated. (Some manual intervention is available for correction of reports.) The observational data, along with NWP gridded data, is stored in a real-time relational data base system (ORACLE/NEONS).

5.     QUALITY CONTROL SYSTEM:

Validity checks are currently confined to within the respective assimilation or analysis schemes. Some gross checking outside these schemes may eventually be installed.

6.     MONITORING OF THE OBSERVING SYSTEM:

Monitoring of the observing system is carried out. The quantity of data available is monitored in real-time to ensure that reports are being received reliably and are made available to the operational systems. For the global system, statistics on the difference between observations and the first guess and analysis fields are routinely prepared to identify any problems with either the analysis system or individual data types. Lists of rejected data are also used to identify unreliable reporting from particular observing platforms.

7.     FORECASTING SYSTEM:

There are three major operational analysis and forecast systems (viz. the global GASP, regional LAPS and the tropical TLAPS) in the NMOC Melbourne. A mesoscale version of LAPS, called MESO_LAPS, provides additional high resolution forecast products over 3 smaller domains (viz., Australia, Sydney and Melbourne). The domains for each of these systems are shown in the figure below. The regional and tropical systems are dependent on the global system for their lateral boundary conditions, whereas the 3 MESO_LAPS systems are all nested in LAPS. An additional system, called TC_LAPS, is run to provide tropical cyclone, and other tropical guidance, for the region. (The possible extent of this guidance is also depicted in the figure below.) Manual intervention is used for mean sea level pressure in both the global and regional systems. The resulting hemispheric "pseudo-observations" for mean sea level pressure are disseminated on the GTS.   The tropical and Australian region limited area systems use bogus moisture data derived from GMS satellite imagery together with a tropical cyclone synthetic specification scheme. An additional feature of the tropical system is its dynamical nudging. Output from the global system is also used in the cold start procedure for the Australian region and tropical systems. It is noted that the MESO_LAPS  systems do not have their own separate  analyses but currently use initial (and boundary) conditions derived directly from LAPS.

Domains of the operational NWP systems in NMOC Melbourne.

The global, Australian region and mesoscale streams have associated sea-state systems. There are a large number of other parts to the basic scheme. These include systems for sea surface temperature analysis, environmental emergency response, generation of weather elements from model output (MOF), amendment and dissemination of aviation products, MCIDAS, archives, verification, display and dissemination of products. A schematic representation of the overall system is shown in the figure below.

Schematic representation of the operational analysis and prediction system in NMOC.

7.1    System Run Schedule and Forecast Ranges:

At the present time, the centre produces major analyses at 00 and 12 UTC daily for the globe, Australian region and a tropical domains. Global forecasts out to 10 days, Australian region  and tropical forecasts out to 48 hours, mesoscale forecasts out to 36 hours, and special tropical cyclone forecasts out to 72 hours are produced off these major analyses. The ECMWF's Supervisor Monitor Scheduler is used to initiate and monitor the various tasks in the operational NWP suite. An approximate daily schedule for the main NWP systems is shown in the table below (with the times during the daylight saving months, November to March, shown in brackets).

System Run Schedule and Forecast Ranges

| SYSTEM | BASE TIME (UTC) | APPROXIMATE START TIME (UTC) | FORECAST AVAILABILITY (UTC) | FORECAST RANGE FROM BASE DATE/TIME (HRS) |
| --- | --- | --- | --- | --- |
| SSTANAL (REGIONAL) | 1200 | 0115 | 0130 | 0 |
| LAPS_PT375 | 0000 | 0145 (0045) | 0215 (0115) | +48 |
| MESO_LAPS_PT125 | 0000 | 0215 (0115) | 0335 (0235) | +36 |
| MESO_LAPS_PT050(ME) | 0000 | 0215 (0115) | 0245 (0145) | +36 |
| MESO_LAPS_PT050(SY) | 0000 | 0245 (0145) | 0330 (0230) | +36 |
| EER PREP (MESO_LAPS_PT050 ME) | 0000 | 0245 (0145) | 0300 (0200) | +36 |
| EER PREP (LAPS) | 0000 | 0315 (0215) | 0330 (0230) | +48 |
| WAVES (REGIONAL) | 0000 | 0315 (0215) | 0325 (0225) | +36 |
| EER PREP (MESO_LAPS_PT050 SY) | 0000 | 0330 (0230) | 0345 (0245) | +36 |
| EER PREP (MESO_LAPS_PT125) | 0000 | 0335 (0235) | 0350 (0250) | +36 |
| TLAPS375 | 0000 | 0345 | 0420 | +48 |
| TC_LAPS | 0000 | 0400 | 0410 | +72 |
| EER PREP (TLAPS375) | 0000 | 0500 | 0520 | +48 |
| GASP | 0000 | 0630 (0530) | 0800 (0700) | +240 |
| GASP_EPS | 0000 | 0710 (0610) | 0900 (0800) | +240 |
| EER PREP (GASP) | 0000 | 0730 (0630) | 0830 (0730) | +72 |
| WAVES (GLOBAL) | 0000 | 0730 (0630) | 0750 (0650) | +96 |
| TLAPS375 | 0600 | 1045 | 1130 | +6 |
| TC_LAPS | 0600 | 1100 | 1140 | +6 |
| LAPS_PT375 | 0600 | 1130 (1030) | 1230 (1130) | +6 |
| LAPS_PT375 | 1200 | 1345 (1245) | 1415 (1315) | +48 |
| MESO_LAPS_PT125 | 1200 | 1415 (1315) | 1535 (1435) | +36 |
| MESO_LAPS_PT050(ME) | 1200 | 1415 (1315) | 1445 (1345) | +36 |
| MESO_LAPS_PT050(SY) | 1200 | 1445 (1345) | 1530 (1430) | +36 |
| EER PREP (MESO_LAPS_PT050 ME) | 1200 | 1445 (1345) | 1500 (1400) | +36 |
| EER PREP (LAPS) | 1200 | 1445 (1345) | 1500 (1400) | +48 |
| WAVES (REGIONAL) | 1200 | 1515 (1415) | 1525 (1425) | +36 |
| EER PREP (MESO_LAPS_PT050 SY) | 1200 | 1530 (1430) | 1545 (1445) | +36 |
| EER PREP (MESO_LAPS_PT125) | 1200 | 1535 (1435) | 1550 (1450) | +36 |
| TLAPS375 | 1200 | 1545 | 1620 | +48 |
| TC_LAPS | 1200 | 1600 | 1610 | +72 |
| EER PREP (TLAPS375) | 1200 | 1700 | 1720 | +48 |
| GASP | 1200 | 1830 (1730) | 2000 (1900) | +240 |
| GASP_EPS | 1200 | 1910 (1810) | 2100 (2000) | +240 |
| EER PREP (GASP) | 1200 | 1930 (1830) | 2030 (1930) | +72 |
| WAVES (GLOBAL) | 1200 | 1930 (1830) | 1950 (1850) | +96 |
| TLAPS375 | 1800 | 2245 | 2330 | +6 |
| TC_LAPS | 1800 | 2300 | 2340 | +6 |
| LAPS_PT375 | 1800 | 2330 (2230) | 0030 (2330) | +6 |
| SST (SUB-SURFACE) | (Monthly) | 2215 (Tuesdays only) | 2245 (Tuesdays only) | 0 |
| NINO3 | (Monthly) | 2300 (Day 12 or 13 of each month) | 2310 (Day 12 or 13 of each month) | +12 months |
| SSTANAL (GLOBAL) | (Mid-week) | 2315 (Mondays only) | 2345 (Mondays only) | 0 |
| AD HOC (TOP PRIORITY): EER | ANYTIME | ANYTIME | ANYTIME + 30 mins | +72 |
| TC_LAPS | 0000 or 1200 | ANYTIME | ANYTIME + 45 mins | +72 |

7.2    Medium-range Forecasting System (4-10 DAYS):

The acronym GASP is given to the Global ASimilation and Prognosis system, which produces medium-range forecast products out to 10 days. Post-processed products from this system are disseminated on the GTS in GRIB form, nationally through "DIFACS" and MCIDAS, and also via Radio-facsimile broadcasts (AXI and AXM).

7.2.1  Data Assimilation, Objective Analysis and Initialization:

Assimilated data: Mean sea level pressure (surface network, ships, drifting buoys),                   thickness (radiosondes, satellite retrievals), moisture (dew points, satellite precipitable         water), wind (rawinsonde, aircraft, geostationary satellites, constant level balloons),            cloud-clear radiances (from NOAA orbiting satellites).

Assimilation cycle, including cut-off time: 6 hourly cycling. H+6 cut-off.

Method of analysis: Multivariate statistical interpolation + univariate O.I. for moisture, one-      dimensional variational retrievals (1DVAR).

Analysed variables: Geopotential, wind, moisture.

First guess: 6 hour forecast from previous cycle.

Coverage: Global.

Horizontal resolution: Triangular 239.

Vertical resolution: 29 sigma levels (0.991, 0.975, 0.950, 0.925, 0.900, 0.875, 0.850, 0.800,                       0.750, 0.700, 0.633, 0.566, 0.500, 0.433, 0.366, 0.320, 0.290, 0.260, 0.230,

0.200, 0.170, 0.140, 0.110, 0.090, 0.070, 0.050, 0.030, 0.020, 0.010)

Initialization: Incremental non-linear normal mode.

7.2.2  Model:

Basic equations: Spectral primitive equations.

Independent variables: latitude,longitude,σ,t

Dependent variables: log p*,T,q,vorticity,divergence.

Numerical technique:

horizontal: Spectral.

vertical: Finite difference.

time: Semi-implicit semi-Lagrangian.

Integration domain (in horizontal and vertical): Global, surface to 10 hPa (approx.).

Horizontal and vertical resolution, time step: Triangular 239, 29 sigma levels,

600 sec.(approx.).

Orography, gravity wave drag: Both included.

Horizontal diffusion: Included.

Vertical diffusion: Included.

Planetary boundary layer: Included.

Treatment of sea surface, earth surface and soil: Included.

Radiation: Diurnal cycle, diagnostic clouds, interactive optical properties.

Convection (deep and shallow): Included.

Atmospheric moisture: Included.

Boundaries: Stand alone.

Albedo: Climatology.

SST Analysis: Weekly (10x10).

7.2.3  Numerical Weather Prediction Products:

The following post-processed fields are available from GASP:

| Mean sea level pressure | Surface pressure | Evaporation (over ocean) |
| --- | --- | --- |
| Surface temperature | Geopotential height | Snow |
| Temperature | Mixing ratio | Sub-surface temperature |
| Topography | Zonal velocity | High level cloud |
| Meridional velocity | Vorticity | Middle level cloud |
| Divergence | Stream function | Low level cloud |
| Velocity potential | Vertical velocity | Outgoing longwave radiation |
| Radiative tendency | Temperature Tendency | Albedo |
| Mixing ratio tendency | Vorticity surface flux tendency | Net downward radiation at surface |
| Divergence surface flux tendency | Zonal stress | Roughness length at surface |
| Meridional stress | Sensible heat flux | Earth albedo |
| Latent heat flux | Solar heating tendency | Net solar radiation |
| Precipitation | Soil moisture (over land) |  |

7.2.4  Operational Techniques for Applications of NWP Products:

The 10 m wind field from GASP is used to drive a global sea-state model.

7.2.5 Ensemble Prediction System:

An Ensemble Prediction System based on the GASP system is currently being run in test mode in real-time in NMOC Melbourne. The 33-member ensemble system is running at the resolution: T79/19L and producing forecasts out to 10 days, off 00 and 12 UTC. Singular vectors are used to perturb the initial state derived from GASP. These perturbed states are then used as the initial conditions for each of the ensemble members.

7.3    Short-range Forecasting System (0-72 HRS):

The Australian region Limited Area Prediction System (LAPS), the Tropical Limited Area Prediction System (TLAPS) and the MESOscale Limited Area Prediction System (MESO_LAPS) provide short-range forecasting guidance and products that are disseminated nationally through "DIFACS" and MCIDAS and also via Radio-facsimile broadcasts (AXI and AXM). TLAPS and TC_LAPS, for specific tropical cyclone guidance, are run on behalf of RSMC Darwin. Again it is noted that, at present, the 3 MESO_LAPS systems do not have their own assimilation, or analysis, but use an initial starting condition derived directly from LAPS. It is also noted that TC_LAPS runs in 2 basic parts. The first preparatory part produces analyses and prognoses over a large domain, or what is called the Large Scale Environment (LSE), and the second part then generates analyses and forecasts at a higher resolution on a relocatable domain centred on the tropical cyclone (and nested within the LSE part).

7.3.1  Data Assimilation, Objective Analysis and Initialization:

Assimilated data: Surface synop, ship, drifting buoy, radiosonde, rawinsonde, GTS TOVS,          locally processed TOVS, GTS and locally derived GMS cloud drift winds, aircraft single         level winds, bogus MSLP ("pseudo-observations"), synthetic GMS moisture data, tropical        cyclone synthetic data.

Assimilation cycle, including cut-off time: 6 hourly cycling; cut-off: LAPS: H+2 hr,

TLAPS: H+4 hr.

Method of analysis: Multivariate statistical interpolation + univariate statistical                                              interpolation for moisture.

Analysed variables: Geopotential, wind, moisture.

First guess: 6 hour forecast from previous cycle.

Coverage:   LAPS: 17.1250N-65.00S, 65.00E-184.6250E

TLAPS: 44.250N-45.00S, 70.00E-188.250E

TC_LAPS: 56.750N-55.00S, 70.00E-164.750W (LSE),  27.00x27.00 (Relocatable)

Horizontal resolution: LAPS and TLAPS: 0.3750

TC_LAPS: 0.750 (LSE) and 0.150 (Relocatable)

Vertical resolution: LAPS, TLAPS: 29 sigma levels (0.9988, 0.9974, 0.9943, 0.9875, 0.9750, 0.9625, 0.9500, 0.9250, 0.9000, 0.8750, 0.8500, 0.8000, 0.7500, 0.7000, 0.6000, 0.5000, 0.4500, 0.4000, 0.3500, 0.3000, 0.2750, 0.2500, 0.2250, 0.2000, 0.1750, 0.1500, 0.1000, 0.0700, 0.0500)

TC_LAPS: 19 sigma levels (0.9910, 0.9750, 0.9500, 0.9000, 0.8500, 0.8000, 0.7500, 0.7000, 0.6000, 0.5000, 0.4000, 0.3500, 0.3000, 0.2500, 0.2000, 0.1500, 0.1000, 0.0700, 0.0500)

Initialization: LAPS and MESO_LAPS: Digital filtering technique.

TLAPS and TC_LAPS: diabatic dynamical nudging scheme incorporating                        GMS IR imagery.

(For Tropical Cyclones: Synthetic vortex specification.)

7.3.2  Model:

Basic equations: Grid primitive equations.

Independent variables: x,y,z,t

Dependent variables: P*,T,q,u,v.

Numerical technique:

horizontal: Finite difference.

vertical: Finite difference.

time: Semi-implicit.

Integration domain (in horizontal and vertical):

LAPS: 17.1250N-65.00S, 65.00E-184.6250E, surface to 50 hPa (approx.)

TLAPS: 44.250N-45.00S, 70.00E-188.250E, surface to 50 hPa (approx.)

MESO_LAPS:

Australian: 4.8750S-55.00S, 95.00E-169.8750E, surface to 50 hPa (approx.)

Sydney: 30.050S-38.000S, 147.000E-154.950E, surface to 50 hPa (approx.)

Melbourne: 34.050S-41.000S, 141.000E-150.450E, surface to 50 hPa (approx.)

TC_LAPS:

LSE: 56.750N-55.00S, 70.00E-164.750W, surface to 50 hPa (approx.)

Relocatable: 27.00x27.00 , surface to 50 hPa (approx.).

Horizontal and vertical resolution, time step:

LAPS: 0.3750  , 29 sigma levels, 40 sec

TLAPS: 0.3750  , 29 sigma levels, 40 sec

MESO_LAPS:

Australian: 0.1250, 29 sigma levels, 10 sec

Sydney: 0.050, 29 sigma levels, 5 sec

Melbourne: 0.050, 29 sigma levels, 5 sec

TC_LAPS:

LSE:  0.750 , 19 sigma levels, 40 sec

Relocatable: 0.150 , 19 sigma levels, 15 sec.

Orography, gravity wave drag: Included.

Horizontal diffusion: Included.

Vertical diffusion: Included.

Planetary boundary layer: Included.

Treatment of sea surface, earth surface and soil: Included.

Soil moisture analysis: Included in LAPS, TLAPS, TC_LAPS and MESO_LAPS.

Radiation: Diurnal cycle, diagnostic clouds, interactive optical properties.

Convection (deep and shallow): Included.

Atmospheric moisture: Included.

Boundaries:  LAPS, TLAPS and TC_LAPS (LSE): Lateral boundaries from GASP.

MESO_LAPS (3 domains): Lateral boundaries from LAPS.

TC_LAPS (Relocatable): Lateral boundaries from LSE TC_LAPS.

Albedo: Climatology.

SST Analysis: Weekly (10x10) - in LAPS, MESO_LAPS (Australian), TLAPS and TC_LAPS.

Daily (0.250x0.250) - in MESO_LAPS (Melbourne and Sydney).

7.3.3  Numerical Weather Prediction Products:

The following post-processed fields are available from the Limited Area Prediction Systems:

| Mean sea level pressure | Dew point depression | V-component of wind |
| --- | --- | --- |
| Surface temperature | Equivalent potential temperature | Potential temperature |
| Convective precipitation | Ucomponent ageostrophic wind | Divergence |
| Thickness (1000-500 hPa) | Shearing deformation | Relative humidity |
| Temperature gradient at 950 hPa | Ucomponent of deformation | Temperature advection |
| Lifting condensation level | Q vector in x-direction | Stretching deformation |
| Grassland fire danger index | U-component stream function | Pressure of cloud top |
| Surface mixing ratio | Moisture advection | Vertical velocity |
| Boundary layer convective energy flux | Surface pressure | Wet bulb potential temperature |
| Sensible heat | Non-convective precipitation | Frontogenesis function |
| U-component of wind | Total precipitation | Vcomponent ageostrophic wind |
| Temperature | Total totals index | 1000-500 hPa shear |
| Geopotential height | Topography | Vcomponent of deformation |
| Dew point temperature | Lifting index | Q vector in y-direction |
| Wind speed | Forest fire danger index | V-component stream function |
| Vorticity | Mixing ratio | Moisture convergence |
| Cloud cover | Stream function |  |
| Vorticity advection | Latent heat |  |

7.3.4  Operational Techniques for Applications of NWP Products:

The 10 m wind field from LAPS and MESO_LAPS are used to drive sea-state models for the Australian region and smaller domains. The Model Output Forecast (MOF) system, which is driven by LAPS and GASP, is used to produce numerous weather elements including temperatures (minimum, maximum, dry bulb, dew point, wet bulb and ground minimum), wind (speed and direction), precipitation, cloud amount, evaporation, sunshine and visibility. Meteograms, giving time series of meteorological variables, are also available. In addition, there is available thunderstorm, based on a decision tree approach, and cold-season tornado (“COLDIES”) guidance, with input from (the Australian domain) MESO_LAPS.

7.4    Specialized Forecasts:

An analogue/regression tropical cyclone model ("TOPEND") is also available for providing guidance to the Australian Tropical Cyclone Warning Centres, but is rarely used. Specialized sea-state forecasts are provided for the North West Cape and Bass Strait gas and oil fields.

7.4.1  Sea Wave Models:

The following table summarises the characteristics of the seastate system in the NMOC:

| Domain | Global | Australian Region | South East Australian |
| --- | --- | --- | --- |
| Numerical Scheme | Deep water 3rd generation (WAM) | Deep water 3rd generation (WAM) | Shallow water 3rd generation (WAM) |
| Wind data source | GASP (10m) | LAPS_PT375 (10m) | MESO_LAPS_PT125 (10m) |
| Grid | Latitude/ longitude | Latitude/ longitude | Latitude/ longitude |
| Resolution | 10 | 10 | 0.250 |
| Nesting | Stand alone | Within Global | Within Regional |
| Start time of forecast | 00,12 UTC | 00, 12 UTC | 00, 12 UTC |
| Forecast Period | +96 hrs | +36 hrs | +36 hrs |
| Initial state | 12 hr hindcasting and assimilation of satellite (ERS) altimeter data | No assimilation |
| Model output | Wind and swell significant wave height, period and direction. Significant wave spectra and probabilities. |
| Verification | With respect to rigs, buoys and satellite (ERS) altimeter data |

7.4.2  Storm Surge System:

A system capable of forecasting storm surges caused by tropical cyclones is currently driven by wind and pressure field distributions defined according to the central pressure and maximum wind radius bogussed for tropical cyclones by Darwin RFC.

7.4.3  Air Dispersion Model:

An air dispersion, or transport, system is available for running on demand and can produce forecast trajectories, concentrations (or exposures) and depositions for nuclear accident, volcanic ash, smoke and other episodes. Currently, the operational Environmental Emergency Response system consists of the Hybrid Single_Particle Lagrangian Integrated Trajectories (HY-SPLIT Version 4.0) system, developed at the NOAA Air Resources Laboratory, with meteorological input from the operational NWP systems in NMOC (viz., GASP, LAPS, TLAPS, and MESO_LAPS). Analysed backward trajectories are also available from GASP, LAPS and TLAPS in operations.

7.4.4  Solar Ultraviolet (UV) Radiation Forecast System:

Forecasts out to 36 hour forecasts of a UV index (defined as the product of the UV irradiance and a human skin response function) are produced operationally. The system analyses ozone concentrations, available from the global 120 km GTS TOVS data, using 2-dimensional univariate statistical interpolation. Forecasts of the ozone distribution are then computed using isentropic fields derived from GASP output. From  vertical profiles of temperature and ozone, the UV index is calculated. Currently, forecasts of the UV index are produced, once per day, after completion of the 1200 UTC run of GASP.

7.5 Extended-range Forecasts (10 - 30 DAYS): Not applicable yet.

7.6 Long-range Forecasts (30 DAYS - 2 YEARS):

A three-month rainfall seasonal climate outlook is prepared. Each month, a risk-assessment for three-month total rainfall across Australia is issued mid-month for the three-month period starting the following month. Probabilities are calculated for the three-month total rainfall being in the lowest one-third of historical falls (tercile 1), the middle one-third (tercile 2), and the upper one-third (tercile 3). The technique used is discriminant analysis, with the inputs being derived from recent Sea Surface Temperature (SST) patterns. Subsidiary techniques involved in the forecast model include principal component analysis of SSTs for the Pacific Ocean, Indian Ocean and Southern Ocean, and principal component analysis of rainfall patterns across Australia. SST EOF (Empirical Orthogonal Function) loadings, at one and three months lag, for the Pacific Ocean ENSO pattern and the Indian Ocean pattern are the current predictor inputs. The tercile probabilities, computed across Australia on a 10x10 grid are published in the form of contoured maps, tabulated averages for the 107 Australian rainfall districts, and tabulated interpolations for cities and towns around Australia. Similar outlooks are now provided for above/below median and for both maximum and minimum temperatures.

Additional guidance at the rainfall district level is presented in the form of stratified rainfall climatologies based on recent values of the SOI (Southern Oscillation Index). Rainfall outcomes for eastern Australia, obtained from SOI analogues, are also described.

Additional forecasts for NINO3 are provided based on an intermediate coupled atmosphere-ocean with sub-surface ocean temperature assimilation. A coupled atmosphere-ocean GCM (General Circulation Model) combined with a sub-surface ocean temperature data assimilation system has been developed and is currently being used to routinely provide forecasts which are currently being assessed.

8.     VERIFICATIONS OF PROGNOSTIC PRODUCTS:

An annual summary of verification statistics for 2001, for the Australian regional and global schemes, is given in the following tables.

The following abbreviations have been used in the tables:

S1         - 30 day mean Teweles skill score over Australian verification area

r           - anomaly correlation coefficient between forecast heights and climatology over                   Australian verification area

PERSIS  - 24, 36 or 48 hour persistence prediction

REGN    - Australian Regional LAPS (Limited Area Prediction System)

GASP     - Global Assimilation and Prognosis model

RMSE    - Root Mean Square Error

Note:

The LAPS and GASP results are with respect to their own analyses.

8.1   Skill Scores and Anomaly Correlation Coefficients:

24 HR VERIFICATION STATISTICS - AUSTRALIAN REGION 2001

BASE TIME: 0000UTC - VALID TIME: 0000UTC

|  |  |  | JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M S L P | S1 S1 r | PERSIS REGN REGN | 57 24 .95 | 53 23 .93 | 54 22 .97 | 50 21 .96 | 57 23 .97 | 52 21 .97 | 54 21 .97 | 59 21 .97 | 59 21 .97 | 63 23 .97 | 58 21 .98 | 54 23 .97 |
| 5 h 0 e 0 i h g p h a t | S1 S1 r | PERSIS REGN REGN | 44 14 .98 | 47 16 .96 | 51 17 .97 | 47 17 .97 | 46 16 .97 | 44 15 .97 | 47 16 .98 | 43 13 .97 | 49 14 .98 | 48 15 .98 | 47 15 .98 | 40 13 .97 |
| 2 h 5 e 0 i h g p h a t | S1 S1 r | PERSIS REGN REGN | 41 13 .98 | 42 14 .97 | 43 14 .97 | 41 14 .97 | 39 14 .97 | 36 13 .97 | 39 13 .97 | 34 10 .97 | 43 12 .98 | 40 12 .98 | 40 12 .98 | 36 12 .97 |

36 HR VERIFICATION STATISTICS - AUSTRALIAN REGION 2001

BASE TIME: 1200UTC - VALID TIME: 0000UTC

|  |  |  | JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M S L P | S1 S1 r | PERSIS GASP GASP | 67 27 .94 | 62 24 .93 | 65 25 .96 | 62 23 .95 | 72 27 .95 | 62 23 .96 | 67 25 .96 | 69 26 .95 | 70 24 .96 | 73 27 .96 | 71 27 .96 | 63 29 .95 |
| 5 h 0 e 0 i h g p h a t | S1 S1 r | PERSIS GASP GASP | 52 17 .97 | 56 18 .96 | 63 21 .96 | 58 19 .96 | 57 19 .96 | 52 18 .96 | 57 20 .97 | 52 17 .95 | 59 18 .96 | 59 18 .97 | 59 19 .96 | 49 17 .96 |
| 2 h 5 e 0 i h g p h a t | S1 S1 r | PERSIS GASP GASP | 49 16 .97 | 52 15 .97 | 53 16 .96 | 51 16 .96 | 48 15 .96 | 43 14 .97 | 46 14 .97 | 41 12 .96 | 53 14 .97 | 49 14 .97 | 50 15 .96 | 44 15 .95 |

48 HR VERIFICATION STATISTICS - AUSTRALIAN REGION 2001

BASE TIME: 0000UTC - VALID TIME: 0000UTC

|  |  |  | JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| M S L P | S1 S1 r | PERSIS GASP GASP | 71 32 .92 | 66 27 .91 | 71 29 .94 | 66 27 .93 | 76 33 .92 | 67 28 .94 | 72 29 .95 | 73 31 .92 | 76 29 .94 | 79 32 .93 | 79 32 .93 | 70 34 .92 |
| 5 h 0 e 0 i h g p h a t | S1 S1 r | PERSIS GASP GASP | 54 20 .94 | 61 21 .94 | 68 24 .95 | 62 23 .95 | 62 24 .93 | 58 22 .93 | 61 23 .95 | 55 21 .93 | 62 22 .94 | 62 22 .95 | 65 24 .93 | 53 21 .93 |
| 2 h 5 e 0 i h g p h a t | S1 S1 r | PERSIS GASP GASP | 51 18 .95 | 56 18 .95 | 57 19 .94 | 55 19 .94 | 52 19 .94 | 47 17 .95 | 48 17 .95 | 43 14 .94 | 54 18 .95 | 51 17 .95 | 56 19 .93 | 47 18 .92 |

8.2  Root Mean Square Errors (Annual 2001):

(a) Verification against analyses:

| AREA | FIELD | RMSE or RMSVE UNIT | +24HR | +72HR | +120HR |
| --- | --- | --- | --- | --- | --- |
|  |  |  | 00UTC | 12UTC | 00UTC | 12UTC | 00UTC | 12UTC |
| Northern Hemisphere | 500 hPa Height | m | 15.4 | 15.3 | 41.2 | 41.5 | 68.7 | 69.0 |
|  | 250 hPa Wind | m/s | 5.5 | 5.5 | 11.4 | 11.4 | 16.5 | 16.6 |
| Southern Hemisphere | 500 hPa Height | m | 18.5 | 18.5 | 47.8 | 47.4 | 75.3 | 74.9 |
|  | 250 hPa Wind | m/s | 5.9 | 5.9 | 12.4 | 12.4 | 17.6 | 17.6 |
| Tropics | 850 hPa Wind | m/s | 2.8 | 2.9 | 4.2 | 4.3 | 4.8 | 4.9 |
|  | 250 hPa Wind | m/s | 5.4 | 5.4 | 8.4 | 8.5 | 10.1 | 10.1 |

(b) Verification against radiosondes:

| AREA | FIELD | RMSE or RMSVE UNIT | +24HR | +72HR | +120HR |
| --- | --- | --- | --- | --- | --- |
|  |  |  | 00UTC | 12UTC | 00UTC | 12UTC | 00UTC | 12UTC |
| North America | 500 hPa Height | m | 17.7 | 17.6 | 44.0 | 45.0 | 73.4 | 73.6 |
|  | 250 hPa Wind | m/s | 8.3 | 8.1 | 14.6 | 14.5 | 20.2 | 19.9 |
| Europe | 500 hPa Height | m | 19.9 | 19.5 | 46.8 | 46.9 | 79.3 | 77.8 |
|  | 250 hPa Wind | m/s | 7.3 | 7.1 | 12.8 | 12.8 | 19.4 | 19.1 |
| Asia | 500 hPa Height | m | 20.2 | 20.2 | 40.1 | 41.0 | 58.7 | 60.4 |
|  | 250 hPa Wind | m/s | 8.1 | 8.4 | 13.0 | 13.5 | 16.4 | 16.9 |
| Australia/NZ | 500 hPa Height | m | 16.1 | 17.0 | 30.2 | 32.7 | 46.5 | 50.0 |
|  | 250 hPa Wind | m/s | 7.9 | 7.8 | 12.4 | 12.6 | 16.7 | 16.9 |
| Tropics | 850 hPa Wind | m/s | 4.5 | 4.6 | 5.3 | 5.5 | 5.9 | 6.0 |
|  | 250 hPa Wind | m/s | 6.8 | 6.9 | 8.6 | 8.9 | 10.1 | 10.4 |
| Northern Hemisphere | 500 hPa Height | m | 20.2 | 20.0 | 46.1 | 46.9 | 75.6 | 75.9 |
|  | 250 hPa Wind | m/s | 7.8 | 7.8 | 13.3 | 13.4 | 18.7 | 18.6 |
| Southern Hemisphere | 500 hPa Height | m | 20.4 | 21.7 | 39.6 | 42.0 | 59.6 | 63.2 |
|  | 250 hPa Wind | m/s | 8.4 | 8.9 | 13.5 | 13.9 | 18.0 | 18.6 |

9.  PLANS FOR THE FUTURE:

Plans for future operational systems in the NMOC Melbourne include:

. an ongoing improvement and generalization of data processing and graphical display                     (including the introduction of MARS, METVIEW and a GIS);

. improvement in data monitoring systems;

. the introduction of a number of changes into LAPS including: 1DVAR, full warm running,          soil moisture nudging, improvements to cloud and radiation parameterisations, a semi-                 implicit semi-Lagrangian formulation, more vertical levels, forecasts extended to 60 hours          (and 48 hours for MESO_LAPS), non-hydrostatic formulation;

. the introduction of a LAPS ensemble prediction system;

. the introduction of a mesoscale assimilation system;

. enhancements to GASP incorporating: locally derived cloud drift winds and                                   scatterometer winds, increased vertical resolution (50 levels up to 0.1 hPa), 3DVAR;

. the introduction of a rainfall verification scheme;

. a move to drive the storm surge model using meteorological input from TC_LAPS;

. an ongoing improvement to the operational Environmental Emergency Response System               including the use of a unified wind input system and an extension to include a number of              chemical transformations;

. the implementation of an urban air quality forecasting system;

. the introduction of a forecast air-borne virus facility within the air quality and EER systems;

. the introduction of a fully coupled ocean-atmospheric model for seasonal analysis and                   prediction.

10.    REFERENCES:

Bourke W., Hart T., Steinle P., Seaman R., Embery G., Naughton M. and Rikus L. : "Evolution of the Bureau of Meteorology's Global Data Assimilation and Prediction System. Part 2: Resolution Enhancements and Case Studies." Australian Meteorological Magazine, 44, 19-40, 1995.

Davidson N.E. and Puri K. : "Tropical prediction using dynamical nudging, satellite defined convective heat source and a cyclone bogus." Monthly Weather Review, 120, 2501-2522, 1992.

Davidson N.E. and Weber H.C.: "The BMRC high resolution tropical cyclone prediction system TC-LAPS.”  Monthly Weather Review, 128, 1245-1265, 2000.

Draxler R.R. and Hess G.D. : "An overview of the HYSPLIT_4 modelling system for trajectories, dispersion and deposition." Australian Meteorological Magazine, 47, 295-308,  1998.

Greenslade D.J.M.: “The BMRC ocean thermal analysis system.” Journal of Marine Systems, 28, 141-160, 2001.

Harris B.A. and Kelly G.: “A satellite radiance bias correction scheme for data assimilation.” Quarterly Journal of the Royal Meteorological Society, 127, 1453-1468, 2001.

Le Marshall J., Pescod N., Seaman R., Mills G. and Stewart P. : "An Operational System for Generating Cloud Drift Winds in the Australian Region and Their Imapct on Numerical Weather Prediction."  Weather and Forecasting, 9, 361-370, 1994.

Le Marshall J.F., Riley P.A., Rouse B.J., Mills G.A., Wu Z.-J., Stewart P.K. and Smith W.L.: "Real-time assimilation and synoptic application of local TOVS raw radiance observations." Australian Meteorological Magazine, 43, 153-166, 1994.

Mills G.A. and Colquhoun J.R.:” Objective Prediction of Severe Thunderstorm Environments: Preliminary Results Linking a Decision Tree with an Operational Regional NWP Model.” Weather and Forecasting, 13, 1078-1092 1998.

Puri K., Dietachmayer G.S., Mills G.A., Davidson N.E., Bowen R.A. and Logan L.W. : "The new BMRC Limited Area Prediction System, LAPS." Australian Meteorological Magazine, 47, 203-223, 1998.

Seaman R., Bourke W., Steinle P., Hart T., Embery G., Naughton M. and Rikus L. : "Evolution of the Bureau of Meteorology's Global Data Assimilation and Prediction System. Part 1: Analysis and Initialisation." Australian Meteorological Magazine, 44, 1-18, 1995.

Stewart P.K. : "RSMC Melbourne - Procedures, Standards, Results of Exercices and Ongoing Products." WMO Expert Team on Environmental Emergency Response. Beijing, China, 20-24 September 1999.