Progress Report on the Global Data Processing System in  2001

# Korean Meteorological Administration

# Republic of Korea

1. Summary of Highlights

The main changes to the global and regional versions of the numerical prediction suites ware the followings:

1 Mar.	Operation of high-resolution Global Data Analysis and Prediction System (GDAPS, T213/L30)

Implementation of 3 dimensional optimal interpolation scheme in GDAPS.

Change of the analysis field from p-level to model sigma level in Regional Data Analysis and Prediction System (RDAPS).

Operation of high- resolution global wave model.

1 Apr.	Operation of new Ensemble Prediction System (EPS, T106/L21) incorporating 16 breeding ensemble members.

15 Jun. 	Extension of Typhoon forecast time up to 72 hours

25 Aug.	Implementation of real-time verification of Typhoon forecast

30 Aug. 	Semi operation of the regional 3DVAR system for using AWS(Automatic Weather Station) data in RDAPS

1 Nov.: 	Improvement of satellite data assimilation using 1DVAR

Increasing the resolution of land-use data for the RDAPS

2. Equipment in Use at the KMA

The supercomputer SX-5/28M is partly dedicated for the operation of the short, medium and long-range numerical weather prediction including climate simulation.

### ( Main computer: SX-5/28M2

- Peak Performance：224 GFlops with 28 processors

- Memory        ：224 Gbytes

- Single CPU performance: 8 Gflops

- Mass storage system ：3.0T bytes

### ( Other facilities: SX-4/2A

-Peak Performance：4 GFlops

-Mass storage system ：1.4Tbytes

3. Data and Products in Use

More than 5,000 synoptic observations, and various asynoptic observations including satellite retrieval data and AWS data etc., are used daily in the GDAPS. The pre-processing procedures such as data acquisition, quality control and decoding, are fully automated. Various real-time quality control checks are performed for each observation received from GTS.  In particular :

(  Vertical consistency checks are performed for TEMP and PILOT data

( Gross error and spatial consistency are checked for removing or correcting  erroneous observations.

Table 1.  The types and numbers of observations received through GTS, and

the percentage of data used in global data assimilation for 24 hours.

|  | Data type | Number of data/day | % used in assimilation |
| --- | --- | --- | --- |
| 1 | SYNOP/ SHIP | 32,000 | 53 |
| 2 | BUOY | 2,500 | 21 |
| 3 | TEMP/ PILOT | 1,600 | 36 |
| 4 | AIREP/ AMDAR | 120,000 | 13 |
| 5 | SATEM | 6,800 | 35 |
| 6 | SATOB | 30,000 | 78 |
| 7 | ATOVS | 30,000 | 15 |
| 8 | ACARS | 100,000 | 4.5 |
| 9 | AWS | 11,000 | - |
| 10 | PAOB | 400 | 100 |

4. Data Input System

Fully automated system

5. Quality Control System

Various real-time quality control checks are performed for each observation from GTS.

In particular:

(  The vertical consistency checks are performed for TEMP and PILOT data using all parts of reports.

(  Gross error and spatial consistency are checked in order to remove or correct erroneous observations.

6. Monitoring of Observing System

Surface observations are monitored on the national level.

7. Forecasting System

Along with data assimilation system having 6-hour updating cycle, the GDAPS produces 240-hour prognosis for the large-scale atmospheric variables. It provides time-dependent lateral boundary conditions for the regional models and steering flow for typhoon model.

The RDAPS runs twice a day for 48-hour forecasts, with 12-hour pre-assimilation with dynamic nudging, FDDA. Five typhoon track forecasts are obtained from BATS, RDAPS, two GDAPS(T106/L21 and T213/L30), and EPS when typhoon appears in Western Pacific. In addition, there are two types of applied models; Wave models for  wave height and direction on both global and regional domain, and two statistical models of Perfect Prog Method and Kalman filter method for max/min temperature and probability of precipitation.

7.1 System Run Schedule

Two types of global forecasts are produced at KMA. The GDAPS for 84-hour projection runs at 00 UTC and 12 UTC with 2.5-hour data cutoff. The 84-hour projection is used for short-range weather forecasts and for the provision of lateral boundary condition for the two high-resolution(10km and 5km with 33 layers) regional models. The GDAPS for 10-day projection runs at 12 UTC with 10-hour data cutoff, in order to utilize as much observation as available. The 10-day projection used for weekly forecast. The RDAPS runs twice a day (00 and 12 UTC) for 48-hour forecasts.

7.2 Medium-range Forecasting System

7.2.1 Data assimilation, Objective Analysis and Initialization

The global analyses are prepared with the 6-hour interval cycling.  A 6-hour forecast from the previous run provides a first guess for the next analysis. If a typhoon exists in the Western Pacific, a typhoon bogus profile is calculated and embedded in the first guess field. The best fits of analysis are made with the 3-dimension multivariate optimal interpolation scheme for height and wind, and with the univariate scheme for relative humidity and surface pressure. The increments from the first guess are estimated at observation points, and interpolated back to grid points. The analysis is performed on the sigma levels in global model.

The moisture analysis is corrected with the cloud information at different vertical layers, including cloud top temperature derived from GMS-5 images. Both moisture and thickness fields are further refined by the 1-dimension variational data assimilation (1DVAR) of ATOVS radiance. The 1DVAR retrieves thickness and precipitable water on the layers of the SATEM data.

A Non-linear Normal Mode Initialization(NNMI) with full physics is performed in order to suppress the amplitude of high-frequency gravity waves. The high frequency component is filtered out for each spherical harmonic component in the five greatest vertical modes which exceed the critical frequency. Machenhauer's iterative scheme is used for determining the non-linear balanced solution.

7.2.2 Model Configuration

| Dynamics |  |
| --- | --- |
| Basic equation | Primitive equations in sigma- pressure hybrid vertical coordinate |
| Numerics | Spectral representation of horizontal variables with triangular truncation of T213, corresponding to a Gaussian grid size of 0.56 degrees or 55km |
| Domain | Global |
| Levels | 30 vertical levels ranging from surface to 10 hPa |
| Time integration | Eulerian semi-implicit scheme |
| Physics |  |
| Horizontal diffusion | Second order Laplacian, and Rayleigh friction |
| Moist processes | Kuo scheme, large-scale condensation, and shallow convection scheme |
| Radiation | Long wave radiation calculated every three hours Short wave radiation calculated every hour |
| Gravity wave drag | Long waves (wavelength>100km) Short waves (wavelength 10km) |
| PBL processes | Mellor-Yamada level-2 closure scheme and similarity theory for surface layer. Non-local diffusion |
| Land surface | Simple biosphere model |
| Surface state | NOAA’s weekly mean anomaly added to monthly changing climatological SST Climatological values are used for the soil moisture, snow depth, roughness length and albedo |

The original T106 version of global model is based on the JMA's global spectral model. The T213 version, which is operational since Mar. 2001, has similar dynamical framework as T106, but with new physics such as non-local boundary diffusion.

The 1DVAR for ATOVS radiance has been operational for the global analysis system since 1 Nov. 2001.

7.2.3 Operational Techniques for Application of NWP Products

The 6-hour forecast of GDAPS is used for the first guess in the analyses of regional model and  the steering flow of typhoon model. The surface winds predicted by GDAPS and RDAPS are used as an input for the global and regional wave model. The wind field predicted by GDAPS is used as an input for the trajectory model for the yellow sand.

7.2.4 Ensemble Prediction System

An ensemble prediction system (EPS), based on breeding method with global model(T106/L21), has been operational since Mar. 2001. An ensemble of 16 members is obtained from the sequence of 6-hour breeding cycle. The EPS runs for 10-day projection once a day at 12 UTC for supporting weekly forecast.

7.3 Short-range Forecasting System

RDAPS was improved considerably in decrease of cold biases and forecast error, in terms of pre-process modifications: surface pressure calculation by the global model’s surface pressure and the topography differences between the global and regional model, and the direct use of the global model outputs of hybrid sigma coordinate instead that of pressure coordinate. More importantly 3DOI was installed in regional modeling system that intends 6-hour cycling data assimilation and to use more observations. Land use categories are improved from 13 to 23 types, which result to decrease of RMSE and bias in temperature below 850hPa. Nested 10km and 5km RDAPS have 24 hours forecast time. Both 30km and 10km RDAPS use mixed phase microphysical process (MP) and Kain-Fritsch convection scheme in the precipitation forecasts, however 5km RDAPS use MP only.

| Assimilation | Four-dimensional Data Assimilation with nudging |
| --- | --- |
| First guess | GDAPS previous 6-hour prognosis |
| Observations | Upper-air sounding (TEMP A, B, C, D) with 12 hour interval |
| Method | 3 Dimensional Optimal Interpolation |
| Variables | Wind, geopotential height, and relative Humidity |
| Vertical levels | 33 model sigma levels |
| Dynamics |  |
| Grids | Triply nested domain (30km for 171 x 191, 10km for 160 x 178 and 5km for 141 x 141 gird points |
| Numerics | Primitive equations based on the non- hydrostatic frame |
| Vertical resolution | 33 layers with model top of 50 hPa |
| Boundary condition | Time and inflow/ outflow dependent relaxation |
| Boundary update Frequency | 30km : 12-hour interval by GDAPS forecasts 10km : 3- hour interval by 30km forecasts 5km : 1- hour interval by 10km forecasts |
| Time integration | 72 hours for 30km mesh, and 24 hours for both 10km and 5km meshes |
| Physics |  |
| Horizontal Diffusion | Fourth order diffusion |
| Precipitation physics | Explicit moisture scheme |
| Deep convection | Kain-Fritch only for 30 km and 10km mesh |
| Planetary layer | Non-local Boundary layer |
| Surface physics | 5-layer soil model for ground temperature |
| Radiation | To be implemented |

7.4 Application for NWP products

Direct model outputs, including the potential vorticity at isentropic surface, are available in both graphic and imagery form. Those products are also disseminated to the end users through intranet or internet. A statistical model with Kalman filter (KF) produces 3-hourly temperature forecasts including the maximum and minimum temperature for 61 domestic stations up to 48 ~ 84 hours  in advance. Also, 10 day maximum and minimum temperatures are provided by the Dynamic Linear Model, which was modified the KF method.

7.5 Ocean Wave Prediction System

Two numerical wave models are currently on operation: Global WAve Model (GoWAM) and Regional WAve Model (ReWAM). Both models are adopted from the 3rd generation WAM model cycle 4 (developed by WAMDI group). The performance of GoWAM is improved by using the surface wind from the global model (T213/L30).

#### Specification of ocean wave prediction models

|  | GoWAM | ReWAM |
| --- | --- | --- |
| Model Type | 3rd generation spectral model |
| Spectral component | 25 frequencies and 12 direction |
| Grid form | Latitude-longitude grid on spherical coordinate |
| Grid size | 1.25deg×1.25deg(288×113) | 0.25deg×0.25deg (141×121) |
| Domain | 70°S ~ 70°N | 20°N ~ 50°N, 115°E ~ 50°E |
| Time step | 720 seconds | 360 seconds |
| Forecast time | 240 hours from 12UTC | 48 hours from 00, 12UTC |
| Initial condition | 24(12) hours forecast (spectral) from previous run |
| Wind fields | from GDAPS | from RDAPS |

7.6 Typhoon Track Prediction System

Typhoon track forecasts are provided from five different models, BATS, two GDAPS(T106/L20 and T213/L30), RDAPS, and EPS. The Barotropic Adaptive grid Typhoon System (BATS) is based on the continuous dynamic grid adaptation technique with the innermost grid spacing of 0.3 degrees. This model is specially designed to run with high resolution grids within little computational load. It runs four times a day by 6-hour interval.

Barotropic Adaptive-grid Typhoon System(BATS)

| Input Data | GDAPS analysis and prognosis |
| --- | --- |
| Vortex Bogusing And Initialization | Specified vortex generated by empirical formulas Global objective analysis field with the symmetric typhoon vortex |
| Dynamics |  |
| Basic equation | Shallow water equations on the latitude-longitude coordinate |
| Horizontal representation | Grid distance of 0.6°with the innermost grid distance of 0.3°on the continuous dynamic grid adaptation |
| Domain | 101 grid points both in zonal and meridional directions over the domain of 60°×60° |
| Products | Central position (lat./lon.) every 6 hours up to 60 hours in advance. |

8. Verification

Annual verification statistics are calculated by comparing the model forecast to the analysis and radiosonde observation (see Table 3 and 4).

Table 3. RMSE verification of KMA’s global model (GDAPS) against the analysis for 2001

| Statistic | Area. | T+24 hr | T+72 hr | T+120 hr |
| --- | --- | --- | --- | --- |
| Z500 | Northern Hemisphere | 16.8 | 42.5 | 69.9 |
| of Z500 | Southern Hemisphere | 25.7 | 64.5 | 94.1 |
| V250 | Northern Hemisphere | 6.7 | 12.9 | 18.2 |
| V250 | Southern Hemisphere | 7.5 | 15.7 | 21.1 |
| V250 | Tropics | 5.4 | 9.2 | 11.3 |
| V850 | Tropics | 2.8 | 4.3 | 5.1 |

Table 4. RMSE verification of KMA’s global model (GDAPS) against observation in 2001.

| Statistic | Area. | T+24 hr | T+72 hr | T+120 hr |
| --- | --- | --- | --- | --- |
| Z500(geopotential height) | North America | 21.0 | 46.7 | 70.6 |
| Z500 | Europe | 18.3 | 41.1 | 69.9 |
| Z500 | Asia | 18.7 | 35.9 | 53.4 |
| Z500 | Australia/ New Zealand | 21.6 | 41.0 | 60.3 |
| V250(wind) | North America | 9.0 | 15.5 | 20.3 |
| V250 | Europe | 7.6 | 13.2 | 19.7 |
| V250 | Asia | 8.5 | 12.9 | 16.6 |
| V250 | Australia/ New Zealand | 9.3 | 14.4 | 19.3 |
| V250 | Tropics | 8.1 | 9.9 | 11.4 |
| V850 | Tropics | 4.9 | 5.6 | 6.3 |

9. Future Plan

The data assimilation of the asynoptic observations, such as radar velocity and reflectivity observations, AWS (Automatic Weather Station) observations, satellite radiances, continuously will be assimilated for the improvement of KMA NWP models in next few years.

New assimilation system called 3DVAR is developing for the global and regional model  (horizontal resolution 30km and 10km). KMA will be implemented 3DVAR in both global and regional analysis system by 2004. Especially AWS and radar data will be applied to make the good regional analysis field of 10km RDAPS for the improvement of local heavy rainfall prediction.

Incremental Analysis Update (IAU) technique for better initialization and 6-hour cycling data assimilation system by use of 3DOI will be implemented in RDAPS. Successive correction method for radar data (radial velocity and reflectivity) assimilation will be tested in 10km RDAPS for better precipitation forecasts in 2002.