# Annual WWW Technical Progress Report on the GDPS

# 2002

Country:  Germany                                                                                              Centre: NMC Offenbach

- Summary of highlights

The modelling suite at DWD consists of the global icosahedral-hexagonal gridpoint model GME (average mesh size ~ 60 km, i.e. 163842 gridpoints/layer, 31 layers) and the nonhydrostatic limited-area “Lokal-Modell” LM (mesh size ~ 7 km, 325 x 325 gridpoints/layer, 35 layers). LM is used operationally at the national meteorological services of Greece, Poland and Switzerland and at the regional meteorological service in Bologna (Italy), too.

The hydrostatic high-resolution regional model HRM of the DWD is being used as operational model at ten national/regional meteorological services, namely Brazil-INMET, Brazil-Navy, Bulgaria, China, Israel, Italy, Oman, Romania, Spain and Vietnam. For lateral boundary conditions, GME data are sent via the Internet to the HRM and LM users.

During the year 2002 the main improvements of the NWP suite included:

- 09/04/02: Operational usage of the new high performance computer at DWD, an IBM RS/6000 SP with 80 nodes equipped with 16 processors each. At the same time, the intermittent data assimilation cycle of GME has been reduced from 6 to 3 hours with an observation window of +/-1.5 hours. Moreover, ozone is introduced as prognostic variable as the basis of a UV-B forecasting scheme.

- 12/08/02: The SST analysis of NOAA/NCEP at a resolution of 0.5°x0.5° is used as background instead of the coarser resolution one (1°x1°) used previously.

- 12/12/02: The Australian PAOB data are used in the global data assimilation scheme; these data increase the quality of the analysis and forecast of GME considerably.

Currently the IBM RS/6000 SP with a total of 80 nodes is logically split into a 28-node system for operational applications and a 52-node one for research an development. During 2003 the full 80-node system will made be available for operational usage allowing for a significant upgrade of GME and LM in the future.

- Equipment in use

2.1	Main computers

    - IBM RS6000 SP

Operating System AIX 4.3

28 Power3-II Nodes (448 Processors, 375 MHz)

Peak performance 1.5 Gflops per processor

8 or 16 GB Memory per processor

SP Switch 2

0.6 TB disk space

Dedicated for operational forecasts

2.1.2	IBM RS6000 SP

Operating System AIX 4.3

52 Power3-II Nodes (832 CPUs with 375 MHz)

Peak performance 1.5 Gflops per CPU

8 or 16 GB Memory per CPU

SP Switch 2

2.6 TB disk space

Used for research and for operational forecasts (backup)

2.1.3	ORIGIN 2000 (Operating System IRIX)

SGI ORIGIN 2000

Operating System IRIX 6.5

System of 4 O2000 servers

70 processors, 250 MHz

62 GB Memory

Access to StorageTek ACS Silo

The total system consists of servers for code development, pre- and postprocessing, Hierarchical Storage Management and  Oracle databases.

    - Storage Tek Silo (3 components)

Attached are

9840 drives: 16

9940 drives: 10

2.2	Networks

2.2.1	Ethernet

Workstations, X-Terminals and PC's are connected to the main computers via routers to the Ethernet.

2.2.2	HPPI

The IBM and the SGI severs are connected by HIPPI via two HIPPI switches.

2.2.3	ATM

Access from the LAN to the O2000 servers is provided via routers to the ATM-connected sys

2.3	Special systems

2.3.1	Satellite data system

Windows 2000 Server

Used for preparation of satellite pictures (from METEOSAT and NOAA and FENGYUN),

vertcal profiles of temperature and humidity (from NOAA).

2.3.2	Interactive graphical system

A number of SGI work stations and colour plotters are used for presentation of satellite- and radar data as well as model output, surface forecast charts significant weather charts, and other interactive graphics,

The MAP (Meteorological Application and Presentation System) Workstation is used to display and animate all available meteorological data  sources.

2.3.3	Telecommunication system

The Meteorological Telecommunications System Offenbach (MTSO) is realized on a High-Availability-Primecluster with two Primepower 400 (Fujitsu Siemens Computers) running on Sun-Solaris systemsoftware and RMS clustersoftware.

The belonging MSS and AFD Applications are communicating in real time via the GTS (RMDCN and leased lines), national and international PTT networks and the Internet with WMO-Partners and global  customers like EUMETSAT, ECMWF and DFS.

3.	Data and products from GTS in use

At present nearly all observational data from the GTS are used. GRIB data from the France and GRIB data from the UK, the US and the ECMWF are used. In addition most of the OPMET data are used.

Typical figures for 24 hours are:

SYNOP, SHIP	53.000 reports,

TEMP, part A	1.100 reports,

METAR	                           32.000 reports,

PILOT, part A	600 reports,

AIREP, AMDAR	28.000 reports,

SATEM, part A	11.000 reports,

SATOB, section 2	240.000 reports,

SATOB, section 3	6.000 reports,

SATOB, section 4	4.300 reports,

SATOB, section 5	68.000 reports,

SATOB, section 7	20.000 reports,

GRIB       	   7.500 bulletins,

BUFR 	700 bulletins

4.	Data input system

Fully automated system. Incoming reports in character orientied code forms are converted into BUFR before storing them into a data base.

5.	Quality control system

There is no quality control system in use regarding outgoing data to the GTS except for formal structure.

5.1	Quality control of incoming data

The formats of all coded reports are checked and if necessary and possible corrected. Surface and upper air reports are checked for internal consistency before storing them into a data base.

6.	Monitoring of the observing system

Surface observations and upper air observations are monitored quantitatively only on the national level. DWD acts as a lead centre for monitoring the surface observations in Region VI. At present, only the surface pressure observational data are checked.

- Forecasting systems

  - System run schedule and forecast ranges

Preprocessing of GTS-data runs on a quasi-real-time basis about every 6 minutes on the ORIGIN 2000.

Independent 4-dim. data assimilation suites are performed for both models, GME and LM. For GME, analyses are derived for the eight analysis times 00, 03, 06, 09, 12, 15, 18 and 21 UTC based on an intermittent optimum interpolation scheme. For LM, a continuous data assimilation system based on the nudging approach provides analyses at hourly intervals.

Forecast runs of GME and LM with a data cut-off of 2h 14 min after the main synoptic hours 00, 12 and 18 UTC consist of 48-h forecasts for LM and 174-h forecasts (48-h for 18 UTC) of the GME. Additionally, three ocean wave models (3rd generation WAM), the global GSM, Mediterranean MSM and local wave model (North, Baltic and Adriatic Sea areas) LSM provide guidance about wind sea and swell based on 00 and 12 UTC wind forecasts of GME and LM.

  - Medium range forecasting system (4-10 days)

    - Data assimilation, objective analysis and initialization

As far as GME is in use for medium range forecasting, the same procedures are applied as for short range forecasting described in item 7.3.1.

7.2.2	Model

Medium range forecasts at the DWD are mainly based on the ECMWF system (deterministic model and EPS). Additionally, GME (see 7.3) forecasts up to 7 days augment the model guidance available.

7.2.3	Numerical weather prediction products

ECMWF and GME global forecasts are available up to day 7. The ECOMET catalogue of the DWD global model products is given in annex 1.

    - Operational techniques for application of NWP products

A statistical interpretation scheme is applied to ECMWF and GME forecasts to provide medium-range forecasts for some German areas up to day 7. The scheme is based on the PPM philosophy. The interpretation results based on ECMWF and GME forecasts are averaged because verification results show that this average scores significantly better than each single model interpretation. Such a simple averaging proves to be a cost effective approach to reduce both the error and the error variance in medium- range forecasts (simplest ensemble prediction). The forecast parameter derived are:

Daily maximum and minimum temperatures, relative sunshine duration, daily precipitation amount and probability, wind speed and direction, probability of thunderstorm, probability of fog.

A new method to produce medium range forecasts in plain language for the public which had been introduced in 1999 was further developed and adapted to user requirements in 2002.  It allows for a centralized medium-range forecast activity. For this purpose a particular software was developed by DWD, which produces texts automatically from a data base. The data base is derived from the scheme described above. Every day in the beginning of the forecast business the meteorologist examines and –  where necessary – postprocesses the data base and only then the text generator will be started. The automatically produced texts contain all significant weather parameters like cloud cover, precipitation, wind and extreme temperatures. In addition to this the automatic text production is  in use for worldwide forecasts, which are available by dialling a premium rate number on a fax machine, on a telephone answering device or on mobile telephones using short message system (SMS). The latter ones are produced however without forecasters’ intervention.

Progress was made in medium range forecasting concerning the risk assessment of extreme weather for the forecast interval 120 hours down to 36 hours by synoptic interpretation of model results in combination with the evaluation of the EFI- (extreme forecast index) charts, provided by ECMWF.  The Risk-Assessment is made available for the regional offices within DWD but will be tailored to users requirements in near future.

Agrometeorological forecasts cover a wide span of applications aiming at a reduction of the use of insecticides and fungicides or at an optimization of the water supply to plants. NWP results are combined with additional models which calculate the drying of leaves or the temperature and water balance in the ground.

7.3	Short-range forecasting system (0-72 hrs)

Operational short-range forecasting is based on the products available from GME and LM, where LM covers the time period up to 48 h only.

The short-range forecasts for Central Europe up to 48 hours are derived from the limited-area “Lokal-Modell” LM. Fig. 1 shows the model domain of LM and Fig. 2 the model levels. The LM is designed as a flexible tool for forecasts on the meso-ß and on the meso-( scale as well as for various scientific applications down to grid spacings of about 100 m. For operational numerical weather prediction, LM is nested in the GME.

    - Data assimilation, objective analysis and initialization

# Global Model (GME)

- Global analysis of mass,  wind field and humidity

The program for the global analysis of mass and wind field, formerly developed by ECMWF, was ported to MPP systems by DWD with the support of the PALLAS software house.

Analysis method	3-dimensional multivariate optimal interpolation (humidity 2-dimensional).

Direct use of thickness data. Box method.

Analysed variables	(, u, v, Rel. Hum.; Ozone from ECMWF analysis (12 UTC)

Horizontal anal. grid	Icosahedral grid of the GME  ( average mesh size of 60 km )

Vertical resolution	31 hybrid layers (see GME)

Products		a)  On icosahedral-hexagonal grid of the GME

(163842 gridpoints/layer, 31 layers)

Variables: ps, T, u, v, qv, qc, o3

b)  On a regular geographical grid, 480 x 361 points (0.75° x 0.5°)

12 pressure levels 1000, 950, 850, 700, 500, ..., 50 hPa

Variables: pmsl, T, (, u, v, Rel. Hum.

Assimilation scheme	Intermittent data assimilation. Insertion of data every 3 hours.

3-h forecast used as first guess. All observations within a ( 1.5-h window

used as synoptic.

Cut-off time 2 h 14 min.

Initialization		Incremental digital filtering initialization (Lynch, 1997) consisting of

a 3-h adiabatic backward run and a 3-h diabatic forward run centered

at the initial time. The filtering is performed in vertical mode space; only the external mode plus the first nine internal ones are filtered.

- Global analysis of surface parameters

Analysis method	Correction method

Analysed variables	Sea surface temperature (SST) and snow cover

Horizontal anal. grid	On icosahedral-hexagonal grid of the GME (average mesh size of 60 km)

Data used		SST:  		Synop-Ship, NCEP-SST analysis as background,

NCEP-data of ice border.

Snow cover: 	Snow depth, present and past weather, precipitation amount,

temperature analysis. History taken into account.

NCEP-data of ice border.

Local Model (LM)

- Limited-area analysis of atmospheric fields

The data assimilation system for the LM is based on the observation nudging technique (Schraff, 1997). The variables nudged are the horizontal wind, temperature, and humidity at all model layers, and pressure at the lowest model level. The lateral spreading of the observational information is horizontal, or optionally along model layers or isentropic surfaces. At present, the scheme uses only conventional data of type TEMP, PILOT, SYNOP, BUOY, AIRCRAFT and AMDAR.

Analysis method	Observation nudging technique

Analysed variables	p, T, u, v, Rel. Hum.

Horizontal anal. grid	325 x 325 points (0.0625° x 0.0625°) on a rotated latitude/longitude grid

Vertical resolution	35 hybrid layers (see LM)

Products		All analysis products are given on the 325 x 325 grid and available at

hourly intervals.

# a)  On the 35 LM layers

Variables: p, T, u, v, w, qv, qc

# b)  On 10 pressure levels (1000, 950, 850, 700, 500, ..., 200 hPa)

Variables: pmsl, (, T, u, v, (, Rel. Hum.

# c)   On 4 constant height levels (1000, 2000, 3000, 5000 m)

Variables: p, T, u, v, w, Rel. Hum.

Assimilation scheme	Continuous data assimilation. Insertion of data in 3-h cycles.

Cut-off time 2 h 14 min for LM runs.

Initialization		None

- Limited-area analysis of soil moisture

Analysis method	2-dimensional (vertical and temporal) variational technique

Analysed variables	Soil moisture of 2 soil layers at 00 UTC

Horizontal anal. grid	325 x 325 points (0.0625° x 0.0625°) on a rotated latitude/longitude grid

Data used		2-m temperature analyses at 12 and 15 UTC

- Limited-area analysis of other surface parameters

Analysis method	Correction methods

Analysed variables	Sea surface temperature (SST) and sea ice cover, snow cover

Horizontal anal. grid	325 x 325 points (0.0625° x 0.0625°) on a rotated latitude/longitude grid

Data used	SST:  Synop-Ship, US-data of ice border, sea ice cover analysis from BSH      (German Institute for shipping and hydrology) for the Baltic Sea and indirectly satellite data (via NCEP-SST and GME_SST analyses).

Snow cover: Snow depth, present and past weather, precipitation amount,

2-m temperature analysis (plus model prediction).

# Additionally, the plant cover is derived on a weekly basis by evaluation of satellite data (NDVI index).

    - Model

7.3.2.1	Schematic summary of the global model GME

Domain		Global

Initial data time		00, 12, 18 UTC

Forecast range		174 h (from 00 and 12 UTC), 48 h (from 18 UTC)

Prognostic variables	ps, T, u, v, qv, qc, o3

Vertical coordinate	hybrid sigma/pressure  (Simmons and Burridge, 1981), 31 layers

Vertical discretization	Finite-difference, energy and angular-momentum conserving

Horizontal grid		Icosahedral-hexagonal (Sadourny et al., 1968), mesh size between

55 and 65 km, average mesh size 60 km; Arakawa-A grid

Horiz. discretization	Finite-difference, second order

Time integration	3-time-level, leapfrog, split semi-implicit scheme, (t = 4 min, time filter.

For moisture variables (water vapour, cloud water): Positive-definite, shape-

preserving horizontal advection (SL-scheme).

Horizontal diffusion	Linear, fourth order

Orography		Grid-scale average based on a 1-km data set

Parameterizations	Surface fluxes based on local roughness length and stability (Louis, 1979)

Free-atmosphere turbulent fluxes based on a level-two scheme

(Mellor and Yamada, 1974)

Sub-grid scale orographic effects (blocking and gravity wave drag) based

on Lott and Miller, 1997

Radiation scheme (two-stream with two solar and five longwave intervals)

after Ritter and Geleyn (1992), full cloud-radiation feedback based on

predicted clouds

Mass flux convection scheme after Tiedtke (1989)

Kessler-type grid-scale precipitation scheme with parameterized cloud

microphysics

Two-layer soil model (Jacobsen and Heise, 1982) including simple vegetation

and snow cover; prescribed climatological values at about 40 cm depth for

temperature and at 100 cm depth for soil moisture.

Over water: Fixed SST from SST analysis; roughness length according to

Charnock´s formula

Analyses and forecasts (up to 78 h) data of GME are sent twice daily (for 00 and 12 UTC) via the Internet to several other national weather services (Brazil, Bulgaria, China, Greece, Israel, Italy, Oman, Poland, Romania, Spain, Switzerland, Vietnam, Yugoslavia). These data serve as initial and lateral boundary data for regional modelling. For a detailed description of GME, see Majewski, 1998 and Majewski et al., 2002.

# 7.2.3.2	Schematic summary of the “Lokal-Modell” LM

Domain		Central Europe

Initial data time		00, 12, 18 UTC

Forecast range		48 h

Prognostic variables	p, T, u, v, w, qv, qc,  TKE

Vertical coordinate	Generalized terrain-following, 35 layers (see Fig. 2)

Vertical discretization	Finite-difference, second order

Horizontal grid		325 x 325 points (0.0625° x 0.0625°) on a rotated latitude/longitude grid,

mesh size 7 km; Arakawa-C grid, see Fig. 1.

Horiz. discretization	Finite-difference, second order

Time integration	Three-time-level, leapfrog, split explicit scheme (Klemp and

Wilhelmson, 1978) with the extensions proposed by

Skamarock and Klemp (1992), (t = 40 s, time filter.

Optionally, a two-time-level split-explicit scheme (Wicker and Skamarock,

1998) and a 3-d semi-implicit scheme (Skamarock et al., 1997) are available.

Horizontal diffusion	Linear, fourth order

Orography	Grid-scale average based on a 1-km data set. Topography has been filtered to remove grid-scale structures

Parameterizations	Surface fluxes based on local roughness length and stability (Louis, 1979)

Free-atmosphere turbulent fluxes based on a level-2.5 scheme with prognostic TKE (Mellor and Yamada, 1974)

Radiation scheme (two-stream with two solar and five longwave intervals)

after Ritter and Geleyn (1992), full cloud-radiation feedback based on

predicted clouds

Mass flux convection scheme after Tiedtke (1989)

Kessler-type grid-scale precipitation scheme with parameterized cloud

microphysics

Two-layer soil model (Jacobsen and Heise, 1982) including simple vegetation

and snow cover; prescribed climatological values at about 40 cm depth for

temperature and at 100 cm depth for soil moisture.

Over water: Fixed SST from SST analysis; roughness length according to

Charnock´s formula

    - Numerical weather prediction products

Short-range forecasts are based on direct model output (DMO) of the LM and on statistically corrected values (simple Kalman filtering). MOS guidance based on GME data is provided, too.

The ECOMET catalogue of the LM is given in annex 2.

    - Operational techniques for application of NWP products

NWP results are used for a variety of further applications. Some of these applications are briefly described below.

DMO is used for the production of any weather situation imaginable in 2-D or 3-D modules as still picture, dynamic graphics, or as a complete film. A graphics system developed for the visualization of meteorological data supports the interactive or automatic presentation of DMO in single images or image sequences.

Short range forecasts of weather and temperature in pictorial form are automatically produced for online presentation on the Internet using Kalman filtered forecasts of both GME (worldwide) and LM (national).

The state of road surfaces is predicted by a road weather forecast system (SWIS – Strassenzustands- und Wetter-Informations-System) using  MOS data based on GME and an energy balance model of the road surface.

The influence of weather on human health is forecasted using a bio-synoptical weather classification scheme and the predicted vorticity, temperature and humidity. The thermal stress on a prototype human being is calculated with an energy balance model which additionally employs forecasted wind and cloudiness. Both weather classification and thermal data are calculated for all grid-points of the

Local Model LM of DWD.

Agrometeorological forecasts cover a wide span of applications aiming at a reduction of the use of insecticides and fungicides or at an optimization of the water supply to plants. NWP results are combined with additional models which calculate the drying of leaves or the temperature and water balance in the ground. These forecasts are presented in www. Agrowetter.de

Significant weather charts which are in use as general guidance for the aeronautical consulting business in the regional forecasting offices and which are issued as products for general aviation cover the middle european area in a layer from  surface up to  24 500 ft. As additional information jet-axes and cat areas are included if within the layer. Icing conditions and turbulence areas are described. The charts are produced interactively on  work stations using LM results in combination with  conventional synoptic methods.

During the season an advice for gliding pilots is prepared which may be received via facsimile. It presents charts of the lowest cloud base or the height of thermal activity, precipitation, wind direction and wind speed for several times during the day. It is based on LM data.

During the summer months an UV-B index is evaluated using predicted ozone concentrations (by GME), TOVS data, and a high resolution radiation model.

  - Specialized forecasts

    - Models

7.4.2.1 	Trajectory Models

# Trajectory model:

Forecast variables		r ((, (, p or z, t)

Data supply			u, v, w, ps from NWP forecasts (or analyses)

Numerical scheme		1st order Euler-Cauchy with iteration (2nd order accuracy)

Interpolation			1st order in time, 2nd (GME) or 3rd (LM) order in space

- Daily routine (ca. 1500 trajectories)

# Trajectories based on LM forecasts:

Domain			Domain of LM (see Fig. 1)

Resolution			0.0625° (as LM)

Initial data time			00, 12 UTC

Trajectory type			Forward trajectories for 36 German, Czech, Swiss, and French

nuclear and chemical installations, backward trajectories for scientific investigations

Forecast range			48-h trajectories, optional start/arrival levels

# Trajectories based on GME forecasts:

Domain			Global

Resolution			~ 60 km (as GME)

Initial data time			00, 12 UTC

Trajectory type	72-h forward trajectories for ca. 60 European nuclear sites and 8 German regional forecast centers, backward trajectories for 37 German radioactivity measuring sites and 8 forecast centers using consecutive +6h to +18h forecast segments.

96-h backward trajectories for the GAW mountain stations Zugspitze, Jungfraujoch, Sonnblick and Hohenpeißenberg, and to the German meteorological observatories.

72-h backward trajectories for 5 African cities in the framework of the

METEOSAT-MDD program, disseminated daily via satellite from

Bracknell.

120-h backward trajectories for the German polar stations Neumayer

(Spitzbergen) and Koldewey (Antarctica) and the research ships

Polarstern and Meteor, disseminated daily.

168-h forward trajectories for 14 Eastern European nuclear power

plants.

Mainly backward trajectories for various scientific investigations.

Forecast range			168h forward and backward trajectories, optional start/arrival levels

b)	Operational emergency trajectory system, trajectory system for scientific investigations:

Models				LM or GME trajectory models

Domain			LM or global

Data supply			u, v, w, ps from LM or GME forecasts or analyses, from current data

base or archives

Trajectory type			Forward and backward trajectories for a choice of offered or freely

eligible stations at optional heights and times in the current period

of 7 to 14 days.

Forecast range			48-h (LM) or 168-h (GME)

Mode				Interactive menu to be executed by forecasters

7.4.2.2	Sea wave models

| Domain | Global | Mediterranean | North, Baltic and Adriatic Sea Areas |
| --- | --- | --- | --- |
| Numerical scheme | Deep water, 3rd generation WAM |
| Wind data supply | GME: u, v at 10 m | LM/GME: u, v at 10 m |
| Grid | geographical (regular lat/lon) |
| Resolution | 0.75° x 0.75° | 0.25° x 0.25° | 0.167° x 0.10° |
| Initial data time | 00 and 12 UTC |
| Forecast range | 174 h | 48 h |
| Model output | significant wave height, frequency, direction |
| Initial state | sea state adapted to analysed wind field over last 12 h |
| Verification | Available on request |

    - Numerical Weather Prediction Products

The forward and backward trajectories are an important tool for emergency response activities. In addition to these forecasts for concentration and deposition of radionuclides are produced using a Lagrangian Particle Dispersion Model.

Based on the Sea wave models charts are produced for swell and significant wave height, frequency and direction .

    - Operational techniques for applications of NWP results

Forecasts of the optimal (shortest and/or safest) route of ships are evaluated using the results of the global sea wave model and of NWP in the ship routing modelling system of the DWD. The system calculates isochrones taking into account the impact of wave and wind on different types of ships.

A very special application of the NWP result is a hydrological one. A model-system called SNOW-D allows for estimating and forecasting snow-cover development and areal melt water release. The model enables a daily calculation and forecast of grid-point values of the water equivalent of the snow cover and meltingwater release. The snow cover development is computed  with the help of physically-based model components which describe accumulation (build-up, increase), metamorphosis (conversion, change) and ablation (decrease, melting).

The model input data are

-	6-hour interval averages of air temperature and vapour pressure

- global radiation/duration of sunshine and precipitation totals of the last 24 h

- three times a week additional data from a part-time network (depth of snow cover, water equivalent of snow cover)

- output data of the „Lokal-Modell“

The model output contains

- current values of the snow cover (reference point 06.00 UTC)

-	snow depth (in cm)

-	water equivalent (in mm)

- specific water equivalent (in mm/cm)

- forecast values of snow cover development (forecast interval maximum 48 hours, forecasting for 6-h-intervals)

-	water equivalent (in mm)

-	precipitation supply, defined as the sum of meltwater release and rain (in mm)

The results are provided grid-oriented and with a blanket coverage for Germany. A summary of the grid values can be made for any area required.

In addition to SNOW-D, a new model-system called SNOW-BW was developed for Baden-Württemberg and will be extended to Rhineland-Palatinate. This model is similar to SNOW-D but it runs every 6 hours and has a higher temporal resolution (1 hour). Not only DWD measurements but also data from regional networks (UMEG) are integrated in the data sampling procedure. Universal Kriging is used for regionalization of measured values to the computational grid.

The strongly improved physics uses wind speed (which is neglected in SNOW-D) for computation of turbulent transfer of heat and moisture taking into account the atmospheric static stability.

The model output contains the quantities of SNOW-D but in addition forecast values of snow depth, snow temperature, ice content and so on can be derived.

The operational UV Index forecast has been upgraded to a physically based fully deterministic global system. It is based on the dynamic prediction of ozone within DWD's global model GME and uses ECMW forecasts +12 h for initialisation. The multiple scattering radiation transfer is computed by lookup tables calculated from the System for Transfer of Atmospheric Radiation (STAR) of the University of Munich. The model comprises modifications for clouds and snow albedo. The forecasts are supplied to the interested WMO member states by the RSMC Offenbach.

- Verifications

Tables 1 up to 6 show verification results of GME  for the european region (36° - 72° N,

12°W – 42 °E), tables 7 up to 12 for the extratropical northern hemisphere and tables 13 up to 18  for  the extratropical southern hemisphere. In all tables forecast times vary from 12 h up to 156 h in intervals of 24 hours. P156.h stands for the RSME-values of persistence and climate for the rsme-values of climate.

# European Region

Table 1 :			GEOPOTENTIAL	500 hPa		RMSE

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 10 | 11 | 10 | 9 | 9 | 8 | 8 | 7 | 8 | 9 | 9 | 9 | 8.9 |
| 36. h | 22 | 21 | 22 | 18 | 16 | 17 | 16 | 16 | 16 | 20 | 19 | 19 | 18.4 |
| 60. h | 38 | 34 | 38 | 28 | 27 | 28 | 26 | 27 | 27 | 31 | 31 | 32 | 30.6 |
| 84. h | 56 | 47 | 54 | 40 | 41 | 40 | 34 | 39 | 39 | 47 | 44 | 50 | 44.3 |
| 108. h | 70 | 65 | 70 | 56 | 59 | 58 | 43 | 49 | 53 | 67 | 59 | 66 | 59.6 |
| 132. h | 89 | 85 | 91 | 73 | 77 | 77 | 55 | 61 | 71 | 83 | 77 | 79 | 76.6 |
| 156. h | 106 | 109 | 112 | 85 | 96 | 93 | 67 | 75 | 86 | 99 | 93 | 96 | 93.1 |
| p156. h | 156 | 170 | 171 | 157 | 124 | 112 | 114 | 92 | 130 | 144 | 148 | 152 | 139.0 |
| climate | 127 | 164 | 130 | 114 | 95 | 90 | 84 | 79 | 119 | 125 | 132 | 128 | 115.5 |

Table 2:		GEOPOTENTIAL	500 hPa		ANOMALY CORRELATION

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 0.99 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 0.997 |
| 36. h | 0.97 | 0.99 | 0.98 | 0.98 | 0.98 | 0.98 | 0.98 | 0.98 | 0.99 | 0.98 | 0.99 | 0.99 | 0.983 |
| 60. h | 0.93 | 0.97 | 0.94 | 0.96 | 0.95 | 0.95 | 0.94 | 0.94 | 0.97 | 0.96 | 0.96 | 0.96 | 0.952 |
| 84. h | 0.86 | 0.95 | 0.88 | 0.92 | 0.89 | 0.88 | 0.89 | 0.87 | 0.94 | 0.91 | 0.93 | 0.90 | 0.900 |
| 108. h | 0.79 | 0.90 | 0.81 | 0.85 | 0.76 | 0.76 | 0.83 | 0.79 | 0.87 | 0.80 | 0.86 | 0.83 | 0.821 |
| 132. h | 0.67 | 0.84 | 0.69 | 0.72 | 0.61 | 0.59 | 0.73 | 0.65 | 0.79 | 0.69 | 0.78 | 0.74 | 0.709 |
| 156. h | 0.54 | 0.73 | 0.52 | 0.61 | 0.42 | 0.39 | 0.63 | 0.46 | 0.70 | 0.58 | 0.69 | 0.62 | 0.574 |

Table 3:			PRESSURE	MSL		RMSE

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 1.2 | 1.2 | 1.2 | 1.1 | 1.0 | 0.9 | 0.9 | 0.9 | 0.9 | 1.0 | 1.0 | 1.0 | 1.03 |
| 36. h | 2.6 | 2.2 | 2.4 | 1.8 | 1.6 | 1.7 | 1.7 | 1.7 | 1.7 | 2.2 | 2.0 | 2.2 | 1.97 |
| 60. h | 4.2 | 3.5 | 3.9 | 2.6 | 2.4 | 2.6 | 2.7 | 2.9 | 2.7 | 3.4 | 3.1 | 3.6 | 3.13 |
| 84. h | 5.4 | 4.8 | 5.4 | 3.6 | 3.4 | 3.6 | 3.3 | 3.8 | 3.5 | 4.8 | 4.5 | 5.1 | 4.26 |
| 108. h | 6.7 | 6.1 | 6.8 | 4.9 | 4.8 | 4.9 | 3.9 | 4.3 | 4.5 | 6.5 | 6.1 | 6.6 | 5.51 |
| 132. h | 8.2 | 8.0 | 8.1 | 6.1 | 6.3 | 6.3 | 4.7 | 5.2 | 5.8 | 8.0 | 7.7 | 7.7 | 6.84 |
| 156. h | 9.6 | 10.2 | 9.6 | 7.2 | 7.7 | 7.1 | 5.5 | 6.0 | 6.8 | 8.8 | 9.7 | 9.4 | 8.14 |
| p156. h | 11.8 | 14.6 | 14.6 | 12.8 | 9.8 | 7.2 | 8.9 | 7.4 | 9.3 | 13.2 | 11.9 | 14.0 | 11.30 |
| climate | 10.5 | 15.8 | 10.3 | 8.5 | 6.5 | 6.0 | 6.1 | 6.0 | 8.1 | 10.0 | 12.6 | 12.6 | 9.43 |

Table 4: 	PRESSURE	MSL		ANOMALY CORRELATION

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 0.99 | 1.00 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 1.00 | 1.00 | 0.992 |
| 36. h | 0.95 | 0.99 | 0.96 | 0.97 | 0.97 | 0.96 | 0.96 | 0.96 | 0.97 | 0.96 | 0.98 | 0.98 | 0.968 |
| 60. h | 0.87 | 0.96 | 0.90 | 0.94 | 0.93 | 0.92 | 0.91 | 0.90 | 0.92 | 0.91 | 0.95 | 0.95 | 0.922 |
| 84. h | 0.80 | 0.92 | 0.83 | 0.89 | 0.85 | 0.81 | 0.85 | 0.81 | 0.88 | 0.84 | 0.89 | 0.88 | 0.854 |
| 108. h | 0.71 | 0.86 | 0.74 | 0.81 | 0.69 | 0.64 | 0.78 | 0.72 | 0.77 | 0.72 | 0.81 | 0.81 | 0.754 |
| 132. h | 0.58 | 0.76 | 0.62 | 0.68 | 0.53 | 0.44 | 0.68 | 0.59 | 0.67 | 0.60 | 0.75 | 0.72 | 0.636 |
| 156. h | 0.46 | 0.60 | 0.49 | 0.53 | 0.33 | 0.29 | 0.60 | 0.45 | 0.58 | 0.51 | 0.65 | 0.60 | 0.508 |

Table 5: 	TEMPERATURE	850 hPa		RMSE

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.91 |
| 36. h | 1.6 | 1.5 | 1.5 | 1.3 | 1.4 | 1.4 | 1.3 | 1.3 | 1.3 | 1.4 | 1.4 | 1.4 | 1.42 |
| 60. h | 2.2 | 2.0 | 2.1 | 1.7 | 1.8 | 1.8 | 1.7 | 1.7 | 1.7 | 1.9 | 1.9 | 2.0 | 1.87 |
| 84. h | 2.8 | 2.5 | 2.8 | 2.1 | 2.2 | 2.3 | 2.0 | 2.2 | 2.2 | 2.4 | 2.4 | 2.7 | 2.38 |
| 108. h | 3.3 | 3.0 | 3.3 | 2.6 | 2.8 | 2.9 | 2.4 | 2.5 | 2.7 | 3.1 | 2.8 | 3.3 | 2.89 |
| 132. h | 4.0 | 3.7 | 3.9 | 3.1 | 3.5 | 3.5 | 2.8 | 2.8 | 3.3 | 3.8 | 3.3 | 3.8 | 3.47 |
| 156. h | 4.4 | 4.4 | 4.8 | 3.6 | 4.2 | 4.1 | 3.3 | 3.3 | 3.8 | 4.3 | 3.9 | 4.4 | 4.03 |
| p156. h | 5.7 | 5.4 | 5.8 | 5.6 | 5.6 | 5.4 | 5.0 | 4.2 | 5.2 | 5.1 | 5.7 | 5.9 | 5.38 |
| climate | 4.8 | 4.7 | 4.2 | 4.2 | 4.5 | 4.0 | 3.7 | 3.2 | 4.7 | 4.8 | 4.3 | 5.5 | 4.39 |

Table 6: 	TEMPERATURE	850 hPa		ANOMALY CORRELATION

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 0.98 | 0.97 | 0.98 | 0.97 | 0.97 | 0.97 | 0.96 | 0.96 | 0.97 | 0.97 | 0.97 | 0.98 | 0.971 |
| 36. h | 0.93 | 0.94 | 0.92 | 0.93 | 0.94 | 0.93 | 0.92 | 0.90 | 0.94 | 0.93 | 0.94 | 0.95 | 0.931 |
| 60. h | 0.87 | 0.89 | 0.85 | 0.89 | 0.89 | 0.88 | 0.88 | 0.84 | 0.90 | 0.87 | 0.90 | 0.91 | 0.880 |
| 84. h | 0.80 | 0.83 | 0.76 | 0.83 | 0.82 | 0.80 | 0.83 | 0.75 | 0.85 | 0.80 | 0.84 | 0.84 | 0.812 |
| 108. h | 0.73 | 0.77 | 0.68 | 0.75 | 0.71 | 0.67 | 0.78 | 0.66 | 0.78 | 0.69 | 0.77 | 0.77 | 0.730 |
| 132. h | 0.62 | 0.67 | 0.56 | 0.64 | 0.58 | 0.54 | 0.70 | 0.57 | 0.67 | 0.58 | 0.66 | 0.67 | 0.621 |
| 156. h | 0.49 | 0.56 | 0.38 | 0.52 | 0.43 | 0.38 | 0.62 | 0.42 | 0.55 | 0.47 | 0.57 | 0.58 | 0.497 |

  - Extratropical northern hemisphere

Table 7:		GEOPOTENTIAL	500 hPa		RMSE

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 12 | 11 | 11 | 10 | 10 | 9 | 9 | 8 | 9 | 9 | 10 | 10 | 9.9 |
| 36. h | 24 | 23 | 23 | 20 | 19 | 17 | 18 | 16 | 17 | 18 | 20 | 21 | 19,6 |
| 60. h | 38 | 36 | 36 | 32 | 29 | 28 | 29 | 24 | 27 | 29 | 31 | 33 | 30.9 |
| 84. h | 52 | 50 | 52 | 44 | 41 | 39 | 39 | 33 | 38 | 42 | 45 | 47 | 43.6 |
| 108. h | 67 | 65 | 68 | 56 | 53 | 51 | 48 | 43 | 51 | 57 | 60 | 63 | 56.8 |
| 132. h | 79 | 80 | 83 | 68 | 64 | 61 | 57 | 53 | 64 | 73 | 75 | 76 | 69.5 |
| 156. h | 92 | 94 | 96 | 80 | 74 | 70 | 65 | 63 | 76 | 85 | 86 | 90 | 81.0 |
| p156. h | 134 | 136 | 137 | 127 | 107 | 95 | 96 | 91 | 109 | 124 | 128 | 144 | 119.0 |
| climate | 110 | 108 | 111 | 105 | 87 | 78 | 69 | 72 | 92 | 111 | 110 | 116 | 97.4 |

Table 8:		GEOPOTENTIAL	500 hPa		ANOMALY CORRELATION

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 0.99 | 0.99 | 1.00 | 1.00 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 1.00 | 1.00 | 1.00 | 0.994 |
| 36. h | 0.98 | 0.98 | 0.98 | 0.98 | 0.98 | 0.97 | 0.96 | 0.97 | 0.98 | 0.98 | 0.98 | 0.98 | 0.977 |
| 60. h | 0.94 | 0.94 | 0.94 | 0.95 | 0.94 | 0.92 | 0.90 | 0.94 | 0.95 | 0.96 | 0.96 | 0.96 | 0.942 |
| 84. h | 0.88 | 0.88 | 0.88 | 0.90 | 0.89 | 0.85 | 0.83 | 0.88 | 0.90 | 0.91 | 0.91 | 0.91 | 0.885 |
| 108. h | 0.81 | 0.80 | 0.80 | 0.84 | 0.80 | 0.74 | 0.73 | 0.80 | 0.82 | 0.84 | 0.83 | 0.85 | 0.805 |
| 132. h | 0.72 | 0.71 | 0.70 | 0.76 | 0.71 | 0.63 | 0.62 | 0.70 | 0.72 | 0.75 | 0.75 | 0.77 | 0.710 |
| 156. h | 0.63 | 0.60 | 0.59 | 0.66 | 0.60 | 0.51 | 0.51 | 0.59 | 0.61 | 0.65 | 0.66 | 0.67 | 0.609 |

Table 9:			PRESSURE	MSL		RMSE

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 1.4 | 1.4 | 1.4 | 1.3 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.3 | 1.4 | 1.29 |
| 36. h | 2.8 | 2.6 | 2.5 | 2.3 | 2.1 | 2.0 | 2.1 | 2.0 | 2.1 | 2.1 | 2.3 | 2.5 | 2.28 |
| 60. h | 4.1 | 3.8 | 3.6 | 3.3 | 3.0 | 2.8 | 2.8 | 2.7 | 3.0 | 3.1 | 3.3 | 3.6 | 3.25 |
| 84. h | 5.3 | 5.1 | 5.0 | 4.4 | 3.8 | 3.6 | 3.6 | 3.4 | 3.9 | 4.2 | 4.6 | 4.9 | 4.31 |
| 108. h | 6.5 | 6.4 | 6.4 | 5.4 | 4.7 | 4.5 | 4.3 | 4.2 | 4.9 | 5.4 | 5.9 | 6.3 | 5.42 |
| 132. h | 7.5 | 7.7 | 7.7 | 6.2 | 5.6 | 5.3 | 4.9 | 5.0 | 6.0 | 6.7 | 7.3 | 7.5 | 6.45 |
| 156. h | 8.4 | 8.8 | 8.7 | 7.1 | 6.3 | 6.0 | 5.5 | 5.8 | 6.8 | 7.8 | 8.3 | 8.7 | 7.36 |
| p156. h | 11.9 | 12.8 | 12.8 | 11.1 | 8.9 | 7.9 | 8.1 | 7.9 | 9.3 | 11.1 | 11.5 | 13.0 | 10.52 |
| climate | 9.8 | 10.2 | 9.9 | 8.1 | 6.8 | 6.0 | 5.5 | 5.9 | 7.2 | 9.0 | 9.4 | 10.4 | 8.18 |

Table 10:	PRESSURE	MSL		ANOMALY CORRELATION

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 0.99 | 0.99 | 0.99 | 0.99 | 0.98 | 0.98 | 0.97 | 0.98 | 0.98 | 0.99 | 0.99 | 0.99 | 0.986 |
| 36. h | 0.96 | 0.96 | 0.97 | 0.96 | 0.95 | 0.94 | 0.92 | 0.94 | 0.95 | 0.97 | 0.97 | 0.97 | 0.955 |
| 60. h | 0.91 | 0.92 | 0.93 | 0.92 | 0.89 | 0.88 | 0.86 | 0.89 | 0.90 | 0.93 | 0.93 | 0.94 | 0.909 |
| 84. h | 0.84 | 0.86 | 0.87 | 0.85 | 0.82 | 0.81 | 0.78 | 0.81 | 0.84 | 0.87 | 0.87 | 0.89 | 0.843 |
| 108. h | 0.76 | 0.77 | 0.78 | 0.77 | 0.72 | 0.70 | 0.68 | 0.73 | 0.75 | 0.79 | 0.78 | 0.81 | 0.753 |
| 132. h | 0.68 | 0.69 | 0.68 | 0.69 | 0.61 | 0.58 | 0.57 | 0.61 | 0.63 | 0.68 | 0.68 | 0.73 | 0.652 |
| 156. h | 0.60 | 0.61 | 0.58 | 0.59 | 0.50 | 0.46 | 0.47 | 0.49 | 0.52 | 0.59 | 0.58 | 0.63 | 0.551 |

Table 11:		TEMPERATURE	850 hPa		RMSE

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 1.1 | 1.05 |
| 36. h | 1.9 | 1.8 | 1.8 | 1.8 | 1.7 | 1.7 | 1.6 | 1.5 | 1.6 | 1.6 | 1.7 | 1.8 | 1.71 |
| 60. h | 2.5 | 2.4 | 2.4 | 2.3 | 2.3 | 2.2 | 2.1 | 1.9 | 2.0 | 2.0 | 2.2 | 2.3 | 2.22 |
| 84. h | 3.1 | 3.1 | 3.0 | 2.9 | 2.7 | 2.6 | 2.5 | 2.3 | 2.4 | 2.5 | 2.7 | 2.9 | 2.73 |
| 108. h | 3.7 | 3.7 | 3.6 | 3.3 | 3.2 | 3.1 | 2.9 | 2.7 | 2.8 | 3.0 | 3.3 | 3.4 | 3.23 |
| 132. h | 4.2 | 4.3 | 4.2 | 3.7 | 3.6 | 3.5 | 3.2 | 3.0 | 3.3 | 3.5 | 3.8 | 4.0 | 3.69 |
| 156. h | 4.7 | 4.8 | 4.7 | 4.2 | 4.0 | 3.9 | 3.5 | 3.3 | 3.7 | 4.0 | 4.2 | 4.5 | 4.12 |
| p156. h | 6.3 | 6.4 | 6.3 | 6.2 | 5.6 | 4.9 | 4.8 | 4.7 | 5.2 | 5.5 | 5.9 | 6.5 | 5.71 |
| climate | 4.9 | 5.1 | 5.0 | 4.7 | 4.6 | 3.9 | 3.5 | 3.5 | 4.3 | 4.8 | 4.8 | 5.3 | 4.54 |

Table 12:	TEMPERATURE	850 hPa		ANOMALY CORRELATION

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 0.98 | 0.98 | 0.98 | 0.97 | 0.97 | 0.96 | 0.95 | 0.95 | 0.96 | 0.97 | 0.97 | 0.98 | 0.968 |
| 36. h | 0.93 | 0.93 | 0.93 | 0.92 | 0.92 | 0.89 | 0.88 | 0.89 | 0.92 | 0.93 | 0.93 | 0.94 | 0.918 |
| 60. h | 0.87 | 0.88 | 0.88 | 0.87 | 0.86 | 0.83 | 0.81 | 0.83 | 0.87 | 0.89 | 0.88 | 0.90 | 0.864 |
| 84. h | 0.79 | 0.80 | 0.82 | 0.80 | 0.79 | 0.75 | 0.74 | 0.76 | 0.82 | 0.83 | 0.81 | 0.84 | 0.796 |
| 108. h | 0.71 | 0.72 | 0.74 | 0.73 | 0.71 | 0.66 | 0.65 | 0.69 | 0.75 | 0.76 | 0.73 | 0.77 | 0.718 |
| 132. h | 0.62 | 0.63 | 0.65 | 0.65 | 0.63 | 0.57 | 0.58 | 0.61 | 0.66 | 0.67 | 0.65 | 0.69 | 0.635 |
| 156. h | 0.53 | 0.55 | 0.56 | 0.56 | 0.54 | 0.48 | 0.51 | 0.55 | 0.57 | 0.57 | 0.56 | 0.61 | 0.549 |

8.3	Extratropical southern hemisphere

Table 13:		GEOPOTENTIAL	500 hPa		RMSE

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 12 | 13 | 14 | 15 | 15 | 16 | 16 | 15 | 15 | 14 | 13 | 12 | 14.0 |
| 36. h | 27 | 30 | 33 | 32 | 33 | 36 | 35 | 33 | 32 | 31 | 29 | 25 | 31.3 |
| 60. h | 41 | 48 | 51 | 49 | 51 | 55 | 53 | 50 | 48 | 48 | 45 | 37 | 48.0 |
| 84. h | 56 | 64 | 69 | 66 | 68 | 75 | 69 | 67 | 63 | 65 | 60 | 48 | 64.0 |
| 108. h | 69 | 76 | 85 | 83 | 82 | 92 | 83 | 82 | 78 | 80 | 74 | 60 | 78.7 |
| 132. h | 81 | 86 | 98 | 98 | 96 | 105 | 95 | 96 | 90 | 91 | 88 | 70 | 91.2 |
| 156. h | 91 | 94 | 107 | 108 | 108 | 117 | 107 | 107 | 100 | 102 | 99 | 78 | 101.7 |
| p156. h | 111 | 129 | 135 | 139 | 139 | 144 | 144 | 155 | 140 | 132 | 116 | 127 | 134.2 |
| climate | 89 | 93 | 113 | 106 | 127 | 118 | 110 | 118 | 112 | 119 | 99 | 88 | 107.7 |

Table 14:	GEOPOTENTIAL	500 hPa		ANOMALY CORRELATION

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.991 |
| 36. h | 0.95 | 0.94 | 0.96 | 0.95 | 0.96 | 0.95 | 0.95 | 0.96 | 0.96 | 0.97 | 0.96 | 0.96 | 0.956 |
| 60. h | 0.88 | 0.86 | 0.90 | 0.89 | 0.91 | 0.89 | 0.89 | 0.91 | 0.90 | 0.92 | 0.90 | 0.91 | 0.897 |
| 84. h | 0.78 | 0.75 | 0.81 | 0.80 | 0.85 | 0.80 | 0.81 | 0.84 | 0.83 | 0.86 | 0.82 | 0.84 | 0.816 |
| 108. h | 0.67 | 0.64 | 0.72 | 0.69 | 0.77 | 0.70 | 0.73 | 0.76 | 0.74 | 0.78 | 0.72 | 0.75 | 0.722 |
| 132. h | 0.56 | 0.55 | 0.64 | 0.58 | 0.70 | 0.60 | 0.64 | 0.67 | 0.65 | 0.71 | 0.60 | 0.65 | 0.629 |
| 156. h | 0.45 | 0.47 | 0.56 | 0.50 | 0.62 | 0.50 | 0.56 | 0.58 | 0.57 | 0.63 | 0.49 | 0.56 | 0.541 |

Table 15:		PRESSURE		MSL		RMSE

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 1.5 | 1.7 | 1.7 | 1.8 | 1.9 | 2.1 | 2.1 | 2.0 | 1.9 | 1.8 | 1.6 | 1.5 | 1.79 |
| 36. h | 2.9 | 3.4 | 3.5 | 3.6 | 3.8 | 4.0 | 4.1 | 3.8 | 3.7 | 3.6 | 3.2 | 2.7 | 3.51 |
| 60. h | 4.1 | 4.9 | 5.2 | 5.0 | 5.4 | 5.6 | 5.8 | 5.5 | 5.2 | 5.0 | 4.6 | 3.7 | 4.99 |
| 84. h | 5.3 | 6.2 | 6.6 | 6.5 | 6.8 | 7.4 | 7.2 | 6.9 | 6.6 | 6.5 | 5.7 | 4.7 | 6.36 |
| 108. h | 6.3 | 7.0 | 7.8 | 7.9 | 8.1 | 8.9 | 8.2 | 8.2 | 7.8 | 7.8 | 6.9 | 5.7 | 7.55 |
| 132. h | 7.2 | 7.8 | 8.9 | 9.0 | 9.2 | 10.1 | 9.2 | 9.4 | 8.7 | 8.9 | 8.0 | 6.4 | 8.57 |
| 156. h | 8.0 | 8.5 | 9.5 | 9.9 | 10.2 | 11.1 | 10.5 | 10.5 | 9.6 | 9.6 | 8.9 | 7.0 | 9.44 |
| p156. h | 9.6 | 10.6 | 11.7 | 11.8 | 12.6 | 12.7 | 13.3 | 13.9 | 12.5 | 12.0 | 10.5 | 10.4 | 11.80 |
| climate | 7.9 | 7.9 | 10.0 | 9.5 | 11.9 | 10.7 | 10.8 | 10.4 | 10.5 | 11.3 | 8.5 | 7.4 | 9.74 |

Table 16:	PRESSURE		MSL		ANOMALY CORRELATION

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 0.98 | 0.98 | 0.99 | 0.98 | 0.99 | 0.98 | 0.98 | 0.98 | 0.98 | 0.99 | 0.98 | 0.98 | 0.982 |
| 36. h | 0.93 | 0.90 | 0.93 | 0.92 | 0.94 | 0.93 | 0.93 | 0.93 | 0.93 | 0.95 | 0.93 | 0.94 | 0.931 |
| 60. h | 0.85 | 0.80 | 0.86 | 0.84 | 0.88 | 0.86 | 0.85 | 0.86 | 0.87 | 0.90 | 0.86 | 0.88 | 0.858 |
| 84. h | 0.75 | 0.68 | 0.78 | 0.74 | 0.82 | 0.76 | 0.78 | 0.77 | 0.79 | 0.84 | 0.78 | 0.79 | 0.772 |
| 108. h | 0.65 | 0.59 | 0.69 | 0.63 | 0.75 | 0.65 | 0.71 | 0.69 | 0.70 | 0.77 | 0.67 | 0.68 | 0.681 |
| 132. h | 0.56 | 0.48 | 0.61 | 0.54 | 0.67 | 0.54 | 0.63 | 0.59 | 0.63 | 0.69 | 0.55 | 0.59 | 0.592 |
| 156. h | 0.46 | 0.39 | 0.55 | 0.47 | 0.60 | 0.46 | 0.53 | 0.49 | 0.56 | 0.63 | 0.44 | 0.51 | 0.508 |

Table 17:	TEMPERATURE	850 hPa		RMSE

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 1.1 | 1.2 | 1.2 | 1.2 | 1.3 | 1.5 | 1.4 | 1.4 | 1.3 | 1.3 | 1.2 | 1.1 | 1.27 |
| 36. h | 1.9 | 2.1 | 2.1 | 2.2 | 2.3 | 2.7 | 2.5 | 2.5 | 2.4 | 2.3 | 2.1 | 1.9 | 2.24 |
| 60. h | 2.5 | 2.7 | 2.8 | 2.8 | 3.0 | 3.4 | 3.2 | 3.1 | 3.1 | 3.0 | 2.7 | 2.3 | 2.88 |
| 84. h | 2.9 | 3.2 | 3.4 | 3.3 | 3.4 | 3.9 | 3.6 | 3.6 | 3.6 | 3.5 | 3.2 | 2.7 | 3.36 |
| 108. h | 3.3 | 3.6 | 3.9 | 3.7 | 3.8 | 4.4 | 4.0 | 4.0 | 3.9 | 3.9 | 3.6 | 3.0 | 3.75 |
| 132. h | 3.7 | 3.8 | 4.2 | 4.0 | 4.1 | 4.6 | 4.3 | 4.4 | 4.2 | 4.2 | 3.9 | 3.3 | 4.06 |
| 156. h | 3.9 | 4.0 | 4.4 | 4.2 | 4.4 | 4.9 | 4.6 | 4.7 | 4.4 | 4.4 | 4.2 | 3.5 | 4.31 |
| p156. h | 4.3 | 5.0 | 4.9 | 5.1 | 4.9 | 5.6 | 5.3 | 5.8 | 5.4 | 5.2 | 4.7 | 4.6 | 5.07 |
| climate | 3.5 | 4.1 | 4.4 | 4.4 | 4.3 | 4.6 | 4.5 | 4.8 | 4.6 | 4.1 | 3.8 | 3.4 | 4.20 |

Table 18:	TEMPERATURE	850 hPa		ANOMALY CORRELATION

|  | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12. h | 0.95 | 0.95 | 0.96 | 0.96 | 0.95 | 0.95 | 0.95 | 0.96 | 0.96 | 0.95 | 0.95 | 0.95 | 0.953 |
| 36. h | 0.85 | 0.86 | 0.87 | 0.87 | 0.85 | 0.83 | 0.84 | 0.88 | 0.88 | 0.86 | 0.85 | 0.86 | 0.858 |
| 60. h | 0.75 | 0.76 | 0.77 | 0.78 | 0.76 | 0.72 | 0.75 | 0.81 | 0.80 | 0.76 | 0.76 | 0.79 | 0.767 |
| 84. h | 0.65 | 0.66 | 0.68 | 0.70 | 0.69 | 0.62 | 0.67 | 0.73 | 0.72 | 0.67 | 0.67 | 0.72 | 0.682 |
| 108. h | 0.55 | 0.57 | 0.59 | 0.63 | 0.61 | 0.53 | 0.60 | 0.68 | 0.66 | 0.59 | 0.57 | 0.64 | 0.602 |
| 132. h | 0.46 | 0.50 | 0.52 | 0.56 | 0.55 | 0.47 | 0.55 | 0.62 | 0.61 | 0.52 | 0.47 | 0.56 | 0.533 |
| 156. h | 0.39 | 0.45 | 0.47 | 0.52 | 0.49 | 0.40 | 0.49 | 0.57 | 0.56 | 0.45 | 0.39 | 0.50 | 0.473 |

9.	Plans for the future

During the first half of 2003, cloud ice will be introduced as prognostic variable in GME and LM to allow for a better simulation of ice and mixed phase clouds. Also, a seven-layer soil model which includes freezing of soil moisture and a better representation of snow will be made operational in 2003.

By the end of the year, the mesh size of GME will be reduced from 60 to 40 km, and the number of layers increased from 31 to 40. For LM, the model domain will be increased from 325 x 325 to about 750 x 638 gridpoints with a mesh size of 7 km, the number of layers will be increased from 35 to 40, and the forecast range extended from 48 to 78 hours.

A nowcasting and very short range (up to 18 hours, initialised every three hours) forecast version of LM is under development with a mesh size of 2.8 km and 50 layers. This high a resolution aims mainly at the explicit prediction of deep convection which is a major forecasting problem in Germany during the warm season. The further development of LM is co-ordinated in the Consortium for Small-Scale Modelling (COSMO). Current members of COSMO are the weather services of Germany, Greece, Italy, Poland and Switzerland

Concerning applications of NWP results it is planned to make a more systematic approach to severe weather forecasting by making use of objective methods based on the EPS provided by the ECMWF. For any kind of postprocessed specialized forecasts of the parameters temperature, wind and significant weather MOS will be used instead of Kalman Filtering.

- References

# Jacobson, I. and E. Heise, 1982: A new economic method for the computation of the surface

temperature in numerical models. Beitr. Phys. Atm., 55, 128-141.

Klemp, J. and   Wilhelmson, 1978: The simulation of three-dimensional convective storm dynamics.

J. Atmos. Sci., 35, 1070-1096.

# Lott, F. and M. Miller, 1997: A new sub-grid scale orographic drag parameterization: its formulation

and testing. Quart. J. Roy. Meteor. Soc., 123, 101-128.

Louis, J.-F., 1979: A parametric model of vertical eddy fluxes in the atmosphere.

Boundary layer Meteor., 17, 187-202.

Lynch, P., 1997: The Dolph-Chebyshev window: A simple optimal filter.

Mon. Wea. Rev., 125, 655-660.

# Majewski, D., 1998: The new icosahedral-hexagonal global gridpoint model GME of the Deutscher

Wetterdienst. ECMWF Seminar “Numerical Methods in Atmospheric Models”, Sept. 1998.

Majewski, D., D. Liermann, P. Prohl, B. Ritter, M. Buchhold, T. Hanisch, G. Paul, W. Wergen and

J. Baumgardner, 2002: The operational global icosahedral-hexagonal gridpoint model GME: Description and high-resolution tests. Mon. Wea. Rev., 130, 319-338

# Mellor, G. L. and T. Yamada, 1974: A hierarchy of turbulent closure models for planetary boundary

layers. J. Atmos. Sci., 31, 1791-1806.

# Ritter, B. and J. F. Geleyn, 1992: A comprehensive radiation scheme for numerical weather prediction

models with potential applications in climate simulations. Mon. Wea. Rev., 119.

# Sadourny, R., Arakawa, A. and Y. Mintz, 1968: Integration of nondivergent barotropic vorticity

equation with an icosahedral-hexagonal grid on the sphere. Mon. Wea. Rev., 96, 351-356.

Schraff, C., 1997: Mesocale data assimilation and prediction of low stratus in the Alpine region.

Meteorol. Atmos. Phys., 64, 21-50.

# Simmons, A. J. and D. M. Burridge, 1981: An energy and angular-momentum conserving vertical

finite-difference scheme and hybrid vertical coordinates. Mon. Wea. Rev., 109, 758-766.

# Skamarock, W. and J. B. Klemp, 1992: The stability of time-splitting numerical methods for the

hydrostatic and nonhydrostatic elastic systems. Mon. Wea. Rev., 120, 2100-2127.

# Skamarock, W., P. Smolarkiewicz and J. B. Klemp, 1997: Preconditioned conjugate residual solvers

for the Helmholtz equations in nonhydrostatic models. Mon. Wea. Rev., 125, 587-599.

# Tiedtke, M., 1989: A comprehensive mass flux scheme for cumulus parameterization in large scale

models. Mon. Wea. Rev., 117, 1779-1800.

# Wicker, L. and W. Skamarock, 1998: A time splitting scheme for the elastic equations incorporating

second-order Runge-Kutta time differencing. Mon. Wea. Rev., 126, 1992-1999.

# Text boxes

Figure 2	Model layers of LM.

Figure 1	Model domain of the “Lokal-Modell” LM

mesh size ~ 7 km, 325 x 325 gridpoints.