# JOINT WMO TECHNICAL PROGRESS REPORT ON THE GLOBAL DATA PROCESSING AND FORECASTING SYSTEM AND NUMERICAL WEATHER PREDICTION RESEARCH ACTIVITIES FOR 2012

Japan Meteorological Agency

## Summary of highlights

- JMA installed a new computer system consisting of two Hitachi SR16000/M1 units (peak performance: 423.5 TFLOPS each), and operation was begun on 5 June, 2012 (see 2).

- Operation of the new convection-resolving 2-km horizontal mesh Local Forecast Model (LFM) was begun on 30 August, 2012, along with Local Analysis (LA) (see 4.3.1.1 (3) and 4.3.2.1 (2)).

- Revisions to the Global Navigation Satellite System (GNSS) Radio Occultation (RO) refractivity data assimilation process were introduced into the operational global Numerical Weather Prediction (NWP) system on 18 December, 2012 (see 4.2.1.2 (1)).

- The stratocumulus parameterization scheme of the operational Global Spectral Model was improved on 18 December, 2012 (see 4.2.2.2 (1)).

## 2.	Equipment in use

On 5 June, 2012, an upgraded version of the computer system used for numerical analysis/prediction and satellite data processing was installed at the Office of Computer Systems Operations in Kiyose, which is about 30 km northwest of JMA’s Tokyo Headquarters. The office in Kiyose and JMA’s Headquarters are connected via a wide-area network. The computer types used in the system are listed in Table 2-1, and further details are provided in Narita (2013).

Table 2-1  Major features of computers

Supercomputers (Kiyose)	Hitachi: SR16000 model M1

Number of subsystem	2

Number of nodes	54 physical nodes per subsystem

432 logical nodes per subsystem

Processors	3,456 IBM POWER7 processors (32 per node)

Performance	423.5 TFlops per subsystem (7.84 TFLOPS per node)

Main memory	55.296 TiB per subsystem (128 GiB per node)

High-speed storage*	Hitachi AMS2500 (138 TB for primary, 210 TB for secondary)

Data transfer rate	96 GiB/s (one way) (between any two nodes)

Operating system	IBM AIX Version 7.1

* Dedicated storage for supercomputers

Primary Satellite Data Processing Servers (Kiyose):  Hitachi EP8000/750

Number of servers	3

Processor	IBM POWER7 (3.0 GHz)

Main memory	128 GiB per server

Operating system	IBM AIX Version 6.1

Secondary Satellite Data Processing Servers (Kiyose):  Hitachi EP8000/750

Number of servers	6

Processor	IBM POWER7 (3.0 GHz)

Main memory	128 GiB per server

Operating system	IBM AIX Version 6.1

Foreign Satellite Data Processing Servers (Kiyose):  Hitachi HA8000/RS220AK1

Number of servers	6

Processor	Intel Xeon X5670 (2.93 GHz)

Main memory	32 GiB per server

Operating system	Linux

Division Processing Servers A (Kiyose):  Hitachi BS2000

Number of servers	16

Processor	Intel Xeon E5640 (2.66 GHz)

Main memory	48 GiB per server

Operating system	Linux

Division Processing Servers B (Kiyose):  Hitachi EP8000/520

Number of servers	2

Processor	IBM Power6+ (4.7 GHz)

Main memory	32 GiB per server

Operating system	IBM AIX Version 6.1

Decording Servers (Kiyose):  Hitachi EP8000/750

Number of servers	2

Processor	IBM Power7 (3.70 GHz)

Main memory	64 GiB per server

Operating system	IBM AIX Version 6.1

Mass Storage System (Kiyose)

Shared storage**	Hitachi VFP500N and AMS2500 (754 TB total, RAID 6)

Data bank storage**	Hitachi VFP500N and AMS2500 (2932 TB total, RAID 6)

Backup tape storage	Hitachi EP8000 and L56/3000 (1520 TB total)

** Shared by supercomputers and servers

Wide Area Network (between HQ and Kiyose)

Network bandwidth	200 Mbps (two independent 100-Mbps WANs)

## 3.	Data and Products from GTS and other sources in use

### 3.1 	Observation

A summary of data received through the GTS and other sources and processed at JMA is given in Table 3-1.

Table 3-1  Number of observation reports in use

SYNOP/SHIP	84,000/day

BUOY	25,000/day

TEMP-A/PILOT-A	1,800/day

TEMP-B/PILOT-B	1,800/day

TEMP-C/PILOT-C	1,300/day

TEMP-D/PILOT-D	1,200/day

AIREP/AMDAR	556,000/day

PROFILER	8,300/day

AIRS/AMSU	320,000/day

NOAA/AMSU-A	1,260,000/day

Metop/AMSU-A	324,000/day

NOAA/AMSU-B	8,050,000/day

NOAA/MHS	5,830,000/day

Metop/MHS	2,910,000/day

Metop/ASCAT        	4,200,000/day

GOES/CSR          	1,400,000/day

MTSAT/CSR         	140,000/day

METEOSAT/CSR     	1,650,000/day

GPSRO              	33,000/day

AMV       	4,000,000/day

SSMIS              	21,600,000/day

TRMM/TMI           	4,730,000/day

GNSS-PWV	164,000/day

AMeDAS  	232,400/day

Radar Reflectivity	4,200/day

Radial Velocity	4,200/day

Typhoon Bogus	         12/day

### 3.2 	Forecast products

Grid Point Value (GPV) products of the global prediction model from ECMWF, NCEP, UKMO, BOM, CMS, DWD and CMA are used for internal reference and monitoring. The products of ECMWF are received via the GTS, and the other products are received via the Internet.

## 4.	Forecasting systems

### 4.1	System run schedule and forecast ranges

Table 4.1-1 summarizes the system run schedule and forecast ranges.

Table 4.1-1 Schedule of the analysis and forecast system

| Model | Initial time (UTC) | Run schedule (UTC) | Forecast range (hours) |
| --- | --- | --- | --- |
| Global Analysis/Forecast | 00 06 12 18 | 0225 – 0330 0825 – 0930 1425 – 1530, 1715 – 1800 2025 – 2130 | 84 84 216 84 |
| Meso-scale Analysis/Forecast | 00 03 06 09 12 15 18 21 | 0055 – 0140 0355 – 0505 0655 – 0740 0955 – 1105 1255 – 1340 1555 – 1705 1855 – 1940 2155 – 2305 | 15 33 15 33 15 33 15 33 |
| Local Analysis/Forecast | 00, 03, 06, 09, 12, 15, 18, 21 | 0035 – 0100, 0335 – 0400, 0635 – 0700, 0935 – 1000, 1235 – 1300, 1535 – 1600, 1835 – 1900, 2135 – 2200 | 9 |
| Typhoon Ensemble Forecast | 00 06 12 18 | 0305 – 0350 0905 – 0950 1505 – 1550 2105 – 2150 | 132 132 132 132 |
| Ocean Wave Forecast | 00 06 12 18 | 0330 – 0350 0930 – 0950 1530 – 1550, 1840–1850 2130 – 2150 | 84 84 216 84 |
| Storm Surge Forecast | 00 03 06 09 12 15 18 21 | 0200 – 0220 0505 – 0525 0800 – 0820 1105 – 1125 1400 – 1420 1705 – 1725 2000 – 2020 2305 – 2325 | 30 33 30 33 30 33 30 33 |
| One-week Ensemble Forecast | 12 | 1605 – 1835 | 216 |
| One-month Ensemble Forecast | 12 | 1855 – 2015 (every Wednesday and Thursday ) | 816 |
| Seasonal Ensemble Forecasts | 00 | 2205 – 2320 (every 5 days) | (7 months) |

### 4.2	Medium-range forecasting system (4 – 10 days)

### 4.2.1	Data assimilation, objective analysis and initialization

### 4.2.1.1	In operation

(1) Global Analysis (GA)

A four-dimensional variational (4D-Var) data assimilation method is employed in analysis of the atmospheric state for the JMA Global Spectral Model (GSM). The control variables are relative vorticity, unbalanced divergence, unbalanced temperature, unbalanced surface pressure and the natural logarithm of specific humidity. In order to improve computational efficiency, an incremental method is adopted in which the analysis increment is evaluated first at a lower horizontal resolution (TL319) and is then interpolated and added to the first-guess field at the original resolution (TL959).

The JMA Global Analysis (GA) is performed at 00, 06, 12 and 18 UTC. An early analysis with a short cut-off time is performed to prepare initial conditions for operational forecasting, and a cycle analysis with a long cut-off time is performed to maintain the quality of the global data assimilation system.

The specifications of the atmospheric analysis schemes are listed in Table 4.2.1-1.

A reduced Gaussian grid system was implemented for the GA in August 2008.

The global land surface analysis system has been in operation since March 2000 to provide the initial conditions of land surface parameters for the GSM. The system includes daily global snow depth analysis, described in Table 4.2.1-2, to obtain appropriate initial conditions for snow coverage and depth.

Table 4.2.1-1  Specifications of the GA

Analysis scheme

Incremental 4D-Var

Data cut-off time

2.3 hours for early run analysis at 00, 06, 12 and 18 UTC

11.8 hours for cycle run analysis at 00 and 12 UTC

7.8 hours for cycle run analysis at 06 and 18 UTC

First guess

6-hour forecast by the GSM

Grid form, resolution and number of grids

Reduced Gaussian grid, roughly equivalent to 0.1875˚

[ 1920 ( tropic ) – 60 ( polar ) ] x 960

Vertical levels

60 forecast model levels up to 0.1 hPa + surface

Analysis variables

Wind, surface pressure, specific humidity and temperature

Observation (as of 31 December 2012)

SYNOP, SHIP, BUOY, TEMP, PILOT, Wind Profiler, AIREP, AMDAR; atmospheric motion vectors (AMVs) from MTSAT-2, GOES-13, 15, METEOSAT-7, 9; MODIS polar AMVs from Terra and Aqua satellites; ocean surface wind from Metop-A/ASCAT; radiances from NOAA-15, 16, 18, 19/ATOVS, Metop-A/ATOVS, Aqua/AMSU-A, DMSP-F16, 17, 18/SSMIS, TRMM/TMI; clear sky radiances from the water vapor channels (WV-CSRs) of MTSAT-2, GOES-13, 15, Meteosat-7, 9; GPS RO refractivity data from Metop-A /GRAS, COSMIC/IGOR, GRACE-A/blackjack, TerraSAR-X/IGOR, C/NOFS/CORISS.

Assimilation window

6 hours

Table 4.2.1-2  Specifications of snow depth analysis

Methodology	Two-dimensional Optimal Interpolation scheme

Domain and grids	Global, 1˚ × 1˚ equal latitude-longitude grids

First guess	Derived from previous snow depth analysis and USAF/ETAC Global Snow Depth climatology (Foster and Davy 1988)

Data used	SYNOP snow depth data

Frequency	Daily

(2) Typhoon bogussing in the Global Analysis

For typhoon forecasts over the western North Pacific, typhoon bogus data are generated to represent typhoon structures accurately in the initial field of forecast models. These data consist of information on artificial sea-surface pressure and wind data around a typhoon. The structure is axi-asymmetric. First, symmetric bogus data are generated automatically based on the central pressure and 30-kt wind speed radius of the typhoon. Axi-asymmetric bogus data are then generated by retrieving asymmetric components from the first-guess field. Finally, these bogus profiles are used as pseudo-observation data for the GA.

### 4.2.1.2	Research performed in the field

- Updates on recent usage of GNSS RO data

Revisions to the Global Navigation Satellite System (GNSS) Radio Occultation (RO) refractivity data assimilation process were introduced into the operational global NWP system on December 18, 2012. The major changes involved improvement of the observation operators and elimination of bias correction. The accuracy of the previous algorithm for vertical interpolation was limited because latitude dependence was not considered in the calculation of gravitational acceleration. A modified version with calculation revised in this regard reduced biases present in the tropical and polar regions, which allowed elimination of the bias correction procedure. The assimilation of refractivity data from GRACE-A, TerraSAR-X and C/NOFS was started with the implementation of new observation operators. Observation system experiments for the new assimilation configuration incorporating all these revisions showed improved analysis and forecasting of temperature and sea surface pressure, especially for the Southern Hemisphere. (H. Owada)

#### 4.2.2	Model

### 4.2.2.1	In operation

- Global Spectral Model (GSM)

The specifications of the operational Global Spectral Model (GSM1212; TL959L60) are summarized in Table 4.2.2-1.

JMA runs the GSM four times a day (at 00, 06 and 18 UTC with a forecast time of 84 hours and at 12 UTC with a forecast time of 216 hours).

Improvement of the Stratocumulus Parameterization Scheme was introduced in the GSM in December 2012.

Table 4.2.2-1  Specifications of the GSM for 9-day forecasts

Basic equations	Primitive equations

Independent variables	Latitude, longitude, sigma-pressure hybrid coordinates, time

Dependent variables	Surface pressure, winds (zonal, meridional), temperature, specific humidity, cloud water content

Numerical techniques	Spectral (spherical harmonic basis functions) in horizontal, finite differences in vertical

Two-time-level, semi-Lagrangian, semi-implicit time integration scheme

Hydrostatic approximation

Integration domain	Global in horizontal, surface to 0.1 hPa in vertical

Horizontal resolution	Spectral triangular 959 (TL959), reduced Gaussian grid system, roughly equivalent to 0.1875˚ × 0.1875˚ lat-lon

Vertical resolution	60 unevenly spaced hybrid levels

Time step	10 minutes

Orography	GTOPO30 dataset, spectrally truncated and smoothed

Gravity wave drag	Longwave scheme (wavelengths > 100 km) mainly for stratosphere

Shortwave scheme (wavelengths approximately 10 km) only for troposphere

Horizontal diffusion	Linear, fourth-order

Vertical diffusion	Stability (Richardson number) dependent, local formulation

Planetary boundary layer	Mellor and Yamada level-2 turbulence closure scheme

Similarity theory in bulk formulae for surface layer

Treatment of sea surface	Climatological sea surface temperature with daily analyzed anomaly

Climatological sea ice concentration with daily analyzed anomaly

Land surface and soil	Simple Biosphere (SiB) model

Radiation	Two-stream with delta-Eddington approximation for shortwave (hourly)

Table look-up and k-distribution methods for longwave (every three hours)

Convection	Prognostic Arakawa-Schubert cumulus parameterization

Cloud	PDF-based cloud parameterization

### 4.2.2.2	Research performed in the field

- Stratocumulus parameterization scheme improvement

Stratocumulus parameterization is implemented in JMA’s GSM to represent subtropical marine stratocumulus clouds off continental western coasts under the conditions of a strong inversion layer (Kawai and Inoue 2006). However, the scheme is operated even in dry conditions and causes spurious clouds over areas including the Sahara, inland North America and the Sea of Japan. Shimokobe (2012) showed that modification involving the addition of a new relative humidity threshold to the conditions so that the scheme is not operated in dry conditions reduces the incidence of spurious clouds and mitigates low-temperature bias in the lower troposphere with the low-resolution (TL319L60) global data assimilation and forecast system. The effects of the modification (in which a relative humidity threshold of more than 80% is added to the conditions) were investigated in a high-resolution (TL959L60) experiment. This modification suppresses stratocumulus scheme operation and leads to the appropriate elimination of spurious cloud in dry regions. In addition, surface downwelling shortwave radiation is enhanced and the temperature in the lower troposphere increases in areas where stratocumulus scheme operation is suppressed. The model temperatures resemble radiosonde observed values. The RMSE against analysis is also reduced, especially in terms of the temperature in the lower troposphere. These results are consistent with those of the low-resolution experiment conducted by Shimokobe (2012). This modified model has been in operation since December 18, 2012. (T. Furukawa)

- Impact of increasing the number of vertical levels in marine stratocumulus representation

JMA plans to enhance the number of vertical levels of the operational GSM from 60 (L60) to 100 (L100), and investigated the impact of such an increase on the representation of stratocumulus cloud near continental western coasts. To represent marine stratocumulus in the GSM, the cloud fraction is diagnosed as a function of inversion strength when specific conditions are met based on the scheme proposed by Kawai and Inoue (2006). Although this diagnostic scheme successfully produces realistic horizontal distribution for marine stratocumulus near continental western coasts in the L60 GSM, it exhibits two problems: (1) excessive sensitivity to model climatology, and (2) production of unnaturally flat cloud structures. A preliminary experiment showed that increasing the number of model vertical levels substantially improves representation of cloud structures by reducing unnatural cloud flatness caused by this excessive sensitivity. To improve low-level cloud forecasting, JMA is developing a method with a central focus on cloud-top entrainment in its planetary boundary layer (PBL) scheme, which does not use a diagnostic approach to represent marine stratocumulus. Another experiment showed that the L100 GSM without the diagnostic scheme and with the modified PBL scheme forecasts more natural vertical profiles of marine stratocumulus. (H. Yonehara)

#### 4.2.3	Operationally available NWP products

The model output products shown below from the GSM are disseminated through JMA’s radio facsimile broadcast (JMH) service, GTS and the Global Information System Centre (GISC) Tokyo website.

Table 4.2.3-1 List of facsimile charts transmitted via the GTS and JMH

The contour lines (upper-case letters) are: D: dew-point depression (T - Td); E: precipitation; H: geopotential height; J: wave height; O: vertical velocity (ω); P: sea level pressure; T: temperature; W: isotach wind speed; Z: vorticity; δ: anomaly from climatology; μ: average over time.

The other symbols are: a: wind arrows; b: observation plots; d: hatch for dewpoint depression < 3 K; g: arrows for prevailing wave direction; j: jet axis; m: wave period in digits; t: temperature in digits; x: streamlines.

The subscripts in the table indicate: srf: surface; trp: tropopause; digit (ex. 500) pressure in hPa.

The superscripts indicate dissemination channels and time: G: sent to GTS; J: sent to JMH; 12: for 12 UTC only; 5: statistics for pentad sent once per five days for 00 UTC; m: statistics for the month sent monthly for 00 UTC.

| Model | Area | Forecast Time [h] |
| --- | --- | --- |
|  |  | Analysis | 12 | 24 | 36 | 48 72 | 96 120 | 144 168 196 |
| GSM | Asia | HZ500G T850O700 G |  | HZ500GJ T500D700GJ Ta850O700GJ PEsrfGJ |  |  |  |
|  | East Asia | HWtab300GJ HTab500G HTbd700G HTbd850GJ |  | PEsrfG |  | HZ500G Ta850O700GJ12 PEsrfGJ | PEsrfJ12 |  |
|  | Asia |  |  |  |  |  | HZ500G12 PsrfT850G12 |
|  | Asia-Pacific | HWtaj200HtrpG HWta250G |  | HWta250G HWta500G |  |  |  |  |
|  | NW Pacific | x200G x850G |  | x200G x850G |  |  |  |  |
|  | N Hem. | HT500G |  |  |  |  |  |  |
| Ocean | Japan | JbgmsrfGJ |  |  |  |  |  |  |
| Wave | NW Pacific | JbgmsrfGJ | JgmsrfJ |  | JgmsrfJ |  |  |
| JCDAS | N Hem. | μHδH100G5, μHδH500G5, μHδH500Gm, μPδPsrfGm |

Table 4.2.3-2 List of GPV products (GRIB2) distributed via the GISC Website

Symbols: H: geopotential height; U: eastward wind; V: northward wind;

T: temperature; R: relative humidity; O: vertical velocity (ω); Z: vorticity; X: stream function;

Y: velocity potential; P: pressure; Ps: sea-level pressure; E: rainfall; N: total cloud cover; Ch: high cloud cover; Cm: middle cloud cover;  Cl: low cloud cover.

| Model | GSM |
| --- | --- |
| Area and resolution | Whole globe, Region II 0.25° × 0.25° (surface) 0.5° × 0.5° (surface, isobar level) |
| Levels | 10 hPa, 20 hPa, 30 hPa, 50 hPa, 70 hPa, 100 hPa, 150 hPa, 200 hPa, 250 hPa, 300 hPa, 400 hPa, 500 hPa, 600 hPa, 700 hPa, 800 hPa, 850 hPa, 900 hPa, 925 hPa, 950 hPa, 975 hPa, 1,000 hPa, surface |
| Elements | Surface: U, V, T, R, Ps, P, E, N, Ch, Cm, Cl 200 hPa: U, V, T, R, H, O, X, Y 500 hPa: U, V, T, R, H, O, Z 850 hPa: U, V, T, R, H, O, X, Y Other levels: U, V, T, R, H, O |
| Forecast hours | 0 – 84 every 3 hours, 90 – 216 every 6 hours (12 UTC) |
| Initial times | 00 UTC, 06 UTC, 12 UTC, 18 UTC |

Table 4.2.3-3 List of GPV products (GRIB) distributed via the GISC website and the GTS

Symbols: D: dew-point depression; E: precipitation; G: prevailing wave direction; H: geopotential height; J: wave height; M: wave period; O: vertical velocity (ω); P: sea level pressure; R: relative humidity; T: temperature; U: eastward wind; V: northward wind; X: stream function; Y: velocity potential; Z: vorticity;

The prefixes µ and σ represent the average and standard deviations of ensemble prediction results, respectively. The symbols °, *, ¶, §, ‡ and † indicate limitations on forecast hours or initial times as shown in the notes below.

| Model | GSM | GSM | GSM |
| --- | --- | --- | --- |
| Destination | GISC | GTS, GISC | GTS, GISC |
| Area and resolution | Whole globe, 1.25° × 1.25° | 20°S – 60°N, 60°E – 160°W 1.25° × 1.25° | Whole globe, 2.5° × 2.5° |
| Levels and elements | 10 hPa: H, U, V, T 20 hPa: H, U, V, T 30 hPa: H, U, V, T 50 hPa: H, U, V, T 70 hPa: H, U, V, T 100 hPa: H, U, V, T 150 hPa: H, U, V, T 200 hPa: H, U, V, T, X, Y 250 hPa: H, U, V, T 300 hPa: H, U, V, T, R, O 400 hPa: H, U, V, T, R, O 500 hPa: H, U, V, T, R, O, Z 600 hPa: H, U, V, T, R, O 700 hPa: H, U, V, T, R, O 850 hPa: H, U, V, T, R, O, X, Y 925 hPa: H, U, V, T, R, O 1,000 hPa: H, U, V, T, R, O Surface: P, U, V, T, R, E† | 10 hPa: H, U, V, T 20 hPa: H, U, V, T 30 hPa: H, U, V, T 50 hPa: H, U, V, T 70 hPa: H, U, V, T 100 hPa: H, U, V, T 150 hPa: H, U, V, T 200 hPa: H§, U§, V§, T§, X, Y 250 hPa: H, U, V, T 300 hPa: H, U, V, T, D 400 hPa: H, U, V, T, D 500 hPa: H§, U§, V§, T§, D§, Z 700 hPa: H§, U§, V§, T§, D§, O 850 hPa: H§, U§, V§, T§, D§, O, X, Y 925 hPa: H, U, V, T, D, O 1,000 hPa: H, U, V, T, D Surface: P¶, U¶, V¶, T¶, D¶, E¶ | 10 hPa: H*, U*, V*, T* 20 hPa: H*, U*, V*, T* 30 hPa: H°, U°, V°, T° 50 hPa: H°, U°, V°, T° 70 hPa: H°, U°, V°, T° 100 hPa: H°, U°, V°, T° 150 hPa: H*, U*, V*, T* 200 hPa: H, U, V, T 250 hPa: H°, U°, V°, T° 300 hPa: H, U, V, T, D*‡ 400 hPa: H*, U*, V*, T*, D*‡ 500 hPa: H, U, V, T, D*‡ 700 hPa: H, U, V, T, D 850 hPa: H, U, V, T, D 1,000 hPa: H, U*, V*, T*, D*‡ Surface: P, U, V, T, D‡, E† |
| Forecast hours | 0 – 84 every 6 hours and 96 – 192 every 12 hours † Except analysis | 0 – 84 every 6 hours § Additional 96 – 192 every 24 hours for 12 UTC ¶ 0 – 192 every 6 hours for 12 UTC | 0 – 72 every 24 hours and 96 – 192 every 24 hours for 12 UTC ° 0 – 120 for 12 UTC † Except analysis * Analysis only |
| Initial times | 00 UTC, 06 UTC, 12 UTC, 18 UTC | 00 UTC, 06 UTC, 12 UTC, 18 UTC | 00 UTC, 12 UTC ‡ 00 UTC only |

| Model | GSM | Ocean Wave Model |
| --- | --- | --- |
| Destination | GISC | GISC |
| Area and resolution | Whole globe, 2.5° × 2.5° | 75°S – 75°N, 0°E – 358.75°E 1.25° × 1.25° |
| Levels and elements | 250 hPa: µU, µV, σU, σV 500 hPa: µH, σH 850 hPa: µU, µV, µT, σU, σV, σT 1,000 hPa: µH, σH Surface: µP, σP | Surface: J, M, G |
| Forecast hours | 0 – 192 every 12 hours | 0 – 84 every 6 hours, 96 – 192 every 12 hours |
| Initial times | 12 UTC | 00 UTC and 12 UTC |

#### 4.2.4	Operational techniques for application of NWP products

- Forecast guidance

The application techniques for both the medium- and short-range forecasting systems are described in 4.3.4.1 (1).

#### 4.2.5	Ensemble Prediction System (EPS)

### 4.2.5.1	In operation

JMA operates the One-week EPS once a day from a base time at 12 UTC with a forecast range of nine days. The specifications of the EPS are shown in Table 4.2.5-1. It is composed of one control forecast and fifty perturbed forecasts. Initial perturbations are generated using the singular vector (SV) method (Buizza and Palmer 1995). The tangent-linear and adjoint models used for SV computation are lower-resolution versions of those used in the four-dimensional variational data assimilation system for the GSM until October 2011. The moist total energy norm (Ehrendorfer et al. 1999) is employed for the metrics of perturbation growth. The forecast model used in the EPS is a low-resolution version of the GSM (see 4.2.2.1). Accordingly, the dynamical framework and physical processes involved are identical to those of the GSM except for the horizontal resolution. Unperturbed analysis is prepared by interpolating the analyzed field in global analysis. The sea surface temperature analysis value is used as a lower boundary condition and prescribed using the persisting anomaly, which means that the anomalies shown from analysis for the initial time are fixed during the time integration. The sea ice concentration analysis value is also prescribed using the persisting anomaly.

A stochastic physics scheme (Buizza et al. 1999) is used in the One-week EPS in consideration of model uncertainties associated with physical parameterizations.

Table 4.2.5-1 Specifications of the One-week EPS

| Integration | Start of operation | March 2001 |
| --- | --- | --- |
|  | Ensemble size | 51 |
|  | Initial time | 12 UTC |
|  | Forecast range | 9 days |
| EPS model | Model type | GSM |
|  | Horizontal resolution | TL319 reduced Gaussian grid system roughly equivalent to 0.5625° × 0.5625° (55 km) in latitude and longitude |
|  | Vertical resolution (model top) | 60 levels (0.1 hPa) |
|  | Model ensemble method | Stochastic physics scheme |
| Initial perturbation (Initial ensemble generator ¦ Singular vector method) | Inner-model resolution | Spectral triangular truncation 63 (T63), 40 levels |
|  | Norm | Moist total energy |
|  | Targeted area | Northern Hemisphere (30°N – 90°N) | Southern Hemisphere (90°S – 30°S) | Tropics (30°S – 30°N) |
|  | Physical process | *Simplified physics | **Full physics |
|  | Optimization time | 48 hours | 24 hours |
|  | Evolved SV | Used |
|  | Number of perturbations | 25 |

*Simplified physics: initialization, horizontal diffusion, surface fluxes and vertical diffusion

**Full physics:  as per simplified physics with the addition of gravity wave drag, large-scale condensation, long-wave radiation and deep cumulus convection

### 4.2.5.2	Research performed in the field

(1) Spatial resolution enhancement for the One-week EPS forecast model

JMA plans to upgrade the forecast model of the operational One-week EPS. One of the related changes involves increasing the horizontal resolution of the model from the current TL319 to TL479, which is almost equivalent to 40 km in the mid-latitudes, to enhance the expression of severe weather conditions and improve local expression with better resolved lower boundary conditions. Preliminary experiments in which the horizontal resolution was increased to TL479 showed positive impacts in several cases. Operation showed that the TL479 model can express typhoons more sharply than the TL319 model, with deeper central pressure values and increased wind speeds around the center. For other cases, probabilistic forecasting of precipitation is verified against data from observation rain gauges located throughout Japan, and related scores are improved in comparison to those of forecasting with the TL319 model.

(H. Yamaguchi)

### 4.2.5.3	Operationally available EPS products

See 4.2.3.

#### 4.3	Short-range forecasting system (0 – 72 hrs)

#### 4.3.1	Data assimilation, objective analysis and initialization

### 4.3.1.1	In operation

(1) Meso-scale Analysis (MA)

A 4D-Var data assimilation method has been employed since 19 March, 2002, for mesoscale analysis of atmospheric conditions (Meso-scale Analysis, or MA). The MA was replaced with a new 4D-Var called the JNoVA (Honda et al. 2005) in April 2009. The JNoVA is based on JMA’s non-hydrostatic model (JMA-NHM; Saito et al. 2006), which is a current mesoscale forecast model (the Meso-Scale Model, or MSM). The specifications of the MA are detailed in Table 4.3.1-1.

Table 4.3.1-1 Specifications of the MA

4D-Var formulation

Incremental 4D-Var using a nonlinear forward model in the inner step with low resolution

Data cut-off time

50 minutes for analysis at 00, 03, 06, 09, 12, 15, 18 and 21 UTC

Observation (as of 31 December 2012)

SYNOP, SHIP, BUOY, TEMP, PILOT, Wind Profiler, Weather Doppler radar (radial velocity, reflectivity), Weather radar (reflectivity), AIREP, AMDAR; AMVs from MTSAT-2; radiances from NOAA-15, 16, 18, 19/ATOVS, Metop-A/ATOVS, Aqua/AMSU-A, DMSP/SSMIS-F16, 17, 18, TRMM/TMI; WV-CSR of MTSAT-2; radar-raingauge analyzed precipitation; precipitation retrievals from TRMM/TMI, DMSP-F16, 17, 18/SSMIS; total Precipitable Water Vapor from ground-based GPS

First guess

3-hour forecast produced by the MSM

Domain configuration

(Outer step)

Lambert projection; 5 km at 60°N and 30°N, 721 × 577

Grid point (1, 1) is at the northwest corner of the domain.

Grid point (489, 409) is at 140°E, 30°N.

(Inner step)

Lambert projection; 15 km at 60°N and 30°N, 241 × 193

Grid point (1, 1) is at the northwest corner of the domain.

Grid point (163., 137) is at 140°E, 30°N.

Vertical levels

(Outer step) 50 levels up to 22 km (consistent with the forecast model setting)

(Inner step) 40 levels up to 22 km

Analysis variables

Wind, potential temperature, surface pressure and pseudo-relative humidity

Assimilation window

3 hours

- Typhoon bogussing of Meso-scale Analysis

The method employed is the same as that in the GA (see 4.2.1.1 (2)).

(3) Local Analysis (LA)

Local Analysis (LA), which was introduced in August 2012, produces initial conditions for the Local Forecast Model (LFM) at a horizontal resolution of 2 km. For the provision of initial conditions to the high-resolution forecast model targeting small-scale severe weather events, the LA is designed to allow rapid production and frequent updating of analysis at a resolution of 5 km. An analysis cycle with hourly three-dimensional variational (3D-Var) data assimilations is executed each time for the previous three-hour period to incorporate information from newly received observations in each case. High-resolution NWP’s capacity to capture small-scale variations in topography is expected to help a reduction of representativeness errors in surface observation assimilation. In association, the LA also assimilates automated surface station (AMeDAS) data ahead of other operational data assimilation systems at lower resolutions to appropriately reflect the effects of local-scale environments near the surface. The specifications of the LA are detailed in Table 4.3.1-2.

Table 4.3.1-2 Specifications of the LA

Analysis cycle

The three-hour analysis cycle repeats hourly assimilation with 3D-Var and one-hour forecasts.

Data cut-off time

30 minutes for analysis at 00, 03, 06, 09, 12, 15, 18 and 21 UTC

Observation (as of 31 December 2012)

AMeDAS, Wind Profiler, Weather Doppler radar (radial velocity), AIREP, AMDAR and total Precipitable Water Vapor from ground-based GPS

First guess

Initial fields produced by the latest MSM

Domain configuration

Lambert projection; 5 km at 60°N and 30°N, 441 × 501

Grid point (1, 1) is at the northwest corner of the domain.

Grid point (311, 381) is at 140°E, 30°N.

Vertical levels

50 levels up to 22 km

Analysis variables

Wind, potential temperature, surface pressure, pseudo-relative humidity and ground potential temperature

### 4.3.1.2	Research performed in the field

#### 4.3.2	Model

### 4.3.2.1	In operation

(1) Meso-Scale Model (MSM)

JMA has operated the MSM since March 2001. Its main roles are disaster prevention and aviation forecasting. The JMA-NHM was adopted as the MSM in September 2004, and 15- or 33-hour forecasts have been provided every 3 hours, i.e., 8 times a day, since May 2007. The specifications of the MSM are listed in Table 4.3.2-1.

Table 4.3.2-1 Specifications of the MSM

Basic equations	Fully compressible non-hydrostatic equations

Independent variables	Latitude, longitude, terrain-following height coordinates, time

Dependent variables	Momentum components in three dimensions, potential temperature, pressure, mixing ratios of water vapor, cloud water, cloud ice, rain, snow and graupel, number concentration of cloud ice

Numerical techniques	Finite discretization on Arakawa-C-type staggered coordinates, horizontally explicit and vertically implicit time integration scheme, fourth-order horizontal finite differencing in flux form with modified advection treatment for monotonicity

Projection and grid size	Lambert projection, 5 km at 60°N and 30°N

Integration domain	Japan, 721 × 577 grid points

Vertical levels	50 (surface to 21. 8 km)

Forecast times	15 hours from 00, 06, 12 and 18 UTC

33 hours from 03, 09, 15 and 21 UTC

Initial fields　　　　　　　　4D-Var analysis with mixing ratios of cloud water, cloud ice, rain, snow and graupel derived from preceding forecasts considering consistency with the analysis field of relative humidity

The MSM runs three hours before the initial time for spin-up.

Lateral boundary	00–36 hour forecasts by the GSM initialized at 00/06/12/18 UTC for (03, 06)/(09, 12)/(15, 18)/(21, 00) UTC forecasts

Orography	Mean orography smoothed to eliminate shortest-wave components

Horizontal diffusion	Linear, fourth-order Laplacian + nonlinear damper

Targeted moisture diffusion applied to grid points where excessive updrafts appear

Convection                             Kain-Fritsch convection scheme

Cloud	Three-ice bulk cloud microphysics

Lagrangian treatment for rain and graupel precipitation

Radiation (short wave)	Two-stream with delta-Eddington approximation (every 15 minutes)

Radiation (long wave)	Table look-up and k-distribution methods (every 15 minutes)

Cloudiness	Cloud water and cloud cover diagnosed using a partial condensation scheme

Gravity wave drag	No parameterization scheme included

PBL	Improved Mellor-Yamada Level 3 scheme

Similarity theory adopted for surface boundary layer

Land surface	Ground temperature predicted using a four-layer ground model

Evaporability predicted initialized by climatological values depending on location and season.

Surface state	Observed SST (fixed during time integration) and sea-ice distribution

Climatological values of evaporability, roughness length and albedo

Snow cover over Japan analyzed daily

(2) Local Forecast Model (LFM)

Making use of the new powerful supercomputer system installed in June 2012, operation of a forecast model called the LFM with an even higher resolution was launched in August 2012 along with LA. The new model has 2-km horizontal grid spacing and 60 vertical layers up to a height of approximately 20.2 km above the surface, and is designed to produce more detailed forecasts with emphasis on predicting localized and short-lived severe events. The LFM is specifically intended to provide very short-range forecasts for the period of nine hours ahead and other periods, and to allow rapid and frequent forecast updates based on initial conditions with the latest observations assimilated by the LA. The specifications of the LFM are listed in Table 4.3.2-2.

Table 4.3.2-2 Specifications of the LFM

Basic equations	Fully compressible non-hydrostatic equations

Independent variables	Latitude, longitude, terrain-following height coordinates, time

Dependent variables	Momentum components in three dimensions, potential temperature, pressure, mixing ratios of water vapor, cloud water, cloud ice, rain, snow and graupel, number concentration of cloud ice

Numerical techniques	Finite discretization on Arakawa-C-type staggered coordinates, horizontally explicit and vertically implicit time integration scheme, fourth-order horizontal finite differencing in flux form with modified advection treatment for monotonicity

Projection and grid size	Lambert projection, 2 km at 60°N and 30°N

Integration domain	Eastern part of Japan, 551 × 801 grid points

Vertical levels	60 (surface to 20. 2 km)

Forecast times	9 hours from 00, 03, 06, 09, 12, 15, 18 and 21 UTC

Initial fields	The LA produces initial conditions through the three-hour analysis cycle based on hourly assimilation with 3D-Var and one-hour forecasts.

Lateral boundary	00–12 hour forecasts produced by the latest MSM

Orography	Mean orography smoothed to eliminate shortest-wave components

Horizontal diffusion	Linear, fourth-order Laplacian + nonlinear damper

Targeted moisture diffusion applied to grid points where excessive updrafts appear

Convection                             No parameterization scheme included

Cloud	Three-ice bulk cloud microphysics

Lagrangian treatment for rain and graupel precipitation

Radiation (short wave)	Two-stream with delta-Eddington approximation (every 15 minutes)

Radiation (long wave)	Table look-up and k-distribution methods (every 15 minutes)

Cloudiness	Cloud water and cloud cover diagnosed using a partial condensation scheme

Gravity wave drag	No parameterization scheme included

PBL	Improved Mellor-Yamada Level 3 scheme

Similarity theory adopted for surface boundary layer

Land surface	Ground temperature predicted using a four-layer ground model

Evaporability predicted initialized by climatological values depending on location and season.

Surface state	Observed SST (fixed during time integration) and sea-ice distribution

Climatological values of evaporability, roughness length and albedo

Snow cover over Japan analyzed daily

### 4.3.2.2	Research performed in the field

### Operationally available NWP products

Short- and medium-range forecast products are described in 4.2.3.

#### 4.3.4    Operational techniques for application of NWP products

### 4.3.4.1	In operation

- Forecast guidance

Forecast guidance is utilized to issue warnings, advisories, information and weather forecasts. Four operational techniques are routinely used to derive guidance from NWP model output. The first involves the use of the Kalman filter, the second involves an artificial neural network, the third is based on logistic regression, and the last is a diagnostic method. These techniques are applied to grid-point values from the GSM (20-km grid squares, 0 – 84 hour forecasts) and the MSM (5-km grid squares, 0 – 33 or 0 – 15 hour forecasts) in order to reduce systematic forecast errors and enable the extraction of useful information such as probability data and categorical/diagnostic values.

The Kalman filter technique is used to derive data on the probability of precipitation, average precipitation amounts, maximum/minimum temperatures, time-series temperature, maximum wind speed/direction, maximum instantaneous wind speed/direction, time-series wind speed/direction, average and minimum visibility, and the probability of minimum visibility values being less than 5,000 or 1,600 meters. New gust speed and direction values have been used since November 2012.

The artificial neural network technique is used to derive data on sunshine durations, minimum humidity, cloud amounts, cloud base heights and point-type maximum snowfall depths. The maximum precipitation guidance is derived by multiplying the average precipitation amount for each grid square by an optimum ratio derived using the artificial neural network. New probability of gusting (PoG) values have been used since November 2012.

The logistic regression technique is used to derive data on the probability of thunderstorms and particular cloud base heights. The Lagged Average Forecast (LAF) method has been applied to determine the probability of thunderstorms since May 2008. The logistic regression technique is also applied to turbulence index values for area forecasts. The turbulence index (also known as the TBindex (Kudo 2011)) is constructed from a number of other turbulence indices used to comprehensively predict various kinds of turbulence. It has been in operation since February 2010, and was upgraded in June 2010.

The diagnostic method is used to derive data on grid-type maximum snowfall depths, weather categories and visibility distribution guidance, which is determined using extinction coefficients for raindrops, snowfall, cloud water and humidity. Visibility distribution guidance has been provided since March 2011. The diagnostic method is also applied to the CB cloud amount, the CB top height and the aircraft icing index for area forecasts. The CB cloud amount and top height are derived based on the technique to discriminate deep convection used in the Kain-Fritsch convective scheme, in which cloud top and base heights are estimated from the surrounding temperature, humidity and updraft conditions. CB cloud forecasting has been performed since 2007, and was upgraded in 2009. The icing index is constructed by multiplying a distribution function of icing for temperature and dewpoint depression based on the results of statistical research performed for the area around Japan. To support marine warnings, new visibility distribution guidance derived from the GSM has been used since November 2012.

(2) Hourly Analysis

JMA Hourly Analysis involves three-dimensional evaluation of temperature and wind fields with a grid spacing of 5 km to provide real-time monitoring of weather conditions. The latest MSM forecast is used as the first guess, and observational information is added through assimilation. The three-dimensional variational data assimilation method is adopted as the analysis technique. The hourly product is made within 30 minutes of the end of each hour, and is provided to operational forecasters and aviation users. The specifications of the Hourly Analysis schemes are listed in Table 4.3.4-1.

Table 4.3.4-1  Specifications of the Hourly Analysis

Analysis scheme

3D-Var

Data cut-off time

20 minutes

First guess

2, 3 or 4-hour forecast by the MSM

Domain configuration

Lambert projection, 5 km at 60°N and 30°N, 721 × 577 grid points

Grid point (1, 1) is at the northwestern corner of the domain.

Grid point (489, 409) is at 140°E, 30°N.

Vertical levels

50 forecast model levels

Analysis variables

Wind, temperature, surface wind and surface temperature

Observation (as of 31 December, 2012)

AMeDAS, Wind Profiler, Weather Doppler radar (radial velocity), AIREP, AMDAR, and AMVs from MTSAT-2

Post-processing

Surface filtering (followed by adjustment of the increment within the PBL)

### Research performed in the field

(1) Forecast guidance

Maximum 24-hour cumulative precipitation guidance has also been improved. To derive the ratio of average precipitation to maximum precipitation, the multiple linear regression method is used in place of the artificial neural network.

Maximum wind speed/direction and time-series wind speed/direction guidance have also been improved. To reduce wind speed bias depending on the wind direction, forecast equations are adopted for each direction.

Maximum wind speed and direction guidance have been developed to support wind information for one-week forecasts. The Kalman filter and the frequency bias correction techniques are applied to each ensemble member of the one-week EPS.

### 4.4	Nowcasting and Very-short-range Forecasting systems (0 – 6 hrs)

Since 1988, JMA has routinely operated a fully automated system of precipitation analysis and very short-range forecasting to monitor and forecast local severe weather conditions. In addition to these, the Agency has issued Precipitation Nowcasts since June 2004, Thunder Nowcasts since May 2010 and Hazardous Wind Potential Nowcasts since May 2010.

The system is used to output the five products outlined below.

(1) Radar/Raingauge-Analyzed Precipitation (hereafter R/A)*, which shows one-hour accumulated precipitation based on observation by radars calibrated half-hourly using raingauge measurements from JMA’s Automated Meteorological Data Acquisition System (hereafter AMeDAS) and other available data, such as those from rain gauges operated by local governments.

(2) Very-Short-Range Forecasts of precipitation (hereafter VSRFs), which are forecasts of one-hour accumulated precipitation based on extrapolation and prediction by the MSM (see 4.3). The forecast time of VSRFs is from one to six hours.

(3) Precipitation Nowcasts, which are forecasts of 10-minute accumulated precipitation and 5-minute-interval precipitation intensity based on extrapolation. The forecast time of Precipitation Nowcasts is up to 60 minutes.

(4) Thunder Nowcasts, which are forecasts of thunder and lightning activity based on lightning detection network system observation. The forecast time of Thunder Nowcasts is up to 60 minutes.

(5) Hazardous Wind Potential Nowcasts, which are forecasts of the probability of hazardous wind conditions such as tornadoes. The forecast time of Hazardous Wind Potential Nowcasts is up to 60 minutes.

*Referred to before 15 November, 2006, as Radar-AMeDAS precipitation.

### 4.4.1	Nowcasting system (0 – 1 hrs)

### 4.4.1.1	In operation

Precipitation Nowcasts predict 10-minute accumulated precipitation and 5-minute-interval precipitation intensity by extrapolation up to one hour ahead. Initial precipitation intensity distribution is derived from radar data obtained at 5-minute intervals, and is calibrated by raingauge observation. Using estimated movement vectors, these forecasts predict precipitation distribution by extrapolation within three minutes of radar observation.

Precipitation Nowcasts are provided to local weather offices and to the public. They are utilized to understand precipitation transition and to support disaster prevention activities.

Table 4.4.1-1 Specifications of the Precipitation Nowcast model

Forecast process	Non-Linear motion/intensity extrapolation
including the lifecycle estimation of storm cells and orographic rainfall trend prediction

Movement vector	Precipitation system and/or cell motion estimated using the cross-correlation pattern matching and discrete interpolation

Time step	5 minutes

Grid form	Cylindrical equidistant projection

Resolution	Approx. 1 km

Number of grids	2,560 × 3,360

Initial	Calibrated radar echo intensities

Forecast time	60 minutes ahead, updated every 5 minutes

Thunder Nowcasts predict thunder and lightning activity up to one hour ahead. Initial activity distribution is derived from lightning detection network system observations obtained at 10-minute intervals. Using estimated movement vectors, these forecasts predict activity distribution by extrapolation within three minutes of radar observation. Thunder Nowcasts are provided to local weather offices and to the public. They are utilized to understand thundercloud transfer and to advise people to stay in or go to safe places in order to avoid lightning strikes.

Table 4.4.1-2 Specifications of Thunder Nowcast model

Forecast process	Extrapolation

Movement vector	As per the Precipitation Nowcast system

Grid form	Cylindrical equidistant projection

Resolution	Approx. 1 km

Number of grids	2,560 × 3,360

Initial	4-level activity of thunder and lightning based on lightning detection network system observation

Forecast time	60 minutes ahead, updated every 10 minutes

Hazardous Wind Potential Nowcasts predict the probability of hazardous wind conditions such as tornadoes up to one hour ahead. Initial probability distribution is established using radar measurements including Doppler radar data obtained at 10-minute intervals and severe weather parameters calculated from Numerical Weather Prediction. Using estimated movement vectors, these forecasts predict probability distribution by extrapolation within three minutes of radar observation. Hazardous Wind Potential Nowcasts are provided to local weather offices and to the public. They are utilized to understand potential hazardous wind transfer and to call attention to hazardous wind conditions.

Table 4.4.1-3 Hazardous Wind Potential Nowcast model

Forecast process	Extrapolation

Movement vector	As per the Precipitation Nowcast system

Grid form	Cylindrical equidistant projection

Resolution	Approx. 10 km

Number of grids	256 × 336

Initial	2-level presumed hazardous wind probabilities

Forecast time	60 minutes ahead, updated every 10 minutes

### 4.4.1.2	Research performed in the field

Research and Application of Precipitation Nowcasts

(1)  Echo Motion Detection and Prediction

A trade-off study was performed to establish an optimally balanced approach for detecting radar echo motion.  A newly developed multi-scale tracking mechanism working in both the spatial and temporal domains was selected for the operational prediction system.  A non-linear echo motion prediction technique was also developed to provide realistic trajectories for echo patterns.

(2)  Echo Intensity Trend Measurement and Prediction

Echo tracking with greater levels of accuracy and efficiency has boosted research activities related to characterization of the precipitation lifecycle, especially in the area of orographic rainfall.  A technique for detecting orographic precipitation using a customized two-dimensional digital filter that separates drifting and virtually settled echo patterns was introduced.  Orographic precipitation is predicted on an extrapolative basis not only from echo intensity trends but also from increments in observed values of surface temperature and humidity.

(3)  Storm Lifecycle Prediction

The new tracking technique also enhanced research aimed at characterizing intensity profiles over the entire lifecycle of small-scale storms, and equations to estimate how long a storm cell will remain have been developed using a statistical approach.  This lifecycle prediction method is expected to expand the application of precipitation nowcasts to areas such as disaster management relating to flash floods caused by short-term heavy rainfall in urban areas.

(4)  Operational Application

The multi-scale tracking mechanism has been operated since March 2011, and the operational software was upgraded in December 2011 to allow orographic rainfall prediction using the technique described below.  Storm lifecycle prediction was operationalized in May 2012.

### 4.4.2	Models for Very-short-range Forecasting Systems (1 – 6 hrs)

### 4.4.2.1	In operation

(1) Radar/Raingauge-Analyzed Precipitation (R/A)

Radar/Raingauge-Analyzed Precipitation (R/A) is a type of precipitation distribution analysis with a resolution of 1 km, and is derived on a half-hourly basis. Radar data and raingauge precipitation data are used to make R/A. The radar data consist of intensity data from 46 weather radars operated by JMA and the Ministry of Land, Infrastructure, Transport and Tourism (MLIT), and the raingauge precipitation data are collected from more than 10,000 raingauges operated by JMA, MLIT and local governments.

After collecting this information, the radar intensity data are accumulated to create one-hour accumulated radar precipitation data. Each set of this data is calibrated with the one-hour accumulated raingauge precipitation data. R/A is a composite of all calibrated and accumulated radar precipitation data. The initial field for extrapolation forecasting is the composite of the calibrated radar intensity data.

(2) Very-Short-Range Forecasts of precipitation (VSRFs)

The extrapolation forecast and precipitation forecast from the MSM (see 4.3.2.1 (1)) are merged into the Very-Short-Range Forecast of precipitation (VSRFs). The merging weight of the MSM forecast is nearly zero for a one-hour forecast, and is gradually increased with forecast time to a value determined from the relative skill of MSM forecasts.

Table 4.4.2-1 Specifications of extrapolation model

Forecast process	Extrapolation

Physical process	Enhancement and dissipation

Movement vector	Precipitation system movement evaluated using the cross-correlation method

Time step	2 – 5 minutes

Grid form	Oblique conformal secant conical projection

Resolution	1 km

Number of grids	1,600 × 3,600

Initial	Calibrated radar echo intensities

Forecast time	Up to six hours from each initial time (every 30 minutes = 48 times/day)

VSRFs products are issued about 20 minutes after radar observation to support local weather offices that issue weather warnings for heavy precipitation, and are used for forecast calculation of applied products such as the Soil Water Index and the R/A Runoff Index.

### 4.4.2.2	Research performed in the field

In response to the fact that the LFM (see 4.3.2.1) will be operated from 2013, JMA is developing a new usage of the Numerical Weather Prediction in the extrapolation and the merging methods, focusing on the LFM.

### 4.5	Specialized numerical prediction

### 4.5.1	Assimilation of specific data, analysis and initialization (where applicable)

### 4.5.1.1	In operation

(1) Global Ocean Data Assimilation System

The Global Ocean Data Assimilation System (named MOVE/MRI.COM-G; Usui et al. 2006) developed by the Meteorological Research Institute of JMA is in operation at JMA. Its specifications are shown in Table 4.5.1-1.

| Table 4.5.1-1 Specifications of the Global Ocean Data Assimilation System |
| --- |
| Basic equations | Primitive equations with free surface |
| Independent variables | Lat-lon coordinates and σ-z hybrid vertical coordinates |
| Dependent variables | u, v, T, S, SSH |
| Numerical technique | Finite difference both in the horizontal and in the vertical |
| Grid size | 1˚ (longitude) × 1˚ (latitude, smoothly decreasing to 0.3˚ toward the equator) grids |
| Vertical levels | 50 levels |
| Integration domain | Global oceans from 75°N to 75°S |
| Forcing data | Heat, water and momentum fluxes are calculated using data from the JMA Climate Data Assimilation System (JCDAS). |
| Observational data | Sea-surface and subsurface temperature and salinity and sea surface height |
| Operational runs | Two kinds of run (final and early) with cut-off times of 33 days and 2 day, respectively, for ocean observation data |

Outputs of MOVE/MRI.COM-G are used to monitor and diagnose tropical ocean status. Some figures based on MOVE/MRI.COM-G output are published in JMA’s Monthly Highlights on Climate System and provided through the Tokyo Climate Center (TCC) website (http://ds.data.jma.go.jp/tcc/tcc/index.html). The data are also used as oceanic initial conditions for JMA’s coupled ocean-atmosphere model (JMA/MRI-CGCM).

(2) High-resolution sea surface temperature analysis for global oceans

High-resolution daily sea surface temperatures (SSTs) in global oceans are objectively analyzed on a 1/4˚ × 1/4˚ grid for ocean information services and to provide boundary conditions for atmospheric short-range prediction models and North Pacific Ocean models. SSTs obtained from AVHRRs on MetOp and the NOAA series of polar-orbiting meteorological satellites are used together with in-situ SST observations. The analysis data are available on the NEAR-GOOS Regional Real Time Data Base (http://goos.kishou.go.jp).

### 4.5.2	Specific models

### 4.5.2.1	In operation

- Typhoon Ensemble Prediction System (Typhoon EPS)

JMA routinely operates the Typhoon EPS to support the issuance of five-day tropical cyclone (TC) track forecasts. This EPS consists of 11 forecasts run up to four times a day from base times at 00, 06, 12 and 18 UTC with a forecast range of 132 hours. The system is operated when any of the following conditions is satisfied:

• A TC of tropical storm (TS*) intensity or higher is present in the RSMC Tokyo - Typhoon Center’s

area of responsibility (0°–60°N, 100°E–180°).

• A TC is expected to reach TS intensity or higher in the area within the next 24 hours.

• A TC of TS intensity or higher is expected to move into the area within the next 24 hours.

* A TS is defined as a TC with maximum sustained wind speeds of 34 knots or more and less than 48 knots.

The specifications of the Typhoon EPS are shown in Table 4.5.2-1. A low-resolution version of the GSM is used in the Typhoon EPS as well as the One-week EPS (see 4.2.5.1). Accordingly, the dynamical framework and physical processes involved are identical to those of the GSM except for the horizontal resolution. The unperturbed analysis is prepared by interpolating the analyzed field in the GA. The sea surface temperature analysis value is used as a lower boundary condition and prescribed using the persisting anomaly, which means that the anomalies shown by analysis for the initial time are fixed during the time integration. The sea ice concentration analysis value is also prescribed using the persisting anomaly. As with the One-week EPS, initial perturbations are also generated using the SV method, but the configurations are different.

- Table 4.5.2-1 Specifications of the Typhoon EPS

| Integration | Start of operation | February 2008 |
| --- | --- | --- |
|  | Ensemble size | 11 |
|  | Initial time | 00, 06, 12 and 18 UTC |
|  | Forecast range | 132 hours |
| EPS model | Model type | GSM |
|  | Horizontal resolution | TL319 reduced Gaussian grid system roughly equivalent to 0.5625° × 0.5625° (55 km) in latitude and longitude |
|  | Vertical resolution (model top) | 60 levels (0.1 hPa) |
|  | Model ensemble method | Stochastic physics scheme |
| Initial perturbation (Initial ensemble generator ¦ Singular vector method) | Inner-model resolution | Spectral triangular truncation 63 (T63), 40 levels |
|  | Norm | Moist total energy |
|  | Targeted area | Northwestern Pacific (20°N – 60°N, 100°E – 180°) | Vicinities of up to 3 TCs in the Typhoon Centre’s area of responsibility |
|  | Physical process | Simplified physics | Full physics |
|  | Optimization time | 24 hours |
|  | Evolved SV | Not used |
|  | Number of perturbations | 10 | 10 for each TC |

- Environmental emergency response system

JMA acts as a Regional Specialized Meteorological Center (RSMC) for Environmental Emergency Response in WMO Regional Association (RA) II, and is responsible for the preparation and dissemination of transport model products on exposure and surface contamination involving accidentally released radioactive materials. An operational tracer transport model is run at the request of National Meteorological Services in RA II and the International Atomic Energy Agency (IAEA) to offer RSMC support for environmental emergency response.

A Lagrangian method is adopted for the transport model, and large numbers of tracers are released at certain times and locations in line with pollutant emission information provided as part of related requests. Effects on three-dimensional advection and horizontal/vertical diffusion, dry and wet deposition and radioactive decay are computed from three-hourly outputs of the high-resolution global model (TL959L60). The standard products of the RSMC involve maps on trajectories, time-integrated low-level concentrations and total deposition up to 72 hours ahead.

As part of the CTBTO-WMO Backtracking Response System, JMA is responsible for providing atmospheric backtracking products to the Comprehensive Nuclear-Test-Ban Treaty Organization (CTBTO) in its role as a Regional Specialized Meteorological Center. The Agency developed an atmospheric backtracking transport model and built up a response system that receives e-mail notifications from CTBTO, executes backtracking calculations and provides the resulting products in line with the procedure defined in WMO no. 485. JMA began operation of the backtracking system in December 2009. When JMA’s new super-computer system was adopted, the operational backtracking system was expanded so that 50-day backtracking (as requested by CTBTO at a 2011 meeting of the Coordination Group for Nuclear Emergency Response Activities (CG-NERA)) can be provided on an operational basis.

- Ocean-wave forecasting models

JMA operates three numerical wave models: the Global Wave Model (GWM), the Coastal Wave Model (CWM) and the Shallow-water Wave Model (SWM), all of which are classified as third-generation wave models. The GWM and the CWM are based on the MRI-III, and were developed at JMA’s Meteorological Research Institute and updated to create new versions in May 2007. The models’ specifications are given in Table 4.5.2.1 (3)-1.

An assimilation scheme developed by JMA for wave models was incorporated into the GWM and the CWM in October 2012.

The SWM is based on the WAM, which was modified at the National Institute for Land and Infrastructure Management of MLIT and put into operation under a cooperative framework with MLIT’s Water and Disaster Management Bureau. The target area is limited, and is currently being expanded. The models’ specifications are given in Table 4.5.2.1 (3)-2.

Table 4.5.2.1 (3)-1  Specifications of the ocean-wave prediction model

| Model name | Global Wave Model | Coastal Wave Model |
| --- | --- | --- |
| Model type | Spectral model (third-generation wave model) |
| Spectral components | 900 (25 frequencies from 0.0375 to 0.3 Hz and 36 directions) |
| Grid form | Equal latitude-longitude grid on spherical coordinates |
| Grid size | 0.5° × 0.5° (720 × 301) | 0.05° × 0.05° (601 × 601) |
| Integration domain | Global 75°N – 75°S | Coastal Sea of Japan 50°N – 20°N, 120°E – 150°E |
| Time step | Advection term: 10 minutes Source term: 30 minutes | Advection term: 1 minute Source term: 3 minutes |
| Forecast time | 84 hours from 00, 06 and 18 UTC 264 hours from 12 UTC | 84 hours from 00, 06, 12 and 18 UTC |
| Boundary conditions | - | Global Wave Model |
| Initial conditions | Hindcast |
| Wind field | Global Spectral Model (GSM) |
|  | Bogus gradient winds (for typhoons in the western North Pacific) |

Table 4.5.2.1 (3)-2 Specifications of the ocean-wave prediction model

| Model name | Shallow-water Wave Model |
| --- | --- |
| Model type | Spectral model (third-generation wave model) |
| Spectral components | 1,260 (35 frequencies from 0.0418 to 1.1 Hz and 36 directions) |
| Grid form | Equal latitude-longitude grid on spherical coordinates |
| Grid resolution | 1’ × 1’ |
| Areas | Domain name | Grid size | Integration domain |
|  | Tokyo Bay | 37 × 43 | 35.05°N – 35.75°N 139.55°E – 140.15°E |
|  | Ise Bay | 61 × 43 | 34.35°N – 35.05°N 136.45°E – 137.45°E |
|  | Harima-Nada Osaka Bay | 79 × 49 | 34.05°N – 34.85°N 134.15°E – 135.45°E |
|  | Ariake Sea | 43 × 49 | 32.45°N – 33.25°N 130.05°E – 130.75°E |
|  | Off Niigata | 55 × 37 | 37.80°N – 38.40°N 138.35°E – 139.25°E |
|  | Sendai Bay | 37 × 43 | 37.75°N – 38.45°N 140.90°E – 141.50°E |
|  | Off Tomakomai | 121 × 43 | 42.00°N – 42.70°N 141.00°E – 143.00°E |
|  | Suo-Nada Iyo-Nada Aki-Nada | 109 × 67 | 33.30°N – 34.40°N 131.00°E – 132.80°E |
| Time step | Advection term: 1 minute Source term: 1 minute |
| Forecast time | 33 hours from 03, 09, 15 and 21 UTC |
| Boundary conditions | Coastal Wave Model |
| Initial conditions | Hindcast |
| Wind field | Meso-Scale Model (MSM) |
|  | Bogus gradient winds (for typhoons in the western North Pacific) |

Wave model products are adopted by various domestic users (such as governmental organizations and private weather companies) via the Japan Meteorological Business Support Center (JMBSC), whereas SWM products are only used within JMA and MLIT’s Regional Development Bureaus. GWM products are available within JMA’s WMO Information System for National Meteorological and Hydrological Services (NMHSs), and are also disseminated to several countries via GTS.

- Storm-surge model

JMA operates a numerical storm surge model to predict storm surges in coastal areas of Japan using sea-surface wind and pressure fields inferred by the MSM. In the case of tropical cyclones (TCs), storm surges for six scenarios are predicted in consideration of TC track forecast errors. In addition to the MSM, TC bogus data corresponding to five tracks (center, faster, slower and rightmost/leftmost of the TC track forecast) are used for each scenario. Data on astronomical tides are required for the prediction of storm tides (i.e., the sum of storm surges and astronomical tides). To predict the spatial distribution of storm tides, a data assimilation method for astronomical tides was developed and put into operation in May 2010. The model’s specifications are given in Table 4.5.2.1 (4)-1.

Table 4.5.2.1 (4)-1 Specifications of the numerical storm-surge model

| Basic equations | Two-dimensional shallow-water equations |
| --- | --- |
| Numerical technique | Explicit finite difference method |
| Integration domain | Coastal areas of Japan (117.4°E – 150.0°E, 20.0°N – 50.0°N) |
| Grid size | Adaptive Mesh Refinement (AMR) method 45 seconds (longitude gradually doubling to 12 minutes toward offshore areas) × 30 seconds (latitude gradually doubling to 8 minutes toward offshore areas) |
| Boundary conditions | Modified radiation condition at open boundaries and zero normal flows at coastal boundaries |
| Forcing data | Meso-Scale Model (MSM) |
|  | Bogus data for TCs around Japan |
| Astronomical tides | Ocean tide model (Egbert and Erofeeva 2002) and data assimilation of harmonic constants at tide stations using the ensemble transform Kalman filter (ETKF) |

JMA developed a storm surge model for the Asian region in 2010 in collaboration with Typhoon Committee Members providing tidal observation and sea bathymetry data. Since 1 June, 2011, horizontal maps of predicted storm surges have been published on JMA’s Numerical Typhoon Prediction website. Since 5 June, 2012, three time-series charts of predicted storm surges have been published. The storm surge model uses the GSM for meteorological forcing. In the case of TCs, storm surges are predicted up to 72 hours ahead using a simple parametric TC track (center) in addition to the GSM. The model’s specifications are given in Table 4.5.2.1 (4)-2. JMA plans to extend the forecast region and add seven stations for time-series charts. The extended region is 95 – 160 degrees in longitude and 0 – 46 degrees in latitude. JMA also plans to add more stations for time-series charts in response to Member requests.

Table 4.5.2.1 (4)-2 Specifications of the Numerical storm-surge model (Asian region)

| Basic equations | Two-dimensional linear shallow-water equations |
| --- | --- |
| Numerical technique | Explicit finite difference method |
| Integration domain | Coastal areas of Asia (98.0°E – 137.0°E, 0.0°N – 42.0°N) |
| Grid size | 2 minutes × 2 minutes |
| Boundary conditions | Modified radiation condition at open boundaries and zero normal flows at coastal boundaries |
| Forcing data | Global Spectral Model (GSM) |
|  | Bogus data for TCs (center) |
| Astronomical tides | Not included |

- Ocean data assimilation system for the North Pacific Ocean

An ocean data assimilation system for the North Pacific is operated to represent ocean characteristics such as the movement of the Kuroshio current in the mid/high latitudes of the North Pacific with the specifications shown below. Data on ocean currents and water temperatures at a depth of 100 m (products of this system) are available on the NEAR-GOOS Regional Real Time Database (http://goos.kishou.go.jp).

| Table 4.5.2.1 (5)-1 Specifications of the ocean data assimilation system for the North Pacific Ocean |
| --- |
| Basic equations | Primitive equations with free surface |
| Independent variables | Lat-lon coordinates and σ-z hybrid vertical coordinates |
| Dependent variables | u, v, T, S, SSH |
| Numerical technique | Finite difference both in the horizontal and in the vertical with a three-dimensional variational (3D-Var) data assimilation system |
| Grid size | (1) Western North Pacific model 0.1° longitude × 0.1° latitude in the seas off Japan, decreasing to 0.166° toward the northern and eastern boundaries with the North Pacific model (2) North Pacific model 0.5° longitude × 0.5° latitude |
| Vertical levels | 54 |
| Integration domain | (1) Western North Pacific model From 15°N to 65°N between 115°E and 160°W (2) North Pacific model From 15°S to 65°N between 100°E and 75°W |
| Forcing data | Heat, water and momentum flux driven from the JMA Climate Data Assimilation System (JCDAS) and from a low-resolution version (TL159) of the operational GSM |
| Observational data | Sea-surface and subsurface temperature/salinity, sea surface height, sea ice concentration |
| Operational runs | 10-day assimilation and 30-day prediction are implemented every day |

- Sea-ice forecasting model

JMA issues information on the state of sea ice in the seas off Japan. A numerical sea-ice model has been run to predict sea ice distribution and thickness in the seas off Hokkaido (mainly in the southern part of the Sea of Okhotsk) twice a week in winter since December 1990 (see Table 4.5.2.1 (6)-1).

Table 4.5.2.1 (6)-1 Specifications of the numerical sea-ice prediction model

| Dynamical processes | Viscous-plastic model (MMD/JMA 1993) – considering wind and seawater stress on sea ice, Coriolis force, force from the sea surface gradient and internal force |
| --- | --- |
| Physical processes | Heat exchange between sea ice, the atmosphere and seawater |
| Dependent variables | Concentration and thickness |
| Grid size and time step | 12.5 km and 6 hours |
| Integration domain | Seas around Hokkaido |
| Initial time and forecast time | 168 hours from 00 UTC (twice a week) |
| Initial condition | Concentration analysis derived from MTSAT and NOAA satellite imagery and thickness estimated by hindcasting |

Grid-point values of the numerical sea-ice model are disseminated to domestic users. Sea ice conditions for the coming seven days as predicted by the model are broadcast by radio facsimile (JMH) twice a week.

- Marine pollution transport model

JMA operates the numerical marine-pollution transport model in the event of marine-pollution accidents. Its specifications are shown in Table 4.5.2.1 (7)-1. The ocean currents used for the model’s input data are derived from the results of the ocean data assimilation system for the North Pacific Ocean.

Table 4.5.2.1 (7)-1 Specifications of the marine pollution transport model

| Area | Western North Pacific |
| --- | --- |
| Grid size | 2 – 30 km (variable) |
| Model type | 3-dimensional parcel model |
| Processes | Advection caused by ocean currents, sea surface winds and ocean waves Turbulent diffusion Chemical processes (evaporation, emulsification) |

- Kosa prediction model

JMA has operated a Kosa (sand-dust storm) prediction model to forecast Kosa distribution since January 2004. The model is directly coupled with a low-resolution version of the GSM, and makes use of several GSM parameters without temporal or spatial interpolation (Tanaka et al. 2003). The model’s specifications are given in Table 4.5.2.1 (8)-1.

The 3D semi-Lagrangian transport scheme was updated in February 2010 to enable appropriate handling of dust advection.

Table 4.5.2.1 (8)-1 Specifications of the Kosa prediction model

| Basic equations | Eulerian model coupled with the Global Spectral Model |
| --- | --- |
| Numerical technique | 3D semi-Lagrangian transport and dust emission calculation from surface meteorology |
| Integration domain | Global |
| Grid size | T106 (1.125°) |
| Vertical levels | 20 (surface – 45 hPa) |
| Initial time and forecast time | 96 hours from 12 UTC (once a day) |
| Boundary conditions | Similar to those of the Global Spectral Model |
| Forcing data (nudging) | Global analysis (GA) and forecasts of the Global Spectral Model (GSM) |
|  | Snow depth analysis |

- Ultraviolet (UV) index prediction system

JMA has operated a UV-index prediction system since May 2005. It consists of a chemical transport model (CTM) that is directly coupled with a low-resolution version of the GSM (Shibata et al. 2005) and the radiative transfer model (Aoki et al. 2002). The models’ specifications are given in Tables 4.5.2.1 (9)-1 and 2.

The UV index is calculated using the radiative transfer model in the area from 122°E to 149°E and from 24°N to 46°N with a grid resolution of 0.25° × 0.20°. The Look-Up Table (LUT) method is adopted in consideration of the computational cost involved. The basic parameters of LUT are the solar zenith angle and the total ozone predicted by the CTM. The clear sky UV index is corrected for aerosols (climatology), distance from the sun, altitude and surface albedo (climatology). The forecast UV index is also corrected for categorized weather forecasting.

| Table 4.5.2.1 (9)-1 Specifications of the chemical transport model in the UV index prediction system |
| --- |
| Basic equations | Eulerian model coupled with the Global Spectral Model |
| Numerical technique | 3D semi-Lagrangian transport and chemical reaction |
| Integration domain | Global |
| Grid size | T42 (2.8125°) |
| Vertical levels | 68 (surface – 0.01 hPa) |
| Initial time and forecast time | 48 hours from 12 UTC (once a day) |
| Boundary conditions | Similar to those of the Global Spectral Model |
| Forcing data (nudging) | Global analysis (GA) and forecasts of the Global Spectral Model (GSM) |
| Observational data | Column ozone from OMI/NASA |

| Table 4.5.2.1 (9)-2 Specifications of the radiative transfer model in the UV index prediction system |
| --- |
| Basic equations | Radiative transfer equations for multiple scattering and absorption by atmospheric molecules and aerosols |
| Numerical technique | Doubling and adding method |
| Spectral region and resolution | 280 – 400 nm and 0.5 nm |

- Photochemical oxidant information for the whole of Japan

JMA has issued photochemical oxidant information for the whole of Japan since August 2010. The information is produced by combining a global chemistry-climate model (MRI-CCM2; Deushi et al. 2011) incorporating chemical transport processes of photochemical oxidants in the troposphere/stratosphere and statistical guidance induced from model outputs associated with past events. The latter is prepared by performing verification of the model’s output against observations to enable quantification of oxidant levels for operational forecasters.

| Table 4.5.2.1 (10)-1 Specifications of the global chemistry-climate model for the photochemical oxidant information prediction system |
| --- |
| Basic equations | Eulerian model coupled with the Global Spectral Model |
| Numerical technique | 3D semi-Lagrangian transport and chemical reaction |
| Integration domain | Global |
| Grid size | T106 (1.125°) |
| Vertical levels | 48 (surface – 0.01 hPa) |
| Initial time and forecast time | 72 hours from 12 UTC (once a day) |
| Boundary conditions | Similar to those of the Global Spectral Model |
| Emission inventories | EDGAR, GEIA (for Global) and REAS (for East-Asia) |
| Forcing data (nudging) | Global analysis (GA) and forecasts of the Global Spectral Model (GSM) |

- Mesoscale air pollution transport model

JMA issues photochemical oxidant information for relevant prefectures on days when high oxidant concentration is expected. This information is based on statistical guidance for oxidant concentration using weather elements and pollutant observation data as input. In addition to this statistical guidance, a mesoscale atmospheric transport model (Takano et al. 2007) is applied to oxidant concentration forecasting with a grid interval of 10 km, in which MSM output is used to calculate the transport of highly concentrated pollutant masses in the air. Using the oxidant forecast from the atmospheric transport model with the initial time at 03 UTC, photochemical

oxidant information is issued hourly for 04 – 09 UTC for the northern part of the Kyushu region and the Kanto region including the Tokyo metropolitan area.

- Mesoscale tracer transport model for volcanic ash

JMA introduced the volcanic ash fall forecast in March 2008 (Shimbori et al. 2009). This is a six-hour prediction of areas where ash is expected to fall as a result of volcanic eruptions in Japan, and is issued when an ash plume reaches a height of 3,000 m above the crater rim or when the JMA Volcanic Alert Level is 3 or higher. The specifications of the volcanic-ash transport model using the outputs of the MSM are given in Table 4.5.2.1 (11)-1. Quantitative forecasting of ash-fall depth is currently under development.

| Table 4.5.2.1 (11)-1 Specifications of the mesoscale tracer transport model for volcanic ash |
| --- |
| Model type | Lagrangian description |
| Number of tracer particles | 100,000 |
| Time step | 3 minutes |
| Forecast time | 6 hours from the time of eruption |
| Initial condition | Eruption column based on observational reports of plume height and continuance of volcanic-ash emissions |
| Meteorological field | Meso-Scale Model (MSM) |
| Processes | 3D advection, horizontal and vertical diffusion, volcanic-ash fallout, dry deposition and washout |

### 4.5.2.2	Research performed in the field

- Storm surge model

Wave setup sometimes plays a predominant role in storm surges at Japanese ports facing the open ocean, but this effect is not included in the current storm surge model. JMA is currently evaluating a number of methods that can be operationally used to estimate sea-level rises caused by wave setup using wave conditions predicted in wave model products.

- Sea-ice forecasting model

A new ocean forecast model and a new ocean data assimilation system for the North Pacific Ocean have been developed (see 4.5.2.1 (5)). JMA introduced ocean current data produced as a result of these two developments into the sea-ice forecast model in March 2011, and is currently verifying calculated sea ice data against observation data.

- Kosa prediction model

The Meteorological Research Institute is developing an earth-system model that contains aerosols for the prediction of global warming and data assimilation systems with the ensemble Kalman filter for aerosols.

- UV index prediction system

The Meteorological Research Institute is developing an earth-system model that contains several chemical species for the prediction of global warming and data assimilation systems with the ensemble Kalman filter for stratospheric ozone.

- An ensemble forecast system for ocean waves

JMA has embarked on the development of an ensemble wave forecast system in response to demand for stochastic wave forecasts up to a week ahead. A prototype of the system has been developed, and further verification and improvement will be carried out. JMA plans to start running this system in quasi-operational mode in early 2013 and issuing stochastic wave forecasts in 2015.

- Regional chemical transport model

JMA plans to improve photochemical oxidant information by introducing the high-horizontal-resolution regional chemical transport model developed by the Meteorological Research Institute.

- Typhoon EPS

JMA plans to improve the Typhoon EPS by March 2014 as follows:

- Enhancement of the horizontal and vertical resolutions of the EPS model from around 55 km and 60 layers (TL319L60) to around 40 km and 100 layers (TL479L100)

- Enhancement of the ensemble size from 11 to 25

An experiment on a higher-resolution (TL479L60) Typhoon EPS was conducted to investigate the impact of a higher horizontal resolution model on typhoon track forecasting. The verification results showed that the error of tracks predicted using the higher-resolution model was smaller than that of operational models, mainly due to the reduction of systematic biases. Another experiment with 25 initial conditions was also conducted to investigate the impact of a larger ensemble size on probabilistic typhoon track forecasting. The verification results showed that the experimental Brier skill score (BSS) for TC strike probabilities was smaller than the operational value, indicating that the larger ensemble size is associated with a higher level of skill than the current size.

- Atmospheric Transport Model (ATM)

JMA participated in joint Atmospheric Transport Model (ATM) tests conducted by WMO RSMCs with the ENSEMBLE project run by the Joint Research Centre of the European Commission (JRC-EC). A preliminary test session by ENSEMBLE was held on 26 January, 2012. A request to produce model ensemble products was sent on 18 April, and JMA successfully uploaded ATM products for three types of tracers from eight different initial times by the deadline (two to three weeks after the request was received). Each test product contains five layers of concentration, time-integrated surface concentration, wet and dry depositions, and model precipitation.

### 4.5.3	Specific products operationally available

- Numerical storm surge prediction products

Time series representations of predicted storm tides/astronomical tides and forecast time on predicted highest tides for the coastal area in Japan are disseminated to local meteorological observatories. This information is used as a major basis for issuing storm surge advisories and warnings.

- Kosa products operationally available

Predicted distributions of the surface concentration and total amount of Kosa in eastern Asia are provided online (http://www.jma.go.jp/en/kosa/index.html) once a day.

- UV index products operationally available

Distributions and time series representations of predicted UV index information are provided online (http://www.jma.go.jp/en/uv/index.html) twice a day.

### 4.6	Extended-range forecasts (ERFs) (10 – 30 days)

### 4.6.1	Models

### 4.6.1.1	In operation

JMA operates One-month Ensemble Prediction System (One-month EPS) once a week. The numerical prediction model applied for this system is a low-resolution version (TL159) of the GSM (Table 4.6.1.1-1). For the lower boundary condition of the model, initial COBE-SST (Ishii et al. 2005) anomalies are fixed during the 34-day time integration. Soil moisture, soil temperature and snow depth are predicted by the model, and their initial states are provided by the land data assimilation system.

An ensemble consists of 50 members per week – 25 member runs for each of the 34 days of ensemble prediction from two consecutive days. Thus, initial perturbations are produced by combining the breeding of growing mode (BGM) method and the LAF method.

Table 4.6.1.1-1 Specifications of the one-month EPS

Atmospheric model	GSM1103C

Integration domain	Global, surface to 0.1 hPa

Horizontal resolution	TL159 (reduced Gaussian grid system, approx. 1.125º Gaussian grid, 320 × 160 – 120 km)

Vertical levels	60 (surface to 0.1 hPa)

Forecast time	816 hours from 12 UTC

Ensemble size	50 members

Perturbation generator	Combination of breeding of growing mode (BGM) method and lagged averaged forecast (LAF) method

Perturbed area	Northern Hemisphere (20ºN – 90ºN) and tropics (20ºS – 20ºN)

### 4.6.1.2 Reanalysis project

### (a) Climate Data Assimilation System

The JMA Climate Data Assimilation System (JCDAS) is an atmospheric global analysis tool for operational climate use, and has been operational since March 2006. It was transitioned from the Japanese 25-year Reanalysis (JRA-25) project that covered the 26-year period from 1979 to 2004, and was produced by JMA and the Central Research Institute of Electric Power Industry (CRIEPI) (Onogi et al. 2007). JCDAS uses the same data assimilation system as JRA-25. It has a spectral resolution of T106 (equivalent to a horizontal grid size of around 120 km), and has 40 vertical layers with the top level at 0.4 hPa. The data assimilation method of JCDAS is the three-dimensional variational (3D-Var) technique that was used in JMA’s operations until February 2005. The background error statistics were taken from 2003 operational analysis, as these were the latest data available when JRA-25 production started. For surface variables, surface pressure is assimilated simultaneously with upper-air variables in 3D-Var; the other surface variables of temperature, wind and relative humidity are assimilated separately with uni-variate two-dimensional optimal interpolation (2D-OI).

JRA-25 and JCDAS have jointly provided long-term consistent and high-quality global analysis fields since 1979. For the operational use of JRA-25 by JMA, a new climate normal value was created and is used as a basic reference for climate monitoring services. Reanalysis data produced by a model with the same characteristics as the seasonal forecast model can provide consistent initial field and verification data for seasonal forecasting and hindcasting. In this way, JRA-25 and JCDAS data contribute significantly to the development of the seasonal forecast model.

(b) JRA-55

JMA conducts the second Japanese global atmospheric reanalysis project, referred to as JRA-55. It covers a period of 55 years stretching back to 1958. The project is intended to provide a comprehensive atmospheric dataset suitable for the study of climate change and multi-decadal variability by producing a more time-consistent body of data covering a longer period than JRA-25. Production of JRA-55 started in August 2010, and computations for a period of more than 50 years had been completed as of December 2012.

The JRA-55 data assimilation system is based on JMA’s operational NWP system as of December 2009, in which a variety of improvements had been implemented since the time of JRA-25’s production.  Among the enhancements introduced are:

(1) an advanced data assimilation scheme (from 3D-Var to 4D-Var)

(2) increased model resolution (from T106L40 to TL319L60)

(3) variational bias correction for satellite radiances

(4) a new radiation scheme

(5) updated dynamical and physical processes

Specific improvements for JRA-55 have also been implemented, such as:

(6) use of historical records on greenhouse gases

(7) updated 3-dimensional daily ozone data

(8) quality control information drawn from previous reanalysis

These improvements are effective in solving some of the known problems in the JRA-25 dataset, such as cold biases in the lower stratosphere and unnatural jumps in time-series representations of mean temperature associated with satellite changes.

The completion of JRA-55 is expected in the first half of 2013.

#### 4.6.2	Operationally available NWP model and EPS ERF products

A model systematic bias was estimated as an average forecast error calculated from hindcast experiments for the years from 1979 to 2004. The bias is removed from forecast fields, and grid-point values are processed to produce several forecast materials such as ensemble means and spreads.

Gridded data products for one-month forecast are disseminated on the Tokyo Climate Center (TCC) website (http://ds.data.jma.go.jp/tcc/tcc/index.html). Details of these products are shown in Table 4.6.2-1, and map products disseminated through TCC are shown in Table 4.6.2-2.

| Table 4.6.2-1 Gridded data products (GRIB2) for one-month forecasts disseminated through the TCC |
| --- |
| Details | Level (hPa) | Area | Base time & forecast times |
| Ensemble mean value of forecast members | Sea-level pressure and its anomaly, rainfall amount and its anomaly | - | Global 2.5˚ × 2.5˚ | Base time: 00 UTC of Thursday 1-day Forecast time :2,3,4…,31,32 days from later initial time |
|  | Temperature and its anomaly | Surf, 850, 700 |  |  |
|  | RH, wind (u, v) | 850 |  |  |
|  | Geopotential height and its anomaly | 500, 100 |  |  |
|  | Wind (u, v) | 200 |  |  |
|  | Stream function and its anomaly | 850, 200 |  |  |
|  | Velocity potential and its anomaly | 200 |  |  |

Table 4.6.2-2 Map products for one-month forecasts disseminated via the TCC

|  | Forecast time | Parameter |
| --- | --- | --- |
| Ensemble mean | Averages of days 2 – 8, 9 – 15, 16 – 29, 2 – 29 | Geopotential height and anomaly at 500 hPa, temperature and anomaly at 850 hPa, sea-level pressure and anomaly, stream function and anomaly at 200hPa and 850hPa, velocity potential and anomaly at 200hPa, precipitation and anomaly, temperature and anomaly at 2m, sea surface temperature (prescribed) |

### 4.7 	Long range forecasts (LRF) (30 days up to two years)

### 4.7.1	Models

### 4.7.1.1	In operation

JMA operates Seasonal Ensemble Prediction System (Seasonal EPS) using an atmosphere-ocean coupled model (JMA/MRI-CGCM; Yasuda et al. 2007) for three-month, warm/cold season and El Niño outlooks. The 51-member ensemble is used for the three-month forecast issued every month and for the warm/cold season forecasts issued five times a year (in February, March, April, September and October). The El Niño outlook is also issued based on the same model results.

The JMA/MRI-CGCM was developed by the Meteorological Research Institute and the Climate Prediction Division of JMA. Its specifications are shown in Table 4.7.1-2. The model is initialized with atmospheric and oceanic analysis using the JMA Climate Data Assimilation System (JCDAS) and MOVE/MRI.COM-G, respectively. Land surface climatological conditions are used as the initial values for the CGCM, and a land surface model coupled to the AGCM is used for the prediction of land surface conditions. The climatological distribution of sea ice is used as the lower boundary condition. The EPS adopts a combination of the LAF method and the initial perturbation method described below. Nine-member ensemble predictions are made every five days, and atmospheric initial perturbations for each initial date are obtained using the BGM method. Oceanic initial perturbations are obtained with MOVE/MRI.COM-G (see 4.5.1.1 (1) for details) forced by the surface heat and momentum fluxes of atmospheric initial perturbation fields using the BGM method.

| Table 4.7.1-1 Specifications of the seasonal EPS |
| --- |
| Model | JMA/MRI-CGCM (Yasuda et al. 2007) |
| Oceanic component | Identical to the model for MOVE/MRI.COM-G |
| Atmospheric components | Basic equations | Primitive equations |
|  | Domain | Global |
|  | Resolution | TL95, 40 vertical levels |
|  | Convection scheme | Arakawa-Schubert |
|  | Land surface processes | SiB of Sellers et al. (1986) |
| Coupling | Coupling interval | 1 hour |
|  | Flux adjustment | Monthly heat and momentum flux adjustment |
| Forecast period | 7 months |
| Model run frequency | Once every 5 days |
| Perturbation generator | Combination of the breeding of growing mode (BGM) method and the LAF method |

### 4.7.2	Operationally available EPS LRF products

A model systematic bias was estimated for use as an average forecast error calculated from hindcast experiments for the 30 years from 1979 to 2008. The bias is removed from forecast fields, and grid-point values are processed to produce several forecast materials such as ensemble means and spreads.

The following model output products (Table 4.7.2-1) for three-month forecast are disseminated through the Tokyo Climate Center (TCC) website (http://ds.data.jma.go.jp/tcc/tcc/index.html).

| Table 4.7.2-1 Gridded data products(GRIB2) and maps for three-month forecast disseminated through TCC |
| --- |
| Details | Level (hPa) | Area | Initial time & forecast time |
| Ensemble members, their ensemble mean and spread (standard deviation) values of forecast members averaged for each one-month and three-month period during the forecast time range | Rainfall amount, surface temperature at 2 m, sea surface temperature, sea-level pressure, and their anomalies | - | Global 2.5˚ × 2.5˚ | Initial time: 00 UTC around the 15th day of each month Forecast times: Each one-month and three-month average |
|  | Temperature and its anomaly | 850 |  |  |
|  | Geopotential height and its anomaly | 500 |  |  |
|  | Wind (u, v) and its anomaly | 850, 200 |  |  |

The following model output products (Table 4.7.2-2) for warm/cold season prediction are disseminated through the Tokyo Climate Center (TCC) website (http://ds.data.jma.go.jp/tcc/tcc/index.html).

| Table 4.7.2-2 Gridded data products (GRIB2) and maps for warm/cold season forecast disseminated through TCC |
| --- |
| Details | Level (hPa) | Area | Initial time & forecast time |
| Ensemble members, their ensemble mean and spread (standard deviation) values averaged for each one-month and three-month period during forecast time range | Rainfall amount, surface temperature at 2 m, sea surface temperature, sea-level pressure, and their anomalies | - | Global 2.5˚ × 2.5˚ | Initial time: 00 UTC around the 15th day in Feb., Mar., Apr., Sep. and Oct. Forecast times: Each one-month and three-month average |
|  | Temperature and its anomaly | 850 |  |  |
|  | Geopotential height and its anomaly | 500 |  |  |
|  | Wind (u, v) and its anomaly | 850, 200 |  |  |
|  | Relative humidity and its anomaly | 850 |  |  |

## 5.	Verification of prognostic products

### 5.1	Annual verification summary

### 5.1.1 	NWP prognostic products

Objective verification of prognostic products is operationally performed against analysis and radiosonde observations according to WMO/CBS recommendations. The results of monthly verification for 2012 are presented in Tables 5.1.1-1 – 5.1.1-20. All verification scores are only for prediction from 1200 UTC initials.

Table 5.1.1-1  Root mean square errors of geopotential height at 500 hPa against analysis (m)

Northern Hemisphere (20–90˚N)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 8.2 | 8.3 | 7.8 | 7.1 | 6.9 | 7.1 | 6.2 | 6.1 | 6.3 | 6.5 | 7.1 | 7.8 | 7.1 |
| 72 | 26.8 | 26.2 | 26.5 | 23.1 | 21.4 | 21.9 | 18.9 | 19.2 | 21.3 | 22.3 | 24.8 | 25.2 | 23.1 |
| 120 | 54.0 | 52.2 | 53.0 | 45.3 | 43.6 | 42.7 | 34.7 | 37.3 | 43.0 | 46.7 | 47.6 | 52.3 | 46.0 |

Table 5.1.1-2  Root mean square errors of geopotential height at 500 hPa against analysis (m)

Southern Hemisphere (20–90˚S)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 8.3 | 8.4 | 8.9 | 9.0 | 9.6 | 10.5 | 9.7 | 10.9 | 10.0 | 9.0 | 8.6 | 7.8 | 9.2 |
| 72 | 26.5 | 27.6 | 30.2 | 29.5 | 33.6 | 37.0 | 33.0 | 36.3 | 33.0 | 31.0 | 28.9 | 24.8 | 31.0 |
| 120 | 49.2 | 55.8 | 59.3 | 54.6 | 64.2 | 70.1 | 61.8 | 67.4 | 63.8 | 61.1 | 54.9 | 47.8 | 59.2 |

Table 5.1.1-3  Root mean square errors of geopotential height at 500 hPa against observations (m)

North America

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 12.0 | 12.3 | 12.0 | 11.7 | 10.3 | 10.8 | 10.0 | 10.0 | 10.4 | 10.6 | 11.2 | 12.2 | 11.1 |
| 72 | 30.2 | 32.3 | 28.3 | 26.9 | 21.6 | 22.0 | 18.6 | 18.2 | 20.6 | 23.2 | 24.5 | 25.5 | 24.3 |
| 120 | 58.2 | 55.4 | 60.1 | 50.7 | 35.7 | 42.6 | 30.9 | 33.4 | 38.0 | 43.6 | 43.4 | 51.6 | 45.3 |
| ob. num. | 92 | 92 | 92 | 92 | 92 | 92 | 93 | 94 | 93 | 94 | 94 | 92 | 92.7 |

Table 5.1.1-4  Root mean square errors of geopotential height at 500 hPa against observations (m)

Europe/North Africa

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 13.7 | 12.0 | 12.6 | 12.2 | 12.2 | 10.9 | 10.5 | 10.7 | 11.8 | 12.0 | 12.7 | 12.6 | 12.0 |
| 72 | 30.2 | 30.2 | 31.1 | 26.8 | 24.3 | 21.9 | 20.8 | 21.0 | 27.4 | 24.0 | 29.7 | 28.9 | 26.4 |
| 120 | 58.9 | 63.6 | 57.5 | 49.7 | 50.8 | 39.5 | 34.4 | 34.8 | 57.5 | 52.2 | 58.7 | 62.9 | 51.7 |
| ob. num. | 61 | 61 | 59 | 59 | 59 | 59 | 58 | 58 | 57 | 59 | 57 | 56 | 58.6 |

Table 5.1.1-5  Root mean square errors of geopotential height at 500 hPa against observations (m)

Asia

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 14.0 | 14.7 | 13.9 | 12.3 | 11.8 | 11.9 | 10.5 | 10.3 | 10.5 | 11.0 | 12.2 | 13.2 | 12.2 |
| 72 | 20.4 | 21.9 | 22.3 | 21.2 | 20.3 | 19.8 | 16.6 | 18.1 | 17.7 | 19.4 | 20.5 | 22.2 | 20.0 |
| 120 | 35.4 | 30.9 | 33.6 | 34.6 | 32.6 | 27.0 | 25.1 | 27.2 | 28.3 | 30.6 | 32.9 | 35.9 | 31.2 |
| ob. num. | 86 | 86 | 88 | 88 | 87 | 87 | 87 | 87 | 87 | 87 | 87 | 86 | 86.9 |

Table 5.1.1-6  Root mean square errors of geopotential height at 500 hPa against observations (m)

Australia/New Zealand

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 11.8 | 10.8 | 11.5 | 12.6 | 10.9 | 12.5 | 11.2 | 12.2 | 13.5 | 12.8 | 13.5 | 13.6 | 12.2 |
| 72 | 20.0 | 17.9 | 22.1 | 22.8 | 23.2 | 24.7 | 19.5 | 22.0 | 28.0 | 24.6 | 24.0 | 21.9 | 22.6 |
| 120 | 33.8 | 33.3 | 38.7 | 33.7 | 45.7 | 46.2 | 42.5 | 40.3 | 45.0 | 47.5 | 45.1 | 32.7 | 40.4 |
| ob. num. | 15 | 14 | 14 | 14 | 14 | 14 | 14 | 12 | 12 | 11 | 12 | 12 | 13.2 |

Table 5.1.1-7  Root mean square errors of geopotential height at 500 hPa against observations (m)

Northern Hemisphere (20–90˚N)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 13.6 | 13.7 | 13.4 | 12.6 | 12.1 | 12.3 | 11.3 | 11.3 | 11.4 | 11.5 | 12.2 | 13.1 | 12.4 |
| 72 | 28.2 | 28.7 | 28.2 | 25.4 | 23.3 | 23.2 | 20.7 | 20.8 | 23.3 | 23.3 | 25.8 | 26.9 | 24.8 |
| 120 | 54.5 | 53.1 | 53.4 | 46.1 | 42.6 | 40.8 | 33.6 | 36.0 | 44.4 | 44.5 | 47.1 | 53.1 | 45.8 |
| ob. num. | 331 | 333 | 331 | 331 | 331 | 330 | 329 | 328 | 330 | 328 | 326 | 324 | 329.3 |

Table 5.1.1-8  Root mean square errors of geopotential height at 500 hPa against observations (m)

Southern Hemisphere (20–90˚S)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 11.9 | 11.9 | 12.6 | 14.5 | 14.5 | 15.7 | 14.7 | 15.9 | 15.7 | 14.2 | 13.7 | 13.1 | 14.0 |
| 72 | 20.8 | 22.7 | 24.5 | 25.7 | 29.9 | 36.9 | 30.1 | 31.6 | 31.2 | 27.9 | 25.1 | 21.9 | 27.4 |
| 120 | 37.6 | 39.7 | 44.2 | 43.9 | 52.1 | 61.3 | 50.2 | 53.7 | 50.6 | 53.1 | 44.2 | 37.7 | 47.4 |
| ob. num. | 42 | 37 | 37 | 35 | 36 | 37 | 39 | 38 | 37 | 36 | 37 | 37 | 37.3 |

Table 5.1.1-9  Root mean square of vector wind errors at 250 hPa against analysis (m/s)

Northern Hemisphere (20–90˚N)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 3.4 | 3.4 | 3.5 | 3.5 | 3.4 | 3.7 | 3.5 | 3.5 | 3.4 | 3.3 | 3.5 | 3.4 | 3.5 |
| 72 | 8.0 | 8.2 | 8.1 | 8.0 | 7.8 | 8.8 | 8.3 | 8.4 | 8.4 | 8.3 | 8.1 | 8.1 | 8.2 |
| 120 | 13.4 | 13.2 | 13.4 | 12.7 | 12.8 | 13.7 | 12.2 | 13.0 | 14.0 | 13.8 | 13.5 | 13.7 | 13.3 |

Table 5.1.1-10  Root mean square of vector wind errors at 250 hPa against analysis (m/s)

Southern Hemisphere (20–90˚S)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 3.5 | 3.4 | 3.5 | 3.6 | 3.6 | 3.7 | 3.5 | 3.7 | 3.6 | 3.5 | 3.5 | 3.3 | 3.5 |
| 72 | 8.7 | 8.8 | 9.0 | 9.1 | 9.3 | 9.9 | 8.9 | 9.3 | 9.0 | 8.7 | 8.5 | 8.3 | 9.0 |
| 120 | 14.0 | 14.3 | 15.2 | 14.8 | 15.4 | 16.0 | 14.3 | 15.0 | 15.0 | 14.3 | 13.8 | 13.3 | 14.6 |

Table 5.1.1-11  Root mean square of vector wind errors at 250 hPa against observations (m/s)

North America

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 5.8 | 6.1 | 5.9 | 5.8 | 5.9 | 6.2 | 5.5 | 5.6 | 5.4 | 5.6 | 5.2 | 5.6 | 5.7 |
| 72 | 10.6 | 11.3 | 10.1 | 9.7 | 9.5 | 10.4 | 9.0 | 9.1 | 9.5 | 9.9 | 9.2 | 9.5 | 9.8 |
| 120 | 16.7 | 17.3 | 17.2 | 15.6 | 13.5 | 16.0 | 12.5 | 13.2 | 14.3 | 15.1 | 14.3 | 15.6 | 15.1 |
| ob. num. | 88 | 90 | 91 | 90 | 90 | 91 | 92 | 92 | 92 | 93 | 93 | 91 | 91.1 |

Table 5.1.1-12  Root mean square of vector wind errors at 250 hPa against observations (m/s)

Europe/North Africa

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 5.3 | 4.9 | 4.8 | 4.6 | 4.9 | 5.0 | 5.3 | 5.1 | 5.6 | 5.3 | 5.5 | 4.8 | 5.1 |
| 72 | 9.5 | 9.0 | 9.0 | 7.8 | 8.5 | 8.4 | 8.9 | 8.6 | 10.6 | 9.7 | 10.2 | 9.0 | 9.1 |
| 120 | 17.6 | 16.5 | 15.3 | 13.6 | 14.1 | 13.3 | 13.3 | 13.9 | 18.9 | 16.7 | 18.2 | 15.9 | 15.6 |
| ob. num. | 62 | 62 | 61 | 61 | 61 | 62 | 60 | 60 | 59 | 60 | 57 | 57 | 60.2 |

Table 5.1.1-13  Root mean square of vector wind errors at 250 hPa against observations (m/s)

Asia

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 4.7 | 5.4 | 5.8 | 6.5 | 6.0 | 6.7 | 6.2 | 5.8 | 5.5 | 4.8 | 5.3 | 5.2 | 5.7 |
| 72 | 7.6 | 8.2 | 8.6 | 9.5 | 9.4 | 11.0 | 10.0 | 9.8 | 8.9 | 7.9 | 8.0 | 7.9 | 8.9 |
| 120 | 11.2 | 9.8 | 11.7 | 12.8 | 13.6 | 13.9 | 12.9 | 12.7 | 12.9 | 11.0 | 11.6 | 11.1 | 12.1 |
| ob. num. | 134 | 133 | 133 | 132 | 133 | 131 | 132 | 134 | 134 | 134 | 134 | 133 | 133.1 |

Table 5.1.1-14  Root mean square of vector wind errors at 250 hPa against observations (m/s)

Australia/New Zealand

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 6.1 | 5.4 | 5.7 | 5.4 | 5.2 | 5.2 | 5.0 | 5.4 | 5.1 | 5.7 | 5.7 | 5.8 | 5.5 |
| 72 | 8.4 | 8.6 | 8.8 | 9.3 | 8.4 | 8.8 | 7.4 | 7.7 | 7.5 | 8.3 | 8.5 | 8.5 | 8.4 |
| 120 | 13.0 | 11.6 | 13.4 | 12.6 | 13.8 | 12.8 | 11.1 | 11.4 | 11.9 | 12.8 | 12.6 | 11.6 | 12.4 |
| ob. num. | 21 | 21 | 22 | 21 | 18 | 18 | 20 | 22 | 22 | 22 | 22 | 21 | 20.8 |

Table 5.1.1-15  Root mean square of vector wind errors at 250 hPa against observations (m/s)

Northern Hemisphere (20–90˚N)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 5.0 | 5.3 | 5.3 | 5.6 | 5.4 | 5.9 | 5.6 | 5.6 | 5.3 | 5.0 | 5.1 | 5.1 | 5.4 |
| 72 | 8.8 | 9.1 | 8.8 | 8.9 | 9.0 | 10.1 | 9.5 | 9.4 | 9.5 | 9.0 | 8.8 | 8.6 | 9.1 |
| 120 | 14.4 | 13.8 | 14.0 | 13.5 | 13.4 | 14.6 | 13.1 | 13.7 | 15.0 | 14.0 | 14.1 | 14.1 | 14.0 |
| ob. num. | 392 | 396 | 394 | 394 | 395 | 394 | 393 | 394 | 395 | 391 | 387 | 385 | 392.5 |

Table 5.1.1-16  Root mean square of vector wind errors at 250 hPa against observations (m/s)

Southern Hemisphere (20–90˚S)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 5.9 | 5.6 | 5.6 | 5.7 | 5.5 | 5.9 | 5.6 | 6.1 | 5.9 | 6.1 | 6.1 | 5.6 | 5.8 |
| 72 | 8.5 | 8.8 | 9.2 | 9.6 | 9.3 | 10.2 | 9.1 | 9.7 | 9.3 | 9.5 | 9.4 | 8.5 | 9.3 |
| 120 | 12.8 | 12.7 | 14.1 | 14.3 | 15.0 | 15.7 | 13.7 | 14.9 | 14.4 | 14.6 | 13.4 | 12.5 | 14.0 |
| ob. num. | 46 | 43 | 44 | 40 | 39 | 41 | 44 | 45 | 45 | 43 | 45 | 45 | 43.3 |

Table 5.1.1-17  Root mean square of vector wind errors at 850 hPa against analysis (m/s)

Tropic

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 1.6 | 1.5 | 1.5 | 1.4 | 1.5 | 1.5 | 1.5 | 1.6 | 1.6 | 1.5 | 1.5 | 1.6 | 1.5 |
| 72 | 2.9 | 2.8 | 3.0 | 2.6 | 2.6 | 2.8 | 2.8 | 2.9 | 2.9 | 2.8 | 2.7 | 2.8 | 2.8 |
| 120 | 3.7 | 3.6 | 3.8 | 3.1 | 3.3 | 3.6 | 3.5 | 3.7 | 3.8 | 3.5 | 3.4 | 3.4 | 3.5 |

Table 5.1.1-18  Root mean square of vector wind errors at 250 hPa against analysis (m/s)

Tropic

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 3.4 | 3.3 | 3.5 | 3.2 | 3.1 | 3.2 | 3.2 | 3.2 | 3.2 | 3.0 | 3.1 | 3.2 | 3.2 |
| 72 | 6.0 | 6.2 | 6.5 | 6.1 | 5.9 | 6.1 | 5.8 | 5.8 | 5.9 | 5.7 | 5.7 | 6.0 | 6.0 |
| 120 | 7.6 | 7.9 | 8.4 | 7.9 | 7.6 | 7.9 | 7.4 | 7.4 | 7.6 | 7.4 | 7.4 | 7.6 | 7.7 |

Table 5.1.1-19  Root mean square of vector wind errors at 850 hPa against observations (m/s)

Tropic

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 3.6 | 3.5 | 3.6 | 3.3 | 3.4 | 3.5 | 3.4 | 3.4 | 3.5 | 3.6 | 3.4 | 3.7 | 3.5 |
| 72 | 4.1 | 3.9 | 4.1 | 3.7 | 3.8 | 4.2 | 4.0 | 4.1 | 4.0 | 4.1 | 3.8 | 4.2 | 4.0 |
| 120 | 4.6 | 4.4 | 4.7 | 4.0 | 4.1 | 4.7 | 4.4 | 4.6 | 4.5 | 4.5 | 4.2 | 4.5 | 4.4 |
| ob. num. | 60 | 59 | 61 | 62 | 61 | 64 | 62 | 62 | 61 | 60 | 62 | 63 | 61.4 |

Table 5.1.1-20  Root mean square of vector wind errors at 250 hPa against observations (m/s)

Tropic

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 5.4 | 5.4 | 5.2 | 4.7 | 4.7 | 5.0 | 5.1 | 5.1 | 4.8 | 4.9 | 4.6 | 4.8 | 5.0 |
| 72 | 7.0 | 7.0 | 6.9 | 6.5 | 6.4 | 6.8 | 6.9 | 7.0 | 7.1 | 6.6 | 6.1 | 6.5 | 6.7 |
| 120 | 8.2 | 8.1 | 8.0 | 7.7 | 7.8 | 8.5 | 8.0 | 8.5 | 8.6 | 8.1 | 7.1 | 7.6 | 8.0 |
| ob. num. | 61 | 59 | 61 | 61 | 61 | 65 | 64 | 64 | 62 | 61 | 63 | 64 | 62.2 |

Verification for One-week EPS is performed against analysis according to the Manual on GDPFS (WMO-No. 485). The Brier Skill Score (BSS) for seasonal (DJF: December-January-February), MAM: March-April-May, JJA: June-July-August, SON: September-October-November) and annual averages in 2012 (December in 2011) are shown in Tables 5.1.1-21 - 5.1.1-26.

Table 5.1.1-21 BSS for geopotential height at 500 hPa over the Northern Hemisphere (20–90˚N)

| Hour | Z500 anomaly +1.0 standard deviation | Z500 anomaly +1.5 standard deviation | Z500 anomaly +2.0 standard deviation |
| --- | --- | --- | --- |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.910 | 0.910 | 0.870 | 0.906 | 0.899 | 0.897 | 0.904 | 0.846 | 0.903 | 0.887 | 0.881 | 0.876 | 0.814 | 0.901 | 0.868 |
| 72 | 0.761 | 0.751 | 0.647 | 0.740 | 0.725 | 0.734 | 0.715 | 0.588 | 0.724 | 0.690 | 0.697 | 0.657 | 0.509 | 0.710 | 0.643 |
| 120 | 0.570 | 0.554 | 0.430 | 0.540 | 0.524 | 0.522 | 0.485 | 0.358 | 0.523 | 0.472 | 0.453 | 0.387 | 0.264 | 0.502 | 0.401 |
| 168 | 0.377 | 0.347 | 0.248 | 0.337 | 0.327 | 0.321 | 0.271 | 0.179 | 0.320 | 0.273 | 0.245 | 0.198 | 0.087 | 0.287 | 0.204 |
| Hour | Z500 anomaly -1.0 standard deviation | Z500 anomaly -1.5 standard deviation | Z500 anomaly -2.0 standard deviation |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.876 | 0.886 | 0.827 | 0.874 | 0.865 | 0.831 | 0.865 | 0.791 | 0.848 | 0.834 | 0.762 | 0.833 | 0.745 | 0.823 | 0.791 |
| 72 | 0.688 | 0.708 | 0.588 | 0.678 | 0.665 | 0.590 | 0.666 | 0.502 | 0.623 | 0.595 | 0.463 | 0.623 | 0.422 | 0.574 | 0.520 |
| 120 | 0.480 | 0.505 | 0.359 | 0.460 | 0.451 | 0.361 | 0.455 | 0.257 | 0.393 | 0.367 | 0.196 | 0.376 | 0.174 | 0.336 | 0.271 |
| 168 | 0.324 | 0.323 | 0.140 | 0.258 | 0.261 | 0.195 | 0.277 | 0.034 | 0.192 | 0.175 | 0.010 | 0.210 | 0.044 | 0.127 | 0.076 |

Table 5.1.1-22 BSS for temperature at 850 hPa over the Northern Hemisphere (20–90˚N)

| Hour | T850 anomaly +1.0 standard deviation | T850 anomaly +1.5 standard deviation | T850 anomaly +2.0 standard deviation |
| --- | --- | --- | --- |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.802 | 0.793 | 0.727 | 0.771 | 0.773 | 0.760 | 0.747 | 0.693 | 0.742 | 0.736 | 0.715 | 0.722 | 0.653 | 0.707 | 0.699 |
| 72 | 0.616 | 0.603 | 0.489 | 0.570 | 0.569 | 0.542 | 0.544 | 0.438 | 0.532 | 0.514 | 0.475 | 0.479 | 0.383 | 0.481 | 0.455 |
| 120 | 0.443 | 0.434 | 0.319 | 0.398 | 0.398 | 0.364 | 0.360 | 0.268 | 0.356 | 0.337 | 0.282 | 0.298 | 0.202 | 0.303 | 0.271 |
| 168 | 0.300 | 0.274 | 0.178 | 0.241 | 0.248 | 0.235 | 0.213 | 0.144 | 0.205 | 0.199 | 0.159 | 0.161 | 0.093 | 0.160 | 0.144 |
| Hour | T850 anomaly -1.0 standard deviation | T850 anomaly -1.5 standard deviation | T850 anomaly -2.0 standard deviation |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.803 | 0.798 | 0.717 | 0.768 | 0.771 | 0.756 | 0.760 | 0.647 | 0.714 | 0.719 | 0.691 | 0.704 | 0.553 | 0.639 | 0.647 |
| 72 | 0.620 | 0.606 | 0.433 | 0.553 | 0.553 | 0.544 | 0.544 | 0.322 | 0.475 | 0.471 | 0.464 | 0.464 | 0.178 | 0.375 | 0.370 |
| 120 | 0.454 | 0.429 | 0.239 | 0.366 | 0.372 | 0.358 | 0.358 | 0.134 | 0.284 | 0.283 | 0.267 | 0.286 | 0.021 | 0.179 | 0.188 |
| 168 | 0.309 | 0.265 | 0.092 | 0.190 | 0.214 | 0.216 | 0.200 | 0.008 | 0.100 | 0.131 | 0.110 | 0.136 | -0.074 | 0.012 | 0.046 |

Table 5.1.1-23 BSS for geopotential height at 500 hPa over the Tropics (20˚S–20˚N)

| Hour | Z500 anomaly +1.0 standard deviation | Z500 anomaly +1.5 standard deviation | Z500 anomaly +2.0 standard deviation |
| --- | --- | --- | --- |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.765 | 0.707 | 0.675 | 0.732 | 0.720 | 0.675 | 0.653 | 0.619 | 0.684 | 0.658 | 0.458 | 0.498 | 0.534 | 0.593 | 0.520 |
| 72 | 0.544 | 0.432 | 0.406 | 0.518 | 0.475 | 0.390 | 0.433 | 0.356 | 0.471 | 0.412 | 0.253 | 0.372 | 0.280 | 0.450 | 0.339 |
| 120 | 0.387 | 0.282 | 0.244 | 0.345 | 0.314 | 0.244 | 0.240 | 0.216 | 0.314 | 0.253 | 0.073 | 0.229 | 0.166 | 0.278 | 0.186 |
| 168 | 0.256 | 0.136 | 0.096 | 0.155 | 0.161 | 0.123 | 0.136 | 0.097 | 0.146 | 0.126 | -0.077 | 0.132 | 0.087 | 0.114 | 0.064 |
| Hour | Z500 anomaly -1.0 standard deviation | Z500 anomaly -1.5 standard deviation | Z500 anomaly -2.0 standard deviation |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.760 | 0.732 | 0.654 | 0.707 | 0.713 | 0.729 | 0.700 | 0.617 | 0.661 | 0.677 | 0.669 | 0.671 | 0.558 | 0.639 | 0.634 |
| 72 | 0.482 | 0.458 | 0.250 | 0.400 | 0.397 | 0.334 | 0.428 | 0.143 | 0.363 | 0.317 | 0.090 | 0.353 | 0.076 | 0.311 | 0.208 |
| 120 | 0.240 | 0.245 | -0.026 | 0.041 | 0.125 | 0.057 | 0.178 | -0.195 | -0.074 | -0.008 | -0.310 | 0.060 | -0.359 | -0.196 | -0.201 |
| 168 | -0.066 | -0.027 | -0.417 | -0.501 | -0.253 | -0.400 | -0.126 | -0.684 | -0.797 | -0.502 | -1.010 | -0.295 | -0.910 | -0.946 | -0.791 |

Table 5.1.1-24 BSS for temperature at 850 hPa over the Tropics (20˚S–b 20˚N)

| Hour | T850 anomaly +1.0 standard deviation | T850 anomaly +1.5 standard deviation | T850 anomaly +2.0 standard deviation |
| --- | --- | --- | --- |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.649 | 0.521 | 0.565 | 0.594 | 0.582 | 0.593 | 0.447 | 0.506 | 0.533 | 0.520 | 0.529 | 0.365 | 0.435 | 0.450 | 0.445 |
| 72 | 0.439 | 0.258 | 0.336 | 0.363 | 0.349 | 0.370 | 0.184 | 0.282 | 0.296 | 0.283 | 0.293 | 0.127 | 0.225 | 0.218 | 0.216 |
| 120 | 0.335 | 0.129 | 0.215 | 0.234 | 0.228 | 0.266 | 0.072 | 0.162 | 0.174 | 0.169 | 0.184 | 0.049 | 0.108 | 0.117 | 0.115 |
| 168 | 0.263 | 0.054 | 0.121 | 0.153 | 0.148 | 0.191 | 0.024 | 0.087 | 0.109 | 0.103 | 0.113 | 0.012 | 0.055 | 0.070 | 0.062 |
| Hour | T850 anomaly -1.0 standard deviation | T850 anomaly -1.5 standard deviation | T850 anomaly -2.0 standard deviation |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.579 | 0.565 | 0.567 | 0.564 | 0.568 | 0.554 | 0.540 | 0.515 | 0.521 | 0.532 | 0.511 | 0.511 | 0.472 | 0.509 | 0.501 |
| 72 | 0.288 | 0.279 | 0.318 | 0.318 | 0.301 | 0.247 | 0.221 | 0.280 | 0.283 | 0.258 | 0.215 | 0.180 | 0.235 | 0.275 | 0.226 |
| 120 | 0.155 | 0.147 | 0.203 | 0.209 | 0.178 | 0.120 | 0.102 | 0.172 | 0.168 | 0.140 | 0.095 | 0.078 | 0.133 | 0.154 | 0.115 |
| 168 | 0.058 | 0.047 | 0.114 | 0.136 | 0.089 | 0.014 | 0.026 | 0.096 | 0.088 | 0.056 | 0.020 | 0.021 | 0.081 | 0.064 | 0.046 |

Table 5.1.1-25 BSS for geopotential height at 500 hPa over the Southern Hemisphere (20–90˚S)

| Hour | Z500 anomaly +1.0 standard deviation | Z500 anomaly +1.5 standard deviation | Z500 anomaly +2.0 standard deviation |
| --- | --- | --- | --- |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.905 | 0.904 | 0.916 | 0.899 | 0.906 | 0.896 | 0.883 | 0.903 | 0.881 | 0.891 | 0.882 | 0.850 | 0.858 | 0.848 | 0.860 |
| 72 | 0.736 | 0.718 | 0.746 | 0.717 | 0.729 | 0.711 | 0.663 | 0.706 | 0.672 | 0.688 | 0.645 | 0.578 | 0.599 | 0.590 | 0.603 |
| 120 | 0.527 | 0.489 | 0.536 | 0.513 | 0.516 | 0.481 | 0.402 | 0.475 | 0.449 | 0.452 | 0.395 | 0.306 | 0.333 | 0.328 | 0.340 |
| 168 | 0.348 | 0.286 | 0.365 | 0.323 | 0.330 | 0.276 | 0.208 | 0.307 | 0.266 | 0.264 | 0.197 | 0.138 | 0.185 | 0.166 | 0.172 |
| Hour | Z500 anomaly -1.0 standard deviation | Z500 anomaly -1.5 standard deviation | Z500 anomaly -2.0 standard deviation |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.898 | 0.888 | 0.881 | 0.895 | 0.891 | 0.882 | 0.878 | 0.860 | 0.873 | 0.873 | 0.843 | 0.863 | 0.812 | 0.845 | 0.841 |
| 72 | 0.712 | 0.673 | 0.670 | 0.693 | 0.687 | 0.668 | 0.644 | 0.611 | 0.644 | 0.642 | 0.595 | 0.604 | 0.547 | 0.580 | 0.582 |
| 120 | 0.519 | 0.440 | 0.446 | 0.472 | 0.469 | 0.460 | 0.400 | 0.376 | 0.389 | 0.406 | 0.375 | 0.343 | 0.297 | 0.301 | 0.329 |
| 168 | 0.351 | 0.234 | 0.243 | 0.279 | 0.277 | 0.275 | 0.206 | 0.174 | 0.193 | 0.212 | 0.180 | 0.155 | 0.118 | 0.124 | 0.144 |

Table 5.1.1-26 BSS for temperature at 850 hPa over the Southern Hemisphere (20–90˚S)

| Hour | T850 anomaly +1.0 standard deviation | T850 anomaly +1.5 standard deviation | T850 anomaly +2.0 standard deviation |
| --- | --- | --- | --- |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.813 | 0.817 | 0.826 | 0.814 | 0.818 | 0.782 | 0.782 | 0.780 | 0.780 | 0.781 | 0.753 | 0.716 | 0.731 | 0.738 | 0.734 |
| 72 | 0.595 | 0.595 | 0.611 | 0.604 | 0.601 | 0.543 | 0.527 | 0.534 | 0.544 | 0.537 | 0.489 | 0.431 | 0.457 | 0.465 | 0.460 |
| 120 | 0.416 | 0.398 | 0.419 | 0.426 | 0.415 | 0.354 | 0.319 | 0.344 | 0.356 | 0.343 | 0.288 | 0.215 | 0.273 | 0.264 | 0.260 |
| 168 | 0.257 | 0.228 | 0.267 | 0.268 | 0.255 | 0.198 | 0.179 | 0.214 | 0.204 | 0.199 | 0.131 | 0.094 | 0.166 | 0.134 | 0.131 |
| Hour | T850 anomaly -1.0 standard deviation | T850 anomaly -1.5 standard deviation | T850 anomaly -2.0 standard deviation |
|  | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual | DJF | MAM | JJA | SON | Annual |
| 24 | 0.836 | 0.815 | 0.822 | 0.841 | 0.829 | 0.834 | 0.783 | 0.789 | 0.817 | 0.806 | 0.863 | 0.717 | 0.734 | 0.789 | 0.776 |
| 72 | 0.650 | 0.591 | 0.602 | 0.635 | 0.619 | 0.663 | 0.540 | 0.540 | 0.599 | 0.585 | 0.734 | 0.447 | 0.436 | 0.557 | 0.544 |
| 120 | 0.488 | 0.401 | 0.412 | 0.450 | 0.438 | 0.521 | 0.336 | 0.354 | 0.410 | 0.405 | 0.635 | 0.240 | 0.265 | 0.356 | 0.374 |
| 168 | 0.363 | 0.231 | 0.256 | 0.296 | 0.286 | 0.411 | 0.176 | 0.205 | 0.270 | 0.265 | 0.545 | 0.106 | 0.137 | 0.254 | 0.261 |

6.	Plans for the future (next 4 years)

### 6.1	Development of the GDPFS

### 6.1.1 	Major changes expected in the next year

- The off-line simple biosphere model (SiB) will be introduced as a new land surface analysis model.

### 6.1.2 	Major changes expected in the next 4 years

- Hyper-spectral infrared sounding data from Aqua/AIRS and Metop/IASI will be assimilated.

- The vertical resolution of the GSM will be enhanced from 60 to around 100 layers, and the model’s top height will be raised.

- A coupled oceanic mixed-layer atmosphere model will be introduced into medium-range deterministic forecasting.

- A SiB will be incorporated into the MSM.

- An urban canopy will be incorporated into the SiB of the MSM.

- Surface observation data will be assimilated into Meso-scale Analysis.

- The vertical resolution of the MSM will be enhanced.

- The second long-term reanalysis project (JRA-55) will be completed.

- The spatial resolution of the one-month prediction system will be enhanced from TL159 to TL319.

- The horizontal resolution of the Kosa and global chemistry-climate models will be enhanced.

- A data assimilation system with an ensemble Kalman filter will be introduced in aerosol and stratospheric ozone analysis.

- A regional chemical transport model for photochemical oxidant information will be introduced.

- The horizontal and vertical resolutions of both the One-week EPS and the Typhoon EPS will be enhanced from TL319 to TL479 and from 60 to around 100 layers, respectively.

- The ensemble size of the Typhoon EPS will be increased from 11 to 25.

- The UV index prediction model is improved by introducing the new global chemistry-climate model (MRI-CCM2).

## References

Aoki, Te., Ta. Aoki, M. Fukabori and T. Takao, 2002: Characteristics of UV-B Irradiance at Syowa Station, Antarctica: Analyses of the Measurements and Comparison with Numerical Simulations. J. Meteor. Soc. Japan., 80, 161–170.

Bechtold, P.and J.Bidlot, 2009: Parametrization of convective gusts. ECMWF Newsletter, 119,15-18

Buizza, R., M. Miller and T. N. Palmer, 1999: Stochastic representation of model uncertainties in the ECMWF ensemble prediction system. Quart. J. Roy. Meteor. Soc., 125, 2887–2908.

Buizza, R. and Palmer, T. N., 1995: The singular-vector structure of the atmospheric global circulation. J. Atmos. Sci., 52, 1434–1456.

Deushi, M., and K. Shibata, 2011: Development of an MRI Chemistry-Climate Model ver. 2 for the study of tropospheric and stratospheric chemistry, Papers in Meteorology and Geophysics, 62, 1 – 46.

Egbert, G. and S. Erofeeva, 2002: Efficient Inverse Modeling of Barotropic Ocean Tides. J. Atmos. Oceanic Technol., 19, 183–204.

Ehrendorfer, M., R. M. Errico and K. D. Raeder, 1999: Singular-Vector Perturbation Growth in a Primitive Equation Model with Moist Physics. J. Atmos. Sci., 56, 1627–1648.

Foster, D. J. and R. D. Davy, 1988: Global Snow Depth Climatology. USAF-ETAC/TN-88/006. Scott Air Force Base, Illinois, p. 48.

Fukuda, J., T. Fujita, Y. Ikuta, Y. Ishikawa and K. Yoshimoto, 2011: Development of JMA Local Analysis. CAS/JSC WGNE Res. Activ. Atmos. Oceanic Modell., 41, 0107-0108.

Hirahara, Y., J. Ishida and T. Ishimizu, 2011: Trial operation of the Local Forecast Model at JMA. CAS/JSC WGNE Res. Activ. Atmos. Oceanic Modell., 41, 0511-0512.

Honda, Y., M. Nishijima, K. Koizumi, Y. Ohta, K. Tamiya, T. Kawabata and T. Tsuyuki, 2005: A pre-operational variational data assimilation system for a non-hydrostatic model at the Japan Meteorological Agency: Formulation and preliminary results. Quart. J. Roy. Meteor. Soc., 131, 3465-3475.

Ishii, M., A. Shouji, S. Sugimoto and T. Matsumoto 2005: Objective analyses of sea-surface temperature and marine meteorological variables for the 20th century using ICOADS and the KOBE Collection. Int. J. Climatol., 25, 865–879.

Kawai, H. and T. Inoue, 2006: A simple parameterization scheme for subtropical marine stratocumulus. SOLA, 2, 17 –20.

Kudo, A., 2011: Development of JMA’s new turbulence index. 15th Conference on Aviation, Range, and Aerospace Meteorology, LA, Amer. Met. Soc.

Narita, M., 2013: Computer System, In Outline of the Operational Numerical Weather Prediction at the Japan Meteorological Agency. Appendix to WMO Technical Progress Report on the Global Data-processing and Forecasting Systems (GDPFS) and Numerical Weather Prediction (NWP) Research. Japan Meteorological Agency, Tokyo, Japan, 1 – 7. (http://www.jma.go.jp/jma/jma-eng/jma-center/nwp/outline2013-nwp/)

Onogi, K., J. Tsutsui, H. Koide, M. Sakamoto, S. Kobayashi, H. Hatsushika, T. Matsumoto, N. Yamazaki, H. Kamahori, K. Takahashi, S. Kadokura, K. Wada, K. Kato, R. Oyama, T. Ose, N. Mannoji and R. Taira 2007: The JRA-25 Reanalysis. J. Meteor. Soc. Japan, 85, 369–432.

Saito, K., T. Fujita, Y. Yamada, J. Ishida, Y. Kumagai, K. Aranami, S. Ohmori, R. Nagasawa, S. Kumagai, C. Muroi, T. Kato, H. Eito and Y. Yamazaki, 2006 : The operational JMA Nonhydrostatic Mesoscale Model. Mon. Wea. Rev., 134, 1266-1298.

Sellers, P. J., Y. Mintz, Y. C. Sud and A. Dalcher, 1986: A simple biosphere model (SiB) for use within general circulation models. J. Atmos. Sci., 43, 505–531.

Shibata, K., M. Deushi, T. Sekiyama and H. Yoshimura, 2005: Development of an MRI Chemical Transport Model for the Study of Stratospheric Chemistry. Papers in Meteorology and Geophysics., 55, 75–119.

Shimbori, T., Y. Aikawa and N. Seino, 2009: Operational implementation of the tephra fall forecast with the JMA mesoscale tracer transport model. CAS/JSC WGNE Res. Activ. Atmos. Oceanic Modell., 39, 5.29–5.30.

Shimokobe, A., 2012: Improvement of the Stratocumulus Parameterization Scheme in JMA’s Operational Global Spectral Model. CAS/JSC WGNE Res. Activ. Atmos. Oceanic Modell., 42, 4.17-4.18.

Takano, I., Y. Aikawa and S. Gotoh, 2007: Improvement of photochemical oxidant information by applying transport model to oxidant forecast. CAS/JSC. WGNE. Res. Activ. Atmos. Oceanic Modell., 37, 5.35–5.36.

Tanaka, T. Y., K. Orito, T. Sekiyama and M. Chiba, 2003: MASINGAR, a global tropospheric aerosol chemical transport model coupled with MRI/JMA98 GCM: Model description. Papers in Meteorology and Geophysics., 53, 119–138.

Usui N., S. Ishizaki, Y. Fujii, H. Tsujino, T. Yasuda, and M. Kamachi, 2006: Meteorological Research Institute multivariate ocean variational estimation (MOVE) system: Some early results. Advances in Space Res., 37, 806-822.

Yasuda, T., Y. Takaya, C. Kobayashi, M. Kamachi, H. Kamahori and T. Ose, 2007: Asian Monsoon Predictability in JMA/MRI Seasonal Forecast System. CLIVAR Exchanges, 43, 18–24.