# JOINT WMO TECHNICAL PROGRESS REPORT ON THE GLOBAL DATA PROCESSING AND FORECASTING SYSTEM AND NUMERICAL WEATHER PREDICTION RESEARCH ACTIVITIES FOR 2015

SLOVAKIA, Slovak Hydrometeorological Institute (SHMU)

## 1.	Summary of highlights

The horizontal and vertical resolution of the lateral boundary data has increased in June 2015 to comply with the driving model (Arpege) resolution increase. High resolution E-suite runs four times/day since September 2015. The internet provider for SHMU was changed (NASES/SWAN - within the GOVNET network) in September 2015. New supercomputer was installed in autumn of 2015, the operational applications are gradually being transferred there.

## 2.	Equipment in use

| supercomputer | 10 nodes of IBM p755 with 4x 8-core 3.3 GHz POWER7, 256 GB RAM per node Management servers: 2x IBM Power750: 1x Power7 6core CPU (3.6GHz), 64 GB RAM |
| --- | --- |
| new HPC | IBM Flex System p460, 12 nodes of 4x Power7+ 8core CPUs (3.6GHz), 256 GB RAM, Red Hat Enterprise Linux |
| archiving | IBM Tivolli Storage 3310 (120 date tapes LTO5 1.5TB) |
| data processing | HP Integrity RX6600; linux PC (EUMETCAST receiving system) |
| visualization | Fault-tolerant Cluster 2xHP Proliant DL 160G6 for IBL Software product VisualWeather |
| telecommunication | Stratus Continuum C 439 (Fault-tolerant system on hardware level) |

## 3.	Data and Products from GTS in use

| SYNOP | SHIP | TEMP | TEMP-SHIP | GRIB | BUFR |
| --- | --- | --- | --- | --- | --- |
| 5500 | 800 | 1800 | 10 | 800 | 7394 |

## Internet, RMDCN and EUMETCAST systems are used for data reception as well (gribs, satellite products). Whole SHMU network was switched to new provider NASES/SWAN within the GOVNET network.

## 4.	Forecasting system

### 4.1	System run schedule and forecast ranges

The limited area NWP model ALADIN (ALADIN/SHMU) is operationally run at SHMU 4 times/day. The schedule of the operational suite is summarized in the table below:

| start time (UTC) | lead time | forecast range |
| --- | --- | --- |
| 02:55 | 00 UTC | +78h |
| 09:45 | 06 UTC | +72h |
| 14:35 | 12 UTC | +72h |
| 21:45 | 18 UTC | +60h |

INCA2 nowcasting system runs hourly 15min after the lead time.

### 4.2	Medium range forecasting system (4-10 days)

The products provided by ECMWF from their medium range global model (both deterministic and EPS forecasts) are used. Horizontal resolution of the surface dataset downloaded to SHMU has been upgraded from 0.25deg to native 0.125deg.

### 4.3	Short-range forecasting system (0-72 hrs)

#### 4.3.1	Data assimilation, objective analysis and initialization

4.3.1.1	In operation

The so-called blending by digital filter technique is used for upper air variables to mix the high-resolution first guess field of local model with the 4DVAR analysis of the driving model ARPEGE. For surface, the optimal interpolation of screen level parameters from SYNOP measurements is used to update the increments of soil variables. The sea surface temperature field is copied from the global model ARPEGE. Analyses are running in full horizontal and vertical resolutions. For both methods a 6h assimilation interval is applied. No initialisation is used.

4.3.1.2	Research performed in this field

All research and development is carried out within ALADIN/ALARO/AROME/HARMONIE and ALADIN/LACE scientific plans. Our focus is on assimilation of radar measurements and surface data assimilation (so-called SURFEX scheme).

#### 4.3.2	Model

4.3.2.1	In operation

| ALADIN | operational | e-suite (future operational) |
| --- | --- | --- |
| model | CY36T1_bf10 | CY40T1_bf05_export |
| horizontal resolution | 9km | 4.5km |
| domain size | 2882x2594km |
| number of grid points | 320 x 288 | 625 x 576 |
| spectral resolution | 106x95 (quadratic) | 312x287 (linear) |
| orography | envelope orography | mean orography (old Z0) |
| number of levels | 37 | 63 |
| time-step | 400s | 180s |
| model dynamics | hydrostatic primitive equations, 2TLSL |
| horizontal diffusion | so-called SLHD (local semiLagrangian HD) |
| coupling model | ARPEGE (long- & short cut off), 3h |
| assimilation | upper air spectral blending with CANARI surface assimilation |
| initialization | none |
| forecast ranges | 72/72/72/60 (a’ 1h) | 78/72/72/60 (a’ 1h) |
| physics | ALARO 3MT, SLHD | ALARO-1 |
| independent variables | spectral T, q, (vorticity, divergence) -> (U, V), Ps |

4.3.2.2	Research performed in this field

All research and development is carried out within ALADIN/ALARO/AROME/HARMONIE and ALADIN/LACE scientific plans. Our focus is on research on the Vertical Finite Elements scheme and physical parametrisations including impact of orographic shading.

#### 4.3.3	Operationally available NWP products

The model parameters (temperature, wind, relative humidity, screen level parameters, other derived and/or diagnostics parameters…) are available on model grid or in lat/lon, on model levels, standard pressure or height levels with hourly output frequency. Various specialized products are produced for downstream applications and internal and external end users.

#### 4.3.4    Operational techniques for application of NWP products

4.3.4.1	In operation

The NWP products are mainly directly visualized or delivered to customers. For some products, the correction of 2m temperature on the orography height is applied. The Kalman filter is used to process the screen level parameters for specific application. Simple interpolation tool and sophisticated algorithm is used to derive automatic text forecasts for the set of predefined points. The area averaged data over river basins are prepared for new hydrological applications within the Flood warning system POVAPSYS.

#### 4.3.5	Ensemble Prediction System

4.3.5.1	In operation

The ECMWF EPS data and ALADIN-LAEF system (that runs at ECMWF) data are operationally used.

4.3.5.2	Research performed in this field

All research and development is carried out within ALADIN/LACE scientific plans. Our focus is on physical perturbations of surface parameters, perturbation of initial conditions of the LAEF system and cycling methods in general including 3DVAR.

#### 4.3.5.3	Operationally available EPS Products

Apart from the ECMWF and ALADIN-LAEF data mentioned above the outputs from PEPS project ("Poor man's" Ensemble Prediction System), run at DWD are available. Simple lagged ensemble system consisting of 5 subsequent ALADIN/SHMU model integrations (with 48 hours overlapping period) is used as well. Ensemble spread and mean is visualized in points epsgrams.

4.4    Nowcasting and Very Short-range Forecasting Systems (0-12 hrs)

4.4.1		   Nowcasting system

4.4.1.1		   In operation

The INCA2 nowcasting system is operationally applied at SHMU, with hourly runs up to 12h. Temperature, dew point temperature, wind filed and wind gust, specific humidity, snow line, zero isotherm are computed using 2mT, 2mRH, 10m wind observations. Also, computation of parameters based on NWCSAF - cloud type, cloud top height, precipitation probabilities - is implemented. The precipitation analyses based on combination of radar measurements and raingauge measurements are performed. Outputs are available on SHMU web pages and in the newly developed HYPOS system dedicated to flood warning.

4.4.1.2   Research performed in this field

Probabilistic nowcasting of precipitation based on motion vectors was tested in frame of diploma thesis.

4.4.2	   Models for Very Short-range Forecasting Systems

none

### 4.5	Specialized numerical predictions

Set of specialized outputs are routinely produced for:

- hydrological models (precipitation forecasts for river catchments - QPF). The HYPOS system (Hydrological Flood Forecasting System) was finalized in frame of the POVAPSYS project aiming to provide online information on current hydrometeorological situation and its evolution with an automatic alert generation. Data from all kinds of NWP systems are netering HYPOS, namely deterministic and probabilistic ALADIN and ECMWF forecasts and INCA nowcasts.

- RODOS model (the Real-time On-line Decision Support system for off-site emergency management in Europe) operated by the Nuclear Regulatory Authority

- CALLPUFF non-steady-state meteorological and air quality modelling system can be fed with ALADIN/SHMU data

- NWCSAF (nowcasting SAF)

- INCA2 nowcasting system

- METRO model for road conditions prediction

#### 4.5.2	Specific Models (as appropriate related to 4.5)

4.5.2.1	In operation

The Canadian road forecast system METRo (Model of the Environment and Temperature of Roads) is running operationally at SHMU. The input parameters are data from RWIS (road weather information system); and screen level temperature and wind speed, precipitation, surface pressure and downward solar and infrared fluxes from ALADIN model. The INCA2 data can be used as well.

### 4.6	Extended range forecasts (ERF) (10 days to 30 days)

none

## 5.	Verification of prognostic products

The outputs from ALADIN/SHMU are regularly verified against SYNOP stations as well as the radio-sounding measurements (point-to-point) in the Central Europe area. Standard scores (BIAS, RMSE, STD) for G, T, WS, WD, RH as well as for screen level parameters are computed. The results are available on intranet. Data are also dispatched to be processed in the frame of the common ALADIN verification project. Local long-term verifications scores (NWP index) are computed for internal purposes.

## 6.	Plans for the future (next 4 years)

### 6.1	Development of the GDPFS

6.1.1  Major changes in the operational DPFS which are expected in the next year

Full operational status of ALADIN on new HPC doubling its current horizontal and vertical resolution and upgrading model version to the newest possible code release. Transfer of all consequent operational applications to the new hpc. Full utilisation of the upgraded dense local observation and monitoring network that is built within the POVAPSYS project.

6.1.2  Major changes in the operational DPFS which are envisaged within the next 4 years

Operational implementation of the 3DVAR data assimilation to fully benefit from the upgraded monitoring network. Implementation of new surface scheme (SURFEX). Testing the convection-permitting model AROME. Consolidation of the nowcasting tools.

### 6.2	Planned research Activities in NWP, Nowcasting, Long-range Forecasting and Specialized Numerical Predictions

6.2.1 Planned Research Activities in NWP

SHMU will further participate in the R&D work on ALADIN/ALARO/AROME/HARMONIE NWP systems.

6.2.2 Planned Research Activities in Nowcasting

The probabilistic precipitation nowcasting. New diagnostic tools to nowcast extreme weather events.

6.2.3 Planned Research Activities in Long-range Forecasting

6.2.4 Planned Research Activities in Specialized Numerical Predictions

## 7. 	References

www.shmu.sk

www.rclace.eu

www.cnrm.meteo.fr/aladin/