DANISH  METEOROLOGICAL  INSTITUTE

Report 2008

- Summary of highlights

The NEC-SX6 computer system was replaced by Cray XT4 and XT5 systems.

All operational numerical weather prediction models and models related to air

pollution and environmental applications at the Danish Meteorological Institute

were ported to the new supercomputer systems. The powerful XT5 computer

became operational in December 2008.  - High resolution non-hydrostatic

models were tested on a daily basis for two model domains covering

Denmark and southern Greenland respectively. A preoperational short range

ensemble prediction system based on the HIRLAM numerical model has been

established. A special version of the HIRLAM (‘Enviro’-HIRLAM) was developed

further for environmental purposes.

- Equipment in use

The new supercomputer systems consists of Cray XT4 and Cray XT5. The XT5

is the main installation and has AMD Opteron Quad-Core microprocessors. It is

divided into two identical systems. Each system contains 256 compute nodes

(8 cores), in total 4096 cores. The peak performance is 38 Tflops, the memory

amounts to  8.2 TBytes and the disk capacity equals 110 Tbytes.

The observation decoding is a modified version of a corresponding system at

ECMWF. This system is run on a double system of Linux servers ( “decode1”  and

“decode2”)

DMI makes use of the product  TSM HSM for data archiving. The HSM system is

installed on an IBM power 52A machine with 11 TB disk cache and an IBM

3584 tape library, which can contain 1600 tapes.

Every tape has a storage capacity of  800 GB, implying that the entire storage

capacity is 1280 TB.

- Data and Products from GTS in use

TEMP, SYNOP, SYNOP SHIP, BUOY, AIREP, AMDAR, ACARS from GTS.

ATOVS AMSU-A, Meteosat-8/9 AMV  from EUMETCast.

QuikScat from ftp-server.

- Forecasting system

4.3  Short range forecasting system

Different versions of the HIRLAM forecasting system are used operationally at

DMI. The main model areas are shown in the Figure. The big limited area T15

(0.15 ° horizontal resolution, 40 model levels) is run on an area comprising the

European-Atlantic area including also the North Pole.  (forecast length 60 hours).

Model S05 ( 0.05 º,  40 levels,  model area covering Northwestern Europe, see

figure). Forecast length: 54 hours.

Model G05 ( 0.05 º, 40 levels, model area covering Greenland). Forecast

length: 36 hours.

All models are run 4 times a day (00 UTC , 06 UTC, 12 UTC, 18 UTC)

    - Data-assimilation and initialization.

Cut-off time = 1h  40 min. - T15 is run with the HIRLAM 3D-VAR and FGAT

Data-assimilation, with lateral boundaries from the ECMWF global model. The data-

assimilation is improved by delayed-mode reanalyses using ECMWF data and

HIRLAM analyses.  – The S05  and G05 models are starting from interpolated

fields based on  T15, and all models are initialized by an incremental Digital Filter

method.   – Experiments are currently performed with regard to the assimilation of

new data into the operational model setups, e.g., assimilation of  AMSU-B/MHS

from NOAA18 and Metop-A, and assimilation of  surface GPS-data estimating

vertically integrated humidity.

4.3.2  Model

HIRLAM forecasting system ( See http://www.hirlam.org ). Some specific DMI features have been implemented which are described in special reports, e.g. DMI reports.

Surface analysis based on HIRLAM  ISBA analysis. SST and Ice data input based on ECMWF data and sst/ice  SAF  gridded data.

4.3.2.1 In operation

Model physics similar to HIRLAM version 7.2

4.3.2.2 Research performed in this field

Research linked to the international HIRLAM-A project.

4.3.3 Operationally available NWP products

GRIB files produced by the operational HIRLAM model setups.

4.3.5   Ensemble prediction system

4.3.5.2  Research performed in this field

Research is linked with the international HIRLAM-A project – Current emphasis on studies with ensembles based on physics perturbations. A preoperational short range ensemble prediction system based on HIRLAM has been established in late 2008. The horizontal grid mesh of each ensemble member is 5 km and the number of ensemble members equals 25. The ensemble describes the effect of initial state perturbations, stochastic physics and two different convection schemes. The system will be further developed and verified in 2009.

4.3.5.3 Operationally available EPS products

Emphasis on products received from ECMWF.

4.4  Nowcasting and Very Short-range Forecasting Systems (0-6hrs)

4.4.2 Models for Very Short-range Forecasting Systems

4.4.2.1  In operation

Forecasts with special version of  HIRLAM used for road-weather prediction.

4.4.2.2  Research performed in this field

Data-assimilation methods (nudging) used in the context of road-weather

modelling and very short range atmospheric predictions.

4.5 Specialized numerical predictions

4.5.2    Specific models (as appropriate related to 4.5)

4.5.2.1    In operation

Danish Emergency Response Model of the Atmosphere (DERMA) – Lagrangian

regional atmospheric dispersion model for nuclear, chemical and veterinary

emergency preparedness.

Danish Atmospheric Chemistry Forecasting System (DACFOS) – Lagrangian

regional chemistry-transport model for ground-level smog and ozone forecasting
   Multi-trajectory Ordinary Differential Equations Numerical Box model (MOON) –

Lagrangian regional chemistry-transport model for ground-level smog and ozone

forecasting.

Risø Mesoscale Puff model system (RIMPUFF) - Lagrangian mesoscale atmospheric

dispersion model for veterinary emergency preparedness.

2- or 3-d trajectory model – all purpose

Hir-Pol - statistical pollen forecasting system using DMI-HIRLAM-data

4.5.2.2 Research performed in this field

Chemistry Aerosol Cloud (CAC) model - used for regional air quality forecasting

within the GEMS EU project.
   Enviro-HIRLAM - integrated coupled air pollution/meteorology model including

feed-back effects, also used for birch pollen dispersion studies.
   Urbanisation effects: Microscale Model for Urban Environment (M2UE) – an

obstacle resolving CFD model.

Products from HIRLAM are being developed for real time prediction of

the available energy for wind mills and solar energy installations.

5.  Verification of prognostic products

The NWP models applied at DMI are quality controlled by verification against

observations in quarterly internal reports available by special request. Obs-

verification in terms of root mean square error/standard deviation and bias is done

separately for surface observations in Denmark, the Faroe Islands, Greenland – and

for the whole of Europe against a common list of surface and radiosonde observations

agreed upon among European countries (EWGLAM)

Verified surface observations are:

mean sea level pressure, accumulated precipitation, temperature, relative humidity

and visibility at 2 meter height and wind velocity at 10 meter height. Special

verification products (including verification against hourly observations and Weibull

distributions for wind at coastal stations in Denmark) are available for temperature

and relative humidity at 2 meter and for wind at 10 meter.

Verification results for accumulated precipitation and visibility are presented in

contingency tables. In addition maps of predicted accumulated precipitation versus

the corresponding observed precipitation for Denmark are presented monthly.

Verified upper level parameters are:

geopotential height, wind velocity, temperature and relative humidity at standard

pressure levels. All the variables are verified at 12 hour intervals from 0 to 48 hour

forecast lead time. In addition geopotential height, temperature and wind are also

verified 6 hourly for pressure levels 850, 500 and 250 hPa.

6.  Plans for the future (next 4 years)

  - Development of the GDPFS

New HIRLAM model versions will become operational in May 2009 with the

following characteristics:

a) The horizontal grid mesh size of  the model domain S05, which is run for northern Europe, is reduced from 5 km (0.05˚ ) to 3 km (0.03 ˚)

b)  Increased  domain for the 5 km grid mesh Greenland model, and increase of forecast length from 36 h to 48 h.

- Preoperational runs of non-hydrostatic Arome  (based of IFS framework) for area

around Denmark (2.5 km grid mesh) and for southern Greenland ( 2 km grid mesh)

6.2  Planned Research Activities in NWP,  Nowcasting and Long-range

Forecasting.

6.2.1 Planned Research activities in NWP and very short range forecasts.

New data-assimilation techniques related to nowcasting and very short range

forecasting will be studied. This involves ‘rapid update cycles’. The goal is to

obtain a maximum synergy between different observational data available, e.g.

conventional data, radar data, satellite data in general, surface based GPS-data and

possibly other data. The performance of  high resolution models, both based on

HIRLAM and on IFS/Harmonie, will be studied. Short range ensemble prediction

systems will be developed for operational use. The Enviro-HIRLAM used for

on-line coupling with air pollution and chemistry effects will be further developed..

6.2.3  Planned Research activities in Long-Range Forecasting.

Statistically significant correlations can be found between the stratospheric circulation

and surface weather parameters when the stratosphere leads with 5-60 days. At DMI

it is investigated to which extent this stratosphere-troposphere coupling is already

represented in ECMWFs new dynamical seasonal prediction model (system 3). With

this system re-forecasts are available for 25 years starting in 1980. Comparisons are

made with results obtained with a simple linear statistical forecast model.

7   References

Publications for 2008 are listed from the DMI web page:  www.dmi.dk  (

“VIDEN” ( “DMI-publikationer”.