# JOINT WMO TECHNICAL PROGRESS REPORT

# ON THE GLOBAL DATA PROCESSING AND FORECASTING SYSTEM AND NUMERICAL WEATHER PREDICTION

# RESEARCH ACTIVITIES FOR “[YEAR]”

## 1.	Summary of highlights

Weather Research and forecasting model (WRF) became a part of our operational NWP system, and automatic verification package used also.

## 2.	Equipment in use

a. For Computations and data base :

i. The IBM Mainframe with central processor unit with:

o Power 80 MIPS

o Processor based on z-architecture , 64bit

o Dynamic I/O reconfigurations management for peripherals

o IBM operating system(VSE/ESA and OS/390)

o Communicate with the already existing computers in the centre of the existing databases of the various units of EMA (According to site survey)

ii. Storage unit:

o 3 ESCON channels and one FICON channel.

o The capacity at least 400 GB useable, raid-protected, with the scalability can be extended to one TB.

o Support parallel access volume.

o Support multiple allegiances

b. For Telecommunication System (AMSS):-

i. Two servers, one live & one back-up, model IBM X series 345.

ii. 3 Supervisory, model IBM Think Centre.

c. For The Numerical Weather Prediction

The Specification (H/w)for Sun Cluster System

Main Node QTY (1):

  - Processor:	4 CPU cores with  1 MB cache per core based on AMD technology.

  - CPU Freq:			2.4 GHz

  - Memory:		4 GB per CPU core DDR2 667 MHz ECC

  - Ethernet:			4 Gigabit Ethernet interface

  - Management:	IPMI 2.0 service processor with dedicated Ethernet port

  - Remote management:	power, keyboard, video, mouse and media

  - Remote access:	using web interface over SSL or command line over SSH

  - Internal storage:	2 x 73 GB

  - USB:	4 USB 2.0 ports

  - Slots:	4 internal PCI-E slots, 1 PCI-X

  - Interfaces:	infiniband adapter, 2 FC HBA for the storage

  - Availability:	Redundant power supply and fans

  - From factor:	2 U preferred

  - Compute nodes: QTY (11):

  - Processor:	4 CPU cores with at least 1 MB cache per core based on AMD technology.

  - Freq:				2.6 GHz

  - Memory:		2 GB per CPU core DDR2 667 MHz ECC up to 16 GB per core

  - Ethernet:			4 Gigabit Ethernet interfaces

  - Management:	IPMI 2.0 service processor with dedicated Ethernet port

  - Remote management:	power, keyboard, video, mouse and media

  - Remote access:	using web interface over SSL or command line over SSH

  - Internal storage:	2 x 250 GB

  - USB:	6 USB 2.0 ports

  - Serial:	1 DB9 ports

  - Slots:	Two 8 lane 64-bit PCI-Express

  - Interfaces:	PCI-Express infini band interface supporting 20 GB/s full duplex bandwidth with copper HSSD

  - From factor:	1 U preferred

Storage QTY (1):

- Technology:	4 GB Fibre channel

- Raid levels:			0,1,3,5, 1+0

- Battery cache:		72 hours min

- Cache:			2 GB

- Controllers:	2

- Disks:	5 x 500 GB SATA 7200 RPM

- Max capacity:	32 TB

- Redundancy:	for power supply and cooling fans

i. One Compaq server with 4 processors with RISC architecture

o 4GBSDRAM

o 510GB total internal storage capacity

ii. One Compaq server with 2 processors with RISC architecture

o 2GBSDRAM

o 120GB total internal storage capacity.

iii. Two IBM compatible PCs

o 2.8GHZ

o 100GB total internal storage capacity

iv. Two IBM compatible PCs

o 1.8GHZ

o 40GB total internal storage capacity

## Data and Products from GTS in use

| WMO observation data | SYNOP, TEMP, METAR, AIREP |
| --- | --- |
| NWP products | ECMWF, |
| Meteorological image data | Satellite images data. |

## 4.	Forecasting system

### 4.1	System run schedule and forecast ranges

| System | Base Time | Approximate start time (UTC) | Forecast Availability (UTC) | Forecast Range from base date (hrs) | For the sake of |
| --- | --- | --- | --- | --- | --- |
| WS-ETA | 0000 | 0600 | 0900 | 120 | Short Range forecast and R&D |
|  | 1200 | 1800 | 2100 |  |  |
| Egypt –ETA | 0000 | 0600 | 1100 | 240 | Medium Range Forecast and R&D |
|  | 1200 | 1800 | 2300 |  |  |
| MM5 | 0000 | 0900 | 1300 | 120 | Medium Range |
|  | 1200 | 2100 | 0100 |  |  |
| WRF(NMM) | 0000 | 0700 | 1230 | 168 | Medium Range |
|  | 1200 | 2100 | 0200 | 168 | Medium Range |
| WAM | 0000 | 0900 | 0920 | 120 | Specialized Numerical Prediction and R&D. |
|  | 1200 | 2100 | 2120 |  |  |

c. Model Variables:-

i. The operational prediction model in use is the regional ETA Model 
             with terrain representation basic equations & primitive equations.

o Independent: Longitude, Latitude, ETA, time

o Prognostic variables: Temperature, wind components, Specific humidity, turbulent kinetic Energy, soil moisture, snow depth, Surface potential temperature.

o Diagnostic variable: Precipitation, vertical velocity, turbulent exchange coefficients.

o Topographic data set: Mean orography, land sea mask.

o Assimilation cycle: 0000, 0006, 0012, 1800UTC,

ii. A new non-hydrostatic forecasting system of, at least, 36 levels Sigma Coordinates Forecast for 48 h.

o Basic equations: primitive equations system.

o Dependent variables: T, U, V, Q, P.

o Integration domain 25E to 37E 22N to 35 N

o Horizontal resolution. 33km

Vertical resolution: 36levels.

iii. Meso-scale Model ( MM5)- Non-hydrostatic

o Additional equations for prognostic 3D vertical velocity and perturbation pressure.

o No equations for prognostic surface pressure diagnostic pressure and diagnostic omega integrations.

o 24 categories for vegetation and physical properties.

o Projections (dx=dy) (Paler-Lambert and Macerator).

o Data Required to run:

• Topography and land use

• Cribbed Analyses (Regional), Wind, Heights, Temp.

• Snow cover, SST, and RH for 18 levels with top at 100hPa.

o Nesting (one and two ways).

o Vertical interpolation from pressure levels to sigma coordinate system.

o Resolution three nested 63,21,7 km.

5. Numerical Weather Prediction Products:

- The geopotential height at the standard level and mean sea level pressure.

- Horizontal wind components (U.V).

- Temperature (T).

- Specific Humidity (q).

- Surface pressure (Ps).

- Soil temperature.

- Soil moisture content.

- Surface temperature.

- Connective precipitation.

- Layer cloud amount.

- Vertical velocity.

- Thunderstorm and sandstorm