# JOINT WMO TECHNICAL PROGRESS REPORT ON THE GLOBAL DATA PROCESSING AND FORECASTING SYSTEM AND NUMERICAL WEATHER PREDICTION RESEARCH ACTIVITIES FOR 2008

Hong Kong Observatory, Hong Kong, China

## 1.	Summary of highlights

- The Local Analysis and Prediction System (LAPS) of the Hong Kong Observatory was upgraded to produce hourly analysis down to 500 m horizontal resolution (see 4.3.1.1(iii)).

- NHM was enhanced with (i) a new turbulent closure model in the planetary boundary layer scheme; (ii) a new partial condensation scheme and; (iii) an improved short wave radiation scheme (see 4.3.2.1(ii)).

- A multi-model ensemble based NWP guidance was implemented to facilitate the preparation of site-specific forecasts for the 2008 Olympic equestrian events (see 4.3.4.1 (vi)).

- A graphical rainfall nowcast product with GIS information based on SWIRLS was launched on the Internet (see 4.4.1.1).

- SWIRLS-2, the second-generation nowcasting system of HKO, was successfully adapted and operated during the 2008 Beijing Olympics (see 4.4.1.2).

- Seasonal temperature and rainfall forecasts for Hong Kong and its neighbouring areas produced by a suite of climate models were made available to the public (see 4.7.1).

## 2.	Equipment in use

The current computer systems at the Hong Kong Observatory (HKO) with their major characteristics are listed below:

| Machine | Quantity | Peak performance | No. of CPU | Memory | Year of Installation |
| --- | --- | --- | --- | --- | --- |
| Galactic SuperBlade | 1 | 460.8 GFLOPS | 64 | 168 GB | 2006 |
| IBM p630 cluster | 1 | 96.0 GFLOPS | 20 | 40 GB | 2004 |
| IBM p690 | 1 | 140.8 GFLOPS | 32 | 48 GB | 2003 |
| IBM SP | 1 | 66.0 GFLOPS | 44 | 31 GB | 2001 |

The Galactic SuperBlade server cluster is used to support the R&D of nowcasting and NWP systems, including the Non-Hydrostatic Model (NHM), 3DVAR and 4DVAR Data Assimilation System (DAS) and Weather Research and Forecasting (WRF) model.

The IBM p630 server cluster is used to provide backup computing resources during contingencies, to operate a global-regional climate model suite and to support development of NWP systems.

The IBM p690 server is used to support the operation of the HKO nowcasting system, the trial operation of NHM and the Rainstorm Analysis and Prediction Integrated Data-processing System (RAPIDS) as well as their related R&D activities.

The IBM SP cluster is used to run the analysis and forecast system of the Operational Regional Spectral Model (ORSM), conduct various data acquisition and processing activities in support of operations of the forecasting office.  Besides, it provides a platform for the trial operations of the Local Analysis and Prediction System (LAPS).

The CRAY SV1-1A, on which the ORSM was previously run, was decommissioned in November 2008.

## 3.	Data and Products from GTS in use

The approximate number of bulletins of observations received from GTS on a typical day in 2008 is given below:

| SYNOP/SHIP | 17,000 |
| --- | --- |
| TEMP/PILOT | 800 |
| AIREP | 600 |
| AMDAR | 4,500 |
| SATEM/SATOB | 200 |
| TOVS/ATOVS | 1,200 |

Other observations, such as RADOB, are also gathered through the GTS during the passage of tropical cyclones.

The approximate number of bulletins of NWP products received from GTS and through the Internet on a typical day in 2008 is given below:

Centre								     	Type	Number

Deutscher Wetterdienst (DWD)						GRIB	  8,000

European Centre for Medium Range Weather Forecasts (ECMWF)		GRIB	  4,000

Japan Meteorological Agency (JMA)					GRIB	  5,500

US National Centers for Environmental Prediction	 (NCEP)		GRIB	18,500

United Kingdom Meteorological Office (UKMO)				GRIB	  2,000

Besides, data from both ECMWF and JMA Ensemble Prediction System (EPS) for grid points in the vicinity of Hong Kong are also acquired through the Internet and/or GTS.

## 4.	Forecasting system

### 4.1	System run schedule and forecast ranges

ORSM operates at 20 km and 60 km resolutions for an inner and an outer domain respectively.  The model was originally developed by Japan Meteorological Agency (JMA) and was adapted for short-range weather forecasting in Hong Kong.  The 60-km model is run in a 6-hourly analysis-forecast cycle with boundary data extracted from JMA’s Global Spectral Model (GSM) forecasts. The 20-km model is run in a 3-hourly analysis-forecast cycle and is one-way nested into the 60-km model.

The forecast range of the 60-km ORSM and 20-km ORSM are 72 hours and 42 hours respectively.  The outer 60-km ORSM is run 4 times a day for the area 9 (S – 59 (N, 65 – 152 (E based on 00, 06, 12 and 18 UTC analysis data, with an observation cut-off time of 3 hours.  The inner 20-km ORSM is run 8 times a day for the area 10 – 35 (N, 100 – 128 (E based on 00, 03, 06, 09, 12, 15, 18 and 21 UTC analyses, with an observation cut-off time of 2 hours.

NHM (Saito et al. 2006) operates on an hourly basis on IBM p690 server at 5 km horizontal resolution.  Model computation with initial time at T hour is started at T+50 minutes.  The domain covers the area 19.5-25.0 oN, 111.2 – 117.1 oE and 12 hour forecasts are produced to give model guidance on severe weather and to support the operation of RAPIDS. The initial field of NHM is from the 20-km ORSM while the mixing ratios of the hydrometeors in the model cloud processes are initialised by moisture analysis output from LAPS (Albers 1995 and Albers et al. 1996) at 5 km horizontal resolution.  The model boundary conditions are extracted from 20-km ORSM.

### 4.2	Medium range forecasting system (4-10 days)

Operationally, forecasts up to 7 days ahead are formulated by forecasters based on a subjective assessment of the prognostic forecast products from ECMWF, JMA, UKMO and NCEP.  Besides the above deterministic NWP models, ECMWF and JMA Ensemble Prediction System (EPS) data sets for four grid points nearest to Hong Kong are also acquired for forecasters’ reference.

An automated medium-range forecasting system (AMFS) provides objective forecast guidance on local winds, state of sky, weather, as well as temperature and relative humidity ranges up to 7 days ahead.  AMFS is run twice a day based on the 00- and 12-UTC model outputs primarily from JMA and ECMWF, supplemented with those from ORSM and the global model of NCEP.  Besides the use of direct model outputs, key post-processing techniques employed in AMFS include linear regression, Kalman–filtering and poor-man ensemble averaging.  The AMFS also incorporates some of the local forecasting rules used by forecasters.

An extreme wind forecast product alerts the forecasters of the possibility of occurrence of high winds in Hong Kong.  The product makes reference to the ensemble maxima of the ECMWF EPS 10-metre wind data from the current and latest model runs.  The possibility of high winds is assessed by tracking the highest ensemble maximum among all valid forecasts.  The forecast information is presented to the forecasters in tabular form via an intranet web page.

#### 4.3	Short-range forecasting system (0-72 hrs)

#### 4.3.1	Data assimilation, objective analysis and initialization

4.3.1.1	In operation

- ORSM

Meteorological data assimilated by the analysis scheme of ORSM are as follows:

    - From GTS

SYNOP, SHIP		surface data and ship data

TEMP, PILOT 		radiosonde and pilot data

AIREP, AMDAR		aircraft data

SATEM		satellite thickness data

TOVS, ATOVS		virtual temperature profiles

SATOB		satellite wind data

    - FY-2C geostationary satellite of CMA

IR1 brightness temperature data

    - From NCEP data server

Daily sea surface temperature analysis at 1-degree resolution

    - Through regional data exchange

Data from automatic weather stations over southern China

    - Local data

Tropical cyclone bogus data during tropical cyclone situations

Automatic weather station data

Wind profiler data

Doppler weather radar data

A three-dimensional multivariate optimal interpolation is performed four times a day based on 00, 06, 12 and 18 UTC data for the 60-km outer domain.  For the inner domain, the same analysis scheme is performed 8 times a day based on 00, 03, 06, 09, 12, 15, 18, and 21 UTC.  All analyses are applied to the 40 model levels.  The first guess fields of the model analyses are provided by their respective latest forecasts.

The hourly rainfall information, derived from the real-time calibration of radar reflectivity with rain gauge data as well as from the FY-2C IR1 brightness temperature data, is incorporated into the model through a physical initialization process.  In this process, the moisture of the initial field (between the lifting condensation level and the cloud top inferred from the cloud top temperature) at the point where rain is observed is adjusted to allow precipitation process to be switched on. The heating rate of the precipitation process is also adjusted to correspond to the rainfall amount observed. Rainfall information in the past hour and three hours are used in the outer and inner models’ analysis respectively.   A nonlinear normal mode initialization is performed before the forecast model is run.

- NHM

The initial condition of NHM is obtained from interpolation of 20-km ORSM forecast output to the model grid at 5-km resolution.

The mixing ratios of hydrometeors (cloud liquid water, cloud ice, rain water, snow and graupel) on model levels in the initial condition are interpolated vertically from LAPS analysis on pressure levels.

- LAPS

LAPS was originally developed by the Forecast Applications Branch in NOAA. The data assimilation system of LAPS is configured to ingest the 20-km ORSM and 5-km NHM outputs as background field.  Hourly analyses are produced for 3-dimensional analysis of wind, temperature, humidity at 10 km, 5 km, 1.5 km and 500 m resolutions.  LAPS products are used in supporting the operation of lightning nowcast in SWIRLS and the initialization of specific humidity of hydrometeors in 5-km NHM.

The objective analysis in LAPS is based on successive correction augmented by a moisture balance computation using three-dimensional variational technique.  Observation data within one-hour assimilation time-window are ingested in LAPS.  They include conventional surface observations (SYNOP, METAR and SHIP), upper level data (TEMP, PILOT, AMDAR and AIREP) and automatic weather stations in Hong Kong and Guangdong.  Remote sensing observations like radar reflectivity and Doppler velocity from the two local weather radars, upper level winds from wind profiler network, FY-2C albedo and IR brightness temperature are also ingested.  LAPS can also assimilate the QuikSCAT sea surface winds, satellite sounding (SATEM and ATOVS), cloud motion winds (SATOB), GPS precipitable water and TREC (Tracking Radar Echoes by Correlation) motion vectors obtained from the SWIRLS nowcasting system.   The data cut-off time for hourly LAPS analysis at hour T for all the domains are set at about T+35 minutes.

4.3.1.2	Research performed in this field

LAPS has also been adapted for mesoscale data assimilation in supporting nowcast operation in WMO/WWRP B08FDP (Beijing 2008 Forecast Demonstration Project) to assimilate AWS, radar and satellite data over the Beijing area.  Analysed profiles of wind, temperature and moisture over the ‘rain’ grids, identified by the reflectivity exceeding a prescribed threshold, were generated for ingestion into the 3DVAR system of 5-km NHM in the Beijing domain.

#### 4.3.2	Model

4.3.2.1	In operation

- ORSM

The characteristics of ORSM are shown as follows:

| Governing equations | Primitive hydrostatic equations |
| --- | --- |
| Prognostic variables | Natural log of surface pressure, horizontal wind components, virtual temperature, specific humidity |
| Horizontal coordinate, resolution, and number of grid points | Mercator projection, 20 km resolution for the inner model and 60 km for the outer, 151x145 grid points |
| Vertical coordinate and grid configuration | Sigma-P hybrid coordinate, 40 levels with model top at 10 hPa |
| Initialization | Non-linear normal mode initialization |
| Radiation scheme | Short wave and long wave (Sugi et al.,1990). Calculated every hour |
| Moisture processes |  |
| Cumulus convection | Arakawa-Schubert (1974) |
| Mid-level convection | Moist convective adjustment proposed by Benwell and Bushby (1970) and Gadd and Keers (1970) |
| Large-scale condensation | Included |
| Grid-scale evaporation and Condensation | Included |
| Planetary boundary layer | Scheme proposed by Troen and Mahrt (1986) in which non-local specification of turbulent diffusion and counter-gradient transport in unstable boundary layer are considered |
| Surface | 4-layer soil model |
|  | Daily sea-surface temperature analysis (fixed in forecast) |
|  | Climatological snow and sea ice distribution |
|  | Climatological evaporation rate, roughness length and albedo |
| Numerical technique | Horizontal: Double Fourier |
|  | Vertical : Finite difference |
|  | Time: Euler semi-implicit time integration |
| Topography | Envelope topography, derived from 30-second latitude/longitude resolution grid point topography data |
| Horizontal diffusion | Linear, second-order Laplacian |
| Boundary conditions | For the outer model, 6-hourly boundary data including mean sea level pressure, wind components, temperature and dew point depression at 16 pressure levels (1000, 925, 850, 700, 500, 400, 300, 250, 200, 150, 100, 70, 50, 30, 20, 10 hPa ) and the surface, are provided by JMA’s GSM. For the inner model, hourly boundary data are provided by the outer 60km model |

For further details on ORSM, please see JMA (2002).

- NHM

A general description of NHM is summarized as follows:

| Governing Equations | Fully compressible non-hydrostatic equations |
| --- | --- |
| Prognostic variables | Momentum in x, y and z directions, pressure, potential temperature, turbulent kinetic energy, mixing ratio of water vapour, cloud water, cloud ice, rain water, snow and graupel |
| Numerical technique | Finite difference method on the Arakawa-C type staggered coordinate grid system. Fourth-order horizontal finite difference operator in flux form with modified advection treatment for improved monotonicity |
| Horizontal coordinates, resolution, and number of grid points | Mercator projection, 5 km resolution, 121x121 grid points |
| Vertical coordinates and grid configuration | Terrain following height coordinates, 45 levels on Lorenz grid with model top at 27 km |
| Time integration and time step | Horizontal explicit and vertical implicit (HE-VI) with acoustic filter, 24 seconds |
| Turbulent closure and planetary boundary layer process | Mellor-Yamada-Nakanishi-Niino Level 3 (MYNN-3) (Nakanishi and Niino, 2004) with partial condensation scheme and implicit vertical turbulent solver: prognostic variables including TKE, covariance and correlation of perturbation liquid water potential temperature and liquid water content; Mixing length determined by length scales of eddies near surface, vertical structure of TKE and buoyancy effects; Height of PBL calculated from virtual potential temperature profile. |
| Precipitation processes | Three-ice bulk cloud microphysics + Kain-Fritsch convective parameterization |
| Diffusion processes | Linear, fourth-order Laplacian with non-linear damper. Targeted moisture diffusion applied to grid-points with excessive updrafts |
| Radiation processes | Long wave radiation process follows Kitagawa (2000); Short wave radiation process using Yabu et al. (2005); Prognostic surface temperature included; cloud fraction determined from the partial condensation scheme. |
| Upper boundary condition | Fixed wall with Rayleigh damping |
| Lateral boundary condition | Hourly boundary conditions from 20-km ORSM forecasts |
| Topography and land-surface characteristics | USGS global 30 second topography (GTOPO30) and (Global Land Cover Characterization) (GLCC) |

Further details on NHM can be found in Saito et al. (2006).

4.3.2.2	Research performed in this field

Numerical simulation of a fog episode in Hong Kong was conducted using NHM equipped with the new turbulent closure model (MYNN-3) and the partial condensation scheme (Wong and Lai, 2008).  It was demonstrated that the new schemes could adequately predict the formation or condensation of cloud liquid water near the surface and hence the distribution of the low clouds or fog.

A new scheme of bulk transfer coefficient and roughness length in NHM was developed in an attempt to reduce the drag effect over the sea surface during high wind conditions.  Numerical experiments conducted on Typhoon Hagupit (0814) suggested that the new scheme could lead to improved simulation of the wind structure and precipitation pattern of the storm.

#### Operationally available NWP products

- ORSM

The products of the 60-km ORSM include sea level pressure / geopotential heights, wind, temperature, dew point depression at 15 pressure levels (1000, 925, 850, 700, 500, 400, 300, 250, 200, 100, 70, 50, 30, 20, 10 hPa) and the surface as well as accumulated rainfall at 3-hourly intervals.  For the inner 20-km domain, the forecast elements are the same as above but the products are generated at hourly intervals.

- NHM

Hourly prognostic charts on surface (hourly accumulated rainfall with sea level pressure and wind) and upper levels (975, 925, 850, 700, 500, 200 hPa), time series and time cross section for grid points at the HKO and near the Hong Kong International Airport are generated.

The 60-km ORSM TC track forecast guidance is routinely generated and disseminated via the GTS.  The guidance is issued and updated twice a day based on the 00 and 12 UTC model runs whenever a TC reaching tropical depression strength appears in the area of responsibility of the HKO (10-30 oN, 105-125 oE).  The information provided in the guidance includes forecast TC positions and intensity changes at 6-hourly intervals out to 72 hours.  The HKO analysed TC warning position and intensity at 00 and 12 UTC are also included as initial values.

The following 60-km ORSM products in GRIB format are made available twice a day on the HKO’s Server for International Exchange for access by registered national meteorological services.

Table 4.3.3.1	List of 60-km ORSM model products on the HKO’s Server for International Exchange

| Level | Content | Initial Time | Forecast Hours | Area | Resolution |
| --- | --- | --- | --- | --- | --- |
| Surface | Sea level pressure | 00 and 12 UTC | 12, 24, 36, 48, 60 and 72 | 5-45 (N, 90-140 (E | 0.5x0.5 Degree |
|  | Temperature |  |  |  |  |
|  | Relative humidity |  |  |  |  |
|  | Wind |  |  |  |  |
| 925, 850, 700, 500 and 400hPa | Geopotential height |  |  |  |  |
|  | Temperature |  |  |  |  |
|  | Relative humidity |  |  |  |  |
|  | Wind |  |  |  |  |
| 300, 250, 200, 150 and 100hPa | Geopotential height |  |  |  |  |
|  | Temperature |  |  |  |  |
|  | Wind |  |  |  |  |

Under a WMO pilot project in Region II, the HKO has been generating city-specific NWP products based on 60-km ORSM in the form of time series of weather parameters for reference by Members in the Region since 2006.  The products, based on the direct model output of 60-km ORSM at the model land grid nearest to the corresponding cities, are made available on a password-protected web site maintained by the HKO.  By the end of 2008, forecasts of 121 cities are being provided by the HKO.  To facilitate the project participants’ adaptation of the model outputs for their own specific applications, a software application in the form of spreadsheet was developed to assist the users in carrying out post-processing and verification of the NWP products.

Table 4.3.3.2	Forecast of meteorological elements provided in the city-specific forecast time series

| Content | Initial Time | Forecast Hours | Display format |
| --- | --- | --- | --- |
| Sea level pressure | 00 and 12 UTC | 3-hourly intervals from 3 to 72 hours | In both graphical and tabulated data formats |
| Surface air temperature |  |  |  |
| Surface dew point temperature |  |  |  |
| Surface relative humidity |  |  |  |
| Surface wind direction and speed |  |  |  |
| Total cloud amount |  |  |  |
| 3-hourly precipitation |  |  |  |

Selected model products derived from ORSM are also disseminated in graphical format via the Internet for public consumption (URL:  http://www.weather.gov.hk/nwp/nwpe.htm).

Table 4.3.3.3	60-km ORSM-based model forecast charts available on the Internet

| Level | Content | Initial Time | Forecast Hours | Area |
| --- | --- | --- | --- | --- |
| Surface | Weather depicting fine, cloudy and rain areas | 00 and 12 UTC | 12, 24, 36, 48, 60 and 72 | 8.5-41.7 (N, 92.1-143.8 (E |
|  | Air temperature |  | 00, 12, 24, 36, 48, 60 and 72 |  |
|  | Sea level pressure |  |  |  |
|  | Wind |  |  |  |
| 850hPa | Wind |  |  |  |
|  | Relative vorticity and streamline |  |  |  |
| 700hPa | Wind |  |  |  |
|  | Relative humidity and streamline |  |  |  |
| 500hPa | Wind |  |  |  |
|  | Geopotential height |  |  |  |
| 200hPa | Wind |  |  |  |
|  | Jet stream and streamline |  |  |  |

#### 4.3.4    Operational techniques for application of NWP products

4.3.4.1	In operation

- ORSM

Local text forecasts based on ORSM prognostic data with warnings of thunderstorms and rainstorms are generated automatically.  ORSM model outputs are also used to derive automatic wind forecasts for preparation of forecast bulletins for the South China Coastal Waters.  Post-processing techniques, including Kalman filter and linear regression, are employed to adjust the temperature forecasts, including the daily minimum and maximum temperature forecasts in Hong Kong.

A weather map algorithm is employed to produce hourly weather map (fine and cloudy areas, accumulated rainfall contours) based on ORSM prognostic data.  Rainstorm risk maps based on model-forecast rainfall rates are compiled from the latest five 20-km ORSM runs, akin to the ensemble approach.  Near real-time rainfall verification results are provided to the forecasters.

TC track forecasts from consecutive runs of 60-km ORSM and 20-km ORSM are generated to facilitate forecaster’s interpretation of model forecasts.  The TC positions, determined as the point of minimum sea level pressure, are identified with the fitting method of overlapping parabolic interpolation (Manning & Haagenson, 1992).

To take advantage of the vast amount of forecast information available from different runs of ORSM , an ensemble forecasting system based on the current and time-lagged forecasts was set up.  A maximum of 14 member forecasts can be obtained at any grid point in the neighbourhood of Hong Kong and the forecast information is presented in the form of standard EPS meteograms.  An interactive web interface is provided for forecaster’s easy control over which elements, grid points, model runs, valid times, etc., are to be included in the meteograms.  An option is also provided to automatically remove any bias in the ensemble mean.

- NHM

The precipitation forecast from NHM is used in the RAPIDS to blend with rainfall nowcast products generated by SWIRLS to provide quantitative precipitation forecast up to 6 hours ahead.  Please refer to Section 4.4.2 below for more details.

During the 2008 Olympic windsurfing race held in Qingdao, the NHM model was operated daily to provide guidance up to 18 hour in supporting the Hong Kong Windsurfing Team.  The model was configured with the finest grid at 3-km resolution, size 151x151, 45 vertical levels.  The forecast products were combined with the WRF outputs (see (vi) below) to generate site-specific forecast guidance on wind speed, wind direction and temperature at the sailing venue.

A 1-km NHM was also tested for local wind prediction over Hong Kong during the trial event of the 2009 East Asian Games.

- LAPS

Based on the LAPS system, a tropical cyclone specific application called TC-LAPS is in operation.  The purpose of the TC-LAPS is to provide the forecasters with rapidly updated analysis of 3-dimensional wind structure of approaching tropical cyclones.  It also aims to help forecasters estimate the probability of the occurrence of strong/gale force winds over the territory.   Wind and moisture fields of horizontal resolution of 10, 5, 1.5 km and 500 m on selected pressure levels are generated hourly.

- TIPS

The Tropical Cyclone Information Processing System (TIPS) has been in operation since 2005, integrating various information and data, including a) NWP products from the Observatory’s ORSM, as well as ECMWF, JMA, UKMO and NCEP models, b) subjective forecasts and warning positions from meteorological centres, and c) satellite and radar imageries, for use by forecasters in the preparation of tropical cyclone forecasts.  TIPS can also generate ensemble tracks from model forecast positions for reference by the forecasters, who can modify interactively the weightings for individual model outputs in order to re-calculate the ensemble track.  A motion vector consensus method to generate TC ensemble tracks has been incorporated in TIPS and will be put into operation in 2009.

- WRF

During the 2008 Olympic windsurfing race held in Qingdao, the WRF model was run twice a day out to 24 hours to provide real-time forecast support to the Hong Kong Windsurfing Team.  The model was configured with the finest grid at 3-km resolution, size 100x100, 45 vertical levels and centred at the Olympic Sailing Centre of Qingdao.  Tailor-made forecast time-series products were delivered to the windsurfing team via the Internet during the Olympic.

- Others

A forecasting tool for estimating the probability of strong and gale force winds in Hong Kong during TC situations is in operation.  The uncertainty in the forecast is basically determined by the following three methods: (i) the regression of the spread of forecast movements from various deterministic models against a Gaussian distribution; (ii) the spread of TC track and intensity forecasts from the ECMWF EPS; and (iii) the historical error of the official forecast track issued by HKO.  The resulting probability is then obtained from the spread and the climatological probability isopleths for occurrence of strong and gale force winds.  The tool also allows users to conduct “what-if” analyses based on their input of alternative forecast positions of the TC.

A TC forecast guidance tool is also in use to forecast the TC intensity up to 72 hours ahead using JMA’s GSM output.  Based on regression of model forecast on central pressure against the best-track data in the past few years, a set of best-estimated parameters is derived and then applied to the real-time NWP forecasts to calculate the probability of particular class of intensity, maximum wind and central pressure of the TCs.

Utilizing the JMA and ECMWF EPS TC data, clustered TC track diagrams, conditioned strike probability maps and time-series of strike probability for various distance thresholds are generated in real-time for reference by the forecasters.  Deterministic forecasts of TC intensity derived from the JMA EPS data are also calibrated using an artificial neural network.

In August and September 2008, automatic site-specific forecasts up to 72 hours ahead were generated from the multi-model ensemble of bias-corrected ECMWF, JMA and ORSM model outputs to support the Olympic and Paralympic equestrian events.

4.3.4.2	Research performed in this field

Based on real-time verification and the lagged averaging technique, a new method was developed to correct the systematic biases in the simple ensemble mean tracks obtained from the ECMWF EPS TC forecast.  Three TC cases from 2008 were tested and the new method was shown to produce more accurate tracks when compared with the simple ensemble mean tracks.  In the case of T. Fengshen (0806), the new method even outperformed the multi-model ensemble technique by as much as 44%.

4.4    Nowcasting and Very Short-range Forecasting Systems (0-6 hrs)

4.4.1		   Nowcasting system

4.4.1.1		   In operation

SWIRLS is a radar-based nowcasting system with output updated every 6 minutes.  It has been put into operation since 1999, with an original objective for short-range rainfall forecasting in support of rainstorm warning operation in Hong Kong.  It has since evolved into a multi-function system with a wide spectrum of applications, including flood warning and landslip warning.  Major components of SWIRLS include: (i) TREC which derives the multi-scale "wind" fields at multi-altitude levels by tracking the movement of individual radar reflectivity cells using the TREC technique; (ii) GTrack which tracks and predicts the movement of clusters of radar echoes using an object-oriented approach; (iii) Dynamic radar-raingauge analysis which updates the Z-R relation dynamically using radar reflectivity and rain-gauge data in order to re-calibrate the radar rainfall in real-time; (iv) QPF which extrapolates the rainfall re-calibrated radar echoes along the TREC wind direction using a semi-Lagrangian advection scheme to produce rainfall accumulations out to 6 hours over Hong Kong and nearby areas; (v) Landslip Alert which predicts the number of landslides in the next 3 hours based on a rainfall-landslide correlation model developed by geotechnical engineers; (vi) Flood Alert which predicts flash floods over low-lying areas based on the 1-hour QPF of SWIRLS; and (vii) TephiViewer which calculates a number of thermodynamical instability indices based on upper-air observations and various NWP model outputs to alert forecasters of the potential of severe weather.

Since mid-2007, several new modules for severe weather nowcasting, namely lightning, downburst / wind gust and hail, were put into operational trial in support of thunderstorm warning operation in Hong Kong.  The lightning algorithm (Yeung et al., 2007) focuses on the initiation and intensity of cloud-to-ground lightning based on isothermal reflectivity data with reference to the 3-dimensional temperature analyses by LAPS.  The downburst/wind gust algorithm (Yeung et al., 2008) is a physically-based scheme to predict the maximum possible wind gust due to downburst associated with severe thunderstorms.  Major inputs include radar-estimated vertically integrated liquid (VIL) water and ascent data.  The hail algorithm predicts the occurrence of hail associated with severe thunderstorms, with the 60-dBZ contour and the VIL in the lowest 2 km as the major inputs.   Besides detection, the above nowcasting modules also extrapolate the severe weather tracks out to 30 min using the TREC motion vectors.

Since 2007, a graphical rainfall nowcast product with GIS information has been made available to government and selected users.  The nowcast data is based on the actual radar-rainfall analyses and the predictions from SWIRLS.  The product is presented as an animated sequence of rainfall maps updated every 30 min.  The underlying GIS platform is Google Earth.  In Oct 2008, the forecast range was extended from 1 to 2 hours and the enhanced product launched to the Internet for use by the general public.

4.4.1.2   Research performed in this field

The second-generation nowcasting system, referred to as SWIRLS-2, was successfully adapted to the Beijing domain and operated smoothly during the Beijing Olympic in August-September 2008 under the B08FDP.  Based on the storm cases in B08FDP Trial 2007, major R&D work done in 2008 prior to the start of the Olympic included: (i) tuning of the downburst/squalls algorithm to reduce the mean error in the forecast gust severity; (ii) tuning of dynamic Z-R conversion algorithm, including the preparation of a new set of default (a, b) parameters; and (iii) replacing the original cell-based tracking method by a new grid-based technique called MOVA (Multi-scale Optical-flow by Variational Analysis).  The new technique resulted in more accurate track forecast, with the additional advantages of being more consistent and robust against new born cells and rapidly changing cells which are difficult to track.  It was also applied to track the isothermal reflectivity field to deduce the probabilistic nowcast product of lightning up to 3 hours ahead over the Beijing region.

In Hong Kong, an impact study was initiated to assess the merits of replacing the TREC by the MOVA echo-motion vectors in the quantitative precipitation forecast (QPF) of SWIRLS.  Preliminary results based on the rainstorm cases in 2008 indicated some potential improvements, including smoothed motion fields with general improvements in the resulting rainstorm alerts generated by SWIRLS.  Moreover, a case study was performed for a hailstorm in 2008 summer using the hail nowcast outputs from SWIRLS.  The signature of overhanging radar echoes was successfully detected by SWIRLS with a significant lead time.  A characteristic jump in the lightning intensity preceding the hail occurrence was also noted.

4.4.2	   Models for Very Short-range Forecasting Systems

4.4.2.1		   In operation

RAPIDS

RAPIDS has been put in trial operation since April 2005 to provide quantitative precipitation forecasts for 1-6 hour forecasts at 2 km resolution on an hourly update basis  (Li et al. 2005, Wong and Lai 2006).  The system blends the output from SWIRLS and NHM with their respective weightings based on real-time verification results of precipitation predictions.  Regional phase correction to correct spatial errors in the forecast precipitation field in NHM was included.  To correct the biases in rainfall intensity occasionally found in NHM forecast, an intensity correction scheme, which is based on comparing cumulative distribution of rainfall intensity from SWIRLS rainfall analysis and NHM short-term forecast, was also implemented.

4.4.2.2    Research performed in this field

RAPIDS was also put into operation during B08FDP with R&D made on (i) improved phase correction technique using optical flow technique, (ii) enhancements in rainfall intensity calibration for more robust correction of NHM QPF, (iii) probability of precipitation using time-lagged ensemble approach.

### 4.5	Specialized numerical predictions

4.5.1	Assimilation of specific data, analysis and initialization

4.5.1.1    In operation

- SLOSH (Storm Surge Model)

The forecast position, minimum pressure and storm size of tropical cyclone at the time of closest approach to Hong Kong and 24/48 hours before this time are used as input.

- WAVEWATCH III (Wave Model)

Forecast surface wind data with grid resolution 1.25°x1.25° from JMA based on 00 and 12 UTC are used as input.

4.5.2	Specific models

4.5.2.1    In operation

(i)		SLOSH (Storm Surge Model)

A general description of SLOSH is summarized as follows:

| Governing equation | Transport equations of motion |
| --- | --- |
| Prognostic variables | Horizontal components of transport, water height |
| Spatial grid and resolution | A curvilinear polar grid, from 1 km resolution near the centre of the Hong Kong Basin to 7 km in open sea, 83x146 grid points |
| Terrain and bathymetry | Land topography and water depth at sea points |
| Initialization | Initialization time proposed by Jelesnianski et al. (1992). Static height elevations due to storm’s pressure drop at the initial time are added to the initial quiescent water level. |
| Boundary conditions | Scheme proposed by Jelesnianski et al. (1992) to cater for different water depths |
| Driving forces | Simplified model storm (Jelesnianski and Taylor, 1973) |
| Numerical technique | Explicit finite difference scheme |

Further details can be found in Jelesnianski et al. (1992).

(ii)		WAVEWATCH III (Wave Model)

A general description of WAVEWATCH III is summarized as follows:

| Governing equation | Spectral action density balance equation |
| --- | --- |
| Prognostic variables | Wave action density spectrum |
| Spatial grid and resolution | Mercator projection for the area bounded by 5-35°N, 105-135°E, 1.25°x1.25° resolution, 27x27 grid points |
| Bathymetry | Water depth at sea points (SRTM) |
| Intra-spectral grid | 24 directions with 15° increment, 25 logarithmic frequency grid points |
| Initial conditions | Parametric fetch-limited JONSWAP spectrum |
| Boundary conditions | Initial conditions applied as constant boundary conditions |
| Source term (input and dissipation) | Tolman and Chalikov parameterization |
| Source term (nonlinear interactions) | Discrete interaction approximation |
| Source term (bottom friction) | JONSWAP parameterization |
| Propagation scheme | Ultimate Quickest scheme with averaging |
| Numerical technique | Fractional step method |

Further details can be found in Tolman (2002).

    - Specific products operationally available

- SLOSH (Storm Surge Model)

The model will be run when a tropical cyclone is approaching Hong Kong and local tropical cyclone warnings are issued. Outputs are tables showing the simulated storm surges and predicted total sea levels for 12 locations as well as time series graphs showing the predicted astronomical tide, storm surges and total sea levels at 4 locations for the period from 18 hours before the time of nearest approach to 12 hours after.

(ii)		WAVEWATCH III (Wave Model)

Forecast parameters include significant wave height, wind wave height and swell direction, period and height for the sea area bounded by 5-35°N, 105-135°E. These products are displayed graphically. The model is run twice daily based on 00 and 12 UTC model runs. Forecasts are available up to 120 hours based on 12 UTC run and up to 72 hours based on 00 UTC run, at 24-hour steps.

### 4.6	Extended range forecasts (ERF) (10 days to 30 days)

No ERF model is being operated at the moment.

### 4.7 	Long range forecasts (LRF) (30 days up to two years)

4.7.1	In operation

The Observatory has been operating a suite of global-regional spectral climate models adapted from the Experimental Climate Prediction Center (ECPC), USA, since 2007.  A verification exercise was carried out and it was found that the regional spectral model generally performed better when it was configured with a larger domain but coarser resolution compared to its previous settings.  The new configuration of the model was effected and began operation in 2008.  The model suite generates seasonal temperature and rainfall forecasts for Hong Kong and its neighbouring areas.  Products are made available to the general public via the Observatory’s Internet website.

4.7.2	Research performed in this field

The Observatory is experimenting with quantitative monthly forecast using the current model suite.  The model suite demonstrated some skill in forecasting monthly temperature but lesser skill in forecasting rainfall.

4.7.3	Operationally available EPS LRF products

No EPS LRF system is being operated at the moment.

## 5.	Verification of prognostic products

5.1	Verification of forecasts generated by ORSM is conducted on a routine basis.  Forecast parameters including zonal and meridional winds, temperature, pressure/geopotential heights and relative humidity at a number of model levels are verified against ORSM analysis and rawinsonde observations for the area 10 – 40 (N, 95 – 135 (E.  The monthly verification results of the 60-km ORSM 12 UTC runs for 2008 are presented in Appendix I.

## 6.	Plans for the future (next 4 years)

### 6.1	Development of the GDPFS

6.1.1	A new high performance computing system with a peak performance exceeding 5 TFLOPS will be procured and installed in 2009 to support the development and operation of a new suite of high resolution NWP models.   The new model suite will comprise meso-scale models based on NHM with horizontal resolutions reaching 2 km.

6.1.2		The servers to process GTS bulletins and message switching will be replaced in 2009. The new servers will have better capacity to cope with the increase of meteorological data in the near future.

6.1.3	The development of a Digital Forecast system for regional temperatures will commence in 2009.

### 6.2	Planned research Activities in NWP, Nowcasting and Long-range Forecasting

6.2.1 	Planned Research Activities in NWP

- Development of a 3-dimensional variational data assimilation system for NHM will continue;

- Research will continue on applying NHM in RAPIDS and providing guidance on severe weather prediction in the very-short-range.Improvements to correct phase and intensity errors of NHM to blend rainfall nowcast in RAPIDS will carry on;

- A high-resolution NHM will be tested and deployed to facilitate the preparation of site-specific forecasts for the 2009 East Asian Games to be held in Hong Kong.

6.2.2 	Planned Research Activities in Nowcasting

- Development and testing SWIRLS-2 for Hong Kong will continue;

- SWIRLS-2 will participate in the trial for the WMO Shanghai World EXPO 2010 Nowcasting Service Demonstration Project (WENS);

6.2.3 	Planned Research Activities in Long-range Forecasting

The feasibility of downscaling global model output from WMO designated Global Producing Centres for Long-range Forecasts (GPC) to Hong Kong will be explored.

7.		References

Albers, S., 1995: The LAPS winds analysis.  Wea. and Forecast, 10, 342-352.

Albers, S., J. McGinley, D. Birkenheuer, and J. Smart, 1996: The Local Analysis and Prediction System (LAPS) – Analysis of clouds, precipitation, and temperature.  Wea. and forecast, 11, 273-287.

Arakawa, A. and W.H. Schubert, 1974: Interaction of a cumulus cloud ensemble with the large-scale environment, Part I. J. Atmos. Sci., 31: 674-701.

Benwell, G.R.R. and F.H. Bushby, 1970: A case study of frontal behavior using a 10-level primitive equation model. Quart. Jour. Roy. Meteor. Soc., 96, 287-296.

Gadd, A.J. and J.F. Keers, 1970 : Surface exchanges of sensible and latent heat in a 10-level model atmosphere. Quart. Jour. Roy. Meteor. Soc., 96, 297-308.

Japan Meteorological Agency (JMA), 2002: Appendix to WMO Numerical Weather Prediction Progress Report.

Jelesnianski, C.P., J. Chen and W.A. Shaffer, 1992: SLOSH Sea, Lake and Overland Surges from Hurricanes. NOAA/NWS Technical Report NWS 48.

Jelesnianski, C.P. and A.D. Taylor, 1973: A preliminary view of storm surges before and after storm modifications. NOAA Technical Memorandum ERL WMPO-3.

Kitagawa, H., 2000: Radiation process.  Report of Numerical Prediction Division, 46, 16-31 (in Japanese).

Li, P. W., W.K. Wong and E.S.T. Lai; 2005: RAPIDS – A new rainstorm nowcasting system in Hong Kong. Proceeding, WWRP Symposium on Nowcasting and Very Short Range Forecasting, 7.17-24.

Manning, K. W. and P. L. Haagenson, 1992: Data ingest and objective analysis for the PSU/NCAR modelling system: Programs DATAGRID and RAWINS.  NCAR Technical Note, NCAR/TN-376+IA, 209 pp.

Nakanishi, M. and H. Niino, 2004: Improvement of the Mellor-Yamada level 3 model with condensation physics: Its design and verification.  Boundary-Layer Meteorol., 112, 1-31.

Saito, K., T. Fujita, Y. Yamada, J. Ishida, Y. Kumagai, K. Aranami, S. Ohmori, R. Nagasawa, S. Kumagai, C. Muroi, T. Kato, H. Eito and Y. Yamazaki, 2006: The operational JMA nonhydrostatic model. Mon. Wea. Rev., 134, 1266-1298.

Sugi, M., K. Kuma, K. Tada, K. Tamiya, N. Hasegawa, T. Iwasaki, S. Yamada and T. Kitade, 1990: Description and performance of the JMA operational global spectral model (JMA-GSM88). Geophys. Mag., 43, 105-130.

Tolman, H.L. 2002: User manual and system documentation of WAVEWATCH-III version 2.22. NOAA/NWS/NCEP/MMAB Technical Note 222.

Troen, I., and L. Mahrt, 1986: A simple model of the atmospheric boundary layer: Sensitivity to surface evaporation.  Boundary Layer Meteorl., 37, 129-148.

Wong, W.K. and E.S.T. Lai, 2006: RAPIDS – Operational Blending of Nowcast and NWP QPF. presented in the 2nd International Symposium on Quantitative Precipitation Forecasting and Hydrology, 4-8 June 2006, Boulder, Colorado, USA.

Wong, W.K. and E.S.T. Lai, 2008: Numerical simulation of fog using non-hydrostatic NWP model with third-order turbulence closure.  Presented in the 2nd International Symposium on Shallow Flows, 10-12 December 2008, HKUST, Hong Kong.

Yabu, S., S. Murai and H. Kitagawa, 2005: Clear sky radiation scheme. Report of Numerical Prediction Division, 51, 53-64 (in Japanese).

Yeung, L.H.Y. , E.S.T. Lai & S.K.S. Chiu, 2007 : Lightning Initiation and Intensity Nowcasting Based on Isothermal Radar Reflectivity - A Conceptual Model, the 33rd International Conference on Radar Meteorology, 6-10 August 2007, Cairns, Australia.

Yeung, L.H.Y., E.S.T. Lai & P.K.Y. Chan, 2008 : Thunderstorm Downburst and Radar-based Nowcasting of Squalls, ERAD 2008 - The Fifth European Conference on Radar in Meteorology and Hydrology, 30 June – 4 July 2008, Helsinki, Finland.

Appendix I — Summary of Verification of Prognostic Products Generated by

60-km ORSM 12 UTC Runs for 2008 (Verification Area: 10 – 40 (N, 95 – 135 (E)

Table 1.	RMS error of geopotential height at 500 hPa against analysis (in m)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Average |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 12.0 | 12.2 | 11.8 | 11.7 | 10.4 | 9.7 | 9.7 | 9.6 | 10.9 | 9.4 | 9.6 | 10.8 | 10.6 |
| 72 | 19.5 | 22.4 | 22.4 | 23.4 | 19.6 | 17.1 | 17.7 | 16.4 | 21.5 | 18.3 | 20.2 | 20.9 | 19.9 |

Table 2.	RMS error of geopotential height at 500 hPa against observations (in m)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Average |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 15.5 | 16.1 | 15.8 | 14.8 | 12.9 | 12.8 | 12.4 | 13.5 | 13.1 | 11.9 | 12.4 | 12.9 | 13.7 |
| 72 | 23.9 | 27.1 | 25.5 | 23.4 | 21.6 | 19.7 | 20.3 | 19.5 | 22.5 | 20.4 | 24.0 | 22.7 | 22.6 |

Table 3.	RMS of vector wind errors at 250 hPa against analysis (in m/s)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Average |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 6.1 | 5.7 | 6.9 | 7.4 | 7.4 | 7.2 | 6.5 | 6.4 | 7.4 | 7.4 | 7.4 | 7.2 | 6.9 |
| 72 | 9.5 | 9.0 | 11.9 | 13.1 | 11.9 | 11.6 | 10.6 | 10.0 | 11.8 | 11.4 | 10.7 | 10.4 | 11.0 |

Table 4.	RMS of vector wind error at 850 hPa against analysis (in m/s)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Average |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 4.7 | 4.8 | 4.3 | 4.5 | 5.0 | 4.7 | 4.6 | 4.6 | 4.9 | 4.5 | 4.9 | 5.2 | 4.7 |
| 72 | 6.7 | 7.2 | 6.2 | 7.4 | 8.1 | 8.2 | 8.1 | 7.5 | 9.5 | 7.3 | 6.9 | 7.8 | 7.6 |

Table 5.	RMS of vector wind errors at 850 hPa against observations (in m/s)

| Hours | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Average |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24 | 5.2 | 5.0 | 4.8 | 4.8 | 4.8 | 5.1 | 4.6 | 4.5 | 4.7 | 4.5 | 4.8 | 4.9 | 4.8 |
| 72 | 6.4 | 6.4 | 6.2 | 6.3 | 6.4 | 6.9 | 6.3 | 6.0 | 6.4 | 6.0 | 6.1 | 6.0 | 6.3 |