# JOINT WMO TECHNICAL PROGRESS REPORT ON THE GLOBAL DATA PROCESSING AND FORECASTING SYSTEM AND NUMERICAL WEATHER PREDICTION RESEARCH ACTIVITIES FOR 2008

Korea Meteorological Administration

Republic of Korea

## 1.	Summary of highlights

Major changes in operational data processing and forecasting system in 2008:

28 February  	Operation of new wave prediction systems for regional and costal areas based on WAVEWATCH-III (WW3). The resolutions for regional and costal areas are 8-km and 1-km, respectively. KMA is also preparing the operation of a global wave model based on WW3.

29 June   	Upgrade of KMA Weather Research and Forecasting (KWRF) model for regional domain with 10-km horizontal resolution. KMA has been using a dual prediction system for regional area.

9 September  	Application of 6-hour cycling 3dVar analysis system to global ensemble prediction system.

15 October 	Adaptation of an 1-hour analysis system throughout the Korean Peninsula using KLAPS (Korea Local Analysis and Prediction System).

## 2.	Equipment in use

The supercomputer Cray X1E-8/1024-L is dedicated to the operation of short-, medium- and long-range numerical weather prediction including climate simulation.

Make and model: Cray X1E-8/1024-L

CPUs and performance

128 modules, 256 nodes, 1024 CPUs

Single CPU performance: 18.08G flops

Peak performance: 18.5 T Flops

Operating system:  UNICOS/MP

Memory

Memory per node:  16  Gbytes

Memory total        :  4.096 Tbytes

Disk storage

Direct-attached storage: 62Tbytes

Global sharing file system based on SAN technology: 20Tbytes

## 3.	Data and products from GTS in use

Synoptic observations, and various asynoptic observations, including satellite and wind profiler data, are used on a daily basis in GDAPS. Table 3.1 presents the types and extent of observations from GTS and FTP.  Pre-processing procedures such as data acquisition, quality control and decoding, are fully automated.

RARS (Regional ATOVS Retransmission Services; Korea, Japan, China and Australia directly received ATOVS data at each country, and 4 countries obtain the RARS data exchanging the ATOVS data among them.) was newly collected in 2008. SSMI data was also added and more QSCAT data was received.

Table 3.1. Types and extent of observations received through GTS and FTP in global data assimilation for 24 hours in 2008.

|  | Data type | Amount of data/day |
| --- | --- | --- |
| 1 | SYNOP | 40,867 |
| 2 | SHIP | 8,421 |
| 3 | BUOY | 7,310 |
| 4 | AIREP | 19,197 |
| 5 | ACARS/AMDAR | 219,955 |
| 6 | TEMP | 4,679 |
| 7 | PILOT | 1,179 |
| 8 | Wind Profiler | 282 |
| 9 | AMV-METEO7 | 148,398 |
| 10 | AMV-MTSAT | 97,682 |
| 11 | AMV_MODIS | 83,427 |
| 12 | ATOVS(NOAA18) | 78,524 |
| 13 | QSCAT | 620,264 |
| 14 | SATEM | 31,616 |
| 15 | SATOB | 69,085 |
| 16 | RARS | 847,793 |
| 17 | AMDAR(Korea) | 2,535 |
| 18 | SSMI | 57,822 |

## 4.	Forecasting system

### 4.1	System run schedule and forecast ranges

Short- and medium-range forecast

Global Data Assimilation and Prediction System (GDAPS) for 10-day projection runs at 00 UTC and 12 UTC with 2.5-hour data cutoff time. 84-hour projection is used for short-range weather forecasts, weekly forecast and for the provision of lateral boundary condition for the two high-resolution (10-km and 5-km with 33 layers) regional models. Regional Data Assimilation and Prediction System (RDAPS) runs twice a day (00 and 12 UTC) for 66-hour forecasts. Another regional model, KWRF-based WRF, with 10-km horizontal resolution and 40 vertical layers, runs twice a day for 66-hour forecasts as well. KLAPS (5-km with 40 layers) runs every hour, analyzing weather conditions around the Korean peninsula.

Four typhoon track forecasts are obtained from Double Fourier Series BARotropic typhoon prediction model (DBAR), RDAPS, GDAPS (T426/L40), and EPS, for typhoons originating in the Western Pacific. Moreover, two types of applied models are used: wave models based on WW3 for wave height and direction in global, regional and 6 coastal areas, and two statistical models using the Perfect Prog Method (PPM) and the Kalman Filter (KF) method for probability of precipitation and max/min temperature, respectively.

Long-range forecast

KMA produces three types of long-range forecasts: 1-month and 3-month forecasts, and seasonal climate outlook. The 1-month forecast is issued three times a month and includes 10-day mean temperature and precipitation, and characteristic pressure pattern for each 10-day period. The 3-month forecast, produced on a monthly basis, includes monthly temperature and precipitation, and characteristic pressure pattern for each month. This forecast also includes special seasonal events such as Asian dust for spring and typhoons for summer and autumn. The seasonal climate outlook is issued four times a year: February for the summer climate outlook; May for the autumn climate outlook; August for the winter climate outlook; and November for the spring climate outlook

### 4.2	Medium-range forecasting system (4-10 days)

#### 4.2.1	Data assimilation, objective analysis and initialization

4.2.1.1	In operation

The major characteristics of the operational global 3dVar are almost identical to those in 2007.

| Analysis resolution | T426L40 (30km) |
| --- | --- |
| Inner loop resolution | T106L40 |
| Analysis domain top | 0.4 hPa |
| Constraints | The climatologic constraint of zonal averaged vorticity is applied in the cost function formulation |
| FGAT | 1-hour interval FGAT (First Guess at Appropriate Time) is applied to reduce errors due to the time difference between observation and background. |
| Moisture profile | The moisture profile, selected based on cloud information derived from MTSAT-1R imaginary data and the profile, is assimilated in 3dVar. |
| ATOVS data assimilation | The direct assimilation of ATOVS radiance data (level 1D type) is embedded in the 3dVar system |
| QuikSCAT data assimilation | Sea surface wind data retrieved from the QuikSCAT satellite is assimilated using the PBL operator based on the MRF PBL method. |
| Typhoon bogus | Background typhoon bogus, which produces a corrected background field by modifying the typhoon position and strength in the background field based on typhoon observation information, is applied |
| Initialization | A Non-linear Normal Mode Initialization (NNMI) with full physics is performed to suppress the amplitude of high-frequency gravity waves. |

There were several major improvements and changes in data assimilation and initialization in 2008:

- AMDAR data from a domestic airline (Korean Air) was introduced, improving the performance of the global model.

- Wind profiler data for 7 domestic sites was additionally assimilated. As a result, a total of 12 domestic wind profilers are being used at present.

- The pre-processes for the QuikSCAT data assimilation were further generalized by applying flexible domain definition. The definition of domain resolution is in the namelist.

4.2.1.2	Research performed in this field

- Global unified 3dVar coupled with the global model

The unified 3dVar, an expanded NCAR WRF-3dVar for the KMA global model, was coupled and tested for performance evaluation. According to a one-month cycle run during the summer season, the global unified 3dVar showed larger RMSE than the operational one with the original quality control parameters.  But it was finally improved and showed a higher score by employing the strict quality control criteria such as the exclusion of observation data with a large observation increment.

- MODIS, ATOVS, and SSMI data assimilation

MODIS (polar wind), ATOVS (radiance, NOAA18) and SSMI (10m wind) were newly added in the global unified 3dVar and made improved results on the whole. The impact from MODIS was the most salient, while the impact from ATOVS and SSMI was not as strong.

- Test of UK Met office 4dVar

The UK Met office 4dVar system, which will replace the current 3dVar from 2010 and onward, was installed on Cray X1E and tested.  The UK Met office data assimilation system was flexibly designed for use with both global and regional models as well as for both 3dVar and 4dVar. KMA expects the introduction of the new 4dVar system to significantly enhance the accuracy of numerical weather prediction.

#### 4.2.2	Models

4.2.2.1	In operation

Key model parameters of global forecast model (GDAPS) for medium-range forecast

| Dynamics |  |
| --- | --- |
| Initialization | Nonlinear normal mode initialization |
| Basic equation | Primitive equations in sigma-pressure hybrid vertical coordinate |
| Numerics | Spectral representation of horizontal variables with triangular truncation of T426, corresponding to a Gaussian grid size of 0.28125 degrees or 30km |
| Domain | Global |
| Levels | 40 sigma-pressure levels ranging from surface to 0.4 hPa |
| Time integration | Eulerian semi-implicit scheme |
| Forecast range | 252 hours (10.5 days) |
| Physics |  |
| Horizontal diffusion | Second-order Laplacian |
| Vertical damping | Rayleigh friction |
| Moist processes | Kuo scheme, large-scale condensation, and shallow convection scheme |
| Radiation | Long-wave radiation calculated every three hours Short-wave radiation calculated every hour |
| Gravity wave drag | GWD due to orography for long waves (wavelength>100km) and short waves (wavelength (10km) (Iwasaki et al. 1989) GWD due to cumulus convection (GWDC) (Chun and Baik 1988) |
| PBL processes | Non-local diffusion scheme and similarity theory for surface layer (Holtslag and Boville 1993) |
| Land surface | Simple biosphere (SiB) model (Sellers et al. 1986) |
| Surface state | NCEP daily SST anomaly added to monthly changing climatological SST Climatological values are used for soil moisture, snow depth, roughness length and albedo |

4.2.2.2	Research performed in this field

The parameterisation scheme of gravity wave drag due to cumulus convection (GWDC) by Chun and Baik (1988) was newly implemented in KMA’s operational global forecast model (GDAPS). The GWDC scheme was proved to improve the performance of the model, especially in the stratosphere, by correcting the structure of stratospheric polar night jets.

The cloud-radiation parameterization scheme of GDAPS was revised to correct the model’s systematic negative bias of calculated cloud amount. A revised diagnostic formulation utilizing the probability density function of relative humidity in the cloud-generating stage was implemented in the cloud-radiation parameterization scheme. The revised cloud-generating method was proved to have a positive effect in increasing the amount of clouds in the model, thereby reducing errors in the cloud-radiation budget.

KMA is planning to operate the Unified Model (UM) as KMA’s next-generation medium-range global forecast model from January 2010, as a replacement for the current global model (GDAPS). The entire UM system, which includes an observation processing system and variational data assimilation (4dVar) system as well as the UM model, was introduced at KMA in 2008, and has been installed and tested on KMA’s CRAY X1E platform. Extensive efforts and collaborative work with the Met Office have been made to make optimal UM system under the KMA circumstances for NWP systems.

Real-time run of UM for a global domain was launched in June 2008 for the purpose of assessing the performance of UM in the East Asian region as well as globally. The configurations of UM for medium-range forecast are as follows:

| Frame |  |
| --- | --- |
| Horizontal resolution | N320 (640(481 / 0.5625((0.375( / ~40km) |
| Vertical resolution | L50 (top ~ 60km) |
| Forecast length | 120 hours |
| Time integration | Semi-Lagrangian semi-implicit scheme |
| Physics |  |
| Large-scale precipitation | Improved mixed phase microphysics based on Wilson and Ballad scheme |
| Convection | CMODS |
| Surface hydrology | MOSES-II |
| Planetary boundary layer | MOSES-II non-local scheme with revised diagnosis of K profile depth |
| Gravity wave drag | Orographic scheme including flow blocking and/or spectral gravity wave scheme |
| Radiation | General 2-stream radiation for both SW and LW |
| Cloud | Standard scheme with triangular probability density function |

#### 4.2.3	Operationally available Numerical Weather Prediction products

Analysis, forecast, and auxiliary weather charts and various graphic images were produced from NWP post-process system and distributed to the forecasters and the public. The KMA’s NWP products on real time base can be offered via KMA website (http://web.kma.go.kr/eng).

In particular, KMA has been providing the products of time series format in specific cities (hereafter city-specific products) via the internet for 160 cities in 14 Asian countries since 2006 as part of a WMO RAII (Region Association II) pilot project. The city-specific products time series products and other images have been offered to RA II members via the KMA website.

#### 4.2.4	Operational techniques for application of NWP products (MOS, PPM, KF, Expert Systems, etc..)

4.2.4.1	In operation

NWP products are automatically generated from NWP systems at KMA.  Various model outputs, including potential vorticity fields on isentropic surfaces, are available in both graphic and imagery forms. Those products are also disseminated to end users through the KMA Intranet or the internet (at: http://www.kma.go.kr/eng/wis/wis04_nwp01.jsp).

For weekly forecasts, the Kalman Filter and Dynamic Linear Model from GDAPS are used to derive maximum and minimum temperature up to 10 days for 6 major cities.

4.2.4.2	Research performed in this field

No activity in this area

#### 4.2.5	Ensemble Prediction System (EPS)

4.2.5.1	In operation

KMA operates a global ensemble prediction system, based on the breeding method. An ensemble of 16 members is obtained using a rotated bred vector method, i.e., applying factor rotation after 12 hours of initial growth of perturbation, then fostering perturbation for another 12 hours. Global EPS runs twice a day up to 10 days at 00 and 12 UTC to support weekly forecasts. Post-processing using a decaying average bias estimation method (Cui et al. 2005) has been introduced to the operation since 30 July 2007.

KMA participates in the WMO THORPEX TIGGE program and provides operational global ensemble forecast to the TIGGE archive centres, and the standard verification scores of EPS will be regularly exchanged through the EPS verification website hosted by JMA.

The specifications of the global ensemble prediction system for medium-range forecast are as follows:

| Horizontal resolution | Spectral triangular truncation of T213 (0.5625 degrees) |
| --- | --- |
| Vertical resolution (model top) | 40 levels (0.4 hPa) |
| Forecast model | GDAPS (Global spectral model) |
| Data assimilation for control analysis | 3dVar using EPS control forecast for background field |
| Forecast length | 10 days |
| Number of runs per day (time) | 2 (00UTC, 12UTC) |
| Initial perturbation method (area) | Breeding + Factor rotation (Northern Hemisphere) |
| Ensemble size | 17 members (1 control + 16 perturbed members) per run *A total of 34 members for products |
| Perturbation of physics | None |
| Post processing | Bias correction (Cui et al. 2005) |

4.2.5.2	Research performed in this field

Introducing a self-cycling data assimilation system for EPS

The KMA EPS system has obtained the initial field for control through interpolation of higher-resolution global analysis. This process could cause loss of high-frequency wave energy. Degradation of the initial field, and eventually forecast performance, is possible as a result of the disagreement in the topography and surface data between the original higher-resolution analysis and lower-resolution forecast model.

To address this problem, KMA has constructed a 3dVar data assimilation system for global EPS. This system uses EPS control forecast as background information and produces analysis on the same resolution as the EPS model. The experiment with this self-cycling data assimilation system shows improvement in later lead time as well as early lead time. This system was applied to the operational system in September 2008.

#### 4.2.5.3	Operationally available EPS Products

The following products from global EPS are available to internal users:

- Mean and Spread for MSLP, geopotential height at 500hPa, and temperature at 850hPa

- Spread and Spaghetti for geopotential height at 500hPa

- Stamp map for geopotential height at 500hPa

- Probability of precipitation and wind exceeding certain amount

- Time series of probabilistic forecast for 6 major cities

#### 4.3	Short-range forecasting system (0-72 hrs)

#### 4.3.1	Data assimilation, objective analysis and initialization

4.3.1.1	In operation

The major characteristics of the operational regional data assimilation system are as follows:

|  | RDAPS 30km | RDAPS 10km | RDAPS 5km | KWRF |
| --- | --- | --- | --- | --- |
| Data assimilation | - | 3dVar | - | Unified 3dVar |
| Initial condition | From the Global model | 3-hour cycle | From RDAPS 10km | From the Unified 3dVar |
| Boundary condition | From the Global model | From RDAPS 30km | From RDAPS 10km | From the Global model |
| Number of vertical layers | 33 | 33 | 33 | 31→40 |
| Domain top | 50hPa | 50hPa | 50hPa | 50hPa |
| Horizontal grids | 251X201 | 178X160 | 141X141 | 574X514 |
| Initialization | FDDA | IAU | - | DFI |
| Domain | East Asia | Around the Peninsula | Around South Korea | East Asia |

※ FDDA: Four Dimensional Data Assimilation (12-hour analysis nudging)

IAU: Incremental Analysis Updates (-1.5 hour ~ +1.5hour window)

DFI: Digital Filter Initialization (-2 hour backward ~ +2 hour forward)

KMA has been operating two regional models. One is RDAPS developed based on MM5, and the other is KWRF.  RDAPS has a 30-km resolution with two nested domains (10-km and 5-km), and KWRF has been operated with 10-km resolution over East Asia. The 10-km RDAPS and KWRF have their own assimilation systems and are characterized by IAU and DFI techniques, respectively.

There were several major improvements and changes in the KWRF 3dVar system in 2008:

- The number of vertical layers was increased from 31 to 40.

- The I/O and minimization processes were optimized to speed up 3dVar run.

- Typhoon bogus used for the global model was incorporated to enhance typhoon forecast performance.

- More QuikSCAT data became available by receiving BUFR format data from NOAA/NESDIS instead of the binary format data from NASA.

- MTSAT AMV data was subsequently assimilated.

- DFI was improved to suppress the noise in the analysis field more effectively. The improved DFI introduced 2-hour backward and forward integration with digital filtering, while the original used 2-hour backward integration without digital filtering and 4-hour forward integration with digital filtering.

4.3.1.2	Research performed in this field

- RARS assimilation experiments

RARS was assimilated through KWRF 3dVar and its impact was evaluated. The RMSE of forecast against observation was slightly decreased and the accuracy of precipitation forecast was improved.

- Calculation using seasonal background error

The results of KWRF cycle experiments with the seasonal background error were compared with those with the annual background error. It was found that the impact of the seasonal background error was not as pronounced as expected. The seasonal period might be redefined and abnormal patterns should be excluded in calculating the background error.

- Tests of First Guess at Appropriate Time(FGAT)

FGAT has been tested using KWRF over the East Asia domain. The verification score of FGAT was similar to 3dVar. Further research is required, including tuning of the observation error and quality control parameters with more observations such as satellite and aircraft data within the assimilation window.

#### 4.3.2	Models

4.3.2.1	In operation

KMA runs the RDAPS twice a day. The RDAPS was constructed based on the NCAR/PSU meso-scale model (so called MM5) and has been operated since 1997. At the beginning of its operation the RDAPS had single domain of 40km grids and 23 vertical layers. After going through updates for about 7 years, the RDAPS has been freezing since 2004 with current features of the RDAPS. Currently, the RDAPS features 3 nested domains (30km, 10km, 5km), non-hydrostatic dynamics, etc. Following table illustrates key features of the RDAPS.

The 30km domain covers the East Asian region and forecasts for 66 hours. Because it also covers much of North Pacific Ocean, the RDAPS 30km is utilized in Typhoon Track and intensity forecasts in the Typhoon season when a Typhoon nears the Korean peninsula. The 10km domain covers the Korean peninsula and its encompassing areas. It has its own analysis cycle using 3dVar technique. The 5km domain covers south Korea. The 10km and 5km domains are for prediction of high-impact weather and forecast for 24 hours.

###### Key model parameters of RDAPS

| Assimilation | Four-dimensional Data Assimilation with nudging (FDDA) |
| --- | --- |
| First guess | GDAPS previous 6-hour prognosis |
| Observations | SYNOP, TEMP, PILOT, ACARS, SATEM, and SATOB with 12 hour interval Radar data for 10km grid spacing with 3-hour interval AWS for 10km and 5km grid spacing with 3-hour interval |
| Method | FDDA(Grid Nudging)/3dVar (for nested 10 km domain) |
| Variables | Wind, geopotential height, and relative humidity |
| Vertical levels | 33 model sigma levels |
| Dynamics |  |
| Grids | Triply nested domain (30km for 171 x 191, 10km for 160 x 178 and 5km for 141 x 141 gird points) |
| Numerics | Primitive equations based on the non- hydrostatic frame |
| Vertical resolution | 33 layers with the model top of 50 hPa |
| Boundary condition | Time and inflow/ outflow dependent relaxation |
| Boundary update Frequency | 30km : 12-hour interval by GDAPS forecasts 10km : 3- hour interval by 30km forecasts 5km : 3- hour interval by 10km forecasts |
| Time integration | 66 hours for 30km mesh, and 24 hours for both 10km and 5km meshes |
| Physics |  |
| Horizontal Diffusion | Fourth order diffusion |
| Precipitation physics | Explicit moisture scheme |
| Deep convection | New Kain-Fritch only for 30 km and 10km grid domains |
| Planetary layer | Non-local boundary layer |
| Surface physics | 5-layer soil model for ground temperature |
| Radiation | Simple cloud scheme |

4.3.2.2	Research performed in this field

KMA plans to operate the Unified Model as its regional model with 10-km resolution (hereafter RUM, Regional UM) to replace RDAPS, all three domains with 30-, 10-, and 5-km resolutions respectively, in January 2010. RUM has been extensively tested to improve the predictability of rainfall forecast over the Korean Peninsula. Its results are compared with those of RDAPS and KWRF, which has been in parallel operation with RDAPS since May 2007. The forecast performance of RUM shows no improvement over the other two. We expect it to be enhanced with the introduction of 4-dimensional variational assimilation to RUM in October 2010. Currently, we tune parameterisation schemes, especially microphysics, and assimilate rainfall rate with a nudging scheme. The nudging rainfall rate improves rainfall forecast, especially in the summer. The configuration of RUM is as follows:

| Frame |  |
| --- | --- |
| Horizontal resolution | ~10km (574(514 / 0.015((0.09() |
| Vertical resolution | L38 (top ~ 36km) |
| Forecast length | 3 days |
| Data assimilation | None (going to be 4dvar on October 2010) |
| Physics |  |
| Large scale precipitation | Improved mixed phase |
| Convection | CMODS |
| Planetary layer | Non-local + revised diagnosis of K profile depth |
| Gravity wave drag | New orographic scheme |
| Radiation | General 2-stream radiation |

#### 4.3.3	Operationally available NWP products

See 4.2.3

#### 4.3.4    Operational techniques for application of NWP products

4.3.4.1	In operation

Three statistical approaches are operated for KMA digital forecast which has been operated since October 2008. The MOS from RDAPS is used to derive eight elements, spot temperature, maximum temperature, minimum temperature, probability of precipitation, relative humidity, precipitation type, wind speed and wind direction. The PPM from RDAPS is used to derive sky cover. The interpretation algorithm of PPM is based on Arabey diagram (Chernykh and Eskridge 1996). The model direct interpretation is used to derive snow depth which is analyzed with mixing ratio of hydrometeor predicted from RDAPS. The ten forecast elements are generated up to 66 hours twice a day.

PPM, Kalman filter and DLM have been operated since 1994. PPM from RDAPS is used to derive maximum temperature, minimum temperature and probability of precipitation. DLM from RDAPS and KWRF is used to derive spot temperature while Kalman filter from RDAPS and KWRF is used to derive maximum temperature and minimum temperature.

4.3.4.2	Research performed in this field

Temperature MOS equations for 205 points were redeveloped to improve the accuracy of Digital Forecast. The new equations were developed using a method similar to that of existing equations, except that the new equations cover 103 automatic weather station (meso-net) points and a new climatic predictor is added. RMSE of the equations decreased about 0.2 ℃, while the accuracy at AWS points did not match that of synoptic observation points.

The post-process for precipitation type MOS was designed to minimize unreasonable prediction. As the MOS equation was developed using multiple linear regression, a snow prediction is possible on a warm day when a predictor is computed in abnormally great magnitude. In order to suppress this problem, the MOS equation is applied only in the neighbourhood of freezing point 0℃.  The new post-process increases threat score from 0.64 to 0.89 for snow.

These two research results have been applied to KMA’s Digital Forecast system since October 2008.

#### 4.3.5	Ensemble Prediction System

4.3.5.1	In operation

No short-range EPS system is in operation at KMA.

4.3.5.2	Research performed in this field

The Short-range Ensemble Prediction System (SENS), based on a multi-model system with 4 different regional models, i.e., WRF, MM5, RAMS and Generalized Sigma coordinate MM5 (GSMM5), has been in development since 2004. SENS has 16 members with 18-km horizontal resolution and 35 vertical layers. A training method was developed using the genetic algorithm for a short-range forecast. For probabilistic training, BMA (Bayesian Mean Averaging) and logistic regression methods were adopted.

#### 4.3.5.3	Operationally available EPS Products

Nothing to report

4.4    Nowcasting and Very Short-Range Forecasting Systems (0-6 hrs)

4.4.1		   Nowcasting system

4.4.1.1		   In operation

No nowcasting system is in operation at KMA.

4.4.1.2   Research performed in this field

McGill Algorithm for Precipitation nowcasting by Lagrangian Extrapolation (MAPLE) is on a real-time experimental run after implementation of a successful variational echo tracking (VET) algorithm and semi-Lagrangian advection scheme with KMA composite radar data.

4.4.2	   Models for Very Short-range Forecasting Systems

4.4.2.1		   In operation

No VSRF system is in operation at KMA.

4.4.2.2    Research performed in this field

KMA has constructed an analysis and forecasting system for very short-range forecasting. It is based on Local Analysis and Prediction System (LAPS), developed at Global Systems Division (GSD) of NOAA (National Oceanic and Atmospheric Administration), and WRF. The analysis component is for analyzing the current weather status and the forecasting component is for predicting future status of weather, especially rainfall. The system consists of two domains: 15-km and 5-km. WRF (15-km) has a 6-hour analysis and forecasting cycle. It provides initial and boundary condition for a 5-km resolution model. The 5-km resolution model generates an analysis field using LAPS and forecast for 12 hours every 3 hours. It is not a cycling system. The system has been run for almost a year. Rainfall verification against observations shows not only higher ETS (Equitable Threat Score) but also produces higher Bias. The cause of such over-forecasts of rainfall is under investigation.

### Specialized numerical predictions

#### 4.5.1	Numerical prediction system for tropical cyclone

The numerical prediction system for tropical cyclones is based on with a horizontal resolution of T426 and 40 vertical levels of hybrid sigma-pressure coordinates. We have also adopted supplementary numerical models such as Double Fourier Series BARotropic typhoon prediction model (DBAR), and MTM (Moving-nest Typhoon Model). DBAR was originally developed by Cheong et al. (2002) in 2002 and introduced for operational TC forecast in 2004. The specifications for DBAR are summarized in Table 4.1.

MTM, also developed in 2002 by Kwon et al., was installed on CRAY X1E in 2006. This model has been adopted for operational TC forecast since 2007. MTM is based on MM5 (a mesoscale model) and GFDL-type typhoon initialization. The bogus procedure starts by initializing the winds within the bogus area. The main difficulty lies in the generation of other variables, such as humidity, temperature, geopotential, etc., which are dynamically consistent with the prescribed wind. However, it was found that there is a simple and practical way to initialize TC, achieved with the use of a built-in function of MM5, the four-dimensional data assimilation (FDDA). A miniature RDAPS is constructed for this purpose. After the initialization of wind within the filter region, all other variables are generated by the model through a strong 24-h nudging to the prescribed wind. It is found after careful analyses that there is an improvement over the no-bogus model.

Table 4.1. Double Fourier Series Barotropic Typhoon Prediction Model (DBAR)

| Input data | GDAPS analysis |
| --- | --- |
| Vortex bogusing and initialization | Geophysical Fluid Dynamics Laboratory (GFDL) bogussing |
| Dynamics | Spectral method using Double Fourier Series |
| Basic equation | Shallow water equations on the latitude-longitude coordinate |
| Horizontal representation | Grid distance of 0.356° |
| Domain | 1024 x 512 |
| Products | Central position (lat./lon.) every 6 hours up to 72 hours in advance. |

4.5.2	Ocean wind wave prediction systems

A major upgrade of ocean wind wave prediction systems took place in early 2008. The previous regional wave prediction system ‘ReWAM’ was replaced by ‘ReWW3’. The primary change consists of modifying the wave model source code from WAM cycle 4 (WAMDI, 1988) to WAVEWATCH-III ver. 2.22 (Tolman et al. 2002). The spatial resolution of the ReWW3 is increased from 1/4° of ReWAM to 1/12°, and the directional discretion is also increased from 15° to 10°. To resolve the scattered islands and complex coast lines, a spatial mesh of 1/120° (approx. 1km resolution) is newly implemented in domains of 3° longitude by 2° latitude nested inside ReWW3. The high-resolution coastal wave system is named CoWW3; there are six CoWW3 systems covering the coast of the Korean peninsula. Table 4.2 summarizes the configurations of the new wind wave prediction systems.

Table 4.2. Configuration of operational ocean wind wave prediction systems

|  | GoWAM | ReWW3 | CoWW3 (6 Domains) |
| --- | --- | --- | --- |
| Code | WAM cycle 4 | WAVEWATCH-III v. 2.22 |
| Coordinate | Spherical Coordinate |
| Domain | 70°S-70°N 0°E-358.75°E | 20°N-50°N 115°E-150°E | RGW1: 36.50°-38.50°N, 124.0°-127.0°E RGW2: 34.75°-36.75°N, 124.0°-127.0°E RGS1: 33.00°-35.00°N, 125.0°-128.0°E RGS2: 33.50°-35.50°N, 127.5°-130.5°E RGE1: 37.00°-39.00°N, 127.5°-130.5°E RGE2: 35.25°-37.25°N, 128.5°-131.5°E |
| Spatial Res. & Dimensions | 1.25° (288 by 113) | 1/4° (421 by 361) | 1/120° (361 by 241) |
| Spectral Res. | 25 frequencies 36 directions |
| Time Step | 720 sec | 300 sec | 30 sec |
| Forecast Length | 256 hours | 66 hours | 24 hours |
| Number of Runs | 2 times / day (00, 12 UTC) |
| Initial & Boundary Data | Previous Runs 12 hour Forecast | Previous Runs 12 hour Forecast ReWW3 boundary |
| Forcing Data | GDAPS Sea SFC Winds | RDAPS Sea SFC Winds (3 hours interval) |

4.5.3	Storm surge/tide prediction system

The Storm Surge/tide Operational Model (STORM) of KMA covers 115°-150°E, 20°-52°N, based on POM (Princeton Ocean Model) (Blumberg and Mellor 1987) with 1/12° horizontal resolutions including the Yellow Sea, East China Sea and the East Sea, and marginal seas around Korea. Table 4.3 summarizes the configuration of the STORM system.

Table 4.3. Configuration of STORM system

| Model | 2-D Ocean Circulation Model (POM 2D) |
| --- | --- |
| Coordinate system | Spherical coordinate |
| Model domain | 115 (E-150 (E, 20 (N-52 (N |
| Horizontal resolution | 1/12 ( by 1/12 (, (421 (385) |
| (T | 200 sec |
| Prediction time | 48 H (00,12UTC) |
| Initial field | Hot start |
| Input data | RDAPS Sea Wind and Pressure, 8 tidal constituents |

### 4.6	Extended range forecasts (ERF) (10 days to 30 days)

#### 4.6.1	Models

4.6.1.1	In operation

Global Climate Model

The operational extended forecasts system is based on the global spectral model, GDAPS, with a horizontal resolution of T106 and 21 vertical levels of hybrid sigma-pressure coordinates. For Ensemble forecasts, we utilize 20 ensemble members with a lagged average method with about a 15-day forecast lead time. The specifications for the model are summarized in Table 4.4.

Table 4.4. Detailed description for global climate model

|  |  | GDAPS(Operational model) |
| --- | --- | --- |
| Major Physics | Cloud Convection | Kuo |
|  | Land Surface & PBL | SiB Yamada-Meller |
|  | Radiation | Lacis & Hansen for SW Roger & Walshaw Glodman & Kyle Houghton for LW |
|  | Large scale condensation | Kanamitsu et al. |
| Dynamics | Three-dimensional global spectral model with hydrostatic primitive equations Hybrid sigma-pressure coordinate Semi-implicit method |
| Resolution | T106L21 |
| Ensemble size | 20 members |
| Sea Surface Temperature | Predicted SST anomaly |
| Land Surface Initial Condition | Observed Climatology |
| Model Climatology | SMIP2/HFP simulation (1979 to 2006) |
| Forecast range | 1-month forecast 3-month forecast 6-month forecast |

Global sea surface temperature forecasting system

The El Nino prediction system (Kang and Kug, 2000) is based on an intermediate ocean and statistical atmosphere model. The ocean model differs from the Zebiak and Cane (1987) model in the parameterization of subsurface temperature and the basic state. The statistical atmosphere model is developed based on the singular value decomposition (SVD) of wind stress and SST.

To reduce the uncertainty of the initial field on the ENSO model, the breeding technique is applied. In the case of an ideal experiment, this would contribute to better predictability, while for our El Nino prediction model, its effect is not as clear because of its weak nonlineality. Our study thus suggests some possibilities for coupled GCM to contribute to the improvement of predictability for complicated future ENSO prediction.

In order to improve the western Pacific SST prediction, KMA introduced a heat flux formula and vertical mixing parameterization to its ocean model. The model is initialized by combining observed SST and wind stress. Wind stress is calculated by using the 925hPa wind of the NCEP/NCAR reanalysis data. The method with calculated wind stress for initialization has shown a better forecast skill than that with FSU wind stress in recent predictions (Kug et al. 2001). In addition, the present prediction is attended with random noise thought to be weather noise, and generates many sets of prediction. Our approach for random noise is similar to that of Kirtman and Schopf (1998).

A statistical model is also applied to correct the systemic error in the prediction model. The Coupled Pattern Projection Model (CPPM, Kang et al. 2004) used is a pointwise regression model, and the main idea of the model is to generate realization of predictions from projections of covariance patterns between the large-scale predictor field and regional predictions onto the large-scale predictor field of the target year. By applying this model to the dynamic model results and compositing the results from both the dynamical and statistical models, the predictability over the tropical Pacific is improved from before.

To predict the entire global SST, a statistical global SST prediction system is being developed by combining the Coupled Pattern Projection Model (CPPM), the Lagged Linear Regression Method (LLRM), the El Nino prediction model, and the persistence method. In the tropical Pacific, predictions produced by the El Nino prediction model are used, whereas in other regions the best results from CPPM, LLRM, and persistence are used. LLRM is a pointwise statistical model based on the lag relationship between the global SST and ENSO index; the optimal lag is selected using the hindcast process in the model. This development is for determining the Indian SST prediction. Using this global ocean forecasting system, boundary conditions for the global climate model are also produced.

4.6.1.2	Research performed in this field

No activity to report

#### 4.6.2	Operationally available NWP model and EPS ERF products

Nothing to report

### 4.7 	Long-range forecasts (LRF) (30 days up to two years)

4.7.1	In operation

The long-range forecast system is identical to the extended range forecast system described in section 4.6, except for the forecast range. The official products of extended range forecasts are 3-categorical forecasts of temperature and precipitation over Korea for the upcoming 3 months (see 4.7.3).

For long-range forecasts, we also utilize the multi-model ensemble (MME) technique developed and operated at APEC Climate Center (APCC). The APCC collects the historical and real-time forecast data of 15 different models from 8 countries for its automatic MME input data producing system. The APCC has developed various MME techniques for deterministic and probabilistic seasonal predictions. For deterministic forecast, three kinds of linear MME techniques are used, namely biased and unbiased simple composite, weighted combination of multi-models based on SVD, and MME with statistical corrections. For probabilistic forecast, three ranges are determined by a ranking method based on the percentage of ensemble members from all the participating models in those three categories. A regional version of the MME system, MME I-IV, has been developed for the Asian Monsoon region.

4.7.2	Research performed in this field

In order to support operational LRF, especially for local provinces, a dynamical downscaling system (with a horizontal grid distance of 30-km) has been constructed by the National Institute of Meteorological Research (NIMR), KMA. This system is based on RegCM3 (ICTP Regional Climate Model Version 3), developed by Giorgi et al. (1993a, b) and improved by Pal et al. (2007). Lateral boundary forcing updated by every 6-hour and daily mean SST to drive RegCM3 are obtained from forecast fields from KMA’s operational LRF model (GDAPS) and predicted SST, respectively. In light of findings from a few sensitivity studies on a cumulus parameterization scheme (CPS) and treatment of lateral boundary condition, the model configuration was set as shown in Table 4.5.

Hindcast simulation was conducted for 10 years from 1996 to 2005, with each year’s simulation consisting of 10 ensemble members. As of 2008, hindcast run was completed for winter (DJF) and spring (MAM) seasons. In terms of skill score, dynamical downscaling is able to increase predictability of precipitation, surface temperature as well as upper atmospheric circulation, compared to the global climate model GDAPS.

| Table 4.5. RegCM3 configuration |
| --- |
| Prototype | PSU/NCAR MM4 (hydrostatic) |
| Resolution | 30-km in horizontal grid distance (96x80), 18 sigma layers |
| Physics | Radiation | CCM3 (Kiehl et al. 1996) |
|  | Convective precipitation | MIT-Emanuel (Emanuel and Zivkovic-Rothman 1999) |
|  | Large-scale precipitation | Sundqvist et al. (1989) |
|  | PBL | Non-local diffusion(Holtslag et al. 1990) |
|  | Land surface | BATS (Dickinson et al., 1993) |
| Lateral boundary condition | Exponential relaxation (Giorgi et al. 1993a, b) with orography blending (Hong and Junang 1998) |

Another research focus in the LRF area is the development of a 12-month climate prediction system. Under KMA’s strategy for seamless prediction from weather to climate, HadGEM2-A and HadGEM2-AO based on the Met Office Unified Model were installed and tested in CRAY-X1E.  Beginning in 2008, AMIP-type simulation for 23 years from 1978 was conducted and the 20 years’ results from 1979 to 1998 were analyzed. Compared to the CMAP observed precipitation, the UM-simulated precipitation is able to produce spatial ITCZ patterns; however, it overestimates the precipitation over the Northern Hemispheric central and western Pacific and underestimates over the eastern Pacific. Meanwhile, the UM simulates the vertical structure of zonal wind fairly well compared with the NCEP/DOE reanalysis. For the East Asian summer monsoon variability, the spatial patterns of the EOF first mode from the CMAP-observed and UM-simulated precipitation are quite close to each other with a slight southward displacement in the simulated precipitation. However, somewhat large discrepancies are apparent in regional- or local-scale circulation in East Asia, and call for further investigation.

In order to reduce uncertainties of the dynamical climate model and develop a probabilistic forecast method as one of the post-process in the climate prediction system, a statistical model was developed to minimize the systematic error of GDAPS using a new statistical approach, i.e., the regularized canonical correlation analysis (CCA) and Bayseian linear model (BLM). The conventional EOF/CCA was also applied for comparison with the capability of the newly developed method. The regularized CCA method shows better skill scores compared with the conventional method as well as GDAPS itself. This method is particularly effective when the interesting area is focused only on a specific region rather than a global one, with skill scores both for the precipitation and lower-atmospheric temperature quite improved. This study also suggested BLM as a new climate prediction method. The basic idea of BLM is to produce forecast by calculating posterior probability distribution using prior probability distribution and statistical models or likelihood. Finally, a probability distribution function for climate prediction was constructed using the GDAPS summertime hindcast and forecast data. This work consists of three procedures, which are producing prediction data using a cross-validation method, estimating the probability distribution of the prediction data, and probabilistic forecast based on percentile.

#### Operationally available EPS LRF products

|  | 1-month forecast | 3-month forecast | Seasonal climate outlook |
| --- | --- | --- | --- |
| Issue Date | · 3rd , 13th, and 23rd day of each month | · 23rd day of each month | · 23rd day of Feb., May, Aug., and Nov. |
| Forecast type | Three-category forecast : Above, below and near normal The anomalies are based on model’s climatologies obtained from a 28 year database (1979 to 2006). |
| Contents | · 10-day mean temperature and precipitation · 30-day mean temperature and precipitation | · 1-month mean temperature and precipitation · 3-month mean temperature and precipitation *1Asian dust outlook *2Typhoon outlook | · seasonal temperature and precipitation |
| Forecast area | Korea | Korea | Korea |

*1Asian dust outlook is issued in late February including the number of days of Asian dust expected to affect Korea for the upcoming spring.

*2 Typhoon outlook is issued in late May and Aug. regarding the number of Typhoon expected to affect Korea for the upcoming summer and autumn.

## 5.	Verification of prognostic products

5.1	Annual verification summary

The summary of annual verification statistics for GDAPS is calculated by comparing the model forecast to the analysis and radiosonde observation (see Table 5.1 and 5.2). Table 5.3 to 5.7 present detailed monthly verification statistics for GDAPS, by comparing the model forecast against the analysis.

Table 5.1. RMSE verification of KMA’s global model (GDAPS) against the analysis in 2008

| Statistic | Area. | T+24 hr | T+72 hr | T+120 hr |
| --- | --- | --- | --- | --- |
| Z500 | Northern Hemisphere | 15.74 | 37.79 | 63.49 |
| Z500 | Southern Hemisphere | 22.43 | 53.78 | 84.12 |
| V250 | Northern Hemisphere | 5.91 | 11.26 | 16.52 |
| V250 | Southern Hemisphere | 6.55 | 13.40 | 18.86 |
| V250 | Tropics | 5.95 | 9.22 | 11.94 |
| V850 | Tropics | 2.96 | 4.59 | 5.21 |

Table 5.2. RMSE verification of KMA’s global model (GDAPS) against observation in 2008

| Statistic | Area. | T+24 hr | T+72 hr | T+120 hr |
| --- | --- | --- | --- | --- |
| Z500 (geopotential height) | North America | 18.80 | 42.42 | 66.87 |
| Z500 | Europe | 16.63 | 36.10 | 64.61 |
| Z500 | Asia | 18.37 | 34.42 | 53.01 |
| Z500 | Australia/ New Zealand | 20.56 | 39.12 | 63.65 |
| V250 (wind) | North America | 8.21 | 14.70 | 20.65 |
| V250 | Europe | 7.14 | 12.72 | 19.17 |
| V250 | Asia | 7.59 | 12.34 | 16.43 |
| V250 | Australia/ New Zealand | 9.00 | 14.66 | 19.59 |
| V250 | Tropics | 7.50 | 10.04 | 11.67 |
| V850 | Tropics | 4.80 | 5.75 | 6.03 |

Table 5.3.  Monthly mean RMSE of 500 hPa geopotential height forecast (m) in the Northern Hemisphere (GDAPS verification against analysis).

| FCST | Jan. | Feb. | Mar. | Apr. | May | Jun. | Jul. | Aug. | Sep. | Oct. | Nov. | Dec. | Ave. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24H | 19.15 | 19.87 | 17.56 | 16.12 | 14.41 | 14.17 | 12.78 | 12.79 | 13.02 | 14.10 | 16.66 | 18.19 | 15.74 |
| 72H | 45.15 | 48.56 | 41.39 | 39.49 | 35.76 | 33.23 | 29.09 | 30.43 | 30.69 | 35.07 | 40.22 | 44.45 | 37.49 |
| 120H | 71.66 | 75.14 | 70.09 | 67.45 | 62.28 | 55.91 | 48.97 | 49.10 | 54.20 | 63.38 | 67.10 | 76.64 | 63.49 |

Table 5.4.  Monthly mean RMSE of 500 hPa geopotential height forecast (m) in the Southern Hemisphere (GDAPS verification against analysis)

| FCST | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Ave |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24H | 20.48 | 19.84 | 21.37 | 21.66 | 22.92 | 23.79 | 24.63 | 24.91 | 25.31 | 22.57 | 21.26 | 19.37 | 22.43 |
| 72H | 47.69 | 47.47 | 53.34 | 54.20 | 55.96 | 58.58 | 58.39 | 63.20 | 59.43 | 51.37 | 49.64 | 46.10 | 53.78 |
| 120H | 72.55 | 75.22 | 79.60 | 88.58 | 87.60 | 92.63 | 96.35 | 98.71 | 90.13 | 77.29 | 77.99 | 72.76 | 84.12 |

Table 5.5.  Monthly mean RMSE of 250 hPa wind forecast (m/s) in the Northern Hemisphere (GDAPS verification against analysis)

| FCST | Jan. | Feb. | Mar. | Apr. | May | Jun. | Jul. | Aug. | Sep. | Oct. | Nov. | Dec. | Ave. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24H | 6.18 | 6.34 | 6.03 | 5.87 | 5.93 | 5.79 | 5.61 | 5.74 | 5.53 | 5.56 | 6.04 | 6.29 | 5.91 |
| 72H | 11.63 | 11.96 | 11.33 | 11.15 | 11.51 | 11.10 | 10.20 | 10.96 | 10.63 | 10.96 | 11.65 | 12.10 | 11.26 |
| 120H | 16.32 | 17.14 | 16.82 | 16.45 | 17.08 | 16.09 | 14.65 | 15.56 | 15.84 | 16.87 | 17.09 | 18.29 | 16.52 |

Table 5.6.  Monthly mean RMSE of 250 hPa wind forecast (m/s) in Southern Hemisphere (GDAPS verification against analysis).

| FCST | Jan. | Feb. | Mar. | Apr. | May | Jun. | Jul. | Aug. | Sep. | Oct. | Nov. | Dec. | Ave. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24H | 6.22 | 6.22 | 6.39 | 6.66 | 6.77 | 6.95 | 6.76 | 7.03 | 6.64 | 6.31 | 6.42 | 6.20 | 6.55 |
| 72H | 12.78 | 12.70 | 13.62 | 13.87 | 13.56 | 14.52 | 13.49 | 14.36 | 13.82 | 12.60 | 12.84 | 12.65 | 13.40 |
| 120H | 17.94 | 18.16 | 18.33 | 19.87 | 19.27 | 20.71 | 19.60 | 19.80 | 19.14 | 17.46 | 18.38 | 17.69 | 18.86 |

Table 5.7. Monthly mean RMSE of 250 hPa wind forecast (m/s) in the Tropics (GDAPS verification against analysis).

| FCST | Jan. | Feb. | Mar. | Apr. | May | Jun. | Jul. | Aug. | Sep. | Oct. | Nov. | Dec. | Ave. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24H | 6.47 | 6.50 | 6.11 | 5.99 | 5.96 | 5.88 | 5.80 | 5.92 | 5.60 | 5.43 | 5.83 | 5.88 | 5.95 |
| 72H | 10.74 | 10.57 | 10.18 | 10.19 | 9.91 | 9.83 | 9.46 | 9.68 | 9.64 | 9.32 | 9.67 | 9.83 | 9.92 |
| 120H | 13.01 | 12.53 | 11.96 | 12.15 | 12.07 | 12.11 | 11.50 | 11.43 | 11.33 | 11.30 | 11.77 | 12.18 | 11.94 |

### 5.2	Research performed in this field

No activity in this field

## 6.	Plans for the future (next 4 years)

### 6.1	Development of GDPFS

    - Major changes in operational DPFS expected in the next year

Installation of a new super computer at KMA

KMA is going to install a new super computer at KMA in the later half of 2009. All the NWP systems based on UM, which are in test run in the current super computer, will be migrated to the new super computer. KMA will put all the effort to the preparation of the operation of new NWP system based on UM in the installed super computer.

6.1.2 Major changes in operational DPFS envisaged within the next 4 years

Operation of the new NWP system based on UM

KMA will start the operation of the UM-based global and regional NWP system in January 2010. The resolution will be N320(40km) with 50 levels for global, and 10km with 38 levels for regional model. All the observations collected by KMA will be used for the data assimilation system. 4dVar will be employed to provide initial fields to global model. Regional model will acquire its initial and boundary conditions from the global model.

In October 2010, the resolution of the global model will be enhanced to N512L70 (25km), and a global ensemble prediction system based on Met Office Global and Regional Ensemble Prediction System (MOGREPS) will start its operation. The ensemble system will have N320 (40km) horizontal resolution and 50 levels vertically. It will use total of 24 members including 1 control forecast.

The 10-km regional model will be equipped with a 4dVar system in October 2010. The background error for East Asia will be recalculated to consider the regional dependency of model error and will be applied to the regional 4dVar cycle.

KMA also plans to configure its higher-resolution model based on UM with 4dVar. The horizontal resolution will be less than 3-km and focus mainly on the enhancement of rainfall forecast over the Korean peninsula. The main feature on the higher-resolution model is for assimilating radar data, reflectivity and radial velocity, and rainfall. It is expected to produce better forecast of heavy rainfall.

### 6.2	Planned research activities in NWP, nowcasting and long-range forecasting

6.2.1 Planned research activities in NWP

The impact of various satellite data will be tested in 2010. Infrared Atmospheric Sounding Interferometer (IASI) temperature and humidity and Advanced Scatterometer (ASCAT) winds from Meteorological Operational satellite (METOP), a polar orbiting satellite launched by the EUMETSAT, will be examined for operation.

Bias correction of the satellite data should be tried to get better impact than the original data. KMA Automatic Weather Station (AWS) and radar data will be also used for the high resolution regional model. The verification tools for estimating the impact of observation data will be developed to improve the reliability of evaluation.

Transition to the hybrid data assimilation which combines the 4dVar and the ensemble Kalman filter will be tested as a part of long term strategy and the related study to build the hybrid system and to check its impact will be executed.  The study results will be used as the basic data to construct the hybrid system.

For the global domain, the impact of the temperature and humidity vertical profiles from GPS Radio Occultation (GPSRO) and Special Sensor Microwave Imager/Sounder (SSMIS) will be estimated.  Radar data will be tested with high resolution (3km) regional model. The various studies to enhance the accuracy and reliability of the data from Communication, Ocean, and Meteorological Satellite (COMS, the first Korea geostationary satellite), which is supposed to be launched in 2009, will be proceeded providing the guideline for the operational use of COMS.

An ensemble training technique will be developed for the support of point forecast in Weather Information Digital (WID) in 2010. The candidate training (learning) methods are artificial life (AL), artificial intelligence (AI), and a hybrid of both. This is similar to the MME technique in a long-range forecast.

6.2.2 Planned research activities in nowcasting

From 2010, a precipitation nowcasting based on a mesoscale model output will be issued by the correction of model errors (phase and intensity errors). This method starts with the systematic evaluation of model errors from a mesoscale model and their consistency in space and time. This correction algorithm assumes the consistency of model errors in time and utilizes radar extrapolation techniques to advect model errors into the future.

6.2.3 Planned research activities in long-range forecasting

Y2009:

- Introduction of GloSea4 based on HadGEM3 and its installation into KMA’s supercomputer

Y2010:

- 15-years’ hindcast using GloSea4 with 30 ensemble members

- Setup of HadREM3 for dynamical downscaling

Y2011:

- Operational launch of new seasonal forecast system based on GloSea4

- Hindcast using GloSea4 for 12-month climate prediction

- Hindcast using HadREM3 for seasonal forecast

Y2012:

- Semi-operation of 12-month climate prediction system

- Operational launch of dynamical downscaling system for seasonal forecast

## 7. 	References

Blumberg, A. F. and G. L. Mellor, 1987: A description of a three-dimensional coastal ocean circulation model. In Heaps (Eds.), Three dimensional Coastal Ocean Models, pp. 1-16, American Geophysical Union, Washington, DC.

Cheong, H.-B., I.-H. Kwon, T.-Y. Goo, and M.-J. Lee, 2002: High-order harmonic spectral filter with the double Fourier series on a sphere, J. Comput. Phy., 177, 313-335.

Chernykh, I. V. and R. E. Eskridge, 1996: Determine of cloud amount and level from radiosonde soundings. J. Appl. Meteor. 35, 1362-1369.

Chun, H.-Y., and J.-J. Baik, 1998: Momentum flux by thermally induced internal gravity waves and its approximation for large-scale models. J. Atmos. Sci., 55, 3299-3310.

Cui, B., Toth, Z., Zhu., Hou, D., and Beauregard, S.: Statistical post-processing of operational and CDC hindcast ensembles, Preprints, 21st Conference on weather analysis and forecasting/17th Conference on Numerical Weather Prediction. Washington DC, 1-5 August 2005, Amer. Meteor. Soc., 12B.2, 2005.

Dickinson, R. E., A. Henderson-Sellers, and P. J. Kennedy, 1993: Bioisphere-atmosphere transfer scheme (BATS) version 1e as coupled to the NCAR community model, NCAR TN+STR.

Emanuel, K. A., and M. Zivkovic-Rothman, 1999: Development and evaluation of a convection scheme for use in climate models, J. Atmos. Sci., 56, 1766-1782.

Giorgi , F., M. R. Marinucci, and G. T. Bates, 1993a: Development of a second generation regional climate model (RegCM2). Part I: Boundary layer and radiative transfer processes. Mon. Wea. Rev., 121, 2794-2813.

Giorgi , F., M. R. Marinucci, G. T. Bates, and De Canio, 1993b: Development of a second generation regional climate model (RegCM2). Part II: Convective processes and assimilation of lateral boundary condition, Mon. Wea. Rev., 121, 2814-2832.

Holtslag, A.A.M., and B.A. Boville, 1993: Local versus nonlocal boundary-layer diffusion in a global climate model, J. Climate, 6, 1825-1842.

Holtslag, A. A. M., E. I. F. de Brujin, and H.-L. Pan, 1990: A high resolution air mass transformation model for short-range weather forecasting, Mon. Wea. Rev., 118, 1561-1575.

Hong, S.-Y., and H. M.-H. Junang, 1998: Orography blending in the lateral boundary of a regional model., Mon. Wea. Rev., 126, 1714-1718.

Iwasaki, T., S. Yamada and K. Tada, 1989: A parameterization scheme of orographic gravity wave drag with two different vertical partitionings, part 1: Impact on medium range forecasts. J. Meteor. Soc. Japan, 67, 11-41.

Kang, I.-S., and J.-S. Kug, 2000: An El-Nino prediction system using an intermediate ocean and a statistical atmosphere, Geophys. Res. Lett., 27, 1167-1170.

Kang, I.S., J.Y. Lee, and C.K. Park, 2004: Potential Predictability of Summer Mean Precipitation in a Dynamical Seasonal Prediction System with Systematic Error Correction. J. Climate, 17, 834–844.

Kiehl, J. T., J. J. Hack, G. B. Bonan, B. A. Bovile, B. P. Breigleb, D. Williamson, and P. Rasch, 1996: Description of the NCAR community climate model (CCM3), NCAR/TN-420+STR, NCAR.

Kirtman, B. P., and P. S. Schopf, 1998: Decadal variability in ENSO predictability and prediction, J. Climate, 11, 2804-2822.

Kug. J.-S., I.-S. Kang, and S. E. Zebiak, 2001: Impact of the model assimilated wind stress data in the initialization of an intermediate ocean model and the ENSO predictability. Geophys. Res. Lett., 28, 3713-3716.

Kwon, H.-J., S.-H. Won, M.-H. Ahn, A.-S. Suh, and H.-S. Chung, 2002: GFDL-type typhoon initialization in MM5. Mon. Wea. Rev., 130, 2966-2974.

Pal, J. S., F. Giorgi, X. B. N. Elguindi, F. Solmon, X. Gao, M. Ashfaq, R. Francisco, J. Bell, N. Diffenbaugh,  L. Sloan, A. Steiner, J. Winter, and A. Zakey, 2007: The ICTP RegCM3 and RegCNET: Regional climate  modelling for the development world. Bull. Amer. Meteor. Soc., 88, 1395-1409.

Sellers. P. J., Y. Mintz, Y.C. Sud and A. Dalcher, 1986: A simple biosphere model (Sib) for use within general circulation models. J. Atmos. Sci., 43, 505-531.

Sundqvist. H., E. Berge, and J. E. Kristjansson, 1989: The effects of domain choice on summer precipitation simulation and sensitivity in a regional climate model. J. Climate, 11, 2698-2712.

Tolman, H.L., Balasubramaniyan B., Burroughs L. D., Chalikov D. V., Chao Y. Y., Chen H. S., and Gerald V. M., Development and implementation of wind generated ocean surface wave models at NCEP, Z. Wea. Forecasting 17 (2002), 311-333.

WAMDI group, The WAM model – a third generation ocean wave prediction model, J. Phys. Oceanogr. 18 (1988), 1775-1810.

Zebiak, S. E., and M. A. Cane, 1987: A model El Nino - Southern Oscillation. Mon. Wea. Rev. , 115, 2262-2278.