ANNUAL JOINT WMO TECHNICAL PROGRESS  REPORT ON

THE GLOBAL DATA PROCESSING AND FORECASTING SYSTEM (GDPFS) INCLUDING NUMERICAL WEATHER PREDICTION (NWP) RESEARCH ACTIVITIES FOR 2009

THAILAND

1. SUMMARY OF HIGHLIGHTS

The Thai Meteorological Department  (TMD) has been running operational NWP models since March 2000.  There are three models: Global (100 km resolution), South East Asia (48 km resolution) and Thailand (17 km resolution). Forecasters use the products and they are satisfied with the performance of the models. The products are also required by other government agencies such as the Thai Royal Irrigation Department, Department of Disaster Prevention and Mitigation, the Royal Rain-

Making Office, and the Pollution Control Department.

In December 2004, time length forecasting of the Global model was extended from 3 days to 7 days.

2. EQUIPMENT IN USE

The IBM RS/6000 SP supercomputer is currently used in operation. It consists of six wide nodes (Power2 SC 135 MHz) and 32 thin nodes (Power2 SC 120 MHz). Each wide node  has 512 Mb of memory and 4.5 Gb storage and each thin node has 128 Mb of memory and 2.2 Gb storage. The total 32-node system has a peak performance of 7.488 GFLOPS (LINPACK DP) and a peak performance of 12.96 GFLOPS (LINPACK TPP). Two RS/6000 model 595 computers (Power2 SC 135 MHz) are used as high availability control workstations for the system. Image and graphics are displayed by the IBM RS/6000 43 P Model 140 workstations with POWER PC604e 233 MHz, 256 Mb memory and 9 Gb disk storage.

3. DATA AND PRODUCTS FROM GTS IN USE

Synoptic observations and various a-synoptic observation including satellite data are used daily in the GDAPS. The preprocessing procedures such as data acquisition ,quality control, and decoding are fully automated.

The following observations are daily averaged number used for running NWP models.

SURFACE - 7000 reports

SONDE - 540 reports

SATWIND - 1400 reports

AIRCRAFT - 5000 reports

4. FORECASTING SYSTEM

4.1 SYSTEM RUN SCHEDULE AND FORECAST RANGES

| Job no. | Time (UTC) | Model | Process | Used time |
| --- | --- | --- | --- | --- |
| 1. | Starting 0305 UTC (00Z Model run ) (Main run) | Asia | - Observation Processing (GTS data 00 UTC) - Model run (forecast T+72) used LBC 12Z - HORACE Data Conversion | ~ 3hr. 40min |
|  |  | Thailand | - Observation Processing (GTS data 00 UTC) - Model run (forecast T+36) used LBC 12Z - HORACE Data Conversion |  |
|  |  | Global | - Observation Processing ( GTS data 00 UTC) - Model run (forecast T+168 (7 days)) - HORACE Data Conversion - Generate Background field for 06Z Model run |  |
|  |  | Asia | - Observation Processing (GTS data 00 UTC) - Model run (forecast T+72) used LBC 00Z - HORACE Data Conversion - Generate Background field for 06Z Model run |  |
|  |  | Thailand | - Observation Processing (GTS data 00 UTC) - Model run (forecast T+36) used LBC 00Z - HORACE Data Conversion - Generate Background field for 06Z Model run |  |
|  |  | Asia | - SST and reconfiguration |  |
|  |  | Thailand | - SST and reconfiguration |  |
| 2. | Starting 0905 UTC (06Z Model run) (Intermediate run) | Global Asia Thailand | - Observation Processing (GTS data 06 UTC) - Model run - Generate Background field for 12Z Model run | ~ 40min |
| 3. | Starting 1505 UTC (12Z Model run ) (Main run) | Global | - Observation Processing (GTS data 12 UTC) - Model run (forecast T+168 (7 days)) - HORACE Data Conversion - Generate Background field for 18Z Model run | ~ 2hr. 40min |
|  |  | Asia | - Observation Processing (GTS data 12 UTC) - Model run (forecast T+72) - HORACE Data Conversion - Generate Background field for 18Z Model run |  |
|  |  | Thailand | - Observation Processing (GTS data 12 UTC) - Model run (forecast T+36) - HORACE Data Conversion - Generate Background field for 18Z Model run |  |
| 4. | Starting 2105 UTC (18Z Model run) (Intermediate run) | Global Asia Thailand | - Observation Processing (GTS data 18 UTC) - Model Run - Generate Background field for 00Z Model run | ~ 1hr |
|  |  |  | - Back up NWP data |  |
| 5. | Starting 2300 UTC |  | - Merge Step (Pre-verification create files for Asia and Thailand Verification System) | ~ 10min |
| 6. | Starting 2330 UTC |  | - Verification Step for Asia and Thailand Model | ~ 30min |

4.2 MEDIUM-RANGE FORECASTING SYSTEM (4-10 days)

4.2.1 Data assimilation, objective analysis and initialization

UK Met Office.

4.2.2 Model

Unified Model of UK Met Office (1998).

4.2.3 Operationally available Numerical Weather Prediction (NWP)

Products

Wind, pressure, temperature, etc. at standard pressure levels

4.2.4 Operational techniques for application of NWP products (MOS,

PPM, KF, Expert Systems ,etc.)

No activity in this area

4.2.5 Ensemble Prediction System (EPS) (Number of members, initial

state, perturbation method, model(s) and number of models used,

perturbation of physics, post-processing: calculation of indices,

clustering)

No activity in this area

4.3 SHORT-RANGE FORECASTING SYSTEM (0-72 hrs)

4.3.1 Data assimilation, objective analysis and initialization

UK Met Office.

4.3.2 Model

Unified Model of UK Met Office (1998).

4.3.3 Operationally available Numerical Weather Prediction (NWP)

Products

Wind, pressure, temperature, etc. at standard pressure levels

4.3.4 Operational techniques for application of NWP products (MOS,

PPM, KF, Expert Systems ,etc.)

No activity in this area

4.3.5 Ensemble Prediction System (EPS) (Number of members, initial

state, perturbation method, model(s) and number of models used,

perturbation of physics, post-processing: calculation of indices,

clustering)

No activity in this area

4.4 Nowcasting and Very short-range Forecasting Systems (0-6 hrs)

4.4.1 Nowcasting system

No such system is run

4.4.2 Models for Very short-range Forecasting Systems

No such system is run

4.5 Specialized numerical predictions

No such system is run

4.6 Extended range forecast (10 days to 30 days)

No such system is run

4.7 Long range forecasts 30 days to two years)

No such system is run

5. Verification of prognostic products

Not report

6. PLANS FOR THE FUTURE

a) Exploring the service oriented architecture in replacing existing mainframe

system with new open architect system.

b) Collaborating with TMD  in implementing higher resolution regional

mesoscale NWP models.

Reference

Met Office. Scientific & Technical Papers: Unified Model & Observation Processing

System. Bracknell, 1998.