# JOINT WMO TECHNICAL PROGRESS REPORT ON THE GLOBAL DATA PROCESSING AND FORECASTING SYSTEM AND NUMERICAL WEATHER PREDICTION RESEARCH ACTIVITIES FOR 2010

Botswana, Department of Meteorological Services

MARCH 2011

## Summary of highlights

| February 2010 | Upgrade of the HRM model to 60 layers to use the DWD 30L60 boundary files. |
| --- | --- |
| MAY 2010 | Upgrade of the WRF-EMS model to version 3 with 35 layers. |
| NOVEMBER 2010 | Upgrade the PUMA system to AMESD PUMA-Synergie system. |

## Equipment in use

  - Numerical Weather Prediction and Central Information Processing Systems:

2.1.1 A twenty four (24) node HP linux cluster is used for Numerical Weather Prediction and Central Information Processing (CIPS-NWP). Sixteen (16) nodes are dedicated to model computation with the following specification:

| Component | Description | Qty |
| --- | --- | --- |
| Master node | quad core xeon 2,6 Ghz | 2 |
|  | 6GB RAM |  |
|  | Gb Ethernet interface |  |
|  | Infiniband interface |  |
|  | Dual 4Gb Fiber HBA (Host Bus Adapter) for SAN (storage areanetwork) Attachment |  |
|  | (2) 72.8 GB SAS Hard drives in Raid 1 |  |
| Computation node | Blade system based: quad core xeon 2,6 Ghz | 16 |
|  | 4GB RAM |  |
|  | Gb Ethernet interface |  |
|  | Infiniband interface |  |
|  | (2) 72.8 GB SAS Hard drives in Raid 1 |  |

Three (3) nodes are used for Central Information Processing and storage purposes with the following specifications.

| Component | Description | Qty |
| --- | --- | --- |
| Database node | quad core xeon 2,6 Ghz | 3 |
|  | 6GB RAM |  |
|  | Gb Ethernet interface |  |
|  | 4Gb Fiber HBA for SAN Attachment |  |
|  | (2) 146.8GB SAS Harddrives Raid1 |  |

The storage system has the following configuration:

| Component | Description | Qty |
| --- | --- | --- |
| Tape library | 2 drives LTO3 | 1 |
|  | Dual 4Gb Attachment to fibre SAN switch |  |
|  | 10 TB scalable to 50 TB |  |
|  | Backup Software (server & agent) running on Linux with disaster recovery option. |  |
|  | License for 30 agents |  |
|  | LTO (tape format) tapes for 10 TB |  |
|  | 19-inch, industry-standard rack |  |

| Storage system | Scalable disk enclosure including: 1 TB of Fibre Channel disk | 1 |
| --- | --- | --- |
|  | 4 TB of SATA (serial ATA) disk |  |
|  | Dual 4 Gbps capable Fibre Channel interfaces |  |
|  | Upgradable up to 20 TB minimum |  |
|  | Management software (running on linux) |  |
|  | Dynamic Capacity Expansion |  |
|  | Dynamic Volume Expansion RAID level 0, 1, 3, 5 and 10 support |  |

2.1.2     A dual quad core Dell Linux workstation is also used to run a smaller domain Weather Research and Forecast (WRF) Environmental Modelling System (EMS) model:

- Linux operating system; Fedora core 6

- CPU 1.86 GHz

- 8 processors

  - Remote Sensing:

Puma (new)

- 3 Dell Optiplex 380 machines, PC 1 for data Reception (MSG, GTS Messages, Vegetation products from VGT4Africa etc)

- PC 2 and PC 3 for Data Processing and Visualization. Synergie software used for visualisation requires license.

AMESD eStation

- 3 Dell Optiplex 380 machines, PC 1 for data Reception (MSG, GTS Messages, Vegetation products from VGT4Africa etc)

- PC 2 (PS) and PC 3 (EMMA) for Data Processing and Visualization. Free software used.

DDS Receiver

- Receives MERIS satellite data

AMESD AFIS fire terminal

- 2 HP Compaq 6000 Pro machines, PC 1 for data Reception (MSG, GTS Messages, Vegetation products from VGT4Africa etc)

- PC 2 for Data Processing and Visualization. AFIS Terminal software used

2.3 Automatic Message Switching System (MSS):

The AMSS consists of:

- Three Dell duo core workstations running on Fedora Core 8 Linux operating system, 2 GB memory, 2 X 160GB HD.

- One workstation acts as a server running the weatherman software.

- E-mail capability as a backup to the leased lines.

- Visible public IP address for external communication

- An automatic plotter.

2.4 Trivis Weather Graphics System:

Two HP Intel Xeon processor workstations run the Trivis weather graphics system on the Enterprise Linux RedHat operating system. One computer acts as backup to the other.

## 3.	Data and Products from GTS in use

- SYNOP

- TEMP

- SHIP

- AMDAR

- AIREP

## 4.	Forecasting system

The Forecasting system consists of the following:

| Model | Grid-spacing | Initial time | Range | Levels | Boundary conditions |
| --- | --- | --- | --- | --- | --- |
| HRM | 12 km | 00Z and 12Z | 72 hours | 61 | DWD |
| WRF-EMS | 15 km | 00Z | 48 hours | 35 | NCEP-GFS |
| *SA-UM12 | 12 km | 00Z | 48 hours |  | UKMO |
| *GFS |  | 00Z and 12Z | 120 hours |  | Global |
| *ECMWF |  | 12Z | 120 hours |  | Global |

* These models are available as processed graphical products via the internet and through the Severe Weather Forecast Demonstration Project (SWFDP).

### 4.1	Forecast ranges

4.1.1 Short range forecast

High resolution Regional Model (HRM)

The Department runs the HRM model supplied by the Duetscher Wetterdienst (DWD)/ German weather centre on the linux cluster. The model runs operationally twice a day, at 00Z and 12Z to produce a 72-hour forecast. The domain of the regional model covers an area 100 W to 560 E and 1440 S to 00 N with 601 E-W by 401 S-N grid points at a grid spacing of 0.110 , that is about 12 km. See figure below.

Weather Research and Forecasting – Environmental   Modelling System (WRF-EMS)

The Department also runs the WRF-EMS on a smaller domain using the dual quad core Dell Linux workstation. The modelling system is supported by the United States-National Weather Service (US-NWS). The model runs with a grid spacing of 15 km over the following domain. (see figure below)

## 4.1.2 Medium range forecasts

European Centre for Medium range Weather Forecast (ECMWF) and Global Forecast System (GFS) graphical products are acquired through the internet and the SWFDP for use in medium range forecasts of up to 120 hrs.

## 5.	Plans for the future

### 5.1	Development of the GDPFS-NWP

5.1.1 Major changes in 2011

No major changes on the GDPFS-NWP are planned.

### 5.2	Planned Activities in NWP

5.2.1 Implementation of the HRM model verification package and Upgrade of HRM

The Department is looking into implementing an operational HRM model verification package.

## 6. 	References

Majewski, D., D. Liermann, P. Prohl, B. Ritter, M. Buchhold, T. Hanisch, G. Paul, W. Wergen and

J. Baumgardner, 2002: The operational global icosahedral-hexagonal gridpoint model GME: Description and high-resolution tests. Mon. Wea. Rev., 130, 319-338.

D. Majewski, DWD, FE13, April 2009 HRM- User’s Guide

Email Detlev.majewski@dwd.de

R. Rozumalski –NOAA/NWS/FDTB, May 2006  WRF Environmental Modelling System User’s Guide

Email Robert.rozumalski@noaa.gov

Web http://strc.comet.ucar.edu/wrfems

Links to centres that provide graphical forecasts :

http://www.weathersa.co.za/RSMC

http://www.wxmaps.org

http://www.metoffice.gov.uk/weather/africa/lam