Activities of RSMC Montréal During the Calendar Year 2010

Executive Summary

Primary activities for 2010 consisted of the RSMC monthly tests - conducted for scenarios over Canada, the United States, Japan, the Czech Republic, Indonesia and Australia - and incremental updates and improvements to the response procedures, software, and to the joint RSMC secure web pages, which are used for communicating transport model products between some of the RSMCs.  The Provisional Technical Secretariat (PTS) of the Comprehensive Test Ban Treaty Organization (CTBTO) made both operational and planned requests for inverse modelling support by RSMC Montréal in May, July, August, October and November.

1.	Introduction

The Canadian Meteorological Centre (Meteorological Service of Canada, Environment Canada) is designated by the WMO as the Montréal Regional Specialized Meteorological Centre (RSMC) for the provision of atmospheric transport modelling in case of an environmental Emergency Response. The primary regions of responsibility are WMO Regional Associations (RA) III & IV, which encompasses Canada, United-States, Mexico, Central and South America. In addition to emergency response, RSMC Montréal contributes global inverse modelling support to the CTBTO verification system.

2.	Operational Contact Information

Canadian Meteorological Centre (CMC)

Environment Canada

2121 Trans-Canada Highway

DORVAL, Québec

Canada H9P 1J3

Business contact: Mr René Servranckx

Tel	: 1 514 421 4704

Fax	: 1 514 421 4679

Email	: rene.servranckx@ec.gc.ca

Operational contact (24 hours): Shift supervisor

Tel	: 1 514 421 4635

Fax	: 1 514 412 4639

3. 	Responses and information on dissemination of products

- Enhanced coverage for response during 2010 Olympic Games and automated runs

During the Vancouver February 2010 Winter Olympic Games, automatic forecasts of hypothetical releases of hazardous materials were performed and updated many times per day. These were used by emergency management officials for planning purposes during the Games.

- Forest fires in Russia – Modelling for Health Canada

In order to help determine whether the atmospheric flow might transport hazardous substances into Canadian territory, modelling of hypothetical releases from the Chernobyl area caused by the forest fires in Russia was performed in August 2010.  The results were made available to Health Canada, the lead department responsible for coordinating Canada's Federal Nuclear Emergency Response Plan.

- Production of CTBTO meteorological bulletins

Work was undertaken in 2010 to transfer the production of bulletins containing meteorological data from CTBTO atmospheric monitoring stations from the Canadian Meteorological Centre (CMC) to Zentralanstalt für Meteorologie und Geodynamik (ZAMG) in Austria.  These bulletins are issued by CMC under header SNCN19 CWAO.  This work was still ongoing at the end of 2010.

iv. Dissemination of products

Transport model graphical products and joint statements are posted to secure joint web pages, and faxed to relevant RSMCs and NMHSs. For examples of the graphical products, see Annex 4 of WMO, 2008.

In addition to the other RSMCs, the following countries' NMHSs are in our email and / or fax lists:

Antigua and Barbuda, Argentina, Bahamas, Belize, Bolivia, Brazil, Chile, Colombia, Costa Rica, Cuba, Dominican Republic, Ecuador, Guatemala, Guyana, Mexico, Netherlands Antilles and Aruba, Panama, Peru, Suriname, Trinidad and Tobago, Uruguay and Venezuela.

v. Response to requests from CTBTO-PTS

There were a total of 21 requests from the Provisional Technical Secretariat of the Comprehensive Test Ban Treaty Organization. Operational requests were received May 5, May 18 (2 requests were received on this date), May 19-21 (inclusive), May 25-28 (inclusive), July 20 and August 4. The nine other requests were between November 4 and 12, and were part of the CBTO-WMO Exercise 2010. In all cases, the products were supplied to CTBTO within a few hours of receiving the request.

4.	Routine operations

Monthly Test:

RSMCs Montréal, Washington and Melbourne hold a joint test on the second Thursday of every month. Following interest demonstrated by other RSMCs, the request to start the exercise is now emailed to all RSMCs. In addition, RSMC Montreal participated in the quarterly test initiated by the IAEA. The following table shows the list of tests in 2010.

| Month | Source location | Initiated by | RSMC providing joint statement |
| --- | --- | --- | --- |
| January | Douglas Point, Canada | RSMC Montréal | Washington |
| February | Jakarta, Indonesia | IAEA | Melbourne |
| March | Maralinga, Australia | RSMC Melbourne | Melbourne |
| April | Gentilly, Canada | RSMC Montréal | Washington |
| May | Darlington, Canada | IAEA | Montréal |
| June | South Texas Project 1 NPP, USA | RSMC Washington | Montréal |
| July | Lucas Heights, Australia | RSMC Melbourne | Melbourne |
| August | Dukovany, Czech Republic | IAEA | RA I and VI RSMCs |
| September | Whiteshell, Canada | RSMC Montréal | Washington |
| October | Leonora, Australia | RSMC Melbourne | Melbourne |
| November | Hamaoka, Japan | IAEA | RA II RSMCs |
| December | Whiteshell, Canada | RSMC Montréal | Washington |

5.	Lessons learned and significant operational or technical changes:

- This was the first full year of use of the Lagrangian model called MLDP0 (see section 7 and http://www.wmo.int/pages/prog/www/DPS/WMOTDNO778/Annex4.html ). No problems were encountered with its implementation.  This model is continually being worked on and several adjustments and improvements to it were implemented in 2010.

6.	Operational issues and challenges:

- Faxing of products to NMHSs continues to exhibit a high failure rate

- Delivery of information by email / web displays a much higher success rate. However, this needs to be discussed and formally consolidated by all RSMCs, as per recommendations of CBS-XIV.

7. 	Other activities:

From 7 to 15 December, René Servranckx (member of RSMC Montreal and Chairperson of the WMO nuclear ERA Coordination Group) worked at WMO in Geneva. The work comprised of

- Some updating to the WMO Emergency Response Activities web pages

- Drafting a letter for WMO Member States regarding updating of contact information and the transition from facsimile to email for RSMC product distribution

- Review of work needed to update WMO Technical Note 170 (Meteorological and Hydrological Aspects of Siting and Operation of Nuclear Power Plants)

- Meeting with the World Health Organization (Geneva)

- Visits to the Meteorological Service of Austria (ZAMG), IAEA and CTBTO in Vienna

8. 	Summary and status of the operational atmospheric transport and dispersion models:

Current global weather conditions and forecasts are available at CMC at all times, to provide, in real time, the necessary input to the atmospheric transport and dispersion models, and for their evaluation and interpretation.

For forecasts, the Global Environmental Multiscale model (GEM) by CMC operations. Two configurations are available: regional and global. The latter, which has a uniform horizontal resolution (33 km) over the globe, is used to provide quality analyses, through the assimilation cycle, and medium term forecast guidance.  The former configuration was changed on 20 October 2010.  The grid spacing of the regional GEM remains at 15 km, but the grid its forecasts are produced on is now slightly larger than the previous one.

i. The Modèle Lagrangien de Dispersion de Particules d’ordre zéro (MLDP0)

This is a Lagrangian particle dispersion model of zeroth order designed for long-range dispersion problems occurring at regional and global scales and is described in details in D’Amours & Malo, 2004. Dispersion is estimated by calculating the trajectories of a very large number of air particles (or parcels). Large scale transport is handled by calculating the displacement due to the synoptic component of the wind field and diffusion through discretized stochastic differential equations to account for the unresolved turbulent motions. Vertical mixing caused by turbulence is handled through a random displacement equation based on a diffusion coefficient. This coefficient is calculated in terms of a mixing length, stability function, and vertical wind shear. Lateral mixing (horizontal diffusion) is modeled according to a first order Langevin Stochastic Equation for the unresolved components of the horizontal wind (mesoscale fluctuations).

MLDP0 is an off-line model and uses the full 3-D meteorological fields provided by a Numerical Weather Prediction (NWP) system. Therefore fields of wind, moisture, temperature and geopotential heights must be provided to the model, which are obtained either from the GEM model forecasts and objective analysis systems in Global, Regional or high resolution configuration.

Dry deposition is modeled in term of a deposition velocity. The deposition rate is calculated by assuming that a particle contributes to the total surface deposition flux in proportion to the tracer material it carries when it is found in a layer adjacent to the ground surface. Wet deposition will occur when a particle is presumed to be in a cloud. The tracer removal rate is proportional to the local cloud fraction.

The source term is controlled through a sophisticated emission scenario module which takes into account the different release rates of several radionuclides over time. For volcanic eruptions, a particle size distribution can be used to model the gravitational settling effects in the trajectory calculations according to Stoke’s law. The total released mass can be estimated from an empirical formula derived by Sparks et al., 1997, which is a function of particle density, plume height and effective emission duration (Malo, 2007). MLDP0 can be run for a large number of isotopes (Cs-137 by default) as well as for volcanic ash or an inert gas tracer.

In MLDP0, tracer concentrations at a given time and location are obtained by assuming that particles carry a certain amount of tracer material. The concentrations are then obtained by calculating the average residence time of the particles, during a given time period, within a given sampling volume, and weighting it according to the material amount carried by the particle. Concentrations are expected to be estimated more accurately near the source with a Lagrangian model than with an Eulerian model.

MLDP0 operates on a polar stereographic grid and can run on both hemispheres. The grid size and resolution define the geographical domain. Five horizontal grid resolutions are available: 50 km (687×687), 33 km (229×229), 15 km (503×503), 10 km (229×229) and 5 km (457×457). A global configuration also exists at horizontal resolution of 1° (360×181). MLDP0 can be executed in inverse (adjoint) mode. The model has been used extensively in this configuration in the context of the WMO-CTBTO cooperation. The vertical discretization is made for 25 levels in the SIGMA, ETA or HYBRID terrain following coordinates depending on the version of the GEM NWP model used.

ii. Trajectory model

This model uses winds directly as given by the analyses and/or GEM model.  The wind fields are available every hour in forecast mode and every 3 hours in diagnostic mode.  Initial positions of one or more air parcels in a column are specified, and the parcels are then incrementally displaced, using time and spatial discriminations of the local three-dimensional wind field. It is assumed that air parcels preserve their identity as they are transported in the wind.

The model has been validated using back-trajectories from stations that measured concentrations of tracers from a single source (D'Amours 1998). The back-trajectories converge remarkably well towards the tracer source location. On the other hand, the lack of a boundary layer treatment and the assumption air parcel identity preservation are reflected in the results, which indicate vertical motions that are not in line with the observations.

8.	Plans for 2011:

- Explore new products, such as the ‘’time of arrival’’ of a plume.

- The schedule of routine monthly tests for all of 2011 and 2012 has been set up in collaboration with RSMCs Washington and Melbourne. Each RSMC will select the simulated accident location and write the joint statement on a rotating basis. Quarterly tests are also scheduled with the IAEA

- Incorporate the script to produce backtracking calculations for CTBTO into the (GUI) toolkit used for environmental emergency response and RSMC modelling.

References

D'Amours, R.., 1998: Modelling the ETEX plume dispersion with the Canadian Emergency Response Model, Atmospheric Environment, 32, 4335-4331

D’Amours, R., and Malo, A., 2004, “A Zeroth Order Lagrangian Particle Dispersion Model: MLDP0”, Internal report, Canadian Meteorological Centre, Environmental Emergency Response Section, Dorval, Québec, Canada, 18 pp.

Malo, A., 16 November 2007, “Total Released Mass Calculation for Volcanic Eruption in CMC’s Long-Range Transport and Dispersion Model MLDP0”, Internal Publication, Canadian Meteorological Centre, Environmental Emergency Response Section, Dorval, Québec, Canada, 2 pp.

WMO, 2008: Documentation on RSMC Support for Environmental Emergency Response. WMO-TD/No.778. Available online at

http://www.wmo.int/pages/prog/www/DPFSERA/td778.html