RSMC Montréal Report of Activities for 2013

Executive Summary

Primary activities for 2013 consisted of the Regional Specialized Meteorological Centre (RSMC) monthly tests - conducted for scenarios over Canada, the United States, Brazil, Germany, Malaysia and Pakistan - and incremental updates and improvements to the response procedures, software, and to the joint RSMC secure web pages, which are used for communicating transport model products to National Meteorological and Hydrological Services (NMHS) and between RSMCs.  RSMC Montréal received requests  - operational as well as planned - for inverse modelling support from the Provisional Technical Secretariat (PTS) of the Comprehensive Test Ban Treaty Organization (CTBTO)  during all months of 2013.

1.	Introduction

The Canadian Meteorological Centre (Meteorological Service of Canada, Environment Canada) is designated by the World Meteorological Organisation (WMO) as the RSMC Montréal for the provision of atmospheric transport modelling (ATM) in case of an environmental emergency response. The primary regions of responsibility are WMO Regional Associations (RA) III & IV, which encompass Canada, United-States, Mexico, Central and South America. In addition to emergency response, RSMC Montréal contributes global inverse modelling support to the CTBTO verification system.

2.	Operational Contact Information

Canadian Meteorological Centre (CMC)

Environment Canada

2121 Trans-Canada Highway

DORVAL, Québec

Canada H9P 1J3

Business contact: Mr. Nils Ek

Tel	: 1 514 421 7207

Fax	: 1 514 421 4679

Email	: Nils.Ek@ec.gc.ca

Operational contact (24 hours): Shift supervisor

Tel	: 1 514 421 4635

Fax	: 1 514 412 4639

3. 	Responses and information on dissemination of products

- Production of CTBTO meteorological bulletins

Work continued in 2013 to transfer the production of bulletins containing meteorological data from CTBTO atmospheric monitoring stations from the Canadian Meteorological Centre (CMC) to Zentralanstalt für Meteorologie und Geodynamik (ZAMG) in Austria.  These bulletins are issued by CMC under header SNCN19 CWAO.  In July 2013, observations from the stations which were given WMO synoptic codes started to be transmitted under header ISAX30 LOWM.  The work to include all stations in this bulletin was still ongoing at the end of 2013.

As part of the work to make these stations officially recognized internationally, the WMO requested that each member-state that has CTBTO stations on its territory assign synoptic codes to identify the stations.  This request was received by Canada, but because of a shortage of available synoptic codes, none had been assigned at the end of 2013.  Work is ongoing to free up synoptic codes, and it is hoped that in 2014, the 4 CTBTO stations operating in Canada will be assigned identifiers.

iv. Dissemination of products

Transport model graphical products and joint statements are posted to secure joint web pages, and faxed to relevant RSMCs and National Meteorological and Hydrological Services (NMHS), when requested by the International Atomic Energy Agency (IAEA). For examples of the graphical products, see Annex 4 of WMO, 2011.  In 2013, efforts were continued to ensure that all the RSMC mirror web pages were indeed identical and RSMC Exeter joined this group.  Work continues to ensure this is the case.

RSMC Montréal now has the operational capability to transmit blank charts to all RSMC mirror websites at the start of each response, before transmitting the actual product charts once the response is underway.

In addition to the other RSMCs, the following countries' NMHSs are in our email and / or fax lists:

Antigua and Barbuda, Argentina, Bahamas, Belize, Bolivia, Brazil, Chile, Colombia, Costa Rica, Cuba, Dominican Republic, Ecuador, Guatemala, Guyana, Mexico, Netherlands Antilles and Aruba, Panama, Peru, Suriname, Trinidad and Tobago, Uruguay and Venezuela.  Continual efforts are made to keep the contact list up-to-date.

v. Response to requests from CTBTO-PTS

There were a total of 20 requests from the PTS of the CTBTO in 2013. Many of these were related to detections in Japan, likely the result of continued emanations originating from the site of the 2011 Fukushima Daiichi Nuclear Power Plant accident.

vi. Other responses

RSMC Montréal participated in a special exercise on 12 November 2013 with the NMHS in Buenos Aires.

4.	Routine operations

Monthly Test:

RSMCs Montréal, Washington and Melbourne hold a joint test on the second Thursday of every month. Following interest demonstrated by other RSMCs, the request to start the exercise is now emailed to all RSMCs. In addition, RSMC Montréal participated in the quarterly test initiated by the IAEA. Note that the regular monthly test scheduled in July was cancelled due to the re-scheduling of February's Quarterly 1 Test with the IAEA for 18 July 2013. The following table lists tests in 2013.

| Month | Source location | Initiated by | RSMC providing joint statement |
| --- | --- | --- | --- |
| January | Lucas Heights, Australia | Melbourne | Melbourne |
| February | Kanupp, Pakistan | IAEA | RA II RSMCs |
| March | Atucha NPP, Argentina | Washington | Montréal |
| April | Manyberries, AB, Canada | Montréal | Washington |
| May | Angra NPP, Brazil | IAEA | RA III and IV RSMC |
| June | Lucas Heights, Australia | Melbourne | Melbourne |
| July | Test cancelled | - | - |
| August | Puspati Research Reactor, Malaysia | IAEA | RA V RSMCs |
| September | Anchorage, AK, USA | Washington | Montréal |
| October | Whiteshell Laboratories, MB, Canada | Montréal | Washington |
| November | Murau NPP, Germany | IAEA | RA I and VI RSMCs |
| December | Lucas Heights, Australia | Melbourne | Melbourne |

5.	Lessons learned and significant operational or technical changes:

Two upgrades to the software used to run the operational Lagrangian model called MLDP0 (see section 4 of http://www.wmo.int/pages/prog/www/DPS/WMOTDNO778/Annex4.html ) were implemented during the course of 2013.  This model is continually being worked on and more adjustments and improvements are expected again in the coming year.

6.	Operational issues and challenges:

Faxing of products to NMHSs has been discontinued for monthly tests, as email has become the preferred method of communications and faxes exhibit a high failure rate.  Faxes continue to be sent to RA III and IV NMHS upon request from the IAEA.

7.	Other activities:

Members of RSMC Montréal Alain Malo and René Servranckx (also Chairperson of the WMO Nuclear ERA Coordination Group) were part of the WMO Technical Task Team on Meteorological Analyses for Fukushima-Daiichi Nuclear Power Plant Accident.

8. 	Summary and status of the operational atmospheric transport and dispersion models:

Current global weather conditions and forecasts are available at CMC at all times, to provide, in real time, the necessary input to the ATM, and for their evaluation and interpretation.

For forecasts, CMC operational uses the Canadian Global Environmental Multiscale (GEM) numerical weather prediction (NWP) model. Two configurations of GEM are available: regional and global. The latter, which has a uniform horizontal resolution (25 km) over the globe, is used to provide quality analyses, through the assimilation cycle, and medium term forecast guidance.  The grid spacing of the regional configuration is approximately 10 km over North America.

i. The Modèle Lagrangien de Dispersion de Particules d’ordre zéro (MLDP0)

This is a Lagrangian particle dispersion model designed for long-range dispersion problems occurring at regional and global scales and is described in detail in D’Amours and Malo, 2004. Dispersion is simulated by calculating the trajectories of a large number of air particles (or parcels). Large scale transport is calculated as the displacement due to the NWP-resolved wind field, while discretized stochastic differential equations account for the unresolved turbulent motions. Turbulent vertical mixing is modelled with a random displacement equation based on a diffusion coefficient. Lateral (horizontal) turbulent diffusion is modelled according to a first order Langevin stochastic equation for the components of the horizontal wind that are not resolved by NWP.

MLDP0 is an off-line model and requires 3-D meteorological fields (wind, moisture, temperature and geopotential heights) from a NWP system. At RSMC Montréal these are obtained from the GEM model forecasts and analysis systems in either Global or Regional configuration.

Dry deposition is modeled using a deposition velocity. The deposition rate is calculated as a proportion of the tracer material carried by particles in a layer adjacent to the ground surface. Wet deposition will occur when a particle is presumed to be in a cloud. The tracer removal rate is proportional to the local cloud fraction.

The source term is controlled through an emission scenario module which allows different release rates of radionuclides over time. MLDP0 can be run for a large number of isotopes (Cs-137 by default) as well as for volcanic ash (D’Amours et al, 2010) or an inert gas tracer.

For volcanic eruptions, a particle size distribution can be used to model the gravitational settling effects in the trajectory calculations according to Stoke’s law. The total released mass can be estimated from an empirical formula derived by Sparks et al., 1997, which is a function of particle density, plume height and effective emission duration (Malo, 2007).

In MLDP0, tracer concentrations at a given time and location are calculated by averaging the residence time of the particles, during a given time period, within a given sampling volume, and weighting it according to the amount of material carried by the particles. Concentrations are expected to be estimated more accurately near the source with a Lagrangian model than with an Eulerian model.

MLDP0 operates on a polar stereographic grid and can run in both northern and southern hemispheres. The grid size and resolution define the geographical domain. More than 30 horizontal grids are now available, some of which are listed below:

- 50 km (687× 687), (477×477), (400×400) and (334×334)

- 33 km (722×722), (606×606), (505×505), (400×400) and (229×229)

- 15 km (503×503) and (251×251)

- 10 km (229×229)

- 5 km (457×457)

- 2 km (300×300)

A global configuration also exists at horizontal resolution of 1° (360×181). MLDP0 can be executed in backward (adjoint) mode. The model has been used extensively in this configuration in the context of the WMO-CTBTO cooperation. The vertical discretization is made for 25 levels in the SIGMA, ETA or HYBRID terrain following coordinates depending on the version of the GEM NWP model used.

ii. Trajectory model

This model uses winds directly from the GEM analyses and/or forecast model.  The wind fields are available every hour in forecast mode and every 3 hours in diagnostic mode.  Initial positions of one or more air parcels in a column are specified, and the parcels are then incrementally displaced, using time and spatial discriminations of the local three-dimensional wind field. It is assumed that air parcels preserve their identity as they are transported in the wind.

The model has been validated using back-trajectories from stations that measured concentrations of tracers from a single source (D'Amours 1998). The back-trajectories converge remarkably well towards the tracer source location. On the other hand, the lack of a boundary layer treatment and the assumption air parcel identity preservation are reflected in the results, which indicate vertical motions that are not in line with the observations.

9.	Plans for 2014:

- The schedule of routine monthly tests for all of 2014 has been set up in collaboration with RSMCs Washington and Melbourne. Each RSMC will select the simulated accident location and write the joint statement, on a rotating basis. Quarterly tests are also scheduled with the IAEA.

- Implement the capability to vary the source term release with time for simulations using the Lagrangian transport and dispersion model.

- Incorporate the script to produce backtracking calculations for CTBTO into the software used for environmental emergency response and RSMC modelling.

References

D'Amours, R.., 1998: Modelling the ETEX plume dispersion with the Canadian Emergency Response Model, Atmospheric Environment, 32, 4335-4331

D’Amours, R., and Malo, A., 2004, “A Zeroth Order Lagrangian Particle Dispersion Model: MLDP0”, Internal report, Canadian Meteorological Centre, Environmental Emergency Response Section, Dorval, Québec, Canada, 18 pp.

D’Amours, R., A. Malo, R. Servranckx, D. Bensimon, S. Trudel, and J.P. Gauthier-Bilodeau (2010), Application of the atmospheric Lagrangian particle dispersion model MLDP0 to the 2008 eruptions of Okmok and Kasatochi volcanoes, J. Geophys. Res., 115, D00L11, doi:10.1029/2009JD013602.

Malo, A., 16 November 2007, “Total Released Mass Calculation for Volcanic Eruption in CMC’s Long-Range Transport and Dispersion Model MLDP0”, Internal Publication, Canadian Meteorological Centre, Environmental Emergency Response Section, Dorval, Québec, Canada, 2 pp.

WMO, 2011: Documentation on RSMC Support for Environmental Emergency Response. WMO-TD/No.778. Available online at

http://www.wmo.int/pages/prog/www/DPFSERA/td778.html