| WORLD METEOROLOGICAL ORGANIZATION ________________ COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES PRAGUE, CZECH REPUBLIC, 22-26 APRIL 2002 |  | ET/DR&C2/Doc. 2.3(1) _______ (12.III.2002) ENGLISH only |
| --- | --- | --- |

Some additional GRIB2 Product Definition Templates

(Submitted by J. Ator (USA))

________________________________________________________________

Summary and Purpose of Document

This paper proposes four new Product Definition Templates for use in representing ensemble forecast products over non-discrete time constructs within GRIB2.

________________________________________________________________

ACTION PROPOSED

The meeting is requested to consider the proposal and recommend it to the upcoming CBS session in 2002 .

DISCUSSION

1.	Background

The U.S. National Centers for Environmental Prediction would like to request that the following four new Product Definition Templates (PDTs) be added to the regulations for GRIB2.  These new templates are similar to existing PDTs 4.1 - 4.4, except that they can be used to indicate a continuous or non-continuous time interval, whereas PDTs 4.1 - 4.4 can only be  used to indicate ensemble forecasts valid at a given single point in time.  In that sense, these new templates would thus have the same relationship to PDTs 4.1 - 4.4 as existing PDTs 4.9 and 4.10 have to existing PDTs 4.5 and 4.6, and, in fact, care was taken in the creation of these new templates in order to keep them as consistent as possible with existing PDTs 4.9 and 4.10.

2.	Proposal

Product Definition Template 4.11:	Individual ensemble forecast, control and perturbed, at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

Octet No.		Contents

10		Parameter category (see Code Table 4.1)

11		Parameter number (see Code Table 4.2)

12		Type of generating process (see Code Table 4.3)

13		Background generating process identifier (defined by originating Centre)

14		Forecast generating process identifier (defined by originating Centre)

15-16		Hours after reference time of data cut-off (see Note 1)

17		Minutes after reference time of data cut-off

18		Indicator of unit of time range (see Code Table 4.4)

19-22		Forecast time in units defined by octet 18 (see Note 2)

23		Type of first fixed surface (see Code Table 4.5)

24		Scale factor of first fixed surface

25-28		Scaled value of first fixed surface

29		Type of second fixed surface (see Code Table 4.5)

30		Scale factor of second fixed surface

31-34		Scaled value of second fixed surface

35		Type of ensemble forecast (see Code Table 4.6)

36		Perturbation number

37		Number of forecasts in ensemble

38-39		Year of end of overall time interval

40		Month of end of overall time interval

41		Day of end of overall time interval

42		Hour of end of overall time interval

43		Minute of end of overall time interval

44		Second of end of overall time interval

45		n - Number of time range specifications describing the time intervals used to calculate the statistically processed field

46-49		Total number of data values missing in statistical process

50-61		Specification of the outermost (or only) time range over which statistical processing is done

50		Statistical process used to calculate the processed field from the field at each time increment during the time range (see Code Table 4.10)

51		Type of time increment between successive fields used in the statistical processing (see Code Table 4.11)

52		Indicator of unit of time for time range over which statistical processing is done (see Code Table 4.4)

53-56		Length of the time range over which statistical processing is done, in units defined by the previous octet

57		Indicator of unit of time for the increment between the successive fields used (see Code Table 4.4)

58-61		Time increment between successive fields, in units defined by the previous octet (see Note 3)

62-nn		These octets are included only if n>1, where nn = 49 + 12*n

62-73		As octets 50 to 61, next innermost step of processing

74-nn		Additional time range specifications, included in accordance with the value of n. Contents as octets 50 to 61, repeated as necessary.

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

(3)	An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples.  Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a rain gauge.  The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 51, 63, 75 ...).  For all but the innermost (last) time range, the next inner range is then processed using these reference and forecast times as the initial reference and forecast time.

Product Definition Template 4.12:	Derived forecasts based on all ensemble members at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

Octet No.		Contents

10		Parameter category (see Code Table 4.1)

11		Parameter number (see Code Table 4.2)

12		Type of generating process (see Code Table 4.3)

13		Background generating process identifier (defined by originating Centre)

14		Forecast generating process identifier (defined by originating Centre)

15-16		Hours after reference time of data cut-off (see Note 1)

17		Minutes after reference time of data cut-off

18		Indicator of unit of time range (see Code Table 4.4)

19-22		Forecast time in units defined by octet 18 (see Note 2)

23		Type of first fixed surface (see Code Table 4.5)

24		Scale factor of first fixed surface

25-28		Scaled value of first fixed surface

29		Type of second fixed surface (see Code Table 4.5)

30		Scale factor of second fixed surface

31-34		Scaled value of second fixed surface

35		Derived forecast (see Code Table 4.7)

36		Number of forecasts in ensemble

37-38		Year of end of overall time interval

39		Month of end of overall time interval

40		Day of end of overall time interval

41		Hour of end of overall time interval

42		Minute of end of overall time interval

43		Second of end of overall time interval

44		n - Number of time range specifications describing the time intervals used to calculate the statistically processed field

45-48		Total number of data values missing in statistical process.

49-60		Specification of the outermost (or only) time range over which statistical processing is done

49		Statistical process used to calculate the processed field from the field at each time increment during the timerange (see Code Table 4.10)

50		Type of time increment between successive fields used in the statistical processing (see Code Table 4.11)

51		Indicator of unit of time for time range over which statisticalprocessing is done (see Code Table 4.4)

52-55		Length of the time range over which statistical processing is done, in units defined by the previous octet

56		Indicator of unit of time for the increment between the successive fields used (see Code Table 4.4)

57-60		Time increment between successive fields, in units defined by the previous octet (see Note 3)

61-nn		These octets are included only if n>1, where nn = 48 + 12*n

61-72		As octets 49 to 60, next innermost step of processing

73-nn		Additional time range specifications, included in accordance with the value of n. Contents as octets 49 to 60, repeated as necessary.

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

(3)	An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples. Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a rain gauge. The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 50, 62, 74 ...). For all but the innermost (last) time range, the next inner range is then processed using these reference and forecast times as the initial reference and forecast time.

Product Definition Template 4.13	Derived forecasts based on a cluster of ensemble members over a rectangular area at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

Octet No.		Contents

10		Parameter category (see Code Table 4.1)

11		Parameter number (see Code Table 4.2)

12		Type of generating process (see Code Table 4.3)

13		Background generating process identifier (defined by originating Centre)

14		Forecast generating process identifier (defined by originating Centre)

15-16		Hours after reference time of data cut-off (see Note 1)

17		Minutes after reference time of data cut-off

18		Indicator of unit of time range (see Code Table 4.4)

19-22		Forecast time in units defined by octet 18 (see Note 2)

23		Type of first fixed surface (see Code Table 4.5)

24		Scale factor of first fixed surface

25-28		Scaled value of first fixed surface

29		Type of second fixed surface (see Code Table 4.5)

30		Scale factor of second fixed surface

31-34		Scaled value of second fixed surface

35		Derived forecast (see Code Table 4.7)

36		Number of forecasts in the ensemble (N)

37		Cluster identifier

38		Number of cluster to which the high resolution control belongs

39		Number of cluster to which the low resolution control belongs

40		Total number of clusters

41		Clustering method (see Code Table 4.8)

42-45		Northern latitude of cluster domain

46-49		Southern latitude of cluster domain

50-53		Eastern longitude of cluster domain

54-57		Western longitude of cluster domain

58-59		Year of end of overall time interval

60		Month of end of overall time interval

61		Day of end of overall time interval

62		Hour of end of overall time interval

63		Minute of end of overall time interval

64		Second of end of overall time interval

65		n - Number of time range specifications describing the time intervals used to calculate the statistically processed field

66-69		Total number of data values missing in statistical process.

70-81		Specification of the outermost (or only) time range over which statistical processing is done

70		Statistical process used to calculate the processed field from the field at each time increment during the time range (see Code Table 4.10)

71		Type of time increment between successive fields used in the statistical processing (see Code Table 4.11)

72		Indicator of unit of time for time range over which statistical processing is done (see Code Table 4.4)

73-76		Length of the time range over which statistical processing is done, in units defined by the previous octet

77		Indicator of unit of time for the increment between the successive fields used (see Code Table 4.4)

78-81		Time increment between successive fields, in units defined by the previous octet (see Note 3)

82-nn		These octets are included only if n>1, where nn = 69 + 12*n

82-93		As octets 70 to 81, next innermost step of processing

94-nn		Additional time range specifications, included in accordance with the value of n.  Contents as octets 70 to 81, repeated as necessary.

(nn+1)-(nn+N) 	List of N ensemble forecast numbers ( N is given in octet 36 )

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

(3)	An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples.  Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a rain gauge.  The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 71, 83, 95 ...). For all but the innermost (last) time range, the next inner range is then processed using these reference and forecast times as the initial reference and forecast time.

Product Definition Template 4.14:	Derived forecasts based on a cluster of ensemble members over a circular area at a horizontal level or in a horizontal layer in a continuous or non-continuous time interval

Octet No.		Contents

10		Parameter category (see Code Table 4.1)

11		Parameter number (see Code Table 4.2)

12		Type of generating process (see Code Table 4.3)

13		Background generating process identifier (defined by originating Centre)

14		Forecast generating process identifier (defined by originating Centre)

15-16		Hours after reference time of data cut-off (see Note 1)

17		Minutes after reference time of data cut-off

18		Indicator of unit of time range (see Code Table 4.4)

19-22		Forecast time in units defined by octet 18 (see Note 2)

23		Type of first fixed surface (see Code Table 4.5)

24		Scale factor of first fixed surface

25-28		Scaled value of first fixed surface

29		Type of second fixed surface (see Code Table 4.5)

30		Scale factor of second fixed surface

31-34		Scaled value of second fixed surface

35		Derived forecast (see Code Table 4.7)

36		Number of forecasts in the ensemble (N)

37		Cluster identifier

38		Number of cluster to which the high resolution control belongs

39		Number of cluster to which the low resolution control belongs

40		Total number of clusters

41		Clustering method (see Code Table 4.8)

42-45		Latitude of central point in cluster domain

46-49		Longitude of central point in cluster domain

50-53		Radius of cluster domain

54-55		Year of end of overall time interval

56		Month of end of overall time interval

57		Day of end of overall time interval

58		Hour of end of overall time interval

59		Minute of end of overall time interval

60		Second of end of overall time interval

61		n - Number of time range specifications describing the time intervals used to calculate the statistically processed field

62-65		Total number of data values missing in statistical process.

66-77		Specification of the outermost (or only) time range over which statistical processing is done

66		Statistical process used to calculate the processed field from the field at each time increment during the time range (see Code Table 4.10)

67		Type of time increment between successive fields used in the statistical processing (see Code Table 4.11)

68		Indicator of unit of time for time range over which statistical processing is done (see Code Table 4.4)

69-72		Length of the time range over which statistical processing is done, in units defined by the previous octet

73		Indicator of unit of time for the increment between the successive fields used (see Code Table 4.4)

74-77		Time increment between successive fields, in units defined by the previous octet (see Note 3)

78-nn		These octets are included only if n>1, where nn = 65 + 12*n

78-89		As octets 66 to 77, next innermost step of processing

90-nn		Additional time range specifications, included in accordance with the value of n. Contents as octets 66 to 77, repeated as necessary.

(nn+1)-(nn+N) 	List of N ensemble forecast numbers ( N is given in octet 36 )

Notes:

(1)	Hours greater than 65534 will be coded as 65534.

(2)	The reference time in section 1 and the forecast time together define the beginning of the overall time interval.

(3)	An increment of zero means that the statistical processing is the result of a continuous (or near continuous) process, not the processing of a number of discrete samples.  Examples of such continuous processes are the temperatures measured by analogue maximum and minimum thermometers or thermographs, and the rainfall measured by a rain gauge.  The reference and forecast times are successively set to their initial values plus or minus the increment, as defined by the type of time increment (one of octets 67, 79, 91 ...).  For all but the innermost (last) time range, the next inner range is then processed using these reference and forecast times as the initial reference and forecast time.