| WORLD METEOROLOGICAL ORGANIZATION ________________ COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES PRAGUE, CZECH REPUBLIC, 22-26 APRIL 2002 |  | ET/DR&C2/Doc. 3.2(2) _______ (9.IV.2002) ENGLISH only |
| --- | --- | --- |

A Proposal for BUFR Templates and Descriptors for

CLIMAT, CLIMAT SHIP, CLIMAT TEMP and CLIMAT TEMP SHIP

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

This document contains a proposal for BUFR templates and descriptors for the traditional CLIMAT, CLIMAT SHIP, CLIMAT TEMP and CLIMAT TEMP SHIP data.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to examine the proposed templates and descriptors, and recommend them for validation tests or consider the possibility to recommend them for approval by CBS.

References:

[1]  Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

[2]  Report of ET on DR&C, Toulouse, 23-27 April 2001.

[3] Report of ET on Migration to TDCF, Geneva, 7-11 May 2001.

[4] Guide to Climatological Practices, WMO - No 100.

Discussion

1. Background

The first session of the Expert Team on Data Representation and Codes (ET/DR&C),  Toulouse, 23-27 April 2001, reviewed a proposal for BUFR/CREX templates for the traditional SYNOP, SHIP, BATHY/TESAC, BUOY, AMDAR, AIREP, TEMP+PILOT and METAR+SPECI data types [2].

At the first session of ET on Migration to Table Driven Code Forms, Geneva, 7-11 May 2001, a preliminary migration plan was elaborated. Traditional code forms were grouped into six categories which were thought to share common characteristic which would allow migration to proceed in parallel. For each of these categories three target dates were set, the start of experimental exchange, the start of operational exchange and the end of operational exchange. CLIMAT, CLIMAT SHIP, CLIMAT TEMP and CLIMAT TEMP SHIP code forms were also put into the first category (the common code forms) with the start of experimental exchange in November 2002 [3]. The BUFR templates for these CLIMAT code forms were not, however, included in [2]. This contribution tries to fill this gap.

2. Proposals for new descriptors

2.1 New descriptors related to temperature data

According to the Guide to Climatological Practices, the monthly mean air temperature is reported as a true mean or corrected value to correspond to a mean based on 24 direct observations a day. The mean of four equally spaced observations may suffice as a close approximation to the true mean [4]. Some countries have notified using eight equally spaced observations a day for this purpose. A new descriptor is, however, needed for standard deviation of daily mean values of temperature (relative to the monthly mean air temperature) which is required in the CLIMAT report. The existing descriptor 0 12 051 (standard deviation temperature) is not suitable to express it.

"Mean daily maximum temperature" and "Mean daily minimum temperature" reported in CLIMAT, cannot be represented as a mean value of 0 12 116 (Maximum temperature at 2 m, past 24 hours) and 0 12 117 (Minimum temperature at 2 m, past 24 hours), respectively, if specification of the height of thermometer above local ground is to be included in the BUFR template for CLIMAT data. In any case, principal time of daily reading of maximum and minimum extreme temperatures is required to be reported.

Referring to the above given discussion, the following new descriptors are proposed:

| 0 12 151 | Standard deviation of daily mean temperature | K | 2 | 0 | 12 |
| --- | --- | --- | --- | --- | --- |
| 0 12 118 | Maximum temperature at height specified, past 24 hours | K | 2 | 0 | 16 |
| 0 12 119 | Minimum temperature at height specified, past 24 hours | K | 2 | 0 | 16 |
| 0 04 051 | Principal time of daily reading of maximum temperature | Hour | 0 | 0 | 5 |
| 0 04 052 | Principal time of daily reading of minimum temperature | Hour | 0 | 0 | 5 |

  - Other new descriptors

The existing entry 3 (Extreme temperature) of the code table 0 08 051 (Qualifier for number of missing values in calculation of statistic) is not capable to represent the required number of days missing from the record of daily maximum temperature and separately number of days missing from the record of daily minimum temperature. Moreover another code figure is needed to express "Wind", required in CLIMAT TEMP and CLIMAT TEMP SHIP data.

A code table 1400 is used in the CLIMAT TEMP and CLIMAT TEMP SHIP code forms to express time of observation used to compute the reported mean values of geopotencial, temperature and humidity. A flag table is proposed for this purpose below.

The following new descriptors are proposed :

| 0 08 050 | Principal time of daily reading of maximum temperature | Code table | 0 | 0 | 4 |
| --- | --- | --- | --- | --- | --- |
| 0 04 059 | Times of observation used to compute the reported mean values | Flag table | 0 | 0 | 6 |

|  | 0 08 050 |
| --- | --- |
|  | Qualifier for number of missing values in calculation of statistic |
| Code figure |  |
| 0 | Reserved |
| 1 | Pressure |
| 2 | Temperature |
| 3 | Extreme temperature |
| 4 | Vapour pressure |
| 5 | Precipitation |
| 6 | Sunshine duration |
| 7 | Maximum temperature |
| 8 | Minimum temperature |
| 9 | Wind |
| 10-14 | Reserved |
| 15 | Missing value |

|  | 0 04 059 |
| --- | --- |
|  | Times of observation used to compute the reported mean values |
| Bit No. |  |
| 1 | 00 UTC |
| 2 | 06 UTC |
| 3 | 12 UTC |
| 4 | 18 UTC |
| 5 | Other hours |
| All 6 | Missing value |

3.  A BUFR template for CLIMAT data

| 3 01 004 |  | Surface station identification |  |
| --- | --- | --- | --- |
|  | 0 01 001 | WMO block number | Numeric |
|  | 0 01 002 | WMO station number | Numeric |
|  | 0 01 015 | Station or site name | CCITT IA5 |
|  | 0 02 001 | Type of station | Code table |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day (= 1) (1) | Day |
| 3 01 012 | 0 04 004 | Hour (= 0) (1) | Hour |
|  | 0 04 005 | Minute (=0) (1) | Minute |
| 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, scale 5 |
|  | 0 06 001 | Longitude (high accuracy) | Degree, scale 5 |
| 0 07 030 |  | Height of station ground above mean sea level | m, scale 1 |
| 0 07 031 |  | Height of barometer above mean sea level | m, scale 1 |
| 0 04 023 |  | Time period (= number of days in the month) | Day |
|  |  | Monthly mean values of pressure, temperature, extreme temperatures and vapour pressure |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 10 004 |  | Pressure | Pa, scale –1 |
| 0 10 051 |  | Pressure reduced to mean sea level | Pa, scale –1 |
| 0 07 004 |  | Pressure (standard level) | Pa, scale –1 |
| 0 10 009 |  | Geopotential height of the standard level | gpm |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, scale 2 |
| 0 02 051 |  | Indicator to specify observing method for extreme temperatures | Code table |
| 0 04 051 |  | Principal time of daily reading of maximum temperature | Hour |
| 0 12 118 |  | Maximum temperature at height specified, past 24 hours | K, scale 2 |
| 0 04 052 |  | Principal time of daily reading of minimum temperature | Hour |
| 0 12 119 |  | Minimum temperature at height specified, past 24 hours | K, scale 2 |
| 0 13 004 |  | Vapour pressure | Pa, scale -1 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 0 12 151 |  | Standard deviation of daily mean temperature | K, scale 2 |
| 0 07 030 |  | Height of station ground above mean sea level (redefine height to previous value) | m, scale 1 |
| 1 02 005 |  | Replicate 2 descriptors 5 times |  |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 1, 2, 4, 7, 8) | Code table |
| 0 08 020 |  | Total number of missing entities (days) | Numeric |
|  |  | Sunshine duration |  |
| 0 14 032 |  | Total sunshine | Hour |
| 0 14 033 |  | Total sunshine | % |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 6; sunshine duration) | Code table |
| 0 08 020 |  | Total number of missing entities (days) | Numeric |
|  |  | Number of days of occurrence |  |
| 1 02 018 |  | Replicate 2 descriptors 18 times |  |
| 0 08 052 |  | Conditions for which number of days of occurrence follows (= 0,1, 2, 3, 4, 5, 6, 7, 8, 16, 17, 18, 19, 20, 21, 22, 23, 24) | Code table |
| 0 08 022 |  | Total number (of days) | Numeric |
|  |  | Occurrence of extreme values of temperature and wind speed |  |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 08 053 |  | Day of occurrence qualifier | Code table |
| 0 04 003 |  | Day | Day |
| 0 12 152 |  | Highest daily mean temperature | K, scale 2 |
| 0 08 053 |  | Day of occurrence qualifier | Code table |
| 0 04 003 |  | Day | Day |
| 0 12 153 |  | Lowest daily mean temperature | K, scale 2 |
| 0 08 053 |  | Day of occurrence qualifier | Code table |
| 0 04 003 |  | Day | Day |
| 0 08 023 |  | First order statistics (= 2; maximum value) | Code table |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, scale 2 |
| 0 08 053 |  | Day of occurrence qualifier | Code table |
| 0 04 003 |  | Day | Day |
| 0 08 023 |  | First order statistics (= 3; minimum value) | Code table |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, scale 2 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 02 002 |  | Type of instrumentation for wind measurement | Flag table |
| 0 08 053 |  | Day of occurrence qualifier | Code table |
| 0 04 003 |  | Day | Day |
| 0 11 046 |  | Maximum instantaneous wind speed | m, scale 1 |
| 0 07 030 |  | Height of station ground above mean sea level (redefine height to previous value) | m, scale 1 |
|  |  | Precipitation |  |
| 0 04 003 |  | Day (= 1) (2) | Day |
| 0 04 004 |  | Hour (= 6) (2) | Hour |
| 0 04 023 |  | Time period (= number of days in the month) (2) | Day |
| 0 13 060 |  | Total accumulated precipitation | kg m-2, scale 1 |
| 0 13 051 |  | Frequency group; precipitation | Code table |
| 0 04 053 |  | Number of days with precipitation equal to or more than 1 mm | Numeric |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 5; precipitation) | Code table |
| 0 08 020 |  | Total number of missing entities (days) | Numeric |
|  |  | Number of days of occurrence |  |
| 1 02 006 |  | Replicate 2 descriptors 6 times |  |
| 0 08 052 |  | Conditions for which number of days of occurrence follows (= 10,11, 12, 13, 14, 15 - precipitation) | Code table |
| 0 08 022 |  | Total number (of days) | Numeric |
|  |  | Occurrence of extreme precipitation |  |
| 0 08 053 |  | Day of occurrence qualifier | Code table |
| 0 04 003 |  | Day | Day |
| 0 13 052 |  | Highest amount of precipitation | kg m-2, scale 1 |
|  |  | NORMALS |  |
| 0 04 001 |  | Year (of beginning of the reference period) | Year |
| 0 04 001 |  | Year (of ending of the reference period) | Year |
| 0 04 002 |  | Month | Month |
| 0 04 003 |  | Day (= 1) (1) | Day |
| 0 04 004 |  | Hour (= 0) (1) | Hour |
| 0 04 022 |  | Time period (= 1) | Month |
|  |  | Nomals of monthly mean pressure, temperatures, vapour pressure and of standard deviation |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 10 004 |  | Pressure | Pa, scale –1 |
| 0 10 051 |  | Pressure reduced to mean sea level | Pa, scale –1 |
| 0 07 004 |  | Pressure (standard level) | Pa, scale –1 |
| 0 10 009 |  | Geopotential height of the standard level | gpm |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, scale 2 |
| 0 02 051 |  | Indicator to specify observing method for extreme temperatures | Code table |
| 0 04 051 |  | Principal time of daily reading of maximum temperature | Hour |
| 0 12 118 |  | Maximum temperature at height specified, past 24 hours | K, scale 2 |
| 0 04 052 |  | Principal time of daily reading of minimum temperature | Hour |
| 0 12 119 |  | Minimum temperature at height specified, past 24 hours | K, scale 2 |
| 0 13 004 |  | Vapour pressure | Pa, scale -1 |
| 0 12 151 |  | Standard deviation of daily mean temperature | K, scale 2 |
| 0 07 030 |  | Height of station ground above mean sea level (redefine height to previous value) | m, scale 1 |
|  |  | Normal of sunshine duration |  |
| 0 14 032 |  | Total sunshine | Hour |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 0 04 001 |  | Year (of beginning of the reference period) | Year |
| 0 04 001 |  | Year (of ending of the reference period) | Year |
| 0 04 002 |  | Month | Month |
| 0 04 003 |  | Day (= 1) (2) | Day |
| 0 04 004 |  | Hour (= 6) (2) | Hour |
| 0 04 022 |  | Time period (= 1) | Month |
|  |  | Normals of precipitation |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 13 060 |  | Total accumulated precipitation | kg m-2, scale 1 |
| 0 04 053 |  | Number of days with precipitation equal to or more than 1 mm | Numeric |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 1 02 006 |  | Replicate 2 descriptors 6 times |  |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 1, 2, 3, 4, 5, 6) | Code table |
| 0 08 020 |  | Total number of missing entities (years) | Numeric |

Notes:

- The time identification refers to the beginning  of the one-month period.

- In case of precipitation measurements, the one-month period begins at 06 UTC on the first day of the month and ends at 06 UTC on the first day of the following month.

4.  A BUFR template CLIMAT SHIP data

| 0 01 011 |  | Ship's call sign | CCITT IA5 |
| --- | --- | --- | --- |
| 0 02 001 |  | Type of station | Code table |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day (= 1) (1) | Day |
| 3 01 012 | 0 04 004 | Hour (= 0) (1) | Hour |
|  | 0 04 005 | Minute (= 0) (1) | Minute |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) | Degree, scale 2 |
|  | 0 06 002 | Longitude (coarse accuracy) | Degree, scale 2 |
| 0 07 030 |  | Height of station ground above mean sea level | m, scale 1 |
| 0 07 031 |  | Height of barometer above mean sea level | m, scale 1 |
| 0 04 023 |  | Time period (= number of days in the month) | Day |
|  |  | Monthly mean values of pressure, temperature, vapour pressure and sea/water temperature |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 10 051 |  | Pressure reduced to mean sea level | Pa, scale –1 |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, scale 2 |
| 0 13 004 |  | Vapour pressure | Pa, scale -1 |
| 0 07 030 |  | Height of station ground above mean sea level (redefine height to previous value) | m, scale 1 |
| 0 22 043 |  | Sea/water temperature | K, scale 2 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
|  |  | Precipitation |  |
| 0 04 003 |  | Day (= 1) (2) | Day |
| 0 04 004 |  | Hour (= 6) (2) | Hour |
| 0 04 023 |  | Time period (= number of days in the month) (2) | Day |
| 0 13 060 |  | Total accumulated precipitation | kg m-2, scale 1 |
| 0 13 051 |  | Frequency group; precipitation | Code table |
| 0 04 053 |  | Number of days with precipitation equal to or more than 1 mm | Numeric |
|  |  | NORMALS |  |
| 0 04 001 |  | Year (of beginning of the reference period) | Year |
| 0 04 001 |  | Year (of ending of the reference period) | Year |
| 0 04 002 |  | Month | Month |
| 0 04 003 |  | Day (= 1) (1) | Day |
| 0 04 004 |  | Hour (= 0) (1) | Hour |
| 0 04 022 |  | Time period (= 1) | Month |
|  |  | Normals of monthly mean pressure, temperature, vapour pressure and sea/water temperature |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 10 051 |  | Pressure reduced to mean sea level | Pa, scale –1 |
| 0 07 032 |  | Height of sensor above local ground | m, scale 2 |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, scale 2 |
| 0 13 004 |  | Vapour pressure | Pa, scale -1 |
| 0 07 030 |  | Height of station ground above mean sea level (redefine height to previous value) | m, scale 1 |
| 0 22 043 |  | Sea/water temperature | K, scale 2 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 0 04 001 |  | Year (of beginning of the reference period) | Year |
| 0 04 001 |  | Year (of ending of the reference period) | Year |
| 0 04 002 |  | Month | Month |
| 0 04 003 |  | Day (= 1) (2) | Day |
| 0 04 004 |  | Hour (= 6) (2) | Hour |
| 0 04 022 |  | Time period (= 1) | Month |
|  |  | Normals of precipitation |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 13 060 |  | Total accumulated precipitation | kg m-2, scale 1 |
| 0 04 053 |  | Number of days with precipitation equal to or more than 1 mm | Numeric |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |

Notes:

- The time identification refers to the beginning  of the one-month period.

- In case of precipitation measurements, the one-month period begins at 06 UTC on the first day of the month and ends at 06 UTC on the first day of the following month.

- A BUFR template for CLIMAT TEMP and CLIMAT TEMP SHIP data

| 3 01 001 | 0 01 001 | WMO block number | Numeric |
| --- | --- | --- | --- |
|  | 0 01 002 | WMO station number | Numeric |
| 0 01 011 |  | Ship's call sign | CCITT IA5 |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day (= 0) (1) | Day |
| 3 01 012 | 0 04 004 | Hour (= 0) (1) | Hour |
|  | 0 04 005 | Minute (= 0) (1) | Minute |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) | Degree, scale 2 |
|  | 0 06 002 | Longitude (coarse accuracy) | Degree, scale 2 |
| 0 07 030 |  | Height of station ground above mean sea level | m, scale 1 |
| 0 07 031 |  | Height of barometer above mean sea level | m, scale 1 |
| 0 07 007 |  | Height release of sonde above mean sea level | m |
| 0 04 023 |  | Time period (= number of days in the month) | Day |
| 0 04 059 |  | Times of observations used to compute the reported mean values | Flag table |
| 1 15 010 |  | Replicate 15 descriptors 10 times (surface and 9 standard levels) |  |
| 0 08 023 |  | First order statistics (= 4; mean value) | Code table |
| 0 07 004 |  | Pressure | Pa, scale –1 |
| 0 08 001 |  | Vertical sounding significance | Flag table |
| 0 10 009 |  | Geopotential height | gpm |
| 0 12 101 |  | Temperature/dry-bulb temperature | K, scale 2 |
| 0 12 103 |  | Dew-point temperature | K, scale 2 |
| 0 08 023 |  | First order statistics (= 32; vector mean) | Code table |
| 0 11 001 |  | Wind direction | Degree true |
| 0 11 002 |  | Wind speed | m s-1 |
| 0 08 023 |  | First order statistics (= 63; missing value) | Code table |
| 0 11 019 |  | Steadiness of wind | % |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 2; temperature) | Code table |
| 0 08 020 |  | Total number of missing entities (days) | Numeric |
| 0 08 050 |  | Qualifier for number of missing values in calculation of statistic (= 9; wind) | Code table |
| 0 08 020 |  | Total number of missing entities (days) | Numeric |

Note:

The time identification refers to the beginning  of the one-month period.

6.  Conclusions

The ET/DR&C is invited to examine the proposed BUFR templates and descriptors and to consider the possibility to recommend them for validation or for approval by the CBS.