| WORLD METEOROLOGICAL ORGANIZATION ________________ COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES PRAGUE, CZECH REPUBLIC, 22-26 APRIL 2002 |  | ET/DR&C2/Doc.3.5.10(1) _______ (13.III.2002) ENGLISH ONLY |
| --- | --- | --- |

A Proposal for new BUFR/CREX Table B descriptors for use with next-generation rawinsonde data

Submitted by J. Ator (USA)

Summary and Purpose of Document

This paper proposes many new BUFR/CREX descriptors which would enable the reporting of next-generation rawinsonde data such as is planned to be introduced within the USA within the coming year.

ACTION PROPOSED

The meeting is requested to consider the proposal and recommend it for fast-track implementation.

DISCUSSION

1.0	Background

The U.S. National Weather Service is planning to introduce a new network of revamped rawinsondes within the next year, under a project known as the “Radiosonde Replacement System (RRS)”.  These rawinsondes will be equipped with GPS locators allowing a precise latitude and longitude to be measured at every data point during the sounding flight as well as some of the most technologically-advanced sensing equipment for temperature, moisture, etc. that are available today.  In addition, enhanced processing software is being developed to encode this high-resolution data into BUFR, both for GTS exchange as well as for national long-term archiving purposes.  The plan is to begin producing test archive data sets within the coming year, followed soon thereafter by the introduction of high-resolution BUFR data sets onto the GTS for international exchange, although it should be noted that alphanumeric TEMP and PILOT messages will also be produced from this data in order to allow continued international exchange with those centers which will not yet be able to handle the enhanced-resolution BUFR products.  The below list represents the set of additional new BUFR descriptors that will be required in order to be able to encode these new products.  Note that, although there are no plans within the USA to make use of any of the corresponding CREX versions of these descriptors, we nonetheless felt that it might be useful to go ahead and propose CREX counterparts for these descriptors in case other centers might eventually wish to exchange such information.

2.0 Proposal

We propose the following new BUFR/CREX descriptors:

| 1. | Radiosonde serial number | 0-01-090 | CCITT IA5 | 0 | 0 | 160 |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | B-01-090 | Character | 0 |  | 20 |
| 2. | Radiosonde ascension number | 0-01-091 | Numeric | 0 | 0 | 14 |
|  |  | B-01-091 | Numeric | 0 |  | 4 |
| 3. | Radiosonde release number | 0-01-092 | Numeric | 0 | 0 | 3 |
|  |  | B-01-092 | Numeric | 0 |  | 1 |
| 4. | Balloon lot number | 0-01-093 | CCITT IA5 | 0 | 0 | 96 |
|  |  | B-01-093 | Character | 0 |  | 12 |
| 5. | WBAN Number | 0-01-094 | Numeric | 0 | 0 | 17 |
|  |  | B-01-094 | Numeric | 0 |  | 5 |
| 6. | Observer identification | 0-01-095 | CCITT IA5 | 0 | 0 | 32 |
|  |  | B-01-095 | Character | 0 |  | 4 |
| 7. | Radiosonde configuration | 0-02-016 | Flag table | 0 | 0 | 5 |
|  |  | B-02-016 | Flag table | 0 |  | 2 |
| 8. | Radiosonde ground receiving system | 0-02-066 | Code table | 0 | 0 | 6 |
|  |  | B-02-066 | Code table | 0 |  | 2 |
| 9. | Radiosonde operating frequency | 0-02-067 | Hz | -5 | 0 | 15 |
|  |  | B-02-067 | Hz | -5 |  | 5 |
| 10. | Balloon manufacturer | 0-02-080 | Code table | 0 | 0 | 4 |
|  |  | B-02-080 | Code table | 0 |  | 2 |
| 11. | Type of balloon | 0-02-081 | Code table | 0 | 0 | 5 |
|  |  | B-02-081 | Code table | 0 |  | 2 |
| 12. | Weight of balloon | 0-02-082 | Kg | 3 | 0 | 12 |
|  |  | B-02-082 | Kg | 3 |  | 4 |
| 13. | Type of balloon shelter | 0-02-083 | Code table | 0 | 0 | 4 |
|  |  | B-02-083 | Code table | 0 |  | 2 |
| 14. | Type of gas used in balloon | 0-02-084 | Code table | 0 | 0 | 2 |
|  |  | B-02-084 | Code table | 0 |  | 1 |
| 15. | Amount of gas used in balloon | 0-02-085 | Kg | 3 | 0 | 13 |
|  |  | B-02-085 | Kg | 3 |  | 4 |
| 16. | Balloon flight train length | 0-02-086 | m | 1 | 0 | 10 |
|  |  | B-02-086 | m | 1 |  | 4 |
| 17. | Type of pressure sensor | 0-02-095 | Code table | 0 | 0 | 5 |
|  |  | B-02-095 | Code table | 0 |  | 2 |
| 18. | Type of temperature sensor | 0-02-096 | Code table | 0 | 0 | 5 |
|  |  | B-02-096 | Code table | 0 |  | 2 |
| 19. | Type of humidity sensor | 0-02-097 | Code table | 0 | 0 | 5 |
|  |  | B-02-097 | Code table | 0 |  | 2 |
| 20. | Type of surface observing equipment | 0-02-115 | Code table | 0 | 0 | 5 |
|  |  | B-02-115 | Code table | 0 |  | 2 |
| 21. | RRS flight level significance | 0-08-040 | Code table | 0 | 0 | 6 |
|  |  | B-08-040 | Code table | 0 |  | 2 |
| 22. | RRS data significance | 0-08-041 | Code table | 0 | 0 | 4 |
|  |  | B-08-041 | Code table | 0 |  | 2 |
| 23. | Type of termination | 0-08-077 | Code table | 0 | 0 | 2 |
|  |  | B-08-077 | Code table | 0 |  | 1 |
| 24. | Relative humidity | 0-13-009 | % | 1 | 1000 | 12 |
|  |  | B-13-009 | % | 1 |  | 4 |
| 25. | Software identification | 0-25-061 | CCITT IA5 | 0 | 0 | 96 |
|  |  | B-25-061 | Character | 0 |  | 12 |
| 26. | Orientation correction (azimuth) | 0-25-065 | Degree | 2 | 1000 | 11 |
|  |  | B-25-065 | Degree | 2 |  | 4 |
| 27. | Orientation correction (elevation) | 0-25-066 | Degree | 2 | 1000 | 11 |
|  |  | B-25-066 | Degree | 2 |  | 4 |
| 28. | Radiosonde release point pressure correction | 0-25-067 | Pa | 0 | 8000 | 14 |
|  |  | B-25-067 | Pa | 0 |  | 4 |
| 29. | Number of archive recomputes | 0-25-068 | Numeric | 0 | 0 | 7 |
|  |  | B-25-068 | Numeric | 0 |  | 3 |
| 30. | RRS flight level pressure corrections | 0-25-069 | Flag table | 0 | 0 | 8 |
|  |  | B-25-069 | Flag table | 0 |  | 3 |
| 31. | RRS Data quality check indicator | 0-33-015 | Code table | 0 | 0 | 6 |
|  |  | B-33-015 | Code table | 0 |  | 2 |
| 32. | RRS Data quality check mark | 0-33-016 | Code table | 0 | 0 | 3 |
|  |  | B-33-016 | Code table | 0 |  | 1 |
| 33. | Reason for termination | 0-35-035 | Code table | 0 | 0 | 5 |
|  |  | B-35-035 | Code table | 0 |  | 2 |

along with the following additional note under BUFR/CREX Class 1:

(12)	Descriptor 0-01-091 is to be used for reporting the sequential number of the current radiosonde reporting period (e.g. synoptic cycle) within a given year or other similar locally-defined length of time.  Descriptor 0-01-092 is to be used in the case of multiple sequential radiosonde releases during a single reporting period (e.g. synoptic cycle), in order to indicate which particular release generated the corresponding data values.

Within the above list, 0-01-094 and 0-13-009 may appear to be odd requests for international descriptors, so in either case we would certainly be willing to use local descriptors instead to report such information if the meeting would prefer such an approach.  In the first instance, this descriptor represents an identifier from the first major attempt (during the 1950's) at a coordinated station numbering scheme among different weather reporting authorities including the U.S. Weather Bureau, the U.S. Air Force, Navy, and Army, the Canadian Department of Transportation, and certain German and Korean stations with close ties to the U.S. Weather Bureau at that time.  This identifier is still used in certain national long-term archives, and therefore it is desired to be able to retain this information under the new (I.e. BUFR) storage scheme.	In the second instance, it is desired to be able to retain the raw (I.e. unprocessed) relative humidity value reported by the sensor in order to track, among other things, when a sensor begins to malfunction.  The meeting may have a better approach in mind to deal with this requirement, although it should be pointed out that the use of Table C operators to amend existing descriptor 0-13-003 was already considered and rejected owing to the inability of the current RRS software (indeed, of much of the software that we have seen!) to handle the 2-03-YYY operator that would be required in order to do so.

At any rate, following are the code and flag tables which complete the definition of the above requested BUFR/CREX descriptors:

Radiosonde configuration (0-02-016)

| Bit | Meaning |
| --- | --- |
| 1 | Train regulator |
| 2 | Light unit |
| 3 | Parachute |
| 4 | Rooftop release |
| All 5 | Missing value |

Radiosonde ground receiving system (0-02-066)

| Code | Meaning |
| --- | --- |
| 0 | ART-1 |
| 1 | ART-2 |
| 2 | VIZ GPS |
| 3 | Vaisala GPS |
| 4 | ATIR |
| 5 | Sippican GPS |
| 6 | IMS GPS |
| 7-61 | Reserved |
| 62 | Other |
| 63 | Missing value |

Balloon manufacturer (0-02-080)

| Code | Meaning |
| --- | --- |
| 0 | Kaysam |
| 1 | Totex |
| 2 | KKS |
| 3-13 | Reserved |
| 14 | Other |
| 15 | Missing value |

Type of balloon (0-02-081)

| Code | Meaning |
| --- | --- |
| 0 | GP26 |
| 1 | GP28 |
| 2 | GP30 |
| 3 | HM26 |
| 4 | HM28 |
| 5 | HM30 |
| 6 | SV16 |
| 7-29 | Reserved |
| 30 | Other |
| 31 | Missing value |

Type of balloon shelter (0-02-083)

| Code | Meaning |
| --- | --- |
| 0 | High bay |
| 1 | Low bay |
| 2 | BILS |
| 3 | Roof-top BILS |
| 4-13 | Reserved |
| 14 | Other |
| 15 | Missing value |

Type of gas used in balloon (0-02-084)

| Code | Meaning |
| --- | --- |
| 0 | Hydrogen |
| 1 | Helium |
| 2 | Natural Gas |
| 3 | Missing value |

Type of pressure sensor (0-02-095)

| Code | Meaning |
| --- | --- |
| 0 | Capacitance aneroid |
| 1 | Derived from GPS |
| 2 | Resistive strain gauge |
| 3-29 | Reserved |
| 30 | Other |
| 31 | Missing value |

Type of temperature sensor (0-02-096)

| Code | Meaning |
| --- | --- |
| 0 | Rod thermistor |
| 1 | Bead thermistor |
| 2 | Capacitance bead |
| 3-29 | Reserved |
| 30 | Other |
| 31 | Missing value |

Type of humidity sensor (0-02-097)

| Code | Meaning |
| --- | --- |
| 0 | VIZ Mark II Carbon Hygristor |
| 1 | VIZ B2 Hygristor |
| 2 | Vaisala A-Humicap |
| 3 | Vaisala H-Humicap |
| 4 | Capacitance sensor |
| 5 | Vaisala RS90 |
| 6 | Sippican Mark IIA Carbon Hygristor |
| 7-29 | Reserved |
| 30 | Other |
| 31 | Missing value |

Type of surface observing equipment (0-02-115)

| Code | Meaning |
| --- | --- |
| 0 | PDB |
| 1 | RSOIS |
| 2 | ASOS |
| 3 | Psychrometer |
| 4 | F420 |
| 5-29 | Reserved |
| 30 | Other |
| 31 | Missing value |

RRS flight level significance (0-08-040)

| Code | Meaning |
| --- | --- |
| 0 | High resolution data sample |
| 1 | Within 20 hPa of surface |
| 2 | Pressure less than 10 hPa (i.e., 9, 8, 7, etc.) when no other reason applies |
| 3 | Base pressure level for stability index |
| 4 | Begin doubtful temperature, height data |
| 5 | Begin missing data (all elements) |
| 6 | Begin missing RH data |
| 7 | Begin missing temperature data |
| 8 | Highest level reached before balloon descent because of icing or turbulence |
| 9 | End doubtful temperature, height data |
| 10 | End missing data (all elements) |
| 11 | End missing RH data |
| 12 | End missing temperature data |
| 13 | Zero degrees C crossing(s) for RADAT |
| 14 | Standard pressure level |
| 15 | Operator added level |
| 16 | Operator deleted level |
| 17 | Balloon re-ascended beyond previous highest ascent level |
| 18 | Significant RH level |
| 19 | RH level selection terminated |
| 20 | Surface level |
| 21 | Significant temperature level |
| 22 | Mandatory temperature level |
| 23 | Flight termination level |
| 24 | Tropopause(s) |
| 25 | Aircraft report |
| 26 | Interpolated (generated) level |
| 27 | Mandatory wind level |
| 28 | Significant wind level |
| 29 | Maximum wind level |
| 30 | Incremental wind level (fixed regional) |
| 31 | Incremental height level (generated) |
| 32 | Wind termination level |
| 33 | Pressure 100 to 110 hPa, when no other reason applies |
| 34-39 | Reserved |
| 40 | Significant thermodynamic level (inversion) |
| 41 | Significant RH level ( per NCDC criteria) |
| 42 | Significant temperature level (per NCDC) |
| 43-61 | Reserved |
| 62 | Other |
| 63 | Missing value |

RRS data significance (0-08-041)

| Code | Meaning |
| --- | --- |
| 0 | RRS parent site |
| 1 | RRS observation site |
| 2 | Balloon manufacture date |
| 3 | Balloon launch point |
| 4 | Surface observation |
| 5 | Surface observation displacement from launch point |
| 6 | Flight level observation |
| 7 | Flight level termination point |
| 8-14 | Reserved |
| 15 | Missing value |

Type of termination (0-08-077)

| Code | Meaning |
| --- | --- |
| 0 | Radiosonde flight |
| 1 | Wind processing |
| 2 | Reserved |
| 3 | Missing value |

RRS Flight Level Pressure Corrections (0-25-069)

| Bit | Meaning |
| --- | --- |
| 1 | Smoothed |
| 2 | Baseline adjusted |
| 3 | Normalized time interval |
| 4 | Outlier checked |
| 5 | Plausibility checked |
| 6 | Consistency checked |
| 7 | Interpolated |
| All 8 | Missing value |

RRS Data Quality Check Indicator (0-33-015)

| Code | Meaning |
| --- | --- |
| 0 | Passed all checks |
| 1 | Missing-data check |
| 2 | Descending/reascending balloon check |
| 3 | Data plausibility check (above limits) |
| 4 | Data plausibility check (below limits) |
| 5 | Superadiabatic lapse rate check |
| 6 | Limiting angles check |
| 7 | Ascension rate check |
| 8 | Excessive change from previous flight |
| 9 | Balloon overhead check |
| 10 | Wind speed check |
| 11 | Wind direction check |
| 12 | Dependency check |
| 13 | Data valid but modified |
| 14 | Data outlier check |
| 15-62 | Reserved |
| 63 | Missing value |

RRS Data Quality Check Mark (0-33-016)

| Code | Meaning |
| --- | --- |
| 0 | Passed all automatic checks |
| 1 | Questionable data (per automatic checks) |
| 2 | Rejected data (per automatic checks) |
| 3 | Missing data |
| 4 | Rejected by user - passed automatic checks |
| 5 | Rejected by user - and questionable (per checks) |
| 6 | Rejected by user |
| 7 | Missing value |

Reason for termination (0-35-035)

| Code | Meaning |
| --- | --- |
| 0 | Balloon burst |
| 1 | Balloon forced down by icing |
| 2 | Leaking or floating balloon |
| 3 | Weak or fading signal |
| 4 | Battery failure |
| 5 | Ground equipment failure |
| 6 | Signal interference |
| 7 | Radiosonde failure |
| 8 | Loss of GPS signal |
| 9 | Limiting angles |
| 10 | Excessive missing data frames |
| 11 | Excessive missing temperature |
| 12 | Excessive missing pressure |
| 13 | User terminated |
| 14 | Software error |
| 15-29 | Reserved |
| 30 | Other |
| 31 | Missing value |

********