| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES PRAGUE, 22-26 APRIL 2002 |  | ET/DR&C2/Doc.3.5.3(1) ______ (1.III.2002) ENGLISH ONLY |
| --- | --- | --- |

BUFR and CREX

A Template for Tropical Cyclone Information from EPS in BUFR,

and associated descriptors and code tables

(Submitted by JAPAN)

----------------------------------------------------------------------------------------------

Summary and Purpose of Document

This document contains a proposal on a template of BUFR for Tropical Cyclone Information derived from Ensemble Prediction Systems, and new descriptors and code tables associated to the template.

----------------------------------------------------------------------------------------------

Action Proposed

The Team is invited to examine the proposed template, and make modifications, if necessary, with a view to including it in the Attachment to FM94-XII BUFR of Manual on Codes, Volume I.2.

The Team is also invited to examine associated descriptors and code tables to be introduced to the BUFR/CREX tables with e view to approving them for fast track implementation.

Reference:

1.	Report of the MEETING OF THE EXPERT TEAM ON ENSEMBLE PREDICTION 	SYSTEMS (Tokyo, 15 - 19 October 2001)

Discussion

1.	The meeting of the Expert Team on Ensemble Prediction Systems (ET/EPS) was held at Tokyo from 15 to 19 October 2001 and noted several trends in EPS.  Among them, the Team noted that the EPS products are targeted at not only extratropical systems but also  tropical phenomena and mesoscale features.  It paid attention to the operational experience in Japan Meteorological Agency, and noted that application of EPS techniques to typhoon track forecast was feasible.

2.	At the meeting, the Team defined several derived products which were recommended for routine dissemination including tropical storm tracks (latitude/longitude locations from EPS members).  It agreed that FM 94-XII BUFR could be used for exchange of tropical storm tracks from EPS members as follows, while the Team considered FM 92-XII GRIB Edition 2 the most practical code for exchange of gridded EPS data.

Lat/Lon position of tropical cyclone tracks could be transmitted using BUFR code.  However, some adjustment will be necessary for having the ensemble set of tracks identified and included in one single BUFR report.  The ET requested the ET on Data Representation and Codes to finalize common sequences in BUFR Tables for that purpose.

3.	According to this agreement, an original template was developed by JMA and circulated to the Members of ET/EPS for examination with a view to submitting it to the meeting of the ET on Data Representation and Codes.  A template, and descriptors and associated tables required for the template, which are based on the comments of the Members of ET/EPS are described in the ANNEX to this document.

4.	A validation test for the template and associated descriptors and tables is planned by ET/EPS.  Centres participating in the test are listed below, and the test will be completed by ..........  The result of the test will be reported to the ET/DR&C by JMA.

ECMWF, Japan Meteorological Agency, .....

Proposal

5.	The proposed template of FM94-XII BUFR for Tropical Cyclone Information derived from EPS is shown in Item 1 in the ANNEX to this document.  The Team is invited to examine the proposed template with a view to including it in the Attachment to BUFR of Manual on Codes, Volume I.2.

6.	Proposed descriptors and associated code tables involved in the template are shown in Item 2 in the ANNEX to this document.  The Team is invited to examine them with a view to approval for fast track implementation.

ANNEX

1.	Template and sample data of BUFR for Tropical Cyclone Tracks derived from EPS to be included in Attachment of the Manual on Codes, Volume I.2

EXAMPLE OF A TROPICAL CYCLONE TRACKS DERIVED FROM EPS

Note: ^ means space in the sample data below.

| Table ref. | Element name | 1st subset | 2nd subset |  | Bits |
| --- | --- | --- | --- | --- | --- |
| 0 01 033 | Identification of originating/generating centre | 34 | 34 | ... | 8 |
| 0 01 034 | Identification of originating/generating subcentre | 0 | 0 | ... | 8 |
| 0 01 032 | Generating application | 70 | 70 |  | 8 |
| 0 01 025 | Storm identifier | 15W | 15W | ... | 24 |
| 0 01 027 | WMO long storm name | DANAS^^^^^ | DANAS^^^^^ | ... | 80 |
| 0 01 090 | Technique for making up initial perturbations | 1 | 1 | ... | 8 |
| 0 01 091 | Ensemble member number | 1 | 2 | ... | 10 |
| 0 01 092 | Type of ensemble forecast | 1 | 3 | ... | 8 |
| 3 01 011 | Year | 2001 | 2001 | ... | 12 |
|  | Month | 9 | 9 | ... | 4 |
|  | Day | 8 | 8 | ... | 6 |
| 3 01 012 | Hour | 0 | 0 | ... | 5 |
|  | Minute | 0 | 0 | ... | 6 |
| 1 10 000 | Delayed replication of 10 descriptors |  |  |  |  |
| 0 31 001 | Delayed descriptor replication factor (the number of forecast hours) | 7 | 7 | ... | 8 |
| 0 08 021 | Time significance (forecast time) | 4 | 4 | ... | 5 |
| 0 04 014 | Time increment | 0 | 0 | ... | 11 |
| 0 08 005 | Meteorological attribute significance (storm centre) | 1 | 1 | ... | 4 |
| 0 05 002 | Latitude (coarse accuracy) | 11850 | 11840 | ... | 15 |
| 0 06 002 | Longitude (coarse accuracy) | 32360 | 32190 | ... | 16 |
| 0 10 051 | Pressure reduced to mean sea level | 9500 | 9450 | ... | 14 |
| 0 08 005 | Meteorological attribute significance (location of maximum wind) | 3 | 3 | ... | 4 |
| 0 05 002 | Latitude (coarse accuracy) | 11630 | 11640 | ... | 15 |
| 0 06 002 | Longitude (coarse accuracy) | 32250 | 32210 | ... | 16 |
| 0 11 012 | Wind speed at 10m | 412 | 437 | ... | 12 |
|  | Time significance (forecast time) | ... | ... | ... | ... |
|  | ... | ... | ... | ... | ... |
|  | Wind speed at 10m | ... | ... | ... | ... |
|  | Time significance (forecast time) | 4 | 4 | ... | 5 |
|  | Time increment | 12 | 12 | ... | 11 |
|  | Meteorological attribute significance (storm centre) | 1 | 1 | ... | 4 |
|  | Latitude (coarse accuracy) | 12520 | 12360 | ... | 15 |
|  | Longitude (coarse accuracy) | 31950 | 31780 | ... | 16 |
|  | Pressure reduced to mean sea level | 9700 | 9600 | ... | 14 |
|  | Meteorological attribute significance (location of maximum wind) | 3 | 3 | ... | 4 |
|  | Latitude (coarse accuracy) | 12430 | 123300 | ... | 15 |
|  | Longitude (coarse accuracy) | 32010 | 31800 | ... | 16 |
|  | Wind speed at 10m | 283 | 360 | ... | 12 |

2.	New descriptors for Tropical Cyclone Tracks derived from EPS

| Table ref. | Element name | Unit | Scale | Ref. value | Data width (Bits) |
| --- | --- | --- | --- | --- | --- |
| 0 01 090 | Technique for making up initial perturbations | Code table | 0 | 0 | 8 |
| 0 01 091 | Ensemble member number | Numeric | 0 | 0 | 10 |
| 0 01 092 | Type of ensemble forecast | Code table | 0 | 0 | 8 |
|  |  | Unit | Scale | Data width (Character) |
| B 01 090 |  | Code table | 0 | 3 |
| B 01 091 |  | Numeric | 0 | 4 |
| B 01 092 |  | Code table | 0 | 3 |

3.	New Code Tables

| 0 01 090 |
| --- |
| Technique for making up initial perturbations |
| Code figure |  |  |  |  |
| 0 | LAF (Lagged-Average Forecasting) |
| 1 | Breeding |
| 2 | Singular vectors |
| 3 | Multiple analysis cycles |
| 4-191 | Reserved |
| 192-254 | Reserved for local use |
| 255 | Missing value |
| 0 01 092 |
| Type of ensemble forecast |
| Code figure |  |  |  |  |
| 0 | Unperturbed high-resolution control forecast |
| 1 | Unperturbed low-resolution control forecast |  |  |  |
| 2 | Negatively perturbed forecast |
| 3 | Positively perturbed forecast |
| 4-191 | Reserved |
| 192-254 | Reserved for local use |
| 255 | Missing value |

# Text boxes

Replicate 5 times