| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES PRAGUE, CZECH REPUBLIC, 22-26 APRIL 2002 |  | ET/DR&C2/Doc.3.5.6(1) _______ (13.II.2002) ENGLISH ONLY |
| --- | --- | --- |

A Proposal for a new BUFR/CREX Table B descriptor for

“Height above surface of the base of the lowest cloud seen”

Submitted by J. Ator (USA)

________________________________________________________________

Summary and Purpose of Document

This paper proposes an improved way of representing, within BUFR and CREX, a code figure from WMO Code Table 1600 that is reported within SYNOP, SHIP, and TEMP reports.

________________________________________________________________

ACTION PROPOSED

The meeting is requested to consider the proposal and recommend it for fast-track implementation.

1.0	Discussion

In SYNOP, SHIP, and TEMP reports, the code figure h represents the “height above surface of the base of the lowest cloud seen” according to the following WMO Code Table 1600 in Manual 306, Part A:

Code

figure

0			   0 to   50m

1			  50 to  100m

2			 100 to  200m

3			 200 to  300m

4			 300 to  600m

5			 600 to 1000m

6			1000 to 1500m

7			1500 to 2000m

8			2000 to 2500m

9			2500m or more, or no clouds

/			Height of base of cloud not known or base of coulds at a level lower and tops at a level higher than that of station

Historically, this information has been presented in BUFR using descriptor 0-20-013; however, we believe this to be inadequate for two reasons:

the value corresponding to 0-20-013 is a discrete value, rather than a range as indicated in the above table, and thus the best we can do is to pick a representative point (e.g. the lower bound, or perhaps the midpoint in the cases of code figures 1 through 8 (?)).  Furthermore, we cannot explicitly represent the range via two consecutive occurrences of the descriptor 0-20-013, because BUFR regulation 94.5.3.4 (or, in the case of CREX, regulation 95.3.5.1) only applies to descriptors within classes 04-07.

Reporting “missing” for 0-20-013 does not adequately convey the full sense of the code figure “/” from WMO Code Table 1600, and there is also no way within 0-20-013 to indicate “no clouds” as reportable via code figure “9" from WMO Code Table 1600.

Thus, it seems that perhaps the best we can do is to create a new BUFR/CREX code table whose entries mirror those of WMO Code Table 1600.  This would allow for an unambiguous one-to-one mapping of code figures between the traditional code forms and BUFR/CREX, and there is certainly ample precedent for such situations.

2.0	Proposal

We propose the following new BUFR/CREX descriptor:

Height above surface of the base of the lowest cloud seen

0-20-007		Code table	0	0	4

B-20-007		Code table	0		2

Code

figure

0		   0 to   50m

1		  50 to  100m

2		 100 to  200m

3		 200 to  300m

4		 300 to  600m

5		 600 to 1000m

6		1000 to 1500m

7		1500 to 2000m

8		2000 to 2500m

9		2500m or more, or no clouds

10-13		Reserved

14		Height of base of cloud not known or base of coulds at a level lower and tops at a level higher than that of station

15		Missing

In addition, we propose that this new descriptor replace the use of 0-20-013 in the SYNOP, SHIP, and radiosonde templates in all situations where it is being used to represent a code figure h from WMO Code Table 1600 in Manual 306, Part A.

In addition, we propose to amend the attachment to Manual 306, Part C in order to indicate the new correlation between BUFR code table 0-20-007 and h - Code table 1600.