| WORLD METEOROLOGICAL ORGANIZATION ___________________ COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES Third session Arusha, Tanzania, 17-21 February 2003 |  | Distribution: RESTRICTED ET/DR&C/Doc. 3.1.1(1)Rev.1 (15.I.2003) _________ Item: 3.1.1 ENGLISH only |
| --- | --- | --- |

Additional entries in BUFR Code tables to support ENVISAT satellite data

Submitted by Milan Dragosavac (ECMWF)

__________________________________________________________________

Summary and Purpose of Document

The ENVISAT satellite has been launched in March 2002. The satellite is multi-instrument producing environmental measurements. This proposal covers oceanographic and meteorological data to support near real time products on the GTS used in NWP.

ACTION PROPOSED

The team is requested to study the document for reservation of BUFR table B and D entries and pre-operational implementation.

DISCUSSION

1. Background

In March 2002, ENVISAT satellite was successfully launched by ESA.  ENVISAT is now completing its commissioning phase. The satellite carries a number of instruments among which ASAR, MERIS, AATSR, RA-2, GOMOS, MIPAS and SCIAMACHY are of meteorological and NWP interest.

ECMWF developed software to extract ENVISAT PDS data and create BUFR data containing subset information available in the original data set.  At the same time some evaluation of SCIAMACHY, MIPAS, GOMOS and ASAR data has been done at ECMWF.

2. Proposal

The proposal covers seven instruments:

a) AATSR - Advanced Along Track Scanning Radiometer is the advanced version of the ATSR system operated on ERS1 and ERS2.  The main objective of the AATSR is precise measurement of sea surface temperature (SST).

Proposal for standard WMO BUFR Table B entries:

------------------------------------------------

025061 SOFTWARE IDENTIFICATION   CCITTIA5        0          0   96

AND VERSION NUMBER

001096 STATION ACQUISITION       CCITTIA5        0          0  160

002173 MEAN ACROSS TRACK PIXEL   NUMERIC         0          0    9

NUMBER

012180 AVERAGED 12 MICRON BT FOR K               2          0   16

ALL CLEAR PIXELS AT NADIR

012181 AVERAGED 11 MICRON BT FOR K               2          0   16

ALL CLEAR PIXELS AT NADIR

012182 AVERAGED 3.7 MICRON BT    K               2          0   16

FOR ALL CLEAR PIXELS AT

NADIR

012183 AVERAGED 12 MICRON BT FOR K               2          0   16

ALL CLEAR PIXELS, FORWARD

VIEW

012184 AVERAGED 11 MICRON BT     K               2          0   16

FOR ALL CLEAR PIXELS,

FORWARD VIEW

012185 AVERAGED 3.7 MICRON BT    K               2          0   16

FOR ALL CLEAR PIXELS,

FORWARD VIEW

012186 MEAN NADIR SEA SURFACE    K               2          0   16

TEMPERATURE

012187 MEAN DUAL VIEW SEA        K               2          0   16

SURFACE TEMPERATURE

021086 NUMBER OF PIXELS IN NADIR NUMERIC         0          0    9

ONLY, AVERAGE

021087 NUMBER OF PIXELS IN DUAL  NUMERIC         0          0    9

VIEW, AVERAGE

033043 AST CONFIDENCE            FLAG TABLE      0          0    8

033043 FLAG TABLE AST CONFIDENCE

Bit No.             Meaning

1                 SEA MDS. NADIR ONLY SST RETRIEVAL USED 3.7

MICRON CHANNEL. LAND MDS RESERVED

2                 SEA MDS. DUAL VIEW SST RETRIEVAL USED 3.7 MICRON

CHANNEL. LAND MDS RESERVED

3                 NADIR VIEW CONTAINS DAY TIME DATA

4                 FORWARD VIEW CONTAINS DAY TIME DATA

5-7               RESERVED

All               MISSING VALUE

Common Code Table C-5:

001007 - satellite identifier

Add 60 for ENVISAT

Proposal for standard WMO BUFR Table D entries:

-----------------------------------------------

312045    - AATSR sea surface temperatures

312045    001007 Satellite identifier

002019 Satellite instruments

001096 Station acquisition

025061 Software identification and version number

005040 Orbit number

301011 Date

301013 Time

301021 Lat/long

007002 Height or altitude

012180 Average 12 micron BT for all clear pixels at nadir

012181 Average 11 micron BT for all clear pixels at nadir

012182 Average 3.7 micron BT for all clear pixels at nadir

012183 Average 12 micron BT for all clear pixels, forward             			view

012184 Average 11 micron BT for all clear pixels, forward

view

012185 Average 3.7 micron BT for all clear pixels, forward

view

002173 Mean across track pixel number

021086 Number of pixels in nadir only, average

012186 Mean nadir sea surface temperature

021087 Number of pixels in dual view, average

012187 Mean dual view sea surface temperature

033043 ATS confidence

b) SCIAMACHY- The Scanning Imaging Absorbtion Spectrometer for Atmospheric Cartography.  The instrument provides spectra measured from light transmitted, back scattered or reflected by trace gases in the atmosphere.

Use standard entry 310020

c) MIPAS - The Michelson Interferometer for Passive Atmospheric Sounding.  The instrument measures atmospheric radiation emitted by trace gases in the infrared spectral range 4.14 to 14.6 micro meters.

BUFR Table B reserved entry:

013080 INTEGRATED WATER VAPOUR KG/M**2       8      0    30

DENSITY

BUFR table D reserved entry:

310030     310022 Satellite id, product type

301011 Date

301013 Time

301021 Lat/long

304034 Lat/long, solar elevation, number of layers

310029 Layer, ozone, height, temperature and water vapour

310029     110000

031001 Delayed replication

201138 Change data width

202130 Change scale

007004 Pressure

007004 Pressure

202000 Cancel operator

201000 Cancel operator

015020 Integrated ozone density

010002 Height

012101 Temperature

013080 Integrated water vapour density

d) GOMOS - The Global Ozone Monitoring by Occulation of Stars Gomos measures tangential atmospheric ultraviolet, visual and infrared light.

The BUFR template is the same as for MIPAS data

e) MERIS - The Medium Resolution Imaging Spectrometer: The instrument produces multi-spectral images obtained in a downward viewing push broom imaging manner.  The 15 bands acquire radiance in the visible and near infra-red bands.

BUFR table B reserved entries:

010080 VIEWING ZENITH ANGLE       DEGREE        2        -9000  15

027080 VIEWING AZIMUTH ANGLE      DEGREE TRUE   2            0  16

013090 CLOUD OPTICAL THICKNESS    NUMERIC       0            0   8

013095 TOTAL COLUMN WATER VAPOUR  KG/M**2       4            0  19

BUFR table D reserved entries:

312050     001007 Satellite identifier

002019 Instrument type

001096 Station acquisition

025061 Software identification

005040 Orbit number

301011 Date

301013 Time

301021 Lat/long

007025 Solar zenith angle

005022 Solar azimuth

010080 Viewing zenith angle

027080 Viewing azimuth angle

008003 Vertical significance

007004 Pressure

013090 Cloud optical thickness

008003 Vertical significance

201131 Change data width

202129 Change scale

007004 Pressure

007004 Pressure

202000 Cancel operator

201000 Cancel operator

013095 Total column water vapour

f) ASAR - The Advanced Synthetic Aperture Radar is a high resolution imaging radar.

Ocean cross spectra -   ( WVS )

312051     001007 Satellite identifier

002019 Satellite instrument type

001096 Station acquisition

025061 Software identification

005040 Orbit number

008075 Ascending/descending orbit designator

301011 Date

301013 Time

301021 Lat/long

001012 Direction of motion of moving observing platform

201131 Change data width

001013 Speed of motion of moving observing platform

201000 Cancel operator

010032 Satellite distance to Earth centre

010033 Altitude (platform to ellipsoid)

010034 Earth radius

007002 Height

008012 Land/sea qualifier

025100 Image processing summary

025101 Number of input data gaps

025102 Number of missing lines excluding data gaps

002104 Antenna polarisation

025103 Number of directional bins

025104 Number of wave-length bins

025105 First directional bin

025106 Directional bin step

025107 First wave-length bin

025108 Last wave-length bin

002111 Radar incidence angle

002121 Mean frequency

002026 Cross track resolution

002027 Along track resolution

021130 Spectrum total energy

021131 Spectrum maximum energy

021132 Direction of spectrum max on higher resolution grid

021133 Wavelength of spectrum max on higher resolution grid

021064 Clutter noise estimate

025014 Azimuth clutter cut-off

021134 Range resolution of cross covariance spectrum

107018 Replicate next 7 descriptors 18 times

005030 Direction (spectral)

105024 Replicate 5 descriptors 24 time

201130 Change data width

006030 Wave number (spectral)

201000 Cancel operator

021135 Real part of cross spectra

021136 Imaginary part of cross spectra

033044 ASAR quality

New Table B descriptors

010032 SATELLITE DISTANCE TO EARTH       M          1           0  27

CENTRE

010033 ALTITUDE (PLATFORM TO ELLIPSOID)  M          1           0  27

010034 EARTH RADIUS                      M          1           0  27

025100 IMAGE PROCESSING SUMMARY          FLAG TABLE 0           0  10

025101 NUMBER OF INPUT DATA GAPS         NUMERIC    0           0   8

025102 NUMBER OF MISSING LINES EXCLUDING NUME       0           0   8

DATA GAPS

025103 NUMBER OF DIRECTIONAL BINS        NUMERIC    0           0   8

025104 NUMBER OF WAVE-LENGHT BINS        NUMERIC    0           0   8

025105 FIRST DIRECTIONAL BIN             DEGREES    3           0  19

025106 DIRECTIONAL BIN STEP              DEGREES    3           0  19

025107 FIRST WAVE-LENGHT BIN             M          3           0  29

025108 LAST WAVE-LENGHT BIN              M          3           0  29

021130 SPECTRUM TOTAL ENERGY             NUMERIC    6           0  28

021131 SPECTRUM MAX ENERGY               NUMERIC    6           0  28

021132 DIRECTION OF SPECTRUM MAX ON      DEGREES    3           0  19

HIGHER RESOLUTION GRID

021133 WAVE-LENGHT OF SPECTRUM MAX ON    M          3           0  29

HIGHER RESOLUTION GRID

021134 RANGE RESOLUTION OF CRESS         RAD/M      3           0  19

COVARIANCE SPECTRUM

021135 REAL PART OF CROSS SPECTRA        NUMERIC    3     -524288  20

POLAR GRID NUMBER OF BINS

021136 IMAGINARY PART OF CROSS SPECTRA   NUMERIC    3     -524288  20

POLAR GRID NUMBER OF BINS

033044 ASAR QUALITY INFORMATION          FLAG TABLE 0           0  15

Flag table 025100 IMAGE PROCESSING SUMMARY

bit number        Meaning

1               Raw data analysis used for raw data correction.

Correction done using default parameters

2               Raw data analysis used for raw data correction.

Correction done using raw data analysis results

3               Antenna elevation pattern correction applied

4               Nominal chirp replica used

5               Reconstructed chirp used

6               Slant range to ground range Conversion applied

7-9             Reserved

All 10          Missing value

Flag table 033044  ASAR QUALITY INFORMATION

bit number        Meaning

1               Input data mean outside nominal range flag

2               Input data standard deviation outside nominal                                             			 range flag

3               Number of input data gaps > threshold value

4               Percentage of missing lines > threshold value

5               Doppler centroid uncertain. Confidence measure < 			 specific value

6               Doppler ambiguity estimate uncertain. Confidence 			 measure < specific value

7               Output data mean outside nominal range flag

8               Output data standard deviation outside nominal 			 range flag

9               Chirp reconstruction failed or is of low quality 			 flag

10               Data set missing

11               Invalid downlink parameters

12               Azimuth cut-off iteration count. The azimuth cut-			 off fit did not converge within

minimum number of iterations

13               Azimuth cut-off fit did not converge within a 				 minimum number of iterations

14               Phase information confidence measure. The 				 imaginary spectral peak is less than

a minimum threshold, or the zero lag shift is 				 greater than a minimum threshold

All 15           Missing value

OCEAN WAVE SPECTRA

--------------------

Table D sequence

312053    001007 Satellite identifier

002019 Satellite instrument type

001096 Station acquisition

025061 Software identification and version number

005040 Orbit number

008075 Ascending/descending orbit designator

301011 Date

301013 Time

301021 Lat/long

001012 Direction of motion of moving observing platform

201131 Change data width

001013 Speed of motion of moving observing platform

201000 Cancel operator

010032 Satellite distance to Earth centre

010033 Altitude (platform to ellipsoid)

010034 Earth radius

007002 Height or altitude

008012 Land/sea qualifier

025100 Image processing summary

025101 Number of input data gaps

025102 Number of missing lines excluding data gaps

002104 Antenna polarisation

025103 Number of directional bins

025104 Number of wave-length bins

025105 First directional bin

025106 Directional bin step

025107 First wave-length bin

025108 Last wave-length bin

011001 Wind direction

011002 Wind speed

022160 Normalized inverse wave age

025138 Average signal to noise ratio

201130 Change data width

202129 Change scale

022021 Height of waves

202000 Cancel operator

201000 Cancel operator

033048 Confidence measure for SAR inversion

033049 Confidence measure for wind retrieval

002026 Cross track resolution

002027 Along track resolution

021130 Spectrum total energy

021131 Spectrum max energy

021132 Direction of spectrum max

021133 Wave-length of spectrum max

025014 Azimuth clutter cut-off

106036 Replicate 6 descriptors 36 times

005030 Direction (spectral)

104024 Replicate 4 descriptors 24 time

201130 Change data width

006030 Wave number (spectral)

201000 Cancel operator

022161 Wave spectra

033044 ASAR quality

Table B descriptors

008075 ASCENDING/DESCENDING ORBIT   CODE TABLE    0            0   2

DESIGNATOR

022160 NORMALIZED INVERSE WAVE AGE  NUMERIC       6            0  21

025138 AVERAGE SIGNAL TO NOISE      NUMERIC       0        -2048  12

RATIO

033048 CONFIDENCE MEASURE OF SAR    CODE TABLE    0            0   2

INVERSION

033049 CONFIDENCE MEASURE OF WIND   CODE TABLE    0            0   2

RETRIEVAL

022161 WAVE SPECTRA                 M**4          4            0  27

Code table 008075  Orbit designator

code figure           Meaning

1                  descending

2                  reserved

3                  Missing

Code table 033048  CONFIDENCE MEASURE OF SAR INVERSION

code figure           Meaning

0                  inversion successful

1                  inversion not successful

2                  reserved

3                  Missing

Code table 033049 CONFIDENCE MEASURE OF WIND RETRIEVAL

code figure           Meaning

0                  external wind direction used during 					 inversion

1                  External wind direction not used during 					 inversion

2                  reserved

3                  Missing

g) RA2 - Radar Altimeter-2

-----------------------

312052    001007 Satellite identifier

002019 Satellite instrument type

001096 Station acquisition

025061 Software identification

005040 Orbit number

025120 Ra2 L2 processing flag

025121 Ra2 L2 processing quality

025124 MWR L2 processing flag

025125 MWR L2 processing quality

025122 Hardware configuration for RF

025123 Hardware configuration for HPA

301011 Date

301013 Time

301021 Lat/long

007002 Height or altitude

002115 Instrument operations

033047 Measurement confidence data

010081 Altitude of COG above reference ellipsoid

010082 Instantaneous altitude rate

010083 Off nadir angle of the satellite from platform data

010084 Off nadir angle of the satellite from waveform data

002116 Percentage of 320 MHz band processed

002117 Percentage of 80 MHz band processed

002118 Percentage of 20 MHz band processed

002156 Percentage of valid Ku ocean retracker measurements

002157 Percentage of valid S  ocean retracker measurements

014050 Solar activity index

022150 Number of 18 Hz valid points for Ku band

022151 Ku band ocean range

022152 STD of 18Hz Ku band ocean range

022153 Number of 18 Hz valid points for S band

022154 S band ocean range

022155 STD of 18 Hz S band ocean range

022156 Ku band significant wave height

022157 STD of 18 Hz Ku band significant wave height

022158 S band significant wave height

022159 STD 18 Hz S band significant wave height

021137 Ku band corrected ocean backscatter coefficient

021138 STD Ku band corrected ocean backscatter coefficient

021139 Ku band net instrumental correction for AGC

021140 S band corrected ocean backscatter coefficient

021141 STD S band corrected ocean backscatter coefficient

021142 S band net instrumental correction for AGC

010085 Mean sea surface height

010086 Geoid height

010087 Ocean depth/land elevation

010088 Total geocentric ocean tide height solution 1

010089 Total geocentric ocean tide height solution 2

010090 Long period tide height

010091 Tidal loading height

010092 Solid earth tide height

010093 Geocentric pole tide height

011002 wind speed

025126 Model dry tropospheric correction

025127 Inverted barometer correction

025128 Model wet tropospheric correction

025129 MWR derived wet tropospheric correction

025130 Ra2 ionospheric correction on Ku band

025131 Ionospheric correction from Doris on Ku band

025132 Ionospheric correction  from model on Ku band

025133 Sea state bias correction on Ku band

025134 Ra2 ionospheric correction on S band

025135 Ionospheric correction from Doris on S band

025136 Ionospheric correction from model on S band

025137 Sea state bias correction on S band

013096 MWR water vapour content

013097 MWR liquid water content

011080 u component of model wind vector

011081 v component of model wind vector

012188 Interpolated 23.8 GHz brightness temp from MWR

012189 Interpolated 36.5 GHz brightness temp from MWR

002158 Mean nadir sea surface temperature

002187 Mean dual view sea surface temperature

033052 S band ocean retracking quality

033053 Ku band ocean retracking quality

021143 Ku band rain attenuation

021144 Altimeter rain flag

Table B descriptors

002115 INSTRUMENT OPERATIONS                CODE TABLE   0      0   3

002116 PERCENTAGE OF 320 MHZ BAND PROCESSED %            0      0   7

002117 PERCENTAGE OF 80 MHZ BAND PROCESSED  %            0      0   7

002118 PERCENTAGE OF 20 MHZ BAND PROCESSED  %            0      0   7

002156 PERCENTAGE OF VALID KU OCEAN         %            0      0   7

RETRACKER MEASUREMENTS

002157 PERCENTAGE OF VALID S OCEAN          %            0      0   7

RETRACKER MEASUREMENTS

002158 INSTRUMENT FLAG                     FLAG TABLE   0       0   9

002187 MWR INSTRUMENT FLAG                 FLAG TABLE   0       0   8

010081 ALTITUDE OF COG ABOVE REFERENCE     M            3       0  31

ELLIPSOID

010082 INSTANTANEOUS ALTITUDE RATE         M/S          3  -65536  17

010083 OFF NADIR ANGLE OF THE SATELLITE    DEGREE       2  -36000  17

FROM PLATFORM DATA

010084 OFF NADIR ANGLE OF THE SATELLITE

FROM WAVEFORM DATA                  DEGREE       2  -36000  17

010085 MEAN SEA SURFACE HEIGHT             M            3 -131072  18

010086 GEOID HEIGHT                        M            3 -131072  18

010087 OCEAN DEPTH/LAND ELEVATION          M            1 -131072  18

010088 TOTAL GEOCENTRIC OCEAN TIDE HEIGHT  M            3  -32768  16

SOLUTION 1

010089 TOTAL GEOCENTRIC OCEAN TIDE HEIGHT  M            3  -32768  16

SOLUTION 2

010090 LONG PERIOD TIDE HEIGHT             M            3  -32768  16

010091 TIDAL LOADING HEIGHT                M            3  -32768  16

010092 SOLID EARTH TIDE HEIGHT             M            3  -32768  16

010093 GEOCENTRIC POLE TIDE HEIGHT         M            3  -32768  16

011080 U COMPONENT OF THE MODEL WIND       M/S          1   -4096  13

VECTOR

011081 V COMPONENT OF THE MODEL WIND       M/S          1   -4096  13

VECTOR

012188 INTERPOLATED 23.8 GHZ BRIGHTNESS T  K            2       0  16

FROM MWR

012189 INTERPOLATED 36.5 GHZ BRIGHTNESS T  K            2       0  16

FROM MWR

013096 MWR WATER VAPOUR CONTENT           KG/M**2      2        0  14

013097 MWR LIQUID WATER CONTENT           KG/M**2      2        0  14

014050 SOLAR ACTIVITY INDEX               NUMERIC      0   -32768  14

021137 KU BAND CORRECTED OCEAN            DB           2   -32768  16

BACKSCATTER COEFFICIENT

021138 STD KU BAND CORRECTED OCEAN        DB           2   -32768  16

BACKSCATTER COEFFICIENT

021139 KU BAND NET INSTRUMENTAL           DB           2    -2048  12

CORRECTION FOR ACG

021140 S  BAND CORRECTED OCEAN            DB           2   -32768  16

BACKSCATTER COEFFICIENT

021141 STD S  BAND CORRECTED OCEAN        DB           2   -32768  16

BACKSCATTER COEFFICIENT

021142 S  BAND NET INSTRUMENTAL           DB           2    -1024  11

CORRECTION FOR ACG

021143 KU BAND RAIN ATTENUATION           DB        2 -1073741824  31

021144 ALTIMETER RAIN FLAG                FLAG TABLE   0        0   2

022150 NUMBER OF 18 HZ VALID POINTS       NUMERIC      0        0  10

FOR KU BAND

022151 KU BAND OCEAN RANGE                M            3        0  31

022152 STD OF 18 HZ KU BAND OCEAN RANGE   M            3        0  16

022153 NUMBER OF 18 HZ VALID POINTS FOR   NUMERIC      0        0  10

S  BAND

022154 S BAND OCEAN RANGE                 M            3        0  31

022155 STD OF 18 HZ S BAND OCEAN RANGE    M            3        0  16

022156 KU BAND SIGNIFICANT WAVE HEIGHT    M            3        0  16

022157 STD 18 HZ KU BAND SIGNIFICANT      M            3        0  16

WAVE HEIGHT

022158 S  BAND SIGNIFICANT WAVE HEIGHT    M            3        0  16

022159 STD 18 HZ S  BAND SIGNIFICANT WAVE M            3        0  16

HEIGHT

025120 RA2_L2_PROCESSING FLAG             CODE TABLE   0        0   2

025121 RA2_L2_PROCESSING QUALITY          %            0        0   7

025122 HARDWARE CONFIGURATION FOR RF      CODE TABLE   0        0   2

025123 HARDWARE CONFIGURATION FOR HPA     CODE TABLE   0        0   2

025124 MWR L2 PROCESSING FLAG             CODE TABLE   0        0   2

025125 MWR L2 PROCESSING QUALITY          %            0        0   7

025126 MODEL DRY TROPOSPHERIC CORRECTION  M            3   -32768  16

025127 INVERTED BAROMETER CORRECTION      M            3   -32768  16

025128 MODEL WET TROPOSPHERIC CORRECTION  M            3   -32768  16

025129 MWR DERIVED WET TROPOSPHERIC       M            3   -32768  16

CORRECTION

025130 RA2 IONOSPHERIC CORRECTION ON KU   M            3   -32768  16

BAND

025131 IONOSPHERIC CORRECTION FROM DORIS  M            3   -32768  16

ON KU BAND

025132 IONOSPHERIC CORRECTION FROM MODEL  M            3   -32768  16

ON KU BAND

025133 SEA STATE BIAS CORRECTION ON       M            3   -32768  16

KU BAND

025134 RA2 IONOSPHERIC CORRECTION ON S    M            3   -32768  16

BAND

025135 IONOSPHERIC CORRECTION FROM DORIS  M            3   -32768  16

ON S BAND

025136 IONOSPHERIC CORRECTION FROM MODEL  M            3   -32768  16

ON S BAND

025137 SEA STATE BIAS CORRECTION ON S     M            3   -32768  16

BAND

033052 S  BAND OCEAN RETRACKING QUALITY   FLAG TABLE   0        0  21

033053 KU BAND OCEAN RETRACKING          FLAG TABLE    0        0  21

QUALITY

033047 MEASUREMENT CONFIDENCE DATA FLAG TABLE          0        0  31

Code table 2180     INSTRUMENT OPERATIONS

Code figure        Meaning

0              IF CAL

1              BITE DGT

2              BITE RF

3              PSET TRK

4              PSET LOOP OUT

5              ACQUISITION

6              TRACKING

7              MISSING VALUE

Flag table 002158   INSTRUMENT FLAG

bit number         Meaning

1              MISMATCH IN RED VEC HPA

2              MISMATCH IN RED VEC RFSS

3              PTR CALIBRATION BAND 320 MHz (Ku)

4              PTR CALIBRATION BAND 80 MHz (Ku)

5              PTR CALIBRATION BAND 20 MHz (Ku)

6              PTR CALIBRATION BAND 160 MHz (S)

7              Ku FLIGHT CALIBRATION PARAMETERS AVAILABLE

8              S FLIGHT CALIBRATION PARAMETERS AVAILABLE

All            Missing value

Flag table 2187   2239 MWR INSTRUMENT FLAG

bit number         Meaning

1               Temperature inconsistency

2               Data is missing

3               Redundancy channel

4               Power bus protection

5               Overvoltage/Overload protection

6               Reserved

7               Reserved

ALL              Missing

Flag table 021144   Altimeter rain flag

bit number       Meaning

1             RAIN

all           Missing value

Code table 25120    RA2_l2_processing flag

code figure       Meaning

0             Percentage of DSRs free of processing errors 				  during Level 2 processing is greater than the 			  acceptable threshold

1             Percentage of DSRs free of processing errors 				  during Level 2 processing is less than the 				  acceptable threshold

2             Reserved

3             Missing value

Code table 25122    Hardware configuration for RF

Code figure      Meaning

0              Hardware configuration for RF is A

1              Hardware configuration for RF is B

2              Reserved

3              Missing

Code table 25123    Hardware configuration for HPA

Code figure      Meaning

0              Hardware configuration for HPA is A

1              Hardware configuration for HPA is B

2              Reserved

3              Missing

Code table 25124   MWR l2 processing flag

Code figure      Meaning

0              Percentage of DSRs free of processing errors 				  during

Level 2 processing is greater than the acceptable 			  threshold

1              Percentage of DSRs free of processing errors 				  during

Level 2 processing is less than the acceptable 			  threshold

2              Reserved

3              Missing

Flag table 33053    Ku band ocean retracking quality

bit number        Meaning

1-20           First 20 least significant bits correspond to the 			  20 values

(one per data block containing 0=valid 					  measurement, 1=invalid)

bit 1 applies to the 20th data block

All             Missing

Flag table 33052    S band ocean retracking quality

bit number        Meaning

1-20           First 20 least significant bits correspond to 			  the 20 values

(one per data block containing 0=valid 					  measurement, 1=invalid)

bit 1 applies to the 20th data block

All             Missing

Flag table 33047    Measurement confidence data

bit number        Meaning

1              Packet length error. Error detected and attempt to recover made

2              OBDH validity. Anomaly in OBDH value detected

3              USO validity. Anomaly in USOP value detected

4              Fault identifier. Errors detected by on-board

5              AGC fault identifier. AGC out of range

6              Rx delay fault. Rx distance out of range

7              Wave form samples fault identifier. Error

8              Reserved

9              Reserved

10              Reserved

11              Reserved

12              Brightness temperature range check (channel 1) 			  out of range

13              Brightness temperature range check (channel 2) 			  out of range

14              Reserved

15              Ku Ocean retracking error

16              S Ocean retracking error

17              Ku Ice 1 retracking error

18              S Ice 1 retracking error

19              Ku Ice 2 retracking error

20              S Ice 2 retracking error

21              Ku Sea Ice retracking error

22              Arithmetic fault error

23              Meteo data state. No map

24              Meteo data state. 1 map

25              Meteo data state 2 maps degraded

26              Meteo data state 2 maps nominal

27              Orbit propagator status for propagation mode, 			  several errors

28              Orbit propagator status for propagation mode, 			  warning detected

29              Orbit propagator status for initialisation mode, 			  several errors

30              Orbit propagator status for initialisation mode, 			  warning detected

All             Missing