| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES ARUSHA, TANZANIA, 17-21 FEBRUARY 2003 |  | ET/DR&C/Doc. 3.2(1) _______ (8.I.2003) ENGLISH ONLY |
| --- | --- | --- |

Updated proposal(s) for encoding SIGMETs in BUFR

(Submitted by J. Ator (USA))

__________________________________________________________________

Summary and Purpose of Document

This document summarizes an ongoing effort to develop a standard for the exchange of SIGMET messages in BUFR.

ACTION PROPOSED

The meeting is requested to consider the proposal, including the questions raised therein, and to document the conclusions under “ALLOCATED ENTRIES (AWAITING VALIDATION)”.  A request is also made for assistance in performing the required validation.

DISCUSSION

1.	At the previous session of the ET/DR+C in Prague (22-26 April 2002), a joint proposal was presented by the representatives from Australia and ICAO for the encoding of volcanic ash SIGMET messages in BUFR.  Using this proposal as a baseline, personnel from the U.S. National Weather Service’s Aviation Weather Center, in conjunction with myself and with the concurrence of the original authors, proceeded to expand the proposal to include a methodology for the encoding of all types of SIGMET messages, including those for tropical cyclones, turbulence, icing, etc.  We now feel that the overall proposal is in a state where it is ready to be validated, and we would like to ask the assistance of members of the ET/DR+C, in particular the UK Met Office as one of our fellow WAFS centers, to assist our Aviation Weather Center personnel in this task through the generation and exchange of various test messages encoded according to the specifications of this proposal.

2.	It should be noted that various members of the ET/DR+C had kindly offered their comments and suggestions via email as this proposal was being developed over the previous year, and so the below proposal has already been subject to some preliminary review at the ET/DR+C level.  However, one major issue still remains to be decided, and that is the issue of whether to allow for the ability to define volumes of any shape as a SIGMET target region, versus only being able to define volume regions which, when viewed from above, have sides that are always perpendicular to the ground between two 0-07-010 flight levels (i.e. base and top).  In other words, it might be useful to be able to use the code figure “3” within 0-08-007 and thereby define a random sequence of points describing any 3-D region!  The current ICAO Annex 3 regulations do not allow for such odd-shaped objects; however, my Aviation Weather Center colleagues have assured me of their intention to soon make such a proposal to ICAO, so it might indeed be useful to allow for this possibility now rather than to create some new descriptors and sequences that may soon become obsolete.

3.	To that end, we have listed two complete proposals below.  The first one contains just the methodology necessary to define SIGMET messages as they are currently allowed within ICAO Annex 3.  On the other hand, the second one contains the enhanced methodology needed to define volumes of any shape as a SIGMET target region, and this is our preferred choice.  Note that the only real differences between the two versions are that, in the second proposal, code figure “3” is listed as a value option for descriptor 0-08-007, and the location sequence 3-01-023 is replaced by a new location sequence 3-01-027 which contains the flight level descriptor 0-07-010 and so therefore is suitable for listing a sequence of points intended to describe any 3-D region. Otherwise, the proposals are identical!

4.	Again, our preference (i.e. myself and my Aviation Weather Center colleagues) would be to favor the enhanced approach which would allow for the specification of volumes of any shape as a SIGMET target region, as this would provide a maximum of flexibility and future extensibility to the proposal.  However, the capability to do this is currently hampered by the lack of any regulations within WMO Manual 306 which describe how to order the points when using 0-08-007 with code figure “3” to define a volume!  More specifically, the notes under code table 0-08-007 currently give a thorough and unambiguous description of how, when using code figure “2”, an area is defined based upon the order of the points in a BUFR message; however, there is no such description for volume when using code figure “3”!  So we would like to ask the help of one or more members of the ET/DR+C in explaining how this is to be done.  Alternatively, if it turns out that there is no known existing practice, we would then instead ask for assistance in developing such regulations from scratch and to add them under the notes for code table 0-08-007.

# FOR CODING SIGMET WITHOUT VOLUME ADDITIONS (I.E. INITIAL PROPOSAL)

# Proposed Table B entries

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |
| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| 0 01 037 | SIGMET sequence identifier | CCITT IA5 | 0 | 0 | 24 | Character | 0 | 3 |
| 0 01 065 | ICAO region identifier | CCITT IA5 | 0 | 0 | 256 | Character | 0 | 32 |
| 0 08 019 | Qualifier for following centre identifier | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 08 079 | Change in status of following product | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 10 064 | SIGMET cruising level | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 20 028 | Expected change in intensity | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 27 035 | Length of phenomenon | m | -3 | 0 | 13 | m | -3 | 4 |
| 0 28 035 | Width of phenomenon | m | -3 | 0 | 13 | m | -3 | 4 |

# Add the following new categories to Table A within BUFR and CREX:

13	Forecasts

14	Warnings

# Add the following new code table values for the descriptors to Table B within BUFR:

0 08 011

21		Thunderstorm

22		Tropical Cyclone

23		Mountain Wave

24		Duststorm

25		Sandstorm

0 20 008

15		Obscured (OBSC)

16		Embedded (EMBD)

0 20 024

5		Severe

# Code tables for proposed new Table B descriptors:

| Code figure | 0 08 019 Qualifier for following centre identifier |
| --- | --- |
| 0 | Reserved |
| 1 | ATS (Air Traffic Service) unit serving FIR (Flight Information Region) |
| 2 | FIR (Flight Information Region) |
| 3 | UIR (Upper Information Region) |
| 4 | CTA (Control Area) |
| 5 | VAAC (Volcanic Ash Advisory Centre) |
| 6 | MWO (Meteorological Watch Office) issuing SIGMET |
| 7-14 | Reserved |
| 15 | Missing value |

| Code figure | 0 08 079 Change in status of following product |
| --- | --- |
| 0 | Cancelled |
| 1-6 | Reserved |
| 7 | Missing value |

| Code figure | 0 10 064 SIGMET cruising level |
| --- | --- |
| 0 | Subsonic |
| 1 | Transonic |
| 2 | Supersonic |
| 3-6 | Reserved |
| 7 | Missing value |

| Code figure | 0 20 028 Expected change in intensity |
| --- | --- |
| 0 | No change (NC) |
| 1 | Forecast to weaken (WKN) |
| 2 | Forecast to intensify (INTSF) |
| 3-6 | Reserved |
| 7 | Missing value |

# New Table D descriptors:

|  |  | (SIGMET header) |
| --- | --- | --- |
| 3 16 030 | 1 02 002 | Replication of 2 descriptors two times (Define validity period) |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 01 037 | SIGMET sequence identifier |
|  | 0 10 064 | SIGMET cruising level |
|  | 0 08 019 | Qualifier for location identifier, 1=ATS unit serving FIR |
|  | 0 01 062 | Short ICAO location identifier |
|  | 1 02 000 | Replicate two descriptors |
|  | 0 31 001 | Replication count |
|  | 0 08 019 | Qualifier for location identifier, 2=FIR, 3=UIR, 4=CTA |
|  | 0 01 065 | ICAO region identifier |
|  | 0 08 019 | Qualifier for location identifier, 6=MWO |
|  | 0 01 062 | Short ICAO location identifier |
|  | 0 08 019 | Qualifier for location identifier, Missing=Cancel |
|  |  | (SIGMET, Obs or Fcst location and motion) |
| 3 16 031 | 0 08 021 | Time Significance, 16=Analysis, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 07 010 | Flight level (base) |
|  | 0 07 010 | Flight level (top) |
|  | 0 27 035 | Length of phenomenon |
|  | 0 28 035 | Width of phenomenon |
|  | 0 08 007 | Dimensional significance, 1=point, 2=area |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 023 | Latitude, longitude |
|  | 0 19 005 | Direction of motion |
|  | 0 19 006 | Speed of motion |
|  | 0 19 007 | Radius of feature |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 20 028 | Expected change in intensity |
|  | 0 08 021 | Time significance, Missing=cancel |
|  |  | (SIGMET, Fcst position) |
| 3 16 032 | 0 08 021 | Time Significance, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 08 007 | Dimensional significance, 1=point, 2=area |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 023 | Latitude, longitude |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 08 021 | Time significance, Missing=cancel |

|  |  | (SIGMET, Outlook) |
| --- | --- | --- |
| 3 16 033 | 0 08 021 | Time Significance, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 1 07 000 | Replicate 7 descriptors |
|  | 0 31 001 | Replication count |
|  | 0 07 010 | Flight level (base) |
|  | 0 07 010 | Flight level (top) |
|  | 0 08 007 | Dimensional significance, 1=point, 2=area |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 023 | Latitude, longitude |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 08 021 | Time significance, Missing=cancel |
|  |  | (Volcanic Ash SIGMET) |
| 3 16 034 | 3 16 030 | SIGMET Header |
|  | 0 08 011 | Meteorological feature, 17=Volcano |
|  | 0 01 022 | Name of feature |
|  | 0 08 007 | Dimensional significance, 0=Point |
|  | 3 01 023 | Location |
|  | 0 08 007 | Dimensional significance, Missing=Cancel |
|  | 0 20 090 | Special Clouds, 5=Clouds from volcanic eruptions |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 1 01 000 | Delayed replication |
|  | 0 31 000 | Short replication factor |
|  | 3 16 032 | SIGMET Fcst position |
|  | 1 01 000 | Delayed replication |
|  | 0 31 001 | Delayed replication factor |
|  | 3 16 033 | SIGMET Outlook |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Thunderstorm SIGMET) |
| 3 16 035 | 3 16 030 | SIGMET Header |
|  | 0 08 011 | Meteorological feature, 21=Thunderstorm |
|  | 0 20 023 | Other weather phenomenon, bit 2=Squalls or all 18 bits = Missing |
|  | 0 20 021 | Type of precipitation, bit 14=Hail or all 30 bits=Missing |
|  | 0 20 008 | Cloud distribution 15=OBSC, 16=EMBD, 12=FRQ, 31=Missing |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |

|  |  | (Tropical Cyclone SIGMET) |
| --- | --- | --- |
| 3 16 036 | 3 16 030 | SIGMET Header |
|  | 0 08 011 | Meteorological feature, 22=Tropical Cyclone |
|  | 0 01 027 | WMO storm name |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 1 01 000 | Delayed replication |
|  | 0 31 000 | Short replication factor |
|  | 3 16 032 | SIGMET Fcst position |
|  | 1 01 000 | Delayed replication |
|  | 0 31 001 | Delayed replication factor |
|  | 3 16 033 | SIGMET Outlook |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Turbulence SIGMET) |
| 3 16 037 | 3 16 030 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 13=Turbulence |
|  | 0 11 031 | Degree of turbulence, 10=Mod, 11=Severe |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Icing SIGMET) |
| 3 16 038 | 3 16 030 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 15=Airframe Icing |
|  | 0 20 041 | Airframe icing, 7=Severe |
|  | 0 20 021 | Type of precip, bit 3=Liquid freezing precip or all 30 bits = Missing |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Mountain Wave SIGMET) |
| 3 16 039 | 3 16 030 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 23=Mountain Wave |
|  | 0 20 024 | Intensity of phenomena, 5=Severe |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Duststorm SIGMET) |
| 3 16 040 | 3 16 030 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 24=Duststorm |
|  | 0 20 024 | Intensity of phenomena, 3=Heavy |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Sandstorm SIGMET) |
| 3 16 041 | 3 16 030 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 25=Sandstorm |
|  | 0 20 024 | Intensity of phenomena, 3=Heavy |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |

|  |  | (SIGMET cancellation) |
| --- | --- | --- |
| 3 16 042 | 3 16 030 | SIGMET header |
|  | 0 08 079 | Change in status of following product, 0 = Cancelled |
|  | 1 02 002 | Replication of 2 descriptors two times (Define validity period) |
|  | 3 01 011 | Year, Month, Day of SIGMET to cancel |
|  | 3 01 012 | Hour, Minute of SIGMET to cancel |
|  | 0 01 037 | SIGMET sequence identifier of SIGMET to cancel |
|  | 0 10 064 | SIGMET cruising level of SIGMET to cancel |
|  | 0 08 079 | Change in status of following product, Missing = Cancel |

FOR CODING SIGMET WITH VOLUME ADDITIONS (I.E. ENHANCED PROPOSAL)

Proposed Table B entries

| Table Reference | Element name | BUFR | CREX |
| --- | --- | --- | --- |

| F X Y |  | Unit | Scale | Ref. value | Data width | Unit | Scale | Data width |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 01 037 | SIGMET sequence identifier | CCITT IA5 | 0 | 0 | 24 | Character | 0 | 3 |
| 0 01 065 | ICAO region identifier | CCITT IA5 | 0 | 0 | 256 | Character | 0 | 32 |
| 0 08 019 | Qualifier for following centre identifier | Code table | 0 | 0 | 4 | Code table | 0 | 1 |
| 0 08 079 | Change in status of following product | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 10 064 | SIGMET cruising level | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 20 028 | Expected change in intensity | Code table | 0 | 0 | 3 | Code table | 0 | 1 |
| 0 27 035 | Length of phenomenon | m | -3 | 0 | 13 | m | -3 | 4 |
| 0 28 035 | Width of phenomenon | m | -3 | 0 | 13 | m | -3 | 4 |

Add the following new categories to Table A within BUFR and CREX:

13	Forecasts

14	Warnings

Add the following new code table values for the descriptors to Table B within BUFR:

0 08 011

21		Thunderstorm

22		Tropical Cyclone

23		Mountain Wave

24		Duststorm

25		Sandstorm

0 20 008

15		Obscured (OBSC)

16		Embedded (EMBD)

0 20 024

5		Severe

Code tables for proposed new Table B descriptors:

| Code figure | 0 08 019 Qualifier for following centre identifier |
| --- | --- |
| 0 | Reserved |
| 1 | ATS (Air Traffic Service) unit serving FIR (Flight Information Region) |
| 2 | FIR (Flight Information Region) |
| 3 | UIR (Upper Information Region) |
| 4 | CTA (Control Area) |
| 5 | VAAC (Volcanic Ash Advisory Centre) |
| 6 | MWO (Meteorological Watch Office) issuing SIGMET |
| 7-14 | Reserved |
| 15 | Missing value |

| Code figure | 0 08 079 Change in status of following product |
| --- | --- |
| 0 | Cancelled |
| 1-6 | Reserved |
| 7 | Missing value |

| Code figure | 0 10 064 SIGMET cruising level |
| --- | --- |
| 0 | Subsonic |
| 1 | Transonic |
| 2 | Supersonic |
| 3-6 | Reserved |
| 7 | Missing value |

| Code figure | 0 20 028 Expected change in intensity |
| --- | --- |
| 0 | No change (NC) |
| 1 | Forecast to weaken (WKN) |
| 2 | Forecast to intensify (INTSF) |
| 3-6 | Reserved |
| 7 | Missing value |

New Table D descriptors:

| 3 01 027 | 0 05 002 | Latitude (coarse accuracy) |
| --- | --- | --- |
|  | 0 06 002 | Longitude (coarse accuracy) |
|  | 0 07 010 | Flight Level |
|  |  | (SIGMET header) |
| 3 16 030 | 1 02 002 | Replication of 2 descriptors two times (Define validity period) |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 01 037 | SIGMET sequence identifier |
|  | 0 10 064 | SIGMET cruising level |
|  | 0 08 019 | Qualifier for location identifier, 1=ATS unit serving FIR |
|  | 0 01 062 | Short ICAO location identifier |
|  | 1 02 000 | Replicate two descriptors |
|  | 0 31 001 | Replication count |
|  | 0 08 019 | Qualifier for location identifier, 2=FIR, 3=UIR, 4=CTA |
|  | 0 01 065 | ICAO region identifier |
|  | 0 08 019 | Qualifier for location identifier, 6=MWO |
|  | 0 01 062 | Short ICAO location identifier |
|  | 0 08 019 | Qualifier for location identifier, Missing=Cancel |
|  |  | (SIGMET, Obs or Fcst location and motion) |
| 3 16 031 | 0 08 021 | Time Significance, 16=Analysis, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 07 010 | Flight level (base) |
|  | 0 07 010 | Flight level (top) |
|  | 0 27 035 | Length of phenomenon |
|  | 0 28 035 | Width of phenomenon |
|  | 0 08 007 | Dimensional significance, 1=point, 2=area, 3=volume |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 027 | Latitude, longitude, flight level |
|  | 0 19 005 | Direction of motion |
|  | 0 19 006 | Speed of motion |
|  | 0 19 007 | Radius of feature |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 20 028 | Expected change in intensity |
|  | 0 08 021 | Time significance, Missing=cancel |
|  |  | (SIGMET, Fcst position) |
| 3 16 032 | 0 08 021 | Time Significance, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 0 08 007 | Dimensional significance, 1=point, 2=area |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 023 | Latitude, longitude |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 08 021 | Time significance, Missing=cancel |

|  |  | (SIGMET, Outlook) |
| --- | --- | --- |
| 3 16 033 | 0 08 021 | Time Significance, 4=Forecast |
|  | 3 01 011 | Year, Month, Day |
|  | 3 01 012 | Hour, Minute |
|  | 1 07 000 | Replicate 7 descriptors |
|  | 0 31 001 | Replication count |
|  | 0 07 010 | Flight level (base) |
|  | 0 07 010 | Flight level (top) |
|  | 0 08 007 | Dimensional significance, 1=point, 2=area, 3=volume |
|  | 1 01 000 | Replicate one descriptor |
|  | 0 31 001 | Replication count |
|  | 3 01 027 | Latitude, longitude, flight level |
|  | 0 08 007 | Dimensional significance, Missing=cancel |
|  | 0 08 021 | Time significance, Missing=cancel |
|  |  | (Volcanic Ash SIGMET) |
| 3 16 034 | 3 16 030 | SIGMET Header |
|  | 0 08 011 | Meteorological feature, 17=Volcano |
|  | 0 01 022 | Name of feature |
|  | 0 08 007 | Dimensional significance, 0=Point |
|  | 3 01 023 | Location |
|  | 0 08 007 | Dimensional significance, Missing=Cancel |
|  | 0 20 090 | Special Clouds, 5=Clouds from volcanic eruptions |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 1 01 000 | Delayed replication |
|  | 0 31 000 | Short replication factor |
|  | 3 16 032 | SIGMET Fcst position |
|  | 1 01 000 | Delayed replication |
|  | 0 31 001 | Delayed replication factor |
|  | 3 16 033 | SIGMET Outlook |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Thunderstorm SIGMET) |
| 3 16 035 | 3 16 030 | SIGMET Header |
|  | 0 08 011 | Meteorological feature, 21=Thunderstorm |
|  | 0 20 023 | Other weather phenomenon, bit 2=Squalls or all 18 bits = Missing |
|  | 0 20 021 | Type of precipitation, bit 14=Hail or all 30 bits=Missing |
|  | 0 20 008 | Cloud distribution 15=OBSC, 16=EMBD, 12=FRQ, 31=Missing |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |

|  |  | (Tropical Cyclone SIGMET) |
| --- | --- | --- |
| 3 16 036 | 3 16 030 | SIGMET Header |
|  | 0 08 011 | Meteorological feature, 22=Tropical Cyclone |
|  | 0 01 027 | WMO storm name |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 1 01 000 | Delayed replication |
|  | 0 31 000 | Short replication factor |
|  | 3 16 032 | SIGMET Fcst position |
|  | 1 01 000 | Delayed replication |
|  | 0 31 001 | Delayed replication factor |
|  | 3 16 033 | SIGMET Outlook |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Turbulence SIGMET) |
| 3 16 037 | 3 16 030 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 13=Turbulence |
|  | 0 11 031 | Degree of turbulence, 10=Mod, 11=Severe |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Icing SIGMET) |
| 3 16 038 | 3 16 030 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 15=Airframe Icing |
|  | 0 20 041 | Airframe icing, 7=Severe |
|  | 0 20 021 | Type of precip, bit 3=Liquid freezing precip or all 30 bits = Missing |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Mountain Wave SIGMET) |
| 3 16 039 | 3 16 030 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 23=Mountain Wave |
|  | 0 20 024 | Intensity of phenomena, 5=Severe |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Duststorm SIGMET) |
| 3 16 040 | 3 16 030 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 24=Duststorm |
|  | 0 20 024 | Intensity of phenomena, 3=Heavy |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |
|  |  | (Sandstorm SIGMET) |
| 3 16 041 | 3 16 030 | SIGMET header |
|  | 0 08 011 | Meteorological feature, 25=Sandstorm |
|  | 0 20 024 | Intensity of phenomena, 3=Heavy |
|  | 3 16 031 | SIGMET Obs or Fcst location and motion |
|  | 0 08 011 | Meteorological feature, Missing=Cancel |

|  |  | (SIGMET cancellation) |
| --- | --- | --- |
| 3 16 042 | 3 16 030 | SIGMET header |
|  | 0 08 079 | Change in status of following product, 0 = Cancelled |
|  | 1 02 002 | Replication of 2 descriptors two times (Define validity period) |
|  | 3 01 011 | Year, Month, Day of SIGMET to cancel |
|  | 3 01 012 | Hour, Minute of SIGMET to cancel |
|  | 0 01 037 | SIGMET sequence identifier of SIGMET to cancel |
|  | 0 10 064 | SIGMET cruising level of SIGMET to cancel |
|  | 0 08 079 | Change in status of following product, Missing = Cancel |