| WORLD METEOROLOGICAL ORGANIZATION ___________________ COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES Third session Arusha, Tanzania, 17-21 February 2003 |  | Distribution: RESTRICTED ET/DR&C/Doc. 3.4(4) (28.I.2003) _________ Item: 3.4 ENGLISH only |
| --- | --- | --- |

OTHER ADDITIONS TO BUFR/CREX

BUFR Templates for PILOT and TEMP data

with identification of radiosonde drift

Submitted by Eva Červená (Czech Republic)

___________________________________________________________________

Summary and Purpose of Document

This document contains BUFR templates for PILOT, PILOT SHIP,  PILOT MOBIL, TEMP,TEMP DROP, TEMP SHIP, TEMP MOBIL data with description of radiosonde position during the ascent.

___________________________________________________________________

Action Proposed

The meeting is invited to examine the submitted templates with the view of their usage for experimental exchange of data in BUFR.

References:

[1]  Manual on Codes, WMO - No 306, Volumes I.1 and I.2.

[2]  Report of ET on Migration to TDCF, Washington, D.C., USA, 13-17 May 2002.

[3]  Benko, M: Radiosonde Drift, Meteorological Journal, Bratislava, 1999, 2, 11-19.

Discussion

1. Background

The last decade has witnessed fast development of high resolution numerical models. Availability of input data which would more precisely describe the actual state of the atmosphere, might improve the quality of numerical weather products. Traditional code forms PILOT, PILOT SHIP, PILOT MOBIL, TEMP, TEMP DROP, TEMP SHIP, TEMP MOBIL  provide information on  vertical profiles of the relevant elements as if the data were measured directly above the launch point, not taking into account the fact that the radiosonde is drifted away from the location of launch during the ascent. Radiosonde drift (distance of the sonde from the launch point) might be quite significant comparing to the recommended horizontal resolution of the models (less than 10 km). Even the average values of the radiosonde drift are bigger than 10 km at levels above 400 hPa (over Central Europe) and the values of the drift might get beyond 10 km as low as at the 700 hPa level. At the end of the ascent, the sonde might get 250 km from the launch point [3].

The table driven code forms BUFR and CREX offer an opportunity to include information on the radiosonde position during the ascent. The existing templates for TEMP and PILOT codes are proposed to be supplemented by latitude and longitude of the radiosonde (3 01 023) at each level. These data are usually available (GPS, Loran C) or might be obtained from azimuth and  elevation angle (radiotheodolite).

In case of the template for TEMP codes, also time increment (since the launch time) 0 04 015 is proposed to be added to the level data. The ascent rate of the radiosonde is not constant and specification of the actual time of measurement at individual levels might be found useful in data processing. If the same were required also in the PILOT templates, time identification of the launch would have to be added.

Besides the modifications mentioned above, one additional change is proposed in the templates for TEMP codes – the identification of launch time has been moved down the template to describe more properly that sea water temperature and cloud data are measured/observed at the nominal time of observation rather than at the time of the radiosonde launch.

2. BUFR templates for vertical sounding data with description of radiosonde position

during the ascent

2.1 BUFR templates for PILOT, PILOT SHIP,  PILOT MOBIL

a)  with pressure as the vertical coordinate

|  |  | Identification and instrumentation |  |
| --- | --- | --- | --- |
| 3 01 001 | 0 01 001 | WMO block number | Numeric |
|  | 0 01 002 | WMO station number | Numeric |
| 0 01 011 |  | Ship or mobile land station identifier | CCITT IA5 |
| 0 02 011 |  | Radiosonde type | Code table |
| 0 02 014 |  | Tracking technique/status of system used | Code table |
| 0 02 003 |  | Type of measuring equipment used | Code table |
|  |  | Date/time, horizontal and vertical coordinates |  |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day | Day |
| 3 01 012 | 0 04 004 | Hour | Hour |
|  | 0 04 005 | Minute | Minute |
| 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, scale 5 |
|  | 0 06 001 | Longitude (high accuracy) | Degree, scale 5 |
| 0 07 030 |  | Height of station ground above mean sea level | m, scale 1 |
| 0 07 031 |  | Height of barometer above mean sea level | m, scale 1 |
| 0 07 007 |  | Height of release of sonde above mean sea level | m |
| 0 33 024 |  | Station elevation quality mark (for mobile stations) | Code table |
|  |  | Level data |  |
| 1 05 000 |  | Delayed replication of 5 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
|  |  | Data from a single level |  |
| 0 08 001 |  | Vertical sounding significance | Flag table |
| 0 07 004 |  | Pressure | Pa, scale –1 |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) | Degree, scale 2 |
|  | 0 06 002 | Longitude (coarse accuracy) | Degree, scale 2 |
| 0 11 001 |  | Wind direction | Degree true |
| 0 11 002 |  | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data |  |
| 0 08 001 |  | Vertical sounding significance | Flag table |
| 0 07 004 |  | Pressure | Pa, scale –1 |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) | Degree, scale 2 |
|  | 0 06 002 | Longitude (coarse accuracy) | Degree, scale 2 |
| 0 11 061 |  | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
| 0 11 062 |  | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

Notes:	(1) If horizontal coordinates of the sonde are not available, latitude and longitude (coarse accuracy) of the location of launch shall be reported for 3 01 023.

b)  with height as the vertical coordinate

|  |  | Identification and instrumentation |  |
| --- | --- | --- | --- |
| 3 01 001 | 0 01 001 | WMO block number | Numeric |
|  | 0 01 002 | WMO station number | Numeric |
| 0 01 011 |  | Ship or mobile land station identifier | CCITT IA5 |
| 0 02 011 |  | Radiosonde type | Code table |
| 0 02 014 |  | Tracking technique/status of system used | Code table |
| 0 02 003 |  | Type of measuring equipment used | Code table |
|  |  | Date/time, horizontal and vertical coordinates |  |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day | Day |
| 3 01 012 | 0 04 004 | Hour | Hour |
|  | 0 04 005 | Minute | Minute |
| 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, scale 5 |
|  | 0 06 001 | Longitude (high accuracy) | Degree, scale 5 |
| 0 07 030 |  | Height of station ground above mean sea level | m, scale 1 |
| 0 07 007 |  | Height of release of sonde above mean sea level | m |
| 0 33 024 |  | Station elevation quality mark (for mobile stations) | Code table |
|  |  | Level data |  |
| 1 05 000 |  | Delayed replication of 5 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
|  |  | Data from a single level |  |
| 0 08 001 |  | Vertical sounding significance | Flag table |
| 0 07 009 |  | Geopotential height | gpm |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) | Degree, scale 2 |
|  | 0 06 002 | Longitude (coarse accuracy) | Degree, scale 2 |
| 0 11 001 |  | Wind direction | Degree true |
| 0 11 002 |  | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data |  |
| 0 08 001 |  | Vertical sounding significance | Flag table |
| 0 07 009 |  | Geopotential height | gpm |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) | Degree, scale 2 |
|  | 0 06 002 | Longitude (coarse accuracy) | Degree, scale 2 |
| 0 11 061 |  | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
| 0 11 062 |  | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

Notes:	(1) If horizontal coordinates of the sonde are not available, latitude and longitude (coarse accuracy) of the location of launch shall be reported for 3 01 023.

BUFR templates for TEMP, TEMP DROP, TEMP SHIP, TEMP MOBIL

|  |  | Identification and instrumentation |  |
| --- | --- | --- | --- |
| 3 01 001 | 0 01 001 | WMO block number | Numeric |
|  | 0 01 002 | WMO station number | Numeric |
| 0 01 011 |  | Ship or mobile land station identifier | CCITT IA5 |
| 0 01 006 |  | Aircraft identifier (for dropsondes) | CCITT IA5 |
| 0 02 011 |  | Radiosonde type | Code table |
| 0 02 013 |  | Solar and infrared radiation correction | Code table |
| 0 02 014 |  | Tracking technique/status of system used | Code table |
| 0 02 003 |  | Type of measuring equipment used | Code table |
|  |  | Date/time, date/time of launch, horizontal and vertical coordinates |  |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day | Day |
| 3 01 012 | 0 04 004 | Hour | Hour |
|  | 0 04 005 | Minute | Minute |
| 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, scale 5 |
|  | 0 06 001 | Longitude (high accuracy) | Degree, scale 5 |
| 0 07 030 |  | Height of station ground above mean sea level | m, scale 1 |
| 0 07 031 |  | Height of barometer above mean sea level | m, scale 1 |
| 0 07 007 |  | Height of release of sonde above mean sea level | m |
| 0 33 024 |  | Station elevation quality mark (for mobile stations) | Code table |
|  |  | Sea water temperature |  |
| 0 22 043 |  | Sea/water temperature (for ship stations) | K, scale 2 |
|  |  | Cloud data |  |
| 0 08 002 |  | Vertical significance | Code table |
| 0 20 011 |  | Cloud amount (of low or middle clouds Nh) | Code table |
| 0 20 013 |  | Height of base of cloud (h) | m, scale –1 |
| 0 20 012 |  | Cloud type (low clouds CL) | Code table |
| 0 20 012 |  | Cloud type (middle clouds CM) | Code table |
| 0 20 012 |  | Cloud type (high clouds CH) | Code table |
| 0 08 021 |  | Time significance (value = 18 (radiosonde launch time)) | Code table |
| 3 01 011 | 0 04 001 | Year | Year |
|  | 0 04 002 | Month | Month |
|  | 0 04 003 | Day | Day |
| 3 01 012 | 0 04 004 | Hour | Hour |
|  | 0 04 005 | Minute | Minute |
| 0 08 021 |  | Time significance (set to missing to cancel the previous value) | Code table |
|  |  | Level data |  |
| 1 09 000 |  | Delayed replication of 9 descriptors |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
|  |  | Data from a single level |  |
| 0 04 015 |  | Time increment (since the launch time) | Minute |
| 0 08 001 |  | Vertical sounding significance | Flag table |
| 0 07 004 |  | Pressure | Pa, scale –1 |
| 0 10 009 |  | Geopotential height | gpm |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) | Degree, scale 2 |
|  | 0 06 002 | Longitude (coarse accuracy) | Degree, scale 2 |
| 0 12 101 |  | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
| 0 12 103 |  | Dew-point temperature (scale 2) | K, scale 2 |
| 0 11 001 |  | Wind direction | Degree true |
| 0 11 002 |  | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data |  |
| 0 08 001 |  | Vertical sounding significance | Flag table |
| 0 07 004 |  | Pressure | Pa, scale –1 |
| 3 01 023 | 0 05 002 | Latitude (coarse accuracy) | Degree, scale 2 |
|  | 0 06 002 | Longitude (coarse accuracy) | Degree, scale 2 |
| 0 11 061 |  | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
| 0 11 062 |  | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

Notes:	(1) If horizontal coordinates of the sonde are not available, latitude and longitude (coarse accuracy) of the location of launch shall be reported for 3 01 023.