| WORLD METEOROLOGICAL ORGANIZATION ________________ COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES KUALA LUMPUR, MALAYSIA, 21 - 26 JUNE 2004 |  | ET/DR&C/Doc. 3.2(2) _______ ENGLISH only |
| --- | --- | --- |

## New BUFR/CREX sequences for high-resolution radiosonde data

Submitted by Jeff Ator (USA)

________________________________________________________________

Summary and Purpose of Document

This document describes some new sequence descriptors that were previously “allocated” and which are now ready for “pre-operational” status.

________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the document and approve the contents for “pre-operational” status.

DISCUSSION

During the previous year, U.S./NCEP obtained sample BUFR high-resolution radiosonde messages generated from the U.S./NWS Radiosonde Replacement System (RRS) and made them available to other members of the ET/DR+C.  These messages made use of new Table D sequences that had only been listed as “allocated” at the time.  However, our colleagues at ECMWF and UKMO were able to subsequently decode these sample messages and thereby validate these new Table D sequences, so it is now requested that the following proposal be approved for “pre-operational” status.

PROPOSAL

| TABLE REFERENCE | TABLE REFERENCES | ELEMENT NAME |
| --- | --- | --- |
| F | X | Y |  |  |
|  |  |  |  |  |  | (Radiosonde abbreviated header and launch information) |
| 3 | 01 | 120 | 3 | 01 | 001 | WMO block and station number |
|  |  |  | 0 | 01 | 094 | WBAN number |
|  |  |  | 0 | 02 | 011 | Radiosonde type |
|  |  |  | 3 | 01 | 121 | Radiosonde launch point location |
|  |  |  |  |  |  | (Radiosonde launch point location) |
| 3 | 01 | 121 | 0 | 08 | 041 | Data significance (3 = “balloon launch point”) |
|  |  |  | 3 | 01 | 122 | Date/time (to hundredths of second) |
|  |  |  | 3 | 01 | 021 | Latitude and longitude (high accuracy) |
|  |  |  | 0 | 07 | 031 | Height of barometer above MSL |
|  |  |  | 0 | 07 | 007 | Height (of radiosonde release above MSL) |
|  |  |  |  |  |  | (Date/time (to hundredths of second)) |
| 3 | 01 | 122 | 3 | 01 | 011 | Date |
|  |  |  | 3 | 01 | 012 | Time |
|  |  |  | 2 | 01 | 135 | Change data width |
|  |  |  | 2 | 02 | 130 | Change scale |
|  |  |  | 0 | 04 | 006 | Second |
|  |  |  | 2 | 02 | 000 | Cancel change scale |
|  |  |  | 2 | 01 | 000 | Cancel change data width |

|  |  |  |  |  |  | (Radiosonde full header information) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 01 | 123 | 1 | 02 | 002 | Replicate 2 descriptors 2 times |
|  |  |  | 0 | 08 | 041 | Data significance (0 = “parent site”, 1 = “observation site”) |
|  |  |  | 0 | 01 | 062 | Short ICAO location identifier |
|  |  |  | 3 | 01 | 001 | WMO block and station number |
|  |  |  | 0 | 01 | 094 | WBAN number |
|  |  |  | 0 | 02 | 011 | Radiosonde type |
|  |  |  | 0 | 01 | 018 | Short station or site name |
|  |  |  | 0 | 01 | 095 | Observer identification |
|  |  |  | 0 | 25 | 061 | Software identification |
|  |  |  | 0 | 25 | 068 | Number of archive recomputes |
|  |  |  | 0 | 01 | 082 | Radiosonde ascension number |
|  |  |  | 0 | 01 | 083 | Radiosonde release number |
|  |  |  | 0 | 01 | 081 | Radiosonde serial number |
|  |  |  | 0 | 02 | 067 | Radiosonde operating frequency |
|  |  |  | 0 | 02 | 066 | Radiosonde ground receiving system |
|  |  |  | 0 | 02 | 014 | Tracking technique/status of system used |
|  |  |  | 0 | 25 | 067 | Release point pressure correction |
|  |  |  | 0 | 25 | 065 | Orientation correction (azimuth) |
|  |  |  | 0 | 25 | 066 | Orientation correction (elevation) |
|  |  |  | 0 | 02 | 095 | Type of pressure sensor |
|  |  |  | 0 | 02 | 096 | Type of temperature sensor |
|  |  |  | 0 | 02 | 097 | Type of humidity sensor |
|  |  |  | 0 | 02 | 016 | Radiosonde configuration |
|  |  |  | 0 | 02 | 083 | Type of balloon shelter |
|  |  |  | 0 | 02 | 080 | Balloon manufacturer |
|  |  |  | 0 | 02 | 081 | Type of balloon |
|  |  |  | 0 | 01 | 093 | Balloon lot number |
|  |  |  | 0 | 02 | 084 | Type of gas used in balloon |
|  |  |  | 0 | 02 | 085 | Amount of gas used in balloon |
|  |  |  | 0 | 02 | 086 | Balloon flight train length |
|  |  |  | 0 | 02 | 082 | Weight of balloon |
|  |  |  | 0 | 08 | 041 | Data significance (2 = “balloon manufacture date”) |
|  |  |  | 3 | 01 | 011 | Date |

|  |  |  |  |  |  | (Radiosonde surface observation) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 02 | 050 | 0 | 08 | 041 | Data significance (5 = “sfc ob displacement from launch pt) |
|  |  |  | 0 | 05 | 021 | Bearing or azimuth |
|  |  |  | 0 | 07 | 005 | Height increment |
|  |  |  | 2 | 02 | 130 | Change scale |
|  |  |  | 0 | 06 | 021 | Distance |
|  |  |  | 2 | 02 | 000 | Cancel change scale |
|  |  |  | 0 | 08 | 041 | Data significance (4 = “surface observation”) |
|  |  |  | 2 | 01 | 131 | Change data width |
|  |  |  | 2 | 02 | 129 | Change scale |
|  |  |  | 0 | 02 | 115 | Type of surface observing equipment |
|  |  |  | 0 | 10 | 004 | Pressure |
|  |  |  | 0 | 02 | 115 | Type of surface observing equipment |
|  |  |  | 0 | 13 | 003 | Relative humidity |
|  |  |  | 2 | 02 | 000 | Cancel change scale |
|  |  |  | 2 | 01 | 000 | Cancel change data width |
|  |  |  | 0 | 02 | 115 | Type of surface observing equipment |
|  |  |  | 0 | 11 | 001 | Wind direction |
|  |  |  | 0 | 11 | 002 | Wind speed |
|  |  |  | 0 | 02 | 115 | Type of surface observing equipment |
|  |  |  | 1 | 02 | 002 | Replicate 2 descriptors 2 times |
|  |  |  | 0 | 12 | 101 | Temperature/dry bulb temperature |
|  |  |  | 0 | 04 | 024 | Time displacement (hour) |
|  |  |  | 0 | 02 | 115 | Type of surface observing equipment |
|  |  |  | 0 | 12 | 103 | Dew-point temperature |
|  |  |  | 0 | 12 | 102 | Wet bulb temperature |
|  |  |  | 1 | 01 | 003 | Replicate 1 descriptor 3 times |
|  |  |  | 0 | 20 | 012 | Cloud type |
|  |  |  | 0 | 20 | 011 | Cloud amount |
|  |  |  | 0 | 20 | 013 | Height of base of cloud |
|  |  |  | 1 | 01 | 002 | Replicate 1 descriptor 2 times |
|  |  |  | 0 | 20 | 003 | Present weather |
|  |  |  |  |  |  | (Radiosonde duration of flight and termination information) |
| 3 | 03 | 040 | 0 | 08 | 041 | Data significance (7 = “flight level termination point”) |
|  |  |  | 0 | 04 | 025 | Time displacement (minute) |
|  |  |  | 0 | 04 | 026 | Time displacement (second) |
|  |  |  | 3 | 01 | 021 | Latitude and longitude (high accuracy) |
|  |  |  | 3 | 01 | 122 | Date/time (to hundredths of second) |
|  |  |  | 2 | 01 | 131 | Change data width |
|  |  |  | 2 | 02 | 129 | Change scale |
|  |  |  | 0 | 25 | 069 | Flight level pressure correction |
|  |  |  | 0 | 07 | 004 | Pressure |
|  |  |  | 0 | 13 | 003 | Relative humidity |
|  |  |  | 2 | 02 | 000 | Cancel change scale |
|  |  |  | 2 | 01 | 000 | Cancel change data width |
|  |  |  | 0 | 02 | 013 | Solar and infrared radiation correction |
|  |  |  | 0 | 12 | 101 | Temperature/dry bulb temperature |
|  |  |  | 0 | 10 | 009 | Geopotential height |
|  |  |  | 1 | 02 | 002 | Replicate 2 descriptors 2 times |
|  |  |  | 0 | 08 | 040 | Flight level significance |
|  |  |  | 0 | 35 | 035 | Reason for termination |

|  |  |  |  |  |  | (Radiosonde complete registration and surface observation) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 09 | 060 | 3 | 01 | 123 | Radiosonde full header information |
|  |  |  | 3 | 01 | 121 | Radiosonde launch point location |
|  |  |  | 3 | 02 | 050 | Radiosonde surface observation |
|  |  |  | 3 | 03 | 040 | Radiosonde duration of flight and termination information |
|  |  |  |  |  |  | (Raw PTU) |
| 3 | 09 | 061 | 3 | 01 | 120 | Radiosonde abbreviated header and launch information |
|  |  |  | 0 | 08 | 041 | Data significance (6 = “flight level observation” ) |
|  |  |  | 3 | 01 | 122 | Date/time (to hundredths of second) |
|  |  |  | 2 | 01 | 131 | Change data width |
|  |  |  | 2 | 02 | 129 | Change scale |
|  |  |  | 0 | 25 | 069 | Flight level pressure correction |
|  |  |  | 0 | 07 | 004 | Pressure |
|  |  |  | 2 | 02 | 000 | Cancel change scale |
|  |  |  | 2 | 01 | 000 | Cancel change data width |
|  |  |  | 0 | 33 | 007 | Percent confidence (for Pressure) |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Pressure) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Pressure) |
|  |  |  | 0 | 13 | 009 | Relative humidity |
|  |  |  | 0 | 33 | 007 | Percent confidence (for Relative humidity) |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Relative humidity) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Relative humidity) |
|  |  |  | 0 | 02 | 013 | Solar and infrared radiation correction |
|  |  |  | 0 | 12 | 101 | Temperature/dry bulb temperature |
|  |  |  | 0 | 33 | 007 | Percent confidence (for Temperature) |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Temperature) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Temperature) |
|  |  |  |  |  |  | (Raw GPS unsmoothed wind) |
| 3 | 09 | 062 | 3 | 01 | 120 | Radiosonde abbreviated header and launch information |
|  |  |  | 0 | 08 | 041 | Data significance (6 = “flight level observation” ) |
|  |  |  | 3 | 01 | 122 | Date/time (to hundredths of second) |
|  |  |  | 0 | 05 | 001 | Latitude (high accuracy) |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Latitude) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Latitude) |
|  |  |  | 0 | 06 | 001 | Longitude (high accuracy) |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Longitude) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Longitude) |
|  |  |  | 0 | 07 | 007 | Height |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Height) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Height) |
|  |  |  | 0 | 11 | 003 | U-component |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for U-component) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for U-component) |
|  |  |  | 0 | 11 | 004 | V-component |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for V-component) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for V-component) |
|  |  |  | 0 | 33 | 007 | Percent confidence (for Raw GPS unsmoothed wind) |

|  |  |  |  |  |  | (Raw GPS smoothed wind) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 09 | 063 | 3 | 01 | 120 | Radiosonde abbreviated header and launch information |
|  |  |  | 0 | 08 | 041 | Data significance (6 = “flight level observation” ) |
|  |  |  | 3 | 01 | 122 | Date/time (to hundredths of second) sequence |
|  |  |  | 0 | 05 | 001 | Latitude (high accuracy) |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Latitude) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Latitude) |
|  |  |  | 0 | 06 | 001 | Longitude (high accuracy) |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Longitude) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Longitude) |
|  |  |  | 0 | 07 | 007 | Height |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Height) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Height) |
|  |  |  | 0 | 11 | 003 | U-component |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for U-component) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for U-component) |
|  |  |  | 0 | 11 | 004 | V-component |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for V-component) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for V-component) |
|  |  |  | 0 | 33 | 007 | Percent confidence (for Raw GPS smoothed wind) |
|  |  |  |  |  |  | (Processed PTU) |
| 3 | 09 | 064 | 3 | 01 | 120 | Radiosonde abbreviated header and launch information |
|  |  |  | 0 | 08 | 041 | Data significance (6 = “flight level observation” ) |
|  |  |  | 3 | 01 | 122 | Date/time (to hundredths of second) |
|  |  |  | 2 | 01 | 131 | Change data width |
|  |  |  | 2 | 02 | 129 | Change scale |
|  |  |  | 1 | 04 | 002 | Replicate 4 descriptors 2 times |
|  |  |  | 0 | 25 | 069 | Flight level pressure correction |
|  |  |  | 0 | 07 | 004 | Pressure |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Pressure) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Pressure) |
|  |  |  | 0 | 13 | 003 | Relative humidity |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Relative humidity) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Relative humidity) |
|  |  |  | 2 | 02 | 000 | Cancel change scale |
|  |  |  | 2 | 01 | 000 | Cancel change data width |
|  |  |  | 1 | 04 | 002 | Replicate 4 descriptors 2 times |
|  |  |  | 0 | 02 | 013 | Solar and infrared radiation correction |
|  |  |  | 0 | 12 | 101 | Temperature/dry bulb temperature |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Temperature) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Temperature) |
|  |  |  | 0 | 12 | 103 | Dew-point temperature |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Dew-point temperature) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Dew-point temperature) |
|  |  |  | 0 | 10 | 009 | Geopotential height |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Geopotential height) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Geopotential height) |

|  |  |  |  |  |  | (Processed GPS) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 09 | 065 | 3 | 01 | 120 | Radiosonde abbreviated header and launch information |
|  |  |  | 0 | 08 | 041 | Data significance (6 = “flight level observation” ) |
|  |  |  | 3 | 01 | 122 | Date/time (to hundredths of second) |
|  |  |  | 0 | 05 | 001 | Latitude (high accuracy) |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Latitude) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Latitude) |
|  |  |  | 0 | 06 | 001 | Longitude (high accuracy) |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Longitude) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Longitude) |
|  |  |  | 0 | 07 | 007 | Height |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for Height) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for Height) |
|  |  |  | 0 | 11 | 003 | U-component |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for U-component) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for U-component) |
|  |  |  | 0 | 11 | 004 | V-component |
|  |  |  | 0 | 33 | 035 | Manual/automatic quality control (for V-component) |
|  |  |  | 0 | 33 | 015 | Data quality-check indicator (for V-component) |
|  |  |  |  |  |  | (Standard and significant levels) |
| 3 | 09 | 066 | 3 | 01 | 120 | Radiosonde abbreviated header and launch information |
|  |  |  | 0 | 08 | 041 | Data significance (6 = “flight level observation” ) |
|  |  |  | 3 | 01 | 122 | Date/time (to hundredths of second) |
|  |  |  | 0 | 08 | 040 | Flight level significance |
|  |  |  | 2 | 01 | 131 | Change data width |
|  |  |  | 2 | 02 | 129 | Change scale |
|  |  |  | 0 | 25 | 069 | Flight level pressure correction |
|  |  |  | 0 | 07 | 004 | Pressure |
|  |  |  | 0 | 13 | 003 | Relative humidity |
|  |  |  | 2 | 02 | 000 | Cancel change scale |
|  |  |  | 2 | 01 | 000 | Cancel change data width |
|  |  |  | 0 | 02 | 013 | Solar and infrared radiation correction |
|  |  |  | 0 | 12 | 101 | Temperature/dry bulb temperature |
|  |  |  | 0 | 12 | 103 | Dew-point temperature |
|  |  |  | 0 | 10 | 009 | Geopotential height |
|  |  |  | 0 | 10 | 007 | Height |
|  |  |  | 0 | 11 | 002 | Wind speed |
|  |  |  | 0 | 11 | 001 | Wind direction |