| WORLD METEOROLOGICAL ORGANIZATION ________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES Kuala Lumpur, 21 to 26 June 2004 |  | ET/DR&C/Doc. 3.3(2) _______ (1.VI. 2004) ENGLISH ONLY |
| --- | --- | --- |

BUFR AND CREX

METAR/SPECI AND TAF TEMPLATES

(Submitted by the International Civil Aviation Organization)

Summary and purpose of document This paper presents information, in the form of templates, regarding the METAR/SPECI and TAF code form requirements as contained in ICAO Annex 3 — Meteorological Service for International Air Navigation/WMO Technical Regulations (C.3.1). The templates presented may be of use for the preparation of the corresponding BUFR code tables.

Action proposed

To note the contents of this information paper.

- Discussion

  - The following tables provide information regarding the requirements for the reporting of METAR/SPECI and TAF as contained in ICAO Annex 3 — Meteorological Service for International Air Navigation/WMO Technical Regulations (C.3.1).

  - The tables are labelled as they appear in the above-mentioned documents. Table A3-2 identifies the requirements for METAR/SPECI with the associated Table A3-5 giving the ranges and resolutions for the various parameters involved. Similarly, Table A5-1 identifies the requirements for TAF with Table A5-3 giving the associated ranges and resolutions.

— — — — — — — —

Table A3-2.    Template for METAR and SPECI

Key:	M	=	inclusion mandatory, part of every message

C	=	inclusion conditional, dependent on meteorological conditions or method of observation

O	=	inclusion optional

Note 1. —	The ranges and resolutions for the numerical elements included in METAR and SPECI  are shown in Table A3-5 of this appendix.

Note 2.—	The explanations for the abbreviations used can be found in the Procedures for Air Navigation Services — ICAO Abbreviations and Codes (PANS-ABC, Doc 8400).

| Element as specified in Chapter 4 | Detailed content | Template(s) | Examples |
| --- | --- | --- | --- |
| Identification of the type of report (M) | Type of report (M) | METAR, METAR COR, SPECI or SPECI COR | METAR METAR COR SPECI |
| Location indicator (M) | ICAO location indicator (M) | nnnn | YUDO1 |
| Time of the observation (M) | Date and actual time of the observation in UTC (M) | nnnnnnZ | 221630Z |
| Identification of an automated or missing report (C)2 | Automated or missing report identifier (C) | AUTO or NIL | AUTO NIL |
| END OF METAR IF THE REPORT IS MISSING |
| Surface wind (M) | Wind direction (M) | nnn | VRB | 24015KMH VRB4KMH (24008KT) (VRB2KT) 19022KMH (19011KT) 00000KMH (00000KT) 140P199KMH (140P99KT) |
|  | Wind speed (M) | [P]nn[n] |  |
|  | Significant speed variations (C)3 | G[P]nn[n] | 12012G35KMH (12006G18KT) 24032G54KMH (24016G27KT) |
|  | Units of measurement (M) | KMH (or KT) |  |
|  | Significant direction al variation s (C)4 | nnnVnnn | — | 02020KMH 350V070 (02010KT 350V070) |
| Visibility (M) | Prevailing or minimum5 visibility (M) | nnnn | C A V O K | 0350 CAVOK 7000NDV 9999 |
|  | Unidirectional visibility (C)6 | NDV |  | 0800 |
|  | Minimum visibility (C)7 | nnnn |  | 2000 1200NW 6000 2800E |
|  | Direction of the minimum visibility (C)7 | N or NE or E or SE or S or SW or W or NW |  |  |

| RVR (C)8 | Name of the element (M) | R |  | R32/0400 |
| --- | --- | --- | --- | --- |
|  | Runway (M) | nn[n]/ |  | R10/M0050 R14L/P2000 |
|  | RVR (M) | [P or M]nnnn |  | R16L/0650 R16C/0500 R16R/0450 R17L/0450 |
|  | RVR variations (C)9 | V[P or M]nnnn |  | R20/0700V1200 R19/0350VP1200 |
|  | RVR past tendency (C)10 | U, D or N |  | R12/1100U R26/0550N R20/0800D R09/0375V0600U R10/M0150V0500D |
| Present weather (C)2,11 | Intensity or proximity of present weather (C)12 | –or + | — | VC |  |  |
|  | Characteristics and type of present weather (M)13 | DZ or RA or SN or SG or PL or DS or SS or TSRA or TSSN or TSPL or TSGR or TSGS or SHRA or SHSN or SHPL or SHGR or SHGS or FZRA or FZDZ or UP6 or FZUP | IC or FG or BR or SA or DU or HZ or FU or VA or SQ or PO or FC or TS or FZFG or BLSN or BLSA or BLDU or DRSN or DRSA or DRDU or MIFG or BCFG or PRFG | FG or PO or FC or DS or SS or TS or SH or BLSN or BLSA or BLDU or VA |  | RA HZ VCFG +TSRA FG VCSH +DZ VA VCTS -SN MIFG VCBLSA +TSRASN -SNRA DZ FG +SHSN BLSN UP FZUP |
| Cloud (M)14 | Cloud amount and height of cloud base or vertical visibility (M) | FEWnnn or SCTnnn or BKNnnn or OVCnnn | VVnnn or VV/// | SKC or NSC or NCD6 |  | FEW015 VV005 SKC OVC030 VV/// NSC SCT010 OVC020 BKN025/// |
|  | Cloud type (C)2 | CB or TCU or /// | — |  |  | BKN009TCU NCD SCT008 BKN025CB |
| Air and dew-point temperature (M) | Air and dew-point temperatures (M) | [M]nn/[M]nn | 17/10 02/M08 M01/M10 |
| Pressure values (M) | Name of the element (M) | Q | Q0995 Q1009 Q1022 Q0987 |
|  | QNH (M) | nnnn |  |
| Supplementary information (C) | Recent weather (C)2 11 | REFZDZ or REFZRA or REDZ or RE[SH]RA or RE[SH]SN or RESG or RE[SH]PL or RESHGR or RESHGS or REBLSN or RESS or REDS or RETSRA, RETSSN or RETSPL or RETSGR or RETSGS or REFC or REVA or REUP | REFZRA RETSRA |
|  | Wind shear (C)2 | WS RWYnn[n] or WS ALL RWY | WS RWY03 WS ALL RWY |
|  | Sea-surface temperature and state of the sea (C)15 | W[M]nn/Sn | W15/S2 |

|  | State of the runway (C)16 | Runway designator (M) | nn | SNOCLO | 99421594 SNOCLO 14CLRD// |
| --- | --- | --- | --- | --- | --- |
|  |  | Runway deposits (M) | n or / | CLRD// |  |  |
|  |  | Extent of runway contamination (M) | n or / |  |  |  |
|  |  | Depth of deposit (M) | nn or // |  |  |  |
|  |  | Friction coefficient or braking action (M) | nn or // |  |  |  |
| Trend forecast (O)17 | Change indicator (M)18 | NOSIG | BECMG or TEMPO | NOSIG BECMG FEW020 |
|  | Period of change (C)2 |  | FMnnnn and/or TLnnnn or ATnnnn |  |
|  | Wind (C)2 |  | nnn[P]nn[n][G [P]nn[n]]KMH (or nnn[P]nn[G[P] nn]KT) | TEMPO 25070G100KMH (TEMPO 25035G50KT) |
|  | Prevailing visibility (C)2 |  | nnnn | C A V O K | BECMG FM1030 TL1130 CAVOK BECMG TL1700 0800 FG BECMG AT1800 9000 NSW BECMG FM1900 0500 +SNRA BECMG FM1100 SN TEMPO FM1130 BLSN TEMPO FM0330 TL0430 FZRA |

|  | Weather phenomenon: intensity (C)12 |  | –or + | — | N S W |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Weather phenomenon: characteristics and type (C)2,11,13 |  | DZ or RA or SN or SG or PLor DS or SS or TSRA or TSSN or TSPL or TSGR or TSGS or SHRA or SHSN or SHPL or SHGR or SHGS or FZRA or FZDZ | IC or FG or BR or SA or DU or HZ or FU or VA or SQ or PO or FC or TS or FZFG or BLSN or BLSA or BLDU or DRSN or DRSA or DRDU or MIFG or BCFG or PRFG |  |  |  |
|  | Cloud amount and height of cloud base or vertical visibility (C)2 |  | FEWnnn or SCTnnn or BKNnnn or OVCnnn | VVnnn or VV/// | S K C or |  | TEMPO TL1200 0600 BECMG AT1200 8000 NSW NSC BECMG AT1130 OVC010 |
|  | Cloud type (C)2 |  | CB or TCU | — | N S C |  | TEMPO TL1530 +SHRA BKN012CB |

Notes.—

1.	Fictitious location.

2.	To be included whenever applicable.

.3.	To be included in accordance with 4.1.4.2 c).

4.	To be included in accordance with 4.1.4.2 b) 1).;

5.	To be included in accordance with 4.2.4.4 b).

6.	For automated reports only, in accordance with Section 4.9.

7.	To be included in accordance with 4.2.4.4 a).

8.	To be included if visibility or RVR < 1500 m; for up to a maximum of four runways in accordance with 4.3.6.5 b).

9.	To be included in accordance with 4.3.6.6 b).

10.	To be included in accordance with 4.3.6.6 a).

11.	One or more, up to a maximum of three, groups in accordance with 4.4.2.6, 4.8.1.1 and Appendix 5, 2.2.4.1.

12.	To be included whenever applicable; no qualifier for moderate intensity in accordance with 4.4.2.5;

13.	Precipitation types listed under 4.4.2.3 a) may be combined in accordance with 4.4.2.6 and Appendix 5, 2.2.4.1. Only moderate or heavy precipitation to be indicated in trend forecasts in accordance with Appendix 5, 2.2.4.

14.	Up to four cloud layers in accordance with 4.5.4.1 g).

15.	To be included; in accordance with 4.8.1.4 a).

16.	To be included in accordance with 4.8.1.4.b).

17.	To be included in accordance with Chapter 6, 6.3.2.

18.	Number of change indicators to be kept to a minimum in accordance with Appendix 5, 2.2.1.1; normally not exceeding three groups

— — — — — — — —

Table A3-5.    Ranges and resolutions for the numerical elements

included in METAR and SPECI

| Element as specified in Chapter 4 | Range | Resolution |
| --- | --- | --- |
| Runway: |  | (no units) | 01 - 36 | 1 |
| Wind direction: |  | ° true | 000 - 360 | 10 |
| Wind speed: |  | KMH KT | 00 - 399* 00 - 199* | 1 1 |
| Visibility: |  | M M M M | 0000 - 0800 0800 - 5 000 5 000 - 9 000 9 000 - 9 999 | 50 100 1 000 999 |
| RVR: |  | M M M | 0000 - 0400 0400 - 0800 0800 - 2 000 | 25 50 100 |
| Vertical visibility: |  | 30’s M (100’s FT) | 000 - 020 | 1 |
| Clouds: height of cloud base: |  | 30’s M (100’s FT) | 000-050 | 1 |
| Air temperature; Dew-point temperature: |  | °C | -80 - +60 | 1 |
| QNH: |  | hPa | 0850 - 1 100 | 1 |
| Sea-surface temperature: |  | °C | -10 - +40 | 1 |
| State of the sea: |  | (no units) | 0 - 9 | 1 |
| State of the runway | Runway designator: | (no units) | 01 - 36; 51 - 86; 88; 99 | 1 |
|  | Runway deposits: | (no units) | 0 - 9 | 1 |
|  | Extent of runway contamination: | (no units) | 1; 2; 5; 9 | — |
|  | Depth of deposit: | (no units) | 00 - 90; 92 - 99 | 1 |
|  | Friction coefficient/ braking action: | (no units) | 00 - 95; 99 | 1 |
| * There is no aeronautical requirement to report surface wind speeds of 200 km/h (100 kt) or more; however, provision has been made for reporting wind speeds up to 399 km/h (199 kt) for non-aeronautical purposes, as necessary. |

— — — — — — — —

Table A5-1.    Template for TAF

Key:		M	=	inclusion mandatory, part of every message

C	=	inclusion conditional, dependent on meteorological conditions or method of observation

O	=	inclusion optional

Note 1.— The ranges and resolutions for the numerical elements included in   TAF  are shown in Table A5-3 of this appendix.

Note 2.— The explanations for the abbreviations used can be found in the Procedures for Air Navigation Services — ICAO Abbreviations and Codes (PANS-ABC, Doc 8400).

| Element as specified in Chapter 6 | Detailed content | Template(s) | Examples |
| --- | --- | --- | --- |
| Identification of the type of forecast (M) | Type of forecast (M) | TAF or TAF AMD or TAF COR | TAF TAF AMD |
| Location indicator (M) | ICAO location indicator (M) | nnnn | YUDO1 |
| Date and time of issue of forecast (M) | Date and time of issue of the forecast in UTC (M) | nnnnnnZ | 160000Z |
| Identification of a missing forecast (C) | Missing forecast identifier (C) | NIL | NIL |
| END OF TAF IF THE FORECAST IS MISSING |
| Date and period of validity of forecast (M) | Date and period of the validity of the forecast in UTC (M) | nnnnnn | 160624 080918 |
| Identification of a cancelled forecast (C) | Cancelled forecast identifier(C) | CNL | CNL |
| END OF TAF IF THE FORECAST IS CANCELLED |
| Surface wind (M) | Wind direction (M) | nnn or VRB3 | 24015KMH; VRB04KMH (24008KT); (VRB02KT) 19022KMH (19011KT) |
|  | Wind speed (M) | [P]nn[n] | 00000KMH (00000KT) 140P199KMH (140P99KT) |
|  | Significant speed variations (C)2 | G[P]nn[n] | 12012G35KMH (12006G18KT) 24032G54KMH (24016G27KT) |
|  | Units of measurement (M) | KMH (or KT) |  |

| Visibility (M) | Prevailing visibility (M) | nnnn | C A V O K | 0350 CAVOK 7000 9000 9999 |
| --- | --- | --- | --- | --- |
| Weather (C)4, 5 | Intensity of weather phenomena (C)6 | – or + | — |  |  |
|  | Characteristics and type of weather phenomena )(C)7. | DZ or RA or SN or SG or PL or DS or SS or TSRA or TSSN or TSPL or TSGR or TSGS or SHRA or SHSN or SHPL or SHGR or SHGS or FZRA or FZDZ | IC or FG or BR or SA or DU or HZ or FU or VA or SQ or PO or FC or TS or FZFG or BLSN or BLSA or BLDU or DRSN or DRSA or DRDU or MIFG or BCFG or PRFG |  | RA HZ +TSRA FG – FZDZ PRFG +TSRASN SNRA FG |
| Cloud (M)8 | Cloud amount and height of base or vertical visibility (M) | FEWnnn or SCTnnn or BKNnnn or OVCnnn | VVnnn or VV /// | SKC or NSC |  | FEW010 VV005 SKC OVC020 VV/// NSC SCT005 BKN012 |
|  | Cloud type (C)4 | CB | — |  |  | SCT008 BKN025CB |
| Temperature (O)9 | Name of the element (M) | TX | TX25/13Z TN09/05Z |
|  | Maximum temperature (M) | [M]nn/ | TX05/12Z TNM02/03Z |
|  | Time of occurrence of the maximum temperature (M) | nnZ |  |
|  | Name of the element (M) | TN |  |
|  | Minimum temperature (M) | [M]nn/ |  |
|  | Time of occurrence of the minimum temperature (M) | nnZ |  |

| Expected significant changes to one or more of the above elements during the period of validity (C)4,10 | Change or probability indicator (M) | PROB30 [TEMPO] or PROB40 [TEMPO] or BECMG or TEMPO or FM |  |
| --- | --- | --- | --- |
|  | Period of occurrence or change (M) | nnnn |  |
|  | Wind (C)4 | nnn[P]nn[n][G[P] nn[n]]KMH or VRBnnKMH (or nnn[P]nn[G[P]nn ]KT or VRBnnKT) | TEMPO 1518 25070G100KMH (TEMPO 1518 25035G50KT) TEMPO 1214 17025G50KMH 1000 TSRA SCT010CB BKN020 (TEMPO 1214 17012G25KT 1000 TSRA SCT010CB BKN020) |
|  | Prevailing visibility (C)4 | nnnn | C A V O K | BECMG 1011 00000KMH 2400 OVC010 (BECMG 1011 00000KT 2400 OVC010) PROB30 1214 0800 FG |
|  | Weather phenomenon: intensity (C)6 | - or + | — | NSW |  | BECMG 1214 RA TEMPO 0304 FZRA TEMPO 1215 BLSN PROB40 TEMPO 0608 0500 FG |
|  | Weather phenomenon: characteristics and type (C)4, 7, | DZ or RA or SN or SG or PL or DS or SS or TSRA or TSSN or TSPL or TSGR or TSGS or SHRA or SHSN or SHPL or SHGR or SHGS or FZRA or FZDZ | IC or FG or BR or SA or DU or HZ or FU or VA or SQ or PO or FC or TS or FZFG or BLSN or BLSA or BLDU or DRSN or DRSA or DRDU or MIFG or BCFG or PRFG |  |  |  |
|  | Cloud amount and height of base or vertical visibility (C)4 | FEWnnn or SCTnnn or BKNnnn or OVCnnn | VVnnn or VV/// | SKC or NSC |  | FM1230 15015KMH 9999 BKN020 (FM1230 15008KT 9999 BKN020 BECMG 1820 8000 NSW NSC |
|  | Cloud type (C)4 | CB | — |  |  | BECMG 0608 SCT015CB BKN020 |

Notes.—

1.	Fictitious location.

2.	To be included in accordance with 1.2.1.

3.	To be used in accordance with.1.2.1.

4.	To be included whenever applicable.

5.	One or more, up to a maximum of three, groups in accordance with 1.2.3.;

6.	To be included whenever applicable in accordance with 1.2.3. No qualifier for moderate intensity;

7.	 Weather phenomena to be included in accordance with 1.2.3.

8.	Up to four cloud layers in accordance with 1.2.4.

9.	To be included in accordance with 1.2.5.

10.	To be included in accordance with.1.3, 1.4 and 1.5.

— — — — — — — —

TableA5-3.    Ranges and resolutions for the numerical elements

- included in TAF

| Element as specified in Chapter 6 | Range | Resolution |
| --- | --- | --- |
| Wind direction: | ° true | 000 - 360 | 10 |
| Wind speed: | KMH KT | 00 - 399* 00 - 199* | 1 1 |
| Visibility: | M M M M | 0000 - 0800 0800 - 5 000 5 000 - 9 000 9 000 - 9 999 | 50 100 1 000 999 |
| Vertical visibility: | 30’s M (100’s FT) | 000 - 020 | 1 |
| Cloud: height of base: | 30’s M (100’s FT) | 000 - 050 | 1 |
| Air temperature (maximum and minimum): | °C | -80 - +60 | 1 |
| *There is no aeronautical requirement to report surface wind speeds of 200 km/h (100 kt) or more; however, provision has been made for reporting wind speeds up to 399 km/h (199 kt) for non-aeronautical purposes, as necessary. |

— END —