| WORLD METEOROLOGICAL ORGANIZATION ______________________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES KUALA LUMPUR, MALAYSIA, 21-26 JUNE 2004 |  | ET/DR&C/Doc. 3.7.1.3(1) (08.VI.2004) ITEM 3.7.1.3 ENGLISH only |
| --- | --- | --- |

DATA CATEGORY AND SUB-CATEGORY DEFINITIONS

(Submitted by the Secretariat)

________________________________________________________________

Summary and Purpose of Document

This document defines international data sub-category in BUFR/CREX.

________________________________________________________________

ACTION PROPOSED

The meeting is requested to consider the proposed new table and make the necessary additional entries.  The new table will be part of an addition to a new edition of BUFR.

Reference:

- Manual on Codes, Volume I.2

DISCUSSION

# Use of data category and data sub-category in FM 94 BUFR

In 2003, the Team agreed to satisfy the requirement for official definition of data sub-category in BUFR.  However, it was agreed that existing local sub-categories should remain available since they were used by many data processing centers.  It was recommended that in the frame of new edition changes, a new two-octet field be defined to contain the official international sub-category.  The new table could be structured in a manner similar to the Common Table C-12 for sub-centres.  The Team had wished that the Secretariat (assisted by member(s) of the Team), define an exhaustive list of known data sub-categories for submission to the Meeting next year.  That new table is proposed below, and it is wished that the members introduce the additional entries they found necessary.

COMMON CODE TABLE C-13: Data sub categories of categories defined by entries in BUFR Table A

| Data categories | International data sub-categories |
| --- | --- |
| BUFR octet 11 CREX nnn in group Annnmmm | BUFR octet 12 CREX mmm in group Annnmmm |
| Code figure | Name | Code figure | Name (corresponding traditional alphanumeric codes are in backets) |
| 000 | Surface data — land | 000 | Synoptical observations hourly (AWS or SYNOP, SYNOP MOBIL) |
|  | 001 | Synoptical observations intermediate time (AWS or SYNOP, SYNOP MOBIL) |
|  | 002 | Synoptical observations main time (AWS or SYNOP, SYNOP MOBIL) |
|  |  | Synoptical observations n-minute (AWS or SYNOP, SYNOP MOBIL) |
|  | 010 | Aeronautical observations (METAR/SPECI) |
|  | 020 | Climatological observations (CLIMAT) |
|  | 030 | Spherics locations (SFLOC) |
|  | 040 | Hydrologic reports |
|  | 100 | Mixed data types |
|  | 200 | Other type |
| 001 | Surface data — sea | 000 | Synoptical observations (SHIP) |
|  | 010 | Climatological observations (CLIMAT SHIP) |
|  | 020 | Surface observation BUOY |
|  | 030 | Tide gauge data |
|  | 031 | Observed water level time series |
| 002 | Vertical soundings (other than satellite) | 001 | Wind profile (PILOT/PILOT SHIP PILOT MOBIL) |
|  |  | 002 | Temp/hum/wind sounding (TEMP/TEMP DROP/TEMP SHIP/TEMP MOBIL) |
|  |  | 003 | Windprofiler |
|  |  | 004 | RASS temp. profile |
|  |  | 005 | ASDAR/ACARS profiles (AMDAR) |
|  |  | 006 | Climatological observations (CLIMAT TEMP, CLIMAT TEMP SHIP) |
| 003 | Vertical soundings (satellite) | 000 | Temperature (SATEM) |
|  | 001 | TIROS (TOVS) |
| 004 | Single level upper-air data (other than satellite) | 000 | ASDAR/ACARS (AMDAR) |
|  | 001 | Manual (AIREP, PIREP) |
| 005 | Single level upper-air data (satellite) | 000 | Cloud wind data (SATOB etc.) |
| 006 | Radar data | 000 | Reflectivity data |
|  | 001 | Doppler wind profiles |
|  | 002 | Derived products |
|  | 003 | Ground radar weather (RADOB) |
| 007 | Synoptic features | 000 | Forecast Tropical cyclone tracks from EPS |
| 008 | Physical/chemical constituents | 000 | Ozone measurement at surface |
|  | 001 | Ozone vertical sounding |
| 009 | Dispersal and transport | 000 | Trajectories, analysis or forecast |
| 010 | Radiological data | 001 | Observation (RADREP) |
|  | 002 | Forecast (RADOF) |

| 012 | Surface data (satellite) | 000 | ERS-uwa |
| --- | --- | --- | --- |
|  | 001 | ERS-uwi |
|  | 002 | ERS-ura |
|  | 003 | ERS-uat |
|  | 004 | SSM/I radiometer |
|  | 005 | Quickscat |
|  | 006 | Surface temp./radiation (SATOB) |
| 031 | Oceanographic data | 000 | Surface observation |
|  | 001 | Surface observation along track (TRACKOB) |
|  | 002 | Spectral wave observation (WAVEOB) |
|  | 003 | Bathythermal observation (eg. BATHY) |
|  | 004 | Sub surface floats (profile) |
|  | 005 | XBT/XCTD profiles (e.g. TESAC) |
|  | 006 | Waves reports |