| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES KUALA LUMPUR, MALAYSIA, 21 - 26 JUNE 2004 |  | ET DR&C/Doc. 6.1(1) ITEM: 6.1 (5.V.2004) ENGLISH ONLY |
| --- | --- | --- |

Review of BUFR templates for PILOT and TEMP data

(including proposal for Common Sequences)

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains review of BUFR templates for PILOT and TEMP data and a proposal for new BUFR sequence descriptors, as a result of validation of BUFR templates for TEMP data.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to examine the presented templates and sequence descriptors and recommend them either for further validation or for submitting to the CBS-XIII.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[2] Final Report, ET DR&C, Prague, 22 - 26 April 2002.

[3] Final Report, ET DR&C, Arusha, 17 - 21 February 2003.

[4] http://www.wmo.int/web/www/DPS/Migration/BUFRCREXTemplates0403.doc

1. Background

The meeting of Expert Team on Data Representation and Codes that was held in Arusha, Tanzania, in February 2003, agreed that BUFR templates for PILOT and TEMP codes would contain data representation of radiosonde drift from the launch site. In February 2004, the Czech Hydrometeorological Institute (CHMI) started to produce BUFR messages containing TEMP data including the time and position identification of the radiosonde at each individual level (available at the RTH Prague under the header IUSD40 OKLI). Based on the following e-mail discussion between ET DR&C Members, in particular Messrs J. Ator of NCEP, M. Dragosavac of ECMWF and Ch. Long of UK MetOffice, and the author, the template for TEMP data has been modified. Changes relevant for PILOT data have been implemented also into the templates for PILOT data.

The new version of BUFR templates for PILOT and TEMP data is shown in chapter 3 of this document. Chapter 2 contains proposal for sequence descriptors for vertical sounding traditional data. Proposal for new Table B descriptors required is presented in document Doc.3.1(4).

The ET DR&C session may consider the possibility to recommend templates in chapter 3 as primary data representation of vertical sounding data to producers of sounding equipment (e.g. Vaisala).

#### 2. Proposals for sequence descriptors for PILOT code and TEMP code data

Following sequence descriptors are proposed:

|  |  |  |  |  |  | (Identification of launch site and instrumentation for wind measurements) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 01 | 110 | 3 | 01 | 001 | WMO block number, WMO station number |
|  |  |  | 0 | 01 | 011 | Ship or mobile land station identifier |
|  |  |  | 0 | 02 | 011 | Radiosonde type |
|  |  |  | 0 | 02 | 014 | Tracking technique/status of system used |
|  |  |  | 0 | 02 | 003 | Type of measuring equipment used |

|  |  |  |  |  |  | (Identification of launch site and instrumentation for P, T, U and wind measurements) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 01 | 111 | 3 | 01 | 001 | WMO block number, WMO station number |
|  |  |  | 0 | 01 | 011 | Ship or mobile land station identifier |
|  |  |  | 0 | 02 | 011 | Radiosonde type |
|  |  |  | 0 | 02 | 013 | Solar and infrared radiation correction |
|  |  |  | 0 | 02 | 014 | Tracking technique/status of system used |
|  |  |  | 0 | 02 | 003 | Type of measuring equipment used |

|  |  |  |  |  |  | (Identification of launch point and instrumentation of dropsonde) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 01 | 112 | 0 | 01 | 006 | Aircraft identifier |
|  |  |  | 0 | 02 | 011 | Radiosonde type |
|  |  |  | 0 | 02 | 013 | Solar and infrared radiation correction |
|  |  |  | 0 | 02 | 014 | Tracking technique/status of system used |
|  |  |  | 0 | 02 | 003 | Type of measuring equipment used |

|  |  |  |  |  |  | (Date/time of launch) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 01 | 113 | 0 | 08 | 021 | Time significance ( = 18 (launch time)) |
|  |  |  | 3 | 01 | 011 | Year, month, day of launch |
|  |  |  | 3 | 01 | 013 | Hour, minute, second of launch |

|  |  |  |  |  |  | (Horizontal and vertical coordinates of launch site) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 01 | 114 | 3 | 01 | 021 | Latitude (high accuracy) |
|  |  |  |  |  |  | Longitude (high accuracy) |
|  |  |  | 0 | 07 | 030 | Height of station ground above mean sea level |
|  |  |  | 0 | 07 | 031 | Height of barometer above mean sea level |
|  |  |  | 0 | 07 | 007 | Height of release of sonde above mean sea level |
|  |  |  | 0 | 33 | 024 | Station elevation quality mark (for mobile stations) |

|  |  |  |  |  |  | (Cloud information reported with vertical soundings) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 02 | 049 | 0 | 08 | 002 | Vertical significance |
|  |  |  | 0 | 20 | 011 | Cloud amount (of low or middle clouds Nh) |
|  |  |  | 0 | 20 | 013 | Height of base of cloud (h) |
|  |  |  | 0 | 20 | 012 | Cloud type (low clouds CL) |
|  |  |  | 0 | 20 | 012 | Cloud type (middle clouds CM) |
|  |  |  | 0 | 20 | 012 | Cloud type (high clouds CH) |
|  |  |  | 0 | 08 | 002 | Vertical significance ( = missing value) |

|  |  |  |  |  |  | (Wind data at a pressure level with radiosonde position) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 03 | 050 | 0 | 04 | 086 | Long time period or displacement (since launch time) |
|  |  |  | 0 | 08 | 042 | Extended vertical sounding significance |
|  |  |  | 0 | 07 | 004 | Pressure |
|  |  |  | 0 | 05 | 015 | Latitude displacement since launch site (high accuracy) |
|  |  |  | 0 | 06 | 015 | Longitude displacement since launch site (high accuracy) |
|  |  |  | 0 | 11 | 001 | Wind direction |
|  |  |  | 0 | 11 | 002 | Wind speed |

|  |  |  |  |  |  | (Wind shear data at a pressure level with radiosonde position) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 03 | 051 | 0 | 04 | 086 | Long time period or displacement (since launch time) |
|  |  |  | 0 | 08 | 042 | Extended vertical sounding significance |
|  |  |  | 0 | 07 | 004 | Pressure |
|  |  |  | 0 | 05 | 015 | Latitude displacement since launch site (high accuracy) |
|  |  |  | 0 | 06 | 015 | Longitude displacement since launch site (high accuracy) |
|  |  |  | 0 | 11 | 061 | Absolute wind shear in 1 km layer below |
|  |  |  | 0 | 11 | 062 | Absolute wind shear in 1 km layer above |

|  |  |  |  |  |  | (Wind data at a height level with radiosonde position) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 03 | 052 | 0 | 04 | 086 | Long time period or displacement (since launch time) |
|  |  |  | 0 | 08 | 042 | Extended vertical sounding significance |
|  |  |  | 0 | 07 | 009 | Geopotential height |
|  |  |  | 0 | 05 | 015 | Latitude displacement since launch site (high accuracy) |
|  |  |  | 0 | 06 | 015 | Longitude displacement since launch site (high accuracy) |
|  |  |  | 0 | 11 | 001 | Wind direction |
|  |  |  | 0 | 11 | 002 | Wind speed |

|  |  |  |  |  |  | (Wind shear data at a height level with radiosonde position) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 03 | 053 | 0 | 04 | 086 | Long time period or displacement (since launch time) |
|  |  |  | 0 | 08 | 042 | Extended vertical sounding significance |
|  |  |  | 0 | 07 | 009 | Geopotential height |
|  |  |  | 0 | 05 | 015 | Latitude displacement since launch site (high accuracy) |
|  |  |  | 0 | 06 | 015 | Longitude displacement since launch site (high accuracy) |
|  |  |  | 0 | 11 | 061 | Absolute wind shear in 1 km layer below |
|  |  |  | 0 | 11 | 062 | Absolute wind shear in 1 km layer above |

|  |  |  |  |  |  | (Temperature, dew-point and wind data at a pressure level with radiosonde position) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 03 | 054 | 0 | 04 | 086 | Long time period or displacement (since launch time) |
|  |  |  | 0 | 08 | 042 | Extended vertical sounding significance |
|  |  |  | 0 | 07 | 004 | Pressure |
|  |  |  | 0 | 07 | 009 | Geopotential height |
|  |  |  | 0 | 05 | 015 | Latitude displacement since launch site (high accuracy) |
|  |  |  | 0 | 06 | 015 | Longitude displacement since launch site (high accuracy) |
|  |  |  | 0 | 12 | 101 | Temperature/dry-bulb temperature (scale 2) |
|  |  |  | 0 | 12 | 103 | Dew-point temperature (scale 2) |
|  |  |  | 0 | 11 | 001 | Wind direction |
|  |  |  | 0 | 11 | 002 | Wind speed |

Common Sequences for representation of PILOT code and TEMP code data

|  |  |  |  |  |  | (Sequence for representation of PILOT,PILOT SHIP and PILOT MOBIL data with pressure as the vertical coordinate) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 09 | 050 | 3 | 01 | 110 | Identification of launch site and instrumentation for wind measurements |
|  |  |  | 3 | 01 | 013 | Date/time of launch |
|  |  |  | 3 | 01 | 014 | Horizontal and vertical coordinates of launch site |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |
|  |  |  | 0 | 31 | 002 | Extended delayed descriptor replication factor |
|  |  |  | 3 | 03 | 050 | Wind data at a pressure level |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |
|  |  |  | 0 | 31 | 001 | Delayed descriptor replication factor |
|  |  |  | 3 | 03 | 051 | Wind shear data at a pressure level |

|  |  |  |  |  |  | (Sequence for representation of PILOT,PILOT SHIP and PILOT MOBIL data with height as the vertical coordinate) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 09 | 051 | 3 | 01 | 110 | Identification of launch site and instrumentation for wind measurements |
|  |  |  | 3 | 01 | 013 | Date/time of launch |
|  |  |  | 3 | 01 | 014 | Horizontal and vertical coordinates of launch site |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |
|  |  |  | 0 | 31 | 002 | Extended delayed descriptor replication factor |
|  |  |  | 3 | 03 | 052 | Wind data at a height level |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |
|  |  |  | 0 | 31 | 001 | Delayed descriptor replication factor |
|  |  |  | 3 | 03 | 053 | Wind shear data at a height level |
|  |  |  |  |  |  | (Sequence for representation of TEMP, TEMP SHIP and TEMP MOBIL data) |
| 3 | 09 | 052 | 3 | 01 | 111 | Identification of launch site and instrumentation for P, T, U and wind measurements |
|  |  |  | 3 | 01 | 013 | Date/time of launch |
|  |  |  | 3 | 01 | 014 | Horizontal and vertical coordinates of launch site |
|  |  |  | 3 | 02 | 049 | Cloud information reported with vertical soundings |
|  |  |  | 0 | 22 | 043 | Sea water temperature |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |
|  |  |  | 0 | 31 | 002 | Extended delayed descriptor replication factor |
|  |  |  | 3 | 03 | 054 | Temperature, dew-point and wind data at a pressure level |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |
|  |  |  | 0 | 31 | 001 | Delayed descriptor replication factor |
|  |  |  | 3 | 03 | 051 | Wind shear data at a pressure level |

|  |  |  |  |  |  | (Sequence for representation of TEMP DROP data) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 09 | 053 | 3 | 01 | 112 | Identification of launch point and instrumentation of dropsonde |
|  |  |  | 3 | 01 | 013 | Date/time of launch |
|  |  |  | 3 | 01 | 014 | Horizontal and vertical coordinates of launch site |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |
|  |  |  | 0 | 31 | 002 | Extended delayed descriptor replication factor |
|  |  |  | 3 | 03 | 054 | Temperature, dew-point and wind data at a pressure level |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |
|  |  |  | 0 | 31 | 001 | Delayed descriptor replication factor |
|  |  |  | 3 | 03 | 051 | Wind shear data at a pressure level |

#### 3. Review of BUFR templates for PILOT code and TEMP code data

BUFR TEMPLATES FOR PILOT, PILOT SHIP,  PILOT MOBIL

a)  with pressure as the vertical coordinate – 3 09 050

| 3 01 110 |  | Identification of launch site and instrumentation for wind measurements |  |
| --- | --- | --- | --- |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark (for mobile stations) | Code table |
|  |  | Wind data at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 050 |  | Wind data at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 3 03 051 |  | Wind shear data at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 061 | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
|  | 0 11 062 | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

b)  with height as the vertical coordinate – 3 09 051

| 3 01 110 |  | Identification of launch site and instrumentation for wind measurements |  |
| --- | --- | --- | --- |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark (for mobile stations) | Code table |
|  |  | Wind data at heights |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 052 |  | Wind data at a height level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data at heights |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 3 03 053 |  | Wind shear data at a height level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 061 | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
|  | 0 11 062 | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

BUFR TEMPLATE FOR TEMP, TEMP SHIP, TEMP MOBIL – 3 09 052

| 3 01 111 |  | Identification of launch site and instrumentation |  |
| --- | --- | --- | --- |
|  | 3 01 001 | WMO block number | Numeric |
|  |  | WMO station number | Numeric |
|  | 0 01 011 | Ship or mobile land station identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 013 | Solar and infrared radiation correction | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark (for mobile stations) | Code table |
| 3 02 049 |  | Cloud information reported with vertical soundings |  |
|  | 0 08 002 | Vertical significance | Code table |
|  | 0 20 011 | Cloud amount (of low or middle clouds Nh) | Code table |
|  | 0 20 013 | Height of base of cloud (h) | m, scale –1 |
|  | 0 20 012 | Cloud type (low clouds CL) | Code table |
|  | 0 20 012 | Cloud type (middle clouds CM) | Code table |
|  | 0 20 012 | Cloud type (high clouds CH) | Code table |
|  | 0 08 002 | Vertical significance ( = missing value) | Code table |
| 0 22 043 |  | Sea/water temperature (for ship stations) | K, scale 2 |
|  |  | Temperature, dew-point, wind at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 054 |  | Temperature, dew-point, wind at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 10 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, scale 2 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor | 1 01 000 |
| 0 31 001 |  | Delayed descriptor replication factor | 0 31 001 |
| 3 03 051 |  | Wind shear data at a pressure level | 3 03 051 |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 061 | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
|  | 0 11 062 | Absolute wind shear in 1 km layer above | m s-1, scale 1 |

BUFR TEMPLATE FOR TEMP DROP – 3 09 053

| 3 01 112 |  | Identification of launch point and instrumentation of dropsonde |  |
| --- | --- | --- | --- |
|  | 0 01 006 | Aircraft identifier | CCITT IA5 |
|  | 0 02 011 | Radiosonde type | Code table |
|  | 0 02 013 | Solar and infrared radiation correction | Code table |
|  | 0 02 014 | Tracking technique/status of system used | Code table |
|  | 0 02 003 | Type of measuring equipment used | Code table |
| 3 01 113 |  | Date/time of launch |  |
|  | 0 08 021 | Time significance ( = 18 (launch time)) | Code table |
|  | 3 01 011 | Year | Year |
|  |  | Month | Month |
|  |  | Day | Day |
|  | 3 01 013 | Hour | Hour |
|  |  | Minute | Minute |
|  |  | Second | Second |
| 3 01 114 |  | Horizontal and vertical coordinates of launch site |  |
|  | 3 01 021 | Latitude (high accuracy) | Degree, scale 5 |
|  |  | Longitude (high accuracy) | Degree, scale 5 |
|  | 0 07 030 | Height of station ground above mean sea level | m, scale 1 |
|  | 0 07 031 | Height of barometer above mean sea level | m, scale 1 |
|  | 0 07 007 | Height of release of sonde above mean sea level | m |
|  | 0 33 024 | Station elevation quality mark | Code table |
|  |  | Temperature, dew-point, wind at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 002 |  | Extended delayed descriptor replication factor | Numeric |
| 3 03 054 |  | Temperature, dew-point, wind at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 10 009 | Geopotential height | gpm |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 12 101 | Temperature/dry-bulb temperature (scale 2) | K, scale 2 |
|  | 0 12 103 | Dew-point temperature (scale 2) | K, scale 2 |
|  | 0 11 001 | Wind direction | Degree true |
|  | 0 11 002 | Wind speed | m s-1, scale 1 |
|  |  | Wind shear data at pressure levels |  |
| 1 01 000 |  | Delayed replication of 1 descriptor |  |
| 0 31 001 |  | Delayed descriptor replication factor | Numeric |
| 3 03 051 |  | Wind shear data at a pressure level |  |
|  | 0 04 086 | Long time period or displacement (since launch time) | Second |
|  | 0 08 042 | Extended vertical sounding significance | Flag table |
|  | 0 07 004 | Pressure | Pa, scale –1 |
|  | 0 05 015 | Latitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 06 015 | Longitude displacement since launch site (high accuracy) | Degree, scale 5 |
|  | 0 11 061 | Absolute wind shear in 1 km layer below | m s-1, scale 1 |
|  | 0 11 062 | Absolute wind shear in 1 km layer above | m s-1, scale 1 |