| WORLD METEOROLOGICAL ORGANIZATION COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES KUALA LUMPUR, MALAYSIA, 21 - 26 JUNE 2004 |  | ET DR&C/Doc. 6.1(5) ITEM: 6.1 (11.VI.2004) ENGLISH ONLY |
| --- | --- | --- |

Review of BUFR templates for AWS, SYNOP, SYNOP MOBIL and SHIP data

(including proposal for sequence descriptors)

Submitted by Eva Červená (Czech Republic)

________________________________________________________________

Summary and Purpose of Document

The document contains review of BUFR templates for AWS, SYNOP, SYNOP MOBIL and SHIP data and a proposal for new BUFR sequence descriptors.

________________________________________________________________

ACTION PROPOSED

The meeting is invited to examine the presented templates and sequence descriptors and recommend them either for further validation or for submitting to the CBS-XIII.

References:

[1] Manual on Codes, WMO-No. 306, Volume I.1 and I.2.

[2] Final Report, ET DR&C, Prague, 22 - 26 April 2002.

[3] Final Report, ET DR&C, Arusha, 17 - 21 February 2003.

[4] http://www.wmo.int/web/www/DPS/Migration/BUFRCREXTemplates0403.doc

1. Background

The meeting of ET DR&C that was held in Prague, Czech Republic, in April 2002, agreed on a set of BUFR templates for AWS data and for representation of data currently reported in traditional codes. The following validation of the template for SYNOP data performed in the Czech Hydrometeorological Institute resulted into a proposal for modification of this template that was approved by the ET DR&C meeting held in Arusha, Tanzania, in February 2003 [3].

Besides that, preparatory work for Training Seminars on Table Driven Code Forms held in Arusha, Tanzania and in San Jose, Costa Rica, lead to indication of some data items (groups 54g0sndT, 56DLDMDH, 57CDaeC, 58p24p24p24 and 59p24p24p24 of SYNOP Section 3) not being represented in the current version of the template [4]. A Table B entry for 24-hour pressure change (0 10 062) is available, but data representation of some of the other items has required a proposal for new Table B descriptors (presented in document Doc.3.1(6)). Moreover, detailed study of the regional practices for reporting of extreme temperatures (internationally distributed data items) resulted into modification of the corresponding part of the template.

In the summer of 2003, templates for SYNOP, SYNOP MOBIL and SHIP data, including proposed new sequence descriptors, were sent to the ET DR&C members for examination. Apart from the modifications and additions described above, sequence descriptors shown in templates in chapter 4 of this document are identical with the sequence descriptors proposed last summer.

Chapter 4 of this document contains a revised version of templates for SYNOP and SYNOP MOBIL and two templates for SHIP data. In the second of them, extensive use of delayed replication was applied to reduce the volume of BUFR messages containing single reports from Voluntary Observing Ships (VOS). This technique had been proposed by Mr Jaap van der Plank and Mr Dick Blaauboer of the KNMI [2] and its using was needed in this case as most of the VOS observations are transmitted via Inmarsat-C terminals and any increase of the volume of the data would cause serious financial problems. The extensive use of delayed replication combined with reduction of the data description to  one sequence descriptor resulted into getting the volume of the BUFR messages into the required range.

2. Proposal for minor changes in the template for AWS data from n-minute period

As a result of the e-mail discussion on usage of increment and displacement descriptors mentioned in Doc. 3.1(6) and Doc. 6.1(1), it is proposed to replace 0 04 025 Time displacement (= - n minutes) by  0 04 015 Time increment (= - n minutes). Thus the template would read:

BUFR TEMPLATE FOR AWS DATA FROM N-MINUTE PERIOD

| 3 01 090 |  | Surface station identification; time, horizontal and vertical co-ordinates |
| --- | --- | --- |
| 0 08 010 |  | Surface qualifier (for temperature data) | Code table |
| 3 01 091 |  | Surface station instrumentation |  |
| 0 04 015 |  | Time increment (= - n minutes) | Minute |
| 0 04 065 |  | Short time increment ( = 1 minute) | Minute |
| 1 14 n |  | Replicate 14 descriptors n- times |  |
|  |  | E.g.: 1 14 006 in case of 6-minute period, 1 14 010 in case of 10-minute period |  |
| 0 10 004 |  | Pressure | Pa, scale –1 |
| etc. |  |  |  |

The current form of this template in the WMO server [4] might give the impression that the entry 0 08 010 is a part of the preceding sequence descriptor 3 01 090. A minor editorial modification would make it  obvious that it is not so.

#### 3. Proposals for sequence descriptors for SYNOP, SYNOP MOBIL and  SHIP data

3.1 List of sequence descriptors displayed in the templates

Following sequence descriptors proposed for representation of SYNOP, SYNOP MOBIL and SHIP data and SHIP data reported from VOS stations are displayed in templates in Chapter 4:

3 01 092,  3 01 093,  3 02 031, 3 02 032, 3 02 033, 3 02 034, 3 02 035,  3 02 036, 3 02 037, 3 02 038, 3 02 039,  3 02 040,  3 02 041, 3 02 042, 3 02 043, 3 02 044, 3 02 045,  3 02 046, 3 02 047,  3 02 048, 3 02 052, 3 02 053,  3 02 054,  3 02 055, 3 02 056, 3 02 057, 3 02 058, 3 02 059,  3 02 060, 3 02 062, 3 02 063 and 3 07 070.

3.2 A proposal for sequence descriptors 3 02 046, 3 02 047 and 3 02 048

As mentioned above, groups 54g0sndT, 56DLDMDH and 57CDaeC of SYNOP Section 3 have not yet got  corresponding data representation in BUFR and CREX. The group 56DLDMDH is frequently reported by stations in the tropical belt as well as group 54g0sndT which BUFR equivalent was explicitly requested by participants of Training Seminar on Table Driven Code Forms in San Jose.

Almost all elements in SYNOP groups 54g0sndT, 56DLDMDH and 57CDaeC are specified by Code tables. In BUFR and CREX, however, unit = Code table is to be used only if any other solution is not applicable, thus usage of code tables has been avoided in the following proposals.

3 02 046 is proposed to express the data of the SYNOP group 54g0sndT, where

g0  is “Period of time, in hours, between the time of observation and the temperature change”,

sn   is “Sign of the temperature change” – Code table 3845,

dT  is “ Amount of temperature change, the sign of the change given by sn “– Code table 0822.

|  |  |  |  |  |  | (Temperature change) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 02 | 046 | 0 | 04 | 024 | Time period or displacement |
|  |  |  | 0 | 04 | 024 | Time period or displacement |
|  |  |  | 0 | 12 | 049 | Temperature change over period specified |

3 02 047 is proposed to express data of SYNOP group 56DLDMDH, where

DL  is  “True direction from which CL clouds are moving” – Code table 0700,

DM  is  “True direction from which CM clouds are moving” – Code table 0700,

DH  is  “True direction from which CH clouds are moving”  – Code table 0700.

|  |  |  |  |  |  | (Direction of cloud drift) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 02 | 047 | 0 | 20 | 054 | True direction from which CL clouds are moving |
|  |  |  | 0 | 20 | 055 | True direction from which CM clouds are moving |
|  |  |  | 0 | 20 | 056 | True direction from which CH clouds are moving |

3 02 048 is proposed to express data of SYNOP group 57CDaeC, where

C  is  “Genus of cloud” – Code table 0500,

Da  is  “True direction in which the phenomenon indicated is observed” – Code table 0700,

eC is  “Elevation angle of the top of the cloud indicated by C”  – Code table 1004.

|  |  |  |  |  |  | (Direction and elevation of cloud) |
| --- | --- | --- | --- | --- | --- | --- |
| 3 | 02 | 048 | 0 | 05 | 021 | Bearing or azimuth |
|  |  |  | 0 | 07 | 021 | Elevation |
|  |  |  | 0 | 20 | 012 | Cloud type |
|  |  |  | 0 | 05 | 021 | Bearing or azimuth ( = missing to cancel the previous value) |
|  |  |  | 0 | 07 | 021 | Elevation ( = missing to cancel the previous value) |

4. Review of BUFR templates for SYNOP, SYNOP MOBIL and  SHIP data

BUFR TEMPLATE FOR SYNOP DATA

| 3 01 090 |  |  | Fixed surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 004 | 0 01 001 | WMO block number II | Numeric, 0 |
|  |  | 0 01 002 | WMO station number iii | Numeric, 0 |
|  |  | 0 01 015 | Station or site name | CCITT IA5, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  | 3 01 011 | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  | 3 01 012 | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) | Degree, 5 |
|  |  | 0 06 001 | Longitude (high accuracy) | Degree, 5 |
|  | 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  |  |  | Pressure data |  |
| 3 02 031 | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  | 0 10 062 |  | 24-hour pressure change p24p24p24 | Pa, –1 |
|  | 0 07 004 |  | Pressure (standard level) a3 | Pa, –1 |
|  | 0 10 009 |  | Geopotential height of the standard level hhh | gpm, 0 |
| 3 02 035 |  |  | Basic synoptic “instantaneous” data |  |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 032 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 033 | 0 07 032 | Height of sensor above local ground (for visibility measurement) | m, 2 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 3 02 034 | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
|  |  |  | Clouds with bases below station level |  |
| 3 02 036 | 1 05 000 |  | Delayed replication of 5 descriptors |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 0 08 002 |  | Vertical significance | Code table, 0 |
|  | 0 20 011 |  | Cloud amount N’ | Code table, 0 |
|  | 0 20 012 |  | Cloud type C’ | Code table, 0 |
|  | 0 20 014 |  | Height of top of cloud H’H’ | m, -1 |
|  | 0 20 017 |  | Cloud top description Ct | Code table, 0 |
| 0 08 002 |  |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Direction of cloud drift gr. 56DLDMDH |  |
| 3 02 047 | 0 20 054 |  | True direction from which CL clouds are moving DL | Degree true, 0 |
|  | 0 20 055 |  | True direction from which CM clouds are moving DM | Degree true, 0 |
|  | 0 20 056 |  | True direction from which CH clouds are moving DH | Degree true, 0 |
|  |  |  | Direction and elevation of cloud gr. 57CDaeC |  |
| 3 02 048 | 0 05 021 |  | Bearing or azimuth Da | Degree true, 2 |
|  | 0 07 021 |  | Elevation eC | Degree, 2 |
|  | 0 20 012 |  | Cloud type C | Code table, 0 |
|  | 0 05 021 |  | Bearing or azimuth (set to missing to cancel the previous value) | Degree true, 2 |
|  | 0 07 021 |  | Elevation (set to missing to cancel the previous value) | Degree, 2 |
|  |  |  | State of ground, snow depth, ground minimum temperature |  |
| 3 02 037 | 0 20 062 |  | State of ground (with or without snow) E or E’ | Code table, 0 |
|  | 0 13 013 |  | Total snow depth sss | m, 2 |
|  | 0 12 113 |  | Ground minimum temperature (scale2), past 12 hours snTgTg | K, 2 |
| 3 02 043 |  |  | Basic synoptic “period” data |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Sunshine data |  |
|  | 3 02 039 | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 14 031 | Total sunshine SSS | Minute, 0 |
|  |  |  | Precipitation measurement |  |
|  | 3 02 040 | 0 07 032 | Height of sensor above local ground (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 3 02 041 | 0 07 032 | Height of sensor above local ground (for temperature measurement) | m, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 042 | 0 07 032 | Height of sensor above local ground (for wind measurement) | m, 2 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 0 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 0 |
|  | 0 07 032 |  | Height of sensor above local ground (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Evaporation data |  |
| 3 02 044 | 0 04 024 |  | Time period in hours | Hour, 0 |
|  | 0 02 004 |  | Type of instrument for evaporation or crop type for evapotranspiration iE | Code table, 0 |
|  | 0 13 033 |  | Evaporation /evapotranspiration EEE | kg m-2, 1 |
|  |  |  | Radiation data |  |
| 3 02 045 | 0 04 025 |  | Time period in minutes | Minute, 0 |
|  | 0 14 002 |  | Long-wave radiation, integrated over period specified 553SS 4FFFF or 553SS 5FFFF | J m-2, -3 |
|  | 0 14 004 |  | Short-wave radiation, integrated over period specified 553SS 6FFFF | J m-2, -3 |
|  | 0 14 016 |  | Net radiation, integrated over period specified 553SS 0FFFF or 553SS 1FFFF | J m-2, -4 |
|  | 0 14 028 |  | Global solar radiation (high accuracy), integrated over period specified 553SS 2FFFF | J m-2, -4 |
|  | 0 14 029 |  | Diffuse solar radiation (high accuracy), integrated over period specified 553SS 3FFFF | J m-2, -4 |
|  | 0 14 030 |  | Direct solar radiation (high accuracy), integrated over period specified 55408 4FFFF | J m-2, -4 |
| 3 02 046 |  |  | Temperature change group 54g0sndT |  |
|  | 0 04 024 |  | Time period or displacement | Hour, 0 |
|  | 0 04 024 |  | Time period or displacement (see Note 3) | Hour, 0 |
|  | 0 12 049 |  | Temperature change over period specified sndT | K, 0 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)        	Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)           To construct the required time range, descriptor 004024 has to be included two times.

BUFR TEMPLATE FOR  SYNOP MOBIL DATA

BUFR template for SYNOP MOBIL is similar to the BUFR template for SYNOP.  The only difference between them is in the very first sequence descriptor; in case of representation of SYNOP MOBIL data, the station identification, time, horizontal and vertical coordinates is provided by a newly proposed sequence descriptor 3 02 092:

| 3 01 092 |  |  | Mobile surface station identification, time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 0 01 011 |  | Mobile land station identifier D….D | CCITT IA5, 0 |
|  | 0 01 003 |  | WMO Region number A1 | Code table, 0 |
|  | 0 02 001 |  | Type of station (ix) | Code table, 0 |
|  | 3 01 011 | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  | 3 01 012 | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  | 3 01 021 | 0 05 001 | Latitude (high accuracy) LaLaLa | Degree, 5 |
|  |  | 0 06 001 | Longitude (high accuracy) LoLoLoLo | Degree, 5 |
|  | 0 07 030 |  | Height of station ground above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  | 0 33 024 |  | Station elevation quality mark im | Code table, 0 |

The rest of the template is identical with the BUFR template for SYNOP data, including the Notes below the template for SYNOP data.

BUFR TEMPLATE FOR SHIP DATA

| 3 01 093 |  |  | Ship identification, movement, type, date/time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 036 | 0 01 011 | Ship or mobile land station identifier D….D | CCITT IA5, 0 |
|  |  | 0 01 012 | Direction of motion of moving observing platform(3) Ds | Degree true, 0 |
|  |  | 0 01 013 | Speed of motion of moving observing platform(4) vs | m s-1, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  |  | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  |  | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  |  | 0 05 002 | Latitude (coarse accuracy) LaLaLa | Degree, 2 |
|  |  | 0 06 002 | Longitude (coarse accuracy) LoLoLoLo | Degree, 2 |
|  | 0 07 030 |  | Height of station platform above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
|  |  |  | Pressure data |  |
| 3 02 001 | 0 10 004 |  | Pressure P0P0P0P0 | Pa, –1 |
|  | 0 10 051 |  | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  | 0 10 061 |  | 3-hour pressure change ppp | Pa, –1 |
|  | 0 10 063 |  | Characteristic of pressure tendency a | Code table, 0 |
| 3 02 054 |  |  | SHIP “instantaneous” data |  |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 052 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 053 | 0 07 032 | Height of sensor above marine deck platform (for visibility measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for visibility measurement) | m, 1 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  | 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 3 02 034 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
| 0 08 002 |  |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Icing and ice |  |
| 3 02 055 | 0 20 031 |  | Ice deposit (thickness) EsEs | m, 2 |
|  | 0 20 032 |  | Rate of ice accretion Rs | Code table, 0 |
|  | 0 20 033 |  | Cause of ice accretion Is | Flag table, 0 |
|  | 0 20 034 |  | Sea ice concentration ci | Code table, 0 |
|  | 0 20 035 |  | Amount and type of ice bi | Code table, 0 |
|  | 0 20 036 |  | Ice situation zi | Code table, 0 |
|  | 0 20 037 |  | Ice development Si | Code table, 0 |
|  | 0 20 038 |  | Bearing of ice edge Di | Degree true, 0 |
| 3 02 057 |  |  | SHIP marine data |  |
|  |  |  | Sea/water temperature |  |
|  | 3 02 056 | 0 02 038 | Method of sea surface temperature measurement | Code table, 0 |
|  |  | 0 22 043 | Sea/water temperature ssTwTwTw | K, 2 |
|  |  |  | Waves |  |
|  | 3 02 021 | 0 22 001 | Direction of waves | Degree true |
|  |  | 0 22 011 | Period of waves PwaPwa | s, 0 |
|  |  | 0 22 021 | Height of waves HwaHwa | m, 1 |
|  | 3 02 024 | 0 22 002 | Direction of wind waves | Degree true, 0 |
|  |  | 0 22 012 | Period of wind waves PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves HwHw | m, 1 |
|  |  | 1 01 002 | Replicate 1 descriptor 2 times |  |
|  |  | 3 02 023 | Swell waves (2 systems of swell) dw1dw1, Pw1Pw1, Hw1Hw1 dw2dw2, Pw2Pw2, Hw2Hw2 |  |
| 3 02 060 |  |  | SHIP“period” data |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Precipitation measurement |  |
|  | 3 02 040 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 3 02 058 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  |  | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 059 | 0 07 032 | Height of sensor above marine deck platform (for wind measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for wind measurement) | m, 1 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 0 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 002 | Replicate next 3 descriptors 2 times |  |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 0 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)        	Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)           0 01 012: Means course made good (average course over the ground) during the three hours preceding the time of observation.

4)         0 01 013: Means speed made good (average speed over the ground) during the three hours preceding the time of observation.

5)          If “plain language” text is reported within Section 2, this information can be conveyed in BUFR via the use of an appropriate 205YYY field as an extra descriptor following the above basic template.

BUFR TEMPLATE FOR SHIP DATA FROM VOS STATIONS …… 3 07 070

3 07 070  =  3 01 093  +  3 02 062   +  3 02 063

| 3 01 093 |  |  | Ship identification, movement, type, date/time, horizontal and vertical coordinates | Unit, scale |
| --- | --- | --- | --- | --- |
|  | 3 01 036 | 0 01 011 | Ship or mobile land station identifier D….D | CCITT IA5, 0 |
|  |  | 0 01 012 | Direction of motion of moving observing platform(3) Ds | Degree true, 0 |
|  |  | 0 01 013 | Speed of motion of moving observing platform(4) vs | m s-1, 0 |
|  |  | 0 02 001 | Type of station (ix) | Code table, 0 |
|  |  | 0 04 001 | Year | Year, 0 |
|  |  | 0 04 002 | Month | Month, 0 |
|  |  | 0 04 003 | Day YY | Day, 0 |
|  |  | 0 04 004 | Hour GG | Hour, 0 |
|  |  | 0 04 005 | Minute gg | Minute, 0 |
|  |  | 0 05 002 | Latitude (coarse accuracy) LaLaLa | Degree, 2 |
|  |  | 0 06 002 | Longitude (coarse accuracy) LoLoLoLo | Degree, 2 |
|  | 0 07 030 |  | Height of station platform above mean sea level | m, 1 |
|  | 0 07 031 |  | Height of barometer above mean sea level | m, 1 |
| 3 02 062 |  |  | SHIP “instantaneous” data from VOS |  |
|  |  |  | Pressure data |  |
|  | 3 02 001 | 0 10 004 | Pressure P0P0P0P0 | Pa, –1 |
|  |  | 0 10 051 | Pressure reduced to mean sea level PPPP | Pa, –1 |
|  |  | 0 10 061 | 3-hour pressure change ppp | Pa, –1 |
|  |  | 0 10 063 | Characteristic of pressure tendency a | Code table, 0 |
|  |  |  | Temperature and humidity data |  |
|  | 3 02 052 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 12 101 | Temperature/dry-bulb temperature(sc.2) snTTT | K, 2 |
|  |  | 0 02 039 | Method of wet-bulb temperature measurement | Code table, 0 |
|  |  | 0 12 102 | Wet-bulb temperature (scale 2) swTbTbTb | K, 2 |
|  |  | 0 12 103 | Dew-point temperature (scale 2) snTdTdTd | K, 2 |
|  |  | 0 13 003 | Relative humidity | %, 0 |
|  |  |  | Visibility data |  |
|  | 3 02 053 | 0 07 032 | Height of sensor above marine deck platform (for visibility measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for visibility measurement) | m, 1 |
|  |  | 0 20 001 | Horizontal visibility VV | m, –1 |
|  | 0 07 033 |  | Height of sensor above water surface (set to missing to cancel the previous value) | m, 1 |
|  |  |  | Precipitation past 24 hours |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 034 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 0 13 023 | Total precipitation past 24 hours R24R24R24R24 | kg m-2, 1 |
|  | 0 07 032 |  | Height of sensor above marine deck platform (set to missing to cancel the previous value) | m, 2 |
|  |  |  | Cloud data |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 004 | 0 20 010 | Cloud cover (total) N | %, 0 |
|  |  | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (of low or middle clouds) Nh | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud h | m, –1 |
|  |  | 0 20 012 | Cloud type (low clouds CL) CL | Code table, 0 |
|  |  | 0 20 012 | Cloud type (middle clouds CM) CM | Code table, 0 |
|  |  | 0 20 012 | Cloud type (high clouds CH) CH | Code table, 0 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 001 |  | Delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 005 | 0 08 002 | Vertical significance | Code table, 0 |
|  |  | 0 20 011 | Cloud amount (Ns) Ns | Code table, 0 |
|  |  | 0 20 012 | Cloud type (C) C | Code table, 0 |
|  |  | 0 20 013 | Height of base of cloud (hshs) hshs | m, -1 |
|  | 0 08 002 |  | Vertical significance (set to missing to cancel the previous value) | Code table, 0 |
|  |  |  | Icing and ice |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 055 | 0 20 031 | Ice deposit (thickness) EsEs | m, 2 |
|  |  | 0 20 032 | Rate of ice accretion Rs | Code table, 0 |
|  |  | 0 20 033 | Cause of ice accretion Is | Flag table, 0 |
|  |  | 0 20 034 | Sea ice concentration ci | Code table, 0 |
|  |  | 0 20 035 | Amount and type of ice bi | Code table, 0 |
|  |  | 0 20 036 | Ice situation zi | Code table, 0 |
|  |  | 0 20 037 | Ice development Si | Code table, 0 |
|  |  | 0 20 038 | Bearing of ice edge Di | Degree true, 0 |
|  |  |  | Sea/water temperature |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 056 | 0 02 038 | Method of sea surface temperature measurement | Code table, 0 |
|  |  | 0 22 043 | Sea/water temperature ssTwTwTw | K, 2 |
|  |  |  | Waves |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 021 | 0 22 001 | Direction of waves | Degree true, 0 |
|  |  | 0 22 011 | Period of waves PwaPwa | s, 0 |
|  |  | 0 22 021 | Height of waves HwaHwa | m, 1 |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 024 | 0 22 002 | Direction of wind waves | Degree true, 0 |
|  |  | 0 22 012 | Period of wind waves PwPw | s, 0 |
|  |  | 0 22 022 | Height of wind waves HwHw | m, 1 |
|  |  | 1 01 002 | Replicate 1 descriptor 2 times |  |
|  |  | 3 02 023 | Swell waves (2 systems of swell) dw1dw1, Pw1Pw1, Hw1Hw1 dw2dw2, Pw2Pw2, Hw2Hw2 |  |
| 3 02 063 |  |  | SHIP“period” data from VOS |  |
|  |  |  | Present and past weather |  |
|  | 3 02 038 | 0 20 003 | Present weather ww | Code table, 0 |
|  |  | 0 04 024 | Time period in hours | Hour, 0 |
|  |  | 0 20 004 | Past weather (1) W1 | Code table, 0 |
|  |  | 0 20 005 | Past weather (2) W2 | Code table, 0 |
|  |  |  | Precipitation measurement |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 040 | 0 07 032 | Height of sensor above marine deck platform (for precipitation measurement) | m, 2 |
|  |  | 1 02 002 | Replicate next 2 descriptors 2 times |  |
|  |  | 0 04 024 | Time period in hours tR | Hour, 0 |
|  |  | 0 13 011 | Total precipitation / total water equivalent of snow RRR | kg m-2, 1 |
|  |  |  | Extreme temperature data |  |
|  | 1 01 000 |  | Delayed replication of 1 descriptor |  |
|  | 0 31 000 |  | Short delayed descriptor replication factor | Numeric, 0 |
|  | 3 02 058 | 0 07 032 | Height of sensor above marine deck platform (for temperature measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for temperature measurement) | m, 1 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  | 0 04 024 | Time period or displacement (see Notes 1 and 2) | Hour, 0 |
|  |  | 0 12 111 | Maximum temperature (scale 2) at height and over period specified snTxTxTx | K, 2 |
|  |  | 0 04 024 | Time period or displacement | Hour, 0 |
|  |  |  | Time period or displacement (see Note 2) | Hour, 0 |
|  |  | 0 12 112 | Minimum temperature (scale 2) at height and over period specified snTnTnTn | K, 2 |
|  |  |  | Wind data |  |
|  | 3 02 059 | 0 07 032 | Height of sensor above marine deck platform (for wind measurement) | m, 2 |
|  |  | 0 07 033 | Height of sensor above water surface (for wind measurement) | m, 1 |
|  |  | 0 02 002 | Type of instrumentation for wind measurement iw | Flag table, 0 |
|  |  | 0 08 021 | Time significance (= 2 (time averaged)) | Code table, 0 |
|  |  | 0 04 025 | Time period (= - 10 minutes, or number of minutes after a significant change of wind) | Minute, 0 |
|  |  | 0 11 001 | Wind direction dd | Degree true, 0 |
|  |  | 0 11 002 | Wind speed ff | m s-1, 0 |
|  |  | 0 08 021 | Time significance (= missing value) | Code table, 0 |
|  |  | 1 03 000 | Delayed replication of 3 descriptors |  |
|  |  | 0 31 001 | Delayed descriptor replication factor | Numeric, 0 |
|  |  | 0 04 025 | Time period in minutes | Minute, 0 |
|  |  | 0 11 043 | Maximum wind gust direction | Degree true, 0 |
|  |  | 0 11 041 | Maximum wind gust speed 910fmfm, 911fxfx | m s-1, 0 |

Notes:

1)	Within RA-IV, the maximum temperature at 1200 UTC is reported for the previous calendar day (i.e. the ending time of the period is not equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

2)        	Within RA-III, the maximum day-time temperature and the minimum night-time temperature is reported (i.e. the ending time of the period may not be equal to the nominal time of the report). To construct the required time range, descriptor 004024 has to be included two times. If the period ends at the nominal time of the report, value of the second 004024 shall be set to 0.

3)          0 01 012: Means course made good (average course over the ground) during the three hours preceding the time of observation.

4)         0 01 013: Means speed made good (average speed over the ground) during the three hours preceding the time of observation.

5)          If “plain language” text is reported within Section 2, this information can be conveyed in BUFR via the use of an appropriate 205YYY field as an extra descriptor following the above basic template.