| WORLD METEOROLOGICAL ORGANIZATION ________________ COMMISSION FOR BASIC SYSTEMS MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES KUALA LUMPUR, MALAYSIA, 21 - 26 JUNE 2004 |  | ET/DR&C/Doc. 6.2(1) _______ ENGLISH only |
| --- | --- | --- |

Encoding TAF into BUFR

Draft created by Charles Sanders (Australia)

________________________________________________________________

Summary and Purpose of Document

This document is a first draft of a template to encode TAF into BUFR.

________________________________________________________________

ACTION PROPOSED

The meeting is requested to review the document and note the

information therein.

Discussion

It should be possible to combine most of the TAF forecast with the TREND part of a METAR or SPECI.  Unfortunately, it appears that the METAR TREND forecast table D entry and the METAR full sequence are in error as they do not include forecast cloud changes within the trend, and do not allow for multiple trends, as could be required for a METAR such as

METAR YUDO 182200Z 12005KT 9999 SCT009 08/07 Q1023

FM2230 BKN009 FM2330 SCT015=

This, together with the absence of provision for probability, makes the existing METAR/SPECI trend sequence 3 07 018 unsuitable for TAF.

The current METAR/SPECI descriptors include

|  |  |  |  |  |  | (Trend-type landing forecast) |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3 | 07 | 018 | 0 | 08 | 016 | Change qualifier of a trend-type | TTTTT |
|  |  |  |  |  |  | forecast or an aerodrome forecast |  |
|  |  |  | 1 | 02 | 000 | Delayed replication of 2 descriptors |  |
|  |  |  | 0 | 31 | 001 | Number of replication (up to 2) |  |
|  |  |  | 0 | 08 | 017 | Qualifier of the time when the forecast | TT |
|  |  |  |  |  |  | change is expected (FM, TL, AT) |  |
|  |  |  | 3 | 01 | 012 | GG, gg |  |
|  |  |  | 1 | 04 | 000 | Delayed replication of 4 descriptor |  |
|  |  |  | 0 | 31 | 001 | Number of replication (up to 1) |  |
|  |  |  | 0 | 07 | 006 | Height above station |  |
|  |  |  | 0 | 11 | 001 | Wind direction | ddd |
|  |  |  | 0 | 11 | 002 | Wind speed | ff |
|  |  |  | 0 | 11 | 041 | Maximum wind speed (gusts) | fmfm |
|  |  |  | 0 | 20 | 009 | General Weather Indicator |  |
|  |  |  | 1 | 01 | 000 | Delayed replication of 1 descriptor |  |
|  |  |  | 0 | 31 | 001 | Number of replication (up to 1) |  |
|  |  |  | 0 | 20 | 001 | Horizontal visibility | VVVV |
|  |  |  | 3 | 07 | 014 | W´w´ |  |
|  |  |  |  |  |  | (Total sequence for representation of METAR/SPECI code in BUFR) |
| 3 | 07 | 021 | 3 | 07 | 011 | Main part of data |  |
|  |  |  | 3 | 07 | 012 | DvVVVV |  |
|  |  |  | 3 | 07 | 013 | DRDRVRVRVRVR |  |
|  |  |  | 3 | 07 | 014 | W´w´ |  |
|  |  |  | 3 | 07 | 015 | Clouds group(s) |  |
|  |  |  | 3 | 07 | 016 | REw´w´ |  |
|  |  |  | 3 | 07 | 017 | Wind shear on runway(s) |  |
|  |  |  | 3 | 07 | 018 | Trend-type landing forecast |  |
|  |  |  | 3 | 07 | 015 | Clouds group(s) |  |

Note that the trend cloud groups are NOT included in the trend (3 07 018) but are included in the full sequence (3 07 021), after the trend. I believe that the forecast cloud (3 07 015) should be included in the trend and deleted from the full sequence.  The current sequence only makes provision for one change, so the difference is moot, but more than one change is, as far as I know, permitted.  More than one change is certainly used within Australia, but I am not sure of the situation in other countries.  Because of the longer distances between airports, Australian trend forecasts cover 3 hours instead of the standard 2 hours.  This should not impact on the code nor on the sequence.  It does, however, make the use of two forecast changes within a trend more likely.

The differences between TAF and METAR trend include

- TAF allows PROBnn, METAR does not.

- TAF has times in hours only while METAR has hours and minutes.

Comparing the TAF specification from ICAO annex 3 in Doc 3.3(2) with the code form in the codes manual reveals some differences:

- Separate time associated with PROB in the TAF code.  I think this is an error, it would require the time of a PROB30 TEMPO to be repeated twice.

- The TAF specification in the codes manual completely omits the changed weather conditions.

There are many other details that need addressing, including

- Do we devise a sequence for the forecast part of both METAR and TAF and use it in both, requiring some unused (always missing) descriptors, or have separate sequences?

- Do we specify the height of the wind and temperature forecasts above the station level?

- The best way to represent all the different times: it seems that it will be necessary to add a new time significance table B descriptor as the existing one has had nearly all its entries used.

- Although TAF represents most times as whole hours, should we use hours and minutes to improve compatibility with the trend forecast from METAR?

One possible sequence would require the new Table D descriptors:

| F X Y | Reference | Element/Sequence name |  |
| --- | --- | --- | --- |
|  |  | (Aerodrome forecast identification and time interval) |  |
| 3 07 aaa | 0 01 063 | ICAO location identifier | CCCC |
|  | 0 08 ddd | Time significance – issue time |  |
|  | 3 01 011 | Year, month, day | YY |
|  | 3 01 012 | Hour, minute | GGgg |
|  | 0 08 ddd | Time significance – Cancel; Forecast ? |  |
|  | 3 01 011 | Year, month, day (start of forecast) | Y1Y1 |
|  | 0 04 004 | Hour (start of forecast) | G1G1 |
|  | 3 01 011 | Year, month, day (end of forecast) |  |
|  | 0 04 004 | Hour (end of forecast) | G2G2 |
|  | 3 01 024 | Latitude, longitude, height of station |  |
|  |  | (Forecast weather for aerodrome forecast) |  |
| 3 07 bbb | 0 07 006 | Height above station (10m) |  |
|  | 0 11 001 | Wind direction | ddd |
|  | 0 11 002 | Wind speed | ff |
|  | 0 11 041 | Maximum wind speed (gusts) | fmfm |
|  | 0 20 009 | General weather indicator (CAVOK, NSW, NSC) |  |
|  | 0 20 001 | Horizontal visibility | VVVV |
|  | 3 07 014 | Weather | w’w’ |
|  | 3 07 015 | Cloud layer(s) |  |
| 3 07 ccc | 3 07 aaa | Identification and time interval |  |
|  | 3 07 bbb | Forecast |  |
|  | 0 05 000 | Delayed replication of five descriptors |  |
|  | 0 31 001 | Replication factor |  |
|  | 0 xx ggg | Probability of following event occurring | C2C2 |
|  | 0 08 016 | Change qualifier of an aerodrome forecast | TTTTT |
|  | 3 01 012 | Start of time of change | GG or GGgg |
|  | 3 01 012 | End of time of change | GeGe |
|  | 3 07 bbb | Forecast conditions during or after change |  |
|  | 0 07 006 | Height above station (2m) |  |
|  | 0 08 ddd | Time significance (Time of maximum temperature) |  |
|  | 0 04 004 | Hour | GFGF |
|  | 0 12 111 | Maximum temperature | TFTF |
|  | 0 08 ddd | Time significance (Time of minimum temperature) |  |
|  | 0 04 004 | Hour | GFGF |
|  | 0 12 111 | Minimum temperature | TFTF |
|  | 0 08 ddd | Time significance (Cancel) |  |