| WORLD METEOROLOGICAL ORGANIZATION ______________________________ MEETING OF EXPERT TEAM ON DATA REPRESENTATION AND CODES KUALA LUMPUR, MALAYSIA, 21-26 JUNE 2004 |  | ET/DR&C/Doc. 6.4.4(2) (08.VI.2004) ITEM 6.4.4 ENGLISH only |
| --- | --- | --- |

MIGRATION TO TABLE DRIVEN CODE FORMS

Report on Production and Experimental Exchanges

of Observations in BUFR

(submitted by Hansjoerg Brust, DWD)

Summary and purpose of document The document presents the realisation and the results of the BUFR Trial carried out by DWD with KNMI and CMC as test partners for validation of the proposed New BUFR Template for AMDAR.

ACTION PROPOSED

CBS ET DR&C is invited to review the information contained in the document.

___________________

Table of Contents

### 1.	Introductory Comment							3

### 2.	Trial Arrangements							3

- Timetable								4

- New AMDAR Template							4

- Report Documentation							6

5.1	BUFR Trial Lido - DWD						7

5.2	BUFR Trial Lido - DWD - KNMI					11

  - BUFR Trial Lido - DWD - CMC					13

6.	Trial Results								17

  - Lido-DWD								17

  - Lido-DWD-KNMI							19

  - Lido-DWD-CMC							19

### 7.	Conclusions								19

### 8.	Proposal									19

9.	Acknowledgements							19

____________________

References:

[1]	BUFR/CREX Templates to transmit in Table Driven Code Forms, WMO, Geneva, March 2003

[2]	Final Report, Expert Team on Data Representation and Codes (ET/DR&C), Prague, 22 to 26 April 2002

[3]	Guide to WMO Table Driven Code Forms: FM 94 BUFR and FM 95 CREX, Geneva, 1st January 2002

1.	Introductory Comment

The purpose of the WMO BUFR Trial is the validation of the New BUFR Template for AMDAR proposed and approved by the CBS ET on Data Representation and Codes at its meeting in Prague 2002 before being approved by the CBS.

DWD as one of the AMDAR BUFR data providers was asked by the WMO AMDAR Panel on behalf of the CBS ET/DR&C to implement the New BUFR Template and to test it in an operational environment in collaboration with another NWS as a test partner and receiver of the test messages.

KNMI and CMC declared their willingness to participate in the WMO BUFR trial and to act as test partners.

The trial was performed by all participants as a contribution in kind to the work of WMO and the AMDAR Panel in particular.

### Trial Arrangements

The operational Lufthansa (LH) AMDAR data are coded by the LH company Lido from ARINC 620-3 to FM 94 BUFR. Therefore the realisation of the trial was planned in compliance with the recommendations according to ref. [2] chap. 1.3.4 in following steps:

- Development of the new BUFR encoder by Lido and implementation at a separate data processing system parallel to the operational system "MetConcentrator".

- Encoding of operational AMDAR data and transmission both in the currently valid and the new format as BUFR bulletins with the header IUAX01 and IUAX40 to DWD via ISDN link for the subsequent data comparison.

- Transmission of the BUFR bulletins IUAX40 in the new format to the test partners KNMI and CMC via GTS.

- Decoding of the received bulletins by the test partners with independently developed decoders. For this, DWD and CMC used their own developed decoders, while KNMI used the DWD decoder. Since the BUFR data were produced by Lido with its own encoder, DWD could act as test receiver too.

- Re-encoding of the decoded BUFR bulletins by the receivers and transmission to DWD for decoding and comparison with the original data.

In preparation of the BUFR trial the following administrative arrangements were made:

- Specification of the BUFR encoding software according to ref. [1] and [2]. Contract with Lido for development, implementation and test of the new BUFR encoding program.

- Installation of a separate data base for the test and reference BUFR data.

- Licence contract with KNMI for delivering and use of the source code of the DWD de/encoding program.

- Bilateral agreements between the test partners to perform the trial.

- Information about bulletin headers and addressees to the involved GTS centres.

The alphanumeric format FM 95 CREX (unused in DWD) was not part of the trial.

### Timetable

The BUFR trial between Lido, DWD, KNMI and CMC was performed in the period from 25th July to 24th October 2003 in three stages:

BUFR Pre-test  Lido - DWD from 25th July to 19th August 2003

- 26th Jun	Contract DWD - Lido for development and test of the new BUFR encoder

- 25th July	First transmission of BUFR bulletins to DWD via ISDN link to validate the

new encoding program

- 01st Aug	First continuous transmission and faultless decoding of the BUFR bulletins

- 19th Aug	End of the pre-tests.

BUFR Trial  Lido - DWD - KNMI from 03rd September to 24th October 2003

- 07th Aug	Contract DWD - KNMI for use of the DWD BUFR de/encoding program

- 03rd Sep	Implementation and test of the BUFR coding program by KNMI

- 09th Sep	First transmission of operational BUFR bulletins via GTS

- 10th Sep	Receiving and decoding successful. Reports were readable after

implementation of the new code tables

- 17th Sep	Transmission of the re-encoded BUFR data was not possible due to

incompatibilities with the GTS file switch used by KNMI

- 24th Oct	End of the BUFR transmission. Results of the decoded BUFR bulletins

were transmitted to DWD for comparison (see chap. 5 and 6).

BUFR Trial  Lido - DWD - CMC from 06th October to 24th October 2003

- 06th Oct	First transmission of operational BUFR bulletins to CMC via GTS

- 09th Oct	Data successfully decoded in readable format. Re-encoding was not

possible due to unavailability of a suitable encoding program

- 24th Oct	End of the trial. The results in form of a comparison between the test and

the contemporaneous operational AMDAR data for ascent, enroute and descent were transmitted to DWD (see chap. 5 and 6).

4.	New AMDAR Template

The revised new AMDAR Template proposed in ref. [1] and [2] uses in comparison to the current template the descriptors:

- 0 01 023 	Observation Sequence Number

- 0 05 001	Latitude in 10-5 degree, instead 0 05 002 in 10-2 degree

- 0 06 001	Longitude in 10-5 degree, instead 0 06 002 in 10-2 degree

- 0 07 010	Flight Level (reference value -1024) instead 0 07 002 Altitude

- 0 08 009	Detailed Phase of Flight in addition to 0 08 004 Phase of Flight

- 0 12 101	Static Air Temperature in 10-2 K, instead 0 12 001 in 10-1 K

- 0 33 025	ACARS interpolated values.

Furthermore the new AMDAR Template contains descriptors for the Humidity parameters RH and Dew Pt as well as for Turbulence and Airframe Icing, whereas other less used descriptors were dropped.

New AMDAR Template

| Element | FM 94 BUFR DESCRIPTOR (BUFR Table B) | RELATED SEQUENCE DESCRIPTOR(S) (BUFR Table D) | Notes |
| --- | --- | --- | --- |
| Aircraft identification | 0 01 008 |  |  | 1 |
| Sequence number | 0 01 023 |  |  | 2, Table 3 |
| Latitude | 0 05 001 | 3 01 021 |  |  |
| Longitude | 0 06 001 |  |  |  |
| Year | 0 04 001 | 3 01 011 |  |  |
| Month | 0 04 002 |  |  | 4, Table 4 |
| Day | 0 04 003 |  |  |  |
| Hour | 0 04 004 | 3 01 013 |  |  |
| Minute | 0 04 005 |  |  |  |
| Second | 0 04 006 |  | 3 11 005 |  |
| Pressure Altitude (flight level) | 0 07 010 | In 3 11 006 |  | 5, Table 3 |
| Detailed phase of aircraft flight | 0 08 009 |  |  | 3, Table 3 |
| Wind Direction | 0 11 001 |  |  | 6, Table 4 |
|  |  | In 3 11 006 |  |  |
| Wind speed/ Maximum wind | 0 11 002 |  |  |  |
| Degree of turbulence | 0 11 031 |  |  |  |
| Maximum derived equivalent gust speed | 0 11 036 |  |  |  |
| Static air temperature (SAT) | 0 12 101 | In 3 11 006 |  |  |
| ACARS interpolated values | 0 33 025 |  |  |  |
| Phase of flight | 0 08 004 |  |  |  |
| Wind quality/roll angle | 0 02 064 | In 3 11 006 |  | 6, Table 4 |
| Humidity | RH | 0 13 003 |  |  |  |
|  | Dew Pt | 0 12 103 | In 3 11 006 |  | 6, Table 4 |
|  | Mixing ratio | 0 13 002 |  |  |  |
| Turbulence (EDR) | Delayed replication of two descriptors | 1 02 000 |  |  | 7 |
|  | Delayed descriptor replication factor | 0 31 001 |  |  | 7 |
|  | Intensity (EDR) | 0 11 075 |  |  |  |
|  | Peak(EDR) | 0 11 076 |  |  |  |
|  | Turbulence index (EDR) | 0 11 037 |  |  |  |
|  | Extended time of occurrence of peak EDR | 0 11 039 |  |  | 8, Table 3 |
|  | EDR reporting interval | 0 11 077 |  |  | 9, Table 3 |
| Airframe Icing | Ice/no ice | 0 20 042 |  |  | 10, Table 3 |
|  | Peak liquid water content | 0 20 043 |  |  | 11, Table 3 |
|  | Average liquid water content | 0 20 044 |  |  | 11, Table 3 |
|  | Supercooled water droplet conditions | 0 20 045 |  |  | 11, Table 3 |

For further explanation please see the notes to Table 2, BUFR Table B and the corresponding Code Tables according to ref. [1] and [2].

5.	Report Documentation

In the period from 1st August until 24th October 2003 (chap. 3) about 12,500 operational test reports per day were continuously sent to the trial partners.

As indicated before it wasn't possible for the trial partners to re-encode the messages after successful decoding due to technical reasons, not due to formatting problems. Therefore examples of the decoded reports were re-transmitted to DWD and compared with the contemporaneous operational reports:

- IUAX40	AMDAR Test Reports generated from the same data source as IUAX01, encoded by Lido (LH) according to the new AMDAR template, sent to DWD by ISDN data link and forwarded to the trial partners KNMI and CMC via GTS.

- IUAX01	Operational AMDAR Reports as reference encoded by Lido according to the currently valid AMDAR template, sent to DWD and forwarded to E-ADAS (E-AMDAR Data Acquisition System, Met Office) by GTS for dissemination with the header IUAg01 EGRR to all AMDAR data users.

In conformity with the BUFR rules the parameters Humidity, Turbulence and Airframe Icing are not included in the test reports IUAX40, since these parameters are not transmitted by ARINC 620-3 from the Lufthansa fleet. There is no difficulty to transmit them as soon as they are available, since the corresponding descriptors are included in the coding program.

For documentation the re-transmitted AMDAR test reports IUAX40 decoded from the trial partners are listed together with the contemporaneous operational reports IUAX01 in the following, each report showing the

- expanded BUFR description (without BUFR section 0 - 2)

- data section with one example for an ascent, enroute and descent report.

The BUFR description of the reference report IUAX01 is shortened by the descriptor sequence 3 11 004 "ACARS supplemental reported values", which is not transmitted.

Since the BUFR data were produced by Lido with its own independently developed encoder, DWD acted as test receiver too. Apart from automatic format monitoring about 100 BUFR reports were individually verified in spot tests.

This chapter shows examples of the used operational AMDAR test and reference reports. The immediate comparison of the trial results is shown in chapter 6.

5.1	BUFR Trial Lido - DWD

IUAX40 	Expanded BUFR Description

0	311005 	311005   	Sequence: STANDARD AMDAR REPORT

1 	001008 	|  YAIRN    	AIRCRAFT REGISTRATION NUMBER 	CCITT IA5    	64 bits

2 	001023 	|  NOSNO    	OBSERVATION SEQUENCE NUMBER                 	NUMERIC       	9 bits

3 	301021 	|  301021   	Sequence: LATITUDE/LONGITUDE

4 	005001 	|  |  MLAH 	LATITUDE (HIGH ACCURACY)                 	DEGREE       	25 bits 10**-5

5 	006001 	|  |  MLOH	LONGITUDE (HIGH ACCURACY)                	DEGREE       	26 bits 10**-5

6        	|  +->End Seq	End Sequence

7 	301011 	|  301011   	Sequence: DATE

8 	004001 	|  |  MJJJ     	YEAR                                     	YEAR         	12 bits

9 	004002 	|  |  MMM   	MONTH                                    	MONTH         	4 bits

10 	004003 	|  |  MYY     	DAY                                      	DAY          	6 bits

11        	|  +->End Seq	End Sequence

12 	301013 	|  301013   	Sequence: HOUR/MINUTE/SECOND

13 	004004 	|  |  MGG      	HOUR                                     	HOUR          	5 bits

14	004005 	|  |  NGG      	MINUTE                                   	MINUTE        	6 bits

15 	004006 	|  |  MSEC	SECOND                                   	SECOND        	6 bits

16        	|  +->End Seq 	End Sequence

17 	007010 	|  NFLEV	FLIGHT LEVEL                                	M            	16 bits

18 	008009 	|  NDEPF    	DETAILED PHASE OF FLIGHT                    	CODE TABLE    	4 bits

19 	011001 	|  NDNDN    	WIND DIRECTION                              	DEGREE TRUE   	9 bits

20 	011002 	|  NFNFN    	WIND SPEED                                  	M/S          	12 bits 10**-1

21 	011031 	|  MB       	DEGREE OF TURBULENCE                        	CODE TABLE    	4 bits

22 	011036 	|  NMDEWX	MAXIMUM DERIVED EQUIVALENT VERTICAL GUST    	M/S          	10 bits 10**-1

23 	311205 	|  311205 	Sequence: STANDARD AMDAR REPORT, PART 2

24 	012101 	|  |  MTDBT 	TEMPERATURE/DRY BULB TEMPERATURE         	K            	16 bits 10**-2

25 	033025 	|  |  MAIV  	ACARS INTERPOLATED VALUES                	CODE TABLE    	3 bits

26        	|  +->End Seq	End Sequence

27        	+->End Seq  	End Sequence

28	008004 	MPHAI   	PHASE OF AIRCRAFT FLIGHT                       	CODE TABLE    	3 bits

29 	002064 	MQARA   	AIRCRAFT ROLL ANGLE QUALITY                    	CODE TABLE    	2 bits

IUAX40 	ASC Report 		24th Oct 2003	05:12 UTC

311005  	Sequence: STANDARD AMDAR REPORT                                        		-1000000000

YAIRN   	AIRCRAFT REGISTRATION NUMBER                              	CCITT IA5         	EU5891

NOSNO   	OBSERVATION SEQUENCE NUMBER                               	NUMERIC      	-1000000000

301021  	Sequence: LATITUDE/LONGITUDE                                           		-1000000000

MLAH    	LATITUDE (HIGH ACCURACY)                           	10**-5 DEGREE	5764833

MLOH    	LONGITUDE (HIGH ACCURACY)                          	10**-5 DEGREE	1226666

End Seq 	End Sequence                                                           		-1000000000

301011  	Sequence: DATE                                                         		-1000000000

MJJJ    	YEAR                                                      	YEAR                	2003

MMM     	MONTH                                                     	MONTH                 	10

MYY     	DAY                                                       	DAY                   	24

End Seq 	End Sequence                                                           		-1000000000

301013  	Sequence: HOUR/MINUTE/SECOND                                           		-1000000000

MGG     	HOUR                                                      	HOUR                   	5

NGG     	MINUTE                                                    	MINUTE                	12

MSEC    	SECOND                                                    	SECOND       	-1000000000

End Seq 	End Sequence                                                           		-1000000000

NFLEV   	FLIGHT LEVEL                                              	M                    	430

NDEPF   	DETAILED PHASE OF FLIGHT                                  	CODE TABLE	7

NDNDN   	WIND DIRECTION                                            	DEGREE TRUE	262

NFNFN   	WIND SPEED                                         	10**-1 M/S 	36

MB      	DEGREE OF TURBULENCE                                      	CODE TABLE	-1000000000

NMDEWX  	MAXIMUM DERIVED EQUIVALENT VERTICAL GUST           	10**-1 M/S	-1000000000

311205  	Sequence: STANDARD AMDAR REPORT, PART 2                                		-1000000000

MTDBT   	TEMPERATURE/DRY BULB TEMPERATURE                   	10**-2 K       	27165

MAIV    	ACARS INTERPOLATED VALUES                                 	CODE TABLE  	1

End Seq 	End Sequence                                                           		-1000000000

End Seq 	End Sequence                                                           		-1000000000

MPHAI   	PHASE OF AIRCRAFT FLIGHT                                  	CODE TABLE 	5

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                               	CODE TABLE   	0

IUAX40 	ENR Report 		24th Oct 2003	05:28 UTC

311005  	Sequence: STANDARD AMDAR REPORT                              		-1000000000

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU0601

NOSNO   	OBSERVATION SEQUENCE NUMBER                     	NUMERIC      	-1000000000

301021  	Sequence: LATITUDE/LONGITUDE                                 		-1000000000

MLAH    	LATITUDE (HIGH ACCURACY)                 	10**-5 DEGREE 	4889166

MLOH    	LONGITUDE (HIGH ACCURACY)                	10**-5 DEGREE    	1061111

End Seq 	End Sequence                                                 		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                 	10

MYY     	DAY                                             	DAY                   	24

End Seq 	End Sequence                                                 		-1000000000

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                   	5

NGG     	MINUTE                                          	MINUTE                	28

MSEC    	SECOND                                          	SECOND       	-1000000000

End Seq 	End Sequence                                                 		-1000000000

NFLEV   	FLIGHT LEVEL                                    	M                   	6437

NDEPF   	DETAILED PHASE OF FLIGHT                        	CODE TABLE     	3

NDNDN   	WIND DIRECTION                                  	DEGREE TRUE    	289

NFNFN   	WIND SPEED                               	10**-1 M/S            	72

MB      	DEGREE OF TURBULENCE                            	CODE TABLE   	-1000000000

NMDEWX  	MAXIMUM DERIVED EQUIVALENT VERTICAL GUST 	10**-1 M/S          	-1000000000

311205  	Sequence: STANDARD AMDAR REPORT, PART 2                      		-1000000000

MTDBT   	TEMPERATURE/DRY BULB TEMPERATURE         	10**-2 K                  23715

MAIV    	ACARS INTERPOLATED VALUES                       	CODE TABLE      	3

End Seq 	End Sequence                                                 		-1000000000

End Seq 	End Sequence                                                 		-1000000000

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE     	3

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE      	0

IUAX40	DES Report		24th Oct 2003	05:25 UTC

311005  	Sequence: STANDARD AMDAR REPORT                              		-1000000000

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU4623

NOSNO   	OBSERVATION SEQUENCE NUMBER                     	NUMERIC      	-1000000000

301021  	Sequence: LATITUDE/LONGITUDE                                 		-1000000000

MLAH    	LATITUDE (HIGH ACCURACY)                 	10**-5 DEGREE  	5293500

MLOH    	LONGITUDE (HIGH ACCURACY)                	10**-5 DEGREE    	923166

End Seq 	End Sequence                                                 		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                 	10

MYY     	DAY                                             	DAY                   	24

End Seq 	End Sequence                                                 		-1000000000

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                   	5

NGG     	MINUTE                                          	MINUTE                	25

MSEC    	SECOND                                          	SECOND       	-1000000000

End Seq 	End Sequence                                                 		-1000000000

NFLEV   	FLIGHT LEVEL                                    	M                   	1622

NDEPF   	DETAILED PHASE OF FLIGHT                        	CODE TABLE        	11

NDNDN   	WIND DIRECTION                                  	DEGREE TRUE    	357

NFNFN   	WIND SPEED                               	10**-1 M/S            	57

MB      	DEGREE OF TURBULENCE                            	CODE TABLE   	-1000000000

NMDEWX  	MAXIMUM DERIVED EQUIVALENT VERTICAL GUST 	10**-1 M/S          	-1000000000

311205  	Sequence: STANDARD AMDAR REPORT, PART 2                      		-1000000000

MTDBT   	TEMPERATURE/DRY BULB TEMPERATURE         	10**-2 K                  26595

MAIV    	ACARS INTERPOLATED VALUES                       	CODE TABLE    	3

End Seq 	End Sequence                                                 		-1000000000

End Seq 	End Sequence                                                 		-1000000000

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE    	6

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE     	0

IUAX01		Expanded BUFR Description

0 	311002 	311002		Sequence: SINGLE LEVEL REPORT: ACARS REP

1 	301065 	|  301065   	Sequence: ACARS IDENTIFICATION

2 	001006 	|  |  YXXNN    	AIRCRAFT FLIGHT NUMBER                   		CCITT IA5    	64 bits

3 	001008 	|  |  YAIRN    	AIRCRAFT REGISTRATION NUMBER             		CCITT IA5    	64 bits

4 	002001 	|  |  NIX      	TYPE OF STATION                          		CODE TABLE    	2 bits

5 	002002 	|  |  NIW      	TYPE OF INSTRUMENT FOR WIND MEASUREMENT	FLAG TABLE    	4 bits

6 	002005 	|  |  MPOTO    	PRECISION OF TEMPERATURE OBSERVATION     	K             		7 bits 10**-2

7 	002062 	|  |  NADRS    	TYPE OF AIRCRAFT DATA RELAY SYSTEM       	CODE TABLE    	4 bits

8 	002070 	|  |  NOSLL    	ORIGINAL SPECIF. OF LATITUDE/LONGITUDE   	CODE TABLE    	4 bits

9 	002065 	|  |  YAGRS    	ACARS GROUND RECEIVING STATION           	CCITT IA5    	40 bits

10       		|  +->End Seq  	End Sequence

11 	301066 	|  301066   	Sequence: ACARS LOCATION

12 	301011 	|  |  301011   	Sequence: DATE

13 	004001 	|  |  |  MJJJ     	YEAR                                     		YEAR         	12 bits

14 	004002 	|  |  |  MMM      	MONTH                                    		MONTH         	4 bits

15 	004003 	|  |  |  MYY      	DAY                                      		DAY           	6 bits

16  			|  |  +->End Seq 	End Sequence

17 	301013 	|  |  301013   	Sequence: HOUR/MINUTE/SECOND

18 	004004 	|  |  |  MGG      	HOUR                                     		HOUR          	5 bits

19 	004005 	|  |  |  NGG      	MINUTE                                   		MINUTE        	6 bits

20 	004006 	|  |  |  MSEC     	SECOND                                   		SECOND        	6 bits

21  			|  |  +->End Seq 	End Sequence

22 	301023 	|  |  301023   	Sequence: LATITUDE/LONGITUDE, COARSE ACC

23 	005002 	|  |  |  MLALA    	LATITUDE (COARSE ACCURACY)               		DEGREE       	15 bits 10**-2

24 	006002 	|  |  |  MLOLO    	LONGITUDE (COARSE ACCURACY)              		DEGREE       	16 bits 10**-2

25  	      		|  |  +->End Seq 	End Sequence

26 	007004 	|  |  MPN      	PRESSURE (VERT.LOCATION)                 		PA           		14 bits 10** 1

27 	002064 	|  |  MQARA    	AIRCRAFT ROLL ANGLE QUALITY              		CODE TABLE    	2 bits

28 	008004 	|  |  MPHAI    	PHASE OF AIRCRAFT FLIGHT                 		CODE TABLE    	3 bits

29        		|  +->End Seq  	End Sequence

30 	311003 	|  311003  	Sequence: ACARS STANDARD REPORTED VARIAB

31 	010070 	|  |  MIAA     	INDICATED AIRCRAFT ALTITUDE              		M 		16 bits

32 	011001 	|  |  NDNDN    	WIND DIRECTION                           		DEGREE TRUE   	9 bits

33 	011002 	|  |  NFNFN    	WIND SPEED                               		M/S          	12 bits 10**-1

34 	012001 	|  |  MTN      	TEMPERATURE/DRY BULB TEMPERATURE         	K  		12 bits 10**-1

35 	013002 	|  |  MMIXR    	MIXING RATIO                             		KG/KG        	14 bits 10**-5

36        		|  +->End Seq  	End Sequence

71        		+->End Seq  	End Sequence

IUAX01	ASC Reference Report 	24th Oct 2003	05:12 UTC

311002  	Sequence: SINGLE LEVEL REPORT: ACARS REP                     		-1000000000

301065  	Sequence: ACARS IDENTIFICATION                               		-1000000000

YXXNN   	AIRCRAFT FLIGHT NUMBER                          	CCITT IA5   	LH3011

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU5891

NIX     	TYPE OF STATION                                 	CODE TABLE      	0

NIW     	TYPE OF INSTRUMENT.FOR WIND MEASUREMENT         	FLAG TABLE    	4

MPOTO   	PRECISION OF TEMPERATURE OBSERVATION     	10**-2 K    	10

NADRS   	TYPE OF AIRCRAFT DATA RELAY SYSTEM              	CODE TABLE     	3

NOSLL   	ORIGINAL SPECIF. OF LATITUDE/LONGITUDE          	CODE TABLE        	0

YAGRS   	ACARS GROUND RECEIVING STATION                  	CCITT IA5    	-1000000000

301066  	Sequence: ACARS LOCATION                                     		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                 	10

MYY     	DAY                                             	DAY                   	24

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                   	5

NGG     	MINUTE                                          	MINUTE                	12

MSEC    	SECOND                                          	SECOND       	-1000000000

301023  	Sequence: LATITUDE/LONGITUDE, COARSE ACC                     		-1000000000

MLALA   	LATITUDE (COARSE ACCURACY)               	10**-2 DEGREE    	5765

MLOLO   	LONGITUDE (COARSE ACCURACY)              	10**-2 DEGREE    	1227

MPN     	PRESSURE (VERT.LOCATION)                 	10** 1 PA           	-1000000000

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE       	0

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE      	5

End Seq 	End Sequence                                                 		-1000000000

311003  	Sequence: ACARS STANDARD REPORTED VARIAB                     		-1000000000

MIAA    	INDICATED AIRCRAFT ALTITUDE                     	M                    	430

NDNDN   	WIND DIRECTION                                  	DEGREE TRUE    	262

NFNFN   	WIND SPEED                               	10**-1 M/S     	36

MTN     	TEMPERATURE/DRY BULB TEMPERATURE         	10**-1 K         	2717

MMIXR   	MIXING RATIO                             	10**-5 KG/KG        	-1000000000

IUAX01	ENR Reference Report	24th Oct 2003	05:28 UTC

311002  	Sequence: SINGLE LEVEL REPORT: ACARS REP                     		-1000000000

301065  	Sequence: ACARS IDENTIFICATION                               		-1000000000

YXXNN   	AIRCRAFT FLIGHT NUMBER                          	CCITT IA5   	LH827

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU0601

NIX     	TYPE OF STATION                                 	CODE TABLE      	0

NIW     	TYPE OF INSTRUMENT.FOR WIND MEASUREMENT         	FLAG TABLE       	4

MPOTO   	PRECISION OF TEMPERATURE OBSERVATION     	10**-2 K               	10

NADRS   	TYPE OF AIRCRAFT DATA RELAY SYSTEM             	CODE TABLE      	3

NOSLL   	ORIGINAL SPECIF. OF LATITUDE/LONGITUDE          	CODE TABLE     	0

YAGRS   	ACARS GROUND RECEIVING STATION                  	CCITT IA5    	-1000000000

301066  	Sequence: ACARS LOCATION                                     		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                 	10

MYY     	DAY                                             	DAY                   	24

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                   	5

NGG     	MINUTE                                          	MINUTE                	28

MSEC    	SECOND                                          	SECOND       	-1000000000

301023  	Sequence: LATITUDE/LONGITUDE, COARSE ACC                     		-1000000000

MLALA   	LATITUDE (COARSE ACCURACY)               	10**-2 DEGREE  	4889

MLOLO   	LONGITUDE (COARSE ACCURACY)              	10**-2 DEGREE   	1061

MPN     	PRESSURE (VERT.LOCATION)                 	10** 1 PA           	-1000000000

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE       	0

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE       	3

311003  	Sequence: ACARS STANDARD REPORTED VARIAB                     		-1000000000

MIAA    	INDICATED AIRCRAFT ALTITUDE                     	M                   	6437

NDNDN   	WIND DIRECTION                                 	DEGREE TRUE    	289

NFNFN   	WIND SPEED                               	10**-1 M/S          	72

MTN     	TEMPERATURE/DRY BULB TEMPERATURE         	10**-1 K         	2372

MMIXR   	MIXING RATIO                             	10**-5 KG/KG        	-1000000000

IUAX01	DES Reference Report 	24th Oct 2003	05:25 UTC

311002  	Sequence: SINGLE LEVEL REPORT: ACARS REP                     		-1000000000

301065  	Sequence: ACARS IDENTIFICATION                               		-1000000000

YXXNN   	AIRCRAFT FLIGHT NUMBER                          	CCITT IA5   	LH182

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU4623

NIX     	TYPE OF STATION                                 	CODE TABLE    	0

NIW     	TYPE OF INSTRUMENT.FOR WIND MEASUREMENT         	FLAG TABLE       	4

MPOTO   	PRECISION OF TEMPERATURE OBSERVATION     	10**-2 K                 	10

NADRS   	TYPE OF AIRCRAFT DATA RELAY SYSTEM              	CODE TABLE        	3

NOSLL   	ORIGINAL SPECIF. OF LATITUDE/LONGITUDE          	CODE TABLE     	0

YAGRS   	ACARS GROUND RECEIVING STATION                  	CCITT IA5    	-1000000000

301066  	Sequence: ACARS LOCATION                                     		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                 	10

MYY     	DAY                                             	DAY                   	24

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                   	5

NGG     	MINUTE                                          	MINUTE                	25

MSEC    	SECOND                                          	SECOND       	-1000000000

301023  	Sequence: LATITUDE/LONGITUDE, COARSE ACC                     		-1000000000

MLALA   	LATITUDE (COARSE ACCURACY)               	10**-2 DEGREE    	5294

MLOLO   	LONGITUDE (COARSE ACCURACY)              	10**-2 DEGREE     	923

MPN     	PRESSURE (VERT.LOCATION)                 	10** 1 PA           	-1000000000

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE     	0

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE      	6

311003  	Sequence: ACARS STANDARD REPORTED VARIAB                     		-1000000000

MIAA    	INDICATED AIRCRAFT ALTITUDE                     	M                   	1622

NDNDN   	WIND DIRECTION                                  	DEGREE TRUE     	357

NFNFN   	WIND SPEED                               	10**-1 M/S       	57

MTN     	TEMPERATURE/DRY BULB TEMPERATURE         	10**-1 K         	2660

MMIXR   	MIXING RATIO                             	10**-5 KG/KG        	-1000000000

5.2	BUFR Trial Lido - DWD - KNMI

IUAX40	Expanded BUFR Description

0 	311005 	311005   	Sequence: STANDARD AMDAR REPORT

1 	001008 	|  001008   	AIRCRAFT REGISTRATION NUMBER            	CCITT_IA5 	64 bits

2 	001023 	|  001023   	OBSERVATION SEQUENCE NUMBER 	NUMERIC	9 bits

3 	301021 	|  301021   	Sequence: LATITUDE/LONGITUDE

4 	005001 	|  |  005001   	LATITUDE (HIGH ACCURACY)       	DEGREE	25 bits 10**-5

5 	006001 	|  |  006001   	LONGITUDE (HIGH ACCURACY)	DEGREE  	26 bits 10**-5

6        	|  +->End Seq  	End Sequence

7 	301011 	|  301011   	Sequence: DATE

8 	004001 	|  |  004001   	YEAR    	YEAR	12 bits

9 	004002 	|  |  004002   	MONTH	MONTH	4 bits

10 	004003 	|  |  004003  	DAY                                 	DAY	6 bits

11        	|  +->End Seq  	End Sequence

12 	301013 	|  301013   	Sequence: HOUR/MINUTE/SECOND

13 	004004 	|  |  004004   	HOUR                                	HOUR	5 bits

14 	004005 	|  |  004005   	MINUTE	MINUTE 	6 bits

15 	004006 	|  |  004006   	SECOND	SECOND   	6 bits

16        	|  +->End Seq  	End Sequence

17 	007010 	|  007010   	FLIGHT LEVEL                        	M	16 bits

18 	008009 	|  008009   	DETAILED PHASE OF FLIGHT	CODE_TABLE	4 bits

19 	011001 	|  011001   	WIND DIRECTION	DEGREE_TRUE  	9 bits

20 	011002 	|  011002   	WIND SPEED                      	M/S	12 bits 10**-1

21 	011031 	|  011031   	DEGREE OF TURBULENCE	CODE_TABLE   	4 bits

22 	011036 	|  011036   	MAXIMUM DERIVED EQUIVALENT VERTICAL GUST 	M/S	10 bits 10**-1

23 	012101 	|  012101   	TEMPERATURE/DRY BULB TEMPERATURE    	K	16 bits 10**-2

24 	033025 	|  033025   	ACARS INTERPOLATED VALUES	CODE_TABLE   	3 bits

25  		+->End Seq  	End Sequence

26 	008004 	008004   	PHASE OF AIRCRAFT FLIGHT               	CODE_TABLE	3 bits

27 	002064 	002064   	AIRCRAFT ROLL ANGLE QUALITY            	CODE_TABLE	2 bits

IUAX40	ENR Report 	09th Sep 2003	13:10 UTC

311005  	Sequence: STANDARD AMDAR REPORT               		-1000000000

001008  	AIRCRAFT REGISTRATION NUMBER         	CCITT_IA5    	EU2983

001023  	OBSERVATION SEQUENCE NUMBER          	NUMERIC         	-1000000000

301021  	Sequence: LATITUDE/LONGITUDE      		-1000000000

005001  	LATITUDE (HIGH ACCURACY)     	10**-5 DEGREE   	5811833

006001  	LONGITUDE (HIGH ACCURACY)     	10**-5 DEGREE	1896833

End Seq 	End Sequence                               		-1000000000

301011  	Sequence: DATE                                  		-1000000000

004001  	YEAR                                 	YEAR	2003

004002  	MONTH                                	MONTH	9

004003  	DAY                               	DAY	9

End Seq 	End Sequence                      		-1000000000

301013  	Sequence: HOUR/MINUTE/SECOND             		-1000000000

004004  	HOUR                                 	HOUR	13

004005  	MINUTE                               	MINUTE	10

004006  	SECOND                               	SECOND  	-1000000000

End Seq 	End Sequence                       		-1000000000

007010  	FLIGHT LEVEL                        	M	8839

008009  	DETAILED PHASE OF FLIGHT             	CODE_TABLE	3

011001  	WIND DIRECTION                       	DEGREE_TRUE	120

011002  	WIND SPEED                    	10**-1 M/S	98

011031  	DEGREE OF TURBULENCE                 	CODE_TABLE 	-1000000000

011036  	MAXIMUM DERIVED EQUIVALENT VERTICAL GUST 	10**-1 M/S	-1000000000

012101  	TEMPERATURE/DRY BULB TEMPERATURE         	10**-2 K      	23065

033025  	ACARS INTERPOLATED VALUES                	CODE_TABLE	3

End Seq 	End Sequence                                   		-1000000000

008004  	PHASE OF AIRCRAFT FLIGHT                 	CODE_TABLE	3

002064  	AIRCRAFT ROLL ANGLE QUALITY              	CODE_TABLE	0

IUAX01		Expanded BUFR Description

0 	311002	311002   	Sequence: SINGLE LEVEL REPORT: ACARS REP

1 	301065	|  301065   	Sequence: ACARS IDENTIFICATION

2 	001006	|  |  YXXNN    	AIRCRAFT FLIGHT NUMBER                   	CCITT IA5    	64 bits

3 	001008	|  |  YAIRN    	AIRCRAFT REGISTRATION NUMBER             	CCITT IA5    	64 bits

4 	002001	|  |  NIX      	TYPE OF STATION                          	CODE TABLE    	2 bits

5 	002002 	|  |  NIW      	TYPE OF INSTRUMENTFOR WIND MEASUREMENT  	FLAG TABLE    	4 bits

6 	002005 	|  |  MPOTO    	PRECISION OF TEMPERATURE OBSERVATION     	K             	7 bits 10**-2

7 	002062 	|  |  NADRS    	TYPE OF AIRCRAFT DATA RELAY SYSTEM       	CODE TABLE    	4 bits

8 	002070 	|  |  NOSLL    	ORIGINAL SPECIF. OF LATITUDE/LONGITUDE   	CODE TABLE    	4 bits

9 	002065 	|  |  YAGRS    	ACARS GROUND RECEIVING STATION           	CCITT IA5    	40 bits

10        	   |  +->End Seq  	End Sequence

11 	301066 	|  301066   	Sequence: ACARS LOCATION

12 	301011 	|  |  301011   	Sequence: DATE

13 	004001 	|  |  |  MJJJ     	YEAR                                     	YEAR         	12 bits

14 	004002 	|  |  |  MMM      	MONTH                                    	MONTH         	4 bits

15 	004003 	|  |  |  MYY      	DAY                                      	DAY           	6 bits

16  		   |  |  +->End Seq 	End Sequence

17 	301013 	|  |  301013   	Sequence: HOUR/MINUTE/SECOND

18 	004004 	|  |  |  MGG      	HOUR                                     	HOUR          	5 bits

19 	004005 	|  |  |  NGG      	MINUTE                                   	MINUTE        	6 bits

20 	004006 	|  |  |  MSEC     	SECOND                                   	SECOND        	6 bits

21  		   |  |  +->End Seq 	End Sequence

22 	301023 	|  |  301023   	Sequence: LATITUDE/LONGITUDE, COARSE ACC

23 	005002 	|  |  |  MLALA    	LATITUDE (COARSE ACCURACY)               	DEGREE       	15 bits 10**-2

24 	006002 	|  |  |  MLOLO    	LONGITUDE (COARSE ACCURACY)              	DEGREE       	16 bits 10**-2

25  	      	   |  |  +->End Seq 	End Sequence

26 	007004 	|  |  MPN      	PRESSURE (VERT.LOCATION)                 	PA           	14 bits 10** 1

27 	002064 	|  |  MQARA    	AIRCRAFT ROLL ANGLE QUALITY              	CODE TABLE    	2 bits

28 	008004 	|  |  MPHAI    	PHASE OF AIRCRAFT FLIGHT                 	CODE TABLE    	3 bits

29        	   |  +->End Seq  	End Sequence

30 	311003 	|  311003   	Sequence: ACARS STANDARD REPORTED VARIAB

31 	010070 	|  |  MIAA     	INDICATED AIRCRAFT ALTITUDE              	M            	16 bits

32 	011001 	|  |  NDNDN    	WIND DIRECTION                           	DEGREE TRUE   	9 bits

33 	011002 	|  |  NFNFN    	WIND SPEED                               	M/S          	12 bits 10**-1

34 	012001 	|  |  MTN      	TEMPERATURE/DRY BULB TEMPERATURE         	K            	12 bits 10**-1

35 	013002 	|  |  MMIXR    	MIXING RATIO                             	KG/KG        	14 bits 10**-5

36        	   |  +->End Seq  	End Sequence

71        	   +->End Seq	End Sequence

IUAX01	ENR Reference Report	09th Sep 2003	13:10 UTC

311002  	Sequence: SINGLE LEVEL REPORT: ACARS REP                     		-1000000000

301065  	Sequence: ACARS IDENTIFICATION                               		-1000000000

YXXNN   	AIRCRAFT FLIGHT NUMBER                          	CCITT IA5   	LH3016

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU2983

NIX     	TYPE OF STATION                                 	CODE TABLE    	0

NIW     	TYPE OF INSTRUMENT.FOR WIND MEASUREMENT         	FLAG TABLE      	4

MPOTO   	PRECISION OF TEMPERATURE OBSERVATION     	10**-2 K            	10

NADRS   	TYPE OF AIRCRAFT DATA RELAY SYSTEM              	CODE TABLE   	3

NOSLL   	ORIGINAL SPECIF. OF LATITUDE/LONGITUDE          	CODE TABLE      	0

YAGRS   	ACARS GROUND RECEIVING STATION                  	CCITT IA5    	-1000000000

301066  	Sequence: ACARS LOCATION                                     		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                  	9

MYY     	DAY                                             	DAY                    	9

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                  	13

NGG     	MINUTE                                          	MINUTE                	10

MSEC    	SECOND                                          	SECOND       	-1000000000

301023  	Sequence: LATITUDE/LONGITUDE, COARSE ACC                     		-1000000000

MLALA   	LATITUDE (COARSE ACCURACY)               	10**-2 DEGREE    	5812

MLOLO   	LONGITUDE (COARSE ACCURACY)              	10**-2 DEGREE     	1897

MPN     	PRESSURE (VERT.LOCATION)                 	10** 1 PA           	-1000000000

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE    	0

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE    	3

311003  	Sequence: ACARS STANDARD REPORTED VARIAB                     		-1000000000

MIAA    	INDICATED AIRCRAFT ALTITUDE                     	M                   	8839

NDNDN   	WIND DIRECTION                                  	DEGREE TRUE    	120

NFNFN   	WIND SPEED                               	10**-1 M/S            	98

MTN     	TEMPERATURE/DRY BULB TEMPERATURE         	10**-1 K          	2307

MMIXR   	MIXING RATIO                             	10**-5 KG/KG        	-1000000000

5.3	BUFR Trial Lido - DWD - CMC

IUAX40	Expanded BUFR Description

0	311005 	311005   	Sequence: STANDARD AMDAR REPORT

1 	001008 	|  YAIRN    	AIRCRAFT REGISTRATION NUMBER 		CCITT IA5    	64 bits

2 	001023 	|  NOSNO    	OBSERVATION SEQUENCE NUMBER                 	NUMERIC       	9 bits

3 	301021 	|  301021   	Sequence: LATITUDE/LONGITUDE

4 	005001 	|  |  MLAH 	LATITUDE (HIGH ACCURACY)                 		DEGREE       	25 bits 10**-5

5 	006001 	|  |  MLOH	LONGITUDE (HIGH ACCURACY)                		DEGREE       	26 bits 10**-5

6        	|  +->End Seq	End Sequence

7 	301011 	|  301011   	Sequence: DATE

8 	004001 	|  |  MJJJ     	YEAR                                     		YEAR         	12 bits

9 	004002 	|  |  MMM   	MONTH                                    		MONTH         	4 bits

10 	004003 	|  |  MYY     	DAY                                      		DAY          	6 bits

11        	|  +->End Seq	End Sequence

12 	301013 	|  301013   	Sequence: HOUR/MINUTE/SECOND

13 	004004 	|  |  MGG      	HOUR                                     		HOUR          	5 bits

14	004005 	|  |  NGG      	MINUTE                                   		MINUTE        	6 bits

15 	004006 	|  |  MSEC	SECOND                                   		SECOND        	6 bits

16        	|  +->End Seq 	End Sequence

17 	007010 	|  NFLEV	FLIGHT LEVEL                                		M 	           	16 bits

18 	008009 	|  NDEPF    	DETAILED PHASE OF FLIGHT                    		CODE TABLE    	4 bits

19 	011001 	|  NDNDN    	WIND DIRECTION                              		DEGREE TRUE   	9 bits

20 	011002 	|  NFNFN    	WIND SPEED                                  		M/S          	12 bits 10**-1

21 	011031 	|  MB    	DEGREE OF TURBULENCE                        		CODE TABLE    	4 bits

22 	011036 	|  NMDEWX	MAXIMUM DERIVED EQUIVALENT VERT. GUST	M/S          	10 bits 10**-1

23 	311205 	|  311205 	Sequence: STANDARD AMDAR REPORT, PART 2

24 	012101 	|  |  MTDBT 	TEMPERATURE/DRY BULB TEMPERATURE        	K     		16 bits 10**-2

25 	033025 	|  |  MAIV  	ACARS INTERPOLATED VALUES                		CODE TABLE  	3 bits

26        	|  +->End Seq	End Sequence

27        	+->End Seq  	End Sequence

28	008004 	MPHAI   	PHASE OF AIRCRAFT FLIGHT                       		CODE TABLE  	3 bits

29 	002064 	MQARA   	AIRCRAFT ROLL ANGLE QUALITY                    	CODE TABLE   	2 bits

IUAX40	ASC Report 	8th Oct 2003	20:21 UTC

311005  	Sequence: STANDARD AMDAR REPORT                                        		-1000000000

YAIRN   	AIRCRAFT REGISTRATION NUMBER                              	CCITT IA5         	EU3733

NOSNO   	OBSERVATION SEQUENCE NUMBER                               	NUMERIC      	-1000000000

301021  	Sequence: LATITUDE/LONGITUDE                                           		-1000000000

MLAH    	LATITUDE (HIGH ACCURACY)                           	10**-5 DEGREE	2445000

MLOH    	LONGITUDE (HIGH ACCURACY)                          	10**-5 DEGREE	5464333

End Seq 	End Sequence                                                           		-1000000000

301011  	Sequence: DATE                                                         		-1000000000

MJJJ    	YEAR                                                      	YEAR                	2003

MMM     	MONTH                                                     	MONTH                 	10

MYY     	DAY                                                       	DAY                   	8

End Seq 	End Sequence                                                           		-1000000000

301013  	Sequence: HOUR/MINUTE/SECOND                                           		-1000000000

MGG     	HOUR                                                      	HOUR                   	20

NGG     	MINUTE                                                    	MINUTE                	21

MSEC    	SECOND                                                    	SECOND       	-1000000000

End Seq 	End Sequence                                                           		-1000000000

NFLEV   	FLIGHT LEVEL                                              	M                    	183

NDEPF   	DETAILED PHASE OF FLIGHT                                  	CODE TABLE         7

NDNDN   	WIND DIRECTION                                            	DEGREE TRUE	51

NFNFN   	WIND SPEED                                         	10**-1 M/S 	62

MB      	DEGREE OF TURBULENCE                                      	CODE TABLE	-1000000000

NMDEWX  	MAXIMUM DERIVED EQUIVALENT VERTICAL GUST           	10**-1 M/S	-1000000000

311205  	Sequence: STANDARD AMDAR REPORT, PART 2                                		-1000000000

MTDBT   	TEMPERATURE/DRY BULB TEMPERATURE                   	10**-2 K       	30365

MAIV    	ACARS INTERPOLATED VALUES                                 	CODE TABLE  	1

End Seq 	End Sequence                                                           		-1000000000

End Seq 	End Sequence                                                           		-1000000000

MPHAI   	PHASE OF AIRCRAFT FLIGHT                                  	CODE TABLE 	5

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                               	CODE TABLE   	0

IUAX40	ENR Report 	8th Oct 2003	19:41 UTC

311005  	Sequence: STANDARD AMDAR REPORT                              		-1000000000

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU1547

NOSNO   	OBSERVATION SEQUENCE NUMBER                     	NUMERIC      	-1000000000

301021  	Sequence: LATITUDE/LONGITUDE                                 		-1000000000

MLAH    	LATITUDE (HIGH ACCURACY)                 	10**-5 DEGREE 	4898055

MLOH    	LONGITUDE (HIGH ACCURACY)                	10**-5 DEGREE    	393333

End Seq 	End Sequence                                                 		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                 	10

MYY     	DAY                                             	DAY                   	8

End Seq 	End Sequence                                                 		-1000000000

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                   	19

NGG     	MINUTE                                          	MINUTE                	41

MSEC    	SECOND                                          	SECOND       	-1000000000

End Seq 	End Sequence                                                 		-1000000000

NFLEV   	FLIGHT LEVEL                                    	M                   	10671

NDEPF   	DETAILED PHASE OF FLIGHT                        	CODE TABLE     	3

NDNDN   	WIND DIRECTION                                  	DEGREE TRUE    	326

NFNFN   	WIND SPEED                               	10**-1 M/S            	360

MB      	DEGREE OF TURBULENCE                            	CODE TABLE   	-1000000000

NMDEWX  	MAXIMUM DERIVED EQUIVALENT VERTICAL GUST 	10**-1 M/S          	-1000000000

311205  	Sequence: STANDARD AMDAR REPORT, PART 2                      		-1000000000

MTDBT   	TEMPERATURE/DRY BULB TEMPERATURE         	10**-2 K                  22415

MAIV    	ACARS INTERPOLATED VALUES                       	CODE TABLE      	3

End Seq 	End Sequence                                                 		-1000000000

End Seq 	End Sequence                                                 		-1000000000

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE     	3

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE      	0

IUAX40	DES Report 	8th Oct 2003	20:28 UTC

311005  	Sequence: STANDARD AMDAR REPORT                              		-1000000000

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU6564

NOSNO   	OBSERVATION SEQUENCE NUMBER                     	NUMERIC      	-1000000000

301021  	Sequence: LATITUDE/LONGITUDE                                 		-1000000000

MLAH    	LATITUDE (HIGH ACCURACY)                 	10**-5 DEGREE  	3899500

MLOH    	LONGITUDE (HIGH ACCURACY)                	10**-5 DEGREE    	-906833

End Seq 	End Sequence                                                 		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                 	10

MYY     	DAY                                             	DAY                   	8

End Seq 	End Sequence                                                 		-1000000000

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                   	20

NGG     	MINUTE                                          	MINUTE                	28

MSEC    	SECOND                                          	SECOND       	-1000000000

End Seq 	End Sequence                                                 		-1000000000

NFLEV   	FLIGHT LEVEL                                    	M                   	2923

NDEPF   	DETAILED PHASE OF FLIGHT                        	CODE TABLE        	11

NDNDN   	WIND DIRECTION                                  	DEGREE TRUE    	74

NFNFN   	WIND SPEED                               	10**-1 M/S            	72

MB      	DEGREE OF TURBULENCE                            	CODE TABLE   	-1000000000

NMDEWX  	MAXIMUM DERIVED EQUIVALENT VERTICAL GUST 	10**-1 M/S          	-1000000000

311205  	Sequence: STANDARD AMDAR REPORT, PART 2                      		-1000000000

MTDBT   	TEMPERATURE/DRY BULB TEMPERATURE         	10**-2 K                  28015

MAIV    	ACARS INTERPOLATED VALUES                       	CODE TABLE    	3

End Seq 	End Sequence                                                 		-1000000000

End Seq 	End Sequence                                                 		-1000000000

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE    	6

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE     	0

IUAX01	Expanded BUFR Description

0 	311002 		311002   	Sequence: SINGLE LEVEL REPORT: ACARS REP

1 	301065 		|  301065   	Sequence: ACARS IDENTIFICATION

2 	001006 		|  |  YXXNN    	AIRCRAFT FLIGHT NUMBER                   		CCITT IA5    	64 bits

3 	001008 		|  |  YAIRN    	AIRCRAFT REGISTRATION NUMBER             		CCITT IA5    	64 bits

4 	002001 		|  |  NIX      	TYPE OF STATION                          		CODE TABLE    	2 bits

5 	002002 		|  |  NIW      	TYPE OF INSTRUMENT FOR WIND MEASUREMENT  	FLAG TABLE    	4 bits

6 	002005 		|  |  MPOTO    	PRECISION OF TEMPERATURE OBSERVATION     	K         		7 bits 10**-2

7 	002062 		|  |  NADRS    	TYPE OF AIRCRAFT DATA RELAY SYSTEM       	CODE TABLE    	4 bits

8 	002070 		|  |  NOSLL    	ORIGINAL SPECIF. OF LATITUDE/LONGITUDE   	CODE TABLE    	4 bits

9 	002065 		|  |  YAGRS    	ACARS GROUND RECEIVING STATION           	CCITT IA5    	40 bits

10       			|  +->End Seq  	End Sequence

11 	301066 		|  301066   	Sequence: ACARS LOCATION

12 	301011 		|  |  301011   	Sequence: DATE

13 	004001 		|  |  |  MJJJ     	YEAR                                     		YEAR         	12 bits

14 	004002 		|  |  |  MMM      	MONTH                                    		MONTH         	4 bits

15 	004003 		|  |  |  MYY      	DAY                                      		DAY           	6 bits

16  				|  |  +->End Seq End Sequence

17 	301013 		|  |  301013   	Sequence: HOUR/MINUTE/SECOND

18 	004004 		|  |  |  MGG      	HOUR                                     		HOUR          	5 bits

19 	004005 		|  |  |  NGG      	MINUTE                                   		MINUTE        	6 bits

20 	004006 		|  |  |  MSEC     	SECOND                                 	  	SECOND        	6 bits

21  				|  |  +->End Seq	End Sequence

22 	301023 		|  |  301023   	Sequence: LATITUDE/LONGITUDE, COARSE ACC

23 	005002 		|  |  |  MLALA    	LATITUDE (COARSE ACCURACY)               		DEGREE       	15 bits 10**-2

24 	006002 		|  |  |  MLOLO    	LONGITUDE (COARSE ACCURACY)              		DEGREE       	16 bits 10**-2

25  	      			|  |  +->End Seq End Sequence

26 	007004 		|  |  MPN      	PRESSURE (VERT.LOCATION)                 		PA           		14 bits 10** 1

27 	002064 		|  |  MQARA    	AIRCRAFT ROLL ANGLE QUALITY              		CODE TABLE    	2 bits

28 	008004 		|  |  MPHAI    	PHASE OF AIRCRAFT FLIGHT                 		CODE TABLE    	3 bits

29        			|  +->End Seq  	End Sequence

30 	311003 		|  311003   	Sequence: ACARS STANDARD REPORTED VARIAB

31 	010070 		|  |  MIAA     	INDICATED AIRCRAFT ALTITUDE              		M            		16 bits

32 	011001 		|  |  NDNDN    	WIND DIRECTION                           		DEGREE TRUE   	9 bits

33 	011002 		|  |  NFNFN    	WIND SPEED                               		M/S          	12 bits 10**-1

34 	012001 		|  |  MTN      	TEMPERATURE/DRY BULB TEMPERATURE         	K            		12 bits 10**-1

35 	013002 		|  |  MMIXR    	MIXING RATIO                             		KG/KG        	14 bits 10**-5

36        			|  +->End Seq  	End Sequence

71        			+->End Seq  	End Sequence

IUAX01	ASC Reference Report 	8th Oct 2003	20:21 UTC

311002  	Sequence: SINGLE LEVEL REPORT: ACARS REP                     		-1000000000

301065  	Sequence: ACARS IDENTIFICATION                               		-1000000000

YXXNN   	AIRCRAFT FLIGHT NUMBER                          	CCITT IA5   	LH637

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU3733

NIX     	TYPE OF STATION                                 	CODE TABLE    	0

NIW     	TYPE OF INSTRUMENT.FOR WIND MEASUREMENT         	FLAG TABLE   	4

MPOTO   	PRECISION OF TEMPERATURE OBSERVATION     	10**-2 K         	10

NADRS   	TYPE OF AIRCRAFT DATA RELAY SYSTEM              	CODE TABLE        	3

NOSLL  	ORIGINAL SPECIF. OF LATITUDE/LONGITUDE          	CODE TABLE    	0

YAGRS   	ACARS GROUND RECEIVING STATION                  	CCITT IA5    	-1000000000

301066  	Sequence: ACARS LOCATION                                     		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                 	10

MYY     	DAY                                             	DAY                    	8

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                  	20

NGG     	MINUTE                                          	MINUTE                	21

MSEC    	SECOND                                          	SECOND       	-1000000000

301023  	Sequence: LATITUDE/LONGITUDE, COARSE ACC                     		-1000000000

MLALA   	LATITUDE (COARSE ACCURACY)               	10**-2 DEGREE    	2445

MLOLO   	LONGITUDE (COARSE ACCURACY)              	10**-2 DEGREE   	5464

MPN     	PRESSURE (VERT.LOCATION)                 	10** 1 PA           	-1000000000

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE   	0

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE     	5

311003  	Sequence: ACARS STANDARD REPORTED VARIAB                     		-1000000000

MIAA    	INDICATED AIRCRAFT ALTITUDE                     	M                    	183

NDNDN   	WIND DIRECTION                                  	DEGREE TRUE     	51

NFNFN   	WIND SPEED                               	10**-1 M/S             	62

MTN     	TEMPERATURE/DRY BULB TEMPERATURE         	10**-1 K            	3037

MMIXR   	MIXING RATIO                             	10**-5 KG/KG        	-1000000000

IUAX01	ENR Reference Report	8th Oct 2003	19:41 UTC

311002  	Sequence: SINGLE LEVEL REPORT: ACARS REP                     		-1000000000

301065  	Sequence: ACARS IDENTIFICATION                               		-1000000000

YXXNN   	AIRCRAFT FLIGHT NUMBER                          	CCITT IA5   	LH4302

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU1547

NIX     	TYPE OF STATION                                 	CODE TABLE        	0

NIW     	TYPE OF INSTRUMENT.FOR WIND MEASUREMENT         	FLAG TABLE      	4

MPOTO   	PRECISION OF TEMPERATURE OBSERVATION     	10**-2 K                	10

NADRS   	TYPE OF AIRCRAFT DATA RELAY SYSTEM              	CODE TABLE       	3

NOSLL   	ORIGINAL SPECIF. OF LATITUDE/LONGITUDE          	CODE TABLE        	0

YAGRS   	ACARS GROUND RECEIVING STATION                  	CCITT IA5    	-1000000000

301066  	Sequence: ACARS LOCATION                                     		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                 	10

MYY     	DAY                                             	DAY                    	8

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                  	19

NGG     	MINUTE                                          	MINUTE                	41

MSEC    	SECOND                                          	SECOND       	-1000000000

301023  	Sequence: LATITUDE/LONGITUDE, COARSE ACC                     		-1000000000

MLALA   	LATITUDE (COARSE ACCURACY)               	10**-2 DEGREE   	4898

MLOLO   	LONGITUDE (COARSE ACCURACY)              	10**-2 DEGREE    	393

MPN     	PRESSURE (VERT.LOCATION)                 	10** 1 PA           	-1000000000

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE    	0

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE     	3

311003  	Sequence: ACARS STANDARD REPORTED VARIAB                     		-1000000000

MIAA    	INDICATED AIRCRAFT ALTITUDE                     	M                  	10671

NDNDN   	WIND DIRECTION                                  	DEGREE TRUE     	326

NFNFN   	WIND SPEED                               	10**-1 M/S             	360

MTN     	TEMPERATURE/DRY BULB TEMPERATURE         	10**-1 K                  2242

MMIXR   	MIXING RATIO                             	10**-5 KG/KG        	-1000000000

IUAX01	DES Reference Report	8th Oct 2003	20:28 UTC

311002  	Sequence: SINGLE LEVEL REPORT: ACARS REP                     		-1000000000

301065  	Sequence: ACARS IDENTIFICATION                               		-1000000000

YXXNN   	AIRCRAFT FLIGHT NUMBER                          	CCITT IA5   	LH4266

YAIRN   	AIRCRAFT REGISTRATION NUMBER                    	CCITT IA5   	EU6564

NIX     	TYPE OF STATION                                 	CODE TABLE     	0

NIW     	TYPE OF INSTRUMENT.FOR WIND MEASUREMENT         	FLAG TABLE     	4

MPOTO   	PRECISION OF TEMPERATURE OBSERVATION     	10**-2 K         	10

NADRS   	TYPE OF AIRCRAFT DATA RELAY SYSTEM              	CODE TABLE   	3

NOSLL   	ORIGINAL SPECIF. OF LATITUDE/LONGITUDE          	CODE TABLE    	0

YAGRS   	ACARS GROUND RECEIVING STATION                  	CCITT IA5    	-1000000000

301066  	Sequence: ACARS LOCATION                                     		-1000000000

301011  	Sequence: DATE                                               		-1000000000

MJJJ    	YEAR                                            	YEAR                	2003

MMM     	MONTH                                           	MONTH                 	10

MYY     	DAY                                             	DAY                    	8

301013  	Sequence: HOUR/MINUTE/SECOND                                 		-1000000000

MGG     	HOUR                                            	HOUR                  	20

NGG     	MINUTE                                          	MINUTE                	28

MSEC    	SECOND                                          	SECOND       	-1000000000

301023  	Sequence: LATITUDE/LONGITUDE, COARSE ACC                     		-1000000000

MLALA   	LATITUDE (COARSE ACCURACY)               	10**-2 DEGREE   	3900

MLOLO   	LONGITUDE (COARSE ACCURACY)              	10**-2 DEGREE     	-907

MPN     	PRESSURE (VERT.LOCATION)                 	10** 1 PA           	-1000000000

MQARA   	AIRCRAFT ROLL ANGLE QUALITY                     	CODE TABLE     	0

MPHAI   	PHASE OF AIRCRAFT FLIGHT                        	CODE TABLE      	6

311003  	Sequence: ACARS STANDARD REPORTED VARIAB                     		-1000000000

MIAA    	INDICATED AIRCRAFT ALTITUDE                     	M                   	2923

NDNDN   	WIND DIRECTION                                  	DEGREE TRUE     	74

NFNFN   	WIND SPEED                               	10**-1 M/S      	72

MTN     	TEMPERATURE/DRY BULB TEMPERATURE         	10**-1 K                	2802

MMIXR   	MIXING RATIO                             	10**-5 KG/KG        	-1000000000

6.	Trial Results

The results of the BUFR trial are presented in the tables below, which show the decoded BUFR elements with their numerical values in the columns "Ref Value IUAX01" and "Test Value IUAX40" in comparison:

- BUFR elements en/decoded with the currently valid template (IUAX01) and the proposed new AMDAR template (IUAX40).  At this the chars "---" indicate elements not covered in the template while the chars "-1000000000" indicate elements covered, but no values transferred in the operational ACARS report formatted in ARINC 620-3.

- Numerical values of the reference BUFR reports IUAX01 and the BUFR test reports IUAX40 of the same operational data source.

As noted in chapter 5 the parameters Humidity, Turbulence and Airframe Icing are not included in the test report IUAX40 in conformity with the BUFR rules, since these parameters are not transmitted from the Lufthansa fleet.

The results of the trial re-sent from CMC were kindly evaluated in comparison to IUAg01 as reference reports, which are officially disseminated from E-ADAS in the GTS. Since the altitude in IUAg01 is reported with a resolution of 10 meters and not in meters as in IUAX01 and IUAX40, small differences appear in comparison to the test values. Similar small differences were also noticed by the co-ordinates caused by different rounding procedures. For this reason the test results decoded by CMC are compared with the original IUAX01 data.

6.1	BUFR Trial Lido - DWD	ASC - Report EU5891 - 24th Oct 2003 05:12 UTC

| Element | Descriptor | Note / Dim. | Ref Value IUAX01 | Test Value IUAX40 |
| --- | --- | --- | --- | --- |
| AIRCRAFT REGISTRATION NUMBER | 0 01 008 | CCITT IA5 | EU5891 | EU5891 |
| AIRCRAFT FLIGHT NUMBER | 0 01 006 | CCITT IA5 | LH3011 | --- |
| OBSERVATION SEQUENCE NUMBER | 0 01 023 | NUMERIC | --- | -1000000000 |
| TYPE OF STATION | 0 02 001 | CODE TABLE | 0 | --- |
| TYPE OF INSTRUMENT FOR WIND MEAS. | 0 02 002 | FLAG TABLE | 4 | --- |
| PRECISION OF TEMPERATURE | 0 02 005 | 10**-2K | 10 | --- |
| TYPE OF AIRCRAFT DATA RELAY SYSTEM | 0 02 062 | CODE TABLE | 3 | --- |
| ORIG. SPECIF. OF LATITUDE/LONGITUDE | 0 02 070 | CODE TABLE | 0 | --- |
| ACARS GROUND RECEIVING STATION | 0 02 065 | CCITT IA5 | -1000000000 | --- |
| LATITUDE (HIGH ACCURACY) | 0 05 001 | 10**-5 DEGREE | --- | 5764833 |
| LONGITUDE (HIGH ACCURACY) | 0 06 001 | 10**-5 DEGREE | --- | 1226666 |
| LATITUDE (COARSE ACCURACY) | 0 05 002 | 10**-2 DEGREE | 5765 | --- |
| LONGITUDE (COARSE ACCURACY) | 0 06 002 | 10**-2 DEGREE | 1227 | --- |
| YEAR | 0 04 001 | YEAR | 2003 | 2003 |
| MONTH | 0 04 002 | MONTH | 10 | 10 |
| DAY | 0 04 003 | DAY | 24 | 24 |
| HOUR | 0 04 004 | HOUR | 5 | 5 |
| MINUTE | 0 04 005 | MINUTE | 12 | 12 |
| SECOND | 0 04 006 | SECOND | -1000000000 | -1000000000 |
| FLIGHT LEVEL | 0 07 010 | M | --- | 430 |
| INDICATED AIRCRAFT ALTITUDE | 0 10 070 | M | 430 | --- |
| PRESSURE (VERT. LOCATION) | 0 07 004 | 10**1 PA | -1000000000 | --- |
| DETAILED PHASE OF FLIGHT | 0 08 009 | CODE TABLE | --- | 7 |
| WIND DIRECTION | 0 11 001 | DEGREE TRUE | 262 | 262 |
| WIND SPEED | 0 11 002 | 10**-1 M/S | 36 | 36 |
| DEGREE OF TURBULENCE | 0 11 031 | CODE TABLE | --- | -1000000000 |
| MAX. DERIVED EQUIVALENT VERT. GUST | 0 11 036 | 10**-1 M/S | --- | -1000000000 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 101 | 10**-2 K | --- | 27165 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 001 | 10**-1 K | 2717 | --- |
| ACARS INTERPOLATED VALUES | 0 33 025 | CODE TABLE | --- | 1 |
| PHASE OF AIRCRAFT FLIGHT | 0 08 004 | CODE TABLE | 5 | 5 |
| AIRCRAFT ROLL ANGLE QUALITY | 0 02 064 | CODE TABLE | 0 | 0 |
| MIXING RATIO | 0 13 002 | 10**-5 KG/KG | -1000000000 | --- |

Lido - DWD	ENR - Report EU0601 - 24th Oct 2003 05:28 UTC

| Element | Descriptor | Note / Dim. | Ref Value IUAX01 | Test Value IUAX40 |
| --- | --- | --- | --- | --- |
| AIRCRAFT REGISTRATION NUMBER | 0 01 008 | CCITT IA5 | EU0601 | EU0601 |
| AIRCRAFT FLIGHT NUMBER | 0 01 006 | CCITT IA5 | LH827 | --- |
| OBSERVATION SEQUENCE NUMBER | 0 01 023 | NUMERIC | --- | -1000000000 |
| TYPE OF STATION | 0 02 001 | CODE TABLE | 0 | --- |
| TYPE OF INSTRUMENT FOR WIND MEAS. | 0 02 002 | FLAG TABLE | 4 | --- |
| PRECISION OF TEMPERATURE | 0 02 005 | 10**-2K | 10 | --- |
| TYPE OF AIRCRAFT DATA RELAY SYSTEM | 0 02 062 | CODE TABLE | 3 | --- |
| ORIG. SPECIF. OF LATITUDE/LONGITUDE | 0 02 070 | CODE TABLE | 0 | --- |
| ACARS GROUND RECEIVING STATION | 0 02 065 | CCITT IA5 | -1000000000 | --- |
| LATITUDE (HIGH ACCURACY) | 0 05 001 | 10**-5 DEGREE | --- | 4889166 |
| LONGITUDE (HIGH ACCURACY) | 0 06 001 | 10**-5 DEGREE | --- | 1061111 |
| LATITUDE (COARSE ACCURACY) | 0 05 002 | 10**-2 DEGREE | 4889 | --- |
| LONGITUDE (COARSE ACCURACY) | 0 06 002 | 10**-2 DEGREE | 1061 | --- |
| YEAR | 0 04 001 | YEAR | 2003 | 2003 |
| MONTH | 0 04 002 | MONTH | 10 | 10 |
| DAY | 0 04 003 | DAY | 24 | 24 |
| HOUR | 0 04 004 | HOUR | 5 | 5 |
| MINUTE | 0 04 005 | MINUTE | 28 | 28 |
| SECOND | 0 04 006 | SECOND | -1000000000 | -1000000000 |
| FLIGHT LEVEL | 0 07 010 | M | --- | 6437 |
| INDICATED AIRCRAFT ALTITUDE | 0 10 070 | M | 6437 | --- |
| PRESSURE (VERT. LOCATION) | 0 07 004 | 10**1 PA | -1000000000 | --- |
| DETAILED PHASE OF FLIGHT | 0 08 009 | CODE TABLE | --- | 3 |
| WIND DIRECTION | 0 11 001 | DEGREE TRUE | 289 | 289 |
| WIND SPEED | 0 11 002 | 10**-1 M/S | 72 | 72 |
| DEGREE OF TURBULENCE | 0 11 031 | CODE TABLE | --- | -1000000000 |
| MAX. DERIVED EQUIVALENT VERT. GUST | 0 11 036 | 10**-1 M/S | --- | -1000000000 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 101 | 10**-2 K | --- | 23715 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 001 | 10**-1 K | 2372 | --- |
| ACARS INTERPOLATED VALUES | 0 33 025 | CODE TABLE | --- | 3 |
| PHASE OF AIRCRAFT FLIGHT | 0 08 004 | CODE TABLE | 3 | 3 |
| AIRCRAFT ROLL ANGLE QUALITY | 0 02 064 | CODE TABLE | 0 | 0 |
| MIXING RATIO | 0 13 002 | 10**-5 KG/KG | -1000000000 | --- |

Lido - DWD	DES - Report EU4623 - 24th Oct 2003 05:25 UTC

| Element | Descriptor | Note / Dim. | Ref Value IUAX01 | Test Value IUAX40 |
| --- | --- | --- | --- | --- |
| AIRCRAFT REGISTRATION NUMBER | 0 01 008 | CCITT IA5 | EU4623 | EU4623 |
| AIRCRAFT FLIGHT NUMBER | 0 01 006 | CCITT IA5 | LH182 | --- |
| OBSERVATION SEQUENCE NUMBER | 0 01 023 | NUMERIC | --- | -1000000000 |
| TYPE OF STATION | 0 02 001 | CODE TABLE | 0 | --- |
| TYPE OF INSTRUMENT FOR WIND MEAS. | 0 02 002 | FLAG TABLE | 4 | --- |
| PRECISION OF TEMPERATURE | 0 02 005 | 10**-2K | 10 | --- |
| TYPE OF AIRCRAFT DATA RELAY SYSTEM | 0 02 062 | CODE TABLE | 3 | --- |
| ORIG. SPECIF. OF LATITUDE/LONGITUDE | 0 02 070 | CODE TABLE | 0 | --- |
| ACARS GROUND RECEIVING STATION | 0 02 065 | CCITT IA5 | -1000000000 | --- |
| LATITUDE (HIGH ACCURACY) | 0 05 001 | 10**-5 DEGREE | --- | 5293500 |
| LONGITUDE (HIGH ACCURACY) | 0 06 001 | 10**-5 DEGREE | --- | 0923166 |
| LATITUDE (COARSE ACCURACY) | 0 05 002 | 10**-2 DEGREE | 5294 | --- |
| LONGITUDE (COARSE ACCURACY) | 0 06 002 | 10**-2 DEGREE | 0923 | --- |
| YEAR | 0 04 001 | YEAR | 2003 | 2003 |
| MONTH | 0 04 002 | MONTH | 10 | 10 |
| DAY | 0 04 003 | DAY | 24 | 24 |
| HOUR | 0 04 004 | HOUR | 5 | 5 |
| MINUTE | 0 04 005 | MINUTE | 25 | 25 |
| SECOND | 0 04 006 | SECOND | -1000000000 | -1000000000 |
| FLIGHT LEVEL | 0 07 010 | M | --- | 1622 |
| INDICATED AIRCRAFT ALTITUDE | 0 10 070 | M | 1622 | --- |
| PRESSURE (VERT. LOCATION) | 0 07 004 | 10**1 PA | -1000000000 | --- |
| DETAILED PHASE OF FLIGHT | 0 08 009 | CODE TABLE | --- | 11 |
| WIND DIRECTION | 0 11 001 | DEGREE TRUE | 357 | 357 |
| WIND SPEED | 0 11 002 | 10**-1 M/S | 57 | 57 |
| DEGREE OF TURBULENCE | 0 11 031 | CODE TABLE | --- | -1000000000 |
| MAX. DERIVED EQUIVALENT VERT. GUST | 0 11 036 | 10**-1 M/S | --- | -1000000000 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 101 | 10**-2 K | --- | 26595 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 001 | 10**-1 K | 2660 | --- |
| ACARS INTERPOLATED VALUES | 0 33 025 | CODE TABLE | --- | 3 |
| PHASE OF AIRCRAFT FLIGHT | 0 08 004 | CODE TABLE | 6 | 6 |
| AIRCRAFT ROLL ANGLE QUALITY | 0 02 064 | CODE TABLE | 0 | 0 |
| MIXING RATIO | 0 13 002 | 10**-5 KG/KG | -1000000000 | --- |

6.2	BUFR Trial Lido - DWD - KNMI	ENR - Report EU2983 - 9th Sep 2003 13:10 UTC

| Element | Descriptor | Note / Dim. | Ref Value IUAX01 | Test Value IUAX40 |
| --- | --- | --- | --- | --- |
| AIRCRAFT REGISTRATION NUMBER | 0 01 008 | CCITT IA5 | EU2983 | EU2983 |
| AIRCRAFT FLIGHT NUMBER | 0 01 006 | CCITT IA5 | LH3016 | --- |
| OBSERVATION SEQUENCE NUMBER | 0 01 023 | NUMERIC | --- | -1000000000 |
| TYPE OF STATION | 0 02 001 | CODE TABLE | 0 | --- |
| TYPE OF INSTRUMENT FOR WIND MEAS. | 0 02 002 | FLAG TABLE | 4 | --- |
| PRECISION OF TEMPERATURE | 0 02 005 | 10**-2K | 10 | --- |
| TYPE OF AIRCRAFT DATA RELAY SYSTEM | 0 02 062 | CODE TABLE | 3 | --- |
| ORIG. SPECIF. OF LATITUDE/LONGITUDE | 0 02 070 | CODE TABLE | 0 | --- |
| ACARS GROUND RECEIVING STATION | 0 02 065 | CCITT IA5 | -1000000000 | --- |
| LATITUDE (HIGH ACCURACY) | 0 05 001 | 10**-5 DEGREE | --- | 5811833 |
| LONGITUDE (HIGH ACCURACY) | 0 06 001 | 10**-5 DEGREE | --- | 1896833 |
| LATITUDE (COARSE ACCURACY) | 0 05 002 | 10**-2 DEGREE | 5812 | --- |
| LONGITUDE (COARSE ACCURACY) | 0 06 002 | 10**-2 DEGREE | 1897 | --- |
| YEAR | 0 04 001 | YEAR | 2003 | 2003 |
| MONTH | 0 04 002 | MONTH | 9 | 9 |
| DAY | 0 04 003 | DAY | 9 | 9 |
| HOUR | 0 04 004 | HOUR | 13 | 13 |
| MINUTE | 0 04 005 | MINUTE | 10 | 10 |
| SECOND | 0 04 006 | SECOND | -1000000000 | -1000000000 |
| FLIGHT LEVEL | 0 07 010 | M | --- | 8839 |
| INDICATED AIRCRAFT ALTITUDE | 0 10 070 | M | 8839 | --- |
| PRESSURE (VERT. LOCATION) | 0 07 004 | 10**1 PA | -1000000000 | --- |
| DETAILED PHASE OF FLIGHT | 0 08 009 | CODE TABLE | --- | 3 |
| WIND DIRECTION | 0 11 001 | DEGREE TRUE | 120 | 120 |
| WIND SPEED | 0 11 002 | 10**-1 M/S | 98 | 98 |
| DEGREE OF TURBULENCE | 0 11 031 | CODE TABLE | --- | -1000000000 |
| MAX. DERIVED EQUIVALENT VERT. GUST | 0 11 036 | 10**-1 M/S | --- | -1000000000 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 101 | 10**-2 K | --- | 23065 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 001 | 10**-1 K | 2307 | --- |
| ACARS INTERPOLATED VALUES | 0 33 025 | CODE TABLE | --- | 3 |
| PHASE OF AIRCRAFT FLIGHT | 0 08 004 | CODE TABLE | 3 | 3 |
| AIRCRAFT ROLL ANGLE QUALITY | 0 02 064 | CODE TABLE | 0 | 0 |
| MIXING RATIO | 0 13 002 | 10**-5 KG/KG | -1000000000 | --- |

6.3	BUFR Trial Lido - DWD - CMC	ASC - Report EU3733 - 8th Oct 2003 20:21 UTC

| Element | Descriptor | Note / Dim. | Ref Value IUAX01 | Test Value IUAX40 |
| --- | --- | --- | --- | --- |
| AIRCRAFT REGISTRATION NUMBER | 0 01 008 | CCITT IA5 | EU3733 | EU3733 |
| AIRCRAFT FLIGHT NUMBER | 0 01 006 | CCITT IA5 | LH637 | --- |
| OBSERVATION SEQUENCE NUMBER | 0 01 023 | NUMERIC | --- | -1000000000 |
| TYPE OF STATION | 0 02 001 | CODE TABLE | 0 | --- |
| TYPE OF INSTRUMENT FOR WIND MEAS. | 0 02 002 | FLAG TABLE | 4 | --- |
| PRECISION OF TEMPERATURE | 0 02 005 | 10**-2K | 10 | --- |
| TYPE OF AIRCRAFT DATA RELAY SYSTEM | 0 02 062 | CODE TABLE | 3 | --- |
| ORIG. SPECIF. OF LATITUDE/LONGITUDE | 0 02 070 | CODE TABLE | 0 | --- |
| ACARS GROUND RECEIVING STATION | 0 02 065 | CCITT IA5 | -1000000000 | --- |
| LATITUDE (HIGH ACCURACY) | 0 05 001 | 10**-5 DEGREE | --- | 2445000 |
| LONGITUDE (HIGH ACCURACY) | 0 06 001 | 10**-5 DEGREE | --- | 5464333 |
| LATITUDE (COARSE ACCURACY) | 0 05 002 | 10**-2 DEGREE | 2445 | --- |
| LONGITUDE (COARSE ACCURACY) | 0 06 002 | 10**-2 DEGREE | 5464 | --- |
| YEAR | 0 04 001 | YEAR | 2003 | 2003 |
| MONTH | 0 04 002 | MONTH | 10 | 10 |
| DAY | 0 04 003 | DAY | 8 | 8 |
| HOUR | 0 04 004 | HOUR | 20 | 20 |
| MINUTE | 0 04 005 | MINUTE | 21 | 21 |
| SECOND | 0 04 006 | SECOND | -1000000000 | -1000000000 |
| FLIGHT LEVEL | 0 07 010 | M | --- | 183 |
| INDICATED AIRCRAFT ALTITUDE | 0 10 070 | M | 183 | --- |
| PRESSURE (VERT. LOCATION) | 0 07 004 | 10**1 PA | -1000000000 | --- |
| DETAILED PHASE OF FLIGHT | 0 08 009 | CODE TABLE | --- | 7 |
| WIND DIRECTION | 0 11 001 | DEGREE TRUE | 51 | 51 |
| WIND SPEED | 0 11 002 | 10**-1 M/S | 62 | 62 |
| DEGREE OF TURBULENCE | 0 11 031 | CODE TABLE | --- | -1000000000 |
| MAX. DERIVED EQUIVALENT VERT. GUST | 0 11 036 | 10**-1 M/S | --- | -1000000000 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 101 | 10**-2 K | --- | 30365 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 001 | 10**-1 K | 3037 | --- |
| ACARS INTERPOLATED VALUES | 0 33 025 | CODE TABLE | --- | 1 |
| PHASE OF AIRCRAFT FLIGHT | 0 08 004 | CODE TABLE | 5 | 5 |
| AIRCRAFT ROLL ANGLE QUALITY | 0 02 064 | CODE TABLE | 0 | 0 |
| MIXING RATIO | 0 13 002 | 10**-5 KG/KG | -1000000000 | --- |

BUFR Trial Lido - DWD - CMC	ENR - Report EU1547 - 8th Oct 2003 19:41 UTC

| Element | Descriptor | Note / Dim. | Ref Value IUAX01 | Test Value IUAX40 |
| --- | --- | --- | --- | --- |
| AIRCRAFT REGISTRATION NUMBER | 0 01 008 | CCITT IA5 | EU1547 | EU1547 |
| AIRCRAFT FLIGHT NUMBER | 0 01 006 | CCITT IA5 | LH4302 | --- |
| OBSERVATION SEQUENCE NUMBER | 0 01 023 | NUMERIC | --- | -1000000000 |
| TYPE OF STATION | 0 02 001 | CODE TABLE | 0 | --- |
| TYPE OF INSTRUMENT FOR WIND MEAS. | 0 02 002 | FLAG TABLE | 4 | --- |
| PRECISION OF TEMPERATURE | 0 02 005 | 10**-2K | 10 | --- |
| TYPE OF AIRCRAFT DATA RELAY SYSTEM | 0 02 062 | CODE TABLE | 3 | --- |
| ORIG. SPECIF. OF LATITUDE/LONGITUDE | 0 02 070 | CODE TABLE | 0 | --- |
| ACARS GROUND RECEIVING STATION | 0 02 065 | CCITT IA5 | -1000000000 | --- |
| LATITUDE (HIGH ACCURACY) | 0 05 001 | 10**-5 DEGREE | --- | 4898055 |
| LONGITUDE (HIGH ACCURACY) | 0 06 001 | 10**-5 DEGREE | --- | 393333 |
| LATITUDE (COARSE ACCURACY) | 0 05 002 | 10**-2 DEGREE | 4898 | --- |
| LONGITUDE (COARSE ACCURACY) | 0 06 002 | 10**-2 DEGREE | 393 | --- |
| YEAR | 0 04 001 | YEAR | 2003 | 2003 |
| MONTH | 0 04 002 | MONTH | 10 | 10 |
| DAY | 0 04 003 | DAY | 8 | 8 |
| HOUR | 0 04 004 | HOUR | 19 | 19 |
| MINUTE | 0 04 005 | MINUTE | 41 | 41 |
| SECOND | 0 04 006 | SECOND | -1000000000 | -1000000000 |
| FLIGHT LEVEL | 0 07 010 | M | --- | 10671 |
| INDICATED AIRCRAFT ALTITUDE | 0 10 070 | M | 10671 | --- |
| PRESSURE (VERT. LOCATION) | 0 07 004 | 10**1 PA | -1000000000 | --- |
| DETAILED PHASE OF FLIGHT | 0 08 009 | CODE TABLE | --- | 3 |
| WIND DIRECTION | 0 11 001 | DEGREE TRUE | 326 | 326 |
| WIND SPEED | 0 11 002 | 10**-1 M/S | 360 | 360 |
| DEGREE OF TURBULENCE | 0 11 031 | CODE TABLE | --- | -1000000000 |
| MAX. DERIVED EQUIVALENT VERT. GUST | 0 11 036 | 10**-1 M/S | --- | -1000000000 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 101 | 10**-2 K | --- | 22415 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 001 | 10**-1 K | 2242 | --- |
| ACARS INTERPOLATED VALUES | 0 33 025 | CODE TABLE | --- | 3 |
| PHASE OF AIRCRAFT FLIGHT | 0 08 004 | CODE TABLE | 3 | 3 |
| AIRCRAFT ROLL ANGLE QUALITY | 0 02 064 | CODE TABLE | 0 | 0 |
| MIXING RATIO | 0 13 002 | 10**-5 KG/KG | -1000000000 | --- |

BUFR Trial Lido - DWD - CMC	DES - Report EU6564 - 8th Oct 2003 20:28 UTC

| Element | Descriptor | Note / Dim. | Ref Value IUAX01 | Test Value IUAX40 |
| --- | --- | --- | --- | --- |
| AIRCRAFT REGISTRATION NUMBER | 0 01 008 | CCITT IA5 | EU6564 | EU6564 |
| AIRCRAFT FLIGHT NUMBER | 0 01 006 | CCITT IA5 | LH4266 | --- |
| OBSERVATION SEQUENCE NUMBER | 0 01 023 | NUMERIC | --- | -1000000000 |
| TYPE OF STATION | 0 02 001 | CODE TABLE | 0 | --- |
| TYPE OF INSTRUMENT FOR WIND MEAS. | 0 02 002 | FLAG TABLE | 4 | --- |
| PRECISION OF TEMPERATURE | 0 02 005 | 10**-2K | 10 | --- |
| TYPE OF AIRCRAFT DATA RELAY SYSTEM | 0 02 062 | CODE TABLE | 3 | --- |
| ORIG. SPECIF. OF LATITUDE/LONGITUDE | 0 02 070 | CODE TABLE | 0 | --- |
| ACARS GROUND RECEIVING STATION | 0 02 065 | CCITT IA5 | -1000000000 | --- |
| LATITUDE (HIGH ACCURACY) | 0 05 001 | 10**-5 DEGREE | --- | 3899500 |
| LONGITUDE (HIGH ACCURACY) | 0 06 001 | 10**-5 DEGREE | --- | -906833 |
| LATITUDE (COARSE ACCURACY) | 0 05 002 | 10**-2 DEGREE | 3900 | --- |
| LONGITUDE (COARSE ACCURACY) | 0 06 002 | 10**-2 DEGREE | -907 | --- |
| YEAR | 0 04 001 | YEAR | 2003 | 2003 |
| MONTH | 0 04 002 | MONTH | 10 | 10 |
| DAY | 0 04 003 | DAY | 8 | 8 |
| HOUR | 0 04 004 | HOUR | 20 | 20 |
| MINUTE | 0 04 005 | MINUTE | 28 | 28 |
| SECOND | 0 04 006 | SECOND | -1000000000 | -1000000000 |
| FLIGHT LEVEL | 0 07 010 | M | --- | 2923 |
| INDICATED AIRCRAFT ALTITUDE | 0 10 070 | M | 2923 | --- |
| PRESSURE (VERT. LOCATION) | 0 07 004 | 10**1 PA | -1000000000 | --- |
| DETAILED PHASE OF FLIGHT | 0 08 009 | CODE TABLE | --- | 11 |
| WIND DIRECTION | 0 11 001 | DEGREE TRUE | 74 | 74 |
| WIND SPEED | 0 11 002 | 10**-1 M/S | 72 | 72 |
| DEGREE OF TURBULENCE | 0 11 031 | CODE TABLE | --- | -1000000000 |
| MAX. DERIVED EQUIVALENT VERT. GUST | 0 11 036 | 10**-1 M/S | --- | -1000000000 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 101 | 10**-2 K | --- | 28015 |
| TEMPERATURE/DRY BULB TEMPERATURE | 0 12 001 | 10**-1 K | 2802 | --- |
| ACARS INTERPOLATED VALUES | 0 33 025 | CODE TABLE | --- | 3 |
| PHASE OF AIRCRAFT FLIGHT | 0 08 004 | CODE TABLE | 6 | 6 |
| AIRCRAFT ROLL ANGLE QUALITY | 0 02 064 | CODE TABLE | 0 | 0 |
| MIXING RATIO | 0 13 002 | 10**-5 KG/KG | -1000000000 | --- |

7.	Conclusions

The WMO BUFR Trial was performed in the period from 25th July to 24th October 2003 with the aim to validate the New BUFR Template for AMDAR.

The AMDAR BUFR data were encoded by the LH company Lido with its independently developed coding program. The trial partners KNMI, CMC and DWD were able to decode the transmitted operational test data faultlessly. CMC and DWD used independently developed decoders. KNMI used the same decoder as DWD, but in a different hardware and software environment.

As shown in chap. 6 the decoded test values IUAX40 meet the reference values IUAX01 exactly. This is also valid for the BUFR elements Latitude, Longitude and Temperature with the higher resolution of the IUAX40 values using scientific rounding rules.

Due to technical, non-formatting reasons, the test partners couldn't re-encode the BUFR reports as originally planned. However in the opinion of the author the correctness of the proposed New BUFR Template is adequately verified after the successful encoding and decoding of the test reports in an operational environment with independently developed coding programs.

8. 	Proposal

With reference to the statements above the introduction of the New BUFR Template for AMDAR is proposed to CBS ET.

9.	Acknowledgements

This report has been compiled at DWD Offenbach. The excellent co-operation of all colleagues at KNMI, CMC, Lido and DWD involved in the BUFR trial is gratefully acknowledged. Special thanks apply to Frank Maier, DWD, who edited and analysed the BUFR messages for this report.