6.  	CALIBRATION AND VALIDATION

- Instrument calibration

    - Introduction

Calibration is the process of quantitatively defining the satellite instrument response to known, controlled signal inputs. The calibration information is contained in a calibration formula, or calibration coefficients that are then used to convert the instrument output (“counts”, previously “analogue signals”) into physical units (e.g., a radiance value).  Instrument calibration is critical for any higher-level data processing, especially for deriving quantitative products or when data from different instruments need to be merged (e.g., composite imagery). For climate applications, the requirement for accurate calibration is particularly stringent since detection of small trends over long periods requires comparability of different instruments flown on different satellites at different times. Building homogeneous climate data records is contingent on very good calibration and error characterization.

The following considerations apply to passive and active instruments alike.

Five calibration domains should be generally considered: radiometric, spectral, spatial, temporal, and polarization. A complete calibration record should allow estimates of uncertainties in calibration parameters. Satellite instrument calibration should take into account all phases of an instrument’s lifetime: from design and pre-launch phases to post-launch, and on-orbit operations.

Inter-calibration of instruments against a common reference instrument allows achieving consistency among satellite measurements at a given point in time. By comparing model-simulated and observed satellite radiances in data assimilation schemes, major NWP centres can also help determine relative biases between instruments. Calibration to absolute standards is, however, necessary to allow traceability of errors and to detect any long-term drift over time.

Calibration using well-characterized, stable Earth targets (“vicarious” calibration) is a fall-back option when a satellite instrument cannot be directly traceable to an agreed reference standard, for example due to the absence of reliable on-board calibration device. Data records from past instruments can be “re-calibrated” retrospectively, if additional information on the state of these instruments becomes available, for example through comparison with reprocessed, well-known historical time series.

    - Factors affecting calibration

The response of an instrument to signal input, i.e., the relationship between the irradiance the instrument is exposed to and the numerical value assigned to the measurement (in physical units, e.g., W(m-2) depends on several elements, such as:

- viewing geometry, shielding effects, stray-light, antenna pattern

- detector sensitivity and aging

- filter optics, its possible contamination and its stability

- temperature of all parts of the instrument, including front-end optics, detector and back-end electronics (focal plane electronics, pre-amplifier, etc.)

- signal processing system (gain, analogue-digital converter, etc.).

All these elements contribute to determine the Spectral Response Function (SRF) and the Point Spread Function (PSF) that characterize the instrument from a radiometric and geometric viewpoint, respectively. They must be modelled before launch and monitored in flight by a set of onboard internal measurements (“housekeeping”). The instrument model and the housekeeping system are useful for understanding the status of the instruments and its trend as well as for prediction and correction of biases.  However, it is generally not possible to analytically describe the exact variation of the instrument response resulting from these factors.  Reference measurements are mandatory to characterize the actual calibration.

    - Pre-flight calibration

The pre-launch calibration of an instrument is performed in the laboratory, by using accurately known radiation sources under controlled conditions.  Simulating all possible instrument states and stress factors before launch is very important because it is the only way to accurately characterize and model the instrument before it is exposed to the harsh orbital environment. Housekeeping systems and instruments need to be built robust enough to withstand physical stress incurred during launch, commissioning, and exploitation phases. Housekeeping data, in combination with post-launch calibration information, will then allow operators to infer the calibration status of the instrument in orbit, and to resolve on-orbit anomalies.

    - On-board calibration

On-board calibration enables monitoring the instrument performance (and stability) while in orbit.  It is performed by using reference targets (e.g., blackbodies in IR, solar diffusers and lamp line sources in SW) for passive instruments or by internal calibration systems (e.g., gain monitors) for active instruments. Some heritage instruments have been in operation without adequate means of on-board calibration, such as the Advanced Very High Resolution Radiometer (AVHRR) which provides long-term observations in VIS and NIR. Other means of calibration (e.g., vicarious, inter-calibration) need to be used for characterizing such instruments. Accuracy of in-flight instrument calibration is a function of the stability of on-board calibration systems (e.g., blackbodies, gain monitors) throughout the instrument’s lifetime. Therefore, the calibration itself must be regularly checked by inter-calibration against highly accurate references.

In the case of IR instruments, if the radiometer detectors are assumed to have linear response, the output voltage is given as:

where R is input radiance, α  is radiometer responsivity, and V0 is system offset. Calibration consists of determining α, V0, which is accomplished by exposing the radiometer to at least two reference targets with significantly different brightness temperatures.

For IR and MW instruments, one reference target is deep space, at a temperature of 2.725 K.  Direct viewing of deep space is not always possible for instruments on a satellite platform.  For instance, pushbroom instruments constantly pointing to the Earth’s surface need to be equipped with a sub-reflector to supply the deep space view at intervals.  A second target is usually a well-characterized source with temperature in the medium to upper dynamic range, often a blackbody, which is ideally traceable to SI standards, i.e., a radiance scale provided by a national metrology institute.

If the instrument response is not linear across the dynamic range, this needs to be accounted for in the pre-launch instrument characterization, e.g., by using a quadratic function, or through linearization in different parts of the dynamic range and possible addition of a second blackbody kept at a different temperature.

For UV, VIS and NIR instruments, on-board calibration is more challenging since it is affected by many factors. On the low-signal extreme, deep space is a useful reference, provided that disturbing effects (e.g., reflections from other parts of the spacecraft) are avoided.  At the high-signal end, an absolute source is generally replaced by Sun diffusers that provide a relatively stable reference. The Moon also may be used as a reference target, with the advantage that it can be viewed without an attenuator; however it must be used in conjunction with an accurate model of the moon’s brightness. Neither the solar diffuser nor the Moon provides an absolute calibration. Another system often used is a bench of lamp line sources of well-controlled intensity.  Spectrally-dependent polarization effects induced by the reflecting surfaces of the instrument optics also need to be taken into account

Another problem with on-board calibration is that often the instrument structure does not allow illumination of the full primary optics with reference sources.  For example, a spin-stabilised radiometer in GEO uses an internal blackbody requiring a model of the contributions of the telescope and foreoptics to the background radiation.  Often, the reference source only illuminates a fraction of the total instrument optics, therefore is more used for stability monitoring than for absolute calibration.

    - Vicarious calibration

On-board calibration can be complemented by stable ground targets used as references in a process termed vicarious calibration.  The target needs to be well characterised in order to infer the emitted or reflected radiance towards space.  The combined effects of the viewing geometry and, in shortwave, the bi-directional reflectance distribution function (BRDF) of surface and atmosphere combined must be taken into account. The radiative transfer through the atmosphere between the satellite and the ground reference source must be accurately known at the time of the satellite overpass.  In a cloud-free case, the short-wave spectrum is particularly affected by aerosols, whereas the long-wave spectrum is particularly influenced by the presence of water vapour.

Vicarious calibration can involve different kinds of targets: polar ice fields as blackbody for MW radiometers; snow fields, sun glint, homogeneous desert areas, deep convective cloud tops, for the upper end of the VIS dynamic range; cloud-free ocean surface for dark VIS targets; cube-corner reflectors for SAR; the rain forest as blackbody for radar scatterometers; etc. Calibration field sites equipped with in-situ observations are used for the calibration of high spatial resolution space-based instruments. During initial payload commissioning or at regular intervals, aircraft over-flights of a target area synchronous with the satellite overpass offer additional vicarious calibration data.

    - Inter-calibration by simultaneous observations

Inter-calibration of satellite instruments involves relating the measurements of one instrument to those of another. This is done for the dual purposes of:

- providing vicarious calibration to instruments that have no or defective internal calibration device (inter-calibration being performed against a high-quality, well-calibrated instrument serving as a reference);

- merging the data from several instruments for the generation of consistent time series.

Inter-calibration of instruments operated during the same period requires careful collocation wherein instrument outputs are compared when the instruments are viewing the same Earth scenes, at the same times, from the same viewing angles. Simultaneous observations from collocations between GEO imagers and a LEO reference imager have been performed on a monthly basis for almost 30 years as a means to normalize GEO satellite imagery; this has been done within the International Satellite Cloud Climatology Project (ISCCP) of the World Climate Research Programme (WCRP). More recently, the Global Space-based Inter-calibration System (GSICS) has developed an operational methodology for such inter-calibrations, specifically for simultaneous collocated observations. The methodology considers the trade-off between accurate spatial-temporal co-registration of the instruments and frequency of occurrence of such events, and takes into account the corrections to be applied for:

- different viewing geometries (with regard to both instrument scan angle and solar position);

- different atmospheric states in the line of sight, including aerosol and clouds;

- different spectral response functions.

It should be noted that simultaneous observations between two sun-synchronous satellites can only occur at the intersections of their orbital planes, which are always located at a given local solar time and at a given, generally high north or south, latitude.

    - Bias adjustment of long-term data records

An alternative approach for instrument inter-calibration, which is less demanding in computation and applicable a posteriori to long data series, is to simply compare the statistical distribution of overlapping time series of two satellite instrument data records without imposing individual matches of individual scenes. This approach enables identifying the relative bias between the two data records. The observed bias is analyzed so that the different conditions of observations (e.g., different local solar times) are accounted for leaving the remaining bias as that part that is actually due to difference in instrument calibration. One successful example of this approach is the inter-calibration of the nine Microwave Sounding Units (MSU) onboard the early NOAA satellites, which represent a 26 year record of global tropospheric temperatures.

    - Using calibration information

The type of calibration information available depends on the processing level and on the instrument considered. Each instrument has its own operating mode and calibration cycle, which includes regular measurements of calibration targets each time a certain number of observations is performed. For instance, Table 6.1 indicates the calibration cycles of AMSU-A, MHS and HIRS/4.

| Table 6.1 – Examples of observation/calibration cycles |
| --- |
|  | AMSU-A | MHS | HIRS/4 |
| Number of Earth views | 1 line of 30 pixels | 1 line of 90 pixels | 38 lines of 56 pixels |
| Number of warm target views | 2 (~ 300 K) | 4 (~ 273 K) | 48 (~ 290 K) |
| Number of cold target views | 2 (deep space ~ 2.73 K) | 4 (deep space ~ 2.73 K) | 56 (deep space ~ 2.73 K) |
| Overall duration of the cycle | 8 s | 8/3 s | 256 s |

An important step in the pre-processing from level 0 to level 1b data is to extract the calibration information in the form of warm/cold view counts and then to compute the resulting calibration coefficients in accordance with the calibration model defined by the satellite operator for the particular instrument (e.g. linear or quadratic calibration function, Look Up Table, etc.). This provides the “operational calibration” for that instrument.

For applications requiring high accuracy and consistency among different instrument data records, a correction can be applied on top of the operational calibration in order to take into account the latest results of inter-calibration activities. Such corrections are provided by GSICS. The corrected calibration coefficients may be included in the level 1.b / level 1.5 data formats as additional calibration information.

    - Traceability of space-based measurement

While inter-calibration can ensure consistency between satellite instruments, it does not necessarily provide traceability to the International System of Units (SI) unless a reference instrument in orbit is SI traceable. There are major challenges to achieving SI traceability in orbit, as most sensors degrade physically after launch. Achieving SI traceability poses instrument design challenges and remains a research topic for all but a few measurement types.

The Climate Absolute Radiance and Refractivity Observatory (CLARREO) mission proposed by the United States National Research Council consists of a highly accurate IR interferometer with a high emissivity reference black-body using a multiple phase-change cells thermometer, a UV-VIS-NIR spectrometer calibrated by Sun and Moonviews, a cryogenically cooled active cavity radiometer, and radio occultation measurements. This suite of instruments is intended to provide absolutely traceable measurements of the full Earth-emitted and reflected solar spectrum. Implementing and maintaining such a mission would provide an anchor point in support of the calibration and traceability of the whole fleet of operational radiometers.

For measurement traceability, one should take advantage of instruments that do not depend on radiometric calibration, such as radio-occultation and Sun or star occultation sensors (see Sections 2.2.4.3 and 2.2.5.1).

  - Product validation

    - Factors to be accounted for in validation

Validation is the process of assessing, by independent means, the quality of the data products derived from satellite instrument measurements.  Product validation should be performed by product developers, downstream of instrument calibration, and should be documented in instrument-specific product validation plans. Guidelines for documenting product quality are provided in the Quality Assurance Framework for Earth Observation (QA4EO).

Geophysical products are generated from satellite data (often radiance measurements) by applying an algorithm that is either physically or empirically based. Comparing the retrieved products, and their trends with in-situ observations or model outputs is an important part of the process to assess and document the reliability of given retrieval algorithms in deriving these products as well as to define its domain of applicability.

If a particular trend is detected, it may relate to the instrument’s performance; a careful analysis of the satellite instrument’s calibration and environmental data must be performed before any empirical correction can be applied.

For many products validation is a complex problem since the comparison between products derived from satellite measurements and independent reference products often from in situ measurements is subject to several errors: (1) an inherent satellite-derived product error, (2) the error in the reference data, and (3) the error introduced by the comparison methodology, often due to non-collocation in time and space. In general, different measurement techniques measure different things: a satellite observation usually refers to a relatively large area (the instantaneous field-of-view, IFOV) and nearly-instantaneous measurements (within milliseconds); ground (in-situ) measurements are generally very local and integrated over a relatively long time. Ground-based remote sensing usually provides information representative of the atmospheric column. Comparison of the different types of measurement requires down-scaling or up-scaling methods that can introduce spatially or temporally dependent errors.

A validation assessment model can be used to improve comparisons by understanding and accounting for these differences and to better account for the advantages and disadvantages of different validation approaches. Validation campaigns run by satellite operators are usually accompanied by such an assessment model.

It should be noted that for certain satellite products, independent validation measurements may not exist, and validation can only be performed by evaluating the impact of the product when used in an application (e.g., when assimilated in a NWP model).

    - Validation strategies

Validation of satellite-derived products should follow defined best-practice, variable-dependent protocols, such as those developed by the CEOS Working Group on Calibration and Validation (WGCV). Validation of satellite-derived parameters and products can be carried out using the following sources:

- Ground-based in-situ measurements

- Ground-based remote sensing measurements

- Model comparison and assimilation

- Other satellite-derived or blended products of a similar type.

For using such validation sources, it is essential that:

- Measurement errors are well-known

- Temporal and spatial sampling follow best-practice protocols

- Sampling is representative of the typical application-dependent environment (e.g., climatic zones, marine regimes, atmospheric regions, land cover types).

For example, to support validated generation of combined sea-surface temperature (SST) satellite products, the Group for High-Resolution SST has developed a comprehensive validation strategy which includes detailed description of protocols, strategies to harmonize validation concepts for different satellite sensors contributing to SST measurements, needs for in-situ (buoy) measurements as in-situ data sources, and metrics to monitor product quality.

    - Impact studies

Experience shows that the results of direct validation are less significant for some satellite-derived products than for others.  Since validation tests combine the effects of different error sources (satellite product, ground measurement, comparison method), the error due to the satellite product itself may be difficult to single out.  For certain geophysical variables ground measurements may be rather inaccurate.  For others the comparison method may depend too much on the observation environment.

An option to evaluate a product for a particular application is thus to evaluate its impact on the application skill.  In this case, the evaluation reflects the quality of the product, combined with the ability of the application to use it. For example, NWP models showed marginal impact for a couple of decades from atmospheric temperature-humidity soundings; this changed to significant positive impact only when direct radiance assimilation was introduced.  An opposite example is the assimilation of cloud-motion winds, which exhibited a strong positive impact at first attempt, although the initial validation exercises were disappointing.

In summary, validation requires rigorous analysis of all error sources and of all steps in the comparison method.  If the analysis shows that the error of the satellite product cannot be singled out, performing an impact study is a remaining validation mechanism.

7.  	CROSS-CUTTING ISSUES

7.1	Frequency protection issues

# 7.1.1 Overall frequency management

A critical issue for sustaining space-based Earth observations is whether the radio-frequency spectrum in the MW range (1 to 300 GHz and above) remains available.  This is important for:

- passive observations of the Earth surface (in windows) and atmospheric trace gases (in absorption bands)

- active observations with radar (altimeters, scatterometers, SAR)

- communications necessary for data downloading and satellite control.

The use of the radio-frequency spectrum is coordinated at the global level by the International Telecommunications Union (ITU).  “Radio Regulations” are adopted by ITU Members at the World Radio Conferences every four years. The ITU is regulating the allocation of radio-frequency bands to the different applications known as “services”, such as fixed and mobile telecommunications, broadband mobile applications, radio navigation, ground-based radars, short-range devices, electronic news gathering, etc. Earth observation applications are identified by ITU as two particular services: the Earth Exploration Satellite Service (EESS) and Meteorological Satellite Service (METSAT).  While some bands are allocated to a service on an exclusive basis, most bands are allocated to several services with certain conditions (e.g., limitation of the number, the emitting power, and the geographical distribution of sources) that aim at avoiding harmful interference.

With the rapid expansion of the telecommunication sector and its increasing spectrum needs, the protection of frequencies required for EESS and METSAT has become very critical. Concerns include:

- interference from uncontrolled emissions within exclusive EESS or METSAT bands, or to out-of-band emissions from nearby frequency bands;

- sharing bands under conditions that are not stringent enough to guarantee reliable protection;

- desire of other services to expand to bands formerly allocated to EESS or METSAT;

- need of EESS or METSAT to use new bands arising because of the evolving remote sensing technology (e.g., MW above 300 GHz), or growing data rates, or expanding telecommunication bandwidths.

In addressing these issues, one must note that frequencies used for passive measurements cannot be selected in any part of the spectrum: they are determined by the physics and must correspond to either absorption peaks of atmospheric components or window channels. Natural emissions are extremely weak compared to most artificial sources, and hence they are easily corrupted.  Therefore, we must consider the passive radiometric bands as a natural heritage to be preserved.

# 7.1.2	Passive MW radiometry

The spectral MW range utilised for Earth observation stretches from ( 1.4 GHz (e.g., for ocean salinity) to ( 2500 GHz and beyond. The most critical issues are for frequencies below 300 GHz. The use of frequencies above ( 300 GHz is still emerging; moreover, since the water vapour continuum prevents viewing the lower troposphere, most of the instruments operating at those frequencies are designed for atmospheric chemistry and exploit limb viewing, which makes them less prone to interferences from ground sources.  The ITU has identified a limited number of bands allocated to EESS, for which active uses are either prohibited or limited.  As the radio-frequency spectrum becomes more crowded and users have a need for higher data rates, there is increasing pressure on higher frequencies, leading the ITU to share EESS bands with active services.  Only a few narrow bands are assigned to EESS on an exclusive basis ensuring reliable legal protection.  This has the following effects:

- the position of the allocated MW channels often does not coincide with the sensitivity peak for the needed geophysical variable or with a spectral area free of contamination from other effects;

- the protected bandwidth may be so narrow that the SNR is poor; this may force consideration of an unprotected band where a wider bandwidth is available, accepting the risk of interference.

Unfortunately, the pressure from other users of the spectrum, including commercial and mobile services, is continuously increasing; specialised groups of WMO, CGMS and space agencies must continuously monitor the situation at each update of ITU Regulations.

7.1.3	Active MW sensing

The problem of frequency protection also holds for active sensing (altimeters, scatterometers, SAR).  For some applications of radar backscattering like precipitation measurement, the sensing frequency has to be chosen in relation with the target properties. In other cases, like altimetry or SAR imagery, it is not very selective and there is some flexibility to find a frequency allocation in  any of the L, S, C, X, Ku, K, Ka, V, or W band (see Table 2.8 for definitions) .

# 7.1.4	Satellite operation and communication frequencies

Frequency allocation for satellite-ground communications is another critical issue.  In this case, as it involves active usage, the ITU Regulations are very restrictive in terms of allowed frequency, bandwidth, and emitted power.  The consequences are:

- higher cost for a ground receiving station that works with low signals;

- higher cost because insufficient bandwidth available in one band for the data rate to be handled forces relocation to higher-frequency bands that require more challenging technology and antenna pointing;

- ultimately, more difficulty to secure a frequency, particularly for real-time transmission; fewer frequencies are available, and sometimes this provokes interferences between satellites of the same family that are in orbit simultaneously.

In any event, frequency protection is difficult to guarantee, and users experience problems, especially in industrialised areas. Table 7.2 provides the frequency bands allocated to data transmission to and from meteorological satellites (From Handbook on Use of Radio Spectrum for Meteorology:  Weather, Water and Climate Monitoring and Prediction, ITU-WMO, 2008, updated after WRC-12).

# TABLE 7.2: Frequency bands for use by meteorological satellites for data transmission

| Frequency band (MHz) | MetSat allocations |
| --- | --- |
| 137-138 | Primary for space-to-Earth direction |
| 400.15-401 | Primary for space-to-Earth direction |
| 401-403 | Primary for Earth-to-space direction |
| 460-470 | Secondary for space-to-Earth direction |
| 1 670-1 710 | Primary for space-to-Earth direction |
| 7 450-7 550 | Primary for space-to-Earth direction, geostationary satellites only |
| 7 750-7 900 | Primary for space-to-Earth direction, non-geostationary satellites only |
| 8 025-8 400 | Primary for space-to-Earth direction for Earth exploration-satellites (Note 1) |
| 8 175-8 215 | Primary for Earth-to-space direction |
| 18 000-18 300 | Primary for space-to-Earth direction in Region 2, geostationary satellites only |
| 18 100-18 400 | Primary for space-to-Earth direction in Regions 1 and 3, geostationary satellites only |
| 25 500-27 000 | Primary for space-to-Earth direction for Earth exploration-satellites (Note 1) |
| Note − Since the MetSat is a sub-class of the Earth exploration-satellite service, Earth exploration-satellite service allocations (as an example: 25 500-27 000 MHz) can also be used for the operation of MetSat applications. |

  - International coordination

    - The Coordination Group for Meteorological Satellites (CGMS)

With a focus on long-term sustained missions, the CGMS, in accordance with an agreed baseline, is coordinating satellite constellations in geostationary and low-Earth orbit in support of WMO and co-sponsored programmes. Established in 1972 with a focus on weather monitoring by geostationary satellites for weather forecasting, CGMS initially defined common standards for low-resolution image dissemination in “weather fac-simile” (WEFAX) and for the International Data Collection System to support mobile stations viewed by the different satellites. The scope of CGMS was extended in 1992 to polar-orbiting meteorological satellites and is now increasingly addressing key climate observations. The agreed baseline describes the missions to be maintained on a long-term basis; it serves as a reference for the intended contributions of the participating members to the Global Observing System (GOS) in response to the WMO Vision for the GOS in 2025. CGMS defines technical standards or best practices to ensure inter-operability across the global system. It has developed contingency plans which provide a framework for action in case of satellite outage or other unexpected difficulties in fully implementing the agreed baseline.

CGMS operates through Working Groups dedicated to: (i) Satellite Systems and Telecommunications, (ii) Satellite Products, (iii) Continuity and Contingency Planning, and (iv) Satellite Data Services. Together with WMO, CGMS originated major collaboration initiatives including GSICS, SCOPE-CM, and the Virtual Laboratory for Education and Training. CGMS works in partnership with several international science groups, is active on a continuous basis, and helps to organise working group meetings at two-year intervals:

- ITWG (International TOVS Working Group)

- IWWG (International Winds Working Group)

- IPWG (International Precipitation Working Group)

- IROWG (International Radio Occultation Working Group).

    - The Committee on Earth Observation Satellites (CEOS)

CEOS was established in 1984 by the Group of Seven (most industrialised countries of the world).  Unlike CGMS, at first CEOS was focussed on land observation satellites (initially Landsat, then also SPOT and IRS), specifically on new technologies such as SAR.  Later, the scope of CEOS was extended to all Earth observation programmes but with less emphasis on meteorology until a new interest arose for climate issues.  An important activity since its establishment was calibration and validation, through the Working Group on Calibration and Validation (WGCV). Other CEOS working groups are the Working Group on Information Systems and Services (WGISS), the Working Group on Capacity Building and Data Democracy (WGCap), and the new Working Group on Climate (WGClimate).

The coordination activity of CEOS is now articulated around the concept of “constellations” to share experience in the development of algorithms, to standardize data products and formats, to exchange information regarding the calibration and validation of measurements, to facilitate the timely exchange of and access to data products from existing and planned missions, and to facilitate planning of new missions. There are currently seven “constellations”:

- ACC (Atmospheric Composition Constellation)

- LSI (Land Surface Imaging constellation)

- OST (Ocean Surface Topography constellation)

- PC (Precipitation Constellation)

- OCR (Ocean Colour Radiometry constellation)

- OSVW (Ocean Surface Vector Wind constellation).

- SST (Sea Surface Temperature constellation).

7.3	Satellite mission planning

    - Satellite programme lifecycle

In the early days of satellite meteorology, the lifecycle of a satellite mission was only a few years. Mission definition, satellite design, system development, and science demonstration happened in one or two years each;  the exploitation period was short and the ground segment often under-dimensioned.

In recent years, an operational programme (e.g., for meteorological purposes) generally proceeds with the following phases:

- Phase 0: User requirements definition, involving the user community, and Mission requirements definition, i.e., identification of the possible techniques to fulfil the user requirements: this lasts about 3 to 4 years;

- Phase A: Feasibility assessment at system level (including a preliminary definition of the ground segment) and of critical instruments (possibly including instrument simulations); and rough order-of-magnitude cost estimation: duration is about 2 years;

- Phase B: Preliminary design, preparatory activities (including airborne campaigns), detailed cost estimation: this takes about another 2 years;

- Phase C: Detailed design and development and testing of all systems (including the ground segment) and subsystems: this phase is the longest requiring about 5 years;

- Phase D: Integration of all subsystems, testing of the whole satellite, and launch campaign: this is often accomplished in 1 year.

Adding some time for the decision making and approval processes, and for in-orbit commissioning, the duration of the development phase is of the order of 15 years.

- Phase E, the exploitation phase, is generally aimed at 15 years for an operational programme including a series of 3 or 4 satellites, with some overlap for contingency purposes (typical lifetime of a LEO satellite is 5 years, of a GEO 7 years). The duration of a satellite generation is a trade-off between the need for a long series to pay-off the development cost and the user learning curve, on one hand, and the need to develop a new generation of satellite instruments in order to benefit from state-of-the-art technology, on the other hand.

The organisation of a space programme involves many participants: the applications community, scientific institutes, R&D space agencies, industry, and governments with their industrial policy and budget constraints. In the case of Earth observation programmes with world-wide scope, coordination with many international partners must be accomplished as much as possible, which may further complicate the decision-making process.

    - Continuity and contingency planning

Continuity of space-based observations has been a critical requirement for the meteorological satellite constellation in geostationary orbit, ever since nowcasting and severe weather forecasting, including tropical cyclone warning, began relying on satellite monitoring. The operational continuity of GEO imagery entails round-the-clock operation, high availability, near-real time data dissemination, and long-term continuity guaranteed by a robust programme that includes provisions for in orbit back-up. When the polar-orbiting constellation was established, and NWP models were increasingly relying on satellite sounding (IR, MW and radio-occultation) and other key satellite observations such as ocean surface winds, a similar requirement for operational continuity was applied to the morning and afternoon satellites that became the core meteorological constellation in polar-orbit. A baseline configuration of the operational space-based observing system was defined and committed upon by the satellite operators contributing to WMO programmes.

While satellite operators committed to give their best efforts to maintain the geostationary and the polar Sun-synchronous constellations, CGMS developed a Global Contingency Plan (see 7.3.1 and box below) providing a technical and legal framework for contingency measures to be taken on a “help-your-neighbour” basis in case of deficiency of one of the elements of the operational configuration.

For geostationary satellites contingency support can be provided if the number of satellites is sufficiently high and their nominal positions are appropriately spaced along the equator (see, for instance, Fig. 4.1).  Moving a satellite from one longitude to another requires little fuel if implemented at a slow pace.  Per the contingency plan, several satellites are maintained in back-up positions and it is possible to relocate a satellite to fill a gap through a manoeuvre lasting a few days or weeks depending on the urgency and the fuel available onboard. Several examples have taken place:  a spare Meteosat satellite was moved to cover the West Atlantic Ocean at the time when the GOES system suffered a launch delay in the early 1990’s; a spare GOES satellite filled the gap in the Western Pacific Ocean during the transition from GMS to MTSAT in the early 2000’s; and the Indian Ocean position has been covered, at instances in the last two decades, by GOES and Meteosat satellites.

# CGMS continuity and contingency planning

The CGMS baseline defines (i) a geostationary constellation comprising six satellites nominally located at fixed longitudes (135°W, 75°W, 0°, 76°E, 105°E, 140°E) and performing a set of agreed missions, (ii) a core meteorological constellation in polar sun-synchronous orbit performing imagery and sounding, and (iii) different constellations dedicated to additional missions in either sun-synchronous or inclined low Earth orbits. The CGMS Working Group on continuity and contingency planning keeps under review the implementation of the baseline, the availability of in-orbit back-ups and the risks of interruption of key missions.

CGMS has adopted a Global Contingency Plan which includes guidelines to ensure continuity e.g. in terms of in orbit back-up and re-launch policy, sets criteria for entering into contingency mode, and identifies actions to be taken in such contingency situation. In particular, the Global Contingency Plan defines a generic procedure for relocating a spare geostationary satellite to take over from a failing satellite, which is referred to as the “Help your neighbour” strategy. This global plan is supplemented by bilateral contingency agreements among geostationary satellite operators. On several occasions over the past three decades such contingency relocations have been essential to preserve the continuity of vital operational missions.

For sun-synchronous satellites contingency is more complicated.  Changing the orbital plane of a satellite requires a very large amount of fuel and is not envisaged, apart from the natural drift of the orbital plane due to precession or orbit keeping manoeuvres to correct this drift. The contingency plan therefore focuses on the availability of back-up satellites in each orbital plane along with regular spacing of the Equatorial Crossing Times (ECT) of these planes.

When WMO adopted its “Vision for the GOS in 2025”, the scope of the operational space-based observing system was extended to climate monitoring, reflecting both the requirement to monitor the climate on a continuing basis, and the maturity of space-based systems evolving from research and development to an operational status. In response, a new baseline was subsequently defined and adopted by CGMS that incorporates a number of climate-oriented missions. Continuity is as crucial for climate monitoring as for operational weather forecasting, however the requirements are different because climate monitoring involves different time scales. On one hand, near-real time availability and short-term gaps in a daily cycle are not driving requirements. On the other hand, major importance is attached to long-term continuity and stability of measurements throughout decades. The GCOS Climate Monitoring Principles require systematic overlap between all consecutive satellites to allow for inter-calibration and traceability. Stability and traceability could also be achieved through maintaining one highly secured reference mission, with in orbit back-up, that serves as a calibration reference standard for all the others (as discussed in Section 6.1.9).  Such a provision should be a major element in the definition of an Architecture for Climate Monitoring from Space.

7.3.3     Long-term evolution

The evolving user requirements for satellite data and the dramatic progress of space and remote-sensing technology call for continuous improvements to satellite systems and instrumentation.

At the same time, the strong pressure on resources stresses the need to seek an optimization of the global effort that assures the availability of a comprehensive observing system and avoids unnecessary redundancy beyond the required margins for robustness. Optimization is also needed in the development, validation, and sustained processing of derived products and requires data sharing, interoperability, and quality assurance. Global coordination under the auspices of the WMO aims at ensuring such optimization, building on the Rolling Review of Requirements, the high-level guidance provided by the Vision of the Global Observing Systems, the Statement of Guidance in each application area, and the Implementation Plan for Evolution of the Global Observing Systems which consolidates the recommendations to observing system implementation agents. A notable initiative is also the Architecture for Climate Monitoring from Space, promoted by WMO, CEOS, and CGMS to provide an end-to-end response from the space-based observing system to the climate monitoring requirements.

_____________________

# REFERENCES

Observing System Capability Analysis and Review (OSCAR) database and tool, WMO, (http:www.wmo.int/oscar)

# W.P. Menzel,  Applications with meteorological satellites, WMO/TD No. 1078, SAT-28, 2001

R.V. Datla, J.P. Rice, K.R. Lykke, C. Johnson, J.J. Butler, X. Xiong,” Best Practice Guidelines for Pre-Launch Characterization and Calibration of Instruments for Passive Optical Remote Sensing”, NISTIR) – 7637, 2009

G. Ohring, Achieving Satellite Instrument Calibration for Climate Change (ASIC3), Center for Satellite Applications and Research, NOAA, 2008

# C.L. Parkinson, A. Ward, M.D. King, Earth Science Reference Handbook, NASA, GSFC, 2006

Handbook on Use of Radio Spectrum for Meteorology:  Weather, Water and Climate Monitoring and Prediction, ITU-WMO, 2008

G. Chander, T.J. Hewison, N. Fox, X. Wu, X. Xiong, W.J. Blackwell, Overview of Intercalibration of satellite instruments, IEEE Transactions on Geoscience and Remote Sensing, Vol. 51, No.3, March 2013

Tobin, D. C., and Coauthors, 2006a: Radiometric and spectral validation of Atmospheric Infrared Sounder observations with the aircraft-based Scanning High-Resolution Interferometer Sounder. J. Geophys. Res., 111, D09S02, doi:10.1029/ 2005JD006094.

Tobin, D. C., H. E. Revercomb, C. C. Moeller, and T. S. Pagano, 2006b: Use of Atmospheric Infrared Sounder high-spectral resolution spectra to assess the calibration of Moderate Resolution Imaging Spectroradiometer on EOS Aqua. J. Geophys. Res., 111, D09S05, doi:10.1029/2005JD006095.

# ACRONYMS

| 3MI | Multi-viewing Multi-channel Multi-polarisation Imager (on EPS-SG) |
| --- | --- |
| AATSR | Advanced Along-Track Scanning Radiometer (= ATSR-2) (on Envisat) |
| ABI | Advanced Baseline Imager (on GOES-R) |
| ABM | Apogee Bust Motor |
| ACC | Accelerometer (on SWARM) |
| ACC | Fraction Correct Accuracy |
| ACE | Advanced Composition Explorer (of NASA) |
| ACE-FTS | Atmospheric Chemistry Experiment - Fourier Transform Spectrometer (on SCISAT) |
| ACRIM-III | Active Cavity Radiometer Irradiance Monitoring - III (on ACRIMSat) |
| ACRIMSat | Satellite carrying ACRIM (of NASA) |
| ADEOS | Advanced Earth Observing Satellite (original name: “Midori”) (of JAXA) |
| ADM-Aeolus | Atmospheric Dynamics Mission - Aeolus (of ESA) |
| AEISS | Advanced Electronic Image Scanning System (on KOMPSAT-3) |
| AHI | Advanced Himawari Imager (on Himawari 8 and 9) |
| AIRS | Atmospheric Infra-Red Sounder (on Aqua) |
| ALADIN | Atmospheric Laser Doppler Instrument (on ADM-Aeolus) |
| ALI | Advanced Land Imager (on NMP EO-1) |
| ALOS | Advanced Land Observing Satellite (original name: “Daichi”) (of JAXA) |
| AlSat | Algeria Satellite (of CNTS) |
| ALT | Radar Altimeter (on HY-2A) |
| AltiKa | Ka-band Altimeter (on SARAL) |
| AM or a.m. | Ante Meridiem (morning) |
| AMAZONIA | AMAZONIA (on INPE) |
| AMI-SAR | Active Microwave Instrument - SAR mode (on ERS) |
| AMI-SCAT | Active Microwave Instrument - Scat mode (on ERS) |
| AMR | Advanced Microwave Radiometer (on Jason-2/3) |
| AMSR-2 | Advanced Microwave Scanning Radiometer - 2 (on GCOM-W) |
| AMSR-E | Advanced Microwave Scanning Radiometer for EOS (on Aqua) |
| AMSU-A | Advanced Microwave Sounding Unit - A (on NOAA 15 to 19, MetOp, Aqua) |
| AMSU-B | Advanced Microwave Sounding Unit - B (on NOAA-15/16/17) |
| AOPOD | Radio-occultation receiver (on KOMPSAT-5) |
| APS | Aerosol Polarimetry Sensor (on Glory) |
| Aqua | EOS-Aqua (of NASA) |
| Aquarius | Aquarius (on SAC-D) |
| ASAR | Advanced Synthetic Aperture Radar (on Envisat) |
| ASCAT | Advanced Scatterometer (on MetOp) |
| A-SCOPE | Advanced Space Carbon and Climate Observation of Planet Earth (ESA study) |
| ASI | Atmospheric Sounding Interferometer (on FY-3 D to G) |
| ASI | Agenzia Spaziale Italiana |
| ASM | Absolute Scalar Magnetometer (on SWARM) |
| ASPRS | American Society for Photogrammetry and Remote Sensing |
| ASTER | Advanced Spaceborne Thermal Emission & Reflection radiometer (on Terra) |
| ATI | Apparent Thermal Inertia (a proxy of Soil moisture) |
| ATLID | Atmospheric Lidar (on Earth-CARE) |
| ATMS | Advanced Technology Microwave Sounder (on SNPP, JPSS) |
| ATS | Application Technology Satellite (of NASA) |
| ATSR | Along-Track Scanning Radiometer (on ERS-1) |
| ATSR-2 | Along-Track Scanning Radiometer (on ERS-2) |
| Aura | EOS-Aura (of NASA) |
| AVHRR/3 | Advanced Very High Resolution Radiometer (on NOAA, MetOp) |
| AVNIR | Advanced Visible and Near-Infrared Radiometer (on ADEOS-1) |
| AVNIR-2 | Advanced Visible and Near-Infrared Radiometer - 2 (on ALOS) |
| AWFI | Advanced Wide Field Imager (on AMAZONIA) |
| AWIFS | Advanced Wide Field Sensor (on ResourceSat) |
| BILSat | BILTEN Satellte (of TÜBITAK-UZAY) |
| BILTEN | Information Technologies and Electronics Research Institute (in Turkey), now UZAY |
| BJ-1 | Beijing-1 (of NRSCC) |
| BlackJack | BlackJack (on CHAMP, GRACE, SAC-C) |
| BNSC | British National Space Centre |
| BRDF | Bidirectional Reflectance Distribution Function |
| CALIOP | Cloud-Aerosol Lidar with Orthogonal Polarisation (on CALIPSO) |
| CALIPSO | Cloud-Aerosol Lidar and Infrared Pathfinder Satellite Observations (of NASA) |
| CartoSat | Satellite for Cartography (of ISRO) |
| CAST | Chinese Academy of Space Technology |
| CBERS | China-Brazil Earth Resources Satellite (of CAST, INPE) |
| CC | Cloud Camera (on Glory) |
| CC | Correlation Coefficient |
| CCD | Charge Coupled Device Camera (on INSAT 2E and 3A, HJ-A/B) |
| CDOM | Colour Dissolved Organic Matter - Former name: “Yellow substance absorbance” |
| CDTI | Centro para el Desarrollo Tecnológico Industrial |
| CEOS | Committee on Earth Observation Satellites |
| CERES | Clouds and the Earth’s Radiant Energy System (on TRMM, Terra, Aqua, SNPP, JPSS-1) |
| CGMS | Coordination Group for Meteorological Satelllites |
| CHAMP | Challenging Mini-Satellite Payload (of DLR) |
| CHRIS | Compact High Resolution Imaging Spectrometer (on PROBA) |
| CIMO | Committee for Instruments and Methods of Observation (of WMO) |
| CLARREO | Climate Absolute Radiance and Refractivity Observatory |
| CloudSat | CloudSat (of NASA) |
| CMA | China Meteorological Administration |
| CNES | Centre National d’Etudes Spatiales (in France) |
| CNTS | Centre National des Techniques Spatiales (of Algeria) |
| COCTS | China Ocean Colour & Temperature Scanner (on HY-1) |
| COMS | Communication, Oceanography and Meteorology Satellite (of KMA) |
| CONAE | Comisión Nacional de Actividades Espaciales (in Argentina) |
| Coriolis | Coriolis (of DoD and NASA) |
| COSI | Corea SAR Instrument (on KOMPSAT-5) |
| COSMIC | Constellation Observing System for Meteorology, Ionosphere & Climate (of NSPO and UCAR) |
| COSMO-SkyMed | Constellation of Small Satellites for Mediterranean basin Observation (of ASI) |
| COSPAR | Committee on Space Research (of ICSU, the International Council of Scientific Unions) |
| CPD | Charged Particle Detector (on Ørsted) |
| CPR | Cloud Profiling Radar for CloudSat (on CloudSat, Earth-CARE) |
| CrIS | Cross-track Infrared Sounder (on SNPP, JPSS) |
| CryoSat | CryoSat (of ESA) |
| CSA | Canadian Space Agency |
| CSG | COSMO-SkyMed 2nd Generation (of ASI) |
| CSI | Critical Success Index |
| CSK | 1st generation of COSMO-SkyMed (of ASI) |
| CZCS | Coastal Zone Colour Scanner (on Nimbus-7) |
| CZI | Coastal Zone Imager (on HY-1 B/C/D) |
| DAC | Ocean Diffuse Attenuation Coefficient - Former name: "Water clarity" |
| DCP | Data Collection Platform |
| DCS | Data Collection Service |
| Deimos | Deimos (of CDTI) |
| DEM | Digital Elevation Model |
| DIAL | Differential Absorption Lidar |
| DIS | Deimos Imaging SL (subsidiary of Deimos Space SL, Spain) |
| DLR | Deutsches Zentrum für Luft- und Raumfahrt (German Aerospace Centre) |
| DMC | Disaster Monitoring Constellation (intended as satellites) |
| DMSP | Defense Meteorological Satellite Program (of DoD) |
| DNSC | Danish National Space Centre |
| DoD | Department of Defense (of the USA) |
| DORIS | Doppler Orbitography and Radiopositioning Integrated by Satellite |
| DPR | Dual-frequency Precipitation Radar (on GPM-core) |
| DRS | Data Relay Satellite |
| DubaiSat | DubaiSat (of EIAST) |
| DWR | Dry-to-Wet Ratio |
| DWSS | Defense Weather Satellite System (formerly NPOESS 2 and 4) (of DoD) |
| E | Eötvös: physical unit for gravity gradients (1 E = 1 mGal / 10 km) |
| Earth-CARE | Earth Clouds, Aerosol and Radiation Explorer (of ESA) |
| EC | European Commission |
| ECT | Equatorial Crossing Time |
| ECV | Essential Climate Variable |
| EFI | Electric Field Instrument (on SWARM) |
| EGG | 3-Axis Electrostatic Gravity Gradiometer (on GOCE) |
| EIAST | Emirates Institution for Advanced Science and Technology |
| Electro | Other name for GOMS (of RosHydroMet) |
| EnMAP | Environmental Mapping and Analysis Programme (of DLR) |
| Envisat | Environmental Satellite (of ESA) |
| EOS | Earth Observing System (Terra, Aqua, Aura) (of NASA) |
| EPS | EUMETSAT Polar System (of EUMETSAT) |
| EPS-SG | EPS Second Generation (of EUMETSAT) |
| ERB | Earth Radiation Budget |
| ERBS | Earth Radiation Budget Satellite (of NASA) |
| ERM-1 | Earth Radiation Measurement – 1 (on FY-3 A, B, C) |
| ERM-2 | Earth Radiation Measurement – 2 (on FY-3E&G) |
| ERS | European Remote-sensing Satellite (of ESA) |
| ERTS | Earth Resources Technology Satellite (of NASA) |
| ESA | European Space Agency |
| ETM+ | Enhanced Thematic Mapper + (on Landsat-7) |
| ETS | Equitable Threat Score |
| ET-SAT | Expert Team on Satellite Systems (of WMO) |
| EUMETSAT | European organisation for the exploitation of meteorological satellites |
| EXIS | Extreme Ultraviolet & X-Ray Irradiance Sensor (on GOES-R) |
| FAPAR | Fraction of Absorbed Photosynthetically Active Radiation |
| FAR | False Alarm Rate |
| FBI | Frequency BIas |
| FCI | Flexible Combined Imager (on Meteosat Third Generation) |
| FGGE | First GARP Global Experiment |
| FIR | Far Infra-Red |
| FM-E | Magnetometer instrument (part of HMS on Electro-L) |
| FormoSat-2 | FormoSat-2 (NSPO) |
| FormoSat-3 | Other name of COSMIC (of NSPO and UCAR) |
| FOV | Field Of View |
| FVM | Fluxgate Vector Magnetometer (on Ørsted) |
| FY-1 | Feng-Yun -1 (in LEO) (of CMA) |
| FY-2 | Feng-Yun - 2 (in GEO) (of CMA) |
| FY-3 | Feng-Yun - 3 (in LEO) (of CMA) |
| FY-4 | Feng-Yun - 4 (in GEO) (of CMA) |
| GACM | Global Atmospheric Composition Mission |
| Gal | “Galileo”: physical unit for the gravity field (1 Gal = 0.01 m/s2. i.e. 1 mGal ≈ 10-6 g0) |
| GAMI | Hyper-spectral Green House Gas Monitor (FY-3 D&F) |
| GARP | Global Atmospheric Research Programme |
| GAS | Geostationary Atmospheric Sounder (ESA study) |
| GCM | General Circulation Model |
| GCOM-C | Global Change Observation Mission for Climate (of JAXA) |
| GCOM-W | Global Change Observation Mission for Water (of JAXA) |
| GEMS | Geostationary Environmental Monitoring Spectrometer (on COMS-2B) |
| GEO | Geostationary Earth Orbit |
| GEOSAR | Geostationary Search and Rescue |
| GEOSS | Global Earth Observation System of Systems |
| GeoSTAR | Geostationary Synthetic Thinned-Aperture Radiometer (on PATH) |
| Geoton | Panchromatic and multispectral radiometer (on Resurs-DK) |
| GERB | Geostationary Earth Radiation Budget (on Meteosat Second Generation) |
| GIC | Geomagnetically Induced Currents |
| GISICS | Global Space-based Inter-Calibration System |
| GISTDA | Geo-Informatics and Space Technology Development Agency (in Tailand) |
| GLAS | Geoscience Laser Altimeter System (on ICESat) |
| GLM | Geostationary Lightning Mapper (on GOES-R) |
| GLONASS | GLObal NAvigation Satellite System (of Russian Federation) |
| Glory | Glory (of NASA) |
| GMI | GPM Microwave Imager (on GPM-core, GPM-NASA, GPM-Brazil) |
| GMSC | Geophysical Monitoring System Complex (on Meteor-M) |
| GNOS | Radio-occultation receiver (on FY-3) |
| GNSS | Global Navigation Satellite System (GPS + GLONASS) |
| GOCE | Gravity Field and Steady-State Ocean Circulation Explorer (ESA) |
| GOCI | Geostationary Ocean Color Imager (on COMS-1 and COMS-2B) |
| GOES | Geostationary Operational Environmental Satellite (of NOAA) |
| GOLPE/BlackJack | GPS Occultation and Passive reflection Experiment (on SAC-C) |
| GOME | Global Ozone Monitoring Experiment (on ERS-2) |
| GOME-2 | Global Ozone Monitoring Experiment - 2 (on MetOp) |
| GOMOS | Global Ozone Monitoring by Occultation of Stars (on Envisat) |
| GOMS | Geostationary Operational Meteorological Satellite (also Electro) (of RosHydroMet) |
| GOS | Global Observing System |
| GOSAT | Green-house gas Observing Satellite (of JAXA) |
| GPM | Global Precipitation Measurement mission |
| GPM-constellation | GPM satellites equipped with MW radiometers (NASA, Brazil) |
| GPM-core | GPM satellite equipped with radar (of NASA and JAXA) |
| GPS | Global Positioning System (intended as navigation system) (of USA) |
| GPS | Global Positioning System (intended as receiver on GOCE, SWARM et al.) |
| GPS/MET | Global Positioning System / Meteorology (on Microlab-1) |
| GRACE | Gravity Recovery and Climate Experiment (of NASA) |
| GRAS | GNSS Receiver for Atmospheric Sounding (on MetOp) |
| GSICS | Global Space-based Inter-Calibration System |
| GUVI | Global Ultraviolet Imager (on TIMED) |
| HAIRS | High Accuracy Inter-satellite Ranging System (on GRACE) |
| Himawari | Follow-on of Multi-functional Transport Satellite (of JMA) |
| Hinode | Japanese name of better-known Solar-B (of ISAS) |
| HIRDLS | High-Resolution Dynamics Limb Sounder (on Aura) |
| HiRI | High-Resolution Imager (on Pléiades) |
| HIRS-3/4 | High-resolution Infra Red Sounder (on NOAA, MetOp A&B) |
| HJ | Huan Jing (of CAST) |
| HMS | Heliogeophysical Measurements System (on Electro-L) |
| HR | Hit Rate |
| H.R, | High Resolution |
| HRG | Haute Résolution Géométrique (on SPOT-5) |
| HRS | Haute Résolution Stéréoscopique (on SPOT-5) |
| HRVIR | Haute Résolution dans le Visible et l’Infra-Rouge (on SPOT-4) |
| HS | Higher Stratosphere |
| HS&M | Higher Stratosphere and Mesosphere |
| HSI | Hyper-Spectral Imager (on EnMAP) |
| HSI | Hyper Spectral Imager (on HJ-1A) |
| HSRL | High Spectral Resolution Laser |
| HSS | Heidke Skill Score |
| HT | Higher Troposphere |
| HY | Hai Yang (of NSOAS and CAST) |
| HYC | HYperspectral Camera (on PRISMA) |
| Hyperion | Hyperion (on NMP EO-1) |
| HyS-I | Hyper Spectral Imager (on IMS-1) |
| IAS | Infrared Atmospheric Sounder (on EPS-SG) |
| IASI | Infrared Atmospheric Sounding Interferometer (on MetOp) |
| ICESat | Ice, Cloud and land Elevation Satellite (of NASA) |
| IFOV | Instantaneous Field Of View |
| IGOR | Integrated GPS Occultation Receiver (on COSMIC, TerraSAR, TanDEM) |
| IIR | Imaging Infrared Radiometer (on CALIPSO) |
| IIS | Interferometric Infrared Sounder (on FY-4) |
| IMAGER | Imager (on GOES 8 to 15, MTSAT-2, INSAT-3D) |
| IMD | India Meteorological Department |
| IMS | Indian Mini-Satellite (of ISRO) |
| Ingenio | Other name of SEOSat (Spanish Earth Observation Satellite) (of CDTI) |
| INPE | Instituto Nacional de Pesquisas Espaciais (in Brazil) |
| INSAT | Indian National Satellite (of IMD and ISRO) |
| IPM | Ionospheric PhotoMeter (part of SES on FY-3) |
| IR | Infra-Red (MWIR + TIR) |
| IR | Infra Red Camera (on HJ-1B) |
| IRAS | Infra Red Atmospheric Sounder (on FY-3 A to C) |
| IRFS-2 | IR Sounding Spectrometer (on Meteor-M N2) |
| IRMSS | Infrared Multispectral Scanner (on CBERS 3/4) |
| IRS | Indian Remote-sensing Satellite (of ISRO) |
| IRS | Infra Red Sounder (on Meteosat Third Generation) |
| ISA | Israeli Space Agency |
| ISAS | Institute of Space and Aeronautics Science (of Japan) |
| ISRO | India Space Research Organisation |
| ITRS | International Terrestrial Reference System |
| ITU | International Telecommunication Union |
| JAMI | Japanese Advanced Meteorological Imager (on MTSAT-1R) |
| JASON-1 | Joint Altimetry Satellite Oceanography Network -1 (of NASA and CNES) |
| JASON-2/3 | Joint Altimetry Satellite Oceanography Network -2/3 (also OSTM) (of NASA, CNES, EUM, NOAA) |
| JAXA | Japan Aerospace Exploration Agency (formerly NASDA) |
| JMA | Japan Meteorological Agency |
| JMR | Jason Microwave Radiometer (on Jason-1) |
| JPSS | Joint Polar Satellite System (formerly NPOESS 1 and 3) (of NOAA) |
| Kalpana | Kalpana (previously MetSat) (of IMD and ISRO) |
| KANOPUS-V | KANOPUS Vulkan (of Roscosmos) |
| KARI | Korea Aerospace Research Institute |
| KGI-4C | Radiation Monitoring System (part of GMSC) |
| KMA | Korea Meteorological Administration |
| KMSS | High-resolution VIS/IR Radiometer (on Meteor-M N1&2) |
| KOMPSAT | KOMPSAT (of KARI) |
| LAGEOS-1 | Laser Geodynamics Satellite - 1 (of NASA) |
| LAGEOS-2 | Laser Geodynamics Satellite - 2 (of ASI and NASA) |
| LAI | Leaf Area Index |
| Landsat | Landsat (of USGS and NASA) |
| LARES | LAser RElativity Satellite (of ASI) |
| Laser | Light Amplification by Stimulated Emission of Radiation |
| LDCM | Landsat Data Continuity Mission (of USGS and NASA) |
| LEO | Low Earth Orbit |
| LI | Lightning Imager (on Meteosat Third Generation) |
| Lidar | LIght Detection And Ranging |
| LIS | Lightning Imaging Sensor (on TRMM) |
| LISS-3 | Linear Imaging Self-Scanning Sensor - 3 (on IRS-1C/1D, ResourceSat) |
| LISS-4 | Linear Imaging Self-Scanning Sensor - 4 (on ResourceSat) |
| LM | Lightning Mapper (on FY-4) |
| LR | Laser Reflector (on GOCE, STARLETTE, STELLA et al.) |
| LRA | Laser Retroreflector Array (on LAGEOS, LARES et al.) |
| LS | Lower Stratosphere |
| LST | Local Solar Time |
| LT | Lower Troposphere |
| LW | Long Wave |
| M | Mesosphere |
| MADRAS | MW Analysis & Detection of Rain & Atmospheric Structures (on Megha-Tropiques) |
| MAESTRO | Measurements of Aerosol Extinction in the Stratosphere and Troposphere Retrieved by Occultation (on SCISAT) |
| MAG | Magnetometer (on GOES-R) |
| MBEI | Multi-Band Earth Imager (on SICH-2) |
| MCSI | Multiple Channel Scanning Imager (on FY-4) |
| ME | Mean Error (or Bias) |
| Megha-Tropiques | Megha-Tropiques (of CNES and ISRO) |
| MERIS | Medium Resolution Imaging Spectrometer (on Envisat) |
| MERSI-1 | Medium Resolution Spectral Imager – 1 (on FY-3 A to B) |
| MERSI-2 | Medium Resolution Spectral Imager - 2 (on FY-3 C to G) |
| Meteor | Meteor (of RosHydroMet) |
| Meteosat | Meteorological Satellite (of EUMETSAT) |
| METI | Ministry of Economy, trade and Industry (of Japan) |
| MetOp | Meteorological Operational satellite (of EUMETSAT) |
| MHS | Microwave Humidity Sounding (on NOAA-18/19, MetOp) |
| MI | Meteorological Imager (on COMS-1) |
| MIAS | Magnetometer Instrument Assembly System (on CHAMP) |
| MicroLab-1 | Re-named OrbView-1 (of NASA and UCAR) |
| MI-FO | COMS Follow-On Imager (on COMS-2A) |
| MIPAS | Michelson Interferometer for Passive Atmospheric Sounding (on Envisat) |
| MIRAS | Microwave Imaging Radiometer using Aperture Synthesis (on SMOS) |
| MIREI | Middle IR Earth Imager (on SICH-2) |
| MIS | Microwave Imager/Sounder (on DWSS) |
| MISR | Multi-angle Imaging Spectro-Radiometer (on Terra) |
| MLS | Microwave Limb Sounder (on UARS, Aura) |
| Mm | Millimetre wave (part of MW) |
| MMC/ Ørsted-2 | Magnetic Mapping Payload / Ørsted-2 (on SAC-C) |
| MMS | Magnetospheric Multiscale mission (of NASA) |
| MODIS | Moderate-resolution Imaging Spectro-radiometer (on Terra, Aqua) |
| MOPITT | Measurement Of Pollution In The Troposphere (on Terra) |
| MSC | Multi-Spectral Camera (on KOMPSAT-2) |
| MSG | Meteosat Second Generation (Meteosat 8 to 11) |
| MSGI-MKA | Spectrometer for Geoactive Measurements (part of GMSC) |
| MSI | Multi-Spectral Imager for Earth-CARE |
| MSI | Multi-Spectral Imager (on Sentinel-2) |
| MSMR | Multi-frequency Scanning Microwave Radiometer (on OceanSat-1) |
| MSS | Multi-Spectral Scanner (on Landsat 1 to 5) |
| MSS | Multispectral film-making system (on KANOPS-V) |
| MSU | Microwave Sounding Unit (on NOAA) |
| MSU-200 | Multispectral high resolution electronic scanner (on KANOPS-V) |
| MSU-GS | Electro-GOMS Imager (on Electro-L N2/3) |
| MSU-MR | VIS/IR Imaging Radiometer (on Meteor-M N1/2) |
| MTF | Modulation Transfer Function |
| MTG-I | Meteosat Third Generation (Meteosat ≥ 12), Imaging |
| MTG-S | Meteosat Third Generation (Meteosat ≥ 13), Sounding |
| MTSAT | Multi-functional Transport Satellite (of JMA) |
| MTVZA-GY | Imaging/Sounding Microwave Radiometer (on Meteor-M N1&2) |
| MUXCAM | Multispectral Camera (on CBERS 3/4) |
| MVIRI | Meteosat Visible Infra-Red Imager (on Meteosat 1 to 7) |
| MVISR | Multichannel Visible Infrared Scanning Radiometer (on FY-1 A to D) |
| MW | Microwave |
| MWHS-1 | Micro-Wave Humidity Sounder - 1 (on FY-3 A and B) |
| MWHS-2 | Micro-Wave Humidity Sounder - 2 (on FY-3 C to G) |
| MWI | Micro-Wave Imager (on EPS-SG) |
| MWIR | Medium-Wave Infra-Red |
| MWR | Micro-Wave Radiometer (on ERS, Envisat, SAD-D, Sentinel-3) |
| MWRI | Micro-Wave Radiation Imager (on FY-3 A to F except E) |
| MWS | Micro-Wave Sounder (on EPS-SG) |
| MWTS-1 | Micro-Wave Temperature Sounder – 1 (on FY-3 A and B) |
| MWTS-2 | Micro-Wave Temperature Sounder – 2 (on FY-3 C to G) |
| Mx-T | Multispectral CCD Camera (on IMS) |
| NAOMI | New AstroSat Optical Modular Instrument (on AlSat) |
| NASA | National Aeronautics and Space Administration (of USA) |
| NASDA | National Space Development Agency (of Japan), now JAXA |
| NASRDA | National Space Research and Development Agency (in Nigeria) |
| NDVI | Normalised Difference Vegetation Index |
| NE(R | Noise Equivalent Difference Radiance |
| NE(T | Noise Equivalent Difference Temperature |
| NESR | Noise Equivalent Spectral Radiance |
| NigeriaSat | NigeriaSat (of NASRDA) |
| Nimbus | Nimbus (of NASA) |
| NIR | Near Infra-Red |
| NIRST | New Infra Red Scanner Technology (on SAC-D) |
| NIVR | Netherlands Institute for Air and Space Development |
| NMP-EO-1 | New Millennium Program - Earth Observing - 1 (of NASA) |
| NOAA | National Oceanic and Atmospheric Administration (also intended as satellite) |
| NPOESS | National Polar-orbiting Operational Environmental Satellite System (of NOAA, DoD and NASA) |
| NRA | NASA Radar Altimeter (on TOPEX-Poseidon) |
| NRL | Naval Research Laboratory (in the USA) |
| NRSCC | National Remote Sensing Centre of China |
| NSAU | National Space Agency of Ukraine (now SSAU, State Space Agency of Ukraine) |
| NSOAS | National Satellite Ocean Application Services (in China) |
| NSPO | National Space Organization (in Taiwan) |
| NWP | Numerical Weather Prediction |
| OceanSat | Satellite for the Ocean (of ISRO) |
| OCM | Ocean Color Monitor (on OceanSat) |
| OCO | Orbiting Carbon Observatory (on OCO-2) |
| OCO-2 | Orbiting Carbon Observatory - 2 (of NASA) |
| OCS | Ocean Colour Scanner (on Meteor-M N3) |
| Odin | Odin (of SNSB) |
| OIS | Optical Imaging System (on RASAT) |
| OLCI | Ocean and Land Colour Imager (on Sentinel-3) |
| OLI | Operational Land Imager (on LDCM) |
| OLS | Operational Linescan System (on DMSP) |
| OMI | Ozone Monitoring Instrument (on Aura) |
| OMPS | Ozone Mapping and Profiler Suite (on SNPP, JPSS) |
| OMS | Hyper-spectral Resolution Ultraviolet Ozone Sounder (on FY-3E&G) |
| OPD | Optical Path Difference |
| OrbView-1 | New name for MicroLab-1 (of NASA and UCAR) |
| OrbView-2 | New name for SeaStar (of NASA) |
| Ørsted | Ørsted (of DNSC) |
| OSIRIS | Optical Spectrograph and Infra-Red Imaging System (on Odin) |
| OSTM | Ocean Surface Topography Mission (also Jason 2 and 3) |
| OT | Optical Thickness |
| OVM | Overhauser Magnetometer (on Ørsted) |
| PALSAR | Phased-Array L-band Synthetic Aperture Radar (on ALOS) |
| PAN | Panchromatic |
| PAN | Panchromatic Camera (on IRS 1 C/D, CartoSat, PRISMA) |
| PAN | Panchromatic Imager (on Ingenio/SEOSat, THEOS ) |
| PANMUX | Panchromatic and Multispectral Camera (on CBERS 3/4) |
| PAR | Photosynthetically Active Radiation |
| PARASOL | Polarisation et Anisotropie des Réflectances au sommet de l'Atmosphère, couplées avec un Satellite d'Observation emportant un Lidar (of CNES) |
| PATH | Precipitation and All-weather Temperature and Humidity (a NASA project) |
| Paz | Paz (“Peace”), other name of SEOSAR (Spanish Earth Observation SAR) (of CDTI) |
| PBL | Planetary Boundary Layer |
| Pixel | Picture element |
| Pléiades | Pléiades (of CNES) |
| PM or p.m. | Post-Meridiem (afternoon) |
| POAM | Polar Ozone and Aerosol Measurement [sun occultation] (on SPOT) |
| POD | Probability Of Detection |
| POFD | Probability Of False Detection |
| POLDER | Polarization and Directionality of the Earth’s Reflectances (on PARASOL) |
| Poseidon 2/3 | Poseidon 2/3 (on JASON) |
| Post-EPS | Programme to follow EPS/MetOp, now called “EPS Second Generation”, or EPS-SG |
| PR | Precipitation Radar (on TRMM) |
| PRARE | Precise Range And Range-rate Equipment (on ERS) |
| PRISM | PAN Remote-sensing Instrument for Stereo Mapping (on ALOS) |
| PRISMA | PRecursore IperSpettrale della Missione Applicativa (of ASI) |
| PROBA | Project for On-Board Autonomy (of ESA) |
| PSC | Polar Stratospheric Clouds |
| PSF | Point Spread Function |
| PSS | Panchromatic film-making system (on KANOPS-V) |
| QuikSCAT | Quick Scatterometer Mission (of NASA) |
| RA | Radar Altimeter (on ERS-1/2) |
| RA-2 | Radar Altimeter (on Envisat) |
| RAD | Microwave Radiometer (on HY-2A) |
| Radar | RAdio Detection And Ranging |
| RadarSat | RadarSat (of CSA) |
| Radiomet | Radio-occultation sounder (on Meteor-M N3) |
| RapidEye | RapidEye (of DLR) |
| RASAT | Remote Sensing Satellite (of TÜBITAK-UZAY) |
| RCM | RadarSat Constellation Mission (of CSA) |
| REIS | RapidEye Earth Imaging System (on RapidEye) |
| RER | Radiant Energy Radiometer (on EPS-SG) |
| ResourceSat | Satellite for Earth Resources (of ISRO) |
| Resurs | Resurs (of Roscosmos) |
| RISAT | Radar Imaging Satellite (of ISRO) |
| RMS | Root Mean Square (used to quote accuracy) |
| RMSE | Root Mean Square Error |
| RO | Radio Occultation sounder (on EPS-SG) |
| ROSA | Radio Occultation Sounder of the Atmosphere (on OceanSat, SAC-D, Megha-Tropiques) |
| Roscosmos | Aeronautics and Space Agency of the Russian Federation |
| RosHydroMet | Hydro-Meteorological Service of the Russian Federation |
| RSI | Remote Sensing Instrument (on Formosat-2) |
| S&R | Search & Rescue |
| SAC-C | Satélite de Aplicaciones Cientificas - C (of CONAE) |
| SAC-D | Satélite de Aplicaciones Cientificas - D (of CONAE) |
| SANSA | South African National Space Agency |
| SAOCOM | SAtélite Argentino de Observación COn Microondas - 1 (of CONAE) |
| SAPHIR | Sondeur Atmospherique du Profil d’Humidite Intertropicale par Radiometrie (on Megha-Tropiques) |
| SAR | Synthetic Aperture Radar |
| SAR RCM | Synthetic Aperture Radar of RadarSat Constellation (on RCM) |
| SAR-2000 | Synthetic Aperture Radar 2000 (on COSMO-SkyMed) |
| SAR-2000 S.G. | Synthetic Aperture Radar 2000 Second Generation (on COSMO-SkyMed S.G.) |
| SARAL | Satellite with ARgos and ALtiKa (of CNES and ISRO) |
| SAR-C | Synthetic Aperture Radar, C-band (on RADARSAT, RISAT-1, Sentinel-1) |
| SAR-L | Synthetic Aperture Radar, L-band (on SAOCOM) |
| SAR-S | Synthetic Aperture Radar (on HJ-1C) |
| SARSAT | Search and Rescue Satellite-Aided Tracking System |
| SAR-X | Synthetic Aperture Radar, X-band (on Meteor-3 N3, Paz/SEOSAR, RISAT-2, TerraSAR, TanDEM |
| SBUS | Solar Backscatter Ultraviolet Sounder (on FT-3 A to C) |
| SBUV/2 | Solar Backscatter Ultraviolet / 2 (on NOAA 9 to 19 except 12/15) |
| SCA | Scatterometer (ASCAT-like) (on EPS-SG) |
| ScaRaB | Scanner for Radiation Budget (on Megha-Tropiques) |
| SCAT | Scatterometer (SeaWinds-like) (on OceanSat, HY-2A, Meteor-M N3 |
| SCIAMACHY | Scanning Imaging Absorption Spectrometer for Atmospheric Cartography (on Envisat) |
| SCISAT | Scientific Satellite (of CSA) |
| SD | Standard Deviation |
| SDO | Solar Dynamics Observatory (of NASA) |
| SeaSat | SeaSat (of NASA) |
| SeaStar | SeaStar (new name: OrbView-2) (of NASA) |
| SeaWiFS | Sea-viewing Wide Field-of-view Sensor (on Orbview-2/SeaStar) |
| SeaWinds | SeaWinds (on QuikSCAT) |
| SEE | Solar Extreme Ultraviolet Experiment (on TIMED) |
| SEISS | Space Environment In-Situ Suite (on GOES-R) |
| SEM (in GEO) | Space Environment Monitor (on GOES, FY-2, FY-4 et al.) |
| SEM (in LEO) | Space Environment Monitor (on NOAA, MetOp, FY-1, FY-3A&B et al.) |
| SEM-N | Space Environment Monitoring for NPOESS (on JPSS, DWSS, EPS-SG) |
| Sentinel-1 | Sentinel-1 (for SAR-C continuity) (of ESA and EC) |
| Sentinel-2 | Sentinel-2 (for land observation) (of ESA and EC) |
| Sentinel-3 | Sentinel-3 (for ocean and land) (of ESA and EC) |
| Sentinel-4 | Sentinel-4 (for chemistry in GEO) (of ESA and EC) (on MTG-S) |
| Sentinel-5 | Sentinel-5 (for chemistry in LEO) (of ESA and EC) (precursor, then on Post-EPS) |
| SEOSAR | Spanish Earth Observation SAR (also called “Paz”) (of CDTI) |
| SEOSat | Spanish Earth Observation Satellite (also called “Ingenio”) (of CDTI) |
| SES | Space Environment Suite (on FY-3C to G) |
| Severjanin-M | Onboard Radar Complex (on Meteor-M N1&2) |
| SEVIRI | Spinning Enhanced Visible Infra-Red Imager (on Meteosat Second Generation) |
| SGLI | Second-generation Global Imager (on GCOM-C) |
| SICH | SICH (of NSAU) |
| SIM | Spectral Irradiance Monitor (on SORCE) |
| SIM-1 | Solar Irradiance Monitor - 1 (on FY-3 A&B) |
| SIM-2 | Solar Irradiance Monitor - 2 (on FY-3 C,E,G) |
| SIRAL | SAR Interferometer Radar Altimeter (on CryoSat) |
| SIR-C/X-SAR | Shuttle Imaging Radar with Payload C / X-SAR (of NASA, DLR, ASI) |
| SLIM6 | Surrey Linear Imager Multispectral 6 channels - but 3 spectral bands (on UK-DMC, BJ, Deimos, AlSat, NigeriaSat) |
| SLSTR | Sea and Land Surface Temperature Radiometer (on Sentinel-3) |
| SMM | Solar Maximum Mission (of NASA) |
| SMMR | Scanning Multichannel Microwave Radiometer) (on Nimbus-7 & SeaSat) |
| SMOS | Soil Moisture and Ocean Salinity (of ESA) |
| SMR | Sub-Millimetre Radiometer (on Odin) |
| SMS | Synchronous Meteorological Satellite (of NOAA and NASA) |
| SNPP | Suomi National Polar Partnership (formerly named NPOESS Preparatory Project) |
| SNR | Signal-to-Noise Ratio |
| SNSB | Swedish National Space Board |
| SOHO | Solar and Heliographic Observatory (of NASA and ESA) |
| SORCE | Solar Radiation and Climate Experiment (of NASA) |
| SOUNDER | Sounder (on GOES 8 to 15, INSAT-3D) |
| SPOT | Satellite Pour l’Observation de la Terre (CNES) |
| SRAL | SAR Radar Altimeter (on Sentinel-3) |
| SSAU | State Space Agency of Ukraine (formerly NSAU, National Space Agency of Ukraine) |
| SSIES | Special Sensor Ion and Electron Scintillation Monitor (on DMSP) |
| SSM/I | Special Sensor Microwave - Imager (on DMSP F8 to 15) |
| SSJ5 | Special Sensor Precipitating Electron and Ion Spectrometer (part of SEM-N) |
| SSM | Special Sensor Magnetometer (on DMSP) |
| SSM/T | Special Sensor Microwave - Temperature (F04 to F15) |
| SSM/T-2 | Special Sensor Microwave - Humidity (on DMSP F11 to F15 |
| SSMIS | Special Sensor Microwave Imager/Sounder (on DMSP F16 to S20) |
| SSP or s.s.p. | Sub Satellite Point |
| SSPD | Data Collection and Transmission System (on Meteor-M N1/N2) |
| SST | Sea Surface Temperature |
| SSTI | Satellite-to-Satellite Tracking System (on GOCE) |
| SSTL | Surrey Satellite Technology Ltd (in UK) |
| SSULI | Special Sensor Ultraviolet Limb Imager (on DMSP) |
| SSUVI | Special Sensor Ultraviolet Spectrographic Imager (on DMSP) |
| STAR | Space Three-axis Accelerometer for Research (on CHAMP) |
| STARLETTE | Satellite de Taille Adaptée avec Réflecteurs Laser por les Etudes de la Terre (of CNES) |
| STELLA | Companion of STARLETTE (of CNES) |
| STEREO | Solar-TErrestrial RElations Observatory (of NASA) |
| STR | Star Tracker (on SWARM) |
| Sub-mm | Submillimetre wave (part of FIR) |
| SumbandilaSat | SumbandilaSat (of SANSA) |
| SuperSTAR | Super Space Three-axis Accelerometer for Research (on GRACE) |
| SUVI | Solar Ultraviolet Imager (on GOES-R) |
| S-VISSR | Stretched Visible-Infrared Spin Scan Radiometer (on FY-2 A to H) |
| SW | Short Wave |
| SWARM | The Earth’s Magnetic Field and Environment Explorers (of ESA) |
| SWIR | Short-Wave Infra-Red |
| SWOT | Surface Water and Ocean Topography (a NASA project) |
| SXEUV | Solar X-EUV imaging telescope (on FY-4) |
| SXI | Solar X-ray Imager (on GOES 12 to 15) |
| SZS | Shore Zone Scanner (on Meteor-M N3) |
| TacSat-2 | Tactical Satellite (also known as RoadRunner) (of DoD and NASA) |
| TanDEM-X | Coupled to TerraSAR for improved DEM (of DLR) |
| TANSO-CAI | Thermal And Near infrared Sensor for carbon Observations - Cloud and Aerosol Imager (on GOSAT) |
| TANSO-FTS | Thermal And Near infrared Sensor for carbon Observations - Fourier Transform Spectrometer (on GOSAT) |
| TBC | To Be Confirmed |
| TEC | Total Electron Content |
| Terra | EOS-Terra (of NASA) |
| TerraSAR | TerraSAR (X-band) (of DLR) |
| TES | Tropospheric Emission Spectrometer (on Aura) |
| THEMIS | Time History of Events and Macroscale Interactions during Substorms (of NASA) |
| THEOS | Thailand Earth Observation System (of GISTDA) |
| TIDI | TIMED Doppler Interferometer (on TIMED) |
| TIM | Total Irradiance Monitoring (on SORCE, Glory) |
| TIMED | Thermosphere, Ionosphere, Mesosphere Energetics and Dynamics mission (of NASA) |
| TIR | Thermal Infra-Red |
| TIROS | Television and Infra-Red Observation Satellite (of NASA) |
| TIRS | Thermal Infra-Red Sensor (on LDCM) |
| TM | Thematic Mapper (on Landsat-4/5) |
| TMI | TRMM Microwave Imager (on TRMM) |
| TOA | Top Of Atmosphere |
| TOMS | Total Ozone Mapping Spectrometer (on Nimbus-7, Meteor-3 6, ADEOS-1) |
| TOPEX-Poseidon | Topography Experiment + Poseidon (of NASA and CNES) |
| TopSat | TopSat (of BNSC) |
| TOU | Total Ozone Unit (on FT-3 A to C) |
| TRACE | Transition Region and Coronal Explorer |
| TRMM | Tropical Rainfall Measuring Mission (of NASA and JAXA) |
| TRSR | Turbo Rogue Space Receiver (for radio occultation) (on Ørsted) |
| TSIS | Total Solar Irradiance Sensor (on JPSS) |
| TÜBITAK | Scientific and Technological Research Council (of Turkey) |
| UARS | Upper Atmosphere Research Satellite (of NASA) |
| UCAR | University Corporation for Atmospheric Research (in USA) |
| UHF | Ultra-High Frequency |
| UK-DMC | UK contribution to the DMC (of BNSC) |
| USGS | United States Geological Survey |
| UTC | Universal Coordinated Time |
| UV | Ultra-Violet |
| UVN | Ultra-violet, Visible and Near-infrared sounder (on Sentinel-5 precursor, MTG/Sentinel-4 |
| UVNS | Ultra-violet, Visible and Near-infrared Sounder (on EPS-SG/Sentinel-5) |
| UZAY | Space Technologies Research Institute (of TÜBITAK) |
| Végétation | Végétation (on SPOT 4/5) |
| VENμS | Vegetation and Environment monitoring on a New Micro-Satellite (of CNES, ISA) |
| VFM | Vector Field Magnetometer (on SWARM) |
| VHF | Very-High Frequency |
| VHRR (in GEO) | Very High Resolution Radiometer (on INSAT-1A to 3A, Kalpana) |
| VHRR (in LEO) | Very High Resolution Radiometer (on NOAA) |
| VII | Visible and Infrared Imager (on EPS-SG) |
| VIIRS | Visible/Infrared Imager Radiometer Suite (on SNPP, JPSS) |
| VIRR | Visible and Infra Red Radiometer (on FY-3 A to C) |
| VIRS | Visible and Infra Red Scanner (on TRMM) |
| VIS | Visible |
| VNIR | Visible and Near Infra-Red (VIS + NIR) |
| VSSC | VENμS SuperSpectral Camera (on VEN(S) |
| WAI | Wide-field Auroral Imager (part of SES on FY-3) |
| WALES | Water vApour and Lidar Experiment in Space (ESA study) |
| WFI-2 | Wide-Field Imager – 2 (on CBERS-3/4) |
| WindRAD | Sea Wind Measurement Radar (on FY-3) |
| WindSat | WindSat (on Coriolis) |
| WMO | World Meteorological Organization |
| WVC | Wide View CCD Camera (on HJ A and B) |

# Footnotes

From the Committee on Earth Observation Satellites (CEOS) Working Group on Calibration and Validation.

See for example: Ohring, G. (Ed.) (2007): Achieving Satellite Instrument Calibration for Climate Change (ASIC3). Report of a workshop organized by NOAA, NIST, NASA, NPOESS-IPO, SDL-USU; Lansdowne VA, USA, 16-18 May 2006.

For guidance on reference standards, see e.g. A Guide to “Reference Standards” in Support of Quality Assurance Requirements of GEO, QA4EO-QAEO-GEN-DQK-003, http://www.qa4eo.org/docs/QA4EO-QAEO-GEN-DQK-003_v4.0.pdf

For a 98 degree inclination, the crossing latitude is above 70 deg when the Equatorial Crossing Time of the two orbits are differing by less than 8 hours, and only drops significantly when the ECT difference increases towards 12 hours.

From the Committee on Earth Observation satellites (CEOS) Working Group on Calibration and Validation.

https://www.ghrsst.org/ghrsst-science/product-validation/