| WORLD METEOROLOGICAL ORGANIZATION __________________ COMMISSION FOR INSTRUMENTS AND METHODS OF OBSERVATION CIMO MANAGEMENT GROUP Ninth Session Geneva, Switzerland 5 - 8 April 2011 |  | CIMO/MG-9/Doc. 5.1(2) (3.III.2011) _______ ITEM: 5.1 Original: ENGLISH |
| --- | --- | --- |

CIMO GUIDE

Update of the Satellite Observations Chapter of the CIMO Guide

Summary and purpose of document In response to an action agreed by the Expert Team on Satellite Systems at its fifth meeting (ET-SAT-5, 26-29 April 2010) new material has been developed with the aim to replace the current Chapter on Satellite Observations in the Guide to Meteorological Instruments and Methods of Observation (CIMO Guide, Part II, Chapter 8), which dates back to 1994. Given the considerable development and diversification of space-based observation capabilities over the past seventeen years, and the increasing importance of space-based observation data for WMO Members, in particular for NWP, for severe weather warning, for Nowcasting, for global climate and environment monitoring, the ET-SAT felt the need to not only update the current Chapter 8 but to expand it substantially. In view of the variety of physical variables that need to be addressed, it is furthermore suggested that a new part (tentatively Part IV) of the CIMO Guide be entirely dedicated to space-based observation. A preliminary draft has been developed and is being submitted to ET-SAT Members for review. Its outline is attached, and the full draft document (163 pages) is available for download at: http://www.wmo.int/pages/prog/sat/meetings/documents/ET-SAT-6_Doc08-1-add.zip . The objective is to introduce to the fundamental principles and the main features of space-based observation. The document aims at raising the technical awareness of the reader on satellite capabilities, explaining the advantages and limitations of space-based observation, and helping WMO Members to consider the best use of these capabilities as an increasingly important source of observation data. This contribution to the CIMO Guide is meant to complement the Dossier on the Space-based Global Observing System (often designated as the “GOS Dossier”), which provides a more comprehensive inventory of current and planned satellites and instruments, as well as an analysis of the capabilities and gaps in key observations. The GOS Dossier is available for download ( ftp://ftp.wmo.int/Documents/PublicWeb/sat/DossierGOS/) and is updated at least every year.

ACTION PROPOSED

The CIMO Management Group is invited:

- to consider the proposal to dedicate a new Part of the CIMO Guide to satellite observation

- to provide guidance to ET-SAT that will discuss this issue on 12-15 April 2011.

________________

Proposed Outline for a Future Part IV of the CIMO Guide

The full draft text (163 pages) is to be downloaded from: http://www.wmo.int/pages/prog/sat/meetings/documents/ET-SAT-6_Doc08-1-add.zip

1	PREAMBLE

1.1	Historical perspective

1.2 	Specific features of space-based remote sensing

1.2.1	Spatial and temporal coverage

1.2.2	Spatial integration

1.2.3	Indirect measurements

1.2.4	Calibration

1.2.5	Validation

1.2.6	Satellite lifecycle

1.3	Updated Programme information

2.	PRINCIPLES OF EARTH OBSERVATION FROM SPACE

2.1	Orbits and Earth viewing from space

2.1.1	Field of view from satellites and instruments - Instrument swath

2.1.2	Orbital period, geostationary orbit, observing cycle, repeat cycle

2.1.3	Orbital precession, sunsynchronous orbits, drifting orbits

2.1.4	Elliptical orbits

2.1.5	Launchers and injection into orbit - Services of the platform

2.2	Principles of remote sensing

2.2.1	The electromagnetic spectrum utilised for remote sensing

2.2.2	The basic laws of the interaction between e.m. radiation and matter

2.2.3 	Observations in the atmospheric windows

2.2.3.1	Emerging radiation

2.2.3.2	Measurements in VIS+NIR+SWIR

2.2.3.3	Measurements in MWIR and TIR

2.2.3.4	Measurements in MW

2.2.4 	Observations in absorption bands

2.2.4.1	The radiative transfer equation

2.2.4.2	Profiles retrieval

2.2.4.3	Limb sounding

2.2.5	Active sensing

2.2.5.1	Radio occultation

2.2.5.2	Radar

2.2.5.3	Lidar

2.3	Data circulation and processing

2.3.1	Data transmission

2.3.2	Data processing

2.3.3	Communication services

3.	REMOTE SENSING INSTRUMENTS

3.1	Instruments basic characteristics

3.1.1	Scanning, swath, observing cycle

3.1.2	Spectral range: radiometers and spectrometers

3.1.3	Spatial resolution (IFOV, pixel, MTF)

3.1.4	Radiometric accuracy

3.2	Visible and Infrared imagers

3.2.1	Multi-purpose imaging VIS/IR radiometer

3.2.2	High resolution optical imager

3.2.3	Medium-resolution VIS/NIR spectro-radiometer

3.2.4	Multi-channel/direction/polarization radiometer

3.3 	Infrared sounders

3.3.1 	Narrow-band channel IR radiometer

3.3.2 	Medium-resolution IR spectrometer

3.4 	Microwave imagers and sounders

3.4.1 	Multi-purpose imaging MW radiometer

3.4.2 	Low-frequency MW radiometer

3.4.3 	Non-scanning MW radiometer

3.4.4 	Absorption-band MW radiometer/spectrometer

3.5 	Spectrometers for atmospheric chemistry

3.5.1 	High-resolution nadir-scanning SW spectrometer

3.5.2 	High-resolution nadir-scanning IR spectrometer

3.5.3	Limb-scanning SW spectrometer

3.5.4 	Limb-scanning IR spectrometer

3.5.5 	Limb-scanning MW spectrometer

3.6 	Special instruments

3.6.1 	Broad-band radiometer

3.6.2 	Solar irradiance monitor

3.6.3 	Lightning imager

3.6.4	GNSS radio-occultation receiver

3.7 	Radar

3.7.1 	Radar altimeter

3.7.2 	Radar scatterometer

3.7.3 	Cloud and precipitation radar

3.7.4 	Imaging radar (SAR)

3.8 	Lidar

3.8.1 	Backscatter lidar

3.8.2 	Doppler lidar

3.8.3 	Lidar altimeter

3.8.4 	Differential Absorption Lidar (DIAL)

3.9 	In-situ measurements at platform level

3.9.1 	Gradiometer / accelerometer

3.9.2 	Satellite-to-Satellite ranging system

3.9.3 	Magnetometer

3.9.4 	Electric field sensor

3.9.5 	Space environment monitor

3.10	Navigation and positioning systems

3.10.1 	Laser retroreflector

3.10.2 	Radio-positioning system

3.10.3	GNSS receiver

3.10.4 		Star tracker

4.		SATELLITE CONSTELLATIONS

4.1		Operational meteorological satellites

4.1.1		Satellite constellation in geostationary orbits

4.1.2		Specialised Atmospheric missions

4.2.1		Precipitation

4.2.2		Radio occultation

4.2.3		Atmospheric radiation

4.2.4		Atmospheric chemistry

4.2.5		Atmospheric dynamics

4.3		Missions to ocean and ice

4.3.1		Ocean topography

4.3.2		Ocean colour

4.3.3		Sea surface wind

4.3.4	Sea surface salinity

4.3.5	Waves

4.4	Land observation missions

4.4.1	Main operational or near-operational missions

4.4.2	The Disaster Monitoring Constellation

4.4.3	All-weather high-resolution monitoring (by SAR)

4.5	Missions to Solid Earth

4.5.1	Space geodesy

4.5.2	Earth’s interior

4.6 	Missions to Space weather

4.6.1	Solar activity monitoring

4.6.2	Magnetosphere and ionosphere monitoring

4.6.2.1 	Observation of the Magnetosphere

4.6.2.2 	Observation of the Ionosphere

4.6.2.3	Space environment observation from operational meteorological satellites

5.	SPACE-BASED OBSERVATION OF GEOPHYSICAL VARIABLES

5.1	Introduction

5.1.1	Processing levels

5.1.2	Products quality

5.1.2.1	Atmospheric volumes (relevant to profiles)

5.1.2.2	The horizontal resolution ((x)

5.1.2.3	The vertical resolution ((z)

5.1.2.4	The observing cycle ((t)

5.1.2.5	The accuracy (RMS)

5.1.2.6	The timeliness (()

5.1.3	Evaluation of satellite product quality

5.2	Basic atmospheric 3D and 2D variables

5.2.1	Atmospheric temperature

5.2.2	Specific humidity

5.2.3	Wind (horizontal)

5.2.4	Wind vector over the surface (horizontal)

5.2.5	Height of the top of the Planetary Boundary Layer

5.2.6	Height of the tropopause

5.2.7	Temperature of the tropopause

5.3	Cloud and Precipitation variables

5.3.1	Cloud detection (mask)

5.3.2	Cloud top temperature

5.3.3	Cloud top height

5.3.4	Cloud type

5.3.5	Cloud cover

5.3.6	Cloud base height

5.3.7	Cloud optical thickness

5.3.8	Cloud liquid water

5.3.9	Cloud drop effective radius

5.3.10	Cloud ice

5.3.11	Cloud ice effective radius

5.3.12	Freezing level height in clouds

5.3.13	Melting layer depth in clouds

5.3.14	Precipitation (liquid or solid)

5.3.15	Precipitation rate at surface (liquid or solid)

5.3.16	Accumulated precipitation (over 24 hours)

5.3.17	Lightning detection

5.4	Aerosol and Radiation

5.4.1	Aerosol optical thickness

5.4.2	Aerosol concentration

5.4.3	Aerosol effective radius

5.4.4	Aerosol type

5.4.5	Volcanic ash

5.4.6	Downward solar irradiance at TOA

5.4.7	Upward spectral radiance at TOA

5.4.8	Upward long-wave irradiance at TOA

5.4.9	Upward short-wave irradiance at TOA

5.4.10	Short-wave cloud reflectance

5.4.11	Downward LW irradiance at Earth’s surface

5.4.12	Downward SW irradiance at Earth’s surface

5.4.13	Earth’s surface albedo

5.4.14	Earth’s surface SW bi-directional reflectance

5.4.15	Upward long-wave irradiance at Earth’s surface

5.4.16	Long-wave Earth surface emissivity

5.4.17	Photosynthetically Active Radiation (PAR)

5.4.18	Fraction of Absorbed Photosynthetically Active Radiation (FAPAR)

5.5	Ocean and sea ice

5.5.1	Ocean chlorophyll concentration

5.5.2	Colour Dissolved Organic Matter (CDOM)

5.5.3	Ocean suspended sediments concentration

5.5.4	Ocean Diffuse Attenuation Coefficient (DAC)

5.5.5	Oil spill cover

5.5.6	Sea surface temperature

5.5.7	Sea surface salinity

5.5.8	Ocean dynamic topography

5.5.9	Coastal sea level (tide)

5.5.10	Significant wave height

5.5.11	Dominant wave direction

5.5.12	Dominant wave period

5.5.13	Wave directional energy frequency spectrum

5.5.14	Sea-ice cover

5.5.15	Sea-ice thickness

5.5.16	Sea-ice type

5.6	Land surface (including snow)

5.6.1	Land surface temperature

5.6.2	Soil moisture at surface

5.6.3	Soil moisture (in the roots region)

5.6.4	Fraction of vegetated land

5.6.5	Vegetation type

5.6.6	Leaf Area Index (LAI)

5.6.7	Normalised Difference Vegetation Index (NDVI)

5.6.8	Fire fractional cover

5.6.9	Fire temperature

5.6.10	Fire radiative power

5.6.11	Snow detection (mask)

5.6.12	Snow status (wet/dry)

5.6.13	Snow cover

5.6.14	Snow water equivalent

5.6.15	Soil type

5.6.16	Land cover

5.6.17	Land surface topography

5.6.18	Glacier cover

5.6.19	Glacier topography

5.7	Solid Earth and Space Weather

5.7.1	Geoid

5.7.2	Crustal plates positioning

5.7.3	Crustal motion (horizontal and vertical)

5.7.4	Gravity field

5.7.5	Gravity gradients

5.7.6	Total Electron Content  (TEC)

5.7.7	Electron density

5.8	Atmospheric chemistry

5.8.1	O3

5.8.2	BrO

5.8.3	C2H2

5.8.4	C2H6

5.8.5	CFC-11

5.8.6	CFC-12

5.8.7	CH2O

5.8.8	CH4

5.8.9	ClO

5.8.10	ClONO2

5.8.11	CO

5.8.12	CO2

5.8.13	COS

5.8.14	H2O

5.8.15	HCl

5.8.16	HDO

5.8.17	HNO3

5.8.18	N2O

5.8.19	N2O5

5.8.20	NO

5.8.21	NO2

5.8.22	OH

5.8.23	PAN

5.8.24	PSC occurrence

5.8.25	SF6

5.8.26	SO2

6. 	CALIBRATION AND VALIDATION

6.1	Instrument calibration

6.1.1	Factors affecting calibration

6.1.2	Pre-flight calibration

6.1.3	On-board calibration

6.1.4	Vicarious calibration

6.1.5	Inter-calibration by Simultaneous Nadir Observations

6.1.6	Bias adjustment of long-term data records

6.1.7	Traceability of space-based measurement

6.1.8	Using calibration information

6.2	Validation of satellite-based products

6.2.1	Factors to be accounted for in validation

6.2.2	Requirements for ground-truth measurements

6.2.3	Continuous statistics

6.2.4	Dichotomous statistics

6.2.5	Impact studies

7.	CROSS-CUTTING ISSUES

7.1	Data access

7.1.1	Direct broadcast

7.1.2	Rebroadcast

7.1.3	Availability of data servers

7.2	Use of the frequency spectrum

7.2.1	Passive MW radiometry

7.2.2	Active MW sensing

7.2.3	Communications

REFERENCES

ACRONYMS